ERBE-like Regional Data (EID-6)

The ERBE-like Regional Data (EID-6) product is generated daily by the ERBE-like Inversion Subsystem (2.0).  It contains data for each 2.5o region observed during a day; there are 10,368 possible regions.  The EID-6 is a CERES Internal Data Product used to pass 2.5o regional statistics calculated in Subsystem 2.0 to Subsystem 3.0.  The EID-6 contains the following data as determined on a regional basis.

2.5o one-dimensional region number

Whole and fractional Julian date

Average of shortwave and longwave TOA flux estimates

Number of individual shortwave and longwave TOA flux estimates

Standard deviation for shortwave and longwave TOA flux estimates

Minimum and maximum individual estimates of shortwave and longwave radiant fluxes at the TOA

Geographic scene type

Cloud fraction (fraction of measurements associated with clear, partly-cloudy, mostly-cloudy, and overcast sky)

Albedo fraction (fraction of shortwave measurements associated with clear, partly-cloudy, mostly-cloudy, and overcast sky)

Satellite and Sun geometry [cosine of the solar zenith angle (shortwave estimates), spacecraft zenith angles (all estimates), relative azimuth angles (shortwave estimates)]

Standard deviation for clear-sky albedos

Average for longwave, clear sky TOA flux estimates

Standard deviation for longwave, clear-sky TOA flux estimates

Number of individual longwave, clear-sky TOA flux estimates

A complete listing of parameters for this data product can be found in Table 1.

Level:  2			Portion of Globe Covered

Frequency:  1/Day			File:  Regional

Configuration Code: 000000 and greater		Record:  Individual Region

Time Interval Covered		Portion of Atmosphere Covered

File:  Day			File:  TOA

Record:  N/A

| ERBE-like Daily Regional Averages (EID-6) |
| --- |
| Description | Units | Range | Elements/Record | Bits/ Elem | Elem Num |
| EID-6 |  |  |  |  |  |
| EID-6_File_Header |  |  |  |  |  |
| Logical Header (RKEY) | N/A |  | 1 | 64 |  |
| Logical Header (IBUF) | N/A |  | 9 | 288 |  |
| Production Date | N/A |  | 1 | 64 |  |
| Production Time | N/A |  | 1 | 80 |  |
| Data Begin Date | N/A |  | 6 | 384 |  |
| Data End Date | N/A |  | 6 | 384 |  |
| EID-6_Regional_Data_Records |  |  |  |  |  |
| Region number | number | 1 .. 10368 | 1 | 64 | 1 |
| Julian day | day | 2449353 .. 2458500 | 1 | 64 | 2 |
| Julian time | day | 0 .. 1 | 1 | 64 | 3 |
| Regional_Average_Estimates |  |  |  |  |  |
| SW flux average value | W m-2 | 0 .. 1400 | 1 | 64 | 4 |
| LW flux average value | W m-2 | 50 .. 450 | 1 | 64 | 5 |
| Regional_SW_Statistics |  |  |  |  |  |
| SW flux number of values | number | 0 .. 500 | 1 | 64 | 6 |
| SW flux standard deviation | W m-2 | 0 .. 1400 | 1 | 64 | 7 |
| SW flux minimum value | W m-2 | 0 .. 1400 | 1 | 64 | 8 |
| SW flux maximum value | W m-2 | 0 .. 1400 | 1 | 64 | 9 |
| Regional_LW_Statistics |  |  |  |  |  |
| LW flux number of values | number | 0 .. 500 | 1 | 64 | 10 |
| LW flux standard deviation | W m-2 | 0 .. 400 | 1 | 64 | 11 |
| LW flux minimum value | W m-2 | 50 .. 450 | 1 | 64 | 12 |
| LW flux maximum value | W m-2 | 50 .. 450 | 1 | 64 | 13 |
| Geo_Scene |  |  |  |  |  |
| Geographic Scene Type | N/A | 1 .. 5 | 1 | 64 | 14 |
| Clear-sky fraction | N/A | 0 .. 1 | 1 | 64 | 15 |
| Partly-cloudy fraction | N/A | 0 .. 1 | 1 | 64 | 16 |
| Mostly-cloudy fraction | N/A | 0 .. 1 | 1 | 64 | 17 |
| Overcast fraction | N/A | 0 .. 1 | 1 | 64 | 18 |
| Albedos |  |  |  |  |  |
| Albedo for Clear-sky | N/A | 0 .. 1 | 1 | 64 | 19 |
| Albedo for partly-cloudy | N/A | 0 .. 1 | 1 | 64 | 20 |
| Albedo for mostly-cloudy | N/A | 0 .. 1 | 1 | 64 | 21 |
| Albedo for overcast | N/A | 0 .. 1 | 1 | 64 | 22 |
| Angular_Averages |  |  |  |  |  |
| Average of cosines of solar zenith angles | N/A | 0 .. 1 | 1 | 64 | 23 |
| Average of spacecraft zenith angles | deg | 0 .. 90 | 1 | 64 | 24 |
| Average of relative azimuth angles | deg | 0 .. 180 | 1 | 64 | 25 |
| Clear-sky_Statistics |  |  |  |  |  |
| Clear-sky albedo standard deviation | N/A | 0 .. 1 | 1 | 64 | 26 |
| Clear-sky LW flux average value | W m-2 | 50 .. 450 | 1 | 64 | 27 |
| Clear-sky LW flux standard deviation | W m-2 | 0 .. 400 | 1 | 64 | 28 |
| Clear-sky LW flux number of values | number | 0 .. 500 | 1 | 64 | 29 |
| Spares |  |  |  |  |  |
| Spare | N/A | N/A | 1 | 64 | 30 |
| Spare | N/A | N/A | 1 | 64 | 31 |

| TRMM Sizes |  |  |
| --- | --- | --- |
|  | Total Data Bits/Record: | 1984 |
|  | Total Records/File (TRMM): | 27597 |
|  | Total Data Bits/File: | 54752448 |
|  | Total Bits/File: | 54752448 |
|  | Total MB/File: | 6.5 |
| Terra Sizes |  |  |
|  | Total Data Bits/Record: | 1984 |
|  | Total Records/File (Terra): | 72845 |
|  | Total Data Bits/File: | 144524480 |
|  | Total Bits/File: | 144524480 |
|  | Total MB/File: | 17.2 |
| Aqua Sizes |  |  |
|  | Total Data Bits/Record: | 1984 |
|  | Total Records/File (Aqua): | 72597 |
|  | Total Data Bits/File: | 141423488 |
|  | Total Bits/File: | 141423488 |
|  | Total MB/File: | 16.9 |
| Note: The sizing estimate for the EID6 in the “Internal Products Summary” Table 4 is for Terra. |

EID6 Revision Record

The product Revision Record contains information pertaining to approved section changes.  The table lists the date the Software Configuration Change Request (SCCR) was approved, the Release and Version Number, the SCCR number, a short description of the revision, and the revised sections.  The authors are listed on the document cover.

| EID6 Revision Record |
| --- |
| SCCR Approval Date | Release/ Version Number | SCCR Number | Description of Revision | Section(s) Affected |
| N/A | R3V1 | N/A | Updated format to comply with standards. | All |
|  |  |  | The EOSDIS Product Code line was removed from the document. (6/17/2008) | Sec. 3.3 |
|  |  |  | Some links were not working. They have now been modified. (12/09/2010) | All |
|  |  |  | The ASDC footer was added to the bottom of the document. (06/06/2013) | All |
|  |  |  | Eliminated section numbers from the Data Products Catalog. Specifically, in this document, section number 3.3 was removed. (12/17/2013) | All |
|  |  |  | Changed Table 1.0-4 to Table 4 and accessed the .pdf file instead of the .doc Introduction section. (06/19/2014) | Table 1 |