ERBE-like Monthly Regional Averages (ES-9)

The ERBE-like Monthly Regional Averages (ES-9) product contains a month of space and time averaged Clouds and the Earth's Radiant Energy System (CERES) data for a single scanner instrument.  The ES-9 is also produced for combinations of scanner instruments.  All instantaneous shortwave and longwave fluxes at the Top-of-the-Atmosphere (TOA) from the CERES ES-8 product for a month are sorted by 2.5-degree spatial regions, by day number, and by the local hour of observation.  The mean of the instantaneous fluxes for a given region-day-hour bin is determined and recorded on the ES-9 along with other flux statistics and scene information.  For each region, the daily average flux is estimated from an algorithm that uses the available hourly data, scene identification data, and diurnal models.  This algorithm is "like" the algorithm used for the Earth Radiation Budget Experiment (ERBE).  The ES-9 also contains hourly average fluxes for the month and an overall monthly average for each region.  These average fluxes are given for both clear-sky and total-sky scenes.

The ES-9 archival data product is created as an HDF file with six Vgroups and contains data for each 2.5-degree region observed during a month.  There are 10,368 regions in the ERBE-Like data; therefore, there is a maximum of 10,368 records in the ES-9 data set.  A summary of the contents of this data product can be found in Table 1.  The ES-9 product size shown in this table assumes that all 2.5-degree regions and all hourboxes contain data.  Since the hourboxes are sparsely populated, sizing estimates per platform are 95 MB (TRMM), 260 MB (Terra), and 260 MB (Aqua).  The sizing estimate for the ES-9 in the "Archival Products Summary" table is for Aqua.  A more detailed listing of the data parameters for this product can be found in the A detailed listing of the data parameters for this product can be found in the ES-9 Collection Guide:  (Reference 3).

Level:  3

Frequency:  1/Month

Portion of Atmosphere Covered:  TOA

Time Interval Covered:		Portion of Global Covered:

File:  1 Month				File:  Global

Record:  Hourbox Data			Record:  Regional

Product Version:

TRMM:  Edition1, Edition2

Terra:  Edition1, Edition1-CV, Edition2, Edition3, Edition4

Aqua:  Edition1, Edition1-CV, Edition2, Edition3, Edition4

NPP:  Edition1-CV

ES-9 Metadata

The content of the ES-9 is summarized in Table 1.  The metadata structures contain information which need only be recorded once per monthly product.   The CERES Metadata are listed in Appendix B.  The ES-9 Product-specific Metadata are shown in Table 2.

| Table 1. ES-9 Product Summary |
| --- |
| HDF Name | Description | Records | Number of Fields | Nominal Size (MB) |
| CERES Baseline Header Metadata | See Table B-1 | 1 | 35 |  |
| CERES_metadata Vdata | See Table B-2 | 1 | 14 |  |
| ES-9 Product Specific Metadata | See Table 2 | 1 | 1 |  |
| ES-9 Vgroup Summary | See Table 3 | 1 | 6 | 1099.115 |
| ES-9 TOTAL SIZE (MB/Month) | 1099.115 |

| Table 2. ES-9 Product Specific Metadata |
| --- |
| Item | Parameter Name | Records | Units | Range | Data Type |
| 1 | ES9BinaryProductionDate | 1 | N/A | N/A | ASCII string |

ES-9 Scientific Data Sets

The ES-9 contains science parameters written as HDF Scientific Data Sets (SDSs) which are 1- or 2-dimensional arrays of spatially ordered records that are organized by Vgroups.  An overview of each of these Vgroups is given in Table 3.  Detailed definitions of each parameter on the ES-9 may be found in the ES-9 Collection Guide (Reference 3).

| Table 3. ES-9 Vgroup Summary |
| --- |
| Vgroup Number | Vgroup Name | Description | Number of Records | Maximum SDS Size (MB) |
| 1 | Regional Summary Data | See Table 4 | 10368a x 10a | 0.396 |
| 2 | Monthly (Day) Averages | See Table 5 | 10368a x 28b | 1.107 |
| 3 | Monthly (Hour) Averages | See Table 5 | 10368a x 28b | 1.107 |
| 4 | Daily Averages | See Table 5 | 10368a x 31 x 28b | 34.330 |
| 5 | Monthly Hourly Averages | See Table 5 | 10368a x 24 x 34b | 32.273 |
| 6 | Hourbox Data | See Table 5 | (10368 x 744)c x 34b | 1029.902 |
| Total SDS size (MB) | 1,099.115 |

a.	The first dimension of the SDS will equal the number of 2.5-degree regions contained on the ES-9.

b.	This dimension represents the number of SDS parameters contained in the Vgroup.

c.	The first dimension of this SDS is equal to the sum of the number of hourboxes per region over all the regions actually contained on this ES-9, or it is equal to the sum of all "Number of hourboxes" from the Regional Summary Data Vgroup.  10,368 is the maximum number of 2.5-degree regions, and 744 is the maximum number of hourboxes per region, so the maximum size of the first dimension for this SDS is 10,368 x 744 = 7,713,792.

Table 4 lists the SDSs contained in the Regional Summary Data Vgroup.

Table 4. Regional Summary Data

Parameter Name

See Table 5-4 in ES-9 Collection Guide

Region number

Longitude

Colatitude

Geographic scene type

Scene fraction histogram (1)

Scene fraction histogram (2)

Scene fraction histogram (3)

Scene fraction histogram (4)

Number of hourboxes

Start position of hourbox data

Table 5 lists the SDSs contained in the Temporal Vgroups for each 2.5-deg region

| Table 5. Temporal Vgroups for 2.5-deg Regions |
| --- |
| Parameter Name | Temporal Vgroups |
|  | Monthly (Day) Averages | Monthly (Hour) Averages | Daily Averages | Monthly Hourly Averages |
| Sky (Cloud Cover) Vgroup | Total | Clear | Total | Clear | Total | Clear | Total | Clear |
| Table in ES-9 Collection Guide | 5-5 | 5-6 | 5-7 | 5-8 | 5-9 | 5-10 | 5-11 | 5-12 |
| Region number | X | X | X | X | X | X | X | X |
| Solar constant, distance corrected |  |  |  |  | X | X |  |  |
| Solar incidence | X | X | X | X | X | X | X | X |
| Net radiant flux | X | X | X | X |  |  |  |  |
| Longwave flux | X | X | X | X | X | X | X | X |
| Longwave flux minimum value | X | X | X | X | X | X | X | X |
| Longwave flux maximum value | X | X | X | X | X | X | X | X |
| Longwave flux standard deviation | X | X | X | X | X | X | X | X |
| Number of hours of longwave flux |  |  | X | X | X | X |  |  |
| Number of days of longwave flux | X | X |  |  |  |  | X | X |
| Longwave sum of estimates |  |  |  |  |  |  | X | X |
| Longwave sum of estimates squared |  |  |  |  |  |  | X | X |
| Shortwave flux | X | X | X | X | X | X | X | X |
| Shortwave flux minimum value | X | X | X | X | X | X | X | X |
| Shortwave flux maximum value | X | X | X | X | X | X | X | X |
| Shortwave flux standard deviation | X | X | X | X | X | X | X | X |
| Number of hours of shortwave flux |  |  | X | X | X | X |  |  |
| Number of days of shortwave flux | X | X |  |  |  |  | X | X |
| Shortwave sum of estimates |  |  |  |  |  |  | X | X |
| Shortwave sum of estimates squared |  |  |  |  |  |  | X | X |
| Albedo | X | X | X | X | X | X | X | X |

Table 6 lists the SDSs contained in the Hourbox Data Vgroup.

| Table 6. Hourbox Data |
| --- |
| Parameter Name | Parameter Name |
| See Table 5-13 in ES-9 Collection Guide |
| Region number | Longwave flux minimum value |
| Number of hourboxes | Longwave flux maximum value |
| Hourbox number | Longwave flux standard deviation |
| Time of observation | Number of longwave flux estimates |
| Scene fraction (1) | Longwave flux maximum difference |
| Scene fraction (2) | Shortwave flux |
| Scene fraction (3) | Shortwave flux minimum value |
| Scene fraction (4) | Shortwave flux maximum value |
| Albedo factor (1) | Shortwave flux standard deviation |
| Albedo factor (2) | Number of shortwave flux estimates |
| Albedo factor (3) | Shortwave flux maximum difference |
| Albedo factor (4) | Clear-sky longwave flux |
| Cosine of the solar zenith angle | Clear-sky longwave flux standard deviation |
| Satellite zenith angle | Number of clear-sky longwave flux estimates |
| Azimuth angle | Clear-sky albedo standard deviation |
| Solar incidence | Longitude |
| Longwave flux | Colatitude |

ES-9 Revision Record

The product Revision Record contains information pertaining to approved section changes.  The table lists the date the Software Configuration Change Request (SCCR) was approved, the Release and Version Number, the SCCR number, a short description of the revision, and the revised sections.  The authors are listed on the document cover.

| ES-9 Revision Record |
| --- |
| SCCR Approval Date | Release/ Version Number | SCCR Number | Description of Revision | Section(s) Affected |
| N/A | R3V1 | N/A | Updated format to comply with standards. | All |
| 02/26/04 | R4V1 | 507 | Updated product versions for Aqua Edition1 to include Edition2. | All |
|  |  |  | Updated format to comply with standards. | All |
|  |  |  | The EOSDIS Product Code line was removed from the document. (6/17/2008) | Sec. 2.3 |
|  |  |  | Some links were not working. They have now been modified. (12/09/2010) | All |
| 04/27/12 | R6V1 | 895 | Updated to add Terra/Aqua/NPP Edition1-CV, and Terra/Aqua Edition3. | Sec. 2.2 |
|  |  |  | The ASDC footer was added to the bottom of the document. (06/05/2013) | All |
| 9/08/11 | R7V1 | 867 | Added Edition4 for Aqua and Terra. | Product Version |
|  |  |  | Eliminated section numbers from the Data Products Catalog. Specifically, in this document, section number 2.3 was removed. (12/05/2013) | All |
|  |  |  | Updated some links to refer to the .pdf file instead of the .doc file and to refer to a specific .pdf document instead of the Website. (06/20/2014) | All |