MODIS Cloud Imager Data (MODIS CID)

MODIS Cloud Imager Data (CID_MODIS) from the EOS spacecraft is a Level-1B data set with nineteen of the MODIS channels.  CID_MODIS consists of two or more data sets.  The first is the Level-1B data set, which contains the calibrated radiances; and the second is the companion Geolocation data set.  The sizes listed in the following data description reflect the estimated number of scan line records (200) in 5 minutes of data.  The files are written in Hierarchical Data Format (HDF) and are composed of Scientific Data Sets (SDS) and Vdatas.

The MODIS Level-1B HDF Structure Summary, Table 1, lists the types and names of HDF structures contained in the Level-1B product along with the names of the structures.  A complete listing of parameters for the Level 1B data product can be found in Table 2 through Table 3.  The MODIS Geolocation HDF Structure Summary, Table 4, lists the names and types of HDF structures contained in the geolocation product.  A complete listing of the parameters for the MODIS Geolocation product can be found in Table 4 and Table 5.  For more information on the MODIS Project, see Reference 6.

It is assumed that only Earth-viewing radiances and uncertainties and any information needed to interpret these values from the Level-1B product will be sent to the LaRC DAAC.  The channels currently requested by the CERES Science Team are

| Channels | Micron | Resolution (km) | Channels | Micron | Resolution (km) |
| --- | --- | --- | --- | --- | --- |
| Channel 1 | 0.645 | 0.25 & 1 | Channel 26 | 1.38 | 1 |
| Channel 6 | 1.64 | 1 | Channel 27 | 6.7 | 1 |
| Channel 7 | 2.13 | 1 | Channel 28 | 8.55 | 1 |
| Channel 17 | 0.91 | 1 | Channel 31 | 11.0 | 1 |
| Channel 18 | 0.93 | 1 | Channel 32 | 12.0 | 1 |
| Channel 19 | 0.94 | 1 | Channel 33 | 13.3 | 1 |
| Channel 20 | 3.75 | 1 | Channel 34 | 13.6 | 1 |
| Channel 23 | 4.0 | 1 | Channel 35 | 13.9 | 1 |
| Channel 24 | 4.46 | 1 | Channel 36 | 14.2 | 1 |
| Channel 25 | 4.52 | 1 |  |  |  |

Level: 1B			Portion of Globe Covered

Type: Ancillary			File: Satellite Swath

Frequency: 1 per 5.0-Min			Record: .25 - 1.0-km by .25 - 1.0-km

Time Interval Covered		Portion of Atmosphere Covered

File: 5.0-Min			File: Satellite Altitude

Record: Instantaneous

| MODIS Level-1B HDF Structure Summary |
| --- |
| HDF Name | HDF Structure Type | Num Records | Table Number | Size (bytes) |
| MODIS Core Metadata | HDF Annotations | 1 | Reference 6 | 10 000 |
| MODIS Archive Metadata | HDF Annotations | 1 | Reference 6 | 10 000 |
| MODIS Product Specific Metadata | HDF Annotations | 1 | Reference 6 | 10 000 |
| MODIS Swath Data | Vdata Structure | 1 | Table 2 | 72 |
| MODIS Level 1-B SDS | SDSs | 1 .. 1044 | Table 3 | 294 693 396 |
| Total MODIS Level-1B Bytes/File: |  |  |  | 294 723 468 |

| MODIS Level-1B Swath Data Vdata |
| --- |
| Field Name | Description | Field Num | Num Records | Data Type | Units | Range |
| Scan Number | Scan number | 1 | 1 | 32-bit integer | N/A | 1 .. 200 |
| Complete Scan Flag | 1 = Complete scan , 0 = Incomplete scan | 2 | 1 | 32-bit integer | N/A | 0 .. 1 |
| Total Frames | Total number of frames in scan | 3 | 1 | 32-bit integer | N/A | TBD |
| EV_Frames | Total number of earth view frames | 4 | 1 | 32-bit integer | N/A | TBD |
| SD_Frames | Total number of solar diffuser frames | 5 | 1 | 32-bit integer | N/A | TBD |
| SRCA_Frames | Total number of SRCA frames | 6 | 1 | 32-bit integer | N/A | TBD |
| BB_Frames | Total number of blackbody frames | 7 | 1 | 32-bit integer | N/A | TBD |
| SV_Frames | Total number of space view frames | 8 | 1 | 32-bit integer | N/A | TBD |
| Scan Type | Type of scan (day, night, mixed) | 9 | 1 | 8-bit character | N/A | N/A |
| Scan Start Time | Start time of scan | 10 | 1 | 64-bit float | TBD | TBD |
| Mirror Side | TBD | 11 | 1 | 8-bit integer | N/A | 1 .. 2 |
| Scan Data Presence | TBD | 12 | 1 | 32-bit integer | TBD | TBD |
| Missing Packets | TBD | 13 | 1 | 32-bit integer | TBD | TBD |
| Packets with Bad CRC | TBD | 14 | 1 | 32-bit integer | TBD | TBD |
| Discarded Packets | TBD | 15 | 1 | 32-bit integer | TBD | TBD |
| Moon in SV Port | TBD | 16 | 1 | 8-bit integer | TBD | 0 .. 1 |
| On-Orbit Maneuver | TBD | 17 | 1 | 8-bit integer | TBD | 0 .. 1 |
| No. SV Outliers | TBD | 18 | 1 | 32-bit integer | TBD | 0 .. 15 |
| No. BB Outliers | TBD | 19 | 1 | 32-bit integer | TBD | 0 .. 15 |
| No. thermistor outliers | TBD | 20 | 1 | 32-bit integer | TBD | 0 .. 12 |

| MODIS Level-1B Science Data Sets |
| --- |
| SDS Name | Description | Rank | Dimensions | Data Type | Units | Range |
| Latitude | Subset of the geodetic latitude | 2 | {2000, 271} scan x pixel | 32-bit float | deg | -90 .. 90 |
| Longitude | Subset of the geodetic longitude | 2 | {2000, 271} scan x pixel | 32-bit float | deg | -180 .. 180 |
| Dimensions | Values of the various dimensions in the product | 1 | {45} | 32-bit integer | N/A | N/A |
| Slope_and_Offset | Values needed to convert scaled instrument data to radiances | 2 | {38, 8} band x scale quantity | 32-bit float | N/A | N/A |
| SD sector Pixel quality | Solar diffuser pixel quality | 3 | {200, 30, 10} scan x SD frame x track | 16-bit integer | TBD | TBD |
| SRCA sector Pixel quality | SRCA pixel quality | 3 | {200, 40, 10} scan x SRCA frame x track | 16-bit integer | TBD | TBD |
| BB sector Pixel quality | Blackbody pixel quality | 3 | {200, 50, 10} scan x BB frame x track | 16-bit integer | TBD | TBD |
| SV sector Pixel quality | Space view pixel quality | 3 | {200, 30, 10} scan x SV frame x track | 16-bit integer | TBD | TBD |
| Earth sector Pixel quality | Earth View pixel quality | 3 | {200, 1354, 10} scan x EV frame x track | 16-bit integer | TBD | TBD |
| EV_250_RefSB | Band 1 radiances at 1/4 km resolution | 3 | {1, 8000, 5416} band x scan x pixel | 16-bit integer | W m-2sr-1m-1 | TBD |
| EV_250_RefSB_ Uncert_Indexes | Band 1 uncertainty indexes at 1/4 km resolution | 3 | {1, 8000, 5416} band x scan x pixel | 8-bit integer | N/A | TBD |
| EV_250_Aggr1km_RefSB | Band 1 radiances at 1 km resolution | 3 | {1, 2000, 1354} band x scan x pixel | 16-bit integer | W m-2sr-1m-1 | TBD |
| EV_250_Aggr1km_RefSB_Uncert_Indexes | Band 1 uncertainty indexes at 1 km resolution | 3 | {1, 2000, 1354} band x scan x pixel | 8-bit integer | N/A | TBD |
| EV_500_Aggr1km_RefSB | Band 6, 7 radiances at 1 km resolution | 3 | {2, 2000, 1354} band x scan x pixel | 16-bit integer | W m-2sr-1m-1 | TBD |
| EV_500_Aggr1km_RefSB_Uncert_Indexes | Band 6, 7 uncertainty indexes at 1 km resolution | 3 | {2, 2000, 1354} band x scan x pixel | 8-bit integer | N/A | TBD |
| EV_1KM_RefSB | Band 17, 18, 19, 26 radiances at 1 km resolution | 3 | {4, 2000, 1354} band x scan x pixel | 16-bit integer | W m-2sr-1m-1 | TBD |
| EV_1KM_RefSB_ Uncert_Indexes | Band 17, 18, 19, 26 uncertainty indexes at 1 km resolution | 3 | {4, 2000, 1354} band x scan x pixel | 8-bit integer | N/A | TBD |
| EV_1KM_Emissive | Band 20, 23, 24, 25, 27, 29, 31, 32, 33, 34, 35, 36 radiances at 1 km resolution | 3 | {12, 2000, 1354} band x scan x pixel | 16-bit integer | W m-2sr-1m-1 | TBD |
| EV_1KM_Emissive_ Uncert_Indexes | Band 20, 23, 24, 25, 27, 29, 31, 32, 33, 34, 35, 36 uncertainty indexes at 1 km resolution | 3 | {12, 2000, 1354} band x scan x pixel | 8-bit integer | N/A | TBD |

| MODIS Geolocation HDF Structure Summary |
| --- |
| HDF Name | HDF Structure Type | Num Records | Table Number | Size (bytes) |
| MODIS Geolocation Core Metadata | HDF Annotations | 1 | Reference 6 | 10 000 |
| MODIS Geolocation Archive Metadata | HDF Annotations | 1 | Reference 6 | 10 000 |
| MODIS Geolocation Product Specific Metadata | HDF Annotations | 1 | Reference 6 | 10 000 |
| MODIS Geolocation Swath Structural Metadata | HDF Annotations | 1 | Reference 6 | 10 000 |
| MODIS Geolocation Data | SDS | 39 | Table 5 | 59 678 050 |
| Total MODIS Geolocation Bytes/File: |  |  |  | 59 718 050 |

| MODIS Geolocation Science Data Sets |
| --- |
| SDS Name | Description | Rank | Dimensions | Data Type | Units | Range |
| Focal_length | Focal length for detectors | 1 | {37} band | 64-bit float | m | TBD |
| band_position | Scan IFOV Offsets of band trailing edges with respect to the Optical Center | 1 | {37} band | 64-bit float | TBD | TBD |
| detector_space | Nominal detector spacing in the cross-scan direction | 1 | {37} band | 64-bit float | m | TBD |
| detector_offsets | Offsets of detector positions from nominal locations on the focal plane | 2 | {37, 2} band x {scan, track} | 64-bit float | m | TBD |
| T_offset | Offsets of the first sample for a band to time of 1km frame | 1 | {37} band | 64-bit float | TBD | TBD |
| num_samples | Number of samples per frame for each band. | 1 | {37} band | 16-bit integer | N/A | N/A |
| Scan number | Scan number in granule | 1 | {200} scan | 16-bit integer | N/A | N/A |
| EV frames | Number of Earth view frames in scan | 1 | {200} scan | 16-bit integer | N/A | N/A |
| SD frames | Number of solar diffuser frames in scan | 1 | {200} scan | 16-bit integer | N/A | N/A |
| SV frames | Number of space view frames in scan | 1 | {200} scan | 16-bit integer | N/A | N/A |
| EV start time | Earth view start time (TAI) | 1 | {200} scan | 64-bit float | sec | TBD |
| SD start time | Solar diffuser view start time (TAI) | 1 | {200} scan | 64-bit float | sec | TBD |
| SV start time | Space view start time (TAI) | 1 | {200} scan | 64-bit float | sec | TBD |
| SD Sun zenith | Sun vector zenith angle in SD frame | 1 | {200} scan | 32-bit float | deg | TBD |
| SD Sun azimuth | Sun vector azimuth angle in SD frame (clockwise rotation about SD Z axis with respect to SD Y axis) | 1 | {200} scan | 32-bit float | deg | TBD |
| Moon Vector | Moon unit vector in instrument frame | 2 | {200, 3} scan x vector dimension | 32-bit float | TBD | TBD |
| sun_ref | Unit Sun vector in ECR frame at scan center time | 2 | {200, 3} scan x vector dimension | 32-bit float | TBD | TBD |
| Mirror side | Mirror side | 1 | {200} scan | 16-bit integer | TBD | TBD |
| num_impulse | Number of mirror encoder samples for this scan | 1 | {200} scan | 8-bit integer | TBD | TBD |
| impulse_enc | Mirror angles from encoder data. | 2 | {200, 25} scan x encoder values | 64-bit float | N/A | N/A |
| impulse_time | Mirror encoder sample times from start of scan | 2 | {200, 25} scan x encoder values | 64-bit float | sec | TBD |
| L1 scan quality | L1A scan quality flags | 2 | {200, 4} scan x flag | 32-bit integer | N/A | N/A |
| Geo scan quality | Geolocation scan quality flags | 2 | {200, 4} scan x flag | 8-bit integer | N/A | N/A |
| EV center time | Earth view center frame time (TAI) | 1 | {200} scan | 64-bit float | sec | TBD |
| orb_pos | ECR orbit position at scan center time | 2 | {200, 3} scan x vector dimension | 64-bit float | m | TBD |
| orb_vel | ECR orbit velocity at scan center time | 2 | {200, 3} scan x vector dimension | 64-bit float | m sec-1 | TBD |
| T_inst2ECR | instrument-to-ECR frame transformation matrix at scan center time | 3 | {200, 3, 3} scan x vector x vector dimension | 64-bit float | TBD | TBD |
| attitude_angles | Spacecraft attitude at scan center time expressed in the Orbital Reference frame (roll, pitch, yaw) | 2 | {200, 3} scan x vector dimension | 64-bit float | deg | TBD |
| ang_rates | Spacecraft attitude rates in spacecraft reference frame (roll, pitch, yaw) | 2 | {200, 3} scan x vector dimension | 32-bit float | deg sec-1 | TBD |
| Longitude | Geodetic longitude | 2 | {2000, 1354} scan x pixel | 32-bit float | deg | -180 .. 180 |
| Latitude | Geodetic latitude | 2 | {2000, 1354} scan x pixel | 32-bit float | deg | -90 .. 90 |
| Height | Height above ellipsoid | 2 | {2000, 1354} scan x pixel | 16-bit integer | m | TBD |
| SensorZenith | Sensor (spacecraft) zenith angle | 2 | {2000, 1354} scan x pixel | 16-bit integer | deg | 0 .. 180 |
| SensorAzimuth | Sensor (spacecraft) azimuth angle | 2 | {2000, 1354} scan x pixel | 16-bit integer | deg | -180 .. 180 |
| Range | Slant range (to spacecraft) | 2 | {2000, 1354} scan x pixel | 16-bit integer | m | TBD |
| SolarZenith | Solar zenith angle | 2 | {2000, 1354} scan x pixel | 16-bit integer | deg | 0 .. 180 |
| SolarAzimuth | Solar azimuth angle | 2 | {2000, 1354} scan x pixel | 16-bit integer | deg | -180 .. 180 |
| Land/SeaMask | EOS Land/Sea Mask | 2 | {2000, 1354} scan x pixel | 8-bit integer | N/A | N/A |
| gflags | Geolocation flags | 2 | {2000, 1354} scan x pixel | 8-bit integer | N/A | N/A |

CID_MODIS Instrument Data		CID_MODIS Geolocation Data		CID_MODIS Total Data Volume

Total Bytes/File:	294 ,723,468	Total Bytes/File:	59,748,050	TotalMbytes/Granule:	338.1

Total Mbytes/File:	281.1	Total Mbytes/File:	56.98	Total Mbytes/Hour:	57.0

Total Mbytes/Hour:	3,372.2	Total Mbytes/Hour:	683.8	Total Mbytes/Day:	97,367

Total Mbytes/Day:	80,948	Total Mbytes/Day:	16,410	Total Mbytes/Month:	3,018,378

MODIS CID Revision Record

The product Revision Record contains information pertaining to approved section changes.  The table lists the date the Software Configuration Change Request (SCCR) was approved, the Release and Version Number, the SCCR number, a short description of the revision, and the revised sections.  The authors are listed on the document cover.

| MODIS CID Revision Record |
| --- |
| SCCR Approval Date | Release/ Version Number | SCCR Number | Description of Revision | Section(s) Affected |
| N/A | R3V1 | N/A | Updated format to comply with standards. | All |
|  |  |  | The EOSDIS Product Code line was removed from the document. (6/17/2008) | Sec. 4.2 |
|  |  |  | Some links were not working. They have now been modified. (12/09/2010) | All |
|  |  |  | The ASDC footer was added to the bottom of the document. (06/07/2013) | All |
|  |  |  | Eliminated section numbers from the Data Products Catalog. Specifically, in this document, section number 4.2 was removed. (12/18/2013) | All |
|  |  |  | Updated some links to refer to the .pdf file instead of the .doc file. (06/20/2014) | All |
|  |  |  | Updated document to change “mm” to “m.” (09/12/2019) | Tables 3 & 5 |