Single Scanner Footprint TOA/Surface Fluxes and Clouds (SSF)

The Single Scanner Footprint TOA/Surface Fluxes and Clouds (SSF) product contains one hour of instantaneous Clouds and the Earth's Radiant Energy System (CERES) data for a single scanner instrument.  The SSF combines instantaneous CERES data with scene information from a higher-resolution imager such as Visible/Infrared Scanner (VIRS) on TRMM or Moderate-Resolution Imaging Spectroradiometer (MODIS) on Terra and Aqua.  Scene identification and cloud properties are defined at the higher imager resolution and these data are averaged over the larger CERES footprint.  For each CERES footprint, the SSF contains the number of cloud layers and for each layer the cloud amount, height, temperature, pressure, optical depth, emissivity, ice and liquid water path, and water particle size.  The SSF also contains the CERES filtered radiances for the total, shortwave (SW), and window (WN) channels and the unfiltered SW, longwave (LW), and WN radiances.  The SW, LW, and WN radiances at spacecraft altitude are converted to Top-of-the-Atmosphere (TOA) fluxes based on the imager defined scene.  These TOA fluxes are used to estimate surface fluxes.

Only footprints with imager coverage are included on the SSF which is much less than the full set of footprints on the CERES ES-8 product.  The number of possible footprints on an SSF depends on the elevation scan mode, azimuth scan mode, and height of the satellite.  Since elevation and azimuth scan modes are programmable, the range on the number of footprints in an SSF product has been set to the largest possible range, namely 0 .. 360000 as shown in 
Table 2.  A smaller number of footprints is used in SSF sizing estimates, namely the estimated maximum number of TRMM full Earth-view footprints per hour given a normal elevation scan and an along-track azimuth scan.  Accounting for the need for imager coverage, the actual number of footprints is expected to be even smaller.  This reduction of footprints due to lack of imager coverage is very evident when CERES is operating in a cross-track azimuth scan mode.  A complete listing of parameters for this data product can be found in Table 3 to Table 15.

A more detailed listing of the data parameters for this product can be found in the SSF Collection Guide:  (Reference 3).

Level:  2

Frequency:  1/Hour

Portion of Atmosphere Covered:  Surface to TOA

Time Interval Covered:		Portion of Globe Covered:

File:  1 Hour			File:  Satellite Swath

Record:  1/100-Second			Record:  1 CERES Footprint

Product Version:

TRMM:  Edition2B

Terra:  Edition2B, Edition2F, Edition2G, Edition3A

Aqua:  Edition1A, Edition1B, Ed2A-NoSW, Edition2A, Ed2B-NoSW, Edition2B,

Ed2C-NoSW, Edition2C, Ed2C-MOD-C4-Land-IGBP, Edition2D, Ed2D-NoSW,

Edition3A, Ed3A-NoSW

SSF Metadata

SSF metadata includes the CERES Baseline Header Metadata and CERES_metadata Vdata, which are listed in Appendix B.  The SSF product-specific metadata parameters are listed in Table 1 and the SSF_Header parameters are listed in Table 2.  For TRMM SSF products, the SSF ID (SSF-H1) will be set to 117 and will contain 131 SDS parameters (SSF-1 through SSF-131).  For Terra and Aqua SSF products, the SSF ID will be set to 1117 and these products will contain an additional 29 MODIS aerosol SDS parameters (SSF-132 through SSF-160).

| Table 1. SSF Product-specific Metadata |
| --- |
| Item | Parameter Name | Units | Range | Data Type |
| 1 | PercentCrosstrackFOV | N/A | 0.0 .. 100.0 | 32-bit real |
| 2 | PercentRapsFOV | N/A | 0.0 .. 100.0 | 32-bit real |
| 3 | PercentOtherFOV | N/A | 0.0 .. 100.0 | 32-bit real |

| Table 2. SSF_Header |
| --- |
| Item | Description | Units | Range | Elements | Bytes/ Elem |
| SSF-H1 | SSF ID | N/A | 117 or 1117 | 1 | 4 |
| SSF-H2 | Character name of CERES instrument | N/A | ASCII string | 1 | 4 |
| SSF-H3 | Day and time at hour start | N/A | ASCII string | 1 | 28 |
| SSF-H4 | Character name of satellite | N/A | ASCII string | 1 | 4 |
| SSF-H5 | Character name of high resolution imager instrument | N/A | ASCII string | 1 | 8 |
| SSF-H6 | Number of imager channels | N/A | 1 .. 20 | 1 | 4 |
| SSF-H7 | Central wavelengths of imager channels | m | 0.4 .. 15.0 | 20 | 4 |
| SSF-H8 | Earth-Sun distance at hour start | AU | 0.98 .. 1.02 | 1 | 4 |
| SSF-H9 | Beta angle | deg | -90 .. 90 | 1 | 4 |
| SSF-H10 | Colatitude of subsatellite point at surface at hour start | deg | 0 .. 180 | 1 | 4 |
| SSF-H11 | Longitude of subsatellite point at surface at hour start | deg | 0 .. 360 | 1 | 4 |
| SSF-H12 | Colatitude of subsatellite point at surface at hour end | deg | 0 .. 180 | 1 | 4 |
| SSF-H13 | Longitude of subsatellite point at surface at hour end | deg | 0 .. 360 | 1 | 4 |
| SSF-H14 | Along-track angle of satellite at hour end | deg | 0 .. 330 | 1 | 4 |
| SSF-H15 | Number of footprints in SSF product | N/A | 0 .. 360000 | 1 | 4 |
| SSF-H16 | Subsystem 4.1 identification string | N/A | ASCII string | 1 | 128 |
| SSF-H17 | Subsystem 4.2 identification string | N/A | ASCII string | 1 | 128 |
| SSF-H18 | Subsystem 4.3 identification string | N/A | ASCII string | 1 | 128 |
| SSF-H19 | Subsystem 4.4 identification string | N/A | ASCII string | 1 | 128 |
| SSF-H20 | Subsystem 4.5 identification string | N/A | ASCII string | 1 | 128 |
| SSF-H21 | Subsystem 4.6 identification string | N/A | ASCII string | 1 | 128 |
| SSF-H22 | IES production date and time | N/A | ASCII string | 1 | 24 |
| SSF-H23 | MOA production date and time | N/A | ASCII string | 1 | 24 |
| SSF-H24 | SSF production date and time | N/A | ASCII string | 1 | 24 |

SSF Scientific Data Sets

The SSF contains Scientific Data Sets (SDS) which are parameter collections of along-track ordered footprints where the first dimension corresponds to the number of footprints; the last dimension corresponds to the number of parameters; and the middle dimension, if rank 3, corresponds to the number of elements in each parameter array.  This ordering is used by the C programming language and most HDF viewers.  In Fortran, the dimensions are reversed such that the number of footprints becomes the last dimension and the first dimension is the number of parameters in the SDS.  The SDSs are divided into tables which map to Vgroups of the same name.  Table 3 to Table 15 summarize the contents of each Vgroup and SDS contained within the SSF file.  The MODIS land and ocean aerosol data (SDS parameters, SSF-132 through SSF-160) described in Table 14 and Table 15 are available only on Terra and Aqua SSF products.

(Note:  the dimension n in the following tables is the number of footprints processed:  Assuming n = 245475 for sizing)

| Table 3. Time and Position |
| --- |
| Item | SDS Name (Parameter Name) | Units | Range | Dimen- sions | Data Type | Maximum Hourly Size (MB) |
| SSF-1 | Time of observation | day | 2440000 .. 2480000 | n | 64-bit real | 1.87 |
| SSF-2 | Radius of satellite from center of Earth at observation | km | 6000 .. 8000 | n | 64-bit real | 1.87 |
| SSF-3 | X component of satellite inertial velocity | km sec-1 | -10 .. 10 | n | 64-bit real | 1.87 |
| SSF-4 | Y component of satellite inertial velocity | km sec-1 | -10 .. 10 | n | 64-bit real | 1.87 |
| SSF-5 | Z component of satellite inertial velocity | km sec-1 | -10 .. 10 | n | 64-bit real | 1.87 |
| SSF-6 | Colatitude of subsatellite point at surface at observation | deg | 0 .. 180 | n | 32-bit real | 0.94 |
| SSF-7 | Longitude of subsatellite point at surface at observation | deg | 0 .. 360 | n | 32-bit real | 0.94 |
| SSF-8 | Colatitude of subsolar point at surface at observation | deg | 0 .. 180 | n | 32-bit real | 0.94 |
| SSF-9 | Longitude of subsolar point at surface at observation | deg | 0 .. 360 | n | 32-bit real | 0.94 |
| SSF-10 | Colatitude of CERES FOV at surface | deg | 0 .. 180 | n | 32-bit real | 0.94 |
| SSF-11 | Longitude of CERES FOV at surface | deg | 0 .. 360 | n | 32-bit real | 0.94 |
| SSF-12 | Scan sample number | N/A | 1 .. 660 | n | 16-bit integer | 0.47 |
| SSF-13 | Packet number | N/A | 0 .. 13100 | n | 16-bit integer | 0.47 |
| SSF-14 | Cone angle of CERES FOV at satellite | deg | 0 .. 90 | n | 32-bit real | 0.94 |
| SSF-15 | Clock angle of CERES FOV at satellite wrt inertial velocity | deg | 0 .. 360 | n | 32-bit real | 0.94 |
| SSF-16 | Rate of change of cone angle | deg sec-1 | -300 .. 300 | n | 32-bit real | 0.94 |
| SSF-17 | Rate of change of clock angle | deg sec-1 | -20 .. 20 | n | 32-bit real | 0.94 |
| SSF-18 | Along-track angle of CERES FOV at surface | deg | -30 .. 330 | n | 32-bit real | 0.94 |
| SSF-19 | Cross-track angle of CERES FOV at surface | deg | -90 .. 90 | n | 32-bit real | 0.94 |

| Table 4. Viewing Angles |
| --- |
| Item | SDS Name (Parameter Name) | Units | Range | Dimen- sions | Data Type | Maximum Hourly Size (MB) |
| SSF-20 | CERES viewing zenith at surface | deg | 0 .. 90 | n | 32-bit real | 0.94 |
| SSF-21 | CERES solar zenith at surface | deg | 0 .. 180 | n | 32-bit real | 0.94 |
| SSF-22 | CERES relative azimuth at surface | deg | 0 .. 360 | n | 32-bit real | 0.94 |
| SSF-23 | CERES viewing azimuth at surface wrt North | deg | 0 .. 360 | n | 32-bit real | 0.94 |

| Table 5. Surface Map |
| --- |
| Item | SDS Name (Parameter Name) | Units | Range | Dimen- sions | Data Type | Maximum Hourly Size (MB) |
| SSF-24 | Altitude of surface above sea level | m | -1000 .. 10000 | n | 32-bit real | 0.94 |
| SSF-25 | Surface type index | N/A | 1 .. 20 | n x 8 | 16-bit integer | 3.75 |
| SSF-26 | Surface type percent coverage | N/A | 0 .. 100 | n x 8 | 16-bit integer | 3.75 |

| Table 6. Scene Type |
| --- |
| Item | SDS Name (Parameter Name) | Units | Range | Dimen- sions | Data Type | Maximum Hourly Size (MB) |
| SSF-27 | CERES SW ADM type for inversion process | N/A | 0 .. 5000 | n | 16-bit integer | 0.47 |
| SSF-28 | CERES LW ADM type for inversion process | N/A | 0 .. 5000 | n | 16-bit integer | 0.47 |
| SSF-29 | Cloud Classification | N/A | 0 .. 32766 | n | 16-bit integer | 0.47 |
| SSF-30 | Snow/ice percent coverage clear-sky overhead-sun vis albedo | N/A | 0 .. 9999 | n | 16-bit integer | 0.47 |

| Table 7. Filtered Radiances |
| --- |
| Item | SDS Name (Parameter Name) | Units | Range | Dimen- sions | Data Type | Maximum Hourly Size (MB) |
| SSF-31 | CERES TOT filtered radiance - upwards | W m-2 sr-1 | 0 .. 700 | n | 32-bit real | 0.94 |
| SSF-32 | CERES SW filtered radiance - upwards | W m-2 sr-1 | -10 .. 510 | n | 32-bit real | 0.94 |
| SSF-33 | CERES WN filtered radiance - upwards | W m-2 sr-1mm-1 | 0 .. 15 | n | 32-bit real | 0.94 |
| SSF-34 | Radiance and Mode flags | N/A | 0 .. (231-1) | n | 32-bit integer | 0.94 |

| Table 8. Unfiltered Radiances |
| --- |
| Item | SDS Name (Parameter Name) | Units | Range | Dimen- sions | Data Type | Maximum Hourly Size (MB) |
| SSF-35 | CERES SW radiance - upwards | W m-2 sr-1 | -10 ..510 | n | 32-bit real | 0.94 |
| SSF-36 | CERES LW radiance - upwards | W m-2 sr-1 | 0 .. 200 | n | 32-bit real | 0.94 |
| SSF-37 | CERES WN radiance - upwards | W m-2 sr-1 | 0 .. 60 | n | 32-bit real | 0.94 |

| Table 9. TOA and Surface Fluxes |
| --- |
| Item | SDS Name (Parameter Name) | Units | Range | Dimen- sions | Data Type | Maximum Hourly Size (MB) |
| SSF-38 | CERES SW TOA flux - upwards | W m-2 | 0 .. 1400 | n | 32-bit real | 0.94 |
| SSF-39 | CERES LW TOA flux - upwards | W m-2 | 0 .. 500 | n | 32-bit real | 0.94 |
| SSF-40 | CERES WN TOA flux - upwards | W m-2 | 0 .. 200 | n | 32-bit real | 0.94 |
| SSF-41 | CERES downward SW surface flux - Model A | W m-2 | 0 .. 1400 | n | 32-bit real | 0.94 |
| SSF-42 | CERES downward LW surface flux - Model A | W m-2 | 0 .. 700 | n | 32-bit real | 0.94 |
| SSF-43 | CERES downward WN surface flux - Model A | W m-2 | 0 .. 250 | n | 32-bit real | 0.94 |
| SSF-44 | CERES net SW surface flux - Model A | W m-2 | 0 .. 1400 | n | 32-bit real | 0.94 |
| SSF-45 | CERES net LW surface flux - Model A | W m-2 | -250 .. 50 | n | 32-bit real | 0.94 |
| SSF-46 | CERES downward SW surface flux - Model B | W m-2 | 0 .. 1400 | n | 32-bit real | 0.94 |
| SSF-47 | CERES downward LW surface flux - Model B | W m-2 | 0 .. 700 | n | 32-bit real | 0.94 |
| SSF-48 | CERES net SW surface flux - Model B | W m-2 | 0 .. 1400 | n | 32-bit real | 0.94 |
| SSF-49 | CERES net LW surface flux - Model B | W m-2 | -250 .. 50 | n | 32-bit real | 0.94 |
| SSF-50 | CERES broadband surface albedo | N/A | 0 .. 1 | n | 32-bit real | 0.94 |
| SSF-51 | CERES LW surface emissivity | N/A | 0 .. 1 | n | 32-bit real | 0.94 |
| SSF-52 | CERES WN surface emissivity | N/A | 0 .. 1 | n | 32-bit real | 0.94 |

| Table 10. Full Footprint Area |
| --- |
| Item | SDS Name (Parameter Name) | Units | Range | Dimen- sions | Data Type | Maximum Hourly Size (MB) |
| SSF-53 | Number of imager pixels in CERES FOV | N/A | 0 .. 32766 | n | 16-bit integer | 0.47 |
| SSF-54 | Imager percent coverage | N/A | 0 .. 100 | n | 16-bit integer | 0.47 |
| SSF-55 | Imager viewing zenith over CERES FOV | deg | 0 .. 90 | n | 32-bit real | 0.94 |
| SSF-56 | Imager relative azimuth over CERES FOV | deg | 0 .. 360 | n | 32-bit real | 0.94 |
| SSF-57 | Surface wind - U-vector | m sec-1 | -100 .. 100 | n | 32-bit real | 0.94 |
| SSF-58 | Surface wind - V-vector | m sec-1 | -100 .. 100 | n | 32-bit real | 0.94 |
| SSF-59 | Surface skin temperature | K | 175 .. 375 | n | 32-bit real | 0.94 |
| SSF-60 | Column averaged relative humidity | N/A | 0 .. 100 | n | 32-bit real | 0.94 |
| SSF-61 | Precipitable water | cm | 0.001 .. 10 | n | 32-bit real | 0.94 |
| SSF-62 | Flag - Source of precipitable water | N/A | 0 .. 120 | n | 16-bit integer | 0.47 |
| SSF-63 | Cloud property extrapolation over cloudy area | N/A | 0 .. 100 | n | 16-bit integer | 0.47 |
| SSF-64 | Notes on general procedure | N/A | 0 .. 32766 | n | 16-bit integer | 0.47 |
| SSF-65 | Notes on cloud algorithms | N/A | 0 .. 32766 | n | 16-bit integer | 0.47 |

| Table 11. Clear Footprint Area |
| --- |
| Item | SDS Name (Parameter Name) | Units | Range | Dimen- sions | Data Type | Maximum Hourly Size (MB) |
| SSF-66 | Clear area percent coverage at subpixel resolution | N/A | 0 .. 100 | n | 32-bit real | 0.94 |
| SSF-67 | Cloud-mask clear-strong percent coverage | N/A | 0 .. 100 | n | 16-bit integer | 0.47 |
| SSF-68 | Cloud-mask clear-weak percent coverage | N/A | 0 .. 100 | n | 16-bit integer | 0.47 |
| SSF-69 | Cloud-mask snow/ice percent coverage | N/A | 0 .. 100 | n | 16-bit integer | 0.47 |
| SSF-70 | Cloud-mask aerosol B percent coverage | N/A | 0 .. 100 | n | 16-bit integer | 0.47 |
| SSF-71 | Flag - Type of aerosol B | N/A | 0 .. 9999 | n | 16-bit integer | 0.47 |
| SSF-72 | Cloud-mask percent coverage supplement | N/A | 0 .. 32766 | n | 16-bit integer | 0.47 |
| SSF-73 | Total aerosol A optical depth - visible | N/A | -1 .. 5 | n | 32-bit real | 0.94 |
| SSF-74 | Total aerosol A optical depth - near IR | N/A | -1 .. 5 | n | 32-bit real | 0.94 |
| SSF-75 | Aerosol A supplement 1 | N/A | -1000 .. 1000 | n | 32-bit real | 0.94 |
| SSF-76 | Aerosol A supplement 2 | N/A | -1000 .. 1000 | n | 32-bit real | 0.94 |
| SSF-77 | Aerosol A supplement 3 | N/A | -1000 .. 1000 | n | 32-bit real | 0.94 |
| SSF-78 | Aerosol A supplement 4 | N/A | -1000 .. 1000 | n | 32-bit real | 0.94 |
| SSF-79 | Imager-based surface skin temperature | K | 175 .. 375 | n | 32-bit real | 0.94 |
| SSF-80 | Vertical temperature change | K | -30 .. 90 | n | 32-bit real | 0.94 |

| Table 12. Cloudy Footprint Area |
| --- |
| Item | SDS Name (Parameter Name) | Units | Range | Dimen- sions | Data Type | Maximum Hourly Size (MB) |
| SSF-81 | Clear/layer/overlap percent coverages | N/A | 0 .. 100 | n x 4 | 32-bit real | 3.74 |
| SSF-82 | Note for cloud layer | N/A | 0 .. (231-1) | n x 2 | 32-bit integer | 1.87 |
| SSF-83 | Mean visible optical depth for cloud layer | N/A | 0 .. 400 | n x 2 | 32-bit real | 1.87 |
| SSF-84 | Stddev of visible optical depth for cloud layer | N/A | 0 .. 300 | n x 2 | 32-bit real | 1.87 |
| SSF-85 | Mean logarithm of visible optical depth for cloud layer | N/A | -6 .. 6 | n x 2 | 32-bit real | 1.87 |
| SSF-86 | Stddev of logarithm of visible optical depth for cloud layer | N/A | 0 .. 6 | n x 2 | 32-bit real | 1.87 |
| SSF-87 | Mean cloud infrared emissivity for cloud layer | N/A | 0 .. 2 | n x 2 | 32-bit real | 1.87 |
| SSF-88 | Stddev of cloud infrared emissivity for cloud layer | N/A | 0 .. 2 | n x 2 | 32-bit real | 1.87 |
| SSF-89 | Mean liquid water path for cloud layer (3.7) | g m-2 | 0 .. 10000 | n x 2 | 32-bit real | 1.87 |
| SSF-90 | Stddev of liquid water path for cloud layer (3.7) | g m-2 | 0 .. 8000 | n x 2 | 32-bit real | 1.87 |
| SSF-91 | Mean ice water path for cloud layer (3.7) | g m-2 | 0 .. 10000 | n x 2 | 32-bit real | 1.87 |
| SSF-92 | Stddev of ice water path for cloud layer (3.7) | g m-2 | 0 .. 8000 | n x 2 | 32-bit real | 1.87 |
| SSF-93 | Mean cloud top pressure for cloud layer | hPa | 0 .. 1100 | n x 2 | 32-bit real | 1.87 |
| SSF-94 | Stddev of cloud top pressure for cloud layer | hPa | 0 .. 600 | n x 2 | 32-bit real | 1.87 |
| SSF-95 | Mean cloud effective pressure for cloud layer | hPa | 0 .. 1100 | n x 2 | 32-bit real | 1.87 |
| SSF-96 | Stddev of cloud effective pressure for cloud layer | hPa | 0 .. 500 | n x 2 | 32-bit real | 1.87 |
| SSF-97 | Mean cloud effective temperature for cloud layer | K | 100 .. 350 | n x 2 | 32-bit real | 1.87 |
| SSF-98 | Stddev of cloud effective temperature for cloud layer | K | 0 .. 150 | n x 2 | 32-bit real | 1.87 |
| SSF-99 | Mean cloud effective height for cloud layer | km | 0 .. 20 | n x 2 | 32-bit real | 1.87 |
| SSF-100 | Stddev of cloud effective height for cloud layer | km | 0 .. 12 | n x 2 | 32-bit real | 1.87 |
| SSF-101 | Mean cloud base pressure for cloud layer | hPa | 0 .. 1100 | n x 2 | 32-bit real | 1.87 |
| SSF-102 | Stddev of cloud base pressure for cloud layer | hPa | 0 .. 600 | n x 2 | 32-bit real | 1.87 |
| SSF-103 | Mean water particle radius for cloud layer (3.7) | m | 0 .. 40 | n x 2 | 32-bit real | 1.87 |
| SSF-104 | Stddev of water particle radius for cloud layer (3.7) | m | 0 .. 20 | n x 2 | 32-bit real | 1.87 |
| SSF-105 | Mean ice particle effective diameter for cloud layer (3.7) | m | 0 .. 300 | n x 2 | 32-bit real | 1.87 |
| SSF-106 | Stddev of ice particle effective diameter for cloud layer (3.7) | m | 0 .. 200 | n x 2 | 32-bit real | 1.87 |
| SSF-107 | Mean cloud particle phase for cloud layer (3.7) | N/A | 1 .. 2 | n x 2 | 32-bit real | 1.87 |
| SSF-108 | Mean water particle radius for cloud layer (1.6) | m | 0 .. 40 | n x 2 | 32-bit real | 1.87 |
| SSF-109 | Mean ice particle effective diameter for cloud layer (1.6) | m | 0 .. 300 | n x 2 | 32-bit real | 1.87 |
| SSF-110 | Mean cloud particle phase for cloud layer (1.6) | N/A | 1 .. 2 | n x 2 | 32-bit real | 1.87 |
| SSF-111 | Mean vertical aspect ratio for cloud layer (TBD) | N/A | 0 .. 20 | n x 2 | 32-bit real | 1.87 |
| SSF-112 | Stddev of vertical aspect ratio for cloud layer (TBD) | N/A | 0 .. 15 | n x 2 | 32-bit real | 1.87 |
| SSF-113 | Percentiles of visible optical depth for cloud layer | N/A | 0 .. 400 | n x 13 x 2 | 32-bit real | 24.35 |
| SSF-114 | Percentiles of IR emissivity for cloud layer | N/A | 0 .. 2 | n x 13 x 2 | 32-bit real | 24.35 |

| Table 13. Footprint Imager Radiance Statistics |
| --- |
| Item | SDS Name (Parameter Name) | Units | Range | Dimen- sions | Data Type | Maximum Hourly Size (MB) |
| SSF-115 | Imager channel central wavelength | m | 0.4 .. 15.0 | n x 5 | 32-bit real | 4.68 |
| SSF-116 | All subpixel clear area percent coverage | N/A | 0 .. 100 | n | 32-bit real | 0.94 |
| SSF-117 | All subpixel overcast cloud area percent coverage | N/A | 0 ..100 | n | 32-bit real | 0.94 |
| SSF-118 | Mean imager radiances over clear area | W m-2 sr-1 m-1 | -1000 .. 1000 | n x 5 | 32-bit real | 4.68 |
| SSF-119 | Stddev of imager radiances over clear area | W m-2 sr-1 m-1 | 0 .. 1000 | n x 5 | 32-bit real | 4.68 |
| SSF-120 | Mean imager radiances over overcast cloud area | W m-2 sr-1 m-1 | -1000 .. 1000 | n x 5 | 32-bit real | 4.68 |
| SSF-121 | Stddev of imager radiances over overcast cloud area | W m-2 sr-1 m-1 | 0 .. 1000 | n x 5 | 32-bit real | 4.68 |
| SSF-122 | Mean imager radiances over full CERES FOV | W m-2 sr-1 m-1 | -1000 .. 1000 | n x 5 | 32-bit real | 4.68 |
| SSF-123 | Stddev of imager radiances over full CERES FOV | W m-2 sr-1 m-1 | 0 .. 1000 | n x 5 | 32-bit real | 4.68 |
| SSF-124 | 5th percentile of imager radiances over full CERES FOV | W m-2 sr-1 m-1 | -1000 .. 1000 | n x 5 | 32-bit real | 4.68 |
| SSF-125 | 95th percentile of imager radiances over full CERES FOV | W m-2 sr-1 m-1 | -1000 .. 1000 | n x 5 | 32-bit real | 4.68 |
| SSF-126 | Mean imager radiances over cloud layer 1 (no overlap) | W m-2 sr-1 m-1 | -1000 .. 1000 | n x 5 | 32-bit real | 4.68 |
| SSF-127 | Stddev of imager radiances over cloud layer 1 (no overlap) | W m-2 sr-1 m-1 | 0 .. 1000 | n x 5 | 32-bit real | 4.68 |
| SSF-128 | Mean imager radiances over cloud layer 2 (no overlap) | W m-2 sr-1 m-1 | -1000 .. 1000 | n x 5 | 32-bit real | 4.68 |
| SSF-129 | Stddev of imager radiances over cloud layer 2 (no overlap) | W m-2 sr-1 m-1 | 0 .. 1000 | n x 5 | 32-bit real | 4.68 |
| SSF-130 | Mean imager radiances over cloud layer 1 and 2 overlap | W m-2 sr-1 m-1 | -1000 .. 1000 | n x 5 | 32-bit real | 4.68 |
| SSF-131 | Stddev of imager radiances over cloud layer 1 and 2 overlap | W m-2 sr-1 m-1 | 0 .. 1000 | n x 5 | 32-bit real | 4.68 |

The MODIS land aerosol parameters described in Table 14 are only available on Terra and Aqua SSF products.

| Table 14. MODIS Land Aerosols |
| --- |
| Item | SDS Name (Parameter Name) | Units | Range | Dimen- sions | Data Type | Maximum Hourly Size (MB) |
| SSF-132 | Percentage of CERES FOV with MODIS land aerosol | N/A | 0 .. 100 | n | 16-bit integer | 0.47 |
| SSF-133 | PSF-wtd MOD04 cloud fraction land | N/A | 0 .. 100 | n | 16-bit integer | 0.47 |
| SSF-134 | PSF-wtd MOD04 aerosol types land | N/A | 0 .. 9999 | n | 32-bit integer | 0.94 |
| SSF-135 | PSF-wtd MOD04 dust weighting factor land | N/A | 0.0 .. 1.0 | n | 32-bit real | 0.94 |
| SSF-136 | PSF-wtd MOD04 corrected optical depth land (0.470) | N/A | 0.0 .. 5.0 | n | 32-bit real | 0.94 |
| SSF-137 | PSF-wtd MOD04 corrected optical depth land (0.550) | N/A | 0.0 .. 5.0 | n | 32-bit real | 0.94 |
| SSF-138 | PSF-wtd MOD04 corrected optical depth land (0.659) | N/A | 0.0 .. 5.0 | n | 32-bit real | 0.94 |
| SSF-139 | MOD04 number pixels percentile land (0.659) in CERES FOV | N/A | 0 .. (231-1) | n | 32-bit integer | 0.94 |
| SSF-140 | PSF-wtd MOD04 mean reflectance land (0.470) | N/A | 0.0 .. 1.0 | n | 32-bit real | 0.94 |
| SSF-141 | PSF-wtd MOD04 mean reflectance land (0.659) | N/A | 0.0 .. 1.0 | n | 32-bit real | 0.94 |
| SSF-142 | PSF-wtd MOD04 mean reflectance land (0.865) | N/A | 0.0 .. 1.0 | n | 32-bit real | 0.94 |
| SSF-143 | PSF-wtd MOD04 mean reflectance land (2.130) | N/A | 0.0 .. 1.0 | n | 32-bit real | 0.94 |
| SSF-144 | PSF-wtd MOD04 mean reflectance land (3.750) | N/A | 0.0 .. 1.0 | n | 32-bit real | 0.94 |
| SSF-145 | PSF-wtd MOD04 std reflectance land (0.470) | N/A | 0.0 .. 2.0 | n | 32-bit real | 0.94 |

The MODIS ocean aerosol parameters described in Table 15 are only available on Terra and Aqua SSF products.

| Table 15. MODIS Ocean Aerosols |
| --- |
| Item | SDS Name (Parameter Name) | Units | Range | Dimen- sions | Data Type | Maximum Hourly Size (MB) |
| SSF-146 | Percentage of CERES FOV with MODIS ocean aerosol | N/A | 0 .. 100 | n | 16-bit integer | 0.47 |
| SSF-147 | PSF-wtd MOD04 cloud fraction ocean | N/A | 0 .. 100 | n | 16-bit integer | 0.47 |
| SSF-148 | PSF-wtd MOD04 solution indices ocean small, average | N/A | 0 .. 99999 | n | 32-bit integer | 0.94 |
| SSF-149 | PSF-wtd MOD04 solution indices ocean large, average | N/A | 0 .. 99999 | n | 32-bit integer | 0.94 |
| SSF-150 | PSF-wtd MOD04 effective optical depth average ocean (0.470) | N/A | 0.0 .. 5.0 | n | 32-bit real | 0.94 |
| SSF-151 | PSF-wtd MOD04 effective optical depth average ocean (0.550) | N/A | 0.0 .. 5.0 | n | 32-bit real | 0.94 |
| SSF-152 | PSF-wtd MOD04 effective optical depth average ocean (0.659) | N/A | 0.0 .. 5.0 | n | 32-bit real | 0.94 |
| SSF-153 | PSF-wtd MOD04 effective optical depth average ocean (0.865) | N/A | 0.0 .. 5.0 | n | 32-bit real | 0.94 |
| SSF-154 | PSF-wtd MOD04 effective optical depth average ocean (1.240) | N/A | 0.0 .. 5.0 | n | 32-bit real | 0.94 |
| SSF-155 | PSF-wtd MOD04 effective optical depth average ocean (1.640) | N/A | 0.0 .. 5.0 | n | 32-bit real | 0.94 |
| SSF-156 | PSF-wtd MOD04 effective optical depth average ocean (2.130) | N/A | 0.0 .. 5.0 | n | 32-bit real | 0.94 |
| SSF-157 | PSF-wtd MOD04 optical depth small average ocean (0.550) | N/A | 0.0 .. 5.0 | n | 32-bit real | 0.94 |
| SSF-158 | PSF-wtd MOD04 optical depth small average ocean (0.865) | N/A | 0.0 .. 5.0 | n | 32-bit real | 0.94 |
| SSF-159 | PSF-wtd MOD04 optical depth small average ocean (2.130) | N/A | 0.0 .. 5.0 | n | 32-bit real | 0.94 |
| SSF-160 | PSF-wtd MOD04 cloud condensation nuclei ocean, average | CCN cm-2 | 0.0 .. 1*1010 | n | 32-bit real | 0.94 |

Estimated GigaBytes / Day:		6.8

SSF Revision Record

The product Revision Record contains information pertaining to approved section changes.  The table lists the date the Software Configuration Change Request (SCCR) was approved, the Release and Version Number, the SCCR number, a short description of the revision, and the revised sections.  The authors are listed on the document cover.

| SSF Revision Record |
| --- |
| SCCR Approval Date | Release/ Version Number | SCCR Number | Description of Revision | Section(s) Affected |
| N/A | R3V1 | N/A | Updated document to reflect new formats and to comply with standards. | All |
| 6/21/02 | R3V2 | 367 | Changed range of SSF ID in SSF_Header. | SSF Metadata |
|  |  |  | Added 2 tables for data available on Terra and Aqua products. | Tables 2.5-14 & 2.5-15 |
|  |  |  | Added explanation about differences between TRMM products and the Terra and Aqua products. | SSF Scientific Data Sets |
|  |  |  | Modified cover page to add information for all CERES satellites. | Cover page |
|  |  |  | Added Revision Record page. | SSF Revision Record |
|  |  |  | Updated format to comply with standards. | All |
| 5/21/03 | R3V3 | 438 | Changed range of PSF-wtd MOD04 effective optical depths (SSF-136 to SSF-138; SSF-150 to SSF-159) from 0.0 .. 3.0 to 0.0 .. 5.0 based on changes to v003 MOD04 inputs starting with data date 01.Apr.2002. | Tables 2.5-14 & 2.5-15 |
|  |  |  | Added Beta1 data set for Aqua satellite. | Cover page |
|  |  |  | Updated format to comply with standards | All |
| 8/27/03 | R3V4 | 463 | Changed range for ADM geo (SSF-30) and removed the ’(TBD)’ in the parameter name. | Table 2.5-6 |
|  |  |  | Updated format to comply with standards. | All |
| 6/04/04 | R4V1 | 533 | Changed (SSF-30) SDS name from "ADM geo" to "Snow/ice percent coverage clear-sky overhead-sun vis albedo." | Table 2.5-6 |
|  |  |  | Changed (SSF-29) SDS name from "CERES WN ADM type for inversion process" to "Cloud Classification." | Table 2.5-6 |
|  |  |  | Changed (SSF-29) Range from "0 .. 5000" to "0 .. 32766." | Table 2.5-6 |
|  |  |  | Updated format to comply with standards. | All |
| 6/15/07 | R4V2 | 659 | Added additional versions for Terra and Aqua. | Product Version Section |
|  |  |  | The EOSDIS Product Code line was removed from the document. (6/17/2008) | Sec. 2.5 |
| 5/28/08 | R4V3 | 673 | Added Edition2C-MOD-C4-Land-IGBP version for Terra and Aqua. | Product Version Section |
| 12/08/08 12/18/09 | R5V1 | 690 751 | Added Edition2D/Ed2D-NoSW for Aqua. Added Edition2G version for Terra. | Product Version Section |
|  |  |  | Some links were not working. They have now been modified. (12/09/2010) | All |
| 10/13/10 | R5V2 | 811 | Added Edition3A version for Terra. | Product Version |
| 10/13/10 |  | 812 | Added Edition3A/Ed3A-NoSW for Aqua. | Product Version |
|  |  |  | The ASDC footer was added to the bottom of the document. (06/11/2013) | All |
|  |  |  | Eliminated section numbers from the Data Products Catalog. Specifically, in this document, section number 2.5 was removed. (12/06/2013) | All |
|  |  |  | Updated some links to refer to the .pdf file instead of the .doc file and to refer to a specific .pdf document instead of the Website. (06/20/2014) | All |