CERES Time-Interpolated TOA Fluxes, Clouds and Aerosols
(SSF1deg-Day)

The SSF1deg-Day product provides daily mean CERES-observed top-of-atmosphere (TOA) radiative fluxes and coincident MODIS-derived cloud and aerosol properties based on the SSF Level 2 measurements. First, each parameter is spatially gridded into a 1° nested grid. Second, the parameters are temporally interpolated between the times of the CERES observations to produce a complete 1-hourly time series for the month. The SSF1deg TOA fluxes are temporally interpolated using the assumption of constant meteorological conditions. For longwave fluxes over oceans and snow/ice surfaces, linear interpolation is used, whereas over land, the daytime heating is estimated using a half-sine curve centered on noon. For shortwave fluxes, empirical diurnal albedo models defined as a function of solar zenith angle and based on cloud and surface conditions are used. The cloud properties are linearly interpolated in time for each layer and are weighted by cloud fraction to compute the total cloud properties. Only clear-sky CERES footprints, which have cloud fractions less than 0.1%, are used to compute the clear-sky parameters. If no regional clear-sky footprints are observed over the month, all clear-sky parameters are set to default. Daily means are calculated using the combination of hourly observed and temporally interpolated parameters for days containing at least one CERES observation.

The SSF1deg-Day product contains these daily mean parameters at the 1°–regional spatial scale:

•	All-sky and clear-sky radiative shortwave (SW), longwave (LW), window-channel (WN) and net fluxes at TOA

•	Total and 4-layered cloud properties for day/night (24-hour) and daytime only

•	Auxiliary parameters, such as aerosol optical depths, skin temperature, and precipitable water, that are used as input to process the CERES fluxes

•	Solar incoming flux

The SSF1deg products are processed separately for each satellite. Although Terra and Aqua have two CERES instruments each, only the instrument in cross-track mode on each satellite is used.

The product data file is written in HDF and is organized by Vgroups containing collections of science parameters written as Scientific Data Sets (SDSs). Each file contains data for one month.

More information about the CERES products can be obtained on the CERES subsetter ordering web page (http://ceres.larc.nasa.gov/order_data.php).

Level:  3

Frequency:  1/Month

Portion of Atmosphere Covered:  TOA

Time Interval Covered:		Portion of Globe Covered:

File:  1 Month			File:  Entire Globe

Record:  1.0-Degree Regions

Product Version:

TRMM:  N/A

Terra:  Edition3A, Edition4A

Aqua:  Edition3A, Edition4A

NPP:  Edition1A

SSF1deg-Day Definition

Table 1 summarizes the overall structure of the SSF1deg-Day HDF file. The HDF file contains metadata in the form of file attributes and a Vdata structure, Vgroups of Scientific Data Sets (SDSs), and dimension scales.

| SSF1deg-Day HDF structure summary. |
| --- |
| Name | Description |
| CERES Baseline Header Metadata | Table B-1 |
| CERES_metadata Vdata | Table B-2 |
| SSF1deg-Day Product-specific Metadata | Table 2 |
| Vgroups of SDSs | Table 5 through Table 13 |
| Dimension Scales | Table 29 |

SSF1deg-Day Metadata

Metadata for the SSF1deg-Day product is contained in three components of the HDF file: two file attributes named coremetadata and archivemetadata and one Vdata structure named CERES_metadata. The information contained in these three components is listed in Appendix B. Metadata that is specific to the SSF1deg-Day product is listed in Table 2; it may be found within the coremetadata attribute.

| SSF1deg-Day product-specific metadata. |
| --- |
| Item | Parameter Name | Units | Range | Data Type |
| 1 | identifier_product_doi | N/A | N/A | string |

SSF1deg-Day Dimensions

Regional (1° latitude x 1° longitude) SDSs are three-dimensional day/latitude/longitude arrays of daily means for the month with Ndayx180x360 elements, where Nday is the number of days in a given month (ranging from 28 to 31). The day index indicates the day of the month. The values of the latitude and longitude indices are shown in Table 3. Cloud parameter SDSs have an additional dimension indicating cloud layer and have 5xNdayx180x360 elements. Values of the cloud layer index are shown in Table 4. There are no zonal or global means in the SSF1deg-Day product.

| Definitions of the latitude and longitude dimensions for the CERES equal-angle 1° latitude by 1° longitude grid. |
| --- |
| Dimension | Size | Definition |
| latitude | 180 | Index #1 is at 89.5°N and #180 is at 89.5°S. |
| longitude | 360 | Index #1 is at 179.5°W and #360 is at 179.5°E. |

| Definition of the cloud_layer dimension. |
| --- |
| Cloud_layer index | Cloud Layer | Pressure layer (hPa) |
| 1 | High | 50-300 |
| 2 | Upper Mid | 300-500 |
| 3 | Lower Mid | 500-700 |
| 4 | Low | 700-Surface |
| 5 | Total | 50 - Surface |

Daily Regional Scientific Data Sets

The tables contained in this section list all daily regional mean parameters in the file. The daily regional mean Scientific Data Sets (SDS) are divided into Vgroups; these Vgroups and their corresponding tables of SDSs are listed in Table 5. All SDS tables include the SDS index, SDS name, long name, data type, units, data range, and the number of elements for each SDS.

Regional (1° latitude x 1° longitude) SDSs are three-dimensional day/latitude/longitude arrays of daily means for the month with Ndayx180x360 elements, where Nday is the number of days in a given month (ranging from 28 to 31). The day index indicates the day of the month. The values of the latitude and longitude indices are shown in Table 3. Cloud parameter SDSs have an additional dimension indicating cloud layer and have 5xNdayx180x360 elements. Values of the cloud layer index are shown in Table 4.

| List of the Vgroups contained in the SSF1deg-Day product |
| --- |
| Vgroup Number | Vgroup Name | SDS Table | Number of SDSs |
| 0 | Regional_Information | Table 6 | 3 |
| 1 | CERES_TOA_Fluxes | Table 7 | 11 |
| 2 | Meteorological_Variables | Table 8 | 9 |
| 3 | CERES_MODIS_Cloud_Layer_Properties_24Hour_Averages | Table 9 | 25 |
| 4 | CERES_MODIS_Cloud_Layer_Properties_Daylight_Only_Averages | Table 10 | 25 |
| 5 | MODIS_Land_Aerosols | Table 11 | 2 |
| 6 | MODIS_Ocean_Aerosols | Table 12 | 2 |
| 7 | Number_of_Observations | Table 13 | 4 |

| Regional_Information |
| --- |
| SDS Index | SDS Name | Long Name | Data Type | Units | Range | Number of Elements |
| 0 | sfc_altitude | Altitude of Surface Above Sea Level | 32-bit real | m | -1000 .. 10000 | Ndayx180x360 |
| 1 | ocean_coverage | Ocean Percent Coverage | 32-bit real | % | 0 .. 100 | Ndayx180x360 |
| 2 | snow_ice_coverage | Snow/Ice Percent Coverage | 32-bit real | % | 0 .. 100 | Ndayx180x360 |

| CERES_TOA_Fluxes |
| --- |
| SDS Index | SDS Name | Long Name | Data Type | Units | Range | Number of Elements |
| 3 | clr_toa_sw | CERES Clear-Sky TOA SW Flux | 32-bit real | W m-2 | 0 .. 1400 | Ndayx180x360 |
| 4 | clr_toa_lw | CERES Clear-Sky TOA LW Flux | 32-bit real | W m-2 | 0 .. 500 | Ndayx180x360 |
| 5 | clr_toa_wn | CERES Clear-Sky TOA WN Flux | 32-bit real | W m-2 | 0 .. 200 | Ndayx180x360 |
| 6 | clr_toa_net | CERES Clear-Sky TOA Net Flux | 32-bit real | W m-2 | -400 .. 400 | Ndayx180x360 |
| 7 | clr_toa_alb | CERES Clear-Sky TOA Albedo | 32-bit real | N/A | 0 .. 1 | Ndayx180x360 |
| 8 | all_toa_sw | CERES All-Sky TOA SW Flux | 32-bit real | W m-2 | 0 .. 1400 | Ndayx180x360 |
| 9 | all_toa_lw | CERES All-Sky TOA LW Flux | 32-bit real | W m-2 | 0 .. 500 | Ndayx180x360 |
| 10 | all_toa_wn | CERES All-Sky TOA WN Flux | 32-bit real | W m-2 | 0 .. 200 | Ndayx180x360 |
| 11 | all_toa_net | CERES All-Sky TOA Net Flux | 32-bit real | W m-2 | -400 .. 400 | Ndayx180x360 |
| 12 | all_toa_alb | CERES All-Sky TOA Albedo | 32-bit real | N/A | 0 .. 1 | Ndayx180x360 |
| 13 | toa_sw_insol | TOA SW Insolation | 32-bit real | W m-2 | 0 .. 1400 | Ndayx180x360 |

| Meteorological_Variables |
| --- |
| SDS Index | SDS Name | Long Name | Data Type | Units | Range | Number of Elements |
| 14 | sfc_wind_speed | Surface Wind Speed | 32-bit real | m s-1 | 0 .. 100 | Ndayx180x360 |
| 15 | sfc_skin_temp | Surface Skin Temperature | 32-bit real | K | 175 .. 375 | Ndayx180x360 |
| 16 | sfc_press | Surface Pressure | 32-bit real | hPa | 0 .. 1100 | Ndayx180x360 |
| 17 | sfc_750_temp_diff | Surface Minus 750 mb Air Temperature Difference | 32-bit real | K | -200 .. 200 | Ndayx180x360 |
| 18 | estim_inversion_strength | Estimated Inversion Strength | 32-bit real | K | -200 .. 200 | Ndayx180x360 |
| 19 | 750_sfc_pot_temp_diff | 750 mb Minus Surface Air Potential Temperature Difference | 32-bit real | K | -200 .. 200 | Ndayx180x360 |
| 20 | pw | Precipitable Water | 32-bit real | cm | 0 .. 10 | Ndayx180x360 |
| 21 | cld_msk_clr_strong_coverage | Cloud-mask Clear-Strong Percent Coverage | 32-bit real | % | 0 .. 100 | Ndayx180x360 |
| 22 | cld_msk_clr_weak_coverage | Cloud-mask Clear-Weak Percent Coverage | 32-bit real | % | 0 .. 100 | Ndayx180x360 |

| CERES_MODIS_Cloud_Layer_Properties_24Hour_Averages |
| --- |
| SDS Index | SDS Name | Long Name | Data Type | Units | Range | Number of Elements |
| 23 | cld_amount | Cloud Amount - Total | 32-bit real | % | 0 .. 100 | 5xNdayx180x360 |
| 24 | cld_amount_liq | Cloud Amount - Liquid | 32-bit real | % | 0 .. 100 | 5xNdayx180x360 |
| 25 | cld_amount_ice | Cloud Amount - Ice | 32-bit real | % | 0 .. 100 | 5xNdayx180x360 |
| 26 | cld_od | Cloud Visible Optical Depth (from 3.7 µm particle size retrieval) | 32-bit real | N/A | 0 .. 400 | 5xNdayx180x360 |
| 27 | cld_od_linavg | Cloud Visible Optical Depth (linear averaged, from 3.7 µm particle size retrieval) | 32-bit real | N/A | 0 .. 400 | 5xNdayx180x360 |
| 28 | cld_ir_emiss | Cloud Infrared Emissivity | 32-bit real | N/A | 0 .. 2 | 5xNdayx180x360 |
| 29 | cld_lwp | Cloud Liquid Water Path (from 3.7 µm particle size retrieval) | 32-bit real | g m-2 | 0 .. 10000 | 5xNdayx180x360 |
| 30 | cld_iwp | Cloud Ice Water Path (from 3.7 µm particle size retrieval) | 32-bit real | g m-2 | 0 .. 10000 | 5xNdayx180x360 |
| 31 | cld_top_press | Cloud Top Pressure | 32-bit real | hPa | 0 .. 1100 | 5xNdayx180x360 |
| 32 | cld_top_temp | Cloud Top Temperature | 32-bit real | K | 100 .. 350 | 5xNdayx180x360 |
| 33 | cld_top_hgt | Cloud Top Height | 32-bit real | km | 0 .. 20 | 5xNdayx180x360 |
| 34 | cld_eff_press | Cloud Effective Pressure | 32-bit real | hPa | 0 .. 1100 | 5xNdayx180x360 |
| 35 | cld_eff_temp | Cloud Effective Temperature | 32-bit real | K | 100 .. 350 | 5xNdayx180x360 |
| 36 | cld_eff_hgt | Cloud Effective Height | 32-bit real | km | 0 .. 20 | 5xNdayx180x360 |
| 37 | cld_base_press | Cloud Base Pressure | 32-bit real | hPa | 0 .. 1100 | 5xNdayx180x360 |
| 38 | cld_base_temp | Cloud Base Temperature | 32-bit real | K | 100 .. 350 | 5xNdayx180x360 |
| 39 | cld_liq_radius_37um | Cloud Liquid Particle Radius (from 3.7 µm particle size retrieval) | 32-bit real | µm | 0 .. 40 | 5xNdayx180x360 |
| 40 | cld_ice_radius_37um | Cloud Ice Particle General Effective Radius (from 3.7 µm particle size retrieval) | 32-bit real | µm | 0 .. 300 | 5xNdayx180x360 |
| 41 | cld_phase_37um | Cloud Particle Phase (from 3.7 µm particle size retrieval) | 32-bit real | N/A | 1 .. 2 | 5xNdayx180x360 |
| 42 | cld_liq_radius_12um | Cloud Liquid Particle Radius (from 1.2 µm particle size retrieval) | 32-bit real | µm | 0 .. 40 | 5xNdayx180x360 |
| 43 | cld_ice_radius_12um | Cloud Ice Particle General Effective Radius (from 1.2 µm particle size retrieval) | 32-bit real | µm | 0 .. 300 | 5xNdayx180x360 |
| 44 | cld_od_12um | Cloud Visible Optical Depth (from 1.2 µm particle size retrieval) | 32-bit real | N/A | 0 .. 400 | 5xNdayx180x360 |
| 45 | cld_liq_radius_21um | Cloud Liquid Particle Radius (from 2.1 µm particle size retrieval) | 32-bit real | µm | 0 .. 40 | 5xNdayx180x360 |
| 46 | cld_ice_radius_21um | Cloud Ice Particle General Effective Radius (from 2.1 µm particle size retrieval) | 32-bit real | µm | 0 .. 300 | 5xNdayx180x360 |
| 47 | cld_od_21um | Cloud Visible Optical Depth (from 2.1 µm particle size retrieval) | 32-bit real | N/A | 0 .. 400 | 5xNdayx180x360 |

| CERES_MODIS_Cloud_Layer_Properties_Daylight_Only_Averages |
| --- |
| SDS Index | SDS Name | Long Name | Data Type | Units | Range | Number of Elements |
| 48 | cld_amount_day | Cloud Amount - Total - Daylight Only | 32-bit real | % | 0 .. 100 | 5xNdayx180x360 |
| 49 | cld_amount_liq_day | Cloud Amount - Liquid - Daylight Only | 32-bit real | % | 0 .. 100 | 5xNdayx180x360 |
| 50 | cld_amount_ice_day | Cloud Amount - Ice - Daylight Only | 32-bit real | % | 0 .. 100 | 5xNdayx180x360 |
| 51 | cld_od_day | Cloud Visible Optical Depth (from 3.7 µm particle size retrieval) - Daylight Only | 32-bit real | N/A | 0 .. 400 | 5xNdayx180x360 |
| 52 | cld_od_linavg_day | Cloud Visible Optical Depth (linear averaged, from 3.7 µm particle size retrieval) - Daylight Only | 32-bit real | N/A | 0 .. 400 | 5xNdayx180x360 |
| 53 | cld_ir_emiss_day | Cloud Infrared Emissivity - Daylight Only | 32-bit real | N/A | 0 .. 2 | 5xNdayx180x360 |
| 54 | cld_lwp_day | Cloud Liquid Water Path (from 3.7 µm particle size retrieval) - Daylight Only | 32-bit real | g m-2 | 0 .. 10000 | 5xNdayx180x360 |
| 55 | cld_iwp_day | Cloud Ice Water Path (from 3.7 µm particle size retrieval) - Daylight Only | 32-bit real | g m-2 | 0 .. 10000 | 5xNdayx180x360 |
| 56 | cld_top_press_day | Cloud Top Pressure - Daylight Only | 32-bit real | hPa | 0 .. 1100 | 5xNdayx180x360 |
| 57 | cld_top_temp_day | Cloud Top Temperature - Daylight Only | 32-bit real | K | 100 .. 350 | 5xNdayx180x360 |
| 58 | cld_top_hgt_day | Cloud Top Height - Daylight Only | 32-bit real | km | 0 .. 20 | 5xNdayx180x360 |
| 59 | cld_eff_press_day | Cloud Effective Pressure - Daylight Only | 32-bit real | hPa | 0 .. 1100 | 5xNdayx180x360 |
| 60 | cld_eff_temp_day | Cloud Effective Temperature - Daylight Only | 32-bit real | K | 100 .. 350 | 5xNdayx180x360 |
| 61 | cld_eff_hgt_day | Cloud Effective Height - Daylight Only | 32-bit real | km | 0 .. 20 | 5xNdayx180x360 |
| 62 | cld_base_press_day | Cloud Base Pressure - Daylight Only | 32-bit real | hPa | 0 .. 1100 | 5xNdayx180x360 |
| 63 | cld_base_temp_day | Cloud Base Temperature - Daylight Only | 32-bit real | K | 100 .. 350 | 5xNdayx180x360 |
| 64 | cld_liq_radius_37um_day | Cloud Liquid Particle Radius (from 3.7 µm particle size retrieval) - Daylight Only | 32-bit real | µm | 0 .. 40 | 5xNdayx180x360 |
| 65 | cld_ice_radius_37um_day | Cloud Ice Particle General Effective Radius (from 3.7 µm particle size retrieval) - Daylight Only | 32-bit real | µm | 0 .. 300 | 5xNdayx180x360 |
| 66 | cld_phase_37um_day | Cloud Particle Phase (from 3.7 µm particle size retrieval) - Daylight Only | 32-bit real | N/A | 1 .. 2 | 5xNdayx180x360 |
| 67 | cld_liq_radius_12um_day | Cloud Liquid Particle Radius (from 1.2 µm particle size retrieval) - Daylight Only | 32-bit real | µm | 0 .. 40 | 5xNdayx180x360 |
| 68 | cld_ice_radius_12um_day | Cloud Ice Particle General Effective Radius (from 1.2 µm particle size retrieval) - Daylight Only | 32-bit real | µm | 0 .. 300 | 5xNdayx180x360 |
| 69 | cld_od_12um_day | Cloud Visible Optical Depth (from 1.2 µm particle size retrieval) - Daylight Only | 32-bit real | N/A | 0 .. 400 | 5xNdayx180x360 |
| 70 | cld_liq_radius_21um_day | Cloud Liquid Particle Radius (from 2.1 µm particle size retrieval) - Daylight Only | 32-bit real | µm | 0 .. 40 | 5xNdayx180x360 |
| 71 | cld_ice_radius_21um_day | Cloud Ice Particle General Effective Radius (from 2.1 µm particle size retrieval) - Daylight Only | 32-bit real | µm | 0 .. 300 | 5xNdayx180x360 |
| 72 | cld_od_21um_day | Cloud Visible Optical Depth (from 2.1 µm particle size retrieval) - Daylight Only | 32-bit real | N/A | 0 .. 400 | 5xNdayx180x360 |

| MODIS_Land_Aerosols |
| --- |
| SDS Index | SDS Name | Long Name | Data Type | Units | Range | Number of Elements |
| 73 | aod_land | PSF-weighted MOD04 Corrected Optical Depth Land (0.550 µm) | 32-bit real | N/A | 0 .. 5 | Ndayx180x360 |
| 74 | deep_blue_aod_land | PSF-weighted MOD04 Deep Blue Aerosol Optical Depth Land (0.550 µm) | 32-bit real | N/A | 0 .. 5 | Ndayx180x360 |

| MODIS_Ocean_Aerosols |
| --- |
| SDS Index | SDS Name | Long Name | Data Type | Units | Range | Number of Elements |
| 75 | aod_ocean | PSF-weighted MOD04 Effective Optical Depth Average Ocean (0.550 µm) | 32-bit real | N/A | 0 .. 5 | Ndayx180x360 |
| 76 | aod_small_ocean | PSF-weighted MOD04 Optical Depth Small Average Ocean (0.550 µm) | 32-bit real | N/A | 0 .. 5 | Ndayx180x360 |

| Number_of_Observations |
| --- |
| SDS Index | SDS Name | Long Name | Data Type | Units | Range | Number of Elements |
| 77 | num_sw_obs | Number of CERES SW Observations | 32-bit integer | N/A | 0 .. 24 | Ndayx180x360 |
| 78 | num_lw_obs | Number of CERES LW Observations | 32-bit integer | N/A | 0 .. 24 | Ndayx180x360 |
| 79 | num_clr_sw_obs | Number of CERES Clear-Sky SW Observations | 32-bit integer | N/A | 0 .. 24 | Ndayx180x360 |
| 80 | num_clr_lw_obs | Number of CERES Clear-Sky LW Observations | 32-bit integer | N/A | 0 .. 24 | Ndayx180x360 |

SSF1deg-Day Dimension Scales

Table 14 lists the dimension scales of the SDS arrays in the HDF file. Each dimension scale variable corresponds to one dimension and has the same name and size as that dimension. The dimension scales store the index values belonging to each dimension and have information like the other SDSs in the file.

| Dimension Scale Information |
| --- |
| SDS Index | Dimension Name | Long Name | Data Type | Units | Range | Number of Elements |
| 81 | longitude | Longitude | 32-bit real | degrees_east | N/A | 360 |
| 82 | latitude | Latitude | 32-bit real | degrees_north | N/A | 180 |
| 83 | day_of_month | Day of the Month | 32-bit integer | N/A | N/A | 28-31 |
| 84 | cloud_layer | Index of Cloud Layers Stratified by Pressure | 32-bit integer | N/A | N/A | 5 |

File Size:  ~850 MB

Number of Regional Parameters: 81

SSF1deg-Day Revision Record

The product Revision Record contains information pertaining to approved section changes. The table lists the date the Software Configuration Change Request (SCCR) was approved, the Release and Version Number, the SCCR number, a short description of the revision, and the revised sections.

| SSF1deg-Day Revision Record |
| --- |
| SCCR Approval Date | Release/ Version Number | SCCR Number | Description of Revision | Section(s) Affected |
| 09/30/2015 (Ed3) | R5V1 | 1086(Ed3) | Initial version of this document. | All |
| 04/18/2017 (Ed4 & Ed1-NPP) |  | 1177(Ed4 & Ed1-NPP) |  |  |