SSF1deg-Month-lite

The SSF1deg-Month-lite product provides CERES-observed temporally interpolated top-of-atmosphere (TOA) radiative fluxes and coincident MODIS-derived cloud and aerosol properties.  Each parameter is available at monthly 1°–regional, zonal and global time-space scales.  TOA fluxes are provided for clear and all-sky conditions in the longwave (LW), shortwave (SW), and window (WN) regions.  The regional means are determined for 1° equal-angle grid boxes calculated by first interpolating each parameter between the times of the CERES observations in order to produce a complete 1-hourly time series for the month.  After interpolation, the time series is used to produce mean parameters.  Monthly means are calculated using the combination of observed and interpolated parameters from all days containing at least one CERES observation.

CERES SSF1deg TOA fluxes are interpolated using the assumption of constant meteorological conditions (termed non-GEO) similar to the process used to average CERES ERBE-like data.

CERES Edition2.6 uses Edition2 algorithms with Edition3 CERES instrument calibration and is a limited parameter precursor product for the full parameter products available after Edition3 has been processed.

SSF1deg-Month contains monthly parameters on a regional, zonal and global basis:

•	All and clear-sky radiative SW, LW, and Net fluxes at TOA

•	Total cloud properties (not 4-layered) for day and day/night (24-hour)

•	Auxiliary parameters, for example aerosol, skin temperature, wind speed used as input to process the CERES fluxes

# Level:  4

# Frequency:  1 Monthly File

# Portion of Atmosphere Covered:  TOA

# Time Interval Covered:		Portion of Globe Covered:

File:  All Months and Climatology		File:  Zonal, Global, Regional

Record:  1 Month			Record:  1-Deg Regions

# Product Version:

Terra:  Edition2.6

Aqua:  Edition2.6

SSF1deg Metadata

The types of SSF1deg metadata are summarized in Table 1 and contain information which need only be recorded once per product.  The CERES metadata are listed in Appendix B.

Table B-1 lists the CERES Baseline Header Metadata and Table B-2 lists the CERES_metadata Vdata.

SSF1deg-Month Metadata Summary

| HDF Name | Description Table | Records | Number of Fields |
| --- | --- | --- | --- |
| CERES Baseline Header Metadata | Table B-1 | 1 | 36 |
| CERES_metadata Science Data | Table B-2 | 1 | 14 |

All of the SSF1deg science data are organized into the HDF Grid data type and are contained in:  SSF1deg-Month, which are shown in Table 2 below.  The table contains a list of the parameters within each grid, including the field number, the field name, the data type, the units, the range, and the number of elements within each field.

SSF1deg Scientific Data Sets

Monthly Gridded Categories of SSF1deg-Month

| Number | Name | Description | No. of Records |
| --- | --- | --- | --- |
| 1 | 1.0 Degree Regional | See Table 3 | 64800 |
| 2 | 1.0 Degree Zonal | See Table 3 | 180 |
| 3 | Global | See Table 3 | 1 |

List of Regional Parameters used to Define Groups of Other Parameters

| Number | Name | Description |
| --- | --- | --- |
| 1 | Region parameters | See Table 4(a) & Table 4(b) |
| 2 | TOA Fluxes | See Table 5 |
| 3 | CERES Cloud Properties | See Table 9 |

Table 4(a) and Table 4(b).  List of the SDSs contained in the Regional Parameters Vgroup.

Region Parameters in SSF1deg-Month

| SDS Name | Data Type | Units | Range | No. of Elements |
| --- | --- | --- | --- | --- |
| Snow/Ice Percent Coverage | 32-Bit Float | percent | 0.0 .. 100.0 | 1 |
| Ocean Fraction Coverage | 32-Bit Float | percent | 0.0 .. 100.0 | 1 |
| Total Aerosol Visible optical Depth @ 0.55 microns | 32-Bit Float | m | -1.0 .. 5.0 | 1 |
| Total Aerosol Visible Optical Depth – Fine Mode @ 0.55 microns | 32-Bit Float | m | -1.0 .. 5.0 | 1 |
| Total Aerosol Visible Optical Depth Percent | 32-Bit Float | percent | 0.0 .. 100.0 | 1 |
| Wind Speed | 32-Bit Float | m | -100.0 .. 100.0 | 1 |
| Skin Temperature | 32-Bit Float | K | 175 .. 375 | 1 |
| Precipitable Water | 32-Bit Float | cm | 0.001 .. 10.0 | 1 |

SDS Index of Region Parameters in SSF1deg-Month

| SDS Name | Regional Monthly | Zonal Monthly | Global Monthly |
| --- | --- | --- | --- |
| Snow/Ice Percent Coverage | 0 | 38 | 77 |
| Ocean Fraction Coverage | 1 | 39 | 78 |
| Total Aerosol Visible optical Depth @ 0.55 microns | 2 | 40 | 79 |
| Total Aerosol Visible Optical Depth – Fine Mode @ 0.55 microns | 3 | 41 | 80 |
| Total Aerosol Visible Optical Depth Percent | 4 | 42 | 81 |
| Wind Speed | 5 | 43 | 82 |
| Skin Temperature | 6 | 44 | 83 |
| Precipitable Water | 7 | 46 | 84 |

- List of the Vgroups contained in the TOA Flux Monthly Vgroup in SSF1deg-Month

| Vgroup Number | Vgroup Name | Monthly Averages |
| --- | --- | --- |
| 1 | Clear-sky non-GEO Method | See Table 6(a) & Table 6(b) |
| 2 | Total-sky non-GEO Method | See Table 7(a) & Table 7(b) |
| 3 | Solar Insolation | See Table 8(a) & Table 8(b) |

Table 6(a) and Table 6(b).  List of SDS contained in Clear-sky TOA Flux Averages in SSF1deg-Month.

- Clear-sky TOA Flux Averages in SSF1deg-Month

| Parameter Name | Data Type | Units | Range | No. of Elements Monthly |
| --- | --- | --- | --- | --- |
| Clear-sky TOA SW Flux - non-GEO Interpolation | 32-Bit Float | W m-2 | 0 .. 800 | 1 |
| Clear-sky TOA LW Flux - non-GEO Interpolation | 32-Bit Float | W m-2 | 0 .. 400 | 1 |
| Clear-sky TOA WN Flux - non-GEO Interpolation | 32-Bit Float | W m-2 | 0 .. 400 | 1 |
| Clear-sky TOA Albedo - non-GEO Interpolation | 32-Bit Float | N/A | 0.0 .. 1.0 | 1 |
| Clear-sky TOA Net Flux - non-GEO Interpolation | 32-Bit Float | W m-2 | -300.0 .. 400.0 | 1 |

- SDS Index of Clear-sky TOA Flux Averages in SSF1deg-Month

| SDS Name | Regional Monthly | Zonal Monthly | Global Monthly |
| --- | --- | --- | --- |
| Clear-sky TOA SW Flux - non-GEO Interpolation | 8 | 46 | 85 |
| Clear-sky TOA LW Flux - non-GEO Interpolation | 9 | 47 | 86 |
| Clear-sky TOA WN Flux - non-GEO Interpolation | 10 | 48 | 87 |
| Clear-sky TOA Albedo - non-GEO Interpolation | 11 | 49 | 88 |
| Clear-sky TOA Net Flux - non-GEO Interpolation | 12 | 50 | 89 |

Table 7(a) and Table 7(b).  List of SDS contained in Total-sky TOA Flux Averages in SSF1deg-Month.

Total-sky TOA Flux Averages in SSF1deg-Month

| Parameter Name | Data Type | Units | Range | No. of Elements Monthly |
| --- | --- | --- | --- | --- |
| Total-sky TOA SW Flux - non-GEO Interpolation | 32-Bit Float | W m-2 | 0 .. 800 | 1 |
| Total-sky TOA LW Flux - non-GEO Interpolation | 32-Bit Float | W m-2 | 0 .. 400 | 1 |
| Total-sky TOA WN Flux - non-GEO Interpolation | 32-Bit Float | W m-2 | 0 .. 400 | 1 |
| Total-sky TOA Albedo - non-GEO Interpolation | 32-Bit Float | N/A | 0.0 .. 1.0 | 1 |
| Total-sky TOA Net Flux - non-GEO Interpolation | 32-Bit Float | W m-2 | -300.0 .. 400.0 | 1 |

SDS Index of Total-sky TOA Flux Averages in SSF1deg-Month

| SDS Name | Regional Monthly | Zonal Monthly | Global Monthly |
| --- | --- | --- | --- |
| Total-sky TOA SW Flux - non-GEO Interpolation | 13 | 51 | 90 |
| Total-sky TOA LW Flux - non-GEO Interpolation | 14 | 52 | 91 |
| Total-sky TOA WN Flux - non-GEO Interpolation | 15 | 53 | 92 |
| Total-sky TOA Albedo - non-GEO Interpolation | 16 | 54 | 93 |
| Total-sky TOA Net Flux - non-GEO Interpolation | 17 | 55 | 94 |

Table 8(a) and Table 8(b).  List of SDS contained in Solar Insolation in SSF1deg-Month.

Solar Insolation Averages in SSF1deg-Month

| Parameter Name | Data Type | Units | Range | No. of Elements Monthly |
| --- | --- | --- | --- | --- |
| Solar Insolation | 32-Bit Float | W m-2 | 0 .. 400 | 1 |

SDS Index of Solar Incoming Flux Averages in SSF1deg-Month

| SDS Name | Zonal Monthly | Global Monthly |
| --- | --- | --- |
| Solar Insolation | 54 | 95 |

- List of the Vgroups contained in the CERES Day Time and Day and Night Time Cloud Monthly Vgroup in SSF1deg-Month

| Vgroup Number | Vgroup Name | Monthly Averages |
| --- | --- | --- |
| 1 | Day Time Clouds | See Table 10(a) & Table 10(b) |
| 2 | Day and Night Time Clouds | See Table 10(a) & Table 10(b) |

Table 10(a) and Table 10(b).  List of the SDS contained in the CERES Day Time and Day and Night Time Cloud Monthly Vgroup in SSF1deg-Month.

- CERES Day Time and Day and Night Time Cloud Averages in SSF1deg-Month

| SDS Name | Data Type | Units | Range | No. of Elements |
| --- | --- | --- | --- | --- |
| Cloud Area Fraction | 32-Bit Float | percent | 0.0 .. 100.0 | 1 |
| Cloud Effective Pressure | 32-Bit Float | hPa | 0.0 .. 1100.0 | 1 |
| Cloud Effective Temperature | 32-Bit Float | K | 180.0 .. 350.0 | 1 |
| Cloud Effective Height | 32-Bit Float | m | -1000 .. 10000 | 1 |
| Cloud Particle Phase | 32-Bit Float | fraction | 1.0 .. 2.0 | 1 |
| Liquid Water Path | 32-Bit Float | gm-2 | 0.0 .. 10000.0 | 1 |
| Ice Water Path | 32-Bit Float | gm-2 | 0.0 .. 10000.0 | 1 |
| Water Particle Radius | 32-Bit Float | micron | 0.0 .. 40.0 | 1 |
| Ice Particle Effective Diam | 32-Bit Float | micron | 0.0 .. 300.0 | 1 |
| Cloud Visible Optical Depth | 32-Bit Float | N/A | 0.0 .. 100.0 | 1 |

- SDS Index of CERES Cloud Averages in SSF1deg-Month

| SDS Name | Day time Regional Monthly | Day time Zonal Monthly | Day time Global Monthly | Day & Night Regional Monthly | Day & Night Zonal Monthly | Day & Night Global Monthly |
| --- | --- | --- | --- | --- | --- | --- |
| Cloud Area Fraction | 18 | 57 | 96 | 28 | 67 | 106 |
| Cloud Effective Pressure | 19 | 58 | 97 | 29 | 68 | 107 |
| Cloud Effective Temperature | 20 | 59 | 98 | 30 | 69 | 108 |
| Cloud Effective Height | 21 | 60 | 99 | 31 | 70 | 109 |
| Cloud Particle Phase | 22 | 61 | 100 | 32 | 71 | 110 |
| Liquid Water Path | 23 | 62 | 101 | 33 | 72 | 111 |
| Ice Water Path | 24 | 63 | 102 | 34 | 73 | 112 |
| Water Particle Radius | 25 | 64 | 103 | 35 | 74 | 113 |
| Ice Particle Effective Diam | 26 | 65 | 104 | 36 | 75 | 114 |
| Cloud Visible Optical Depth | 27 | 66 | 105 | 37 | 76 | 115 |

SSF1deg Month

Total Record/File:	64,981

Total Bits/Record:	3,712

Total Bytes/Record:	464

Total Bits/File:	241,209,472

Total Bytes/File:	30,151,184

SSF1deg-Month-lite Revision Record

The product Revision Record contains information pertaining to approved section changes.  The table lists the date the Software Configuration Change Request (SCCR) was approved, the Release and Version Number, the SCCR number, a short description of the revision, and the revised sections.  The authors are listed on the document cover.

| SSF1deg-Month-lite Revision Record |
| --- |
| SCCR Approval Date | Release/ Version Number | SCCR Number | Description of Revision | Section(s) Affected |
| 07/26/11 | R5V1 | 860 | New document. | All |
|  |  |  | The ASDC footer was added to the bottom of the document. (06/05/2013) | All |
|  |  |  | Changed Section numbering 2.15 to 2.16. (10/21/2013) | All |
|  |  |  | Eliminated section numbers from the Data Products Catalog. Specifically, in this document, section number 2.16 was removed. (12/12/2013) | All |
|  |  |  | Updated some links to refer to the .pdf file instead of the .doc file. (06/20/2014) | All |