SYN1deg-Day-lite

The SYN1deg-Day-lite product provides CERES-observed temporally interpolated top-of-atmosphere (TOA) radiative fluxes and coincident MODIS-derived cloud and aerosol properties.  Each parameter is available at daily 1°–regional, zonal and global time-space scales.  TOA fluxes are provided for clear and all-sky conditions in the longwave (LW), shortwave (SW), and window (WN) regions.  The regional means are determined for 1° equal-angle grid boxes calculated by first interpolating each parameter between the times of the CERES observations in order to produce a complete 1-hourly time series for the month.  After interpolation, the time series is used to produce mean parameters.  Daily means are calculated using the combination of observed and interpolated parameters from all days containing at least one CERES observation.

CERES SYN1deg uses 3-hourly radiance and cloud property data from geostationary imagers to more accurately model variability between CERES observations.  To use GEO data to enhance diurnal sampling, several steps are involved.  First GEO radiances are cross-calibrated with the MODIS imager using only data that is coincident in time and ray-matched in angle.  Next, the GEO cloud retrievals are inferred from the calibrated GEO radiances.  The GEO radiances are converted from narrowband to broadband using empirical regressions, and then broadband GEO TOA fluxes using ADMs and directional models.  To ensure GEO and CERES TOA fluxes are consistent, a normalization technique is used.  Instantaneous matched gridded fluxes from CERES and GEO are regressed against one another over a month from the 5°(5° latitude-longitude regions.  The regression relation is then applied to all GEO fluxes to remove biases that depend upon cloud amount, solar and view zenith angles as well as regional dependencies.  The all-sky GEO-LW TOA fluxes use the same approach as in Edition2 and employ regional instantaneous normalization.

CERES Edition2.6 uses Edition2 algorithms with Edition3 CERES instrument calibration and is a limited parameter precursor product for the full parameter products available after Edition3 has been processed.

SYN1deg-Daily contains daily parameters on a regional, zonal and global basis:

•	All-sky and clear-sky radiative SW, LW, and Net fluxes at TOA

•	Total cloud properties (not 4-layered) for day and day/night (24-hour)

•	Auxiliary parameters, for example aerosol, skin temperature, wind speed used as input to process the CERES fluxes

# Level:  4

# Frequency: 1 Daily File

# Portion of Atmosphere Covered:  TOA

# Time Interval Covered:		Portion of Globe Covered:

File:  All Months and Climatology		File:  Zonal, Global, Regional

Record:  1 Month			Record:  1-Deg Regions

# Product Version:

Terra:  Edition2.6

Aqua :  Edition2.6

SYN1deg Metadata

The types of SYN1deg metadata are summarized in Table 1 and contain information which need only be recorded once per product.  The CERES metadata are listed in Appendix B.

Table B-1 lists the CERES Baseline Header Metadata and Table B-2 lists the CERES_metadata Vdata.

SYN1deg-Day Metadata Summary

| HDF Name | Description Table | Records | Number of Fields |
| --- | --- | --- | --- |
| CERES Baseline Header Metadata | Table B-1 | 1 | 36 |
| CERES_metadata Science Data | Table B-2 | 1 | 14 |

All of the SYN1deg science data are organized into the HDF Grid data type and are contained in SYN1deg-Day, which are shown in Table 2 below.  The table contains a list of the parameters within each grid, including the field number, the field name, the data type, the units, the range, and the number of elements within each field.

SYN1deg Scientific Data Sets

Daily Gridded Categories SYN1deg-Day

| Number | Name | Description | Number of Records |
| --- | --- | --- | --- |
| 1 | 1.0 Degree Regional | See Table 3 | 64800 x Days in Month |
| 2 | 1.0 Degree Zonal | See Table 3 | 180 x Days in Month |
| 4 | Global | See Table 3 | Days in Month |

List of Regional Parameters used to Define Groups of Other Parameters

| Number | Name | Description |
| --- | --- | --- |
| 1 | Region parameters | See Table 4(a) & Table 4(b) |
| 2 | TOA Fluxes | See Table 5 |
| 3 | CERES Cloud Properties | See Table 10 |

Table 4(a) and Table 4(b)  List of the SDSs contained in the Regional Parameters Vgroup of SYN1deg-Day.

Region Parameters in SYN1deg-Day

| SDS Name | Data Type | Units | Range | No. of Elements |
| --- | --- | --- | --- | --- |
| Snow/Ice Percent Coverage | 32-Bit Float | percent | 0.0 .. 100.0 | 28 .. 31 |
| Ocean Fraction Coverage | 32-Bit Float | percent | 0.0 .. 100.0 | 28 .. 31 |
| Total Aerosol Visible optical Depth @ 0.55 microns | 32-Bit Float | m | -1.0 .. 5.0 | 28 .. 31 |
| Total Aerosol Visible Optical Depth – Fine Mode @ 0.55 microns | 32-Bit Float | m | -1.0 .. 5.0 | 28 .. 31 |
| Total Aerosol Visible Optical Depth Percent | 32-Bit Float | percent | 0.0 .. 100.0 | 28 .. 31 |
| Wind Speed | 32-Bit Float | m | -100.0 .. 100.0 | 28 .. 31 |
| Skin Temperature | 32-Bit Float | K | 175 .. 375 | 28 .. 31 |
| Precipitable Water | 32-Bit Float | cm | 0.001 .. 10.0 | 28 .. 31 |

SDS Index of Region Parameters in SYN1deg-Day

| SDS Name | Regional Monthly | Zonal Monthly | Global Monthly |
| --- | --- | --- | --- |
| Snow/Ice Percent Coverage | 0 | 42 | 85 |
| Ocean Fraction Coverage | 1 | 43 | 86 |
| Total Aerosol Visible optical Depth @ 0.55 microns | 2 | 44 | 87 |
| Total Aerosol Visible Optical Depth – Fine Mode @ 0.55 microns | 3 | 45 | 88 |
| Total Aerosol Visible Optical Depth Percent | 4 | 46 | 89 |
| Wind Speed | 5 | 47 | 90 |
| Skin Temperature | 6 | 48 | 91 |
| Precipitable Water | 7 | 49 | 92 |

- List of the Vgroups contained in the TOA Fluxes Vgroup in SYN1deg-Day

| Vgroup Number | Vgroup Name | Daily Averages |
| --- | --- | --- |
| 1 | Clear-Sky GEO Method | See Table 6(a) & Table 6(b) |
| 2 | Total-Sky GEO Method | See Table 7(a) & Table 7(b) |
| 3 | Number of Observations | See Table 8(a) & Table 8(b) |
| 4 | Incoming Solar Flux | See Table 9(a) & Table 9(b) |

Table 6(a) and Table 6(b).  List of the SDSs contained in the Clear-Sky TOA Flux Average Vgroup.

- Clear-sky TOA Flux Average in SYN1deg-Day

| SDS Name | Data Type | Units | Range | No. of Elements Monthly |
| --- | --- | --- | --- | --- |
| Clear-sky TOA SW Flux - GEO Interpolation | 32-Bit Float | Wm-2 | 0.0 .. 800.0 | 28 .. 31 |
| Clear-sky TOA LW Flux - GEO Interpolation | 32-Bit Float | Wm-2 | 0.0 .. 400.0 | 28 .. 31 |
| Clear-sky TOA WN Flux - GEO Interpolation | 32-Bit Float | Wm-2 | 0.0 .. 400.0 | 28 .. 31 |
| Clear-sky TOA Albedo - GEO Interpolation | 32-Bit Float | N/A | 0.0 .. 1.0 | 28 .. 31 |
| Clear-sky TOA Net Flux - GEO Interpolation | 32-Bit Float | Wm-2 | -300.0 .. 400.0 | 28 .. 31 |

- SDS Index of Clear-Sky TOA Flux Data Average in SYN1deg-Day

| Parameter Name | Regional Daily | Zonal Daily | Global Daily |
| --- | --- | --- | --- |
| Clear-sky TOA SW Flux - GEO Interpolation | 8 | 50 | 93 |
| Clear-sky TOA LW Flux - GEO Interpolation | 9 | 51 | 94 |
| Clear-sky TOA WN Flux - GEO Interpolation | 10 | 52 | 95 |
| Clear-sky TOA Albedo - GEO Interpolation | 11 | 53 | 96 |
| Clear-sky TOA Net Flux - GEO Interpolation | 12 | 54 | 97 |

Table 7(a) and Table 7(b).  List of the SDSs contained in the Total-Sky TOA Flux Average Vgroup.

Total-sky TOA Flux Average in SYN1deg-Day

| SDS Name | Data Type | Units | Range | No. of Elements Monthly |
| --- | --- | --- | --- | --- |
| Total-sky TOA SW Flux - GEO Interpolation | 32-Bit Float | Wm-2 | 0.0 .. 800.0 | 28 .. 31 |
| Total-sky TOA LW Flux - GEO Interpolation | 32-Bit Float | Wm-2 | 0 .. 400 | 28 .. 31 |
| Total-sky TOA WN Flux - GEO Interpolation | 32-Bit Float | Wm-2 | 0 .. 400 | 28 .. 31 |
| Total-sky TOA Albedo - GEO Interpolation | 32-Bit Float | N/A | 0 .. 1 | 28 .. 31 |
| Total-sky TOA Net Flux - GEO Interpolation | 32-Bit Float | Wm-2 | -300 .. 400 | 28 .. 31 |

SDS Index of Total-Sky TOA Flux Data Average in SYN1deg-Day

| Parameter Name | Regional Daily | Zonal Daily | Global Daily |
| --- | --- | --- | --- |
| Total-sky TOA SW Flux - GEO Interpolation | 13 | 55 | 98 |
| Total-sky TOA LW Flux - GEO Interpolation | 14 | 56 | 99 |
| Total-sky TOA WN Flux - GEO Interpolation | 15 | 57 | 100 |
| Total-sky TOA Albedo - GEO Interpolation | 16 | 58 | 101 |
| Total-sky TOA Net Flux - GEO Interpolation | 17 | 59 | 102 |

Table 8(a) and Table 8(b).  List of the SDSs contained in the Number of Observations Vgroup.

Number of Observations in SYN1deg-Day

| SDS Name | Data Type | Units | Range | No. of Elements Monthly |
| --- | --- | --- | --- | --- |
| Clear-sky TOA SW Number of Obs. – GEO Daily | 32-Bit Float | N/A | 0 .. 24 | 28 .. 31 |
| Clear-sky TOA LW Number of Obs. – GEO Daily | 32-Bit Float | N/A | 0 .. 24 | 28 .. 31 |
| Total-sky TOA SW Number of Obs. – GEO Daily | 32-Bit Float | N/A | 0 .. 24 | 28 .. 31 |
| Total-sky TOA LW Number of Obs. – GEO Daily | 32-Bit Float | N/A | 0 .. 24 | 28 .. 31 |

SDS Index of Number of Observations in SYN1deg-Day

| Parameter Name | Regional Daily | Zonal Daily | Global Daily |
| --- | --- | --- | --- |
| Clear-sky TOA SW Number of Obs. – GEO Daily | 18 | 60 | 103 |
| Clear-sky TOA LW Number of Obs. – GEO Daily | 19 | 61 | 104 |
| Total-sky TOA SW Number of Obs. – GEO Daily | 20 | 62 | 105 |
| Total-sky TOA LW Number of Obs. – GEO Daily | 21 | 63 | 106 |

Table 9(a) and Table 9(b).  List of the SDSs contained in the Incoming Solar Vgroup.

Incoming Solar in SYN1deg-Day

| SDS Name | Data Type | Units | Range | No. of Elements Monthly |
| --- | --- | --- | --- | --- |
| Incoming Solar Flux | 32-Bit Float | Wm-2 | 0 .. 400 | 28 .. 31 |

SDS Index of Incoming Solar in SYN1deg-Day

| Parameter Name | Zonal Daily | Global Daily |
| --- | --- | --- |
| Incoming Solar Flux | 64 | 107 |

- List of the Vgroups contained in the CERES Day Time and Day and Night Time Cloud Daily Vgroup in SYN1deg-Day

| Vgroup Number | Vgroup Name | Monthly Averages |
| --- | --- | --- |
| 1 | Day Time Clouds | See Table 11(a) & Table 11(b) |
| 2 | Day and Night Time Clouds | See Table 11(a) & Table 11(b) |

Table 11(a) and Table 11(b).  CERES Day Time and Day and Night Time Cloud Properties in SYN1deg-Day.

- Day Time and Day and Night Time CERES Cloud Averages in SYN1deg-Day

| SDS Name | Data Type | Units | Range | No. of Elements |
| --- | --- | --- | --- | --- |
| Cloud Area Fraction | 32-Bit Float | percent | 0.0 .. 100.0 | 28 .. 31 |
| Cloud Effective Pressure | 32-Bit Float | hPa | 0.0 .. 1100.0 | 28 .. 31 |
| Cloud Effective Temperature | 32-Bit Float | K | 180.0 .. 350.0 | 28 .. 31 |
| Cloud Effective Height | 32-Bit Float | m | -1000 .. 10000 | 28 .. 31 |
| Cloud Particle Phase | 32-Bit Float | fraction | 1.0 .. 2.0 | 28 .. 31 |
| Liquid Water Path | 32-Bit Float | gm-2 | 0.0 .. 10000.0 | 28 .. 31 |
| Ice Water Path | 32-Bit Float | gm-2 | 0.0 .. 10000.0 | 28 .. 31 |
| Water Particle Radius | 32-Bit Float | micron | 0.0 .. 40.0 | 28 .. 31 |
| Ice Particle Effective Diam | 32-Bit Float | micron | 0.0 .. 300.0 | 28 .. 31 |
| Cloud Visible Optical Depth | 32-Bit Float | N/A | 0.0 .. 100.0 | 28 .. 31 |

- SDS Index of day Time and Day and Night Time CERES Cloud Averages in SYN1deg-Day

| SDS Name | Day time Regional Monthly | Day time Zonal Monthly | Day time Global Monthly | Day & Night Regional Monthly | Day & Night Zonal Monthly | Day & Night Global Monthly |
| --- | --- | --- | --- | --- | --- | --- |
| Cloud Area Fraction | 22 | 65 | 108 | 32 | 75 | 118 |
| Cloud Effective Pressure | 23 | 66 | 109 | 33 | 76 | 119 |
| Cloud Effective Temperature | 24 | 67 | 110 | 34 | 77 | 120 |
| Cloud Effective Height | 25 | 68 | 111 | 35 | 78 | 121 |
| Cloud Particle Phase | 26 | 69 | 112 | 36 | 79 | 122 |
| Liquid Water Path | 27 | 70 | 113 | 37 | 80 | 123 |
| Ice Water Path | 28 | 71 | 114 | 38 | 81 | 124 |
| Water Particle Radius | 29 | 72 | 115 | 39 | 82 | 125 |
| Ice Particle Effective Diam | 30 | 73 | 116 | 40 | 83 | 126 |
| Cloud Visible Optical Depth | 31 | 74 | 117 | 41 | 84 | 127 |

SYN1deg Day

Total Record/File:	64,981

Total Bits/Record:	4098

Total Bytes/Record:	512

Total Bits/File:	266,162,176

Total Bytes/File:	33,270,272

# SYN1deg-Day-lite Revision Record

The product Revision Record contains information pertaining to approved section changes.  The table lists the date the Software Configuration Change Request (SCCR) was approved, the Release and Version Number, the SCCR number, a short description of the revision, and the revised sections.  The authors are listed on the document cover.

| SYN1deg-Day-lite Revision Record |
| --- |
| SCCR Approval Date | Release/ Version Number | SCCR Number | Description of Revision | Section(s) Affected |
| 07/26/11 | R5V1 | 860 | New document. | All |
|  |  |  | The ASDC footer was added to the bottom of the document. (06/05/2013) | All |
|  |  |  | Eliminated section numbers from the Data Products Catalog. Specifically, in this document, section number 2.17 was removed. (12/12/2013) | All |
|  |  |  | Updated some links to refer to the .pdf file instead of the .doc file. (06/20/2014) | All |