Monthly Averaged Synoptic Radiative Fluxes and Clouds
(SYN1deg-Month)

The SYN1deg product contains the monthly regional, zonal and global means of the CERES geostationary (GEO) enhanced temporally interpolated TOA fluxes, MODIS and 3-hourly GEO cloud properties, MODIS aerosols, and computed TOA, surface and in-atmospheric (profile) fluxes consistent with the observed TOA fluxes, clouds and aerosols.  The Edition3A SYN1deg product has combined the Terra and Aqua CERES observed fluxes and cloud retrievals.  The SYN1deg-Month product is distributed in monthly HDF-EOS files.

The constrained (tuned) to the observed CERES TOA fluxes and the initial (untuned) profile (TOA, 70mb, 200mb, 500mb, and surface) longwave, shortwave, and window channel fluxes retrieved from the Langley Fu-Liou radiative transfer model are based on inputs from MODIS and GEO cloud properties stratified by 4 vertical layers, GEOS atmosphere and skin temperature, MATCH aerosol constituents, and MODIS spectral aerosol optical depths. The fluxes are given for pristine (clear-sky no-aerosol), clear-sky, total-sky-no-aerosol, and total-sky conditions.  The initial and adjusted cloud, aerosols, GEOS precipitable water, humidity and skin temperatures are also given.

The SYN1deg product contains direct and diffuse shortwave surface fluxes.  The product also contains direct and diffuse surface UVA, UVB, and photosynthetically active radiation (PAR) fluxes and surface UV Index for pristine, clear-sky, and total-sky conditions. Some of these surface fluxes are also given for total-sky-no-aerosol conditions.

More information about the CERES products can be obtained on the CERES subsetter ordering web page (http://ceres.larc.nasa.gov/order_data.php)

A complete listing of metadata and science parameters for this data product can be found in Table 1, Table 2, and Table 3.

Level:  3

Frequency:  1/Month

Portion of Atmosphere Covered:  Surface, In-Atmosphere, and TOA

Time Interval Covered:		Portion of Globe Covered:

File:  1 Month			File:  Entire Globe

Record:  1 Month			Record:  1.0-Deg Regional, Zonal or Global

Product Version:

TRMM:  N/A

Terra+Aqua:  Edition3A

Monthly Metadata

The types of Monthly metadata are summarized in Table 1 and contain information which need only be recorded once per product.  The CERES metadata are listed in Appendix B.  The Vgroups are listed in Table 2 and Table 3.

| Monthly Metadata Summary |
| --- |
| HDF Name | Description Table | Records | Number of Fields |
| CERES Baseline Header Metadata | Table B-1 | 1 | 36 |
| CERES_metadata gridded data | Table B-2 | 1 | 14 |

| List of the Vgroups for different Gridded Categories |
| --- |
| Vgroup Number | Vgroup Name | Description | Number of Records |
| 1 | 1.0 Degree Regional | See Table 3 | 360,180 |
| 2 | 1.0 Degree Zonal | See Table 3 | 180 |
| 3 | Global | See Table 3 | 1 |

| List of the Vgroups contained in the Regional, Zonal, and Global Monthly Averages |
| --- |
| Regional Vgroup Number | Zonal & Global VgroupNumber | Vgroup Name | Monthly Averages for Regional, Zonal and Global |
| 1* |  | Time and Position* | See Table 5(a) & Table 5(b) |
| 2 | 1 | Observed TOA Fluxes | See Table 6(a) & Table 6(b) |
| 3 | 2 | Cloud Layer - High | See Table 7(a) & Table 7(b) |
| 4 | 3 | Cloud Layer - UpperMid | See Table 7(a) & Table 7(b) |
| 5 | 4 | Cloud Layer - LowerMid | See Table 7(a) & Table 7(b) |
| 6 | 5 | Cloud Layer - Low | See Table 7(a) & Table 7(b) |
| 7 | 6 | Stowe-Ignatov Aerosol Optical Depth | See Table 8(a) & Table 8(b) |
| 8 | 7 | MODIS Aerosol Optical Depth | See Table 9(a) & Table 9(b) |
| 9 | 8 | Tuned Pristine Fluxes | See Table 10(a) & Table 10(b) |
| 10 | 9 | Tuned ClearSky Flux Profiles | See Table 11(a) & Table 11(b) |
| 11 | 10 | Tuned TotalSky-NoAerosol Fluxes | See Table 12(a) & Table 12(b) |
| 12 | 11 | Tuned TotalSky Flux Profiles | See Table 13(a) & Table 13(b) |
| 13 | 12 | Untuned Pristine Fluxes | See Table 14(a) & Table 14(b) |
| 14 | 13 | Untuned ClearSky Fluxes | See Table 15(a) & Table 15(b) |
| 15 | 14 | Untuned TotalSky-NoAerosol Fluxes | See Table 16(a) & Table 16(b) |
| 16 | 15 | Untuned TotalSky Fluxes | See Table 17(a) & Table 17(b) |
| 17 | 16 | Satellite Emulated WN TOA Fluxes | See Table 18(a) & Table 18(b) |
| 18 | 17 | TOA Flux Error | See Table 19(a) & Table 19(b) |
| 19* |  | Number of Hourboxes* | See Table 20(a) & Table 20(b) |
| 20 | 18 | Constrainment Adjustments | See Table 21(a) & Table 21(b) |
| 21 | 19 | Surface SW Fluxes** | See Table 22(a) & Table 22(b) |
| 22 | 20 | UVA - UVB Fluxes | See Table 23(a) & Table 23(b) |
| 23 | 21 | PAR Fluxes | See Table 24(a) & Table 24(b) |
| 24 | 22 | Pristine-Sky SW MultiStream Correction | See Table 25(a) & Table 25(b) |

* Applicable to Regional data only

** Direct/Diffuse

Monthly Regional, Zonal and Global Science Data

The Scientific Data Sets (SDS) are divided into tables which map to Vgroups of the same name.  All of the Monthly regional science data are organized into the HDF-EOS Grid data type, which is shown in Table 4(a).  All parameter (a) tables contain a list of the gridded parameters, which includes the field name, the data type, the units, the range, and the number of elements within each field for Regional data with notes provided under the table for Zonal and Global.  The No. of Elements or Dimensions are defined in the first set of tables.  All parameter (b) tables contain the list of SDS indices, which are grouped into monthly regional, zonal and global means.  The first 2 dimensions noted, Nlat and Nlon, correspond to the CERES region index; for zonal, Nlat corresponds to the 1° latitudinal zone. Global parameters do not have an Nlat nor Nlon dimension. The last dimension is Ns and contains the mean and the standard deviation (temporal).  On a few parameters, the last dimension is Nlev and defines the atmospheric profile levels.  This ordering is used by the C programming language and most HDF viewers, such as IDL.  In FORTRAN, the dimensions are reversed such that the number of regions becomes the last dimension and the first dimension is the number of parameters in the SDS.

Nlat, Nlon dimensions that define the CERES equal-angle
1° latitude by 1° longitude grid

| Dimension | No on indices | Definition |
| --- | --- | --- |
|  | Regional | Zonal | Global |  |
| Nlat | 180 | 180 | 0 | Index #1 is defined at 89.5°N and #180 is at 89.5°S |
| Nlon | 360 | 0 | 0 | Index #1 is defined at 179.5°W and #360 is at 179.5°E |

* The Zonal and Global parameters no longer support placeholders for Nlon and Nlon and Nlat, respectively.

Ns dimension that defines the parameter statistics for individual grid cell

| Ns | Statistic |
| --- | --- |
| 1 | Mean |
| 2 | Standard deviation |

Nlev dimension that defines the atmospheric profile levels

| Nlev | Atmospheric level |
| --- | --- |
| 1 | TOA (30 km) |
| 2 | 70mb |
| 3 | 200mb |
| 4 | 500mb |
| 5 | Surface |

IGBP Surface types used in Table 2.11-5(a).  For a geographical distribution of the scene types see http://snowdog.larc.nasa.gov/surf/pages/sce_type.html

| Nsfc | Surface Type |
| --- | --- |
| 1 | Evergreen Needle Forest |
| 2 | Evergreen Broadleaf Forest |
| 3 | Deciduous Needle Forest |
| 4 | Deciduous Broadleaf Forest |
| 5 | Mixed Forest |
| 6 | Closed Shrubs |
| 7 | Open Shrubs |
| 8 | Woody Savannas |
| 9 | Savannas |
| 10 | Grassland |
| 11 | Wetlands |
| 12 | Crops |
| 13 | Urban |
| 14 | Crop/Mosaic |
| 15 | Permanent Snow/Ice |
| 16 | Barren Desert |
| 17 | Water |
| 18 | Tundra |
| 19 | Land Snow |
| 20 | Sea Ice |

Table of Time and Position.  Nsfc dimension is defined in Table 4(d)

| SDS Name | DataType | Units | Range | No. Of Elements Regional |
| --- | --- | --- | --- | --- |
| Region Number | 32-bit real | N/A | 1 .. 64800 | Nlon*Nlat |
| Colatitude | 32-bit real | Degree | 0 .. 180 | Nlon*Nlat |
| Longitude | 32-bit real | Degree | 0 .. 360 | Nlon*Nlat |
| Surface altitude above sea level | 32-bit real | m | -1000 .. 10000 | Nlon*Nlat |
| Surface type percent coverage | 32-bit real | Percent | 0 .. 100 | Nlon*Nlat*Nsfc |

SDS Index of Time and Position

| SDS Name | Regional Monthly |
| --- | --- |
| Region Number | 0 |
| Colatitude | 1 |
| Longitude | 2 |
| Surface altitude above sea level | 3 |
| Surface type percent coverage | 4 |

Table of Observed TOA Fluxes

| SDS Name | DataType | Units | Range | No. Of Elements Regional |
| --- | --- | --- | --- | --- |
| SW TOA Total-Sky | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| LW TOA Total-Sky | 32-bit real | W m-2 | 0 .. 500 | Nlon*Nlat*Ns |
| WN TOA Total-Sky | 32-bit real | W m-2 | 0 .. 200 | Nlon*Nlat*Ns |
| SW TOA Clear-Sky | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| LW TOA Clear-Sky | 32-bit real | W m-2 | 0 .. 500 | Nlon*Nlat*Ns |
| WN TOA Clear-Sky | 32-bit real | W m-2 | 0 .. 200 | Nlon*Nlat*Ns |

* No. of Elements for Zonal:  Nlat*Ns

* No. of Elements for Global:  Ns

SDS Index of Observed TOA Fluxes

| SDS Name | Regional Monthly | Zonal Monthly | Global Monthly |
| --- | --- | --- | --- |
| SW TOA Total-Sky | 5 | 223 | 435 |
| LW TOA Total-Sky | 6 | 224 | 436 |
| WN TOA Total-Sky | 7 | 225 | 437 |
| SW TOA Clear-Sky | 8 | 226 | 438 |
| LW TOA Clear-Sky | 9 | 227 | 439 |
| WN TOA Clear-Sky | 10 | 228 | 440 |

Observed Cloud Properties for Four Cloud Layers

| SDS Name | DataType | Units | Range | No. Of Elements Regional |
| --- | --- | --- | --- | --- |
| Area Fraction Percentage | 32-bit real | Percent | 0 .. 100 | Nlon*Nlat*Ns |
| Vis. Opt. Depth (linear) | 32-bit real | N/A | 0 .. 400 | Nlon*Nlat*Ns |
| Vis. Opt. Depth (log) | 32-bit real | N/A | -6 .. 6 | Nlon*Nlat*Ns |
| Infrared Emissivity | 32-bit real | N/A | 0 .. 1* | Nlon*Nlat*Ns |
| Liquid Water Path | 32-bit real | g m-2 | 0 .. 10000 | Nlon*Nlat*Ns |
| Ice Water Path | 32-bit real | g m-2 | 0 .. 10000 | Nlon*Nlat*Ns |
| Top Pressure | 32-bit real | hPa | 0 .. 1100 | Nlon*Nlat*Ns |
| Effective Pressure | 32-bit real | hPa | 0 .. 1100 | Nlon*Nlat*Ns |
| Effective Temperature | 32-bit real | K | 100 .. 350 | Nlon*Nlat*Ns |
| Effective Height | 32-bit real | km | 0 .. 20 | Nlon*Nlat*Ns |
| Bottom Pressure | 32-bit real | hPa | 0 .. 1100 | Nlon*Nlat*Ns |
| Liquid Particle Radius | 32-bit real | m | 0 .. 40 | Nlon*Nlat*Ns |
| Ice Particle Diameter | 32-bit real | m | 0 .. 300 | Nlon*Nlat*Ns |
| Particle Phase | 32-bit real | N/A | 1 .. 2 | Nlon*Nlat*Ns |
| Vertical Aspect Ratio | 32-bit real | N/A | 0 .. 20 | Nlon*Nlat*Ns |

* Range check from 0 to 2 to compensate for roundoff error.

* No. of Elements for Zonal:  Nlat*Ns

* No. of Elements for Global:  Ns

SDS Index of Observed Cloud Properties for four layers.
Table 4(c) defines the 4 cloud layers

| SDS Name | Regional Monthly | Zonal Monthly | Global Monthly |
| --- | --- | --- | --- |
| Area Fraction Percentage |  |  |  |  | 229 | 244 | 259 | 274 |  |  |  |  |
| Vis. Opt. Depth (linear) |  |  |  |  | 230 | 245 | 260 | 275 |  |  |  |  |
| Vis. Opt. Depth (log) |  |  |  | 2 | 231 | 246 | 261 | 276 |  |  |  |  |
| Infrared Emissivity |  |  |  |  | 232 | 247 | 262 | 277 |  |  |  |  |
| Liquid Water Path |  |  |  |  | 233 | 248 | 263 | 278 |  |  |  |  |
| Ice Water Path |  |  |  |  | 234 | 249 | 264 | 279 |  |  |  |  |
| Top Pressure |  |  |  |  | 235 | 250 | 265 | 280 |  |  |  |  |
| Effective Pressure |  |  |  |  | 236 | 251 | 266 | 281 |  |  |  |  |
| Effective Temperature |  |  |  |  | 237 | 252 | 267 | 282 |  |  |  |  |
| Effective Height |  |  |  |  | 238 | 253 | 268 | 283 |  |  |  |  |
| Bottom Pressure |  |  |  |  | 239 | 254 | 269 | 284 |  |  |  |  |
| Liquid Particle Radius |  |  |  |  | 240 | 255 | 270 | 285 |  |  |  |  |
| Ice Particle Diameter |  |  |  |  | 241 | 256 | 271 | 286 |  |  |  |  |
| Particle Phase |  |  |  |  | 242 | 257 | 272 | 287 |  |  |  |  |
| Vertical Aspect Ratio |  |  |  |  | 243 | 258 | 273 | 288 |  |  |  |  |

Color Red	-	High Cloud

Color Green	-	Uppermid Cloud

Color Blue	-	Lowermid Cloud

Color Black	-	Low Cloud

- Table of Cloud Layers

| Cloud Layer Index | Cloud Layer | Pressure level (mb) |
| --- | --- | --- |
| 1 | High | 50-300 |
| 2 | Upper Mid | 300-500 |
| 3 | Lower Mid | 500-700 |
| 4 | Low | 700-Surface |

Stowe-Ignatov Aerosol Optical Depth

| SDS Name | DataType | Units | Range | No. Of Elements Regional |
| --- | --- | --- | --- | --- |
| Aerosol visible optical depth - 0.63 m | 32-bit real | N/A | 0 .. 5 | Nlon*Nlat*Ns |
| Aerosol visible optical depth - 1.6 m | 32-bit real | N/A | 0 .. 5 | Nlon*Nlat*Ns |

* No. of Elements for Zonal:  Nlat*Ns

* No. of Elements for Global:  Ns

SDS Index of Stowe-Ignatov Aerosol Optical Depth

| SDS Name | Regional Monthly | Zonal Monthly | Global Monthly |
| --- | --- | --- | --- |
| Aerosol visible optical depth - 0.63 m | 71 | 289 | 501 |
| Aerosol visible optical depth - 1.6 m | 72 | 290 | 502 |

| MODIS Aerosol Optical Depth |
| --- |
| SDS Name | DataType | Units | Range | No. Of Elements Regional |
| Initial Aerosol Optical Depth | 32-bit real | N/A | 0 .. 5 | Nlon*Nlat*Ns |
| Aerosol Opt. Depth at 0.47 m in Land | 32-bit real | N/A | 0 .. 5 | Nlon*Nlat*Ns |
| Aerosol Opt. Depth at 0.55 m in Land | 32-bit real | N/A | 0 .. 5 | Nlon*Nlat*Ns |
| Aerosol Opt. Depth at 0.66 m in Land | 32-bit real | N/A | 0 .. 5 | Nlon*Nlat*Ns |
| Aerosol Opt. Depth at 0.47 m in Ocean | 32-bit real | N/A | 0 .. 5 | Nlon*Nlat*Ns |
| Aerosol Opt. Depth at 0.55 m in Ocean | 32-bit real | N/A | 0 .. 5 | Nlon*Nlat*Ns |
| Aerosol Opt. Depth at 0.66 m in Ocean | 32-bit real | N/A | 0 .. 5 | Nlon*Nlat*Ns |
| Aerosol Opt. Depth at 0.87 m in Ocean | 32-bit real | N/A | 0 .. 5 | Nlon*Nlat*Ns |
| Aerosol Opt. Depth at 1.24 m in Ocean | 32-bit real | N/A | 0 .. 5 | Nlon*Nlat*Ns |
| Aerosol Opt. Depth at 1.64 m in Ocean | 32-bit real | N/A | 0 .. 5 | Nlon*Nlat*Ns |
| Aerosol Opt. Depth at 2.13 m in Ocean | 32-bit real | N/A | 0 .. 5 | Nlon*Nlat*Ns |

* No. of Elements for Zonal:  Nlat*Ns

* No. of Elements for Global:  Ns

SDS Index of MODIS Aerosol Optical Depth

| SDS Name | Regional Monthly | Zonal Monthly | Global Monthly |
| --- | --- | --- | --- |
| Initial Aerosol Optical Depth | 73 | 291 | 503 |
| Aerosol Opt. Depth at 0.47 m in Land | 74 | 292 | 504 |
| Aerosol Opt. Depth at 0.55 m in Land | 75 | 293 | 505 |
| Aerosol Opt. Depth at 0.66 m in Land | 76 | 294 | 506 |
| Aerosol Opt. Depth at 0.47m in Ocean | 77 | 295 | 507 |
| Aerosol Opt. Depth at 0.55 m in Ocean | 78 | 296 | 508 |
| Aerosol Opt. Depth at 0.66 m in Ocean | 79 | 297 | 509 |
| Aerosol Opt. Depth at 0.87 m in Ocean | 80 | 298 | 510 |
| Aerosol Opt. Depth at 1.24 m in Ocean | 81 | 299 | 511 |
| Aerosol Opt. Depth at 1.64 m in Ocean | 82 | 300 | 512 |
| Aerosol Opt. Depth at 2.13 m in Ocean | 83 | 301 | 513 |

| Tuned Pristine Fluxes |
| --- |
| SDS Name | DataType | Units | Range | No. Of Elements Regional |
| Tuned Pristine SW Surface Up | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Tuned Pristine SW Surface Down | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Tuned Pristine SW TOA Up | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Tuned Pristine LW Surface Up | 32-bit real | W m-2 | 0 .. 850 | Nlon*Nlat*Ns |
| Tuned Pristine LW Surface Down | 32-bit real | W m-2 | 0 .. 700 | Nlon*Nlat*Ns |
| Tuned Pristine LW TOA Up | 32-bit real | W m-2 | 0 .. 850 | Nlon*Nlat*Ns |
| Tuned Pristine WN Surface Up | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ns |
| Tuned Pristine WN Surface Down | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ns |
| Tuned Pristine WN TOA Up | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ns |

* No. of Elements for Zonal:  Nlat*Ns

* No. of Elements for Global:  Ns

SDS Index of Tuned Pristine Fluxes

| SDS Name | Regional Monthly | Zonal Monthly | Global Monthly |
| --- | --- | --- | --- |
| Tuned Pristine SW Surface Up | 84 | 302 | 514 |
| Tuned Pristine SW Surface Down | 85 | 303 | 515 |
| Tuned Pristine SW TOA Up | 86 | 304 | 516 |
| Tuned Pristine LW Surface Up | 87 | 305 | 517 |
| Tuned Pristine LW Surface Down | 88 | 306 | 518 |
| Tuned Pristine LW TOA Up | 89 | 307 | 519 |
| Tuned Pristine WN Surface Up | 90 | 308 | 520 |
| Tuned Pristine WN Surface Down | 91 | 309 | 521 |
| Tuned Pristine WN TOA Up | 92 | 310 | 522 |

Tuned ClearSky Flux Profiles, Table 4(c) defines Nlev

| SDS Name | DataType | Units | Range | No. Of Elements Regional |
| --- | --- | --- | --- | --- |
| Tuned Clear-Sky SW Up | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns*Nlev |
| Tuned Clear-Sky SW Down | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns*Nlev |
| Tuned Clear-Sky LW Up | 32-bit real | W m-2 | 0 .. 850 | Nlon*Nlat*Ns*Nlev |
| Tuned Clear-Sky LW Down | 32-bit real | W m-2 | 0 .. 700 | Nlon*Nlat*Ns*Nlev |
| Tuned Clear-Sky WN Up | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ns*Nlev |
| Tuned Clear-Sky WN Down | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ns*Nlev |

* No. of Elements for Zonal:  Nlat*Ns

* No. of Elements for Global:  Ns

SDS Index of Tuned ClearSky Flux Profiles

| SDS Name | Regional Monthly | Zonal Monthly | Global Monthly |
| --- | --- | --- | --- |
| Tuned Clear-Sky SW Up | 93 | 311 | 523 |
| Tuned Clear-Sky SW Down | 94 | 312 | 524 |
| Tuned Clear-Sky LW Up | 95 | 313 | 525 |
| Tuned Clear-Sky LW Down | 96 | 314 | 526 |
| Tuned Clear-Sky WN Up | 97 | 315 | 527 |
| Tuned Clear-Sky WN Down | 98 | 316 | 528 |

Tuned TotalSky-NoAerosol Fluxes

| SDS Name | DataType | Units | Range | No. Of Elements Regional |
| --- | --- | --- | --- | --- |
| Tuned Total-Sky-NoAerosol SW Surface Up | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Tuned Total-Sky-NoAerosol SW Surface Down | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Tuned Total-Sky-NoAerosol SW TOA Up | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Tuned Total-Sky-NoAerosol LW Surface Up | 32-bit real | W m-2 | 0 .. 850 | Nlon*Nlat*Ns |
| Tuned Total-Sky-NoAerosol LW Surface Down | 32-bit real | W m-2 | 0 .. 700 | Nlon*Nlat*Ns |
| Tuned Total-Sky-NoAerosol LW TOA Up | 32-bit real | W m-2 | 0 .. 850 | Nlon*Nlat*Ns |
| Tuned Total-Sky-NoAerosol WN Surface Up | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ns |
| Tuned Total-Sky-NoAerosol WN Surface Down | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ns |
| Tuned Total-Sky-NoAerosol WN TOA Up | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ns |

* No. of Elements for Zonal:  Nlat*Ns

* No. of Elements for Global:  Ns

SDS Index of Tuned TotalSky-NoAerosol Fluxes

| SDS Name | Regional Monthly | Zonal Monthly | Global Monthly |
| --- | --- | --- | --- |
| Tuned Total-Sky-NoAerosol SW Surface Up | 99 | 317 | 529 |
| Tuned Total-Sky-NoAerosol SW Surface Down | 100 | 318 | 530 |
| Tuned Total-Sky-NoAerosol SW TOA Up | 101 | 319 | 531 |
| Tuned Total-Sky-NoAerosol LW Surface Up | 102 | 320 | 532 |
| Tuned Total-Sky-NoAerosol LW Surface Down | 103 | 321 | 533 |
| Tuned Total-Sky-NoAerosol LW TOA Up | 104 | 322 | 534 |
| Tuned Total-Sky-NoAerosol WN Surface Up | 105 | 323 | 535 |
| Tuned Total-Sky-NoAerosol WN Surface Down | 106 | 324 | 536 |
| Tuned Total-Sky-NoAerosol WN TOA Up | 107 | 325 | 537 |

Tuned TotalSky Flux Profiles, Table 4(c) defines Nlev

| SDS Name | DataType | Units | Range | No. Of Elements Regional |
| --- | --- | --- | --- | --- |
| Tuned Total-Sky SW Up | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns*Nlev |
| Tuned Total-Sky SW Down | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns*Nlev |
| Tuned Total-Sky LW Up | 32-bit real | W m-2 | 0 .. 850 | Nlon*Nlat*Ns*Nlev |
| Tuned Total-Sky LW Down | 32-bit real | W m-2 | 0 .. 700 | Nlon*Nlat*Ns*Nlev |
| Tuned Total-Sky WN Up | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ns*Nlev |
| Tuned Total-Sky WN Down | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ns*Nlev |

* No. of Elements for Zonal:  Nlat*Ns*Nlev

* No. of Elements for Global:  Ns*Nlev

SDS Index of Tuned TotalSky Flux Profiles

| SDS Name | Regional Monthly | Zonal Monthly | Global Monthly |
| --- | --- | --- | --- |
| Tuned Total-Sky SW Up | 108 | 326 | 538 |
| Tuned Total-Sky SW Down | 109 | 327 | 539 |
| Tuned Total-Sky LW Up | 110 | 328 | 540 |
| Tuned Total-Sky LW Down | 111 | 329 | 541 |
| Tuned Total-Sky WN Up | 112 | 330 | 542 |
| Tuned Total-Sky WN Down | 113 | 331 | 543 |

Untuned Pristine Fluxes

| SDS Name | DataType | Units | Range | No. Of Elements Regional |
| --- | --- | --- | --- | --- |
| Untuned Pristine SW Surface Up | 32-bit real | W m-2 | 0 .. 1500 | Nlon*Nlat*Ns |
| Untuned Pristine SW Surface Down | 32-bit real | W m-2 | 0 .. 1500 | Nlon*Nlat*Ns |
| Untuned Pristine SW TOA Up | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Untuned Pristine LW Surface Up | 32-bit real | W m-2 | 0 .. 850 | Nlon*Nlat*Ns |
| Untuned Pristine LW Surface Down | 32-bit real | W m-2 | 0 .. 700 | Nlon*Nlat*Ns |
| Untuned Pristine LW TOA Up | 32-bit real | W m-2 | 0 .. 850 | Nlon*Nlat*Ns |
| Untuned Pristine WN Surface Up | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ns |
| Untuned Pristine WN Surface Down | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ns |
| Untuned Pristine WN TOA Up | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ns |

* No. of Elements for Zonal:  Nlat*Ns

* No. of Elements for Global:  Ns

SDS Index of Untuned Pristine Fluxes

| SDS Name | Regional Monthly | Zonal Monthly | Global Monthly |
| --- | --- | --- | --- |
| Untuned Pristine SW Surface Up | 114 | 332 | 544 |
| Untuned Pristine SW Surface Down | 115 | 333 | 545 |
| Untuned Pristine SW TOA Up | 116 | 334 | 546 |
| Untuned Pristine LW Surface Up | 117 | 335 | 547 |
| Untuned Pristine LW Surface Down | 118 | 336 | 548 |
| Untuned Pristine LW TOA Up | 119 | 337 | 549 |
| Untuned Pristine WN Surface Up | 120 | 338 | 550 |
| Untuned Pristine WN Surface Down | 121 | 339 | 551 |
| Untuned Pristine WN TOA Up | 122 | 340 | 552 |

Untuned ClearSky Fluxes

| SDS Name | DataType | Units | Range | No. Of Elements Regional |
| --- | --- | --- | --- | --- |
| Untuned Clear-Sky SW Surface Up | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Untuned Clear-Sky SW Surface Down | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Untuned Clear-Sky SW TOA Up | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Untuned Clear-Sky LW Surface Up | 32-bit real | W m-2 | 0 .. 850 | Nlon*Nlat*Ns |
| Untuned Clear-Sky LW Surface Down | 32-bit real | W m-2 | 0 .. 700 | Nlon*Nlat*Ns |
| Untuned Clear-Sky LW TOA Up | 32-bit real | W m-2 | 0 .. 850 | Nlon*Nlat*Ns |
| Untuned Clear-Sky WN Surface Up | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ns |
| Untuned Clear-Sky WN Surface Down | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ns |
| Untuned Clear-Sky WN TOA Up | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ns |

* No. of Elements for Zonal:  Nlat*Ns

* No. of Elements for Global:  Ns

| SDS Index of Untuned ClearSky Fluxes |
| --- |
| SDS Name | Regional Monthly | Zonal Monthly | Global Monthly |
| Untuned Clear-Sky SW Surface Up | 123 | 341 | 553 |
| Untuned Clear-Sky SW Surface Down | 124 | 342 | 554 |
| Untuned Clear-Sky SW TOA Up | 125 | 343 | 555 |
| Untuned Clear-Sky LW Surface Up | 126 | 344 | 556 |
| Untuned Clear-Sky LW Surface Down | 127 | 345 | 557 |
| Untuned Clear-Sky LW TOA Up | 128 | 346 | 558 |
| Untuned Clear-Sky WN Surface Up | 129 | 347 | 559 |
| Untuned Clear-Sky WN Surface Down | 130 | 348 | 560 |
| Untuned Clear-Sky WN TOA Up | 131 | 349 | 561 |

| Untuned TotalSky-NoAerosol Fluxes |
| --- |
| SDS Name | DataType | Units | Range | No. Of Elements Regional |
| Untuned Total-Sky-NoAerosol SW Surface Up | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Untuned Total-Sky-NoAerosol SW Surface Down | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Untuned Total-Sky-NoAerosol SW TOA Up | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Untuned Total-Sky-NoAerosol LW Surface Up | 32-bit real | W m-2 | 0 .. 850 | Nlon*Nlat*Ns |
| Untuned Total-Sky-NoAerosol LW Surface Down | 32-bit real | W m-2 | 0 .. 700 | Nlon*Nlat*Ns |
| Untuned Total-Sky-NoAerosol LW TOA Up | 32-bit real | W m-2 | 0 .. 850 | Nlon*Nlat*Ns |
| Untuned Total-Sky-NoAerosol WN Surface Up | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ns |
| Untuned Total-Sky-NoAerosol WN Surface Down | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ns |
| Untuned Total-Sky-NoAerosol WN TOA Up | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ns |

* No. of Elements for Zonal:  Nlat*Ns

* No. of Elements for Global:  Ns

SDS Index of Untuned TotalSky-NoAerosol Fluxes

| SDS Name | Regional Monthly | Zonal Monthly | Global Monthly |
| --- | --- | --- | --- |
| Untuned Total-Sky-NoAerosol SW Surface Up | 132 | 350 | 562 |
| Untuned Total-Sky-NoAerosol SW Surface Down | 133 | 351 | 563 |
| Untuned Total-Sky-NoAerosol SW TOA Up | 134 | 352 | 564 |
| Untuned Total-Sky-NoAerosol LW Surface Up | 135 | 353 | 565 |
| Untuned Total-Sky-NoAerosol LW Surface Down | 136 | 354 | 566 |
| Untuned Total-Sky-NoAerosol LW TOA Up | 137 | 355 | 567 |
| Untuned Total-Sky-NoAerosol WN Surface Up | 138 | 356 | 568 |
| Untuned Total-Sky-NoAerosol WN Surface Down | 139 | 357 | 569 |
| Untuned Total-Sky-NoAerosol WN TOA Up | 140 | 358 | 570 |

| Untuned TotalSky Fluxes |
| --- |
| SDS Name | DataType | Units | Range | No. Of Elements Regional |
| Untuned Total-Sky SW Surface Up | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Untuned Total-Sky SW Surface Down | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Untuned Total-Sky SW TOA Up | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Untuned Total-Sky LW Surface Up | 32-bit real | W m-2 | 0 .. 850 | Nlon*Nlat*Ns |
| Untuned Total-Sky LW Surface Down | 32-bit real | W m-2 | 0 .. 700 | Nlon*Nlat*Ns |
| Untuned Total-Sky LW TOA Up | 32-bit real | W m-2 | 0 .. 850 | Nlon*Nlat*Ns |
| Untuned Total-Sky WN Surface Up | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ns |
| Untuned Total-Sky WN Surface Down | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ns |
| Untuned Total-Sky WN TOA Up | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ns |

* No. of Elements for Zonal:  Nlat*Ns

* No. of Elements for Global:  Ns

SDS Index of Untuned TotalSky Fluxes

| SDS Name | Regional Monthly | Zonal Monthly | Global Monthly |
| --- | --- | --- | --- |
| Untuned Total-Sky SW Surface Up | 141 | 359 | 571 |
| Untuned Total-Sky SW Surface Down | 142 | 360 | 572 |
| Untuned Total-Sky SW TOA Up | 143 | 361 | 573 |
| Untuned Total-Sky LW Surface Up | 144 | 362 | 574 |
| Untuned Total-Sky LW Surface Down | 145 | 363 | 575 |
| Untuned Total-Sky LW TOA Up | 146 | 364 | 576 |
| Untuned Total-Sky WN Surface Up | 147 | 365 | 577 |
| Untuned Total-Sky WN Surface Down | 148 | 366 | 578 |
| Untuned Total-Sky WN TOA Up | 149 | 367 | 579 |

Satellite Emulated WN TOA Fluxes

| SDS Name | DataType | Units | Range | No. Of Elements Regional |
| --- | --- | --- | --- | --- |
| Untuned Satellite Emulated WN TOA | 32-bit real | W m-2 | 0 .. 200 | Nlon*Nlat*Ns |
| Tuned Satellite Emulated WN TOA | 32-bit real | W m-2 | 0 .. 200 | Nlon*Nlat*Ns |

* No. of Elements for Zonal:  Nlat*Ns

* No. of Elements for Global:  Ns

SDS Index of Satellite Emulated WN TOA Fluxes

| SDS Name | Regional Monthly | Zonal Monthly | Global Monthly |
| --- | --- | --- | --- |
| Untuned Satellite Emulated WN TOA | 150 | 368 | 580 |
| Tuned Satellite Emulated WN TOA | 151 | 369 | 581 |

TOA Fluxes Error

| SDS Name | DataType | Units | Range | No. Of Elements Regional |
| --- | --- | --- | --- | --- |
| Tuned Minus Observed SW TOA | 32-bit real | W m-2 | -1400 .. 1400 | Nlon*Nlat*Ns |
| Untuned Minus Observed SW TOA | 32-bit real | W m-2 | -1400 .. 1400 | Nlon*Nlat*Ns |
| Tuned Minus Observed LW TOA | 32-bit real | W m-2 | -600 .. 600 | Nlon*Nlat*Ns |
| Untuned Minus Observed LW TOA | 32-bit real | W m-2 | -600 .. 600 | Nlon*Nlat*Ns |

* No. of Elements for Zonal:  Nlat*Ns

* No. of Elements for Global:  Ns

SDS Index of TOA Fluxes Error

| SDS Name | Regional Monthly | Zonal Monthly | Global Monthly |
| --- | --- | --- | --- |
| Tuned Minus Observed SW TOA | 152 | 370 | 582 |
| Untuned Minus Observed SW TOA | 153 | 371 | 583 |
| Tuned Minus Observed LW TOA | 154 | 372 | 584 |
| Untuned Minus Observed LW TOA | 155 | 373 | 585 |

Number of Hourboxes

| SDS Name | DataType | Units | Range | No. Of Elements Regional |
| --- | --- | --- | --- | --- |
| Number of Observed SW | 32-bit real | N/A | 0 .. 744 | Nlon*Nlat |
| Number of Untuned SW | 32-bit real | N/A | 0 .. 744 | Nlon*Nlat |
| Number of Tuned SW | 32-bit real | N/A | 0 .. 744 | Nlon*Nlat |
| Number of Observed LW | 32-bit real | N/A | 0 .. 744 | Nlon*Nlat |
| Number of Untuned LW | 32-bit real | N/A | 0 .. 744 | Nlon*Nlat |
| Number of Tuned LW | 32-bit real | N/A | 0 .. 744 | Nlon*Nlat |

SDS Index of Number of Hourboxes

| SDS Name | Regional Monthly |
| --- | --- |
| Number of Observed SW | 156 |
| Number of Untuned SW | 157 |
| Number of Tuned SW | 158 |
| Number of Observed LW | 159 |
| Number of Untuned LW | 160 |
| Number of Tuned LW | 161 |

| Constrainment Adjustments, Table 4(c) defines Nlev |
| --- |
| SDS Name | DataType | Units | Range | No. Of Elements Regional |
| Total column precipitable water - initial | 32-bit real | cm | 0 .. 10 | Nlon*Nlat*Ns |
| Total column precipitable water - adjusted | 32-bit real | cm | 0 .. 10 | Nlon*Nlat*Ns |
| Upper tropospheric precipitable water - initial | 32-bit real | cm | 0 .. 10 | Nlon*Nlat*Ns |
| Upper tropospheric precipitable water - adjusted | 32-bit real | cm | 0 .. 10 | Nlon*Nlat*Ns |
| Upper tropospheric humidity - initial | 32-bit real | N/A | 0.0 .. 100.0 | Nlon*Nlat*Ns |
| Upper tropospheric humidity - adjusted | 32-bit real | N/A | 0.0 .. 100.0 | Nlon*Nlat*Ns |
| Aerosol optical depth - initial | 32-bit real | N/A | 0 .. 5 | Nlon*Nlat*Ns |
| Aerosol optical depth - adjusted | 32-bit real | N/A | 0 .. 5 | Nlon*Nlat*Ns |
| Skin temperature - initial | 32-bit real | K | 175 .. 375 | Nlon*Nlat*Ns |
| Skin temperature - adjusted | 32-bit real | K | 175 .. 375 | Nlon*Nlat*Ns |
| Surface pressure | 32-bit real | hPa | 0 .. 1100 | Nlon*Nlat*Ns |
| Column ozone - initial | 32-bit real | DU | 0 .. 1000 | Nlon*Nlat*Ns |
| Mean visible optical depth- adjusted | 32-bit real | N/A | -400 .. 400 | Nlon*Nlat*Ns *Nlev |
| Mean cloud fractional area - adjusted | 32-bit real | Percent | 0 .. 100 | Nlon*Nlat*Ns *Nlev |
| Mean cloud effective temperature - adjusted | 32-bit real | K | 100 .. 350 | Nlon*Nlat*Ns *Nlev |

* No. of Elements for Zonal:  Nlat*Ns and Nlat*Ns*Nlev accordingly

* No. of Elements for Global:  Ns and Ns*Nlev accordingly

| SDS Index of Constrainment Adjustments |
| --- |
| SDS Name | Regional Monthly | Zonal Monthly | Global Monthly |
| Total column precipitable water - initial | 162 | 374 | 586 |
| Total column precipitable water - adjusted | 163 | 375 | 587 |
| Upper tropospheric precipitable water - initial | 164 | 376 | 588 |
| Upper tropospheric precipitable water - adjusted | 165 | 377 | 589 |
| Upper tropospheric humidity - initial | 166 | 378 | 590 |
| Upper tropospheric humidity - adjusted | 167 | 379 | 591 |
| Aerosol optical depth - initial | 168 | 380 | 592 |
| Aerosol optical depth - adjusted | 169 | 381 | 593 |
| Skin temperature - initial | 170 | 382 | 594 |
| Skin temperature - adjusted | 171 | 383 | 595 |
| Surface pressure | 172 | 384 | 596 |
| Column ozone - initial | 173 | 385 | 597 |
| Mean visible optical depth- adjusted | 174 | 386 | 598 |
| Mean cloud fractional area - adjusted | 175 | 387 | 599 |
| Mean cloud effective temperature - adjusted | 176 | 388 | 600 |

Surface SW Direct/Diffuse Fluxes

| SDS Name | DataType | Units | Range | No. Of Elements Regional |
| --- | --- | --- | --- | --- |
| Total-Sky SW flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Clear-sky SW flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Pristine-Sky SW flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Actinic-Sky SW flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Total-Sky SW flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Clear-sky SW flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Pristine-Sky SW flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Actinic-Sky SW flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |

* No. of Elements for Zonal:  Nlat*Ns

* No. of Elements for Global:  Ns

SDS Index of Surface SW Direct/Diffuse Fluxes

| SDS Name | Regional Monthly | Zonal Monthly | Global Monthly |
| --- | --- | --- | --- |
| Total-Sky SW flux - Diffuse | 177 | 389 | 601 |
| Clear-sky SW flux - Diffuse | 178 | 390 | 602 |
| Pristine-Sky SW flux - Diffuse | 179 | 391 | 603 |
| Actinic-Sky SW flux - Diffuse | 180 | 392 | 604 |
| Total-Sky SW flux - Direct | 181 | 393 | 605 |
| Clear-sky SW flux - Direct | 182 | 394 | 606 |
| Pristine-Sky SW flux - Direct | 183 | 395 | 607 |
| Actinic-Sky SW flux - Direct | 184 | 396 | 608 |

| UVA - UVB Fluxes |
| --- |
| SDS Name | DataType | Units | Range | No. Of Elements Regional |
| TOA Downwelling UVB Flux | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| TOA Downwelling UVA Flux | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Pristine UVB Surface flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Pristine UVB Surface flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Pristine UVA Surface flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Pristine UVA Surface flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Clear-Sky UVB Surface flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Clear-Sky UVB Surface flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Clear-Sky UVA Surface flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Clear-Sky UVA Surface flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Total-Sky-NoAerosol UVB Surface flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Total-Sky-NoAerosol UVB Surface flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Total-Sky-NoAerosol UVA Surface flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Total-Sky-NoAerosol UVA Surface flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Total-Sky UVB Surface flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Total-Sky UVB Surface flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Total-Sky UVA Surface flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Total-Sky UVA Surface flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Total-Sky Surface UV Index | 32-bit real | N/A | 0 .. 30 | Nlon*Nlat*Ns |
| Clear-Sky Surface UV Index | 32-bit real | N/A | 0 .. 30 | Nlon*Nlat*Ns |
| Pristine Surface UV Index | 32-bit real | N/A | 0 .. 30 | Nlon*Nlat*Ns |
| Total-Sky-NoAerosol Surface UV- Index | 32-bit real | N/A | 0 .. 30 | Nlon*Nlat*Ns |
| Total-Sky UVB Surface Up | 32-bit real | W m-2 | 0 .. 5 | Nlon*Nlat*Ns |
| Snow Grain Size | 32-bit real | μm | 50 .. 2000 | Nlon*Nlat*Ns |
| Match Total Aerosol Optical Depth at 0.55 μm | 32-bit real | N/A | 0 .. 10 | Nlon*Nlat*Ns |

* No. of Elements for Zonal:  Nlat*Ns

* No. of Elements for Global:  Ns

SDS Index of UVA – UVB Fluxes

| SDS Name | Regional Monthly | Zonal Monthly | Global Monthly |
| --- | --- | --- | --- |
| TOA Downwelling UVB Flux | 185 | 397 | 609 |
| TOA Downwelling UVA Flux | 186 | 398 | 610 |
| Pristine UVB Surface flux - Direct | 187 | 399 | 611 |
| Pristine UVB Surface flux - Diffuse | 188 | 400 | 612 |
| Pristine UVA Surface flux - Direct | 189 | 401 | 613 |
| Pristine UVA Surface flux - Diffuse | 190 | 402 | 614 |
| Clear-Sky UVB Surface flux - Direct | 191 | 403 | 615 |
| Clear-Sky UVB Surface flux - Diffuse | 192 | 404 | 616 |
| Clear-Sky UVA Surface flux - Direct | 193 | 405 | 617 |
| Clear-Sky UVA Surface flux - Diffuse | 194 | 406 | 618 |
| Total-Sky-NoAerosol UVB Surface flux - Direct | 195 | 407 | 619 |
| Total-Sky-NoAerosol UVB Surface flux - Diffuse | 196 | 408 | 620 |
| Total-Sky-NoAerosol UVA Surface flux - Direct | 197 | 409 | 621 |
| Total-Sky-NoAerosol UVA Surface flux - Diffuse | 198 | 410 | 622 |
| Total-Sky UVB Surface flux - Direct | 199 | 411 | 623 |
| Total-Sky UVB Surface flux - Diffuse | 200 | 412 | 624 |
| Total-Sky UVA Surface flux - Direct | 201 | 413 | 625 |
| Total-Sky UVA Surface flux - Diffuse | 202 | 414 | 626 |
| Total-Sky Surface UV Index | 203 | 415 | 627 |
| Clear-Sky Surface UV Index | 204 | 416 | 628 |
| Pristine Surface UV Index | 205 | 417 | 629 |
| Total-Sky-NoAerosol Surface UV- Index | 206 | 418 | 630 |
| Total-Sky UVB Surface Up | 207 | 419 | 631 |
| Snow Grain Size | 208 | 420 | 632 |
| Match Total Aerosol Optical Depth at 0.55 μm | 209 | 421 | 633 |

| PAR Fluxes |
| --- |
| SDS Name | DataType | Units | Range | No. Of Elements Regional |
| TOA Downwelling PAR Flux | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Total-Sky PAR Surface flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Total-Sky PAR Surface flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Total-Sky PAR PURV Surface flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Total-Sky PAR PURV Surface flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Total-Sky PAR ChlorA Surface flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Total-Sky PAR ChlorA Surface flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Clear-Sky PAR Surface flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Clear-Sky PAR Surface Surface flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Pristine PAR Surface flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |
| Pristine PAR Surface flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ns |

* No. of Elements for Zonal:  Nlat*Ns

* No. of Elements for Global:  Ns

SDS Index of PAR Fluxes

| SDS Name | Regional Monthly | Zonal Monthly | Global Monthly |
| --- | --- | --- | --- |
| TOA Downwelling PAR Flux | 210 | 422 | 634 |
| Total-Sky PAR Surface flux - Direct | 211 | 423 | 635 |
| Total-Sky PAR Surface flux - Diffuse | 212 | 424 | 636 |
| Total-Sky PAR PURV Surface flux - Direct | 213 | 425 | 637 |
| Total-Sky PAR PURV Surface flux - Diffuse | 214 | 426 | 638 |
| Total-Sky PAR ChlorA Surface flux - Direct | 215 | 427 | 639 |
| Total-Sky PAR ChlorA Surface flux - Diffuse | 216 | 428 | 640 |
| Clear-Sky PAR Surface flux - Direct | 217 | 429 | 641 |
| Clear-Sky PAR Surface flux - Diffuse | 218 | 430 | 642 |
| Pristine PAR Surface flux - Direct | 219 | 431 | 643 |
| Pristine PAR Surface flux - Diffuse | 220 | 432 | 644 |

Pristine-Sky SW MultiStream Correction

| SDS Name | DataType | Units | Range | No. Of Elements Regional |
| --- | --- | --- | --- | --- |
| SW TOA Flux - Up - Pristine-Sky - Corrected | 32-bit real | W m-2 | 0 .. 1000 | Nlon*Nlat*Ns |
| SW Surface Flux - Down- Pristine-Sky - Corrected | 32-bit real | W m-2 | 0 .. 1000 | Nlon*Nlat*Ns |

* No. of Elements for Zonal:  Nlat*Ns

* No. of Elements for Global:  Ns

SDS Index of Pristine-Sky SW MultiStream Correction

| SDS Name | Regional Monthly | Zonal Monthly | Global Monthly |
| --- | --- | --- | --- |
| SW TOA Flux - Up - Pristine-Sky - Corrected | 221 | 433 | 645 |
| SW Surface Flux - Down- Pristine-Sky - Corrected | 222 | 434 | 646 |

File Size:  SYN1deg-Monthly 148.69 MB

Number of Regional parameters:  222

Number of Zonal and Global parameters:  212

Sets of Regional Records:  64800

Sets of Zonal Records:  180

Set of Global Records:  1

SYN1deg-Month Revision Record

The product Revision Record contains information pertaining to approved section changes.  The table lists the date the Software Configuration Change Request (SCCR) was approved, the Release and Version Number, the SCCR number, a short description of the revision, and the revised sections.  The authors are listed on the document cover.

| SYN1deg-Month Revision Record |
| --- |
| SCCR Approval Date | Release/ Version Number | SCCR Number | Description of Revision | Section(s) Affected |
| 07/19/2010 | R5V1 | 795 | Initial version of this document. This data product was previously named AVG/ZAVG. | All |
|  |  |  | The ASDC footer was added to the bottom of the document. (12/04/2013) | All |
|  |  |  | Eliminated section numbers from the Data Products Catalog. Specifically, in this document, section number 2.11 was removed. (12/17/2013) | All |
|  |  |  | Updated some links to refer to the .pdf file instead of the .doc file. (06/20/2014) | All |