Synoptic Radiative Fluxes and Clouds Intermediate (SYNI)

The Synoptic Radiative Fluxes and Clouds Intermediate (SYNI) product contains a month of space and time averaged Clouds and the Earth's Radiant Energy System (CERES) data for a single broadband scanner instrument; it also incorporates 3-hourly narrowband data from several geostationary satellites.  Flux data from the TSIB product, along with MOA data, are used to calculate radiate flux profiles, cloud conditions, and aerosol optical depths using the same models as the Instantaneous SARB subsystem.  There are data for every hour of the month for each 1-degree region.  These data are organized into 180 zonal files, each of which contains nested regions depending on the colatitude.

The SYNI contains the following apriori and observed input:

Regional data

Cloud category properties for four (low, lower middle, upper middle and high) cloud layers

Observed CERES TOA clear-sky and all-sky fluxes

MODIS based spectral aerosol optical depths

The SYNI contains the following constrained (tuned) vertical flux profiles for both clear-sky and total-sky conditions evaluated at the TOA, 70mb, 200mb, 500mb, and surface:

Longwave, Shortwave, and Window channels upward and downward.

The constrained (tuned) and initial (untuned) profiles for the following are included for pristine (clear-sky no-aerosol), clear-sky, total-sky-no-aerosol, and total-sky conditions:

Longwave upward at the surface and TOA.

Longwave downward at the surface.

Shortwave upward at the surface and TOA.

Shortwave downward at the surface.

Window channel upward at the surface and TOA.

Window channel downward at the surface.

The adjustments to the radiative transfer model input parameters between the initial and the constrained (adjusted) passes are also contained on the SYNI.  These parameters include:

Surface albedo and skin temperature

Total column precipitable water, upper tropospheric relative humidity, and column ozone

Aerosol optical depth

Cloud optical depth, fractional area, and effective temperature

The SYNI contains the direct and diffuse shortwave surface fluxes for total-sky, clear-sky, pristine and actinic conditions. The SYNI also contains surface UVA and UVB downwelling and direct diffuse ratios for total-sky, clear-sky, pristine, and total-sky-no-aerosol conditions.

Level:  3

Frequency:  1/Month

Portion of Atmosphere Covered:  Surface, Internal and TOA

Time Interval Covered:		Portion of Globe Covered:

File:  Monthly			File:  1 colatitude zone

Record:  Hourly			Record:  1 degree equal angle region

Product Version:

TRMM: N/A

Terra: Beta3, Edition2C, Edition3A

Aqua: Beta4, Edition2B, Edition3A

SYNI Data Fields

The SYNI contains 162 data fields which are parameter collections of one-degree regional data where multiple dimensions refer to pressure levels, cloud conditions, or bandwidths.  Product sizing information is given in Table 1.

| Product Sizing Information |
| --- |
| Name | Units | Range | Dim | Data Type |
| Photosynthetically active radiation over surface | W m-2 | 0 .. 780 | 1 | 32 bit-real |
| Direct/diffuse surface ratio | N/A | 0 .. 30 | 1 | 32 bit-real |
| Corrected initial broadband surface albedo | N/A | 0 .. 1 | 1 | 32 bit-real |
| Number of atmospheric levels | N/A | 0 .. 5 | 1 | 32 bit integer |
| Pressure levels | hPa | 0 .. 1100 | 5 | 32 bit-real |
| SW flux - upward – pristine | W m-2 | 0 .. 1400 | 2 | 32 bit-real |
| SW flux - downward – pristine | W m-2 | 0 .. 1400 | 2 | 32 bit-real |
| LW flux - upward – pristine | W m-2 | 0 .. 850 | 2 | 32 bit-real |
| LW flux - downward – pristine | W m-2 | 0 .. 700 | 2 | 32 bit-real |
| WN flux - upward – pristine | W m-2 | 0 .. 370 | 2 | 32 bit-real |
| WN flux - downward – pristine | W m-2 | 0 .. 370 | 2 | 32 bit-real |
| SW flux - upward for clear-sky | W m-2 | 0 .. 1400 | 5 | 32 bit-real |
| SW flux - downward for clear-sky | W m-2 | 0 .. 1400 | 5 | 32 bit-real |
| LW flux - upward for clear-sky | W m-2 | 0 .. 850 | 5 | 32 bit-real |
| LW flux - downward for clear-sky | W m-2 | 0 .. 700 | 5 | 32 bit-real |
| WN flux - upward for clear-sky | W m-2 | 0 .. 370 | 5 | 32 bit-real |
| WN flux - downward for clear-sky | W m-2 | 0 .. 370 | 5 | 32 bit-real |
| SW flux - upward for total-sky | W m-2 | 0 .. 1400 | 5 | 32 bit-real |
| SW flux - downward for total-sky | W m-2 | 0 .. 1400 | 5 | 32 bit-real |
| LW flux - upward for total-sky | W m-2 | 0 .. 850 | 5 | 32 bit-real |
| LW flux - downward for total-sky | W m-2 | 0 .. 700 | 5 | 32 bit-real |
| WN flux - upward for total-sky | W m-2 | 0 .. 370 | 5 | 32 bit-real |
| WN flux - downward for total-sky | W m-2 | 0 .. 370 | 5 | 32 bit-real |
| SW flux adjustment at surface - upward - pristine | W m-2 | -1400 .. 1400 | 1 | 32 bit-real |
| SW flux adjustment at TOA - upward – pristine | W m-2 | -1400 .. 1400 | 1 | 32 bit-real |
| SW flux adjustment at surface - downward - pristine | W m-2 | -1400 .. 1400 | 1 | 32 bit-real |
| LW flux adjustment at surface - upward - pristine | W m-2 | -600 .. 600 | 1 | 32 bit-real |
| LW flux adjustment at surface - downward - pristine | W m-2 | -700 .. 700 | 1 | 32 bit-real |
| LW flux adjustment at TOA - upward – pristine | W m-2 | -700 .. 700 | 1 | 32 bit-real |
| WN flux adjustment at surface - upward - pristine | W m-2 | -50 .. 50 | 1 | 32 bit-real |
| WN flux adjustment at surface - downward - pristine | W m-2 | -50 .. 50 | 1 | 32 bit-real |
| WN flux adjustment at TOA - upward – pristine | W m-2 | -50 .. 50 | 1 | 32 bit-real |
| SW flux adjustment at surface - upward for clear-sky | W m-2 | -1400 .. 1400 | 1 | 32 bit-real |
| SW flux adjustment at TOA - upward for clear-sky | W m-2 | -1400 .. 1400 | 1 | 32 bit-real |
| SW flux adjustment at surface - downward for clear-sky | W m-2 | -1400 .. 1400 | 1 | 32 bit-real |
| LW flux adjustment at surface - upward for clear-sky | W m-2 | -600 .. 600 | 1 | 32 bit-real |
| LW flux adjustment at surface - downward for clear-sky | W m-2 | -700 .. 700 | 1 | 32 bit-real |
| LW flux adjustment at TOA - upward for clear-sky | W m-2 | -700 .. 700 | 1 | 32 bit-real |
| WN flux adjustment at surface - upward for clear-sky | W m-2 | -50 .. 50 | 1 | 32 bit-real |
| WN flux adjustment at surface - downward for clear-sky | W m-2 | -50 .. 50 | 1 | 32 bit-real |
| WN flux adjustment at TOA - upward for clear-sky | W m-2 | -50 .. 50 | 1 | 32 bit-real |
| SW flux adjustment at surface - upward for total-sky | W m-2 | -1400 .. 1400 | 1 | 32 bit-real |
| SW flux adjustment at TOA - upward for total-sky | W m-2 | -1400 .. 1400 | 1 | 32 bit-real |
| SW flux adjustment at surface - downward for total-sky | W m-2 | -1400 .. 1400 | 1 | 32 bit-real |
| LW flux adjustment at surface - upward for total-sky | W m-2 | -600 .. 600 | 1 | 32 bit-real |
| LW flux adjustment at surface - downward for total-sky | W m-2 | -700 .. 700 | 1 | 32 bit-real |
| LW flux adjustment at TOA - upward for total-sky | W m-2 | -700 .. 700 | 1 | 32 bit-real |
| WN flux adjustment at surface - upward for total-sky | W m-2 | -50 .. 50 | 1 | 32 bit-real |
| WN flux adjustment at surface - downward for total-sky | W m-2 | -50 .. 50 | 1 | 32 bit-real |
| WN flux adjustment at TOA - upward for total-sky | W m-2 | -50 .. 50 | 1 | 32 bit-real |
| WN filtered radiance -satellite emulated | W m-2sr-1 | 0 .. 50 | 1 | 32 bit-real |
| WN filtered radiance adjustment-satellite emulated | W m-2sr-1 | 0 .. 50 | 1 | 32 bit-real |
| WN flux - satellite emulated – TOA | W m-2 | 2 .. 50 | 1 | 32 bit-real |
| WN flux adjustment - satellite emulated – TOA | W m-2 | 2 .. 50 | 1 | 32 bit-real |
| Total LW unfiltered radiance - satellite emulated | W m-2sr-1 | 0 .. 200 | 1 | 32 bit-real |
| Total LW unfiltered radiance adjustment - satellite emulated | W m-2sr-1 | 0 .. 200 | 1 | 32 bit-real |
| Total column precipitable water – initial | cm | 0 .. 10 | 1 | 32 bit-real |
| Total column precipitable water – adjustment | cm | -10 .. 10 | 1 | 32 bit-real |
| Upper tropospheric precipitable water – initial | cm | 0 .. 10 | 1 | 32 bit-real |
| Upper tropospheric precipitable water - adjustment | cm | -10 .. 10 | 1 | 32 bit-real |
| Upper tropospheric humidity – initial | N/A | 0.0 .. 100.0 | 1 | 32 bit-real |
| Upper tropospheric humidity – adjustment | N/A | 0.0 .. 100.0 | 1 | 32 bit-real |
| Surface albedo – adjustment | N/A | -1 ..1 | 1 | 32 bit-real |
| Aerosol optical depth – initial | N/A | 0 .. 2 | 1 | 32 bit-real |
| Aerosol optical depth – adjustment | N/A | -2 .. 2 | 1 | 32 bit-real |
| Skin temperature – initial | K | 175 .. 375 | 1 | 32 bit-real |
| Skin temperature – adjustment | K | -50 .. 50 | 1 | 32 bit-real |
| Column ozone – initial | DU | 0 .. 1000 | 1 | 32 bit-real |
| Column ozone source flag | N/A | 0 .. 3 | 1 | 32 bit integer |
| Aerosol constituency flags | N/A | 01000000 .. 18999999 | 7 | 32 bit integer |
| Aerosol and Surface Albedo Sources Flag | N/A | 0 .. 900 | 1 | 32 bit integer |
| Mean visible optical depth- adjustment | N/A | -400 .. 400 | 4 | 32 bit-real |
| Mean cloud fractional area – adjustment | N/A | -1 .. 1 | 4 | 32 bit-real |
| Mean cloud effective temperature - adjustment | K | -50 .. 50 | 4 | 32 bit-real |
| Number of tuning iterations | N/A | 0 .. 1 | 1 | 32 bit integer |
| Constrainment status flag | N/A | 0 .. 600 | 1 | 32 bit integer |
| FuLiou model error code | N/A | 1 .. 3500 | 1 | 32 bit integer |
| TOA downwelling UVB | W m-2 | 0 .. 100 | 1 | 32 bit-real |
| TOA downwelling UVA | W m-2 | 0 .. 100 | 1 | 32 bit-real |
| TOA downwelling PAR | W m-2 | 0 .. 600 | 1 | 32 bit-real |
| Downward UVB at surface for total-sky | W m-2 | 0 .. 100 | 1 | 32 bit-real |
| Direct Diffuse UVB at surface for total-sky | W m-2 | 0 .. 100 | 1 | 32 bit-real |
| Downward UVA at surface for total-sky | W m-2 | 0 .. 100 | 1 | 32 bit-real |
| Direct Diffuse UVA at surface for total-sky | W m-2 | 0 .. 100 | 1 | 32 bit-real |
| MATCH aerosol optical depth | N/A | 0 .. 2 | 1 | 32 bit-real |
| Downward UVB at surface for clear-sky | W m-2 | 0 .. 100 | 1 | 32 bit-real |
| Direct Diffuse UVB at surface for clear-sky | W m-2 | 0 .. 100 | 1 | 32 bit-real |
| Downward UVA at surface for clear-sky | W m-2 | 0 .. 100 | 1 | 32 bit-real |
| Direct Diffuse UVA at surface for clear-sky | W m-2 | 0 .. 100 | 1 | 32 bit-real |
| Broadband surface albedo | N/A | 0 .. 1 | 1 | 32 bit-real |
| Downward UVB at surface for pristine-sky | W m-2 | 0 .. 100 | 1 | 32 bit-real |
| Direct Diffuse UVB at surface for pristine-sky | W m-2 | 0 .. 100 | 1 | 32 bit-real |
| Downward UVA at surface for pristine-sky | W m-2 | 0 .. 100 | 1 | 32 bit-real |
| Direct Diffuse UVA at surface for pristine-sky | W m-2 | 0 .. 100 | 1 | 32 bit-real |
| Snow grain radius using broadband retrieval | um | 0 .. 2000 | 1 | 32 bit-real |
| Downward UVB at surface for cloudy-sky with no aerosol | W m-2 | 0 .. 100 | 1 | 32 bit-real |
| Direct Diffuse UVB at surface for cloudy-sky with no aerosol | W m-2 | 0 .. 100 | 1 | 32 bit-real |
| Downward UVA at surface for cloudy-sky with no aerosol | W m-2 | 0 .. 100 | 1 | 32 bit-real |
| Direct Diffuse UVA at surface for cloudy-sky with no aerosol | W m-2 | 0 .. 100 | 1 | 32 bit-real |
| Upward UVB at surface for total sky | W m-2 | 0 .. 100 | 1 | 32 bit-real |
| Surface total-sky UV-Index | N/A | 0 .. 30 | 1 | 32 bit-real |
| Surface clear-sky UV-Index | N/A | 0 .. 30 | 1 | 32 bit-real |
| Surface pristine-sky UV-Index | N/A | 0 .. 30 | 1 | 32 bit-real |
| Surface cloudy-sky with no aerosol UV-Index | N/A | 0 .. 30 | 1 | 32 bit-real |
| PAR at surface for total-sky | W m-2 | 0 .. 700 | 1 | 32 bit-real |
| Direct Diffuse PAR at surface for total-sky | W m-2 | 0 .. 700 | 1 | 32 bit-real |
| PAR Purv for total sky | W m-2 | 0 .. 700 | 1 | 32 bit-real |
| Direct Diffuse PAR Purv for total sky | W m-2 | 0 .. 700 | 1 | 32 bit-real |
| PAR ChlorA for total sky | W m-2 | 0 .. 700 | 1 | 32 bit-real |
| Direct Diffuse PAR ChlorA for total sky | W m-2 | 0 .. 700 | 1 | 32 bit-real |
| PAR at surface for clear-sky | W m-2 | 0 .. 700 | 1 | 32 bit-real |
| Direct Diffuse PAR at surface for clear-sky | W m-2 | 0 .. 700 | 1 | 32 bit-real |
| PAR at surface for pristine-sky | W m-2 | 0 .. 700 | 1 | 32 bit-real |
| Direct Diffuse PAR at surface for pristine-sky | W m-2 | 0 .. 700 | 1 | 32 bit-real |
| Upwards SW TOA pristine-sky correction | W m-2 | 0 .. 1500 | 1 | 32 bit-real |
| Downwards SW surface pristine-sky correction | W m-2 | 0 .. 1500 | 1 | 32 bit-real |
| SW flux - upward for cloudy-sky with no aerosol | W m-2 | 0 .. 1400 | 2 | 32 bit-real |
| SW flux - downward for cloudy-sky with no aerosol | W m-2 | 0 .. 1400 | 2 | 32 bit-real |
| LW flux - upward for cloudy-sky with no aerosol | W m-2 | 0 .. 850 | 2 | 32 bit-real |
| LW flux - downward for cloudy-sky with no aerosol | W m-2 | 0 .. 700 | 2 | 32 bit-real |
| WN flux - upward for cloudy-sky with no aerosol | W m-2 | 0 .. 370 | 2 | 32 bit-real |
| WN flux - downward for cloudy-sky with no aerosol | W m-2 | 0 .. 370 | 2 | 32 bit-real |
| SW flux adjustment at surface - upward for cloudy-sky with no aerosol | W m-2 | -1400 .. 1400 | 1 | 32 bit-real |
| SW flux adjustment at TOA - upward for cloudy-sky with no aerosol | W m-2 | -1400 .. 1400 | 1 | 32 bit-real |
| SW flux adjustment at surface - downward for cloudy sky with no aerosol | W m-2 | -1400 .. 1400 | 1 | 32 bit-real |
| LW flux adjustment at surface - upward for cloudy sky with no aerosol | W m-2 | -600 .. 600 | 1 | 32 bit-real |
| LW flux adjustment at surface - downward for cloudy-sky with no aerosol | W m-2 | -700 .. 700 | 1 | 32 bit-real |
| LW flux adjustment at TOA - upward for cloudy sky with no aerosol | W m-2 | -700 .. 700 | 1 | 32 bit-real |
| WN flux adjustment at surface - upward for cloudy-sky with no aerosol | W m-2 | -50 .. 50 | 1 | 32 bit-real |
| WN flux adjustment at surface - downward for cloudy-sky with no aerosol | W m-2 | -50 .. 50 | 1 | 32 bit-real |
| WN flux adjustment at TOA - upward for cloudy-sky with no aerosol | W m-2 | -50 .. 50 | 1 | 32 bit-real |
| Spectral interval – SW | TBD | TBD | 15 | 32 bit-real |
| Diffuse SW broadband for total sky | W m-2 | 0 .. 1450 | 1 | 32 bit-real |
| Diffuse SW broadband for clear sky | W m-2 | 0 .. 1450 | 1 | 32 bit-real |
| Diffuse SW broadband for pristine sky | W m-2 | 0 .. 1450 | 1 | 32 bit-real |
| Diffuse SW broadband for cloudy-sky with no aerosol | W m-2 | 0 .. 1450 | 1 | 32 bit-real |
| Direct SW broadband for total sky | W m-2 | 0 .. 1450 | 1 | 32 bit-real |
| Direct SW broadband for clear sky | W m-2 | 0 .. 1450 | 1 | 32 bit-real |
| Direct SW broadband for pristine sky | W m-2 | 0 .. 1450 | 1 | 32 bit-real |
| Direct SW broadband for cloudy-sky with no aerosol | W m-2 | 0 .. 1450 | 1 | 32 bit-real |
| Hour of month | N/A | 0 .. 744 | 1 | 32 bit integer |
| Region number | N/A | 0 .. 64800 | 1 | 32 bit integer |

Sizing Information

| Data Quantity | Size (GB) |
| --- | --- |
| Zonal SYNI Size | 0.23 |
| Monthly TOTAL SYNI Size | 42.40 |

SYNI Revision Record

The product Revision Record contains information pertaining to approved section changes.  The table lists the date the Software Configuration Change Request (SCCR) was approved, the Release and Version Number, the SCCR number, a short description of the revision, and the revised sections.  The authors are listed on the document cover.

| SYNI Revision Record |
| --- |
| SCCR Approval Date | Release/ Version Number | SCCR Number | Description of Revision | Section(s) Affected |
| N/A | R4V1 | N/A | New Data Products Catalog section. (6/24/2008) | All |
|  |  |  | Clarified wording in the first paragraph. (10/02/2009) | Sec. 3.5 |
|  |  |  | The ASDC footer was added to the bottom of the document. (06/06/2013) | All |
| N/A | R5V1 | N/A | Updated Product Version information for Edition2 and Edition3 products. | Sec. 3.5 |
|  |  |  | Eliminated section numbers from the Data Products Catalog. Specifically, in this document, section number 3.5 was removed. (12/18/2013) | All |