Synoptic Radiative Fluxes and Clouds (SYN)

The Synoptic Radiative Fluxes and Clouds (SYN) product contains a day of space and time averaged Clouds and the Earth's Radiant Energy System (CERES) data for a single scanner instrument.  The 1-degree regional flux at the hour of observation from the CERES FSW product and concurrent diurnal data from geostationary satellites are used to estimate the regional flux at 3-hour GMT based intervals.  Also at 3-hour intervals are estimates of the adjusted (tuned) fluxes at the five atmospheric levels as defined by the CERES CRS product for both clear-sky and total-sky scenes, estimates of the average cloud parameters in four cloud height categories, and averaged cloud parameters.

The SYN contains the following apriori and observed input:

Regional data

Cloud category properties for four (low, lower middle, upper middle and high) cloud layers

Observed CERES TOA clear-sky and all-sky fluxes

MODIS based spectral aerosol optical depths

The SYN contains the following constrained (tuned) vertical flux profiles for both clear-sky and total-sky conditions evaluated at the TOA, 70mb, 200mb, 500mb, and surface:

Longwave, Shortwave, and Window channels upward and downward.

The constrained (tuned) and initial (untuned) profiles for the following are included for pristine (clear-sky no-aerosol), clear-sky, total-sky-no-aerosol, and total-sky conditions:

Longwave upward at the surface and TOA.

Longwave downward at the surface.

Shortwave upward at the surface and TOA.

Shortwave downward at the surface.

Window channel upward at the surface and TOA.

Window channel downward at the surface.

The adjustments to the radiative transfer model input parameters between the initial and the constrained (adjusted) passes are also contained on the SYN.  These parameters include:

Surface albedo and skin temperature

Total column precipitable water, upper tropospheric relative humidity, and column ozone

Aerosol optical depth

Cloud optical depth, fractional area, and effective temperature

The SYN contains the direct and diffuse shortwave surface fluxes for total-sky, clear-sky, pristine and actinic conditions. The SYN also contains surface UVA and UVB downwelling and direct diffuse ratios for total-sky, clear-sky, pristine, and total-sky-no-aerosol conditions.

Level:  3

Frequency:  Every 3 Hours

Portion of Atmosphere Covered:  Surface, Internal and TOA

Time Interval Covered:		Portion of Globe Covered:

File:  3 Hours			File:  Entire Global

Record:  3 Hours			Record:  1 CERES region

Product Version:

TRMM:  N/A

Terra:  Beta5, Beta6, Edition2C, Edition2F

Aqua:  Beta6, Edition2B, Edition2C

SYN Metadata

The types of SYN metadata are summarized in Table 1 and contain information which need only be recorded once per hour.  The CERES metadata are listed in Appendix B.  The SYN product-specific metadata parameters are listed in Table 1 and the SYN_Header_Vdata parameters are listed in Table 2.

| SYN Metadata Summary |
| --- |
| HDF Name | Description Table | Records | Number of Fields |
| CERES Baseline Header Metadata | Table B-1 | 1 | 36 |
| CERES_metadata Vdata | Table B-2 | 1 | 14 |
| SYN_Header Vdata | Table 2 | 1 | 25 |

| SYN_Header_Vdata |
| --- |
| Item | Description | Units | Range | Elements | Bytes/Elem |
| SYN-H1 | SYN ID | N/A | 112 .. 200 | 1 | 4 |
| SYN-H2 | Julian Day | N/A | ASCII string | 1 | 28 |
| SYN-H3 | MOA production date and time | N/A | ASCII string | 1 | 24 |
| SYN-H4 | Synoptic SARB Version number | N/A | 1 .. 26 | 1 | 2 |
| SYN-H5 | SYN production date and time | N/A | ASCII string | 1 | 19 |

| List of the Vgroups contained in the Monthly Hourly Averages and Monthly Averages Vgroups in AVG |
| --- |
| Vgroup Number | Vgroup Name | Daily 3-Hourly Averages |
| 1 | Time and Position | See Table 5 |
| 2 | Observed TOA Fluxes | See Table 6 |
| 3 | Cloud Layer - High | See Table 7(a) & Table 7(b) |
| 4 | Cloud Layer - UpperMid | See Table 7(a) & Table 7(b) |
| 5 | Cloud Layer - LowerMid | See Table 7(a) & Table 7(b) |
| 6 | Cloud Layer - Low | See Table 7(a) & Table 7(b) |
| 7 | Stowe-Ignatov Aerosol Optical Depth | See Table 8 |
| 8 | MODIS Aerosol Optical Depth | See Table 9 |
| 9 | Tuned Pristine Fluxes | See Table 10 |
| 10 | Tuned ClearSky Flux Profiles | See Table 11 |
| 11 | Tuned TotalSky-NoAerosol Fluxes | See Table 12 |
| 12 | Tuned TotalSky Flux Profiles | See Table 13 |
| 13 | Untuned Pristine Fluxes | See Table 14 |
| 14 | Untuned ClearSky Fluxes | See Table 15 |
| 15 | Untuned TotalSky-NoAerosol Fluxes | See Table 16 |
| 16 | Untuned TotalSky Fluxes | See Table 17 |
| 17 | Satellite Emulated WN TOA Fluxes | See Table 18 |
| 18 | TOA Flux Error | See Table 19 |
| 19 | Number of Hourboxes | See Table 20 |
| 20 | Constrainment Adjustments | See Table 21 |
| 21 | Surface SW Direct/Diffuse Fluxes | See Table 22 |
| 22 | UVA - UVB Fluxes | See Table 23 |
| 23 | PAR Fluxes | See Table 24 |
| 24 | Pristine-Sky SW MultiStream Correction | See Table 25 |

SYN Science Data

The Scientific Data Sets (SDS) are divided into tables which map to Vgroups of the same name.  All of the SYN science data are organized into the HDF-EOS Grid data type, which is shown in Table 5 below.  All parameter tables contain a list of the gridded parameters, which includes the SDS index, field number, the field name, the data type, the units, the range, and the number of elements within each field.  The 3 dimensions are based on the 1° CERES regional data of 8 3-hourly means of hourly computations for the given daily file.  The first 2 dimensions Nlat and Nlon corresponds to the CERES region index, the next dimension is Ngmt and refers to the time index.  On a few parameters, the last dimension is Nlev and defines the atmospheric profile levels.  Only the means are given, unlike the AVG and ZAVG files.  This ordering is used by the C programming language and most HDF viewers, such as IDL.  In FORTRAN, the dimensions are reversed such that the number of regions becomes the last dimension and the first dimension is the number of parameters in the SDS.

Nlat, Nlon dimensions that define the CERES equal angle 1° latitude by longitude grid

| Dimension | No of indices | Definition |
| --- | --- | --- |
| Nlat | 180 | Index #1 is defined at 89.5°N and #180 is at 89.5°S |
| Nlon | 360 | Index #1 is defined at 179.5°W and #360 is at 179.5°E |

Ngmt dimension that defines the 8 3-hourly GMT time increments.  For the Monthly Ngmt only has one index

| Ngmt index | 3-hourly daily increment |
| --- | --- |
| 1 | 00-03 GMT |
| 2 | 03-06 GMT |
| 3 | 06-09 GMT |
| 4 | 09-12 GMT |
| 5 | 12-15 GMT |
| 6 | 15-18 GMT |
| 7 | 18-21 GMT |
| 8 | 21-24 GMT |

Nlev dimension that define the atmospheric profile levels

| Nlev | Atmospheric level |
| --- | --- |
| 1 | TOA (30 km) |
| 2 | 70mb |
| 3 | 200mb |
| 4 | 500mb |
| 5 | Surface |

| IGBP Surface types used in Table 5. For a geographical distribution of the scene types, see http://snowdog.larc.nasa.gov/surf/pages/sce_type.html |
| --- |
| Nsfc | Surface Type |
| 1 | Evergreen Needle Forest |
| 2 | Evergreen Broadleaf Forest |
| 3 | Deciduous Needle Forest |
| 4 | Deciduous Broadleaf Forest |
| 5 | Mixed Forest |
| 6 | Closed Shrubs |
| 7 | Open Shrubs |
| 8 | Woody Savannas |
| 9 | Savannas |
| 10 | Grassland |
| 11 | Wetlands |
| 12 | Crops |
| 13 | Urban |
| 14 | Crop/Mosaic |
| 15 | Permanent Snow/Ice |
| 16 | Barren Desert |
| 17 | Water |
| 18 | Tundra |
| 19 | Land Snow |
| 20 | Sea Ice |

- Table of Time and Position.  Nsfc dimension is defined in Table 4(d)

| SDS Index | SDS Name | DataType | Units | Range | No of Elements |
| --- | --- | --- | --- | --- | --- |
| SYN-0 | Region number | 32-bit real | N/A | 1 .. 64800 | Nlon*Nlat |
| SYN-1 | Colatitude | 32-bit real | Degree | 0 .. 180 | Nlon*Nlat |
| SYN-2 | Longitude | 32-bit real | Degree | 0 .. 360 | Nlon*Nlat |
| SYN-3 | Surface altitude above sea level | 32-bit real | m | -1000 .. 10000 | Nlon*Nlat *Ngmt |
| SYN-4 | Surface type percent coverage | 32-bit real | Percent | 0 .. 100 | Nlon*Nlat Ngmt*Nsfc |

Observed TOA Fluxes

| SDS Index | SDS Name | DataType | Units | Range | No of Elements |
| --- | --- | --- | --- | --- | --- |
| SYN-5 | SW TOA Total-Sky | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-6 | LW TOA Total-Sky | 32-bit real | W m-2 | 0 .. 500 | Nlon*Nlat*Ngmt |
| SYN-7 | WN TOA Total-Sky | 32-bit real | W m-2 m-1 | 2 .. 50 | Nlon*Nlat*Ngmt |
| SYN-8 | SW TOA Clear-Sky | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-9 | LW TOA Clear-Sky | 32-bit real | W m-2 | 0 .. 500 | Nlon*Nlat*Ngmt |
| SYN-10 | WN TOA Clear-Sky | 32-bit real | W m-2 m-1 | 2 .. 50 | Nlon*Nlat*Ngmt |

| Cloud Properties for Four Cloud Layers |
| --- |
| SDS Name | DataType | Units | Range | No of Elements |
| Area Fraction Percentage | 32-bit real | Percent | 0 .. 100 | Nlon*Nlat*Ngmt |
| Vis. Opt. Depth (linear) | 32-bit real | N/A | 0 .. 400 | Nlon*Nlat*Ngmt |
| Vis. Opt. Depth (log) | 32-bit real | N/A | -6 .. 6 | Nlon*Nlat*Ngmt |
| Infrared Emissivity | 32-bit real | N/A | 0 .. 1 | Nlon*Nlat*Ngmt |
| Liquid Water Path | 32-bit real | g m-2 | 0 .. 10000 | Nlon*Nlat*Ngmt |
| Ice Water Path | 32-bit real | g m-2 | 0 .. 10000 | Nlon*Nlat*Ngmt |
| Top Pressure | 32-bit real | hPa | 0 .. 1100 | Nlon*Nlat*Ngmt |
| Effective Pressure | 32-bit real | hPa | 0 .. 1100 | Nlon*Nlat*Ngmt |
| Effective Temperature | 32-bit real | K | 100 .. 350 | Nlon*Nlat*Ngmt |
| Effective Height | 32-bit real | km | 0 .. 20 | Nlon*Nlat*Ngmt |
| Bottom Pressure | 32-bit real | hPa | 0 .. 1100 | Nlon*Nlat*Ngmt |
| Liquid Particle Radius | 32-bit real | m | 0 .. 40 | Nlon*Nlat*Ngmt |
| Ice Particle Diameter | 32-bit real | m | 0 .. 300 | Nlon*Nlat*Ngmt |
| Particle Phase | 32-bit real | N/A | 1 .. 2 | Nlon*Nlat*Ngmt |
| Vertical Aspect Ratio | 32-bit real | N/A | 0 .. 20 | Nlon*Nlat*Ngmt |

- SDS Index of High, Uppermid, Lowermid, and Low Cloud Properties

| SDS Name | Regional Daily 3- Hourly |
| --- | --- |
| Area Fraction Percentage | 11 | 26 | 41 | 56 |
| Vis. Opt. Depth (linear) | 12 | 27 | 42 | 57 |
| Vis. Opt. Depth (log) | 13 | 28 | 43 | 58 |
| Infrared Emissivity | 14 | 29 | 44 | 59 |
| Liquid Water Path | 15 | 30 | 45 | 60 |
| Ice Water Path | 16 | 31 | 46 | 61 |
| Top Pressure | 17 | 32 | 47 | 62 |
| Effective Pressure | 18 | 33 | 48 | 63 |
| Effective Temperature | 19 | 34 | 49 | 64 |
| Effective Height | 20 | 35 | 50 | 65 |
| Bottom Pressure | 21 | 36 | 51 | 66 |
| Liquid Particle Radius | 22 | 37 | 52 | 67 |
| Ice Particle Diameter | 23 | 38 | 53 | 68 |
| Particle Phase | 24 | 39 | 54 | 69 |
| Vertical Aspect Ratio | 25 | 40 | 55 | 70 |

Color Red	-	High Cloud

Color Green	-	Uppermid Cloud

Color Blue	-	Lowermid Cloud

Color Black	-	Low Cloud

- Stowe-Ignatov Aerosol Optical Depth

| SDS Index | SDS Name | DataType | Units | Range | No of Elements |
| --- | --- | --- | --- | --- | --- |
| SYN-71 | Aerosol visible optical depth - 0.63 m | 32-bit real | N/A | 0 .. 5 | Nlon*Nlat*Ngmt |
| SYN-72 | Aerosol visible optical depth - 1.6 m | 32-bit real | N/A | 0 .. 5 | Nlon*Nlat*Ngmt |

MODIS Aerosol Optical Depth

| SDS Index | SDS Name | DataType | Units | Range | No of Elements |
| --- | --- | --- | --- | --- | --- |
| SYN-73 | Initial Aerosol Optical Depth | 32-bit real | N/A | 0 .. 5 | Nlon*Nlat*Ngmt |
| SYN-74 | Aerosol Opt. Depth at 0.47 m in Land | 32-bit real | N/A | 0 .. 5 | Nlon*Nlat*Ngmt |
| SYN-75 | Aerosol Opt. Depth at 0.55 m in Land | 32-bit real | N/A | 0 .. 5 | Nlon*Nlat*Ngmt |
| SYN-76 | Aerosol Opt. Depth at 0.66 m in Land | 32-bit real | N/A | 0 .. 5 | Nlon*Nlat*Ngmt |
| SYN-77 | Aerosol Opt. Depth at 0.47 m in Ocean | 32-bit real | N/A | 0 .. 5 | Nlon*Nlat*Ngmt |
| SYN-78 | Aerosol Opt. Depth at 0.55 m in Ocean | 32-bit real | N/A | 0 .. 5 | Nlon*Nlat*Ngmt |
| SYN-79 | Aerosol Opt. Depth at 0.66 m in Ocean | 32-bit real | N/A | 0 .. 5 | Nlon*Nlat*Ngmt |
| SYN-80 | Aerosol Opt. Depth at 0.87 m in Ocean | 32-bit real | N/A | 0 .. 5 | Nlon*Nlat*Ngmt |
| SYN-81 | Aerosol Opt. Depth at 1.24 m in Ocean | 32-bit real | N/A | 0 .. 5 | Nlon*Nlat*Ngmt |
| SYN-82 | Aerosol Opt. Depth at 1.64 m in Ocean | 32-bit real | N/A | 0 .. 5 | Nlon*Nlat*Ngmt |
| SYN-83 | Aerosol Opt. Depth at 2.13 m in Ocean | 32-bit real | N/A | 0 .. 5 | Nlon*Nlat*Ngmt |

Tuned Pristine Fluxes

| SDS Index | SDS Name | DataType | Units | Range | No of Elements |
| --- | --- | --- | --- | --- | --- |
| SYN-84 | Tuned Pristine SW Surface Up | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-85 | Tuned Pristine SW Surface Down | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-86 | Tuned Pristine SW TOA Up | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-87 | Tuned Pristine LW Surface Up | 32-bit real | W m-2 | 0 .. 850 | Nlon*Nlat*Ngmt |
| SYN-88 | Tuned Pristine LW Surface Down | 32-bit real | W m-2 | 0 .. 700 | Nlon*Nlat*Ngmt |
| SYN-89 | Tuned Pristine LW TOA Up | 32-bit real | W m-2 | 0 .. 850 | Nlon*Nlat*Ngmt |
| SYN-90 | Tuned Pristine WN Surface Up | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ngmt |
| SYN-91 | Tuned Pristine WN Surface Down | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ngmt |
| SYN-92 | Tuned Pristine WN TOA Up | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ngmt |

Tuned ClearSky Flux Profiles, Table 4(c) defines Nlev

| SDS Index | SDS Name | DataType | Units | Range | No of Elements |
| --- | --- | --- | --- | --- | --- |
| SYN-93 | Tuned Clear-Sky SW Up | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Nlev |
| SYN-94 | Tuned Clear-Sky SW Down | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Nlev |
| SYN-95 | Tuned Clear-Sky LW Up | 32-bit real | W m-2 | 0 .. 850 | Nlon*Nlat*Ngmt*Nlev |
| SYN-96 | Tuned Clear-Sky LW Down | 32-bit real | W m-2 | 0 .. 700 | Nlon*Nlat*Ngmt*Nlev |
| SYN-97 | Tuned Clear-Sky WN Up | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ngmt*Nlev |
| SYN-98 | Tuned Clear-Sky WN Down | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ngmt*Nlev |

Tuned TotalSky-NoAerosol Fluxes

| SDS Index | SDS Name | DataType | Units | Range | No of Elements |
| --- | --- | --- | --- | --- | --- |
| SYN-99 | Tuned Total-Sky-NoAerosol SW Surface Up | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-100 | Tuned Total-Sky-NoAerosol SW Surface Down | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-101 | Tuned Total-Sky-NoAerosol SW TOA Up | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-102 | Tuned Total-Sky-NoAerosol LW Surface Up | 32-bit real | W m-2 | 0 .. 850 | Nlon*Nlat*Ngmt |
| SYN-103 | Tuned Total-Sky-NoAerosol LW Surface Down | 32-bit real | W m-2 | 0 .. 700 | Nlon*Nlat*Ngmt |
| SYN-104 | Tuned Total-Sky-NoAerosol LW TOA Up | 32-bit real | W m-2 | 0 .. 850 | Nlon*Nlat*Ngmt |
| SYN-105 | Tuned Total-Sky-NoAerosol WN Surface Up | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ngmt |
| SYN-106 | Tuned Total-Sky-NoAerosol WN Surface Down | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ngmt |
| SYN-107 | Tuned Total-Sky-NoAerosol WN TOA Up | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ngmt |

Tuned TotalSky Flux Profiles, Table 4(c) defines Nlev

| SDS Index | SDS Name | DataType | Units | Range | No of Elements |
| --- | --- | --- | --- | --- | --- |
| SYN-108 | Tuned Total-Sky SW Up | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Nlev |
| SYN-109 | Tuned Total-Sky SW Down | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt*Nlev |
| SYN-110 | Tuned Total-Sky LW Up | 32-bit real | W m-2 | 0 .. 850 | Nlon*Nlat*Ngmt*Nlev |
| SYN-111 | Tuned Total-Sky LW Down | 32-bit real | W m-2 | 0 .. 700 | Nlon*Nlat*Ngmt*Nlev |
| SYN-112 | Tuned Total-Sky WN Up | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ngmt*Nlev |
| SYN-113 | Tuned Total-Sky WN Down | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ngmt*Nlev |

Untuned Pristine Fluxes

| SDS Index | SDS Name | DataType | Units | Range | No of Elements |
| --- | --- | --- | --- | --- | --- |
| SYN-114 | Untuned Pristine SW Surface Up | 32-bit real | W m-2 | 0 .. 1500 | Nlon*Nlat*Ngmt |
| SYN-115 | Untuned Pristine SW Surface Down | 32-bit real | W m-2 | 0 .. 1500 | Nlon*Nlat*Ngmt |
| SYN-116 | Untuned Pristine SW TOA Up | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-117 | Untuned Pristine LW Surface Up | 32-bit real | W m-2 | 0 .. 850 | Nlon*Nlat*Ngmt |
| SYN-118 | Untuned Pristine LW Surface Down | 32-bit real | W m-2 | 0 .. 700 | Nlon*Nlat*Ngmt |
| SYN-119 | Untuned Pristine LW TOA Up | 32-bit real | W m-2 | 0 .. 850 | Nlon*Nlat*Ngmt |
| SYN-120 | Untuned Pristine WN Surface Up | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ngmt |
| SYN-121 | Untuned Pristine WN Surface Down | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ngmt |
| SYN-122 | Untuned Pristine WN TOA Up | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ngmt |

Untuned ClearSky Fluxes

| SDS Index | SDS Name | DataType | Units | Range | No of Elements |
| --- | --- | --- | --- | --- | --- |
| SYN-123 | Untuned Clear-Sky SW Surface Up | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-124 | Untuned Clear-Sky SW Surface Down | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-125 | Untuned Clear-Sky SW TOA Up | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-126 | Untuned Clear-Sky LW Surface Up | 32-bit real | W m-2 | 0 .. 850 | Nlon*Nlat*Ngmt |
| SYN-127 | Untuned Clear-Sky LW Surface Down | 32-bit real | W m-2 | 0 .. 700 | Nlon*Nlat*Ngmt |
| SYN-128 | Untuned Clear-Sky LW TOA Up | 32-bit real | W m-2 | 0 .. 850 | Nlon*Nlat*Ngmt |
| SYN-129 | Untuned Clear-Sky WN Surface Up | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ngmt |
| SYN-130 | Untuned Clear-Sky WN Surface Down | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ngmt |
| SYN-131 | Untuned Clear-Sky WN TOA Up | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ngmt |

| Untuned TotalSky-NoAerosol Fluxes The names in this table are NOT those used in the actual HDF files at this time. The parameter names in the HDF files do not include “NoAerosol”, making them identical to those in Table 17. Please use the sds numbers noted here for data retrieval. The names will be corrected in a future edition. |
| --- |
| SDS Index | SDS Name | DataType | Units | Range | No of Elements |
| SYN-132 | Untuned Total-Sky-NoAerosol SW Surface Up | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-133 | Untuned Total-Sky-NoAerosol SW Surface Down | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-134 | Untuned Total-Sky-NoAerosol SW TOA Up | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-135 | Untuned Total-Sky-NoAerosol LW Surface Up | 32-bit real | W m-2 | 0 .. 850 | Nlon*Nlat*Ngmt |
| SYN-136 | Untuned Total-Sky-NoAerosol LW Surface Down | 32-bit real | W m-2 | 0 .. 700 | Nlon*Nlat*Ngmt |
| SYN-137 | Untuned Total-Sky-NoAerosol LW TOA Up | 32-bit real | W m-2 | 0 .. 850 | Nlon*Nlat*Ngmt |
| SYN-138 | Untuned Total-Sky-NoAerosol WN Surface Up | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ngmt |
| SYN-139 | Untuned Total-Sky-NoAerosol WN Surface Down | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ngmt |
| SYN-140 | Untuned Total-Sky-NoAerosol WN TOA Up | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ngmt |

Untuned TotalSky Fluxes

Please see the notation in Table 16.

| SDS Index | SDS Name | DataType | Units | Range | No of Elements |
| --- | --- | --- | --- | --- | --- |
| SYN-141 | Untuned Total-Sky SW Surface Up | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-142 | Untuned Total-Sky SW Surface Down | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-143 | Untuned Total-Sky SW TOA Up | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-144 | Untuned Total-Sky LW Surface Up | 32-bit real | W m-2 | 0 .. 850 | Nlon*Nlat*Ngmt |
| SYN-145 | Untuned Total-Sky LW Surface Down | 32-bit real | W m-2 | 0 .. 700 | Nlon*Nlat*Ngmt |
| SYN-146 | Untuned Total-Sky LW TOA Up | 32-bit real | W m-2 | 0 .. 850 | Nlon*Nlat*Ngmt |
| SYN-147 | Untuned Total-Sky WN Surface Up | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ngmt |
| SYN-148 | Untuned Total-Sky WN Surface Down | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ngmt |
| SYN-149 | Untuned Total-Sky WN TOA Up | 32-bit real | W m-2 | 0 .. 370 | Nlon*Nlat*Ngmt |

Satellite Emulated WN TOA Fluxes

| SDS Index | SDS Name | DataType | Units | Range | No of Elements |
| --- | --- | --- | --- | --- | --- |
| SYN-150 | Untuned Satellite Emulated WN TOA | 32-bit real | W m-2 | 50 .. 400 | Nlon*Nlat*Ngmt |
| SYN-151 | Tuned Satellite Emulated WN TOA | 32-bit real | W m-2 | 50 .. 400 | Nlon*Nlat*Ngmt |

TOA Flux Error

| SDS Index | SDS Name | DataType | Units | Range | No of Elements |
| --- | --- | --- | --- | --- | --- |
| SYN-152 | Tuned Minus Observed SW TOA | 32-bit real | W m-2 | -1400 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-153 | Untuned Minus Observed SW TOA | 32-bit real | W m-2 | -1400 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-154 | Tuned Minus Observed LW TOA | 32-bit real | W m-2 | -600 .. 600 | Nlon*Nlat*Ngmt |
| SYN-155 | Untuned Minus Observed LW TOA | 32-bit real | W m-2 | -600 .. 600 | Nlon*Nlat*Ngmt |

Number of Hourboxes

| SDS Index | SDS Name | DataType | Units | Range | No of Elements |
| --- | --- | --- | --- | --- | --- |
| SYN-156 | Number of Observed SW | 32-bit real | N/A | 1 .. 744 | Nlon*Nlat*Ngmt |
| SYN-157 | Number of Untuned SW | 32-bit real | N/A | 1 .. 744 | Nlon*Nlat*Ngmt |
| SYN-158 | Number of Tuned SW | 32-bit real | N/A | 1 .. 744 | Nlon*Nlat*Ngmt |
| SYN-159 | Number of Observed LW | 32-bit real | N/A | 1 .. 744 | Nlon*Nlat*Ngmt |
| SYN-160 | Number of Untuned LW | 32-bit real | N/A | 1 .. 744 | Nlon*Nlat*Ngmt |
| SYN-161 | Number of Tuned LW | 32-bit real | N/A | 1 .. 744 | Nlon*Nlat*Ngmt |

Constrainment Adjustments, Table 4(c) defines Nlev

| SDS Index | SDS Name | DataType | Units | Range | No of Elements |
| --- | --- | --- | --- | --- | --- |
| SYN-162 | Total column precipitable water - initial | 32-bit real | cm | 0 .. 10 | Nlon*Nlat*Ngmt |
| SYN-163 | Total column precipitable water - adjusted | 32-bit real | cm | -10 .. 10 | Nlon*Nlat*Ngmt |
| SYN-164 | Upper tropospheric precipitable water - initial | 32-bit real | cm | 0 .. 10 | Nlon*Nlat*Ngmt |
| SYN-165 | Upper tropospheric precipitable water - adjusted | 32-bit real | cm | 0 .. 10 | Nlon*Nlat*Ngmt |
| SYN-166 | Upper tropospheric humidity - initial | 32-bit real | N/A | 0.0 .. 100.0 | Nlon*Nlat*Ngmt |
| SYN-167 | Upper tropospheric humidity - adjusted | 32-bit real | N/A | 0.0 .. 100.0 | Nlon*Nlat*Ngmt |
| SYN-168 | Corrected initial broadband surface albedo | 32-bit real | N/A | 0.0 .. 1.0 | Nlon*Nlat*Ngmt |
| SYN-169 | Surface albedo - adjusted | 32-bit real | N/A | 0 .. 1 | Nlon*Nlat*Ngmt |
| SYN-170 | Aerosol optical depth - initial | 32-bit real | N/A | 0 .. 5 | Nlon*Nlat*Ngmt |
| SYN-171 | Aerosol optical depth - adjusted | 32-bit real | N/A | 0 .. 5 | Nlon*Nlat*Ngmt |
| SYN-172 | Skin temperature - initial | 32-bit real | K | 175 .. 375 | Nlon*Nlat*Ngmt |
| SYN-173 | Skin temperature - adjusted | 32-bit real | K | 175 .. 375 | Nlon*Nlat*Ngmt |
| SYN-174 | Surface pressure | 32-bit real | hPa | 0 .. 800 | Nlon*Nlat*Ngmt |
| SYN-175 | Column ozone - initial | 32-bit real | du | 0 .. 800 | Nlon*Nlat*Ngmt |
| SYN-176 | Column ozone - Flag source | 32-bit integer | N/A | 0 .. 3 | Nlon*Nlat*Ngmt |
| SYN-177 | Mean visible optical depth- adjusted | 32-bit real | N/A | 0 .. 400 | Nlon*Nlat*Ngmt*Nlev |
| SYN-178 | Mean cloud fractional area - adjusted | 32-bit real | % | 0 .. 1 | Nlon*Nlat*Ngmt*Nlev |
| SYN-179 | Mean cloud effective temperature - adjusted | 32-bit real | K | 175 .. 375 | Nlon*Nlat*Ngmt*Nlev |

Surface SW Direct/Diffuse Fluxes

| SDS Index | SDS Name | DataType | Units | Range | No of Elements |
| --- | --- | --- | --- | --- | --- |
| SYN-180 | Total-Sky SW flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-181 | Clear-sky SW flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-182 | Pristine-Sky SW flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-183 | Actinic-Sky SW flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-184 | Total-Sky SW flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-185 | Clear-sky SW flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-186 | Pristine-Sky SW flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-187 | Actinic-Sky SW flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |

| UVA – UVB Fluxes |
| --- |
| SDS Index | SDS Name | DataType | Units | Range | No of Elements |
| SYN-188 | TOA Downwelling UVB Flux | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-189 | TOA Downwelling UVA Flux | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-190 | Pristine UVB Surface flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-191 | Pristine UVB Surface flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-192 | Pristine UVA Surface flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-193 | Pristine UVA Surface flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-194 | Clear-Sky UVB Surface flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-195 | Clear-Sky UVB Surface flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-196 | Clear-Sky UVA Surface flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-197 | Clear-Sky UVA Surface flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-198 | Total-Sky-NoAerosol UVB Surface flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-199 | Total-Sky-NoAerosol UVB Surface flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-200 | Total-Sky-NoAerosol UVA Surface flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-201 | Total-Sky-NoAerosol UVA Surface flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-202 | Total-Sky UVB Surface flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-203 | Total-Sky UVB Surface flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-204 | Total-Sky UVA Surface flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-205 | Total-Sky UVA Surface flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-206 | Total-Sky Surface UV Index | 32-bit real | N/A | 0 .. 30 | Nlon*Nlat*Ngmt |
| SYN-207 | Clear-Sky Surface UV Index | 32-bit real | N/A | 0 .. 30 | Nlon*Nlat*Ngmt |
| SYN-208 | Pristine Surface UV Index | 32-bit real | N/A | 0 .. 30 | Nlon*Nlat*Ngmt |
| SYN-209 | Total-Sky-NoAerosol Surface UV Index | 32-bit real | N/A | 0 .. 30 | Nlon*Nlat*Ngmt |
| SYN-210 | Total-Sky UVB Surface Up | 32-bit real | W m-2 | 0 .. 5 | Nlon*Nlat*Ngmt |
| SYN-211 | Snow Grain Size | 32-bit real | m | 50 .. 2000 | Nlon*Nlat*Ngmt |
| SYN-212 | Match Total Aerosol Optical Depth at 0.55 m | 32-bit real | N/A | 0 .. 10 | Nlon*Nlat*Ngmt |

| PAR Fluxes |
| --- |
| SDS Index | SDS Name | DataType | Units | Range | No of Elements |
| SYN-213 | TOA Downwelling PAR Flux | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-214 | Total-Sky PAR Surface flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-215 | Total-Sky PAR Surface flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-216 | Total-Sky PAR PURV Surface flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-217 | Total-Sky PAR PURV Surface flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-218 | Total-Sky PAR ChlorA Surface flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-219 | Total-Sky PAR ChlorA Surface flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-220 | Clear-Sky PAR Surface flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-221 | Clear-Sky PAR Surface Surface flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-222 | Pristine PAR Surface flux - Direct | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |
| SYN-223 | Pristine PAR Surface flux - Diffuse | 32-bit real | W m-2 | 0 .. 1400 | Nlon*Nlat*Ngmt |

Pristine-Sky SW MultiStream Correction

| SDS Index | SDS Name | DataType | Units | Range | No of Elements |
| --- | --- | --- | --- | --- | --- |
| SYN-224 | SW TOA Flux - Up - Pristine-Sky - Corrected | 32-bit real | W m-2 | 0 .. 1000 | Nlon*Nlat*Ngmt |
| SYN-225 | SW Surface Flux - Down- Pristine-Sky - Corrected | 32-bit real | W m-2 | 0 .. 1000 | Nlon*Nlat*Ngmt |

Sizing Information

| Data Quantity | Size (MB) |
| --- | --- |
| Daily TOTAL SYN Size | 596 |
| Monthly TOTAL SYN Size | 18476 |

SYN Revision Record

The product Revision Record contains information pertaining to approved section changes.  The table lists the date the Software Configuration Change Request (SCCR) was approved, the Release and Version Number, the SCCR number, a short description of the revision, and the revised sections.  The authors are listed on the document cover.

| SYN Revision Record |
| --- |
| SCCR Approval Date | Release/ Version Number | SCCR Number | Description of Revision | Section(s) Affected |
| N/A | R3V1 | N/A | Updated format to comply with standards. | All |
| 11/15/06 | R3V2 | 639 | Updated to change all tables and added the SDS Index tables. | All |
|  |  |  | The EOSDIS Product Code line was removed from the document. (6/17/2008) | Sec. 2.9 |
| 02/08/08 | R3V3 | 667 | Updated to add three parameters and changed the SDS Index tables. (08/20/2008) | Tables 2.9-22, 2.9-23, 2.9-24 |
|  |  |  | Section numbering was changed due to insertion of the ISCCP D2-like DPC. (09/23/2008) | All |
| 11/12/08 | R5V1 | 689 | Updated “Product Version” category. | Sec. 2.10 |
|  |  |  | Removed Beta3 from “Product Version” category. (11/17/2008) | Sec. 2.10 |
|  |  |  | Corrected the Terra and Aqua product versions. (12/08/2008) | Sec. 2.10 |
|  |  |  | Corrected the Terra and Aqua product versions. (12/16/2008) | Sec. 2.10 |
|  |  |  | Reorganized tables for clarity. (02/07/2009) | All |
|  |  |  | Some links were not working. They have now been modified. (12/09/2010) | All |
|  |  |  | Added the word “NoAerosol” in the SDS Name column and a note in the title. (03/29/2012) | Table 2.10-16 |
|  |  |  | Added a note in the title. | Table 2.10-17 |
|  |  |  | The ASDC footer was added to the bottom of the document. (06/05/2013) | All |
|  |  |  | Changed Section numbering 2.10 to 2.11. (10/21/2013) | All |
|  |  |  | Eliminated section numbers from the Data Products Catalog. Specifically, in this document, section number 2.11 was removed. (12/10/2013) | All |
| 11/12/08 (Cont'd) | R5V1 | 689 | Updated some links to refer to the .pdf file instead of the .doc file. (06/20/2014) | All |