TSI Product

The TSI Zonal Data product is generated monthly by the TISA subsystem (7.1). It contains data for every hour of the month for each 1-degree region; there are 180 zonal files each contains nested regions depending on the colatitude.  The TSI data are the CERES Internal Data Product used to provide hourly TOA fluxes and cloud informations to Subsystem 8.1. The TSI contains the following data as determined on a regional basis.

Julian time and region location with sun geometry, view zenith angles and relative azimuth angles.

Radiative fluxes for both Clear-sky and Total-sky at TOA fluxes and land and ocean aerosol optical depths.

The TOA flux data flags.

Cloud category properties for four cloud layers.

Surface Emissivities and Skin Temperature.

Overlap data for eleven cloud conditions.

Level: 3			Portion of Globe Covered

Frequency: 1/Month			File: 180 Zonal

Configuration Code: 000000 and greater		Record: 1-Deg Equal-angle Regions

Time Interval Covered

File: Monthly

Record: Hour

| TSI Data Record |
| --- |
| Description | Element Number | Units | Range | Elements/ Record | Data Type | Bits/ Elem |
| Julian Hour | 1 | N/A | 0 .. 235959 | 1 | 32 bit real | 32 |
| Region Number | 2 | N/A | 1 .. 64800 | 1 | 32 bit integer | 32 |
| Hour box number | 3 | N/A | 1 .. 744 | 1 | 32 bit integer | 32 |
| Surface altitude | 4 | m | 1000 .. 100000 | 1 | 32 bit real | 32 |
| Cosine – Solar Zenith Angle | 5 | deg | -1.0 .. 1.0 | 1 | 32 bit real | 32 |
| Surface percent coverage | 6 | N/A | 0 .. 100 | 20 | 32 bit real | 640 |
| Spacecraft Zenith Angle | 7 | deg | 0 .. 180 | 1 | 32 bit real | 32 |
| Geo-stationary satellite ID | 8 | N/A | N/A | 1 | 32 bit integer | 32 |
| Relative Azimuth Angle | 9 | deg | 0 .. 180 | 1 | 32 bit real | 32 |
| Aerosol Optical Depth at 0.63um in clr | 10 | N/A | 0 .. 5.0 | 1 | 32 bit real | 32 |
| Aerosol Optical Depth at 1.60 um in clr | 11 | N/A | 0 .. 5.0 | 1 | 32 bit real | 32 |
| Infrared Radiance | 12 | W m-2 sr-1 m-1 | 1000.0 .. 1000.0 | 1 | 32 bit real | 32 |
| Imager Radiance Field of View | 13 | W m-2 sr-1 μm-1 | 1000.0 .. 1000.0 | 1 | 32 bit real | 32 |
| Data flag | 14 | N/A | 1111 .. 3333 | 1 | 32 bit real | 32 |
| Total SW mean | 15 | W m-2 | 0 .. 1400 | 1 | 32 bit real | 32 |
| Total SW std | 16 | N/A | N/A | 1 | 32 bit real | 32 |
| Total LW mean | 17 | W m-2 | 0 .. 500 | 1 | 32 bit real | 32 |
| Total LW std | 18 | N/A | N/A | 1 | 32 bit real | 32 |
| Total albedo mean | 19 | W m-2 | 0 .. 1 | 1 | 32 bit real | 32 |
| Total albedo std | 20 | N/A | N/A | 1 | 32 bit real | 32 |
| Total WN mean | 21 | W m-2 | 0 .. 50 | 1 | 32 bit real | 32 |
| Total WN std | 22 | N/A | N/A | 1 | 32 bit real | 32 |
| Clear SW mean | 23 | W m-2 | 0 .. 1400 | 1 | 32 bit real | 32 |
| Clear SW std | 24 | N/A | N/A | 1 | 32 bit real | 32 |
| Clear LW mean | 25 | W m-2 | 0 .. 500 | 1 | 32 bit real | 32 |
| Clear LW std | 26 | N/A | N/A | 1 | 32 bit real | 32 |
| Clear albedo mean | 27 | W m-2 | 0 .. 1 | 1 | 32 bit real | 32 |
| Clear albedo std | 28 | N/A | N/A | 1 | 32 bit real | 32 |
| Clear WN mean | 29 | W m-2 | 0 .. 50 | 1 | 32 bit real | 32 |
| Clear WN std | 30 | N/A | N/A | 1 | 32 bit real | 32 |
| Cloud area fraction | 31 | Percent | 0 .. 100 | 4 | 32 bit real | 128 |
| Cloud optical depth – linear - mean | 32 | N/A | 0 .. 400 | 4 | 32 bit real | 128 |
| Cloud optical depth – linear - std | 33 | N/A | N/A | 4 | 32 bit real | 128 |
| Cloud optical depth – log – mean | 34 | N/A | -6 .. 6 | 4 | 32 bit real | 128 |
| Cloud optical depth – log – std | 35 | N/A | N/A | 4 | 32 bit real | 128 |
| Cloud infrared emissivity – mean | 36 | N/A | 0 .. 2 | 4 | 32 bit real | 128 |
| Cloud infrared emissivity – std | 37 | N/A | N/A | 4 | 32 bit real | 128 |
| Cloud liquid water path – mean | 38 | g m-2 | 0 .. 10000 | 4 | 32 bit real | 128 |
| Cloud liquid water path – std | 39 | N/A | N/A | 4 | 32 bit real | 128 |
| Cloud ice water path – mean | 40 | g m-2 | 0 .. 10000 | 4 | 32 bit real | 128 |
| Cloud ice water path – std | 41 | N/A | N/A | 4 | 32 bit real | 128 |
| Cloud top pressure – mean | 42 | hPA | 0 .. 1100 | 4 | 32 bit real | 128 |
| Cloud top pressure – std | 43 | N/A | N/A | 4 | 32 bit real | 128 |
| Cloud effective pressure - mean | 44 | hPA | 0 .. 1100 | 4 | 32 bit real | 128 |
| Cloud effective pressure - std | 45 | N/A | N/A | 4 | 32 bit real | 128 |
| Cloud effective temperature – mean | 46 | K | 100 .. 350 | 4 | 32 bit real | 128 |
| Cloud effective temperature - std | 47 | N/A | N/A | 4 | 32 bit real | 128 |
| Cloud effective height - mean | 48 | km | 0 .. 20 | 4 | 32 bit real | 128 |
| Cloud effective height - std | 49 | N/A | N/A | 4 | 32 bit real | 128 |
| Cloud bottom pressure - mean | 50 | hPA | 0 .. 20 | 4 | 32 bit real | 128 |
| Cloud bottom pressure - std | 51 | N/A | N/A | 4 | 32 bit real | 128 |
| Cloud liquid particle size - mean | 52 | m | 0 .. 12 | 4 | 32 bit real | 128 |
| Cloud liquid particle size - std | 53 | N/A | N/A | 4 | 32 bit real | 128 |
| Cloud ice particle size - mean | 54 | m | 0 .. 300 | 4 | 32 bit real | 128 |
| Cloud ice particle size -std | 55 | N/A | N/A | 4 | 32 bit real | 128 |
| Cloud phase - mean | 56 | N/A | 1.0 .. 2.0 | 4 | 32 bit real | 128 |
| Cloud phase - std | 57 | N/A | N/A | 4 | 32 bit real | 128 |
| Cloud aspect ratio - mean | 58 | N/A | 1.0 .. 20.0 | 4 | 32 bit real | 128 |
| Cloud aspect ratio - std | 59 | N/A | N/A | 4 | 32 bit real | 128 |
| Area fraction overlap | 60 | N/A | 0 .. 1.0 | 4 | 32 bit real | 128 |
| LW surface emissivity | 61 | N/A | 0 .. 1 | 1 | 32 bit real | 32 |
| WN surface emissivity | 62 | N/A | 0 .. 1 | 1 | 32 bit real | 32 |
| Surface skin temperature | 63 | K | 175 .. 375 | 1 | 32 bit real | 32 |
| Initial aerosol optical depth | 64 | N/A | 0.0 .. 5.0 | 1 | 32 bit real | 32 |
| Aerosol constituency ratio | 65 | N/A | 0.0 .. 100.0 | 7 | 32 bit real | 224 |
| Aerosol optical depth - 0.47 m - land | 66 | N/A | 0.0 .. 5.0 | 1 | 32 bit real | 32 |
| Aerosol optical depth - 0.55 m - land | 67 | N/A | 0.0 .. 5.0 | 1 | 32 bit real | 32 |
| Aerosol optical depth - 0.66 m - land | 68 | N/A | 0.0 .. 5.0 | 1 | 32 bit real | 32 |
| Aerosol optical depth - 0.47 m - ocean | 69 | N/A | 0.0 .. 5.0 | 1 | 32 bit real | 32 |
| Aerosol optical depth - 0.55 m - ocean | 70 | N/A | 0.0 .. 5.0 | 1 | 32 bit real | 32 |
| Aerosol optical depth - 0.66 m - ocean | 71 | N/A | 0.0 .. 5.0 | 1 | 32 bit real | 32 |
| Aerosol optical depth - 0.47 m - ocean | 72 | N/A | 0.0 .. 5.0 | 1 | 32 bit real | 32 |
| Aerosol optical depth - 0.55 m - ocean | 73 | N/A | 0.0 .. 5.0 | 1 | 32 bit real | 32 |
| Aerosol optical depth - 0.66 m - ocean | 74 | N/A | 0.0 .. 5.0 | 1 | 32 bit real | 32 |
| Aerosol optical depth - 0.87 m - ocean | 75 | N/A | 0.0 .. 5.0 | 1 | 32 bit real | 32 |
| Aerosol optical depth - 1.24 m - ocean | 76 | N/A | 0.0 .. 5.0 | 1 | 32 bit real | 32 |
| Aerosol optical depth - 1.64 m - ocean | 77 | N/A | 0.0 .. 5.0 | 1 | 32 bit real | 32 |
| Aerosol optical depth - 2.13 m - ocean | 78 | N/A | 0.0 .. 5.0 | 1 | 32 bit real | 32 |

Total Data Bits/Record:	5408

Total Data Bytes/Record:	676

Max. Total Records/File:	267,840

Total Data Bits/File:	1,448,478,720

Total Data Bytes/File:	181,059,840

Total MBytes/File:	181.06

TSI Revision Record

The product Revision Record contains information pertaining to approved section changes.  The table lists the date the Software Configuration Change Request (SCCR) was approved, the Release and Version Number, the SCCR number, a short description of the revision, and the revised sections.  The authors are listed on the document cover.

| TSI Revision Record |
| --- |
| SCCR Approval Date | Release/ Version Number | SCCR Number | Description of Revision | Section(s) Affected |
| N/A | R4V1 | N/A | New Data Products Catalog section. (6/24/2008) | All |
|  |  |  | The ASDC footer was added to the bottom of the document. (06/06/2013) | All |
|  |  |  | Eliminated section numbers from the Data Products Catalog. Specifically, in this document, section number 3.6 was removed. (12/18/2013) | All |
|  |  |  | Updated document to change “mm” to “m.” (09/12/2019) | Table 1 |