VIIRS Cloud Imager Data (VIIRS CID)

The VIIRS instrument on the NPP spacecraft has imagery, moderate, and day-night sensors.  The instrument data are received by the IDPS.  The geolocation, geometry, and Level-1 radiances are written to separate files as individual SDRs.  The SDS Land PEATE aggregates the files into approximately five-minute granules.  These aggregated granules are subset and sub-sampled by the CERES NPP VIIRS Sub-sample Processor.  The processor sub-samples three VIIRS SDRs and combines them into one data file called NPP_VIMD.  Because of the data name, many documents refer to the data as VIMD.  Traditionally, CERES has called subsetted MODIS data MODIS CID; therefore in this document CERES will be referring to the subsetted VIIRS data, VIMD, as VIIRS CID.

The CID_VIIRS file contains VIIRS Cloud Imager Data (the calibrated radiances and geolocation data).  The sizes listed in the following data description reflect the estimated number of scan line records (1536) for moderate resolution in about 5 minutes of data.  The file is written in Hierarchical Data Format (HDF) and is composed of Scientific Data Sets (SDS).

The VIIRS Level-1B HDF Structure Summary, Table 1, lists the types and names of HDF structures contained in the Level-1B product along with the names of the structures.  A complete listing of parameters for the Level 1B data product can be found in Table 2 through Table 4.

It is assumed that only Earth-viewing radiances and uncertainties and any information needed to interpret these values from the Level-1B product will be sent to the LaRC ASDC.  The channels currently requested by the CERES Science Team are

| Channels | Micron | Resolution (km) | Channels | Micron | Resolution (km) |
| --- | --- | --- | --- | --- | --- |
| I1 | 0.64 | 0.375 & 0.750 | M9 | 1.378 | 0.750 |
| I3 | 1.61 | 0.375 & 0.750 | M10 | 1.61 | 0.750 |
| I4 | 3.74 | 0.375 & 0.750 | M11 | 2.25 | 0.750 |
| I5 | 11.45 | 0.375 & 0.750 | M12 | 3.70 | 0.750 |
| M3 | 0.488 | 0.750 | M14 | 8.55 | 0.750 |
| M4 | 0.555 | 0.750 | M15 | 10.763 | 0.750 |
| M5 | 0.672 | 0.750 | M16 | 12.013 | 0.750 |
| M7 | 0.865 | 0.750 | DNB | 0.7 | 0.750 |
| M8 | 1.24 | 0.750 |  |  |  |

Level: 1B			Portion of Globe Covered

Type:  Ancillary			File:  Satellite Swath

Frequency:  1 per ~5.0-Min		Record:  .375 – 0.750-km by .375 – 0.750-km

Time Interval Covered		Portion of Atmosphere Covered

File:  ~5.0-Min			File:  Satellite Altitude

Record:  Instantaneous

| VIIRS Level-1B HDF Structure Summary |
| --- |
| HDF Name | HDF Structure Type | Num Records | Table Number | Size (bytes) |
| VIIRS Global Attribute | HDF annotations | 3 |  | 396,871 |
| VIIRS Level 1-B Imagery SDS | SDSs | 4…3200 | Table 2 |  |
| VIIRS Level 1-B Moderate SDS | SDSs | 1…1600 | Table 3 | 409,974,879 |
| VIIRS Level 1-B Day/Night SDS | SDSs | 4064 | Table 4 |  |
| Total VIIRS Level-1B Bytes/File (HDF compressed): |  |  |  | 410,371,750 |

| VIIRS Level-1B Imagery Science Data Sets |
| --- |
| SDS Name | Description | Rank | Dimensions | Data Type | Unit | Range |
| Radiance_Img_I1_Avg | Radiances for I1 in moderate resolution | 2 | (1536,1600) | Unsigned 2-byte integer | W m-2sr-1 m-1 | TBD |
| Radiance_Img_I3_Avg | Radiances for I3 in moderate resolution | 2 | (1536,1600) | Unsigned 2-byte integer | W m-2sr-1 m-1 | TBD |
| Radiance_Img_I4_Avg | Radiances for I4 in moderate resolution | 2 | (1536,1600) | Unsigned 2-byte integer | W m-2sr-1 m-1 | TBD |
| Radiance_Img_I5_Avg | Radiances for I5 in moderate resolution | 2 | (1536,1600) | Unsigned 2-byte integer | W m-2sr-1 m-1 | TBD |
| Reflectance_Img_I1_Sub | Reflectance for I1 in imagery resolution | 2 | (3072,3200) | Unsigned 2-byte integer | N/A | TBD |
| Reflectance_Img_I1_Avg | Reflectance for I1 in moderate resolution | 2 | (1536,1600) | Unsigned 2-byte integer | N/A | TBD |
| Reflectance_Img_I3 Sub | Reflectance for I3 in imagery resolution | 2 | (3072,3200) | Unsigned 2-byte integer | N/A | TBD |
| Reflectance_Img_I3_Avg | Reflectance for I3 in moderate resolution | 2 | (1536,1600) | Unsigned 2-byte integer | N/A | TBD |
| BrightTemp_Img_I4_Sub | Brightness temperature for I4 at imagery resolution | 2 | (3072,3200) | Unsigned 2-byte integer | (K | TBD |
| BrightTemp_Img_I4_Avg | Brightness temperature for I4 at moderate resolution | 2 | (1536,1600) | Unsigned 2-byte integer | (K | TBD |
| BrightTemp_Img_I5_Sub | Brightness temperature for I5 at imagery resolution | 2 | (3072,3200) | Unsigned 2-byte integer | (K | TBD |
| BrightTemp_Img_I5_Avg | Brightness temperature for I5 at moderate resolution | 2 | (1536,1600) | Unsigned 2-byte integer | (K | TBD |
| QF_VIIRS_I1_SDR_1_Sub | Quality control flag for I1 | 2 | (3072,3200) | Unsigned 1-byte integer | N/A | TBD |
| QF_VIIRS_I3_SDR_1_Sub | Quality control flag for I3 | 2 | (3072,3200) | Unsigned 1-byte integer | N/A | TBD |
| QF_VIIRS_I4_SDR_1_Sub | Quality control flag for I4 | 2 | (3072,3200) | Unsigned 1-byte integer | N/A | TBD |
| QF_VIIRS_I5_SDR_1_Sub | Quality control flag for I5 | 2 | (3072,3200) | Unsigned 1-byte integer | N/A | TBD |

| VIIRS Level-1B Moderate Science Data Sets |
| --- |
| SDS Name | Description | Rank | Dimensions | Data Type | Unit | Range |
| scanStartTime_V | Time at the beginning of the scan | 1 | (192) | 8-byte float | Sec | TBD |
| scanMidTime_V | Time at the mid of the scan | 1 | (192) | 8-byte float | Sec | TBD |
| NumScans | Number of scan lines | 1 | (1) | 4-byte integer | N/A | TBD |
| Latitude_Sub | Geodetic latitude | 2 | (1536,1600) | 4-byte float | Deg | -90 to 90 |
| Longitude_Sub | Geodetic longitude | 2 | (1536,1600) | 4-byte float | Deg | -180 to 180 |
| TerrainHgt_Mod_Sub | Terrain height | 2 | (1536,1600) | 4-byte float | TBD | TBD |
| SatelliteRange_Sub | Sensor location | 2 | (1536,1600) | 4-byte float | TBD | TBD |
| SenAziAng_Mod_Sub | Sensor azimuth angle | 2 | (1536,1600) | 4-byte float | Deg | TBD |
| SenZenAng_Mod_Sub | Sensor zenith angle | 2 | (1536,1600) | 4-byte float | Deg | TBD |
| SolAziAng_Mod_Sub | Solar azimuth angle | 2 | (1536,1600) | 4-byte float | Deg | TBD |
| SolZenAng_Mod_Sub | Solar zenith angle | 2 | (1536,1600) | 4-byte float | Deg | TBD |
| Radiance_Mod_M10_Sub | Radiances for M10 in moderate resolution | 2 | (1536,1600) | Unsigned 2-byte integer | W m-2sr-1 m | TBD |
| Radiance_Mod_M11_Sub | Radiances for M11 in moderate resolution | 2 | (1536,1600) | Unsigned 2-byte integer | W m-2sr-1 m | TBD |
| Radiance_Mod_M12_Sub | Radiances for M12 in moderate resolution | 2 | (1536,1600) | Unsigned 2-byte integer | W m-2sr-1 m | TBD |
| Radiance_Mod_M14_Sub | Radiances for M14 in moderate resolution | 2 | (1536,1600) | Unsigned 2-byte integer | W m-2sr-1 m | TBD |
| Radiance_Mod_M15_Sub | Radiances for M15 in moderate resolution | 2 | (1536,1600) | Unsigned 2-byte integer | W m-2sr-1 m | TBD |
| Radiance_Mod_M16_Sub | Radiances for M16 in moderate resolution | 2 | (1536,1600) | Unsigned 2-byte integer | W m-2sr-1 m | TBD |
| Radiance_Mod_M3_Sub | Radiances for M3 in moderate resolution | 2 | (1536,1600) | 4-byte float | W m-2sr-1 m | TBD |
| Radiance_Mod_M4_Sub | Radiances for M4 in moderate resolution | 2 | (1536,1600) | 4-byte float | W m-2sr-1 m | TBD |
| Radiance_Mod_M5_Sub | Radiances for M5 in moderate resolution | 2 | (1536,1600) | 4-byte float | W m-2sr-1 m | TBD |
| Radiance_Mod_M7_Sub | Radiances for M7 in moderate resolution | 2 | (1536,1600) | 4-byte float | W m-2sr-1 m | TBD |
| Reflectance_Mod_M10_Sub | Reflectance for M10 in moderate resolution | 2 | (1536,1600) | Unsigned 2-byte integer | N/A | TBD |
| Reflectance_Mod_M11_Sub | Reflectance for M11 in moderate resolution | 2 | (1536,1600) | Unsigned 2-byte integer | N/A | TBD |
| Reflectance_Mod_M3_Sub | Reflectance for M3 in moderate resolution | 2 | (1536,1600) | Unsigned 2-byte integer | N/A | TBD |
| Reflectance_Mod_M4_Sub | Reflectance for M4 in moderate resolution | 2 | (1536,1600) | Unsigned 2-byte integer | N/A | TBD |
| Reflectance_Mod_M5_Sub | Reflectance for M5 in moderate resolution | 2 | (1536,1600) | Unsigned 2-byte integer | N/A | TBD |
| Reflectance_Mod_M7_Sub | Reflectance for M7 in moderate resolution | 2 | (1536,1600) | Unsigned 2-byte integer | N/A | TBD |
| Reflectance_Mod_M8_Sub | Reflectance for M8 in moderate resolution | 2 | (1536,1600) | Unsigned 2-byte integer | N/A | TBD |
| Reflectance_Mod_M9_Sub | Reflectance for M9 in moderate resolution | 2 | (1536,1600) | Unsigned 2-byte integer | N/A | TBD |
| BrightTemp_Mod_M12_Sub | Brightness temperature for M12 at moderate resolution | 2 | (1536,1600) | Unsigned 2-byte integer | (K | TBD |
| BrightTemp_Mod_M14_Sub | Brightness temperature for M14 at moderate resolution | 2 | (1536,1600) | Unsigned 2-byte integer | (K | TBD |
| BrightTemp_Mod_M15_Sub | Brightness temperature for M15 at moderate resolution | 2 | (1536,1600) | Unsigned 2-byte integer | (K | TBD |
| BrightTemp_Mod_M16_Sub | Brightness temperature for M16 at moderate resolution | 2 | (1536,1600) | Unsigned 2-byte integer | (K | TBD |
| QF_Mod_Geo_2_Sub | Quality control flag for geolocation | 2 | (1536,1600) | Unsigned 1-byte integer | N/A | TBD |
| QF_VIIRS_M10_SDR_1_Sub | Quality control flag for M10 | 2 | (1536,1600) | Unsigned 1-byte integer | N/A | TBD |
| QF_VIIRS_M11_SDR_1_Sub | Quality control flag for M11 | 2 | (1536,1600) | Unsigned 1-byte integer | N/A | TBD |
| QF_VIIRS_M12_SDR_1_Sub | Quality control flag for M12 | 2 | (1536,1600) | Unsigned 1-byte integer | N/A | TBD |
| QF_VIIRS_M14_SDR_1_Sub | Quality control flag for M14 | 2 | (1536,1600) | Unsigned 1-byte integer | N/A | TBD |
| QF_VIIRS_M15_SDR_1_Sub | Quality control flag for M15 | 2 | (1536,1600) | Unsigned 1-byte integer | N/A | TBD |
| QF_VIIRS_M16_SDR_1_Sub | Quality control flag for M16 | 2 | (1536,1600) | Unsigned 1-byte integer | N/A | TBD |
| QF_VIIRS_M3_SDR_1_Sub | Quality control flag for M3 | 2 | (1536,1600) | Unsigned 1-byte integer | N/A | TBD |
| QF_VIIRS_M4_SDR_1_Sub | Quality control flag for M4 | 2 | (1536,1600) | Unsigned 1-byte integer | N/A | TBD |
| QF_VIIRS_M5_SDR_1_Sub | Quality control flag for M5 | 2 | (1536,1600) | Unsigned 1-byte integer | N/A | TBD |
| QF_VIIRS_M7_SDR_1_Sub | Quality control flag for M7 | 2 | (1536,1600) | Unsigned 1-byte integer | N/A | TBD |
| QF_VIIRS_M8_SDR_1_Sub | Quality control flag for M8 | 2 | (1536,1600) | Unsigned 1-byte integer | N/A | TBD |
| QF_VIIRS_M9_SDR_1_Sub | Quality control flag for M9 | 2 | (1536,1600) | Unsigned 1-byte integer | N/A | TBD |

| VIIRS Level-1B DNB Science Data Sets |
| --- |
| SDS Name | Description | Rank | Dimensions | Data Type | Unit | Range |
| Latitude_Dnb_Sub | Geodetic latitude | 2 | (1536,2032) | 4-byte float | Deg | -90 to 90 |
| Longitude_Dnb_Sub | Geodetic longitude | 2 | (1536,2032) | 4-byte float | Deg | -180 to 180 |
| TerrainHgt_Dnb_Sub | Terrain height | 2 | (1536,2032) | 4-byte float | TBD | TBD |
| MoonAziAng_Dnb_Sub | Lunar azimuth angle | 2 | (1536,2032) | 4-byte float | Deg | TBD |
| MoonZenAng_Dnb_Sub | Lunar zenith angle | 2 | (1536,2032) | 4-byte float | Deg | TBD |
| SenAziAng_Dnb_Sub | Sensor azimuth angle | 2 | (1536,2032) | 4-byte float | Deg | TBD |
| SenZenAng_Dnb_Sub | Sensor zenith angle | 2 | (1536,2032) | 4-byte float | Deg | TBD |
| SolAziAng_Dnb_Sub | Solar azimuth angle | 2 | (1536,2032) | 4-byte float | Deg | TBD |
| SolZenAng_Dnb_Sub | Solar senith angle | 2 | (1536,2032) | 4-byte float | Deg | TBD |
| Radiance_Dnb_Sub | Radiances for DNB in DNB resolution | 2 | (1536,2032) | 4-byte float | W m-2sr-1 m | TBD |
| QF_VIIRS_DNB_SDR_1_Sub | Quality control flag for DNB | 2 | (1536,2032) | Unsigned 1-byte integer | N/A | TBD |
| QF2_VIIRS_SDR_GEO_Dnb_Sub | Quality control flag for DNB geolocation | 2 | (1536,2032) | Unsigned 1-byte integer | N/A | TBD |

CID_VIIRS Total Data Volume

Total Mbytes/Granule:	205.6

Total Mbytes/Hour:	2,467.2

Total Mbytes/Day:	59,212.8

Total Mbytes/Month:	1,835,597

VIIRS CID Revision Record

The product Revision Record contains information pertaining to approved section changes.  The table lists the date the Software Configuration Change Request (SCCR) was approved, the Release and Version Number, the SCCR number, a short description of the revision, and the revised sections.  The authors are listed on the document cover.

| VIIRS CID Revision Record |
| --- |
| SCCR Approval Date | Release/ Version Number | SCCR Number | Description of Revision | Section(s) Affected |
| N/A | R5V1 | N/A | New CERES-NPP Data Products Catalog section. | All |
| 02/11/09 | R5V2 | 701 | 3 more SDSs from M5 (0.672 micro meter), M10 (1.61 micro meter) and M12 (3.7 micro meter) were added with the same sub-sampling scheme as the other sub-setted Moderate bands. | Table 4.3-3 |
|  |  |  | Created the dimensions in Table 4.3-4. | Table 4.3-4 |
|  |  |  | Modified first paragraph for clarity. (07/10/2009) | Sec. 4.3 |
|  |  |  | Channels M1 and M2 were removed from the chart on the first page of this section. (07/22/2009) | Sec. 4.3 |
|  |  |  | Modified SDS Names and deleted some SDS files. (09/01/2009) | Tables 4.3.2, 4.3.3, & 4.3.4 |
|  |  |  | Channels M12 and M14 were added. (09/08/2009) | Sec. 4.3 |
| 08/16/10 | R5V3 | 802 | Filename changes. | Tables 4.3-3 & 4.3-4 |
|  |  |  | Added SCCR 701 to the Revision Record for R5V2. This SCCR didn’t exist when the document was updated, but it is the SCCR associated with the document modifications. | Rev. Rec. R5V2 |
|  |  |  | A small correction was made to the QF2_VIIRS filename. (09/10/10) | Table 4.3-4 |
|  |  |  | The ASDC footer was added to the bottom of the document. (06/07/2013) | All |
|  |  |  | Eliminated section numbers from the Data Products Catalog. Specifically, in this document, section number 4.3 was removed. (12/18/2013) | All |
|  |  |  | Updated document to change “mm” to “m.” (09/12/2019) | Tables 2, 3, & 4 |