Clouds and the Earth's Radiant Energy System

(CERES)

Data Management System

Operator’s Manual

CERES ERBE-like Averaging to Monthly TOA Fluxes

(Subsystem 3.0)

CER3.1P1

CER3.2P1

Release 8

Version 1

Dale Walikainen

Jeremie Lande

Science Systems and Applications, Inc. (SSAI)

One Enterprise Parkway, Suite 200

Hampton, VA  23666

NASA Langley Research Center

Climate Science Branch

Science Directorate

21 Langley Boulevard

Hampton, VA  23681-2199

SW Delivered to CM:  June 2012

Document Date:  March 2018

Document Revision Record

The Document Revision Record contains information pertaining to approved document changes.  The table lists the date the Software Configuration Change Request (SCCR) was approved, the Release and Version Number, the SCCR number, a short description of the revision, and the revised sections.  The document authors are listed on the cover.  The Head of the CERES Data Management Team approves or disapproves the requested changes based on recommendations of the Configuration Control Board.

| Document Revision Record |
| --- |
| SCCR Approval Date | Release/ Version Number | SCCR Number | Description of Revision | Section(s) Affected |
| 06/21/01 | R3V5 | 271 | Added exit codes and screen messages. | Secs. 1.5.1, 1.5.2, 2.5.1, & 2.5.2 |
|  |  |  | Updated format to comply with standards. | All |
| 04/26/02 | R3V6 | 341 | Added reference to new PGE 2.4P1. | Introduction |
|  |  |  | Added PCF, PCFin, and Toolkit Log files to the Expected output file listings. | Secs. 1.6 & 2.6 |
|  |  |  | Removed /QA from Expected output file listings destination column. | Secs. 1.6 & 2.6 |
|  |  |  | Updated format to comply with standards. | All |
| 04/17/03 | R4V1 | 432 | Added new PGE 3.2P2. | Introduction, Sec. 3 & App. C |
|  |  |  | Modified input file environment parameters for CER3.2P1 and CER3.2P2. | Secs. 2.2.2 & 3.2.2 |
|  |  |  | Updated format to comply with standards. | All |
| 12/09/03 | R4V2 | 484 | Added new es4 statistics plot and output files to CER3.1P1 and CER3.2P1 processing. | Tables 1-7 & 2-6 |
|  |  |  | Modified CER3.2P2 direct comparison and three channel inter-comparison output file names to reflect the production strategy. | Table 3-6 |
|  |  |  | Added Scatter plots to CER3.2P2 processing. | Table 3-6 |
|  |  |  | Updated format to comply with standards. | All |
| 08/18/05 | R4V3 | 592 | Changed the status from mandatory to optional for the last 7 files in Table 1-7. | Table 1-7 |
|  |  |  | Updated format to comply with standards. | All |
|  |  |  | Modified filename CER_ES8N_$SS3 to $SS2. (11/6/2008) | Sec. 3.3.2 |
| 10/28/09 | R5V1 | 735 | Updated contact info for responsible persons. | Table 1-1 |
|  |  |  | Updated disk space & time requirements to reflect new production platform (magneto). | Secs. 1.2.4 & 2.2.4 |
|  |  |  | Updated directory paths to reflect new IBM-based directory structure. | Secs. 1, 2, & App. B |
|  |  |  | Updated typical file size info for input files as on new production platform (magneto). | Secs. 1.3.1 & 2.3.1 |
|  |  |  | Updated typical file size info for output files as on new production platform (magneto). | Tables 1-7 & 2-6 |
|  |  |  | Updated & clarified execution instructions to reflect new production platform (magneto). | Secs. 1.4 & 2.4 |
|  |  |  | Removed Appendix C - Sample ASCII (PCFin) File Listing since PCFin files are no longer required. | App. C |
|  |  |  | Fixed the environment script parameter definitions for the inputs to CER3.1P1 (SS2, PS2, CC2). (01/20/2010) | Sec. 1.2.2 |
|  |  |  | Added data editions options to allow selection of the new Edition3 versions of the environment scripts for CER3.1P1 and CER3.2P1. (01/20/2010) | Secs. 1.4.1 & 2.4.1 |
|  |  |  | A small modification was made to the CXDR input filenames. (03/12/2010) | Sec. 1.3.2 |
|  |  |  | Removed /QA from expected output file listings destination column. (05/26/2010) | Tables 1-7, 2-6, & 3-6 |
|  |  |  | Added “Available Through Ordering Tool” column and removed red “meta” from expected output tables. (09/13/2010) | All Expected Output Tables |
|  |  |  | “Permanent” was deleted and “rm” was added to ES9 output file in “Destination” column. (09/22/2010) | Table 1-7 |
| 11/25/09 | R6V1 | 740 | Modified script/executable names for AMI. Updated with new AMI directory structure. Added SGE scripts. Updated PS1 environment variable to PS1_0 on AMI. | All |
|  |  |  | PGE CER3.2P2 was deleted. | Sec. 3.0 |
|  |  |  | Modified and added parameters. (09/30/2011) | Secs. 1.2.2 & 2.2.2 |
|  |  |  | Added “Web” to the destination columns of the output file listing tables. (10/13/2011) | Tables 1-7 & 2-6 |
| 11/25/09 (Cont’d) | R6V1 | 740 | “Archive, permanent” was modified to read “No Archive” in the DQCBW and DQCGW output files. (10/17/2011) | Tables 1-7 & 2-6 |
|  |  |  | Modified a link and document title name. (04/10/2012) | References |
|  |  |  | In the “m/o” column for the DQCX output file, the “m” was changed to “o.” (05/31/2012) | Table 1-7 |
| 09/21/11 | R7V1 | 867 | Added SS3in environment variable as alternative to SS2 for inputs to CER3.1P1. | Sec. 1.2.2 |
|  |  |  | Made the scanmode parameter optional. | Secs. 1.2.1 & 2.2.1 |
|  |  |  | Got rid of ‘ 1’,’ –1’ extensions for PCF generators & Driver scripts. | Table 1-4 & 2-3, Secs. 1.4 & 2.4 |
|  |  |  | Got rid of using ./ for starting scripts. | Secs. 1.4 & 2.4 |
|  |  |  | Specified that CXDRs are optional inputs to 3.1P1. | Sec. 1.3.2 |
|  |  |  | Added optional arguments listing for SGE Drivers and provided typical examples. | Secs. 1.4.2 & 2.4.2 |
|  |  |  | Updated exit codes/messages to new CERES standards. | Secs. 1.5 & 2.5, Tables 1-5, 1-6, 2-4, & 2-5 |
|  |  |  | Updated output tables to reflect elimination of DQCBW, DQCGW, and addtion of ES4G plots. | Secs. 1.6 & 2.6, Tables 1-7 & 2-6 |
|  |  |  | Eliminated redundant notes under 3.1’s temp file table. | Table 1-8 |
|  |  |  | Added .summary file and sge_log and updated Log files destination to expected output files listings for CERs 3.1P1 and 3.2P1. (10/31/2012) | Tables 1-7 & 2-6 |
|  |  |  | Modified information for PGE CER2.4P1 in ERBE-like table in Subsystem Overview. (09/18/2013) | Subsystem Overview |
|  |  |  | Fixed some cross reference link issues. (10/10/2013) | All |
|  |  |  | Added DPO to destination column for output files that need to be placed not only into the Archive, but into the DPO, and modified other destinations concerning Archive vs. No Archive. (06/05/2014) | Tables 1-7 & 2-6 |
| 09/21/11 (Cont'd) | R7V1 | 867 | Added "after successful completion." (06/05/2014) | Secs. 1.3.1, 1.3.2, & 2.3.1 |
|  |  |  | Changed destination for .summary files from ‘Archive, rm’ to ‘permanent, No Archive.’ (10/01/2014) Changed references to Edition3 to Edition3/4. (10/01/2014) | Tables 1-7 & 2-6 Secs. 1.2.2 & 2.2.2 |
|  |  |  | Changed sge_logs from optional to mandatory. (03/21/2017) | Tables 1-7 & 2-6 |
|  |  |  | Added "_2" to ES4G output file. (03/21/2017) | Table 2-6 |
|  |  |  | Corrected sampling strategy and production strategy environment variables for ES4G files. (05/03/2017) | Table 2-6 |
| 2/27/18 | R8V1 | 1337 | Remove all p6 references, and change –s and –e to –start and –end. | Secs. 1.4.2 & 2.4.2 |

Preface

The Clouds and the Earth’s Radiant Energy System (CERES) Data Management System supports the data processing needs of the CERES Science Team research to increase understanding of the Earth’s climate and radiant environment.  The CERES Data Management Team works with the CERES Science Team to develop the software necessary to support the science algorithms.  This software, being developed to operate at the Langley Atmospheric Science Data Center (ASDC), produces an extensive set of science data products.

The Data Management System consists of 12 subsystems; each subsystem represents one or more stand-alone executable programs.  Each subsystem executes when all of its required input data sets are available and produces one or more archival science products.

This Operator’s Manual is written for the data processing operations staff at the Langley ASDC by the Data Management Team responsible for this Subsystem.  Each volume describes all Product Generation Executables for a particular subsystem and contains the Runtime Parameters, Production Request Parameters, the required inputs, the steps used to execute, and the expected outputs for each executable included within this Subsystem.  In addition, all subsystem error messages and subsequent actions required by the ASDC operations staff are included.

Acknowledgment is given to the CERES Documentation Team for their support in preparing this document.

Document Revision Record	ii

Preface		vi

Introduction	1

Document Overview	1

Subsystem Overview	2

1.0	PGEName:  CER3.1P1	5

1.1	PGE Details	5

1.1.1	Responsible Persons	5

1.1.2	E-mail Distribution List	5

1.1.3	Parent PGE(s)	5

1.1.4	Target PGE(s)	6

1.2	Operating Environment	6

1.2.1	Runtime Parameters (List all Dynamic Parameters needed at Runtime)	6

1.2.2	Environment Script Requirements	6

1.2.3	Execution Frequency (daily, hourly, or monthly)	7

1.2.4	Memory/Disk Space/Time Requirements	7

1.2.5	Restrictions Imposed in Processing Order	7

1.3	Processor Dependencies (Previous PGEs, Ingest Data)	7

1.3.1	Input Dataset Name (#1):  EID-6	7

1.3.2	Input Dataset Name (#2):  CXDR	8

1.4	Operating Procedures (Procedure for each part of the processor’s elements)	8

1.4.1	How to Generate the PCF	9

1.4.2	How to Execute the Main-Processor	9

1.4.3	Special Case Considerations	10

1.4.4	Special Reprocessing Instructions	10

1.5	Execution Evaluation	10

1.5.1	Exit Codes	10

1.5.2	Screen Messages (Use Table format for large number of messages)	11

1.5.3	Log and Status Files Results (Include ALL Log Files)	13

1.5.3.1	Report Log File:  CER3.1P1_LogReport_$SS3_$PS3_$CC3.yyyymm	13

1.5.3.2	Status Log File:  CER3.1P1_LogStatus_$SS3_$PS3_$CC3.yyyymm	13

1.5.3.3	User Log File:  CER3.1P1_LogUser_$SS3_$PS3_$CC3.yyyymm	13

1.5.4	Solutions to Possible Problems	13

1.5.5	Conditions for Subsystem and/or Target PGE(s) Terminal Failure
	(Halt all further processing)	13

1.6	Expected Output Dataset(s)	13

1.7	Expected Temporary Files/Directories	16

2.0	PGEName:  CER3.2P1	17

2.1	PGE Details	17

2.1.1	Responsible Persons	17

2.1.2	E-mail Distribution List	17

2.1.3	Parent PGE(s)	17

2.1.4	Target PGE(s)	17

2.2	Operating Environment	17

2.2.1	Runtime Parameters (List all Dynamic Parameters needed at Runtime)	17

2.2.2	Environment Script Requirements	18

2.2.3	Execution Frequency (daily, hourly, or monthly)	19

2.2.4	Memory/Disk Space/Time Requirements	19

2.2.5	Restrictions Imposed in Processing Order	19

2.3	Processor Dependencies (Previous PGEs, Ingest Data)	19

2.3.1	Input Dataset Name (#1):  DES9	19

2.4	Operating Procedures (Procedure for each part of the processor’s elements)	19

2.4.1	How to Generate the PCF	20

2.4.2	How to Execute the Main-Processor	20

2.4.3	Special Case Considerations	21

2.4.4	Special Reprocessing Instructions	21

2.5	Execution Evaluation	22

2.5.1	Exit Codes	22

2.5.2	Screen Messages (Use Table format for large number of messages)	22

2.5.3	Log and Status Files Results (Include ALL Log Files)	23

2.5.3.1	Report Log File:  CER3.2P1_LogReport_$SS3_2_$PS3_2_$CC3_2.
	yyyymm	24

2.5.3.2	Status Log File:  CER3.2P1_LogStatus_$SS3_2_$PS3_2_$CC3_2.
	yyyymm	24

2.5.3.3	User Log File:  CER3.2P1_LogUser_$SS3_2_$PS3_2_$CC3_2.yyyymm	24

2.5.4	Solutions to Possible Problems	24

2.5.5	Conditions for Subsystem and/or Target PGE(s) Terminal Failure
	(Halt all further processing)	24

2.6	Expected Output Dataset(s)	24

2.7	Expected Temporary Files/Directories.	27

References	28

Appendix A - Acronyms and Abbreviations	A-1

Appendix B - Error Messages	B-1

Table 1-1.  Subsystem Software Analysts Contacts	5

Table 1-2.  Parent PGEs for CER3.1P1	5

Table 1-3.  Target PGEs after CER3.1P1	6

Table 1-4.  Runtime Parameters for CER3.1P1	6

Table 1-5.  Exit Codes for CER3.1P1	11

Table 1-6.  Screen Messages for execution of CER3.1P1	11

Table 1-7.  Expected Output File Listing for CER3.1P1	14

Table 1-8.  Temporary Files Listing	16

Table 2-1.  Parent PGEs for CER3.2P1	17

Table 2-2.  Target PGEs after CER3.2P1	17

Table 2-3.  Runtime Parameters for CER3.2P1	17

Table 2-4.  Exit Codes for CER3.2P1	22

Table 2-5.  Screen Messages for execution of CER3.2P1	22

Table 2-6.  Expected Output File Listing for CER3.2P1	25

Table 2-7.  Temporary Files Listing	27

Table B-1.  PGE CER3.1P1 & CER3.2P1 Error Messages	B-3

Introduction

CERES is a key component of EOS and NPP.  The first CERES instrument (PFM) flew on TRMM, four instruments are currently operating on the EOS Terra (FM1 and FM2) and Aqua (FM3 and FM4) platforms, and NPP (FM5) platform.  CERES measures radiances in three broadband channels:  a shortwave channel (0.3 - 5 m), a total channel (0.3 - 200 m), and an infrared window channel (8 - 12 m).  The last data processed from the PFM instrument aboard TRMM was March 2000; no additional data are expected.  Until June 2005, one instrument on each EOS platform operated in a fixed azimuth scanning mode and the other operated in a rotating azimuth scanning mode; now all are typically operating in the fixed azimuth scanning mode.  The NPP platform carries the FM5 instrument, which operates in the fixed azimuth scanning mode though it has the capability to operate in a rotating azimuth scanning mode.

CERES climate data records involve an unprecedented level of data fusion:  CERES measurements are combined with imager data (e.g., MODIS on Terra and Aqua, VIIRS on NPP), 4-D weather assimilation data, microwave sea-ice observations, and measurements from five geostationary satellites to produce climate-quality radiative fluxes at the top-of-atmosphere, within the atmosphere and at the surface, together with the associated cloud and aerosol properties.

The CERES project management and implementation responsibility is at NASA Langley.  The CERES Science Team is responsible for the instrument design and the derivation and validation of the scientific algorithms used to produce the data products distributed to the atmospheric sciences community.  The CERES DMT is responsible for the development and maintenance of the software that implements the science team’s algorithms in the production environment to produce CERES data products.  The Langley ASDC is responsible for the production environment, data ingest, and the processing, archival, and distribution of the CERES data products.

Document Overview

This document, CERES ERBE-like Averaging to Monthly TOA Fluxes Subsystem 3.0 Release 5 Operator’s Manual is part of the CERES Subsystems 2.0 and 3.0 Release 5 software package provided to the Langley Atmospheric Science Data Center (ASDC).  It provides a description of the CERES ERBE-like Subsystem 3.0 Release 3 software and explains the procedures for executing the software.  A description of acronyms and abbreviations is provided in Appendix A and a comprehensive list of messages that can be generated during the execution of PGEs CER3.1P1 and CER3.2P1 are contained in Appendix B.

This document is organized as follows:

Introduction

Document Overview

Subsystem Overview

PGEName:  CER3.1P1	-	CERES ERBE-like Monthly TOA Flux Averaging for a Single Instrument.

PGEName:  CER3.2P1	-	CERES ERBE-like Monthly TOA Flux Averaging for Multiple Instruments.

References

Appendix A - Acronyms and Abbreviations

Appendix B - Error Messages

Subsystem Overview

The ERBE-like software is divided into two subsystems; Subsystem 2.0 - ERBE-like Inversion, which processes daily data, and Subsystem 3.0 - ERBE-like Monthly Averaging, which processes once a month.  The ERBE-like Subsystems 2.0 and 3.0 come from the ERBE Subsystems V and VI.  Details concerning the conversion process from the ERBE to the CERES ERBE-like code may be found in the CERES Software Requirement Documents for Subsystem 2.0 and 3.0 (Reference 1).

Subsystem 3.0 (ERBE-like Averaging to Monthly TOA Fluxes)

Up to this phase of the processing, data are processed in time-ordered sequence, regardless of the location of the measurements (see CERES ERBE-like Inversion to Instantaneous Top-of-Atmosphere (TOA) Fluxes Subsystem 2.0 Release 6 Operator’s Manual, Reference 2).  To obtain monthly averages of the radiometric measurements for geographic regions, the data must be made accessible by region.  To accomplish this data transition, a Daily Data Base which contains data for an entire month is created to store the time-sequenced inverted data.

The data base is comprised of 36 latitudinal data files and a housekeeping file.  The housekeeping file provides the necessary information for accessing data from the data base.  As each daily EID-6 file from Inversion is processed, individual records are written to one of the 36 latitudinal data files based on region number.  After all EID-6 files are processed, a final sort is performed to each of the 36 latitudinal files.

The function of the ERBE-like Monthly Time/Space Averaging Subsystem is to produce monthly averages of shortwave and longwave radiant flux at the TOA on a regional basis.  These calculations are made at the spatial resolution of a 2.5-degree region on the Earth’s surface.  These data are processed for each instrument to produce monthly daily averages, monthly hourly averages (each hour averaged for all data during the month), and two grand monthly averages (averages of the daily and monthly hourly averages) for each geographic region.  The averages are stored in the ES-9 and then used to produce regional, zonal, and global output products, ES-4/ES-4G.

At minimum, 3 (or more depending on the Processing Mode) Product Generation Executives (PGEs) are needed to run the ERBE-like software (Subsystems 2.0 and 3.0).  This Operator’s Manual will describe the Subsystem 3.0 PGE requirements.  An accompanying ERBE-like Subsystem 2.0 Operator’s Manual has been provided to complete the ERBE-like software PGE processing requirements.

In the Subsystem 2.0 Operator’s Manual are described the Overlap-Processors: CER2.3P1 and CER2.3P2 which have been written to process hours seen by the satellite in a given datayear and datamonth but had been recorded at the end of the previous month and at the beginning of the next month.  These processors are considered as the ’initial’ processors to the Subsystem 3.0 Processing Scenarios.

The following table contains each PGE with its execution frequency, PGE dependencies (input requirements), target PGEs, and a short description.

| ERBE-like (Subsystems 2.0 and 3.0) Processing (FAPS+RAPS) Overview |
| --- |
| PGE | Freq. | PGE Dependencies | Target PGEs | Description |
| CER2.1P1 | 1/month | Ingest Data (NSIDC snow/ice SURFMAP) | CER2.2P1 CER2.3P1 CER2.3P2 | This PGE is run after the end of the data month after all ingest data have arrived. |
| CER2.2P1 | 1/day (Quick Look, validation) | CER1.2P1 | N/A | This PGE is processed three times, the first time with composite snow. The output is viewed and deleted after the PGE is processed a second time with actual snow, see next item. |
| CER2.2P1 | 1/day/month (Baseline, validation) | CER1.2P1 CER2.1P1 | N/A | This PGE is processed a second time after the end of the data month with actual snow (output from 2.1P1). The output is used in spectral response function analysis, see next item. |
| CER2.2P1 | 1/day/month (for archival) | CER1.2P1 CER2.1P1 CER2.4P1 | CER3.1P1 | This PGE is processed a third time after the processing of the spectral correction coefficients. Actual snow (output from 2.1P1) and updated spectral correction coefficients (output from 2.4P1). Output from this process will be input to Subsystem 3.0. |
| CER2.3P1 | 1/month | CER1.2P1 CER2.1P1 CER2.4P1 | CER3.1P1 | This PGE creates an overlap data file from the first day of the next month. Actual snow of the current month and updated spectral correction coefficients of the current month are used. Ancillary input must be the same as used for the second processing of CER2.2P1. |
| CER2.3P2 | 1/month | CER1.2P1 CER2.1P1 CER2.4P1 | CER3.1P1 | This PGE creates an overlap data file from the last day of the previous month. Actual snow of the current month and updated spectral correction coefficients of the current month are used. Ancillary input must be the same as used for the second processing of CER2.2P1. |
| CER2.4P1 | 1/month | None (gain trends included in filtered data of the input product: Pre-ES8) | CER2.2P1 CER2.3P1 CER2.3P2 CER4.5-6.1P2 | This PGE creates an updated set of monthly spectral correction coefficient values for the Edition2+ inversion process, based on corrected monthly SW spectral response functions. |
| Note: From this point on the processors are considered as part of Subsystem 3.0 process scenario. |
| CER3.1P1 | 1/month | CER2.2P1 CER2.3P1 CER2.3P2 | CER3.2P1 | Monthly Averaging. This PGE creates archival products ES-4 and ES-9. |
| CER3.2P1 | 1/month | CER3.1P1 | N/A | Multi-Instrument Monthly Averaging. This PGE creates archival products ES-4 and ES-9. |

Seven Product Generation Executives (PGEs) are used to run the ERBE-like software (Subsystems 2.0 and 3.0).  This Operator’s Manual describes the Subsystem 3.0 PGE procedures.  The CERES ERBE-like Inversion to Instantaneous TOA Fluxes (Subsystem 2.0) Operator’s Manual (Reference 2) is also available.

# PGEName:  CER3.1P1

CERES ERBE-like Monthly TOA Flux Averaging for a Single Instrument.

## PGE Details

### Responsible Persons

Table 1-1.  Subsystem Software Analysts Contacts

| Item | Primary | Alternate |
| --- | --- | --- |
| Contact Name | Dale R. Walikainen | Jeremie Lande |
| Organization | SSAI | SSAI |
| Address | 1 Enterprise Parkway | 1 Enterprise Parkway |
| City | Hampton | Hampton |
| State | VA 23666 | VA 23666 |
| Phone | (757) 951-1692 | (757) 951-1916 |
| Fax | (757) 951-1900 | (757) 951-1900 |
| LaRC email | d.r.walikainen@nasa.gov | jeremie.lande-1@nasa.gov |

### E-mail Distribution List

E-mail distribution list can be obtained from the primary contact listed in Table 1-1.

### Parent PGE(s)

A parent PGE generates data for input to the current PGE CER3.1P1.

Table 1-2.  Parent PGEs for CER3.1P1

| PGEName | Description |
| --- | --- |
| CER2.2P1 | CERES ERBE-like Daily Inversion to Instantaneous TOA Fluxes Main-Processor for FAPS+RAPS data for a Single Instrument. |
| CER2.3P1 | CERES ERBE-like Monthly Inversion to Instantaneous TOA Fluxes Overlap-Processor for FAPS+RAPS data for a Single Instrument for the First Day of the Next Month. |
| CER2.3P2 | CERES ERBE-like Monthly Inversion to Instantaneous TOA Fluxes Overlap-Processor for FAPS+RAPS data for a Single Instrument for the Last Day of the Previous Month. |

### Target PGE(s)

A target PGE requires input data generated from the current PGE CER3.1P1.

Table 1-3.  Target PGEs after CER3.1P1

| PGEName | Description |
| --- | --- |
| CER3.2P1 | CERES ERBE-like Monthly TOA Flux Averaging Main-Processor for FAPS+RAPS data for Multiple Instruments. |

## Operating Environment

### Runtime Parameters (List all Dynamic Parameters needed at Runtime)

Table 1-4.  Runtime Parameters for CER3.1P1

| Parametera | Description | Valid Values |
| --- | --- | --- |
| yyyy | CERDataDateYear | >= 1984 |
| mm | CERDataDateMonth | 01 .. 12 |
| scanmodeb | Process both FAPS and RAPS data together (1)b | 1 |

a.	All character strings.

b.	Optional parameter since for PGE CER3.1P1, both scan modes (FAPS and RAPS) data will be processed in any case, if available.  The parameter value “1” is therefore the only option for scanmode in the processing of these scripts.

### Environment Script Requirements

Refer to the CERES internal paper (Reference 3) for a detailed description of the CERES environment parameters.  For the current values of the Sampling Strategy and Production Strategy variables listed below, see “CERES DMT to DAAC Processing Requests.”  (URL:  http://ceres.larc.nasa.gov/dmt2daac.php )

One Environment Script is required and should define the following parameters:

SS2 or SS3in	-	Sampling Strategy for input files, see Production Request (Reference 4) Note: For Edition3/4, SS3in = $SAT-Xtrk

SS3 	-	Sampling Strategy for CER3.1P1, see Production Request (Reference 4) Note: For Edition3/4, SS3 = $SAT

PS2	-	Production Strategy for CER2.2P1, see Production Request (Reference 4)

PS3	-	Production Strategy for CER3.1P1, see Production Request (Reference 4)

CC2	-	Configuration Code for CER2.2P1, see CM Database

CC3	-	Configuration Code for CER3.1P1, see CM Database

SW2	-	Software SCCR number for CER2.2P1, see CM Database

DATA2 	-	Data SCCR number for CER2.2P1, see CM Database

SW3	-	Software SCCR number for CER3.1P1, see CM Database

DATA3 	-	Data SCCR number for CER3.1P1, see CM Database

SAT	-	Satellite, see Production Request (Reference 4)

INST	-	Instrument, see Production Request ( Reference 4)

PROD	-	Production mode, optional since ‘Yes’ by default

PGE	-	PGE name, optional and set to ‘CER3.1P1’

ERBELIKEHOME	-	can be different from but in production will be the same as CERESHOME

InputArchive	-	location of ASDC DPO, by default set to ‘/ASDC_archive’

### Execution Frequency (daily, hourly, or monthly)

Monthly (1/month) - This PGE is to be processed once per month, when input is available.

### Memory/Disk Space/Time Requirements

Memory:	288 MB

Disk Space:	625 MB

Total Run Time:	3 minutes

### Restrictions Imposed in Processing Order

PGE CER3.1P1 requires a minimum of 15 days of the input data set EID-6 (see Section 1.3.1).  If the required number of input files are not available, contact the Subsystem software analysts from Table 1-1.

## Processor Dependencies (Previous PGEs, Ingest Data)

Note:  Include required .met files, header files, .. all required inputs

### Input Dataset Name (#1):  EID-6

Directory Location/Inputs Expected (Including .met files, header files, etc.):

$CERESHOME/erbelike/data/CERES/EID6/$SS2_$PS2/yyyy/mm /CER_EID6_$SS2_$PS2_$CC2.yyyymmdd (dd = 1 .. 31)

Total number of files equals number of days in DataDate month.

dd = 01 through 31, maximum.

Mandatory/Optional:  These files are mandatory, if they exist.  A minimum of 15 days must exist in order to process.

Time Related Dependency:  The DataDate must match the runtime parameters: yyyy, mm

Waiting Period:  None, process when all input data are available.

Source of Information (Source is PGE name or Ingest Source):

Source PGE:  CER2.2P1

Alternate Data Set, if one exists (maximum waiting period):  None.

File Disposition after successful execution:  Remove, after successful completion.

Typical file size (MB):  9

### Input Dataset Name (#2):  CXDR

- Directory Location/Inputs Expected (Including .met files, header files, etc.):

$CERESHOME/erbelike/data/CERES/CXDR/$SS2_$PS2/yyyy/mm/
CER_CXDR_$SS2_$PS2_$CC2.pypmpd

$CERESHOME/erbelike/data/CERES/CXDR/$SS2_$PS2/yyyy/mm/
CER_CXDR_$SS2_$PS2_$CC2.nynmnd

Two files total where ‘pypmpd’ equals the year, month, and day corresponding to the Last day of the previous month and ‘nynmnd’ equals the year, month, and day corresponding to the First day of the next month.  (See the CERES ERBE-like Inversion to Instantaneous Top-of-Atmosphere (TOA) Fluxes Subsystem 2.0 Operator’s Manual, PGEs CER2.3P1 and CER2.3P2, for more information.)

- Mandatory/Optional:  These optional files are mandatory only if they exist.

Time Related Dependency:  The DataDate must be the previous and next month in reference to the runtime parameters:  yyyy, mm

Waiting Period:  None, process when all input data are available.

Source of Information (Source is PGE name or Ingest Source):

Source PGEs:  CER2.3P1 and CER2.3P2

Alternate Data Set, if one exists (maximum waiting period):  None.

File Disposition after successful execution:  Remove, after successful completion.

Typical file size (MB):  0.4 – 0.8

## Operating Procedures (Procedure for each part of the processor’s elements)

Clear the output directories of files previously generated from this PGE (for this particular data instance) by executing script, clr_dir.PGE3.1P1.csh, with the runtime parameter data date:

At the command-line (>) type:

> cd $CERESHOME/erbelike/CER3.1P1/rcf

> clr_dir.PGE3.1P1.csh yyyymm

The production script, CER3.1P1.pl, references a Process Control File (PCF) containing the file names and paths for the PGE.  For manual processing, this PCF is created by first sourcing an ERBE-like-specific environment script mentioned in Section 1.2.2 above, then executing the PCF generator, gen_pcf.CER3.1P1.pl.  If processing via SGE, the PCF generator will be called via the driver script CER3.1P1-SGE_Driver.pl followed by the runtime parameters of Table 1-4, as shown in Section 1.2.2.

### How to Generate the PCF

The PCF generator requires two command line arguments: data date (yyyymm) and scan mode (= 1 by default, so as to include both FAPS+RAPS) (see Table 1-4).

At the command-line (>) type (Note: this step is not needed for SGE testing):

> gen_pcf.CER3.1P1.pl yyyymm

The following files are generated and located in $CERESHOME/erbelike/CER3.1P1/rcf/pcf/:

CER3.1P1_PCF_$SS3_$PS3_$CC3.yyyymm

CER3.1P1_PCF_$SS3_$PS3_$CC3.yyyymm.log

### How to Execute the Main-Processor

Before running the program, make sure the necessary executables are where they should be:  7 in $CERESHOME/erbelike/bin (sol_dec, pre_es4, ddbint, ddbupd, es4, gen_es9hdf, and gen_es4hdf), and 3 in $CERESHOME/erbelike/CER3.1P1/bin (ddbuer, ddbsrt, and mtsa1).  Also, to avoid segmentation faults with hdf file generation, run the ‘unlimit’ command at the prompt.  If processing manually, execute the production script by typing the script name, CER3.1P1.pl, followed by a string which designates the instance of the data.  The string should be formatted, “Sampling Strategy”_”Production Strategy”_”Configuration Code”.”DataDate”.  The date parameter is formatted, yyyymm, where yyyy is the data year and mm is the data month (see Table 1-4).

At the command-line (>) type (Note: this step is not needed for SGE testing):

> CER3.1P1.pl $SS3_$PS3_$CC3.yyyymm

To run using SGE instead, type:

> CER3.1P1-SGE_Driver.pl –d yyyymm

To run using SGE for multiple sequential dates, type:

> CER3.1P1-SGE_Driver.pl –start y1m1 –end y2m2

where y1m1 and y2m2 are the start and end dates, respectively.

The CER3.1P1-SGE_Driver.pl script will search for the required input data files and any existing data product files for the requested data date(s) and time(s) provided.  If all the input data files are available and previously created output for this data date does not exist, the job will be submitted to the SGE queue.  However, if any mandatory data files are missing the script will not submit the job to the SGE queue.  Instead the information on which data files are missing or already exist can be found in the CER3.1P1_PCF_$SS3_$PS3_$CC3.yyyymm.log file.  Mandatory files may then be staged or existing output files can be deleted before trying again.

Here are the optional arguments for CER3.1P1-SGE_Driver.pl:

[-clean]	Delete any existing outputs that are encountered.

[-force]	Force the job to run regardless of any input scanning checks.

[-help]	Display this help message.

[-platform CPU]	Run the PGE on the platform designated by CPU.

[-nosummary]	Disable the creation of the summary file.

[-automatic]	Run in automatic (non-interactive) mode.

[-date YYYYMM]	Run the PGE on the data month specified by YYYYMM.

[-start YYYYMM]	Run the PGE starting on the data month specfied by YYYYMM.

[-end YYYYMM]	Run the PGE stopping on the data month specified by YYYYMM.

Below is a typical example of executing the driver script.

To run a single month on an x86 platform:

> CER3.1P1-SGE_Driver.pl –d 200912 –p x86

### Special Case Considerations

When running either the pcf generator or directory-clearing script, the system may display a message that it cannot access or remove certain files/directories.  This can happen to the former when either or both monthly overlap files are missing from the input data set.  Since these files are optional, this is not a problem.  In the latter case, the directory-clearing script removes temporary output directories which should only exist only during run time (i.e., the scratch directory) or until the next data run instance (i.e., the web output directories).  Failure to find these indicates either a successful last run or an initial run for this data instance.

### Special Reprocessing Instructions

All output files are opened with Status = NEW in the CER3.1P1 software.  These files must be removed before rerunning these procedures.  A script, which removes PGE created files, clr_dir.PGE3.1P1, is located in directory $CERESHOME/erbelike/CER3.1P1/rcf.  Using data date as a command line argument:

> clr_dir.PGE3.1P1.csh yyyymm

See reprocessing requirements in “CERES DMT to DAAC Processing Requests” available on the Web at:  http://ceres.larc.nasa.gov/docs.php .

## Execution Evaluation

### Exit Codes

The processor CER3.1P1 terminates using the CERES-defined EXIT CODES for the Langley TRMM Information System (LaTIS), as seen in Table 1-5.  Other Exit Codes may appear from the program, which may be the result of a system, compiler, or Toolkit related error.  In these cases, contact the responsible person for assistance (see Table 1-1).

| Table 1-5. Exit Codes for CER3.1P1 |
| --- |
| Exit Code | Definition | Action |
| 0 | Normal Exit | Proceed normally |
| 198 | Fatal | “PCF missing error CER3.1P1_PCF_$SS3_$PS3_$CC3.yyyymm. DoesNOT exist”. Inform the primary contact in Table 1-1 |
| 75 | Failure | “JSS invalid date error”. Check the Log Files and take the appropriate action (see Appendix B). |
| 151 | Failure | “PCF file write error”. Check the Log Files and take the appropriate action (see Appendix B). |
| 152 | Failure | “PCF parameter Error”. Check the Log Files and take the appropriate action (see Appendix B). |
| 250 | Failure | “PLT_ERROR: UNSUCCESSFULLY terminated in plot_es4 ”. Check the Log Files and take the appropriate action (see Appendix B). |
| 200 | Failure | “Non-specific PGE error”. Check the Log Files and take the appropriate action (see Appendix B). |
| 239 | Failure | “PGE HDF compression error. CER3.1P1 CER3.1P1_PCF_$SS3_$PS3_$CC3.yyyymm UNSUCCESSFULLY terminated in gen_es9hdf”. Check the Log Files and take the appropriate action (see Appendix B). |
| 239 | Failure | “PGE HDF compression error. CER3.1P1 CER3.1P1_PCF_$SS3_$PS3_$CC3.yyyymm UNSUCCESSFULLY terminated in gen_es4hdf”. Check the Log Files and take the appropriate action (see Appendix B). |

### Screen Messages (Use Table format for large number of messages)

| Table 1-6. Screen Messages for execution of CER3.1P1 |
| --- |
| Message | Definition/Action |
| Cannot access <filename>: No such file or directory | From the clear directory script, clr_dir.PGE3, as a part of the Main-Processor. This message occurs when the script tries to remove an old output file that does not exist. Proceed normally. |
| CER3.1P1_PCF_$SS3_$PS3_$CC3.yyyymm SUCCESSFULLY terminated Exit Status = 0 | From running the production script, CER3.1P1, this message written to the screen signifies no fatal errors during production. Proceed normally. |
| PCF: CER3.1P1_PCF_$SS3_$PS3_$CC3.yyyymm DoesNOT exist Exit Status = 198 | This message is written to the screen signifying a fatal error has occurred. Refer to the Log files for more detailed information (see Appendix B). |
| CER3.1P1_PCF_$SS3_$PS3_$CC3.yyyymm UNSUCCESSFULLY terminated in sol_dec Exit Status = 200 | From running the production script, CER3.1P1, this message written to the screen signifies a fatal error has occurred. Refer to the Log files for more detailed information (see Appendix B). |
| CER3.1P1_PCF_$SS3_$PS3_$CC3.yyyymm UNSUCCESSFULLY terminated in pre_es4 Exit Status = 200 | From running the production script, CER3.1P1, this message written to the screen signifies a fatal error has occurred. Refer to the Log files for more detailed information (see Appendix B). |
| CER3.1P1_PCF_$SS3_$PS3_$CC3.yyyymm UNSUCCESSFULLY terminated in ddbint Exit Status = 200 | From running the production script, CER3.1P1, this message written to the screen signifies a fatal error has occurred. Refer to the Log files for more detailed information (see Appendix B). |
| CER3.1P1_PCF_$SS3_$PS3_$CC3.yyyymm UNSUCCESSFULLY terminated in ddbupd Exit Status = 200 | From running the production script, CER3.1P1, this message written to the screen signifies a fatal error has occurred. Refer to the Log files for more detailed information (see Appendix B). |
| CER3.1P1_PCF_$SS3_$PS3_$CC3.yyyymm UNSUCCESSFULLY terminated in ddbuer Exit Status = 200 | From running the production script, CER3.1P1, this message written to the screen signifies a fatal error has occurred. Refer to the Log files for more detailed information (see Appendix B). |
| CER3.1P1_PCF_$SS3_$PS3_$CC3.yyyymm UNSUCCESSFULLY terminated in ddbsrt Exit Status = 200 | From running the production script, CER3.1P1, this message written to the screen signifies a fatal error has occurred. Refer to the Log files for more detailed information (see Appendix B). |
| CER3.1P1_PCF_$SS3_$PS3_$CC3.yyyymm UNSUCCESSFULLY terminated in mtsa1 Exit Status = 200 | From running the production script, CER3.1P1, this message written to the screen signifies a fatal error has occurred. Refer to the Log files for more detailed information (see Appendix B). |
| CER3.1P1 CER3.1P1_PCF_$SS3_$PS3_$CC3.yyyymm UNSUCCESSFULLY terminated in es4 Exit Status = 200 | From running the production script, CER3.1P1, this message written to the screen signifies a fatal error has occurred. Refer to the Log files for more detailed information (see Appendix B). |
| CER3.1P1 CER3.1P1_PCF_$SS3_$PS3_$CC3.yyyymm UNSUCCESSFULLY terminated in gen_es9hdf Exit Status = 239 | From running the production script, CER3.1P1, this message written to the screen signifies a fatal error has occurred. Refer to the Log files for more detailed information (see Appendix B). |
| CER3.1P1 CER3.1P1_PCF_$SS3_$PS3_$CC3.yyyymm UNSUCCESSFULLY terminated in gen_es4hdf Exit Status = 239 | From running the production script, CER3.1P1, this message written to the screen signifies a fatal error has occurred. Refer to the Log files for more detailed information (see Appendix B). |
| CER3.1P1 CER3.1P1_PCF_$SS3_$PS3_$CC3.yyyymm UNSUCCESSFULLY terminated in plot_es4 Exit Status = 250 | From running the production script, CER3.1P1, this message written to the screen signifies a fatal error has occurred. Refer to the Log files for more detailed information (see Appendix B). |

### Log and Status Files Results (Include ALL Log Files)

The Log files contain all error and/or status messages produced by the PGE.  The files are located in directory: $CERESHOME/erbelike/runlogs/CER3.1P1.

#### Report Log File:  CER3.1P1_LogReport_$SS3_$PS3_$CC3.yyyymm

The Report Log File contains the ERBE-like related messages.  These messages may be strictly informative (Error Type = Status or Warning) or may indicate a fatal condition that results in premature PGE termination (Error Type = Fatal).  A comprehensive list of these messages, that can be generated during the execution of the PGE, is contained in Appendix B.

#### Status Log File:  CER3.1P1_LogStatus_$SS3_$PS3_$CC3.yyyymm

The Status Log File contains all messages created by the Toolkit.  If an abnormal exit is encountered by the PGE, this file should be examined for ‘_F_’, fatal message type.  The responsible person should be advised (see Table 1-1).

#### User Log File:  CER3.1P1_LogUser_$SS3_$PS3_$CC3.yyyymm

The User Log File is not used at this time, but exists to satisfy the Toolkit requirements.  Typically the ‘_U_’ and ‘_N_’ (User information and Notice) will be written to User Log File and the Status Log File.

### Solutions to Possible Problems

### Conditions for Subsystem and/or Target PGE(s) Terminal Failure (Halt all further processing)

- Subsystem Termination

Please refer to Appendix B for a descriptive list of all errors and the result of those errors.

Target PGE Termination

Please refer to Appendix B for a descriptive list of all errors and the result of those errors.

If .met files have not been created, the Target PGE(s) will not run.  Target PGEs should not be processed in instances of PGE failure.

## Expected Output Dataset(s)

The expected Output Datasets (including all expected web files) are listed below for each instance of the PGE.  This PGE is expected to process once a month.

| Table 1-7. Expected Output File Listing for CER3.1P1 If “(.met)” is written next to an expected Output Filename in the following table, then the metadata file must exist with the identical file name and .met extension. |
| --- |
| File Namea/Directory | m/ob | File Size (MB) | Freq/ PGE | Target PGE | Destinationc | Available Through Ordering Tool |
| CER3.1P1_PCF_$SS3_$PS3_$CC3.yyyymm @($CERESHOME/erbelike/CER3.1P1/rcf/pcf/) | m | 0.05 | 1/month | N/A | Archive, rm | No |
| CER3.1P1_PCF_$SS3_$PS3_$CC3.yyyymm.log @($CERESHOME/erbelike/CER3.1P1/rcf/pcf/) | m | 0.008 | 1/month | N/A | Archive, rm | No |
| CER3.1P1_$SS3_$PS3_$CC3.yyyymm.summary or CER3.1P1_$SS3_$PS3_$CC3.y1m1-y2m2.summary @($CERESHOME/erbelike/CER3.1P1/rcf/pcf/summary) | o | 0.005 | 1/run | N/A | permanent, No archive | No |
| CER3.1P1_LogReport_$SS3_$PS3_$CC3.yyyymm @($CERESHOME/erbelike/runlogs/CER3.1P1/) | m | 0.072 | 1/month | N/A | Archive, rm | No |
| CER3.1P1_LogStatus_$SS3_$PS3_$CC3.yyyymm @($CERESHOME/erbelike/runlogs/CER3.1P1/) | m | 0.032 | 1/month | N/A | Archive, rm | No |
| CER3.1P1_LogUser_$SS3_$PS3_$CC3.yyyymm @($CERESHOME/erbelike/runlogs/CER3.1P1) | m | 0.008 | 1/month | N/A | Archive, rm | No |
| CER3.1P1_$SS3_$PS3_$CC3.yyyymm.o# @($CERESHOME/erbelike/sge_logs/CER3.1P1) | m |  | 1/month | N/A | Archive, rm | No |
| CER_DES9_$SS3_$PS3_$CC3.yyyymm (.met) @($CERESHOME/erbelike/data/CERES/DES9/ $SS3_$PS3/yyyy/mm/) | m | 100 | 1/month | CER3.2P1 | DPO, Archive | No |
| CER_ES9_$SS3_$PS3_$CC3.yyyymm (.met) @($CERESHOME/erbelike/data/CERES/ES9/ $SS3_$PS3/yyyy/mm/) | m | 55 | 1/month | N/A | DPO, Archive, rm | Yes |
| CER_DMSG_$SS3_$PS3_$CC3.yyyymm (.met) @($CERESHOME/erbelike/data/CERES/DMSG/ $SS3_$PS3/yyyy/mm/) | m | 0.05 | 1/month | N/A | DPO, Archive, rm | No |
| CER_DQCD_$SS3_$PS3_$CC3.yyyymm (.met) @($CERESHOME/erbelike/data/CERES/DQCD/ $SS3_$PS3/yyyy/mm/) | m | 1.60 | 1/month | N/A | DPO, Web, Archive, rm | No |
| CER_DQCS_$SS3_$PS3_$CC3.yyyymm (.met) @($CERESHOME/erbelike/data/CERES/DQCS/ $SS3_$PS3/yyyy/mm/) | m | 0.008 | 1/month | N/A | DPO, Web, Archive, rm | No |
| CER_DQCX_$SS3_$PS3_$CC3.yyyymm (.met) @($CERESHOME/erbelike/data/CERES/DQCX/ $SS3_$PS3/yyyy/mm/) | o | 0.008 | 1/month | N/A | DPO, Web, Archive, rm | No |
| CER_DQCA_$SS3_$PS3_$CC3.yyyymm (.met) @($CERESHOME/erbelike/data/CERES/DQCA/ $SS3_$PS3/yyyy/mm/) | m | 0.112 | 1/month | N/A | DPO, Web, Archive, rm | No |
| CER_DQCB_$SS3_$PS3_$CC3.yyyymm (.met) @($CERESHOME/erbelike/data/CERES/DQCB/ $SS3_$PS3/yyyy/mm/) | m | 0.192 | 1/month | N/A | DPO, Web, Archive, rm | No |
| CER_DQCC_$SS3_$PS3_$CC3.yyyymm (.met) @($CERESHOME/erbelike/data/CERES/DQCC/ $SS3_$PS3/yyyy/mm/) | m | 0.05 | 1/month | N/A | DPO, Web, Archive, rm | No |
| CER_DQCG_$SS3_$PS3_$CC3.yyyymm (.met) @($CERESHOME/erbelike/data/CERES/DQCG/ $SS3_$PS3/yyyy/mm/) | m | 0.12 | 1/month | N/A | DPO, Web, Archive, rm | No |
| CER_DES4_$SS3_$PS3_$CC3.yyyymm (.met) @($CERESHOME/erbelike/data/CERES/DES4/ $SS3_$PS3/yyyy/mm/) | m | 17.4 | 1/month | N/A | DPO, Archive, rm | No |
| CER_ES4_$SS3_$PS3_$CC3.yyyymm (.met) @($CERESHOME/erbelike/data/CERES/ES4/ $SS3_$PS3/yyyy/mm/) | m | 9 | 1/month | N/A | DPO, Archive, rm | Yes |
| CER_ES4G1_$SS3_$PS3_$CC3.yyyymm (.met) @($CERESHOME/erbelike/data/CERES/ES4G1/ $SS3_$PS3/yyyy/mm/) | m | 3.5 | 1/month | N/A | DPO, Archive, rm | No |
| CER_ES4G2_$SS3_$PS3_$CC3.yyyymm (.met) @($CERESHOME/erbelike/data/CERES/ES4G2/ $SS3_$PS3/yyyy/mm/) | m | 6.9 | 1/month | N/A | DPO, Archive, rm | No |
| CER_ES4G3_$SS3_$PS3_$CC3.yyyymm (.met) @($CERESHOME/erbelike/data/CERES/ES4G3/ $SS3_$PS3/yyyy/mm/) | m | 2.3 | 1/month | N/A | DPO, Archive, rm | No |
| CER_ES4G4_$SS3_$PS3_$CC3.yyyymm (.met) @($CERESHOME/erbelike/data/CERES/ES4G4/ $SS3_$PS3/yyyy/mm/) | m | 5.7 | 1/month | N/A | DPO, Archive, rm | No |
| MH_ct_R2520.gif @($CERESHOME/erbelike/web/CER3.1P1/ s4g/gif/S4G_yyyymm_i/) | m | 0.17 | 1/month | N/A | permanent, No archive | No |
| MH_ct_R2520 @($CERESHOME/erbelike/web/CER3.1P1/ s4g/dat/S4G_yyyymm_i/) | m | 0.08 | 1/month | N/A | permanent, No archive | No |
| CER_ES4G_$SS3_$PS3_$CC3.yyyymm_j @($CERESHOME/erbelike/data/CERES/ES4G/ $SS3_$PS3/yyyy/mm/) | m | 0.032 | 1/month | N/A | DPO, Archive, rm | No |

a.	See Section 1.2 for information on variable data values.

If “(.met)” is written next to an expected output filename, then the metadata file with the identical filename and .met extension must exist.

Note:	yyyy 	- 4 digit year (See Runtime Parameters Table 1-4)

mm 	- 2 digit month {valid values: 01 .. 12} (See Runtime Parameters Table 1-4)
		# 	- SGE job number, generated upon job submission

i	- instrument ID (valid values: 1,2,3,4,5, or combination: 13, 245, etc.)

ct	- plotted parameter {valid values: ALB, CS_ALB, CS_LW, CS_SW, LW_CF, LW, NET_CF, SW_CF, SW}			j	- plot ID corresponding to ct parameter (valid values: 1,2,3,4,5,6,7,8,9.)

b.	Note:	m	- mandatory output

o	- optional output

c.	Note:	rm 	- remove

## Expected Temporary Files/Directories

Table 1-8.  Temporary Files Listing

| Directory | File Name |
| --- | --- |
| $CERESHOME/erbelike/runlogs/CER3.1P1 | TmpStatus |
| $CERESHOME/erbelike/runlogs/CER3.1P1 | TmpReport |
| $CERESHOME/erbelike/runlogs/CER3.1P1 | TmpUser |
| $CERESHOME/erbelike/runlogs/CER3.1P1 | MailFile |
| $CERESHOME/erbelike/CER3.1P1/data/scr/CER3.1_$SS3_$PS3_$CC3.yyyymm | ES4HSK.yyyymm |
| $CERESHOME/erbelike/CER3.1P1/data/scr/CER3.1_$SS3_$PS3_$CC3.yyyymm | GetAttr.temp.yyyymm |
| $CERESHOME/erbelike/CER3.1P1/data/scr/CER3.1_$SS3_$PS3_$CC3.yyyymm | MCFWrite.temp.yyyymm |
| $CERESHOME/erbelike/CER3.1P1/data/scr/CER3.1_$SS3_$PS3_$CC3.yyyymm | PLTF.yyyymm |
| $CERESHOME/erbelike/CER3.1P1/data/scr/CER3.1_$SS3_$PS3_$CC3.yyyymm | PLTFnn.yyyymm |
| $CERESHOME/erbelike/CER3.1P1/data/scr/CER3.1_$SS3_$PS3_$CC3.yyyymm | PSCHSK.yyyymm |
| $CERESHOME/erbelike/CER3.1P1/data/scr/CER3.1_$SS3_$PS3_$CC3.yyyymm | PTEMP.yyyymm |
| $CERESHOME/erbelike/CER3.1P1/data/scr/CER3.1_$SS3_$PS3_$CC3.yyyymm | RDB.yyyymm |
| $CERESHOME/erbelike/CER3.1P1/data/scr/CER3.1_$SS3_$PS3_$CC3.yyyymm | SLTFnn.yyyymm |
| $CERESHOME/erbelike/CER3.1P1/data/scr/CER3.1_$SS3_$PS3_$CC3.yyyymm | SOLDEC.yyyymm |
| $CERESHOME/erbelike/CER3.1P1/data/scr/CER3.1_$SS3_$PS3_$CC3.yyyymm | SSCHSK.yyyymm |
| $CERESHOME/erbelike/CER3.1P1/data/scr/CER3.1_$SS3_$PS3_$CC3.yyyymm | STEMP.yyyymm |
| $CERESHOME/erbelike/CER3.1P1/data/scr/CER3.1_$SS3_$PS3_$CC3.yyyymm | ShmMem |

Note:	yyyy	- 4 digit year (See Runtime Parameters Table 1-4)

mm	- 2 digit month {valid values: 01 .. 12} (See Runtime Parameters Table 1-4)

# PGEName:  CER3.2P1

CERES ERBE-like Monthly TOA Flux Averaging for Multiple Instruments.

## PGE Details

### Responsible Persons

Responsible persons are listed in the Subsystem Software Analysts Contacts Table 1-1.

### E-mail Distribution List

E-mail distribution list can be obtained from the primary contact listed in Table 1-1.

### Parent PGE(s)

Table 2-1.  Parent PGEs for CER3.2P1

| PGEName | Description |
| --- | --- |
| CER3.1P1 | CERES ERBE-like Monthly TOA Flux Averaging Main-Processor for FAPS+RAPS data for a Single Instrument. |

### Target PGE(s)

Table 2-2.  Target PGEs after CER3.2P1

| PGEName | Description |
| --- | --- |
| N/A | N/A |

## Operating Environment

### Runtime Parameters (List all Dynamic Parameters needed at Runtime)

Table 2-3.  Runtime Parameters for CER3.2P1

| Parametera | Description | Valid Values |
| --- | --- | --- |
| yyyy | CERDataDateYear | >= 1984 |
| mm | CERDataDateMonth | 01 .. 12 |
| scanmodeb | Process both FAPS and RAPS data togetherb | 1 |

a.	All character strings.

b.	Optional parameter since for PGE CER3.2P1, both FAPS and RAPS data will be processed, if available.  The value “1” will automatically be used for scanmode in the processing of these scripts.

### Environment Script Requirements

Refer to the CERES internal paper (Reference 3) for a detailed description of the CERES environment parameters.  For the current values of the Sampling Strategy and Production Strategy variables listed below, see “CERES DMT to DAAC Processing Requests.”  (URL:  http://ceres.larc.nasa.gov/dmt2daac.php )

One Environment Script is required and should define the following parameters:

SS3_2in	-	Sampling Strategy for CER3.1P1, see Production Request (Reference 4) Note: For Edition3/4, SS3_2in = $SAT1+$SAT2

SS3_2	-	Sampling Strategy for CER3.2P1, see Production Request (Reference 4) Note: For Edition3/4, SS3_2 = $SAT1+$SAT2

PS3_2in	-	Production Strategy for CER3.1P1, see Production Request (Reference 4)

PS3_2	-	Production Strategy for CER3.2P1, see Production Request (Reference 4)

CC3_2in	-	Configuration Code for CER3.1P1, see CM Database

CC3_2	-	Configuration Code for CER3.2P1, see CM Database

SW2	-	Software SCCR number for CER2.2P1, see CM Database

DATA2	-	Data SCCR number for CER2.2P1, see CM Database

SW3	-	Software SCCR number for CER3.2P1, see CM Database

DATA3	-	Data SCCR number for CER3.2P1, see CM Database

SAT	-	Satellite, see Production Request (Reference 4)

INST	-	Instrument, see Production Request (Reference 4)

PROD	-	Production mode, optional since ‘Yes’ by default

PGE	-	PGE name, optional and set to ‘CER3.2P1’

ERBELIKEHOME	-	can be different from but in production will be the same as CERESHOME

InputArchive	-	location of ASDC DPO, by default set to ‘/ASDC_archive’

SS3_2in, PS3_2in, and CC3_2in are the environment variables used to generate the single instrument processing output file names for each instrument as input for the multi-instrument processor.  SS3_2in, PS3_2in, and CC3_2in contain these values separated by a “+” character.

SS3_2in = SS31+SS32+...+SS3n-1+SS3n , where n = the number of instruments

PS3_2in = PS31+PS32+...+PS3n-1+PS3n , where n = the number of instruments

CC3_2in = CC31+CC32+...+CC3n-1+CC3n , where n = the number of instruments

Ex :	Given the instance of the input files (Terra-FM1_Edition2_024031.yyyymm

Aqua-FM3_Edition2_024031.yyyymm), the following must be set:

SS3_2in = Terra-FM1+Aqua-FM3

PS3_2in = Edition2+Edition2

CC3_2in = 024031+024031

The environment variables are used for output file names

SS3_2 = FM1+FM3

PS3_2 = Edition2

CC3_2 = 024031

The generated output instance is:  FM1+FM3_Edition2_024031.yyyymm

### Execution Frequency (daily, hourly, or monthly)

Monthly (1/month) - This PGE is to be processed once per month, when input is available.

### Memory/Disk Space/Time Requirements

Memory:	453 MB

Disk Space:	700 MB

Total Run Time:	5:20 minutes

### Restrictions Imposed in Processing Order

None, process when Input Data are available, (see Section 2.3).

## Processor Dependencies (Previous PGEs, Ingest Data)

### Input Dataset Name (#1):  DES9

The “$SS3i” environment variable represents the ith instrument’s Sampling Strategy.

The “$PS3i” environment variable represents the ith instrument’s Production Strategy.

The “$CC3i” environment variable represents the ith instrument’s Configuration Code.

- Directory Location/Inputs Expected (Including .met files, header files, etc.):

$CERESHOME/erbelike/data/CERES/DES9/$SS3i_$PS3i/yyyy/mm/		CER_DES9_$SS3i_$PS3i_$CC3i.yyyymm

CER_DES9_$SS3i_$PS3i_$CC3i.yyyymm.met

- Mandatory/Optional:  These files are mandatory.

Time Related Dependency:  The DataDate must match the runtime parameters:  yyyy, mm

Waiting Period:  None, Process when all input data are available.

Source of Information (Source is PGE name or Ingest Source):

Source PGE:  CER3.1P1

Alternate Data Set, if one exists (maximum waiting period):  None.

File Disposition after successful execution:  Remove, after successful completion.

Typical file size (MB):  100

## Operating Procedures (Procedure for each part of the processor’s elements)

Clear the output directories of files previously generated from this PGE (for this particular data instance) by executing script, clr_dir.PGE3.2P1.csh, with the runtime parameter data date:

At the command-line (>) type:

> cd $CERESHOME/erbelike/CER3.2P1/rcf

> clr_dir.PGE3.2P1.csh yyyymm

The production script, CER3.2P1.pl, references a Process Control File (PCF) containing the file names and paths for the PGE.  For manual processing, this PCF is created by first sourcing an ERBE-like-specific environment script mentioned in Section 2.2.2 above, then executing the PCF generator, gen_pcf.CER3.2P1.pl.  If processing via SGE, the PCF generator will be called via the driver script CER3.2P1-SGE_Driver.pl followed by the runtime parameters of Table 2-3, as shown in Section 2.2.1.

### How to Generate the PCF

The PCF generator requires two command line arguments: data date (yyyymm) and scan mode (= 1 by default, so as to include both FAPS+RAPS) (see Table 2-3).

At the command-line (>) type (Note: this step is not needed for SGE testing):

> gen_pcf.CER3.2P1.pl yyyymm

The following files are generated and located in $CERESHOME/erbelike/CER3.2P1/rcf/pcf/:

CER3.2P1_PCF_$SS3_2_$PS3_2_$CC3_2.yyyymm

CER3.2P1_PCF_$SS3_2_$PS3_2_$CC3_2.yyyymm.log

### How to Execute the Main-Processor

Before running the program, make sure the necessary executables are where they should be: 5 in $CERESHOME/erbelike/bin (sol_dec, pre_es4, es4, gen_es9hdf, and gen_es4hdf) and 2 in $CERESHOME/erbelike/CER3.2P1/bin (mtsa0 and mtsa3).  Also, to avoid segmentation faults with hdf file generation, run the ‘unlimit’ command at the prompt.  Then (if processing manually) execute the production script by typing the script name, CER3.2P1.pl, followed by a string which designates the instance of the data.  The string should be formatted, “Sampling Strategy”_”Production Strategy”_”Configuration Code”.”DataDate”.  The date parameter is formatted, yyyymm, where yyyy is the data year and mm is the data month (see Table 2-3).

At the command-line (>) type (Note: this step is not needed for SGE testing):

> CER3.2P1.pl $SS3_2’_’$PS3_2’_’$CC3_2’.yyyymm’

To run using SGE instead, type:

> CER3.2P1-SGE_Driver.pl –d yyyymm

To run using SGE for multiple sequential dates, type:

> CER3.2P1-SGE_Driver.pl –start y1m1 –end y2m2

where y1m1 and y2m2 are the start and end dates, respectively.

The CER3.2P1-SGE_Driver.pl script will search for the required input data files and any existing data product files for the requested data date(s) and time(s) provided.  If all the input data files are available and previously created output for this data date does not exist, the job will be submitted to the SGE queue.  However, if any mandatory data files are missing the script will not submit the job to the SGE queue.  Instead the information on which data files are missing or already exist can be found in the CER3.2P1_PCF_$SS3_2_$PS3_2_$CC3_2.yyyymm.log file.  Mandatory files may then be staged or existing output files can be deleted before trying again.

Here are the optional arguments for CER3.2P1-SGE_Driver.pl:

[-clean]	Delete any existing outputs that are encountered.

[-force]	Force the job to run regardless of any input scanning checks.

[-help]	Display this help message.

[-platform CPU]	Run the PGE on the platform designated by CPU.

[-nosummary]	Disable the creation of the summary file.

[-automatic]	Run in automatic (non-interactive) mode.

[-date YYYYMM]	Run the PGE on the data month specified by YYYYMM.

[-start YYYYMM]	Run the PGE starting on the data month specfied by YYYYMM.

[-end YYYYMM]	Run the PGE stopping on the data month specified by YYYYMM.

Below is a typical example of executing the driver script.

To run a single month on an x86 platform:

> CER3.2P1-SGE_Driver.pl –d 200912 –p x86

### Special Case Considerations

When running the directory-clearing script, the system may display a message that it cannot remove certain directories.  This occurs because, in addition to removing files that match the current data instance (i.e. instrument, data edition, configuration code, data date), the script also removes temporary output directories which should only exist only during run time (i.e., the scratch directory) or until the next data run instance (i.e., the Web output directories).  Failure to find these indicates either a successful last run or that this is the initial run for this data instance.

### Special Reprocessing Instructions

- All output files are opened with Status = NEW in the CER3.2P1 software.  These files must be removed before rerunning these procedures.  A script, which removes PGE created files, clr_dir.PGE3.2P1.csh, is located in directory $CERESHOME/erbelike/CER3.2P1/rcf.  Using data date as a command line argument:

> clr_dir.PGE3.2P1.csh yyyymm

See reprocessing requirements in “CERES DMT to DAAC Processing Requests” available on the Web at:  http://ceres.larc.nasa.gov/docs.php .

## Execution Evaluation

### Exit Codes

The processor CER3.2P1 terminates using the CERES-defined EXIT CODES for the Langley TRMM Information System (LaTIS) as seen in Table 2-4.  Other Exit Codes may appear from the program, which may be the result of a system, compiler, or Toolkit related error.  In these cases, contact the responsible person for assistance (see Table 1-1).

| Table 2-4. Exit Codes for CER3.2P1 |
| --- |
| Exit Code | Definition | Action |
| 0 | Normal Exit | Proceed normally |
| 198 | Fatal | “PCF missing error CER3.2P1_PCF_$SS3_2_$PS3_2_$CC3_2.yyyymm. Does NOT exist”. Inform the primary contact in Table 1-1. |
| 75 | Failure | “JSS invalid date error”. Check the Log Files and take the appropriate action (see Appendix B). |
| 151 | Failure | “PCF file write error”. Check the Log Files and take the appropriate action (see Appendix B). |
| 200 | Failure | “Non-specific PGE error”. Check the Log Files and take the appropriate action (see Appendix B). |
| 239 | Failure | “PGE HDF compression error. CER3.2P1 CER3.2P1_PCF_$SS3_2_$PS3_2_$CC3_2.yyyymm UNSUCCESSFULLY terminated in gen_es9hdf”. Check the Log Files and take the appropriate action (see Appendix B). |
| 239 | Failure | “PGE HDF compression error. CER3.2P1 CER3.2P1_PCF_$SS3_2_$PS3_2_$CC3_2.yyyymm UNSUCCESSFULLY terminated in gen_es4hdf”. Check the Log Files and take the appropriate action (see Appendix B). |
| 250 | Failure | “Non-specific plotting error CER3.2P1 CER3.2P1_PCF_$SS3_2_$PS3_2_$CC3_2.yyyymm UNSUCCESSFULLY terminated in plot_es4”. Check the Log Files and take the appropriate action (see Appendix B). |

### Screen Messages (Use Table format for large number of messages)

| Table 2-5. Screen Messages for execution of CER3.2P1 |
| --- |
| Message | Definition/Action |
| Cannot access <filename>: No such file or directory | From the clear directory script, clr_dir.PGE3_2, as a part of the Main-Processor. This message occurs when the script tries to remove an old output file that does not exist. Proceed normally. |
| CER3.2P1_PCF_$SS3_2_$PS3_2_$CC3_2.yyyymm SUCCESSFULLY terminated Exit Status = 0 | From running the production script, CER3.2P1, this message written to the screen signifies no fatal errors during production. Proceed normally. |
| PCF: CER3.2P1_PCF_$SS3_2_$PS3_2_$CC3_2.yyyymm DoesNOT exist Exit Status = 198 | This message is written to the screen signifying a fatal error has occurred. Refer to the Log files for more detailed information (see Appendix B). |
| CER3.2P1 CER3.2P1_PCF_$SS3_2_$PS3_2_$CC3_2.yyyymm UNSUCCESSFULLY terminated in sol_dec Exit Status = 200 | From running the production script, CER3.2P1, this message written to the screen signifies a fatal error has occurred. Refer to the Log files for more detailed information (see Appendix B). |
| CER3.2P1 CER3.2P1_PCF_$SS3_2_$PS3_2_$CC3_2.yyyymm UNSUCCESSFULLY terminated in pre_es4 Exit Status = 200 | From running the production script, CER3.2P1, this message written to the screen signifies a fatal error has occurred. Refer to the Log files for more detailed information (see Appendix B). |
| CER3.2P1 CER3.2P1_PCF_$SS3_2_$PS3_2_$CC3_2.yyyymm UNSUCCESSFULLY terminated in mtsa0 Exit Status = 200 | From running the production script, CER3.2P1, this message written to the screen signifies a fatal error has occurred. Refer to the Log files for more detailed information (see Appendix B). |
| CER3.2P1 CER3.2P1_PCF_$SS3_2_$PS3_2_$CC3_2.yyyymm UNSUCCESSFULLY terminated in mtsa3 Exit Status = 200 | From running the production script, CER3.2P1, this message written to the screen signifies a fatal error has occurred. Refer to the Log files for more detailed information (see Appendix B). |
| CER3.2P1 CER3.2P1_PCF_$SS3_2_$PS3_2_$CC3_2.yyyymm UNSUCCESSFULLY terminated in es4 Exit Status = 200 | From running the production script, CER3.2P1, this message written to the screen signifies a fatal error has occurred. Refer to the Log files for more detailed information (see Appendix B). |
| CER3.2P1 CER3.2P1_PCF_$SS3_2_$PS3_2_$CC3_2.yyyymm UNSUCCESSFULLY terminated in gen_es9hdf Exit Status = 239 | From running the production script, CER3.2P1, this message written to the screen signifies a fatal error has occurred. Refer to the Log files for more detailed information (see Appendix B). |
| CER3.2P1 CER3.2P1_PCF_$SS3_2_$PS3_2_$CC3_2.yyyymm UNSUCCESSFULLY terminated in gen_es4hdf Exit Status = 239 | From running the production script, CER3.2P1, this message written to the screen signifies a fatal error has occurred. Refer to the Log files for more detailed information (see Appendix B). |
| CER3.2P1 CER3.2P1_PCF_$SS3_2_$PS3_2_$CC3_2.yyyymm UNSUCCESSFULLY terminated in plot_es4 Exit Status = 250 | From running the production script, CER3.2P1, this message written to the screen signifies a fatal error has occurred. Refer to the Log files for more detailed information (see Appendix B). |

### Log and Status Files Results (Include ALL Log Files)

The Log files contain all error and/or status messages produced by the PGE.  The files are located in directory: $CERESHOME/erbelike/runlogs/CER3.2P1.

#### Report Log File:  CER3.2P1_LogReport_$SS3_2_$PS3_2_$CC3_2.yyyymm

The Report Log File contains the ERBE-like related messages.  These messages may be strictly informative (Error Type = Status or Warning) or may indicate a fatal condition that results in premature PGE termination (Error Type = Fatal).  A comprehensive list of these messages, that can be generated during the execution of the PGE, is contained in Appendix B.

#### Status Log File:  CER3.2P1_LogStatus_$SS3_2_$PS3_2_$CC3_2.yyyymm

The Status Log File contains all messages created by the Toolkit.  If an abnormal exit is encountered by the PGE, this file should be examined for ‘_F_’, fatal message type.  The responsible person should be advised (see Table 1-1).

#### User Log File:  CER3.2P1_LogUser_$SS3_2_$PS3_2_$CC3_2.yyyymm

The User Log File is not used at this time, but exists to satisfy the Toolkit requirements.  Typically the _U_ and _N_ (User information and Notice) will be written to User Log File and Status Log File.

### Solutions to Possible Problems

### Conditions for Subsystem and/or Target PGE(s) Terminal Failure (Halt all further processing)

- Subsystem Termination

Please refer to Appendix B for a descriptive list of all errors and the result of those errors.

Target PGE Termination

N/A

## Expected Output Dataset(s)

The expected output datasets (including all expected web files) are listed below for each instance of the PGE.  This PGE is expected to process once a month.

| Table 2-6. Expected Output File Listing for CER3.2P1 If “(.met)” is written next to an expected Output Filename in the following table, then the metadata file must exist with the identical file name and .met extension. |
| --- |
| File Namea/Directory | m/ob | File Size (MB) | Freq/ PGE | Target PGE | Destinationc | Available Through Ordering Tool |
| CER3.2P1_PCF_$SS3_2_$PS3_2_$CC3_2.yyyymm @($CERESHOME/erbelike/CER3.2P1/rcf/pcf/) | m | 0.04 | 1/month | N/A | Archive, rm | No |
| CER3.2P1_PCF_$SS3_2_$PS3_2_$CC3_2.yyyymm.log @($CERESHOME/erbelike/CER3.2P1/rcf/pcf/) | m | 0.008 | 1/month | N/A | Archive, rm | No |
| CER3.2P1_$SS3_2_$PS3_2_$CC3_2.yyyymm.summary or CER3.2P1_$SS3_2_$PS3_2_$CC3_2.y1m1-y2m2.summary @($CERESHOME/erbelike/CER3.2P1/rcf/pcf/summary) | o | 0.005 | 1/run | N/A | permanent, No archive | No |
| CER3.2P1_LogReport_$SS3_2_$PS3_2_$CC3_2.yyyymm @($CERESHOME/erbelike/runlogs/CER3.2P1/) | m | 0.2 | 1/month | N/A | Archive, rm | No |
| CER3.2P1_LogStatus_$SS3_2_$PS3_2_$CC3_2.yyyymm @($CERESHOME/erbelike/runlogs/CER3.2P1/) | m | 0.04 | 1/month | N/A | Archive, rm | No |
| CER3.2P1_LogUser_$SS3_2_$PS3_2_$CC3_2.yyyymm @($CERESHOME/erbelike/runlogs/CER3.2P1/) | m | 0.024 | 1/month | N/A | Archive, rm | No |
| CER3.2P1_$SS3_2_$PS3_2_$CC3_2.yyyymm.o# @($CERESHOME/erbelike/sge_logs/CER3.2P1) | m |  | 1/month | N/A | Archive, rm | No |
| CER_DES9_$SS3_2_$PS3_2_$CC3_2.yyyymm (.met) @($CERESHOME/erbelike/data/CERES/DES9/$SS3_2_$PS3_2/yyyy/mm/) | m | 180 | 1/month | N/A | Archive, rm | No |
| CER_ES9_$SS3_2_$PS3_2_$CC3_2.yyyymm (.met) @($CERESHOME/erbelike/data/CERES/ES9/$SS3_2_$PS3_2/yyyy/mm/) | m | 100 | 1/month | N/A | DPO, Archive, rm | Yes |
| CER_DMSG_$SS3_2_$PS3_2_$CC3_2.yyyymm (.met) @($CERESHOME/erbelike/data/CERES/DMSG/$SS3_2_ $PS3_2/yyyy/mm/) | m | 0.05 | 1/month | N/A | DPO, Archive, rm | No |
| CER_DQCA_$SS3_2_$PS3_2_$CC3_2.yyyymm (.met) @($CERESHOME/erbelike/data/CERES/DQCA/$SS3_2_$PS3_2/yyyy/mm/) | m | 0.1 | 1/month | N/A | DPO, Web, Archive, rm | No |
| CER_DQCB_$SS3_2_$PS3_2_$CC3_2.yyyymm (.met) @($CERESHOME/erbelike/data/CERES/DQCB/$SS3_2_$PS3_2/yyyy/mm/) | m | 0.2 | 1/month | N/A | DPO, Web, Archive, rm | No |
| CER_DQCC_$SS3_2_$PS3_2_$CC3_2.yyyymm (.met) @($CERESHOME/erbelike/data/CERES/DQCC/$SS3_2_$PS3_2/yyyy/mm/) | m | 0.05 | 1/month | N/A | DPO, Web, Archive, rm | No |
| CER_DQCG_$SS3_2_$PS3_2_$CC3_2.yyyymm (.met) @($CERESHOME/erbelike/data/CERES/DQCG/$SS3_2_ $PS3_2/yyyy/mm/) | m | 0.12 | 1/month | N/A | DPO, Web, Archive, rm | No |
| CER_DES4_$SS3_2_$PS3_2_$CC3_2.yyyymm (.met) @($CERESHOME/erbelike/data/CERES/DES4/$SS3_2_$PS3_2/yyyy/mm/) | m | 17 | 1/month | N/A | Archive, rm | No |
| CER_ES4_$SS3_2_$PS3_2_$CC3_2.yyyymm (.met) @($CERESHOME/erbelike/data/CERES/ES4/$SS3_2_$PS3_2/yyyy/mm/) | m | 9 | 1/month | N/A | DPO, Archive, rm | Yes |
| CER_ES4G1_$SS3_2_$PS3_2_$CC3_2.yyyymm (.met) @($CERESHOME/erbelike/data/CERES/ES4G1/$SS3_2_ $PS3_2/yyyy/mm/) | m | 3.5 | 1/month | N/A | DPO, Archive, rm | No |
| CER_ES4G2_$SS3_2_$PS3_2_$CC3_2.yyyymm (.met) @($CERESHOME/erbelike/data/CERES/ES4G2/$SS3_2_ $PS3_2/yyyy/mm/) | m | 6.9 | 1/month | N/A | DPO, Archive, rm | No |
| CER_ES4G3_$SS3_2_$PS3_2_$CC3_2.yyyymm (.met) @($CERESHOME/erbelike/data/CERES/ES4G3/$SS3_2_ $PS3_2/yyyy/mm/) | m | 2.3 | 1/month | N/A | DPO, Archive, rm | No |
| CER_ES4G4_$SS3_2_$PS3_2_$CC3_2.yyyymm (.met) @($CERESHOME/erbelike/data/CERES/ES4G4/$SS3_2_ $PS3_2/yyyy/mm/) | m | 5.7 | 1/month | N/A | DPO, Archive, rm | No |
| MH_ct_R2520.gif @($CERESHOME/erbelike/web/CER3.2P1/s4g/gif/ S4G_yyyymm_i/) | m | 0.168 | 1/month | N/A | permanent, No archive | No |
| MH_ct_R2520 @($CERESHOME/erbelike/web/CER3.2P1/s4g/dat/ S4G_yyyymm_i/) | M | 0.08 | 1/month | N/A | permanent, No archive | No |
| DQCG_Stats_$SS3_2_$PS3_2.web @($CERESHOME/erbelike/web/CER3.2P1/es4_stats/data/) | M | .008 | 1/sat | N/A | permanent, No archive | No |
| Monthly_LW_Stats_$SS3_2_$PS3_2.web @($CERESHOME/erbelike/web/CER3.2P1/es4_stats/data/) | M | .008 | 1/sat | N/A | permanent, No archive | No |
| Monthly_SW_Stats_$SS3_2_$PS3_2.web @($CERESHOME/erbelike/web/CER3.2P1/es4_stats/data/) | M | .008 | 1/sat | N/A | permanent, No archive | No |
| Monthly_Stats_log_$SS3_2_$PS3_2.yyyymm @($CERESHOME/erbelike/web/CER3.2P1/es4_stats/data/) | M | .008 | 1/month | N/A | permanent, No archive | No |
| CER_ES4G_$SS3_2_$PS3_2_$CC3_2.yyyymm_j @($CERESHOME/erbelike/data/CERES/ES4G/ $SS3_2_$PS3_2/yyyy/mm/) | M | 0.032 | 1/month | N/A | DPO, Archive, rm | No |

a.	See Section 2.2 for information on variable data values.

If “(.met)” is written next to an expected output filename, then the metadata file with the identical filename and .met extension must exist.

Note:	yyyy 	- 4 digit year (See Runtime Parameters Table 2-3)

mm 	- 2 digit month {valid values: 01 .. 12} (See Runtime Parameters Table 2-3)
		# 	- SGE job number, generated upon job submission

i	- instrument ID (valid values: 1,2,3,4,5, or combination: 13, 245, etc.)

ct	- plotted parameter {valid values: ALB, CS_ALB, CS_LW, CS_SW, LW_CF, LW, NET_CF, SW_CF, SW}

j	- plot ID corresponding to ct parameter (valid values: 1,2,3,4,5,6,7,8,9)

b.	Note:	m	- mandatory output

o	- optional output

c.	Note:	rm 	- remove

## Expected Temporary Files/Directories.

Table 2-7.  Temporary Files Listing

| Directory | File Name |
| --- | --- |
| $CERESHOME/erbelike/runlogs/CER3.2P1 | TmpStatus |
| $CERESHOME/erbelike/runlogs/CER3.2P1 | TmpReport |
| $CERESHOME/erbelike/runlogs/CER3.2P1 | TmpUser |
| $CERESHOME/erbelike/runlogs/CER3.2P1 | MailFile |
| $CERESHOME/erbelike/CER3.2P1/data/scr/CER3.2P1_$SS3_2_$PS3_2_$CC3_2.yyyymm | ES4HSK.yyyymm |
| $CERESHOME/erbelike/CER3.2P1/data/scr/CER3.2P1_$SS3_2_$PS3_2_$CC3_2.yyyymm | M9.yyyymm |
| $CERESHOME/erbelike/CER3.2P1/data/scr/CER3.2P1_$SS3_2_$PS3_2_$CC3_2.yyyymm | RDB.yyyymm |
| $CERESHOME/erbelike/CER3.2P1/data/scr/CER3.2P1_$SS3_2_$PS3_2_$CC3_2.yyyymm | ShmMem |
| $CERESHOME/erbelike/CER3.2P1/data/scr/CER3.2P1_$SS3_2_$PS3_2_$CC3_2.yyyymm | SOLDEC.yyyymm |

Note:	yyyy	- 4 digit year (See Runtime Parameters Table 2-3)

mm	- 2 digit month {valid values: 01 .. 12} (See Runtime Parameters Table 2-3)

References

- CERES Data Management System, Software Requirements Documents, Release 1, Version 1, January, 1995.

- CERES ERBE-like Inversion to Instantaneous Top-of-Atmosphere (TOA) Fluxes Subsystem 2.0 Release 6 Operator’s Manual.

- Reference “Sampling Strategy, Production Strategy, and Configuration Code Implementation at the Langley TRMM and Terra Information System (LATIS)” internal paper for detail description of the CERES environment parameters.  URL:  http://ceres.larc.nasa.gov/Internal/intern_docs.php

- Reference “DMT to DAAC Production Request.”  URL: http://ceres.larc.nasa.gov/dmt2daac.php

Acronyms and Abbreviations

ASDC	Atmospheric Science Data Center

CERES	Clouds and the Earth’s Radiant Energy System

CM	Configuration Management

DAAC	Distributed Active Archive Center

DB	Data Base

EOS	Earth Observing System

EOS-AM	EOS Morning Crossing (Ascending) Mission

EOS-PM	EOS Afternoon Crossing (Descending) Mission

ERBE	Earth Radiation Budget Experiment

ERBS	Earth Radiation Budget Satellite

HDF 	Hierarchical Data Format

LaRC	Langley Research Center

LaTIS	Langley TRMM Information System

LW	Longwave

MB	Mega Byte

met	metadata file (or .met)

m	microns

MOA	Meteorological, Ozone, and Aerosol

N/A	Not Applicable

NASA	National Aeronautics and Space Administration

NOAA	National Oceanic and Atmospheric Administration

PCF	Process Control File

PGE	Product Generation Executives

PSF	Point Spread Function

PRE_SSF	Preliminary Single Satellite CERES Footprint TOA and Surface Fluxes

QC	Quality Control

SSAI	Science Systems and Applications, Inc

SMF	Status Message File

SSF	Single Satellite CERES Footprint TOA and Surface Fluxes, Clouds

SW	Shortwave

TOA	Top of the Atmosphere, Top of Atmosphere

TRMM	Tropical Rainfall Measuring Mission

VD	Validation Days

Error Messages

Appendix B contains a list of messages that can be generated during the execution of PGEs CER2.3P1 through CER3.2P1.  These messages are used to inform the operator or analyst of specific circumstances encountered during data processing.  These messages may be strictly informative (Error Type = Status or Warning), or may indicate a fatal condition that results in premature PGE termination (Error Type = Fatal).  All messages are written to the LogReport file of the processing instance.

Table B-1 contains a list of the diagnostic messages for PGEs CER3.1P1 and CER3.2P1.  Each table entry includes a message number, the message content, the source Module, the Error Type and the recommended action that should be taken when the message is encountered.

Operator Instructions:

If a PGE prematurely terminates, then take the following steps:

- Look at the last few records on the LogStatus file.

- Find the error message in the following Error Message listing(s), and follow the appropriate ACTION.

- If an error message is not in the LogStatus File, then repeat steps 1 and 2 using the LogReport File.

- If no information is derived, then call the responsible person in Table 1-1.

- If the appropriate ACTION failed, then call the responsible person in Table 1-1.

- In all cases, log all steps that were taken after the PGE failure, and send a copy to the responsible person listed in Table 1-1.

Error Messages for PGEs CER3.1P1 and CER3.2P1

Errors for Subsystem 3.0, PGEs CER3.1P1 and CER3.2P1, are listed in numerical order.  Variables in Action Items and Table B-1 are defined as follows:

PGEx = PGE name (CER3.1P1 / CER3.1 or CER3.2P1)

SCRdir = $CERESHOME/erbelike/PGEx/data/scr

yyyy = Data year (> 1985)

mm = Data month (01 .. 12)

dd = Data day (01 .. 31)

nn = 01 .. 36

The following are Action Items for PGEs CER3.1P1 through CER3.2P1.  Action Items appear in the Action column as bold type.

  - Verify SCRdir/PGEx_$SS3_$PS3_$CC3.yyyymm/ES4HSK.yyyymm is valid.

  - Verify SCRdir/CER3.1_$SS3_$PS3_$CC3.yyyymm/PLTFnn.yyyymm is valid.

  - Verify SCRdir/CER3.1_$SS3_$PS3_$CC3.yyyymm/PSCHSK.yyyymm is valid.

  - Verify SCRdir/PGEx_$SS3_$PS3_$CC3.yyyymm/RDB.yyyymm is valid.

  - Verify SCRdir/ CER3.1_$SS3_$PS3_$CC3.yyyymm/SLTFnn.yyyymm is valid.

  - Verify SCRdir/PGEx_$SS3_$PS3_$CC3.yyyymm/SOLDEC.yyyymm is valid.

  - Verify SCRdir/CER3.1_$SS3_$PS3_$CC3.yyyymm/SSCHSK.yyyymm is valid.

  - Verify $CERESHOME/erbelike/data/CERES/CXDR/$SS2_$PS2/yyyy/mm/
CER_CXDR_$SS2_$PS2_$CC2.yyyymmdd is valid for both overlaps.

  - Verify $CERESHOME/erbelike/data/CERES/DES9/$SS31_$PS31/yyyy/mm/
CER_DES9_$SS31_$PS31_$CC31.yyyymm is valid for first input.

  - Verify $CERESHOME/erbelike/data/CERES/DES9/$SS32_$PS32/yyyy/mm/
CER_DES9_$SS32_$PS32_$CC32.yyyymm is valid for the 2nd input.

- See $CERESHOME/erbelike/data/CERES/DMSG/$SS3_$PS3/yyyy/mm/
CER_DMSG_$SS3_$PS3_$CC3.yyyymm for further information.

- See $CERESHOME/erbelike/data/CERES/DQCS/$SS3_$PS3/yyyy/mm/

CER_DQCS_$SS3_$PS3_$CC3.yyyymm for further information.

- See $CERESHOME/erbelike/data/CERES/DQCD/$SS3_$PS3/yyyy/mm/

CER_DQCD_$SS3_$PS3_$CC3.yyyymm for further information.

| Table B-1. PGE CER3.1P1 & CER3.2P1 Error Messages |
| --- |
| Message | Module Name | Error Type | Action |
| mtsa1(): Notice ... Beginning of mtsa1 software. | mtsa1 | Notice | None |
| mtsa0(): Notice ... Beginning of mtsa0 software. | mtsa0 | Notice | None |
| mtsa3(): Notice ... Beginning of mtsa3 software. | mtsa3 | Notice | None |
| MESSAGE NUMBER : 1 ddbint():Error ... Opening House Keeping File. | ddbint | Fatal | (C,a) |
| MESSAGE NUMBER : 1 filint(): Error ... Opening data file. | es4 | Fatal | (D,a) |
| MESSAGE NUMBER : 1 initl(): Error ... Opening data file. | es4 | Fatal | Refer to MSG files for file ID and other information regarding this error. (a) |
| MESSAGE NUMBER : 1 s4g(): Error ... Opening data file. | es4 | Fatal | Verify all four $CERESHOME/erbelike/data/CERES/ES4Gn/$SS3_$PS3/yyyy/mm/CER_ES4Gn_$SS3_$PS3_$CC3.yyyymm files exist and are valid for n = 1 .. 4 (a) |
| MESSAGE NUMBER : 1 initms(): Opening House Keeping File. | mtsa1 | Fatal | (G,a) |
| MESSAGE NUMBER : 1 predrv(): Error ... Opening data file. | pre_es4 | Fatal | (A,F,a) |
| MESSAGE NUMBER : 1 readsd(): Error ... Opening Latitude File. | mtsa1 | Fatal | (E,a) |
| MESSAGE NUMBER : 1 soldec(): Error ... Opening Solar Declination File. | sol_dec | Fatal | (F,a) |
| MESSAGE NUMBER : 1 srtltf(): Error ... Opening PTemp File. | ddbsrt | Fatal | Verify SCRdir/ CER3.1_$SS3_$PS3_$CC3.yyyymm/PTEMP.yyyymm exists and is valid. (a,b) |
| MESSAGE NUMBER : 1 srtltf(): Error ... Opening PLTF File. | ddbsrt | Fatal | (B,a,b) |
| MESSAGE NUMBER : 1 srtltf(): Error ... Opening STemp File. | ddbsrt | Fatal | Verify SCRdir/ CER3.1_$SS3_$PS3_$CC3.yyyymm/STEMP.yyyymm exists and is valid. (a,b) |
| MESSAGE NUMBER : 1 ssortf(): Error ... Opening Latitude File. | ddbsrt | Fatal | (B,a,b) |
| MESSAGE NUMBER : 1 ssortf(): Error ... Opening Latitude File. | ddbsrt | Fatal | (E,a,b) |
| MESSAGE NUMBER : 1 ssumrp(): Error ... Opening Message File MSGOUT. | ddbsrt | Fatal | Verify $CERESHOME/erbelike/data/CERES/DQCS/$SS3_$PS3/yyyy/mm/CER_DQCS_$SS3_$PS3_$CC3.yyyymm is valid. (a) |
| MESSAGE NUMBER : 1 ssvlhk(): Error ... Opening House Keeping File. | ddbsrt | Fatal | (C,a,b) |
| MESSAGE NUMBER : 1 ssvlot(): Error ... Opening House Keeping File. | ddbsrt | Fatal | (G,a,b) |
| MESSAGE NUMBER : 1 sueopn(): Error ... Opening House Keeping File. | ddbuer | Fatal | (C,a) |
| MESSAGE NUMBER : 1 sueopn(): Error ... Opening Latitude File. | ddbuer | Fatal | (B,a) |
| MESSAGE NUMBER : 1 sueopn(): Error ... Opening Overlap File. | ddbuer | Fatal | (H,a) |
| MESSAGE NUMBER : 1 suopdb(): Error ... Opening House Keeping File. | ddbupd | Fatal | (C,a,c) |
| MESSAGE NUMBER : 1 suopdb(): Error ... Opening Latitude File. | ddbupd | Fatal | (B,a,c) |
| MESSAGE NUMBER : 1 suopdb(): Error ... Opening Overlap File. | ddbupd | Fatal | (H,a,c) |
| MESSAGE NUMBER : 1 suopin(): Error ... Opening Inversion EID6 File. | ddbupd | Fatal | Verify the $CERESHOME/erbelike/data/CERES/EID6/$SS2_$PS2/yyyy/mm/CER_EID6_$SS2_$PS2_$CC2.yyyymmdd (CER3.1P1 input) file exists and is valid. (a,c) |
| MESSAGE NUMBER : 1 suwrep(): Error ... Opening QC Report File. | ddbuer | Fatal | Verify $CERESHOME/erbelike/data/CERES/DQCX/$SS3_$PS3/yyyy/mm/CER_DQCX_$SS3_$PS3_$CC3.yyyymm is valid. (a) |
| MESSAGE NUMBER : 1 suwrep(): Error ... Opening QC Report File. | ddbupd | Fatal | Verify the $CERESHOME/erbelike/data/CERES/DQCD/$SS3_$PS3/yyyy/mm/CER_DQCD_$SS3_$PS3_$CC3.yyyymm (CER3.1P1 output) file exists and is valid. (a,c) |
| MESSAGE NUMBER : 2 ddbuer(): Error ... Reading Overlap File. | ddbuer | Fatal | (H,a) |
| MESSAGE NUMBER : 2 fildrv(): Error ... Reading data file. | es4 | Fatal | (D,a) |
| MESSAGE NUMBER : 2 initl(): Error ... Reading data file. | es4 | Fatal | (A,a) |
| MESSAGE NUMBER : 2 initl(): Error ... Reading data file. | es4 | Fatal | (A,a) |
| MESSAGE NUMBER : 1 initms(): Error ... Opening House Keeping File. | mtsa1 | Fatal | (G,a) |
| MESSAGE NUMBER : 2 predrv(): Error ... Reading data file. | pre_es4 | Fatal | (F,a) |
| MESSAGE NUMBER : 2 readat(): Error ... Reading data file. | es4 | Fatal | Verify $CERESHOME/erbelike/data/CERES/DES4/$SS3_$PS3/yyyy/mm/CER_DES4_$SS3_$PS3_$CC3.yyyymm (CER3.1P1 output) is valid for reading. (a) |
| MESSAGE NUMBER : 2 readsd(): Error ... Reading House Keeping File. | mtsa1 | Fatal | (G,a) |
| MESSAGE NUMBER : 2 readsd(): Error ... Reading Latitude File. | mtsa1 | Fatal | (E,a) |
| MESSAGE NUMBER : 2 readsd(): Error ... Reading Latitude File. | mtsa1 | Fatal | (E,a) |
| MESSAGE NUMBER : 2 s4g(): Error ... Reading data file. | es4 | Fatal | Verify $CERESHOME/erbelike/data/CERES/DES4/$SS3_$PS3/yyyy/mm/CER_DES4_$SS3_$PS3_$CC3.yyyymm (CER3.1P1 output) is valid for reading. (a) |
| MESSAGE NUMBER : 2 soldec(): Error ... Using Solar Declination File. | sol_dec | Fatal | Toolkit routines PGS_CBP_Earth_CB_Vector or PGS_CBP_SolarTimeCoords returned unfavorable status. (a) |
| MESSAGE NUMBER : 2 srtltf(): Error ... Reading PLTF File. | ddbsrt | Fatal | (B,a,b) |
| MESSAGE NUMBER : 2 sucldb(): Error ... Reading House Keeping File. | ddbupd | Fatal | (C,a,c) |
| MESSAGE NUMBER : 2 suecls(): Error ... Reading House Keeping File. | ddbuer | Fatal | (C,a) |
| MESSAGE NUMBER : 2 suopdb(): Error ... Reading House Keeping File. | ddbupd | Fatal | (C,a,c) |
| MESSAGE NUMBER : 2 sueopn(): Error ... Reading House Keeping File. | ddbuer | Fatal | (C,a) |
| MESSAGE NUMBER : 2 sueopn(): Error ... Opening Overlap File. | ddbuer | Fatal | (H,a) |
| MESSAGE NUMBER : 2 ddbint(): Error ... Writing House Keeping File. | ddbint | Fatal | (C,a) |
| MESSAGE NUMBER : 3 ddbuer(): Error ... Writing Latitude File. | ddbuer | Fatal | (B,a) |
| MESSAGE NUMBER : 3 es4(): Error ... Writing Namelist NAMGLB. | es4 | Fatal | Verify $CERESHOME/erbelike/data/CERES/DMSG/$SS3_$PS3/yyyy/mm/CER_DMSG_$SS3_$PS3_$CC3.yyyymm (CER3.1P1 output) is valid. |
| MESSAGE NUMBER : 3 fildrv(): Error ... Writing data file. | es4 | Fatal | Verify temporary file is valid for writing. (a) |
| MESSAGE NUMBER : 3 initl(): Error ... Writing data file. | es4 | Fatal | Verify $CERESHOME/erbelike/data/CERES/DES4/$SS3_$PS3/yyyy/mm/CER_DES4_$SS3_$PS3_$CC3.yyyymm (CER3.1P1) output file is valid. (a) |
| MESSAGE NUMBER : 3 polar(): Error ... Writing data file. | pre_es4 | Fatal | (A,a) |
| MESSAGE NUMBER : 3 predrv(): Error ... Writing data file. | pre_es4 | Fatal | Verify $CERESHOME/erbelike/data/CERES/DMSG/$SS3_$PS3/yyyy/mm/CER_DMSG_$SS3_$PS3_$CC3.yyyymm (CER3.1P1 output) is valid. |
| MESSAGE NUMBER : 3 sinhsk(): Error ... Writing House Keeping File. | ddbint | Fatal | (C,a) |
| MESSAGE NUMBER : 3 sucldb(): Error ... Writing House Keeping File. | ddbupd | Fatal | (C,a,c) |
| MESSAGE NUMBER : 3 sucldb(): Error ... Writing Overlap File. | ddbupd | Fatal | (H,a,c) |
| MESSAGE NUMBER : 3 suecls(): Error ... Writing House Keeping File. | ddbuer | Fatal | (C,a) |
| MESSAGE NUMBER : 3 suopdb(): Error ... Writing Overlap File. | ddbupd | Fatal | (H,a,c) |
| MESSAGE NUMBER : 3 suscan(): Error ... Writing Latitude File. | ddbupd | Fatal | (B,a,c) |
| MESSAGE NUMBER : 3 suscan(): Error ... Writing Overlap File. | ddbupd | Fatal | (H,a,c) |
| MESSAGE NUMBER : 3 weight(): Error ... Writing data file. | pre_es4 | Fatal | (A,a) |
| MESSAGE NUMBER : 3 wrtrec(): Error ... Writing data file. | es4 | Fatal | Verify $CERESHOME/erbelike/data/CERES/DES4/$SS3_$PS3/yyyy/mm/CER_DES4_$SS3_$PS3_$CC3.yyyymm (CER3.1P1) output file is valid. (a) |
| MESSAGE NUMBER : 6 suscan(): Warning ... Region Number out of Range. | ddbupd | Warning | Program continues to process the next record. (a,c) |
| MESSAGE NUMBER : 8 suopdb(): Error ... Overlap Data Already Processed. | ddbupd | Fatal | (C,a) |
| MESSAGE NUMBER : 8 sueopn(): Error ... Overlap Data Already Processed. | ddbuer | Fatal | (H, a) |
| MESSAGE NUMBER : 9 nest(): Error ... Unable to Find Polar Flag. | es4 | Fatal | Calculations done with constants defined within the es4 program. (a) |
| MESSAGE NUMBER : 12 npolar(): Warning ... Proccessing Daily data. | es4 | Warning | (D,a) |
| MESSAGE NUMBER : 12 npolar(): Warning ... Proccessing Monthly Hourly data. | es4 | Warning | (D,a) |
| MESSAGE NUMBER : 12 npolar(): Warning ... Proccessing Monthly(Day) data. | es4 | Warning | Program does not process Monthly (Day) Grand Monthly Shortwave and Solar Inc. Values. (a) |
| MESSAGE NUMBER : 12 npolar(): Warning ... Proccessing Monthly(Hour) data. | es4 | Warning | Program does not process Monthly (Hour) Grand Monthly Shortwave and Solar Inc. Values. (a) |
| MESSAGE NUMBER : 12 polar(): Warning ... Proccessing Daily data. | es4 | Warning | Program skips processing Daily SW and Solar Inc and continues to MonthlyHourly. (D,a) |
| MESSAGE NUMBER : 12 polar(): Warning ... Proccessing Monthly Hourly data. | es4 | Warning | Check MSG files for further information. (D,a) |
| MESSAGE NUMBER : 12 polar(): Warning ... Proccessing Monthly(Day) data. | es4 | Warning | Program skips processing Monthly(Day) SW and Solar Inc and continues to Monthly(Hour). Check MSG files for further information. (D,a) |
| MESSAGE NUMBER : 12 polar(): Warning ... Proccessing Monthly(Hour) data. | es4 | Warning | Program skips processing Monthly(Hour) SW and Solar Inc and continues to Daily. Check MSG files for further information. (D,a) |
| MESSAGE NUMBER : 14 ssrdnl(): Error ... Start File Greater then End File. | ddbsrt | Fatal | Calculations done with constants defined within the ddbsrt program. (a,b) |
| MESSAGE NUMBER : 14 ssrdnl(): Error ... Value out of Range. | ddbsrt | Fatal | Verify PCF values for ID 601 (year), 603 (month), and 607 (spacecraft number). (a,b) |
| MESSAGE NUMBER : 16 suopdb(): Error ... Opening Latitude File. | ddbupd | Fatal | This error will accompany one or more of the “MESSAGE 1 FROM SUOPDB: ERROR OPENING LATITUDINAL FILE PLTFnn” error messages. Follow the recommended action for them. |
| MESSAGE NUMBER : 16 sueopn(): Error ... Opening Latitude File. | ddbuer | Fatal | (E,a) |
| MESSAGE NUMBER : 20 ddbuer(): Notice ... Number of Records Processed. | ddbuer | Notice | None |
| MESSAGE NUMBER : 21 initms(): Warning ... Unable to Sort Latitude File. | mtsa1 | Warning | (E,a) |
| MESSAGE NUMBER : 23 initms(): Warning ... Unable to Sort Latitude File. | mtsa1 | Warning | (G,a) |
| MESSAGE NUMBER : 24 sueopn(): Notice ... No Overlap Data. | ddbuer | Notice | Program continues processing. (H,a) |
| MESSAGE NUMBER : 101 filesc(): Notice ... Science Product File. | mtsa1 | Notice | None. |
| MESSAGE NUMBER : 101 inutil(): Error ... Opening Error Message File. | inutil | Fatal | Verify output $CERESHOME/erbelike/data/CERES/DMSG/$SS3_$PS3/yyyy/mm/CER_DMSG_$SS3_$PS3_$CC3.yyyymm (CER3.1P1) |
| MESSAGE NUMBER : 101 filesc(): Notice ... Science Product File. | mtsa3 | Notice | None. |
| MESSAGE NUMBER : 102 filesc(): Notice ... Regional Database File. | mtsa1 mtsa3 | Notice | None. |
| MESSAGE NUMBER : 106 initsc(): Warning ... Error Determining Datadate Month. | initsc | Warning | Verify PCF value for ID 603 (month). (a) |
| MESSAGE NUMBER : 106 minit(): Error ... Month is Not Between 1 and 12. | mtsa0 | Fatal | Verify PCF value for ID 603 (month). (a) |
| MESSAGE NUMBER : 107 initsc(): Warning ... Error Determining Datadate Year. | initsc | Warning | Verify PCF value for ID 601 (year). (a) |
| MESSAGE NUMBER : 107 minit(): Error ... Year is Not Greater Then 0. | mtsa0 | Fatal | Verify PCF value for ID 601 (year). (a) |
| MESSAGE NUMBER : 108 initsc(): Warning ... Error Determining Resolution. | initsc | Warning | Resolution set as constant in calling program. (a) |
| MESSAGE NUMBER : 109 ldtbls(): Warning ... Error Getting Table Data. | ldtbls | Warning | Verify $CERESHOME/erbelike/data/ancillary/static/CER3.1P1/ISDM2.YYYYMMDD exists and is valid. (F,a) |
| MESSAGE NUMBER : 109 mldtbl(): Error ... Uable to Proccess Table Files. | mtsa0 | Fatal | (F,a) |
| MESSAGE NUMBER : 110 mldtbl(): Error ... Uable to Proccess Table Files. | mtsa0 | Fatal | (F,a) |
| MESSAGE NUMBER : 112 mldtbl(): Error ... Uable to Proccess Table Files. | mtsa0 | Fatal | (F,a) |
| MESSAGE NUMBER : 113 mldtbl(): Error ... Uable to Proccess Table Files. | mtsa0 | Fatal | Data year is not correct. (F,a) |
| MESSAGE NUMBER : 114 mfiles(): Notice ... Science Product File. | mtsa0 | Status | None. |
| MESSAGE NUMBER : 117 stddev(): Notice ... Unable to Calculate Std Dev. | stddev | Status | Cannot take the square root, so the program sets sigma to a constant value. |
| MESSAGE NUMBER : 117 stdev1(): Notice ... Unable to Calculate Std Dev. | stdev1 | Status | Cannot take the square root, so the program sets sigma to a constant value. |
| MESSAGE NUMBER : 118 stddev(): Notice ... Unable to Calculate Std Dev. | stddev | Status | Number of values is less than or equal to one. Value set as constant in main program. (a) |
| MESSAGE NUMBER : 118 stdev1(): Notice ... Unable to Calculate Std Dev. | stdev1 | Status | Number of values is less than or equal to one. (a) |
| MESSAGE NUMBER : 119 runavg(): Warning ... Unable to Average Records. | mtsa0 | Warning | (a) |
| MESSAGE NUMBER : 120 loadsc(): Error ... Matching Previous with Current Month. | mtsa1 | Fatal | (a) |
| MESSAGE NUMBER : 120 mload(): Warning ... Overlap GeoType NOT Match Current GeoType. | mtsa0 | Warning | (a) |
| MESSAGE NUMBER : 121 prtpcv(): Notice ... No Data in Region. | prtpcv | Notice | All data has a fill value - no good values. Returns to calling program. (a) |
| MESSAGE NUMBER : 122 scscan(): Warning ... Error in Local Solar Hr, SW Data Ignored. | mtsa1 | Warning | (a) |
| MESSAGE NUMBER : 124 filesc(): Error ... Opening Global Summary File. | mtsa1 | Fatal | Verify $CERESHOME/erbelike/data/CERES/DQCC/$SS3_$PS3/yyyy/mm/CER_DQCC_$SS3_$PS3_$CC3.yyyymm output file is valid. (a) |
| MESSAGE NUMBER : 124 filesc(): Error ... Opening PCV Summary File. | mtsa1 | Fatal | Verify $CERESHOME/erbelike/data/CERES/DQCA/$SS3_$PS3/yyyy/mm/CER_DQCA_$SS3_$PS3_$CC3.yyyymm output file is valid. (a) |
| MESSAGE NUMBER : 124 filesc(): Error ... Opening Regional Database File. | mtsa1 | Fatal | (D,a) |
| MESSAGE NUMBER : 124 filesc(): Error ... Opening Science Product File. | mtsa1 | Fatal | (J, a) |
| MESSAGE NUMBER : 124 filesc(): Error ... Opening Statistics Summary File. | mtsa1 | Fatal | Verify $CERESHOME/erbelike/data/CERES/DQCA/$SS3_$PS3/yyyy/mm/CER_DQCA_$SS3_$PS3_$CC3.yyyymm output file is valid. (a) |
| MESSAGE NUMBER : 124 mfiles(): Error ... Opening Science Product File. | mtsa0 | Fatal | (J, a) |
| MESSAGE NUMBER : 124 filesc(): Error ... Opening PCV Summary File. | mtsa3 | Fatal | (a) |
| MESSAGE NUMBER : 124 filesc(): Error ... Opening Statistics Summary File. | mtsa3 | Fatal | (a) |
| MESSAGE NUMBER : 124 filesc(): Error ... Opening Science Product File. | mtsa3 | Fatal | (J, a) |
| MESSAGE NUMBER : 124 filesc(): Error ... Opening Regional Database File. | mtsa3 | Fatal | (D,a) |
| MESSAGE NUMBER : 125 regdrs(): Error ... Writing Regional Database File. | mtsa1 | Fatal | (D,a) |
| MESSAGE NUMBER : 125 regdrs(): Error ... Writing Regional Database File. | mtsa3 | Fatal | (D,a) |
| MESSAGE NUMBER : 126 adjust(): Notice ... Albedo Greater then 1., Set to 1. | mtsa1 | Status | Adjusted albedo not within range, set to 1. (a) |
| MESSAGE NUMBER : 127 ritesc(): Warning ... Error Writing to Science Data Product. | ritesc | Warning | (J, a) |
| MESSAGE NUMBER : 129 filesc(): Error ... Writing Header Record to Tape File. | mtsa1 | Fatal | (J, a) |
| MESSAGE NUMBER : 129 filesc(): Error ... Writing Scale Factors to Tape File. | mtsa1 or mtsa3 | Fatal | (J, a) |
| MESSAGE NUMBER : 129 filesc(): Error ... Writing Header Record to Tape File. | mtsa3 | Fatal | (a) |
| MESSAGE NUMBER : 130 mverif(): Error ... Invalid Satellite Code. | mtsa0 | Fatal | Verify PCF value for ID 607 (ksc). (a) |
| MESSAGE NUMBER : 131 mverif(): Error ... Reading Scale Factors to Tape File. | mtsa0 | Fatal | (J, a) |
| MESSAGE NUMBER : 133 rddata(): Error ... Reading Science Product File. | mtsa0 | Fatal | (J, a) |
| MESSAGE NUMBER : 134 wrdata(): Error ... Writing Science Product File. | mtsa0 | Fatal | (a) |
| MESSAGE NUMBER : 135 mverif(): Error ... Opening Science Product File. | mtsa0 | Fatal | (J, a) |
| MESSAGE NUMBER : 136 lwmod(): Notice ... Error Getting LW Model Data. | lwmod | Notice | None. |
| MESSAGE NUMBER : 137 mfiles(): Error ... Writing Header Record to Tape File. | mtsa0 | Fatal | (a) |
| MESSAGE NUMBER : 137 mfiles(): Error ... Writing Scale Factors to Tape File. | mtsa0 | Fatal | (J, a) |
| MESSAGE NUMBER : 138 mload(): Error ... Writing Science Product File. | mtsa0 | Fatal | (a) |
| MESSAGE NUMBER : 139 dumrd(): Error ... Reading Science Product File. | mtsa3 | Fatal | (a) |
| MESSAGE NUMBER : 139 rdfile(): Error ... Reading Latitude File. | mtsa3 | Fatal | Verify $CERESHOME/erbelike/CER3.2P1/data/scr/CER3.2P1_$SS3_2_$PS3_2_$CC3_2.yyyymm/M9.yyyymm (a) |
| MESSAGE NUMBER : 140 loadsc(): Error ... Reading Science Product File. | mtsa3 | Fatal | (a) |
| MESSAGE NUMBER : 141 loadsc(): Error ... Writing Science Product File. | mtsa3 | Fatal | (a) |
| MESSAGE NUMBER : 142 loadsc(): Error ... Writing Regional Database File. | mtsa3 | Fatal | (D,a) |
| MESSAGE NUMBER : 143 loadsc(): Warning ... Overlap GeoType NOT Match Current GeoType. | mtsa1 | Warning | None. |
| MESSAGE NUMBER : 301 suscan(): Error ... Reading Inversion EID6 File. | ddbupd | Fatal | Verify the $CERESHOME/erbelike/data/CERES/EID6/$SS2_$PS2/yyyy/mm/CER_EID6_$SS2_$PS2_$CC2.yyyymmdd (CER3.1P1) file exists and is valid. (a,c) |
| getfnm(): Error ... Getting filename from PCF. | getfnm | Fatal | Verify PCF is valid - the module is trying to retrieve a filename from a given file ID. (a) |
| pgspci(): Error ... Getting PC Parameter Value. | pgspci | Fatal | Verify PCF is valid - the module is trying to retrieve a particular parameter. (a) |
| MESSAGE NUMBER : 9023 regrpt(): Warning ... Error Data Array Length. | regrpt | Warning | Normal Termination. (a) |
| MESSAGE NUMBER : 9024 regrep(): Warning ... Error Resolution. | regrep | Warning | (a,c) |
| MESSAGE NUMBER : 9024 regrpt(): Warning ... Error Resolution. | regrpt | Warning | Normal Termination. (a) |
| maines4g():Notice ... Beginning of es4hdf software. | MainES4 | Notice | None. |
| MESSAGE NUMBER : 1100 es4hdf(): Error ... Failed to Open Data File. | MainES4 | Fatal | Verify ES-4 output filename is correct in PCF. |
| MESSAGE NUMBER : 1101 es4hdf(): Error ... Creating SDS and or Vgroup. | MainES4 | Fatal | (a) |
| MESSAGE NUMBER : 1102 es4hdf(): Error ... Naming and Attaching Temporal Vgroups. | MainES4 | Fatal | (a) |
| MESSAGE NUMBER : 1103 es4hdf(): Error ... Naming and Attaching Sky Vgroups. | MainES4 | Fatal | (a) |
| MESSAGE NUMBER : 1104 es4hdf(): Error ... Getting SDS Reference Numbers. | MainES4 | Fatal | (a) |
| MESSAGE NUMBER : 1105 es4hdf(): Error ... Failed to Open Data File. | MainES4 | Fatal | Verify ES4G1 file exists and is valid. |
| MESSAGE NUMBER : 1106 es4hdf(): Error ... Failed to Open Data File. | MainES4 | Fatal | Verify ES4G2 file exists and is valid. |
| MESSAGE NUMBER : 1107 es4hdf(): Error ... Failed to Open Data File. | MainES4 | Fatal | Verify ES4G3 file exists and is valid. |
| MESSAGE NUMBER : 1109 es4hdf(): Error ... Failed to Open Data File. | MainES4 | Fatal | Verify ES4G4 file exists and is valid. |
| MESSAGE NUMBER : 1108 es4hdf(): Error ... Failed to Write Data File. | MainES4 | Fatal | (a) |
| MESSAGE NUMBER : 1110 es4hdf(): Error ... Failed to Write Data File. | MainES4 | Fatal | (a) |
| MESSAGE NUMBER : 1111 es4hdf(): Error ... Failed to Write Data File. | MainES4 | Fatal | (a) |
| MESSAGE NUMBER : 1112 es4hdf(): Error ... Failed to Write Data File. | MainES4 | Fatal | (a) |
| MESSAGE NUMBER : 1113 es4hdf(): Error ... Failed to Write Data File. | MainES4 | Fatal | (a) |
| MESSAGE NUMBER : 1114 es4hdf(): Error ... Failed to Write Data File. | MainES4 | Fatal | (a) |
| MESSAGE NUMBER : 1115 es4hdf(): Error ... Failed to Write Data File. | MainES4 | Fatal | (a) |
| MESSAGE NUMBER : 1116 es4hdf(): Error ... Failed to Write Data File. | MainES4 | Fatal | (a) |
| MESSAGE NUMBER : 1117 es4hdf(): Error ... Failed to Write Data File. | MainES4 | Fatal | (a) |
| MESSAGE NUMBER : 1118 es4hdf():Error ... Failed to Insert Temporal Group. | MainES4 | Fatal | (a) |
| MESSAGE NUMBER : 1119 es4hdf():Error ... Failed to Insert Sky Group. | MainES4 | Fatal | (a) |
| MESSAGE NUMBER : 1120 es4hdf():Error ... Failed to Add SDS Data Set. | MainES4 | Fatal | (a) |
| MESSAGE NUMBER : 1121 es4hdf():Error ... Failed to Insert Geo, Lat and Lon SDS. | MainES4 | Fatal | (a) |
| MESSAGE NUMBER : 1122 es4hdf():Error ... Failed to End SDS and Vgroup. | MainES4 | Fatal | (a) |
| MESSAGE NUMBER : 1123 es4hdf():Error ... Failed to End Vgroup. | MainES4 | Fatal | (a) |
| MESSAGE NUMBER : 1124 es4hdf():Error ... Failed to Close Data File. | MainES4 | Fatal | (a) |
| maines9():Notice ... Beginning of es9hdf software. | MainES9 | Notice | None. |
| MESSAGE NUMBER : 1001 maines9():Error ... Failed to Read Data File. | MainES9 | Fatal | (J, a) |
| MESSAGE NUMBER : 1000 maines9():Error ... Failed to Open Data File. | MainES9 | Fatal | (J, a) |
| MESSAGE NUMBER : 1002 maines9():Error ... Failed to Open Data File. | MainES9 | Fatal | Verify ES9 HDF output filename is correct in PCF. |
| MESSAGE NUMBER : 1003 maines9():Error ... Creating SDS and or Vgroup. | MainES9 | Fatal | (a) |
| maines9():MESSAGE NUMBER : 1004 Error ... Failed to Read Data File. | MainES9 | Fatal | (J, a) |
| MESSAGE NUMBER : 1005 maines9():Error ... Failed to Write Data File. | MainES9 | Fatal | (a) |
| MESSAGE NUMBER : 1006 maines9():Error ... Failed to Insert Sky Group. | MainES9 | Fatal | (a) |
| MESSAGE NUMBER : 1007 maines9():Error ... Failed to Add SDS Data Set. | MainES9 | Fatal | (a) |
| MESSAGE NUMBER : 1008 maines9():Error ... Failed to Close Data File. | MainES9 | Fatal | (a) |
| Number of Hourboxes: Invalid Value For Number Of Hourboxes | ConvertES9 | Warning | (J, a) |
| Scene Fraction Histogram: Sum of scene fractions for the month exceeds number of hourboxes | ConvertES9 | Warning | (J, a) |
| Monthly_Average_Day:SW Flux Less Than Minimum Boundary | ConvertES9 | Warning | (J, a) |
| Monthly_Average_Day:SW Flux Larger Than Maximum Boundary | ConvertES9 | Warning | (J, a) |
| Monthly_Average_Hour:SW Flux Less Than Minimum Boundary | ConvertES9 | Warning | (J, a) |
| Monthly_Average_Hour:SW Flux Larger Than Maximum Boundary | ConvertES9 | Warning | (J, a) |
| Monthly_Average_Day:SW or Clear_Sky SW Value Out of Range | ConvertES9 | Warning | (J, a) |
| Monthly_Average_Hour:SW or Clear_Sky SW Value Out of Range | ConvertES9 | Warning | (J, a) |
| Monthly_Average_Day:LW or Clear Sky LW Value Out of Range | ConvertES9 | Warning | (J, a) |
| Monthly_Average_Hour:LW or Clear Sky LW Value Out of Range | ConvertES9 | Warning | (J, a) |
| Monthly_Average_Day:LW or Clear Sky LW Flux Standard Deviation Out of Range | ConvertES9 | Warning | (J, a) |
| Monthly_Average_Hour:LW or Clear Sky LW Flux Standard Deviation Out of Range | ConvertES9 | Warning | (J, a) |
| Monthly_Average_Day:Flux # of Days with at Least 1 Sample Out of Range | ConvertES9 | Warning | (J, a) |
| Monthly_Average_Hour:Flux # of Days with at Least 1 Sample Out of Range | ConvertES9 | Warning | (J, a) |
| Monthly_Average_Day:Albedo or Clear Sky Albedo Out of Range | ConvertES9 | Warning | (J, a) |
| Monthly_Average_Hour:Albedo or Clear Sky Albedo Out of Range | ConvertES9 | Warning | (J, a) |
| Monthly_Average_Day:Net Flux or Clear Sky Net Radiant Flux Out of Range | ConvertES9 | Warning | (J, a) |
| Monthly_Average_Hour:Net Flux or Clear Sky Net Radiant Flux Out of Range | ConvertES9 | Warning | (J, a) |
| Monthly_Average_Day:Monthly Total or Clear Sky Solar Incidence Out of Range | ConvertES9 | Warning | (J, a) |
| Monthly_Average_Hour:Monthly Total or Clear Sky Solar Incidence Out of Range | ConvertES9 | Warning | (J, a) |
| Notice ... Beginning of es4 stats software. | hourbox_stats or data_read |  | (a) |
| Error ... Opening input data file. | hourbox_stats or data_read | Fatal | (a) |
| Error ... Opening output Data file. | hourbox_stats or data_read | Fatal | (a) |
| Error ... Closing input data file. | hourbox_stats or data_read | Fatal | (a) |
| Error ... Closing output Data file. | hourbox_stats or data_read | Fatal | (a) |
| Error ... Reading input Data file. | hourbox_stats or data_read | Fatal | (a) |
| Error ... Reading input Data file. | hourbox_stats or data_read | Fatal | (a) |
| Error ... Converting char ID to integer ID. | hourbox_stats or data_read | Fatal | (a) |
| Error ... Unable to get HDF input file from PCF. | hourbox_stats or data_read | Fatal | (a) |
| Error ... Unable to get SD info from input file. | hourbox_stats or data_read | Fatal | (a) |
| Error ... Unable to get info from input file. | hourbox_stats or data_read | Fatal | (a) |
| Error ... Not prepared for specified data type. | hourbox_stats or data_read | Fatal | (a) |