Clouds and the Earth's Radiant Energy System

(CERES)

Data Management System

CERES Library (CERESlib)

Test Plan

Release 5

Version 2

Primary Authors

Nelson Hillyer, Joseph C. Stassi, Scott Zentz

Science Systems and Applications, Inc. (SSAI)

One Enterprise Parkway

Hampton, Virginia  23666

NASA Langley Research Center

Climate Science Branch

Science Directorate

21 Langley Boulevard

Hampton, VA  23681-2199

SW Delivered to CM:  November 2011

Document Date:  November 2011

Document Revision Record

The Document Revision Record contains information pertaining to approved document changes.  The table lists the date the Software Configuration Change Request (SCCR) was approved, the Release and Version Number, the SCCR number, a short description of the revision, and the revised sections.  The document authors are listed on the cover.  The Head of the CERES Data Management Team approves or disapproves the requested changes based on recommendations of the Configuration Control Board.

| Document Revision Record |
| --- |
| SCCR Approval Date | Release/ Version Number | SCCR Number | Description of Revision | Section(s) Affected |
| 04/11/02 | R3V3 | 343 | Updated document to specify that entire contents of the CERESlib subdirectories /bin and /data get promoted to production. | Secs. 4.0 |
|  |  |  | F77 added to abbreviation list. | App. A |
|  |  |  | Updated directory structure diagrams. | App. B |
|  |  |  | Updated File Descriptions. | App. C |
|  |  |  | Updated cover information. | Cover |
|  |  |  | Updated format to comply with standards. | All |
| 11/18/05 | R4V1 | 604 | Added new sections pertaining to procedures for IBM/Linux cluster testing. | Secs. 1.1, 1.2, 2.2, & 3.4 |
|  |  |  | Updated directory structure diagrams. | App. B |
|  |  |  | Updated format to comply with standards. | All |
| 03/14/06 | R4V2 | 617 | Removed reference to NAG compiler. | Secs. 2.0 & 3.0 |
|  |  |  | Added commands to copy the promotion files to the NAG version directory. | Sec. 2.2 |
|  |  |  | Updated format to comply with standards. | All |
| 09/18/09 | R5V1 | 724 | Added sections for AMI CERESlibs. | Secs. 2.2, 3.4, & 3.5 |
| 08/22/11 | R5V2 | 859 | Updated reference to document version number. | Sec. 1.1 |
|  |  |  | Removed references to SGI 3800. | All |
|  |  |  | Added cereslib_Ed4.a, data_products_Ed3.a, and data_products_Ed4.a. | Sec. 1.2 |
|  |  |  | Removed smf_compile step for AMI versions of CERESlib. | Sec. 2.2 |
|  |  |  | Removed duplicate TRMM acronym expansion. | App. A |
|  |  |  | Formatting was modified for easier testing. (12/11/2012) | All |

Document Revision Record	ii

1.0	Introduction	1

1.1	Document Overview	1

1.2	CERES Library Overview	1

1.2.1	Archive Library Files:  cereslib.a, cereslib_Ed4.a, data_products.a,
	data_products_Ed3.a, and data_products_Ed4.a.	2

1.2.2	Multiple Compiler Versions	2

1.2.3	CERESlib Version Definition	2

2.0	Software Installation Procedures	3

2.1	Installation	3

2.2	Compilation	4

3.0	Test and Evaluation Procedures	6

3.1	Compiling and Executing the XLF CERESlib Test Suite	6

3.2	Compiling and Executing the AMI PPC64 CERESlib Test Suite	6

3.3	Compiling and Executing the AMI X86_64 CERESlib Test Suite	6

4.0	CERESlib File Promotion into Production	7

Appendix A - Acronyms and Abbreviations	A-1

Appendix B - Directory Structure Diagrams	B-1

Appendix C - File Description Tables	C-1

C.1	Production Scripts and Executables	C-1

C.2	Executables	C-2

C.3	Status Message Files	C-2

C.4	PCF/MCF Templates	C-3

C.5	HDF Read Software	C-3

C.6	Ancillary Input Files	C-3

C.7	Temporary Files	C-3

Figure B-1.  CERES Library Directory Structure	B-1

Table C-1.  lib/bin/ subdirectory	C-1

Table C-2.  lib/bin subdirectory	C-2

Table C-3.  lib/smf subdirectory	C-2

Table C-4.  lib/data subdirectory	C-3

# Introduction

CERES is a key component of EOS and NPP.  The first CERES instrument (PFM) flew on TRMM, four instruments are currently operating on the EOS Terra (FM1 and FM2) and Aqua (FM3 and FM4) platforms, and NPP (FM5) platform.  CERES measures radiances in three broadband channels:  a shortwave channel (0.3 - 5 m), a total channel (0.3 - 200 m), and an infrared window channel (8 - 12 m).  The last data processed from the PFM instrument aboard TRMM was March 2000; no additional data are expected.  Until June 2005, one instrument on each EOS platform operated in a fixed azimuth scanning mode and the other operated in a rotating azimuth scanning mode; now all are typically operating in the fixed azimuth scanning mode.  The NPP platform carries the FM5 instrument, which operates in the fixed azimuth scanning mode though it has the capability to operate in a rotating azimuth scanning mode.

CERES climate data records involve an unprecedented level of data fusion:  CERES measurements are combined with imager data (e.g., MODIS on Terra and Aqua, VIIRS on NPP), 4-D weather assimilation data, microwave sea-ice observations, and measurements from five geostationary satellites to produce climate-quality radiative fluxes at the top-of-atmosphere, within the atmosphere and at the surface, together with the associated cloud and aerosol properties.

The CERES project management and implementation responsibility is at NASA Langley.  The CERES Science Team is responsible for the instrument design and the derivation and validation of the scientific algorithms used to produce the data products distributed to the atmospheric sciences community.  The CERES DMT is responsible for the development and maintenance of the software that implements the science team’s algorithms in the production environment to produce CERES data products.  The Langley ASDC is responsible for the production environment, data ingest, and the processing, archival, and distribution of the CERES data products.

## Document Overview

This document, CERES Library Release 5 Test Plan, is part of the CERES Library Release 5 delivery package provided to the Langley Distributed Active Archive Center (DAAC).  It provides procedures for installing and testing the CERES Library software.  A description of acronyms and abbreviations is provided in Appendix A, a directory structure diagram is contained in Appendix B and a description of the software and data files is contained in Appendix C.

This document is organized as follows:

Section 1.0 - Introduction

Section 2.0 - Software Installation Procedures

Section 3.0 - Test and Evaluation Procedures

Appendix A - Acronyms and Abbreviations

Appendix B - Directory Structure Diagram

Appendix C - File Description Tables

## CERES Library Overview

The CERES library (CERESlib) contains no PGEs.  Rather, it is a collection of routines and utilities used by multiple subsystems.  Fortran and C routines are contained within five archive library files:  cereslib.a, cereslib_Ed4.a, data_products.a, data_products_Ed3.a, and data_products_Ed4.a.  Utility scripts are located in the $CERESLIB/bin directory.

### Archive Library Files:  cereslib.a, cereslib_Ed4.a, data_products.a, data_products_Ed3.a, and data_products_Ed4.a.

For implementation purposes, the Fortran and C routines in CERESlib are divided between five different archive library files:  cereslib.a, cereslib_Ed4.a, data_products.a, data_products_Ed3.a, and data_products_Ed4.a.  The data_products archive files contains modules related to CERES data products:  CERES Editions 1 through 2 in data_products.a, CERES Edition 3 in data_products_Ed3.a, and CERES Edition 4 in data_products_Ed4.a.  All other library modules and routines are located within the cereslib archive files; CERES Editions 1-3 in cereslib.a and CERES Edition 4 in cereslib_Ed4.a.

### Multiple Compiler Versions

There are two different versions of CERESlib included with the CERESlib delivery for the AMI Linux platform and one version for the CERESlib delivery for the IBM/Linux cluster.  These versions correspond to the varied Fortran compiler needs of the different CERES subsystems as well as multiple architectures.  The first version of CERESlib for AMI X86_64 Linux is located in the $CERESHOME/lib/x86-gnu directory and uses the GNU Fortran compiler in 64-bit mode.  The second, for AMI PPC64 Linux, is located in the $CERESHOME/lib/p6-xlf directory and uses the IBM XL Fortran compiler in 64-bit mode.  The single library for the IBM/Linux cluster is located in the $CERESHOME/lib directory and uses the IBM XL Fortran compiler in 64-bit mode.

### CERESlib Version Definition

The CERESlib version is defined by the date of the latest change to the source code within the library.  The format of the version is given as YYYYMMDD.  The current version of the CERESlib will be documented in the Delivery Memo.

# Software Installation Procedures

This section describes how to install the CERESlib software in preparation for making the necessary test runs at the Langley DAAC.  The installation procedures include instructions for uncompressing and untarring the delivered tar files, properly defining environmental variables, and compiling the code to create the CERES library files.

## Installation

The scripts and makefiles in the CERESlib delivery package expect the CERES environment variable, $CERESENV, to point to a file which sets the following environment variables:

CERESHOME	-	Top directory for CERES software

CERESLIB 	-	Top directory for CERESlib software (this location will be different for the different CERESlib versions)

PGSDAT	-	Toolkit database directory.  (This variable is set by the Toolkit

pgs-dev-env.csh script.)

PGSLIB	-	Directory containing the PGSTK Toolkit library

PGSBIN	-	Directory location of Toolkit scripts (e.g. smfcompile)

F90	-	Pointer to the F90 compiler

F90COMP	-	Pointer to the Fortran 90 compilation flags

F90LOAD	-	Pointer to the Fortran 90 load flags

CC	-	Pointer to the C compiler

CFLAGS	-	Pointer to the C compiler compilation flags

PGSINC	-	Directory for Toolkit and CERES Message Include Files

PGSMSG	-	Directory for Toolkit and CERES Message Files

PGSDIR	-	Directory for Toolkit libraries

ADD_LFLAGS	-	A DAAC required environment variable

ADD_LIBS	-	A DAAC required environment variable

In the installation instructions below, use the following definition for the TAG variable, which is included in the file name of the delivery files.

TAG = R{R#}-{SCCR#}

where 	R# = CERES Software Release Number
			SCCR# = SCCR Number for the CERESlib Delivery

Ex: 	TAG = R2-050 
		for CERES Software Release 2 and GGEO SCCR #050

Follow the steps below to install the CERESlib software.

source $CERESENV (any version)

mv CERESlib_src_{TAG}.tar.gz $CERESHOME

cd $CERESHOME

uncompress CERESlib_src{TAG}.tar.gz

tar xf CERESlib_src{TAG}.tar

## Compilation

Complete the following steps to compile the CERESlib source code.

On AMI with PPC64 arch:

- Compile the PPC64 CERESlib version.

source $CERESENV

cd $CERESLIB/src

./makeall clean

./makeall

On AMI with X86_64 arch:

- Compile the X86_64 CERESlib version.

source $CERESENV

cd $CERESLIB/src

./makeall clean

./makeall

On IBM/Linux cluster:

- Create the message and message include files.

source $CERESENV

cd $CERESLIB/smf

$CERESLIB/bin/smfcompile_all.csh

cd $CERESLIB/bin

./cp_inc_and_msg_files.csh

Compile the XLF F90 CERESlib version

source $CERESENV

cd $CERESLIB/src

./makeall clean

./makeall

Notes:

When moving from one version of CERESlib to the other, do not simply change directory locations, but be sure that the appropriate start-up script has been sourced.  Failure to do so will cause errors to occur.

The smfcompile_all.csh script and the makeall scripts will report at the end whether all the operations performed were successful.  If problems are encountered, contact one of the CERESlib analysts before proceeding further.

DAAC personnel may have an alternate procedure for compiling the message files.  Any alternate procedure should copy all message include files to the $PGSINC directory and all message files to the $PGSMSG directory.

Because the compiled message and include files go to the $PGSMSG and $PGSINC directories respectively, and because the CERES subsystems will look for these files in these directories and not in the $CERESLIB subdirectories, it is only necessary that the message files be compiled for one of the CERESlib versions.

# Test and Evaluation Procedures

This section provides instructions for compiling and executing the CERESlib test suite.  (See Section 2.1 for an explanation of the CERESENV environment variable.)

The test suite will be executed once for each version of CERESlib.  In each case, the runtest script will print a warning message to the screen and pause processing for each problem discovered during execution.  If no problems are encountered, then the script will complete without interruption until the end.  If problems are encountered, then contact one of the CERESlib analysts.

## Compiling and Executing the XLF CERESlib Test Suite

- Compile XLF F90 CERESlib test suite.

source $CERESENV

cd $CERESLIB/test_suites

./makeall clean

./makeall

If the makeall script reports SUCCESS, then proceed with the testing.

./runtest

## Compiling and Executing the AMI PPC64 CERESlib Test Suite

- Compile XLF F90 CERESlib test suite.

source $CERESENV

cd $CERESLIB/test_suites

./makeall clean

./makeall

If the makeall script reports SUCCESS, then proceed with the testing.

./runtest

## Compiling and Executing the AMI X86_64 CERESlib Test Suite

- Compile Gfortran F90 CERESlib test suite.

source $CERESENV

cd $CERESLIB/test_suites

./makeall clean

./makeall

If the makeall script reports SUCCESS, then proceed with the testing.

./runtest

# CERESlib File Promotion into Production

After CERESlib testing is complete, the following subdirectories and all their contents should be promoted to the production directories:

- $CERESLIB/bin

$CERESLIB/data

It doesn’t matter from which version of CERESlib these files are moved.

Acronyms and Abbreviations

CERES	Clouds and the Earth’s Radiant Energy System

CERESlib	CERES library

DAAC	Distributed Active Archive Center

EOS	Earth Observing System

EOS-AM	EOS Morning Crossing Mission

EOS-PM	EOS Afternoon Crossing Mission

ERBE	Earth Radiation Budget Experiment

ERBS	Earth Radiation Budget Satellite

F77	Fortran 77

F90	Fortran 90

F95	Fortran 95

NAG	Numerical Algorithms Group

NASA	National Aeronautics and Space Administration

NOAA	National Oceanic and Atmospheric Administration

SGI	Silicon Graphics Incorporated

TRMM	Tropical Rainfall Measuring Mission

Directory Structure Diagrams

Figure B-1.  CERES Library Directory Structure

Figure B-1.  CERES Library Directory Structure

Figure B-1.  CERES Library Directory Structure

Figure B-1.  CERES Library Directory Structure

Figure B-1.  CERES Library Directory Structure

Figure B-1.  CERES Library Directory Structure

File Description Tables

Production Scripts and Executables

| Table C-1. lib/bin/ subdirectory |
| --- |
| File Name | Format | Description |
| border_echo.csh | ASCII | echoes a string with a border |
| ceresutil | ASCII | CERES utility scripts |
| check_files.csh | ASCII | checks existence of files |
| cleanpath | ASCII | removes duplicates entries from path |
| cmp_binary.csh | ASCII | compares binary files |
| day_and_hour.csh | ASCII | prints day and hour from the hour of the month |
| day_of_year.csh | ASCII | prints day of year from year, month, and day |
| diff_ascii.csh | ASCII | takes a difference between two ASCII files |
| diff_logs.csh | ASCII | takes a difference between production log files |
| directory_listing.csh | ASCII | creates a listing of files in a directory |
| echo_border.csh | ASCII | echoes a string with a border |
| echo_string.csh | ASCII | echoes a string follows by dots |
| echo_underline.csh | ASCII | echoes and underlines a string |
| hour_of_month | ASCII | prints hour of the month from day and hour |
| last_day.csh | ASCII | prints last day of month given month and year |
| local_version.csh | ASCII | echoes the local CERESlib version date |
| numeric_check.csh | ASCII | checks whether an input parameter is numeric |
| setVariables.csh | ASCII | creates a file with variables identifying the local environment |
| smfcompile_all.csh | ASCII | compiles and places message files |
| tarfile_listing.csh | ASCII | creates a listing of files contained in a tarfile |
| three_digits.csh | ASCII | echoes three-digit numeral from input parameter |
| tk_version.csh | ASCII | echoes Toolkit version number |
| two_digits.csh | ASCII | echoes three-digit numeral from input parameter |
| version.csh | ASCII | echoes the local CERESlib version date and the DAAC CERESlib version date |
| year_month_day.csh | ASCII | echoes yyyy/mm/dd from year and day of year |

Executables

Table C-2.  lib/bin subdirectory

| File Name | Byte Size | Description |
| --- | --- | --- |
| convert.exe | Binary | Converts F77 files to F90 |
| echo2.exe | Binary | echoes to standard error |
| f2c.exe | Binary | Converts F77 files to C |
| grid_interactive.exe | Binary | Runs reference_grid routines interactively |
| meta_read.exe | Binary | program for reading meta_data |

Status Message Files

| Table C-3. lib/smf subdirectory |
| --- |
| File Name | Format | Description |
| CERES_25000.t | ASCII | CERES utility module messages |
| GFDLAER_25716.t | ASCII | gfdl_aer_clim.f90 module messages |
| PMOA_FILE_26210.t | ASCII | post_moa_file.f90 module messages |
| SOLDEC_26400.t | ASCII | solar_declination.f90 module messages |
| TISA_FSW_25899.t | ASCII | fsw.f90 and fsw_file.f90 module messages |
| TISA_SFC_26299.t | ASCII | sfc.f90 and sfc_file.f90 module messages |
| TSI_25910.t | ASCII | tsi_type_mod.f90 module messages |
| VALREG_25714.t | ASCII | valreg_utils.f90 module messages |
| crs_io_25700.t | ASCII | crs_io.f90 module messages |
| ggeofile.t | ASCII | ggeo.f90 and ggeo_file.f90 module messages |
| moa_io_26500.t | ASCII | moa_io module messages |
| refgrid.t | ASCII | reference grid module messages |
| surf_io_26550.t | ASCII | surfmap_io.f90 module messages |
| syn_index_26001.t | ASCII | syn_index.f90 module messages |
| syn_io_26000.t | ASCII | syn_io.f90 module messages |

PCF/MCF Templates

Not Applicable

HDF Read Software

Not Applicable

Ancillary Input Files

Table C-4.  lib/data subdirectory

| File Name | Format | Description |
| --- | --- | --- |
| CERES_constants.dat | ASCII | CERES constants accessible through Toolkit |
| CERES_defaults.dat | ASCII | CERES default values accessible through Toolkit |
| ceres_SI_FM1_day.20020328 | ASCII | Static spectral response functions & spectral correction coefficient files |
| ceres_SI_FM2_day.20020328 | ASCII | same as above |
| ceres_SI_PFM_day.20020328 | ASCII | same as above |
| ceres_SI_FM1_night.20020328 | ASCII | Static spectral correction coefficient files |
| ceres_SI_FM2_night.20020328 | ASCII | same as above |
| ceres_SI_PFM_night.20020328 | ASCII | same as above |

Temporary Files

Not Applicable

# Text boxes

AMI

write_data_files

data_products

cereslib

test_suites*

src

smf

rcf

mod

message

lib

1

1

p6-xlf

x86-gnu

1

lib

IBM/Linux

Cluster

4

Weights

5

WaterMap

4

Solar_declination

8

Reference_grid

Record_lengths

Polar_flag

4

4

Pcf_c

4

Pcf

4

Msg_c

7

Msg

5

Meta_util_c

5

Meta_util

Quality_flags

5

3

8

input

out_comp

out_exp

5

out_comp

out_exp

4

Julian_date_routines

4

Hhmmss

4

Day_of_year

Yyyymmdd

4

Interactive

Header_time

runlogs

4

Test_report

5

5

5

Write_input

Report_success

Read_output

4

Read_nonexist

5

Open_da

6

4

Test_status

7

out_exp

out_comp

input

9

data

4

Weights

4

Solar_declination

4

Output_grid

Nested_grid_test

Interactive_test

Consistency_test

Border_test

9

Figure B-1.  CERES Library Directory Structure

Figure B-1.  CERES Library Directory Structure

Figure B-1.  CERES Library Directory Structure

Figure B-1.  CERES Library Directory Structure

Figure B-1.  CERES Library Directory Structure

Figure B-1.  CERES Library Directory Structure

Figure B-1.  CERES Library Directory Structure

include

data

bin

bin_programs

mod

lib

common_lib

constants

defaults

Convert

1

F2c

2

CUC

Echo2

Meta_read

Io_c

4

Check_time

3

Check_time_c

5

Constants

4

Compiler_defaults

Print_defaults

Defaults

Defaults_c

5

3

Ceres_time

4

C_type_sizes

3

Ceres_time_c

C_getenv

4

C_f90_interface

bin

6

Io

F90_type

Finutl

HDF_version

Header_time

EOF

2