Clouds and the Earth's Radiant Energy System

(CERES)

Data Management System

CERES RegridMOA Subsystem

Subsystem 12.0 Test Plan

Release 5

Version 4

Primary Authors

Thomas Caldwell, Lisa Coleman

Science Systems and Applications, Inc. (SSAI)

One Enterprise Parkway, Suite 200

Hampton, VA  23666

NASA Langley Research Center

Climate Science Branch

Science Directorate

21 Langley Boulevard

Hampton, VA  23681-2199

SW Delivered to CM:  October 2010

Document Date:  October 2010

Document Revision Record

The Document Revision Record contains information pertaining to approved document changes.  The table lists the date the Software Configuration Change Request (SCCR) was approved, the Release and Version Number, the SCCR number, a short description of the revision, and the revised sections.  The document authors are listed on the cover.  The Head of the CERES Data Management Team approves or disapproves the requested changes based on recommendations of the Configuration Control Board.

| Document Revision Record |
| --- |
| SCCR Approval Date | Release/ Version Number | SCCR Number | Description of Revision | Section(s) Affected |
| 10/01/02 | R3V4 | 396 | Removed GEOS2 test cases. | Sec. 3.0 |
|  |  |  | Added GEOS4 test cases. | Sec.3.0 |
|  |  |  | Updated format to comply with standards. | All |
| 10/02/03 | R3V5 | 473 | Changed data date for GEOS4 and ECMWF-GEOS4 test cases. | Secs. 3.1.2.1.2, 3.1.2.2.2, & 3.3 |
|  |  |  | Added new names of DAS input files to Appendix C (Table C.7-1). | App. C |
|  |  |  | Updated format to comply with standards. | All |
| 02/24/05 | R3V6 | 577 | Updated compiler options; added file removal script instructions. | Sec. 2.1 |
|  |  |  | Updated names of ASCII file and PCF generators. | Sec. 3.1.1 |
|  |  |  | Changed testing data dates and file names; updated runscript command; updated testing summaries. | Secs. 3.1.2.1 & 3.1.2.2 |
|  |  |  | Updated names of comparison output files. | Secs. 3.2.2 & 3.2.4 |
|  |  |  | Updated removal script commands. | Sec. 3.3 |
|  |  |  | Updated format to comply with standards. | All |
| 03/01/06 | R4V1 | 615 | Removed ECMWF test cases. | All |
|  |  |  | Removed GEOS3 test case. | All |
|  |  |  | Updated script names to Perl names. | All |
|  |  |  | Updated 32-bit compiler options to 64-bit. | Sec. 2.1 |
|  |  |  | Updated test case date and instance information. | Secs. 3.1.2, 3.2.3, 3.2.4, & 3.3 |
|  |  |  | Added test summary tables for cluster statistics. | Secs. 3.1.2.1 & 3.1.2.2 |
|  |  |  | Updated format to comply with standards. | All |
| 10/21/08 | R5V1 | 686 | Removed references to previous ozone backup source OMI including test case and other information. | Secs. 1.2, 3.0, 1.1.1.1, & App. C |
|  |  |  | Removed reference to outdated scripts. Reversed order of steps 3 and 4 of installation. | Sec. 2.1 |
|  |  |  | Changed pathnames throughout document to reflect new directory structure. | Secs. 2.2, 3.1, 3.2, 3.3, App. B, & App. C |
|  |  |  | Removed reference to processing of previous MOA versions. | Sec. 3.0 |
|  |  |  | Removed GEOS4 test cases and associated information and replaced with G5-CERES test cases and information. | Sec. 3.1.2.1.1 & App. C |
|  |  |  | Updated data space requirements. | Sec. 3.1.2 & Table 3-1 |
|  |  |  | Changed test cases dates. | Secs. 3.1 & 3.2 |
|  |  |  | Added PROD environment variable and “unlimit” command. (11/17/2008) | Sec. 3.1.2.1.1 |
| 03/04/09 | R5V2 | 705 | Added new PGE CER12.1P2. | 2.3 & 4.0 |
| 12/16/09 | R5V3 | 753 | Updated INSTANCE variable. | Secs. 3.1.2.1.1 |
|  |  |  | Updated test case information. | Tables 3-1 & 4-1 |
|  |  |  | Updated MOA file names. | Secs. 3.2.3, 3.2.4, & 3.3 |
| 12/18/09 | R5V4 | 749 | Updated executable names. | Secs. 2.2, 2.3, & Table C.2-1 |
|  |  |  | Removed references to outdated scripts. | Secs. 3.1.1, 4.1.1, & Table C.1-1 |
|  |  |  | Updated output directories. | Secs. 3.1.1.2.1 & 4.1.1.2.1 |
|  |  |  | Updated test case information. | Tables 3-1 & 4-1 |
|  |  |  | Corrected case. | Sec. 3.3 |
|  |  |  | Removed SMOBA reference. | Sec. 4.1.2.1.1 |
|  |  |  | Modified comparison executables to reflect platform dependence. | Secs. 2.2 & 2.3 |
|  |  |  | Modified script file names. (01/11/2011) | Secs. 2.2.1 & 2.2.2 |
| 12/18/09 (Cont’d) | R5V4 | 749 | Added note for running comparison software. (01/11/2011) | Secs. 3.1.2 & 3.2.2 |
|  |  |  | Modifications were made concerning which platforms the code should be compiled on. (01/31/2011) | Secs. 2.2.1 & 2.2.2 |
|  |  |  | Modified the clean-up instructions. (03/01/2011) | Secs. 3.1.1.1 & 3.2.1.1 |
|  |  |  | Modified the “Introduction” paragraph. (12/03/2012) | Sec. 1.0 |
|  |  |  | Formatting issues were fixed. (12/03/2012) | All |

Preface

The Clouds and the Earth’s Radiant Energy System (CERES) Data Management System (DMS) supports the data processing needs of the CERES Science Team research to increase understanding of the Earth’s climate and radiant environment.  The CERES Data Management Team works with the CERES Science Team to develop the software necessary to support the science algorithms.  This software, being developed to operate at the Langley Atmospheric Science Data Center (ASDC), produces an extensive set of science data products.

The DMS consists of 12 subsystems; each subsystem contains one or more Product Generation Executables.  Each subsystem executes when all of its required input data sets are available and produces one or more archival science products.

This Test Plan is written by the responsible CERES subsystem team for the CERES Configuration Management Team and the Langley ASDC to support subsystem testing.  This document describes the software and supporting data files for this Subsystem and explains the procedures for installing, executing, and testing the software in the Science Software Integration and Testing environment.  A section is also included on validating the software results.

Acknowledgment is given to CERES Documentation Team for their support in preparing this document.

Document Revision Record	ii

Preface	v

1.0	Introduction	1

1.1	Document Overview	1

1.2	Subsystem Overview	1

2.0	Software and Data File Installation Procedures	3

2.1	Installation	3

2.2	Compilation	3

2.2.1	Compiling PGE 12.1P1	4

2.2.2	Compiling PGE 12.1P2	4

3.0	Test and Evaluation Procedures for RegridMOA	5

3.1	CER12.1P1 on the p6 and x86 Platforms	5

3.1.1	Stand-alone Test Procedures	5

3.1.1.1	Execution	5

3.1.1.2	Test Summary	6

3.1.2	Evaluation Procedures	6

3.1.2.1	Log and Status File Results	6

3.1.2.2	Metadata Evaluation	7

3.1.2.3	Evaluation of Comparison Software Output	7

3.1.3	Solutions to Possible Problems	7

3.2	CER12.1P2 on the p6 and x86 Platforms	8

3.2.1	Stand-alone Test Procedures	8

3.2.1.1	Execution	8

3.2.1.2	Test Summary	8

3.2.2	Evaluation Procedures	8

3.2.2.1	Log and Status File Results	9

3.2.2.2	Metadata Evaluation	9

3.2.2.3	Evaluation of Comparison Software Output	10

3.2.3	Solutions to Possible Problems	10

Appendix A - Acronyms and Abbreviations	A-1

Appendix B - Directory Structure Diagrams	B-1

Appendix C - File Description Tables	C-1

C.1	Production Scripts	C-1

C.2	Executables	C-1

C.3	Status Message Files (SMF)	C-2

C.4	Processing Control Files (PCF) and Metadata Control Files (MCF)	C-3

C.5	Production Source Code and Makefile	C-3

C.6	Ancillary Input Data	C-5

C.7	Primary Input Data	C-6

Figure B-1.  SARB Regrid MOA Delivery Directory Structure	B-1

Table C.1-1.  Production Scripts @ $(CERESHOME)/sarb/CER12.1P1/rcf/	C-1

Table C.2-1.  Executables @ $(CERESHOME)/sarb/CER12.1P1/bin/	C-1

Table C.3-1.  Status Message Files @ $(PGSMSG)	C-2

Table C.4-1.  Metadata Control Files @ $(CERESHOME)/sarb/CER12.1P1/rcf/mcf/	C-3

Table C.4-2.  Process Control File @ $(CERESHOME)/sarb/CER12.1P1/rcf/pcf/	C-3

Table C.5-1.  Fortran 90 Main Processor Code @ $(CERESHOME)/sarb/CER12.1P1/src/	C-3

Table C.6-1.  Ancillary Input Data @ $(CERESHOME)/sarb/ancillary/CER12.1P1/	C-5

Table C.7-1.  Primary Input Data Files @ $(CERESHOME)/sarb/data/inpuregridmoa/	C-6

# Introduction

CERES is a key component of EOS and NPP.  The first CERES instrument (PFM) flew on TRMM, four instruments are currently operating on the EOS Terra (FM1 and FM2) and Aqua (FM3 and FM4) platforms, and NPP (FM5) platform.  CERES measures radiances in three broadband channels:  a shortwave channel (0.3 - 5 m), a total channel (0.3 - 200 m), and an infrared window channel (8 - 12 m).  The last data processed from the PFM instrument aboard TRMM was March 2000; no additional data are expected.  Until June 2005, one instrument on each EOS platform operated in a fixed azimuth scanning mode and the other operated in a rotating azimuth scanning mode; now all are typically operating in the fixed azimuth scanning mode.  The NPP platform carries the FM5 instrument, which operates in the fixed azimuth scanning mode though it has the capability to operate in a rotating azimuth scanning mode.

CERES climate data records involve an unprecedented level of data fusion:  CERES measurements are combined with imager data (e.g., MODIS on Terra and Aqua, VIIRS on NPP), 4-D weather assimilation data, microwave sea-ice observations, and measurements from five geostationary satellites to produce climate-quality radiative fluxes at the top-of-atmosphere, within the atmosphere and at the surface, together with the associated cloud and aerosol properties.

The CERES project management and implementation responsibility is at NASA Langley.  The CERES Science Team is responsible for the instrument design and the derivation and validation of the scientific algorithms used to produce the data products distributed to the atmospheric sciences community.  The CERES DMT is responsible for the development and maintenance of the software that implements the science team’s algorithms in the production environment to produce CERES data products.  The Langley ASDC is responsible for the production environment, data ingest, and the processing, archival, and distribution of the CERES data products.

## Document Overview

This document, CERES Regrid Meteorological, Ozone, and Aerosol (MOA) Subsystem (Subsystem 12) Release 3 Test Plan, is part of the CERES Subsystem 12.0 Release 3 delivery package provided to the Atmospheric Science Data Center (ASDC).  It provides a description of the CERES RegridMOA Subsystem Release 3 software and explains the procedures for installing, executing, and testing the software in the Science Software Integration and Testing (SSI&T) environment.  A section is also included on validating the software results. A description of acronyms and abbreviations is provided in Appendix A, a directory structure diagram is contained in Appendix B, and a description of the software and data files is contained in Appendix C.

This document is organized as follows:

Section 1.0 - Introduction

Section 2.0 - Software and Data File Installation Procedures

Section 3.0 - Test and Evaluation Procedures for RegridMOA

Appendix A - Acronyms and Abbreviations

Appendix B - Directory Structure Diagram

Appendix C - File Description Tables

## Subsystem Overview

The CERES RegridMOA Subsystem ingests meteorological, ozone, and aerosol data from several different external sources and combines these data into one product, the MOA product.  The RegridMOA Subsystem executes once per day, and produces one MOA file every six hours.  Since the input data from the different external sources do not conform to a common horizontal grid system, this Subsystem horizontally interpolates the input aerosol and ozone data to conform to the same horizontal grid as the meteorological data.  Microwave humidity data, however, are retained on their original input grid.  Vertical and temporal interpolations of the meteorological and ozone data are also necessary to meet CERES requirements.  Software developed by the CERES Clouds, Surface and Atmospheric Radiation Budget (SARB), and Time Interpolation and Spatial Averaging (TISA) Working Groups all require access to the data contained in MOA.

External products the RegridMOA Subsystem accesses in Release 3 include meteorological, ozone, and microwave precipitable water data.  The primary meteorological data, such as temperature, humidity, and wind speed profile data, are obtained from the Global Modeling and Assimilation Office (GMAO) at Goddard Space Flight Center.  The primary ozone data is obtained from the National Centers for Environmental Prediction (NCEP) Stratospheric Monitoring Group Ozone Blended Analysis (SMOBA).  The SSM/I (Special Sensor Microwave Imager) precipitable water data are obtained from the Global Hydrology Resource Center (GHRC) at NASA Marshall.  CERES provides the input climatological data sets for aerosol optical depth at the time of software delivery.

This Subsystem first interpolates the ozone and aerosol input data horizontally, which is the domain where the data have the smallest variability.  The aerosol optical depth data requires neither temporal nor vertical interpolation.  The ozone data also require no temporal interpolation.  Next, the nonmicrowave meteorological data are temporally interpolated.  The meteorological profile data--temperature, specific humidity, and wind speed vectors--are interpolated in the vertical domain where the data have the largest variability.  Data interpolated in the vertical domain provide vertical profiles at pressure levels selected by the CERES Science Team.  While the microwave humidity data are neither horizontally nor vertically interpolated, they are temporally interpolated to provide hourly data.  This temporal interpolation requires data from both the previous and succeeding days.

For purposes of testing the RegridMOA Subsystem software in the ASDC SSI&T environment, the CERES SARB Working Group provides the input data sets.  For production processing, however, the Langley TRMM Information System (LaTIS) obtains the external ancillary input data required by this Subsystem and performs the initial ingestion of these data.  The spatial and temporal resolutions of these data are not altered by LaTIS.  LaTIS provides a scheduler that tracks the availability of these input data sets and subsequently controls processing of the RegridMOA Subsystem Product Generation Executive (PGE).  The CERES Science Team decides on an allowable lag time between the measurement of CERES data and the execution of this Subsystem.  This lag time is built into the processing scheduler, thus, allowing for the accumulation of the necessary input data from the external sources.  If microwave humidity data are not available from the external source after this lag time, the RegridMOA Subsystem may still process.  If the ozone data for a given day is not available within the allowable lag time, the most recent ozone data file may be used.

# Software and Data File Installation Procedures

This section describes how to install the Subsystem 12 RegridMOA software in preparation for making the necessary test runs at the Langley ASDC.  The installation procedures include instructions for uncompressing and untarring the delivered files, properly defining environmental variables, and compiling the RegridMOA programs.

## Installation

Software/Data File Install Procedure:

- The scripts, makefiles, and Process Control Files (PCF) in the Subsystem 7.2 delivery package expect the following environment variables, found in the $CERESENV script, to be defined:

PGSDIR	-	Directory for Toolkit libraries

CERESHOME	-	Top Directory for CERES Software

CERESLIB	-	Directory for CERESlib

PGSINC	-	Pointer to the PGS Include file directory

PGSLIB	-	Directory which contains the 64-bit Toolkit library file

PGSMSG	-	Directory which contains Toolkit and CERES

Status Message Files

HDFDIR	-	Pointer to the HDF home directory

The included makefiles for RegridMOA redefine the following environment variables for x86 compilation:

F90COMP	-	Fortran 90 compilation flags (use the following options: -c -O2 -fno-second-underscore -fconvert=big-endian)

- Change directory to the directory where you plan to install the RegridMOA Subsystem.  (The following instructions assume that the directory will be $CERESHOME.)

- Uncompress and untar the RegridMOA Subsystem files:

uncompress RegridMOA_data_R5-749.tar.Z

tar xf RegridMOA_data_R5-749.tar

uncompress RegridMOA_anc_R5-749.tar.Z

tar xf RegridMOA_anc_R5-749.tar

uncompress RegridMOA_src_R5-749.tar.Z

tar xf RegridMOA_src_R5-749.tar

## Compilation

Since many modules and their associated error messages are shared between SARB subsystems, all error message files are stored in one directory.  The instructions for compiling these portions of the subsystem follow.  Instructions for generating the executables for PGEs CER 12.1P1 and CER12.1P2 are contained in Section 2.2.1.  Depending where compilation occurs, executables will contain the platform type in the names.  In this document, the variable $host will be either ppc64 or x86_64.

### Compiling PGE 12.1P1

NOTE:  For full subsystem deliveries, use the following commands to compile all the software:

cd $CERESHOME/sarb/CER12.1P1/rcf

./compile-CER12.1P1.pl all

- The PGE 12.1P1 Main-Processor executable can be made on both the P6 and x86 platforms by typing:

cd $CERESHOME/sarb/CER12.1P1/rcf

./compile-CER12.1P1.pl src

The resulting executable, CER12.1P1_$host.exe, is stored in the directory $CERESHOME/sarb/CER12.1P1/bin.

- Execute the following on the x86 platform to compile the comparison software for the Main-Processor output:

cd $CERESHOME/sarb/CER12.1P1/rcf

./compile-CER12.1P1.pl test

The resulting executable, CER12.1P1Comp_x86_64.exe, remains in the directory $CERESHOME/sarb/CER12.1P1/test_suites.

### Compiling PGE 12.1P2

NOTE:  For full subsystem deliveries, use the following commands to compile all the software:

cd $CERESHOME/sarb/CER12.1P2/rcf

./compile-CER12.1P2.pl all

- The PGE 12.1P2 Main-Processor executable can be made on both the P6 and x86 platforms by typing:

cd $CERESHOME/sarb/CER12.1P2/rcf

./compile-CER12.1P2.pl src

The resulting executable, CER12.1P2_$host.exe, is stored in the directory $CERESHOME/sarb/CER12.1P2/bin.

- Execute the following on the x86 platform to compile the comparison software for the Main-Processor output:

cd $CERESHOME/sarb/CER12.1P2/rcf

./compile-CER12.1P2.pl test

The resulting executable, CER12.1P2Comp_x86_64.exe, remains in the directory $CERESHOME/sarb/CER12.1P2/test_suites.

# Test and Evaluation Procedures for RegridMOA

This section provides general information on how to execute the Subsystem 12 PGEs and provides an overview of the test and evaluation procedures.  It includes a description of what is being tested and the order in which the tests should be performed.

## CER12.1P1 on the p6 and x86 Platforms

### Stand-alone Test Procedures

#### Execution

CER12.1P1:  Edition2

Command Line Instructions:

unlimit

setenv PROD no (read input locally)

cd $CERESHOME/sarb/CER12.1P1/rcf

source MOA-Ed2-env.csh

cleanup-CER12.1P1.pl CERES_SSIT-GMAO-G5-Edition2_999999.19971215

cd $CERESHOME/sarb/CER12.1P1/rcf

CER12.1P1-pcfgen.pl -date 19971215

run-CER12.1P1.pl CER12.1P1_PCF_CERES_SSIT-GMAO-G5-Edition2_999999.19971215

SGE Testing Instructions:

setenv PROD no (read input locally)

cd $CERESHOME/sarb/CER12.1P1/rcf

source MOA-Ed2-env.csh

cleanup-CER12.1P1.pl CERES_SSIT-GMAO-G5-Edition2_999999.19971215

cd $CERESHOME/sarb/CER12.1P1/rcf

CER12.1P1-SGE_Driver.pl -date 19971215

Exit Codes

0	- Normal Exit,

200	- Fatal Error.

#### Test Summary

CER12.1P1:  Edition2

Total Run Time:	5 min

### Evaluation Procedures

This section provides information on how to execute the comparison software for the Regrid MOA Subsystem PGE CER12.1P1.

CER12.1P1:  Edition2

To compare the created output data:

NOTE:  Please run this test only on an x86 machine.

unlimit

cd $CERESHOME/sarb/CER12.1P1/rcf

source MOA-Ed2-env.csh

cd $CERESHOME/sarb/CER12.1P1/test_suites

compare_CER12.1P1_files.pl

#### Log and Status File Results

There are five Log files associated with this PGE.  The first three listed below are required by the Toolkit. The Toolkit Log files contain all error and/or status messages produced by the PGE during processing.

- Report Log File:  $CERESHOME/sarb/runlogs/CER12.1P1/CER12.1P1_LogReport_CERES_SSIT-GMAO-G5-Edition2_999999.19971215
The Report Log File contain RegridMOA-related informational messages.  These messages may be strictly informative (Error Type = Status or Warning) or may indicate a fatal condition that results in premature PGE termination (Error Type = Fatal).

- Status Log File:  $CERESHOME/sarb/runlogs/CER12.1P1/CER12.1P1_LogStatus_CERES_SSIT-GMAO-G5-Edition2_999999.19971215
The Status Log File contains all messages created by the Toolkit and RegridMOA-related messages that can lead to abnormal ending of the Preprocessor.  If an abnormal exit is encountered by the PGE, this file should be examined for ’_E_’, (error) or ’_F_’ (fatal) message types.

- User Log File:  $CERESHOME/sarb/runlogs/CER12.1P1/CER12.1P1_LogUser_CERES_SSIT-GMAO-G5-Edition2_999999.19971215
The User Log File is not used at this time, but exists to satisfy the Toolkit requirements.  Typically the _U_ and _N_ (User information and Notice) will be written to User Log File and Status Log File.

- PCF Log File:  $CERESHOME/sarb/CER12.1P1/rcf/pcf/CER12.1P1_PCF_CERES_SSIT-GMAO-G5-Edition2_999999.19971215.log

This log file is created when the PCF is generated and contains a listing of all the environment variables set when the PCF was created along with a listing of all the files used to create this PCF.  There is also a listing of any missing optional and mandatory files. The list of existing output data files will only be created if the PGE is run more than once without clean-up.

#### Metadata Evaluation

TBD

#### Evaluation of Comparison Software Output

All comparisons done in Section 3.1.1.1 by the test script should look like the following:

Comparing MOA file:  CER_MOA_CERES_SSIT-GMAO-G5-Edition2_999999.19971215---SUCCESSFUL

If an error in a file comparison is found the following message will be displayed:

Comparing MOA file:  CER_MOA_CERES_SSIT-GMAO-G5-Edition2_999999.19971215 -- ERROR: Check comparison file

The comparison file will be here:

{$CERESHOME}/sarb/CER12.1P1/test_suites

CER_MOA_CERES_SSIT-GMAO-G5-Edition2_999999.19971215.compare

### Solutions to Possible Problems

All MOA data should be deleted before rerunning any of the above tests.   This can be done by using the following commands:

cd $CERESHOME/sarb/CER12.1P1/rcf

source MOA-Ed2-env.csh

cleanup-CER12.1P1.pl CERES_SSIT-GMAO-G5-Edition2_999999.19971215

## CER12.1P2 on the p6 and x86 Platforms

### Stand-alone Test Procedures

#### Execution

CER12.1P2: Edition4

Command Line Instructions:

unlimit

setenv PROD no (read input locally)

cd $CERESHOME/sarb/CER12.1P2/rcf

source MOA-Ed4-env.csh

cleanup-CER12.1P2.pl CERES_SSIT-GMAO-G5-Edition4_999999.19971215

cd $CERESHOME/sarb/CER12.1P2/rcf

CER12.1P2-pcfgen.pl -date 19971215

run-CER12.1P2.pl CER12.1P2_PCF_CERES_SSIT-GMAO-G5-Edition4_999999.19971215

SGE Testing Instructions:

setenv PROD no (read input locally)

cd $CERESHOME/sarb/CER12.1P2/rcf

source MOA-Ed4-env.csh

cleanup-CER12.1P2.pl CERES_SSIT-GMAO-G5-Edition4_999999.19971215

cd $CERESHOME/sarb/CER12.1P2/rcf

CER12.1P2-SGE_Driver.pl -date 19971215

Exit Codes

0	- Normal Exit,

200	- Fatal Error.

#### Test Summary

CER12.1P2: Edition4

Total Run Time:	10 min

### Evaluation Procedures

This section provides information on how to execute the comparison software for the Regrid MOA Subsystem PGE CER12.1P2.

CER12.1P2:  Edition4

To compare the created output data:

NOTE:  Please run this test only on an x86 machine.

unlimit

cd $CERESHOME/sarb/CER12.1P2/rcf

source MOA-Ed4-env.csh

cd $CERESHOME/sarb/CER12.1P2/test_suites

compare_CER12.1P2_files.pl

#### Log and Status File Results

There are five Log files associated with this PGE.  The first three listed below are required by the Toolkit. The Toolkit Log files contain all error and/or status messages produced by the PGE during processing.

- Report Log File:  $CERESHOME/sarb/runlogs/CER12.1P2/CER12.1P2_LogReport_CERES_SSIT-GMAO-G5-Edition4_999999.19971215
The Report Log File contain RegridMOA-related informational messages.  These messages may be strictly informative (Error Type = Status or Warning) or may indicate a fatal condition that results in premature PGE termination (Error Type = Fatal).

- Status Log File:  $CERESHOME/sarb/runlogs/CER12.1P2/CER12.1P2_LogStatus_CERES_SSIT-GMAO-G5-Edition4_999999.19971215
The Status Log File contains all messages created by the Toolkit and RegridMOA-related messages that can lead to abnormal ending of the Preprocessor.  If an abnormal exit is encountered by the PGE, this file should be examined for ’_E_’, (error) or ’_F_’ (fatal) message types.

- User Log File:  $CERESHOME/sarb/runlogs/CER12.1P2/CER12.1P2_LogUser_CERES_SSIT-GMAO-G5-Edition4_999999.19971215
The User Log File is not used at this time, but exists to satisfy the Toolkit requirements.  Typically the _U_ and _N_ (User information and Notice) will be written to User Log File and Status Log File.

- PCF Log File:  $CERESHOME/sarb/CER12.1P2/rcf/pcf/CER12.1P2_PCF_CERES_SSIT-GMAO-G5-Edition4_999999.19971215.log

This log file is created when the PCF is generated and contains a listing of all the environment variables set when the PCF was created along with a listing of all the files used to create this PCF.  There is also a listing of any missing optional and mandatory files. The list of existing output data files will only be created if the PGE is run more than once without clean-up.

#### Metadata Evaluation

TBD

#### Evaluation of Comparison Software Output

All comparisons done in Section 3.2.1.1 by the test script should look like the following:

Comparing MOA file:  CER_MOA_CERES_SSIT-GMAO-G5-Edition4_999999.19971215--- SUCCESSFUL

If an error in a file comparison is found the following message will be displayed:

Comparing MOA file: CER_MOA_CERES_SSIT-GMAO-G5-Edition4_999999.19971215 -- ERROR: Check comparison file

The comparison file will be here:

{$CERESHOME}/sarb/CER12.1P2/test_suites

CER_MOA_CERES_SSIT-GMAO-G5-Edition4_999999.19971215.compare

### Solutions to Possible Problems

All MOA data should be deleted before rerunning any of the above tests.   This can be done by using the following commands:

cd $CERESHOME/sarb/CER12.1P2/rcf

source MOA-Ed4-env.csh

cleanup-CER12.1P2.pl CERES_SSIT-GMAO-G5-Edition4_999999.19971215

Acronyms and Abbreviations

ASCII	American Standard Code Information Interchange

ASDC	Atmospheric Science Data Center

CERES	Clouds and the Earth’s Radiant Energy System

CERESlib	CERES library

DAAC	Distributed Active Archive Center

DAO	Data Assimilation Office

DAS	Data Assimilation System

ECMWF	European Centre for Medium-Range Weather Forecasting

ECS	EOSDIS Core System

EOS	Earth Observing System

EOS-AM	EOS Morning Crossing Mission

EOSDIS	EOS Data Information System

EOS-PM	EOS Afternoon Crossing Mission

EP-TOMS	Earth Probe - Total Ozone Mapping Spectrometer

ERBE	Earth Radiation Budget Experiment

ERBS	Earth Radiation Budget Satellite

F90	Fortran 90

GEOS	Goddard Earth Observing System

GHRC	Global Hydrology Resource Center

GMAO	Global Modeling and Assimilation Office

HDF 	Hierarchical Data Format

LaTIS	Langley TRMM Information System

MCF	Metadata Control Files

MOA	Meteorological, Ozone, and Aerosol

NASA	National Aeronautics and Space Administration

NCEP	National Centers for Environmental Prediction

NOAA	National Oceanic and Atmospheric Administration

PCF	Process Control File

PGE	Product Generation Executive

QC	Quality Control

SARB	Surface and Atmospheric Radiation Budget

SMF	Status Message Files

SMOBA	Stratospheric Monitoring Group Ozone Blended Analysis

SSF	Single Satellite CERES Footprint TOA and Surface Fluxes, Clouds

SSI&T	Subsystem Integration and Testing

SSM/I	Special Sensor Microwave / Imager

TISA	Time Interpolation and Spatial Averaging

TOA	Top-of-Atmosphere

TRMM	Tropical Rainfall Measuring Mission

Directory Structure Diagrams

Figure B-1.  SARB Regrid MOA Delivery Directory Structure

Figure B-1.  SARB Regrid MOA Delivery Directory Structure

Figure B-1.  SARB Regrid MOA Delivery Directory Structure

File Description Tables

Production Scripts

Table C.1-1.  Production Scripts @ $(CERESHOME)/sarb/CER12.1P1/rcf/

| File Name | Format | Description |
| --- | --- | --- |
| CER12.1P1-pcfgen.pl | ASCII | Perl script which creates the PCF for the Main Processor |
| Compile-CER12.1P1.pl | ASCII | Perl script which compiles the status message files and generates the MOA executable |
| Run-CER12.1P1.pl | ASCII | Perl script which executes the Main Processor |
| cleanup-CER12.1P1.pl | ASCII | Perl script which removes SS 12.0 output files |
| MOA-Ed2-env.csh | ASCII | C shell script which sets the environment variables for test described in section 3.1.2.1 |

Executables

Table C.2-1.  Executables @ $(CERESHOME)/sarb/CER12.1P1/bin/

| File Name | Format | Description |
| --- | --- | --- |
| CER12.1P1_ppc64.exe, CER12.1P1_x86_64.exe | Binary | Main Processor executable |

Status Message Files (SMF)

Table C.3-1.  Status Message Files @ $(PGSMSG)

| File Name | Format | Description |
| --- | --- | --- |
| PGS_26500a | ASCII | Toolkit Status Message File |
| PGS_26501a | ASCII | Toolkit Status Message File |
| PGS_26502a | ASCII | Toolkit Status Message File |
| PGS_26503a | ASCII | Toolkit Status Message File |
| PGS_26504a | ASCII | Toolkit Status Message File |
| PGS_26505a | ASCII | Toolkit Status Message File |
| PGS_26506a | ASCII | Toolkit Status Message File |
| PGS_26507a | ASCII | Toolkit Status Message File |
| PGS_26508a | ASCII | Toolkit Status Message File |
| PGS_26509a | ASCII | Toolkit Status Message File |
| PGS_26510a | ASCII | Toolkit Status Message File |
| PGS_26511a | ASCII | Toolkit Status Message File |
| PGS_26512a | ASCII | Toolkit Status Message File |
| PGS_26513a | ASCII | Toolkit Status Message File |
| PGS_26514a | ASCII | Toolkit Status Message File |
| PGS_26515a | ASCII | Toolkit Status Message File |
| a. These files will be generated on execution of production software and are not included in the tar file. |

Processing Control Files (PCF) and Metadata Control Files (MCF)

The Process Control Files are not included in the Software Delivery Package.  They will be created by the PCF generator scripts.

Table C.4-1.  Metadata Control Files @ $(CERESHOME)/sarb/CER12.1P1/rcf/mcf/

| File Name | Format | Description |
| --- | --- | --- |
| CPMOA_AA.mcf | ODL | MCF for Main Processor MOA files. |
| CPQCR_AA.mcf | ODL | MCF for Main Processor QC Report file |

Table C.4-2.  Process Control File @ $(CERESHOME)/sarb/CER12.1P1/rcf/pcf/

| File Name | Format | Description |
| --- | --- | --- |
| CER12.1P1_PCF_$SS12_$PS12_$CC12. yyyymmdda | ASCII | Process Control File template for Main Processor |
| a. This file will be generated on execution of Subsystem software and is not included in the tar file. See operators manual for environment variable descriptions. |

Production Source Code and Makefile

| Table C.5-1. Fortran 90 Main Processor Code @ $(CERESHOME)/sarb/CER12.1P1/src/ |
| --- |
| File Name | Format | Description |
| Aerosols_Mod.f90 | ASCII | Processes aerosol data |
| AirCalc_Mod.f90 | ASCII | Determines air mass index |
| ColOzone_Mod.f90 | ASCII | Processes ozone data |
| GEOS_Params.f90 | ASCII | Contains parameters required to process DAS meteorological input data |
| GEOS2_MOD.f90 | ASCII | Drives ingestion and processing of DAS-GEOS2 meteorological input data |
| GEOS3_MOD.f90 | ASCII | Drives ingestion and processing of DAS-GEOS3 meteorological input data |
| GEOS4_MOD.f90 | ASCII | Drives ingestion and processing of DAS-GEOS4 meteorological input data |
| ECMWF_Access.f90 | ASCII | Contains routines required to access ECMWF meteorological input data |
| ECMWF_Main.f90 | ASCII | Drives processing of ECMWF meteorological data |
| ECMWF_Mod.f90 | ASCII | Contains routines used in processing of ECMWF data |
| G5_Mod.f90 | ASCII | Drives processing of G5-CERES meteorological input data |
| Grid_Params.f90 | ASCII | Contains parameters required by the gridding process |
| Grid_Setup.f90 | ASCII | Contains routines necessary for gridding to the MOA output grid |
| Horiz_Inter.f90 | ASCII | Converts data on one horizontal grid to another horizontal grid |
| MOA_Init.f90 | ASCII | Contains initialization routines |
| MOA_Main.f90 | ASCII | Regrid MOA Subsystem main program |
| MOA_LOGID.f90 | ASCII | Parameter module of logic IDs for input and output files |
| MOA_Var.f90 | ASCII | Contains type declarations for variables used throughout the Regrid MOA Subsystem |
| MW_H2O.f90 | ASCII | Drives processing of microwave humidity data |
| NCEP_Ingest.f90 | ASCII | Ingests NCEP (backup source) meteorological data |
| NCEP_Main2.f90 | ASCII | Drives processing of NCEP data |
| PostProc.f90 | ASCII | Drives processing of QC reports and MetaData |
| SAGE_Replace.f90 | ASCII | Vertically and horizontally interpolates SAGE data to the output grid |
| Temp_Humid.f90 | ASCII | Temporally and vertically interpolates temperature and humidity data |
| Temp_Humid_G5.f90 | ASCII | Variation of Temp_Humid.f90 which accommodates G5 processing requirements |
| gbytes.c | ASCII | Extracts requested number of bytes from a word |
| sphertlib3.f90 | ASCII | Converts NCEP wave data to data on a Gaussian grid |
| Makefile_$hosttype | ASCII | Makefile to produce executable |
| run_make | ASCII | Script to manage make settings on different platforms |

Ancillary Input Data

Table C.6-1.  Ancillary Input Data @ $(CERESHOME)/sarb/ancillary/CER12.1P1/

| File Name | Format | Description |
| --- | --- | --- |
| CERES000.prod.assim.const_2d_asm_Nx.00000000.hdf | HDF | DAS G5 orography data for G5 processing |
| GRIBZ19980701.bin | Binary | C program for reading orography data of ECMWF regions |
| GridParams_SS12.20081024 | Formatted Namelist | Sizes and region counts for all of the grids used in the Regrid MOA Subsystem |
| RegCenters_SS12.20081024 | Binary | Latitudinal and longitudinal coordinates of the CERES and Gaussian grids |
| Ozwts_mmm mmm = jan ... dec | ASCII | Monthly Zonal and pressure level dependent weighting factors for generating a vertical ozone profile |
| Pink_Stow_mm mm = 01 .. 12 | Binary | Monthly Aerosol climatological data set |
| SAGE_WV_sss sss = spr, sum, aut, win | Binary | Seasonal SAGE water vapor climatology data set |
| ozone_clim.dat | ASCII | Ozone climatology derived from EPToms data |

Primary Input Data

| Table C.7-1. Primary Input Data Files @ $(CERESHOME)/sarb/data/inpuregridmoa/ |
| --- |
| File Name | Format | Description |
| CERES100.prod.assim.tavg1_2d_slv_Nx.yyyymmdd.hdfa | HDF | DAS-G5 0.5x0.67 hourly surface data Use when Production Strategy is DAO-G5-CERES |
| CERES100.prod.assim.inst6_3d_ana_Np.yyyymmdd.hdfa | HDF | DAS-G5 0.5x0.67 6-hourly profile data Use when Production Strategy is DAO-G5-CERES |
| f13_iwva_yyJJJ_dayAD.hdfb | HDF | SSM/I microwave humidity data |
| f14_iwva_yyJJJ_dayAD.hdfb | HDF | SSM/I microwave humidity data |
| ozYYMMDD.datc | ASCII | SMOBA ozone data |
| ozYYMMDD.datc | ASCII | SMOBA ozone data |
| a. yyyymmdd = 19971215 b. yyJJJ = 97347 thru 97351 c. YYMMDD = 971214, 971215 |

# Text boxes

BREAKDOWN OF THE SARB REGRIDMOA DIRECTORY STRUCTURE

sarb

runlogs

smf

CER12.1P1*

data*

ancillary

regridmoa

data_exp

CER12.1P1

CER12.1P1

*Indicates additional charts for subpaths

BREAKDOWN OF THE DATA DIRECTORY

data

input

output

scr

qc

BREAKDOWN OF THE CER12.1P1 DIRECTORY

CER12.1P1

bin

src

test_suites

pcf

rcf

mcf