Clouds and the Earth's Radiant Energy System

(CERES)

Data Management System

CERES Synoptic SARB

(Subsystem 7.2)

Release 5 Test Plan

Version 6

Primary Authors

Tom Caldwell

Science Systems and Applications, Inc. (SSAI)

One Enterprise Parkway, Suite 200

Hampton, VA 23666

NASA Langley Research Center

Climate Science Branch

Science Directorate

21 Langley Boulevard

Hampton, VA  23681-2199

SW Delivered to CM:  November 2016

Document Date:  November 2016

Document Revision Record

The Document Revision Record contains information pertaining to approved document changes.  The table lists the date the Software Configuration Change Request (SCCR) was approved, the Release and Version Number, the SCCR number, a short description of the revision, and the revised sections.  The document authors are listed on the cover.  The Head of the CERES Data Management Team approves or disapproves the requested changes based on recommendations of the Configuration Control Board.

| Document Revision Record |
| --- |
| SCCR Approval Date | Release/ Version Number | SCCR Number | Description of Revision | Section(s) Affected |
| 06/19/03 | R3V1 | 445 | Initial version of document. | All |
|  |  |  | Updated format to comply with standards. | All |
| 08/13/04 | R3V2 | 550 | Updated tar filenames. | 2.1 |
|  |  |  | Updated environment variable filename and generalized filename variables. | 3.1.1.1 through 3.1.1.4, 3.1.2 |
|  |  |  | Updated runtime information. | 3.1.1.1.2 |
|  |  |  | Added new section for Terra test case. | 3.2 |
|  |  |  | Updated filenames and added new ones. | Appendix C (Table C3-1) |
|  |  |  | Updated format to comply with standards. | All |
| 08/11/06 | R3V3 | 634 | Updated tar filenames. | 2.1 |
|  |  |  | Updated section to reflect use of new compilation script. | 2.2 |
|  |  |  | Changed names of scripts to reflect conversion to Perl. | 3.1, 3.2, App. C (Table C1-1) |
|  |  |  | Added use of input data file move script. | 3.1.1.1, 3.2.1.1 |
|  |  |  | Updated sections to reflect use of new Perl scripts. | 3.1.1.1, 3.2.1.1 |
|  |  |  | Updated test summary information tables. | Table 3-1, Table 3-2 |
|  |  |  | Updated filenames and added new ones. | App. C (Table C3-1) |
|  |  |  | Updated format to comply with standards. | All |
| 12/12/07 | R4V1 | 663 | Added description of new SYNs output. | 1.2.1 |
|  |  |  | Updated SCCR number in filenames. | 2.1 |
|  |  |  | Updated test case information. | 3.2.1.1 |
|  |  |  | Updated test case summary. | 3.2.1.1.2 |
|  |  |  | Added new section for Aqua test case. | 3.3 |
|  |  |  | Updated filenames and added surface albedo history and site list filenames. | Table C-3 |
| 08/19/09 | R5V1 | 721 | Updated names of tar files. | 2.1 |
|  |  |  | Updated directory information. | 2.2, 3.1, 3.2, 3.3, Appendix B |
|  |  |  | Updated test case statistics. | Table 3-2, Table 3-3 |
| 09/09/10 | R5V2 | 804 | Updated compilation information and tar file names. | Secs. 2.1 & 2.2 |
|  |  |  | Updated compilation script names and information. | Sec. 2.2.1 |
|  |  |  | Updated library and executable information. | Sec. 2.1 |
|  |  |  | Added new section for 3.0 and removed old one. | Sec. 3.0 |
|  |  |  | Updated directory charts. | App. B |
|  |  |  | Updated script and executable names and data file paths. | App. C |
| 12/12/12 | R5V3 | 938 | Updated tar file names. | Sec. 2.1 |
|  |  |  | Removed command line instructions from test cases. | Sec. 3.1.1.1 |
| 06/14/14 | R5V4 | 1017 | Updated tar file names. | Sec. 2.1 |
|  |  |  | Added compilation information for PGE CER7.2.1P2. | Secs. 2.2 & 2.2.2 |
|  |  |  | Added a new section for PGE CER7.2.1P2. | Sec. 3.2 |
|  |  |  | Added ancillary and executable filenames for PGE CER7.2.1P2. | App. C |
|  |  |  | Corrected log file names for PGE CER7.2.1P1. | Sec. 3.1.2.1 |
|  |  |  | Added subsystem overview for PGE CER7.2.1P2. | Sec. 1.2.2 |
|  |  |  | Cleaned up compilation instructions for PGEs CER7.2.1P1 and CER7.2.1P2. | Secs. 2.2, 2.2.1, & 2.2.2 |
|  |  |  | Removed references to P6 testing. | Sec. 3.2.1.1 |
|  |  |  | Changed $host to $CPUTYPE. (04/09/2015) | Sec. 2.2 |
| 09/30/15 | R5V5 | 1089 | Updated tar file names. Added note regarding execution of comparison software. | Sec. 2.1 Sec. 3.2.2 |
| 10/27/16 | R5V6 | 1185 | Updated tar file names. | Sec. 2.1 |
|  |  |  | Updated test case information and added case for NPP and Terra-NPP testing. | Secs. 3.2.1.1, 3.2.2.2, 3.2.2, & 3.2.3 |
|  |  |  | Updated test case information and added case for Terra-NPP testing. (06/22/2017) | Sec. 3.2.1.2 |
|  |  |  | Removed PGE and any references to the following PGE CER7.2.1P1. (02/07/2019) | All |
|  |  |  | Appendix B was removed as it is no longer relevant and replaced with Appendix C. (03/13/2019) | App. B |

Document Revision Record	ii

1.0	Introduction	1

1.1	Document Overview	1

1.2	Subsystem Overview	2

1.2.1	CER7.2.1P2:  CERES Synoptic SARB Subsystem Edition4 Main-Processor	2

2.0	Software and Data File Installation Procedures	3

2.1	Installation	3

2.2	Compilation	3

2.2.1	Compiling PGE 7.2.1P2	4

3.0	Test and Evaluation Procedures for Synoptic SARB	5

3.1	CER7.2.1P2 on the x86 Platform	5

3.1.1	Stand-alone Test Procedures	5

3.1.1.1	Execution	5

3.1.1.2	Test Summary	6

3.1.2	Evaluation Procedures	6

3.1.2.1	Log and Status File Results	7

3.1.2.2	Metadata Evaluation	8

3.1.2.3	Evaluation of Comparison Software Output	8

3.1.3	Solutions to Possible Problems	8

Appendix A - Acronyms and Abbreviations	A-1

Appendix B - File Description Tables	B-1

B.1	Production Scripts and Executables	B-1

B.2	Processing Control Files (PCF), Metadata Control Files (MCF) and Status Message Files (SMF)	B-1

B.3	Ancillary Input Data	B-4

B.4	Output Temporary Data Files (Production Results)	B-5

Table B.1-1.  Production Scripts	B-1

Table B.1-2.  Executables	B-1

Table B.2-1.  Metadata Control Files	B-1

Table B.2-2.  Process Control Files	B-2

Table B.2-3.  Status Message Files (SMF)	B-2

Table B.3-1.  Ancillary Input Data	B-4

Table B.4-1.  Output Temporary Data Files	B-5

# Introduction

CERES is a key component of EOS and NPP.  The first CERES instrument (PFM) flew on TRMM, four instruments are currently operating on the EOS Terra (FM1 and FM2) and Aqua (FM3 and FM4) platforms, and NPP (FM5) platform.  CERES measures radiances in three broadband channels:  a shortwave channel (0.3 - 5 m), a total channel (0.3 - 200 m), and an infrared window channel (8 - 12 m).  The last data processed from the PFM instrument aboard TRMM was March 2000; no additional data are expected.  Until June 2005, one instrument on each EOS platform operated in a fixed azimuth scanning mode and the other operated in a rotating azimuth scanning mode; now all are typically operating in the fixed azimuth scanning mode.  The NPP platform carries the FM5 instrument, which operates in the fixed azimuth scanning mode though it has the capability to operate in a rotating azimuth scanning mode.

CERES climate data records involve an unprecedented level of data fusion:  CERES measurements are combined with imager data (e.g., MODIS on Terra and Aqua, VIIRS on NPP), 4-D weather assimilation data, microwave sea-ice observations, and measurements from five geostationary satellites to produce climate-quality radiative fluxes at the top-of-atmosphere, within the atmosphere and at the surface, together with the associated cloud and aerosol properties.

The CERES project management and implementation responsibility is at NASA Langley.  The CERES Science Team is responsible for the instrument design and the derivation and validation of the scientific algorithms used to produce the data products distributed to the atmospheric sciences community.  The CERES DMT is responsible for the development and maintenance of the software that implements the science team’s algorithms in the production environment to produce CERES data products.  The Langley ASDC is responsible for the production environment, data ingest, and the processing, archival, and distribution of the CERES data products.

## Document Overview

This document, the CERES Release 3 Delivery Test Plan for the CERES Synoptic Surface and Atmospheric Radiation Budget (SARB) Subsystem (Subsystem 7.2), is part of the CERES Subsystem 7.2 Release 3 delivery package provided to the Langley Atmospheric Science Data Center (ASDC).  It provides a description of the CERES Synoptic SARB Subsystem Release 3 software, and explains the procedures for installing, executing, and testing the software.  A section is also included on validating the results of executing the software.  A description of acronyms and abbreviations is provided in Appendix A, and a description of the software and data files is contained in Appendix B.

The document is organized as follows:

Section 1.0 - Introduction

Section 2.0 - Software and Data File Installation Procedures

Section 3.0 - Test and Evaluation Procedures for Synoptic SARB

Appendix A - Acronyms and Abbreviations

Appendix B - File Description Tables

## Subsystem Overview

### CER7.2.1P2:  CERES Synoptic SARB Subsystem Edition4 Main-Processor

The Product Generation Executive (PGE) CER7.2.1P2 processes the CERES Synoptic SARB Subsystem.  This PGE is used in Edition4 processing.  The Synoptic SARB Subsystem Main-Processor computes vertical longwave, shortwave, and flux profiles that span from the surface to the top of the Earth’s atmosphere for each CERES region within a 1-degree latitudinal zone for each hour of the month.  The output is the Synoptic Intermediate (SYNI) product, which contains vertical flux profile data for all CERES regions.  An ASCII Quality Control (QC) report is also produced with each run of the Subsystem.

The SYNI serves as input for CERES Subsystem 8.0, PGE CER8.1P2.

# Software and Data File Installation Procedures

This section describes how to install both the SARB library and the Subsystem 7.2 Synoptic SARB software in preparation for making the necessary test runs at the Langley ASDC.  The installation procedures include instructions for uncompressing and untarring the delivered files, properly defining environmental variables, and compiling the Synoptic SARB programs.

## Installation

Software/Data File Install Procedure:

The scripts, makefiles, and Process Control Files (PCF) in the Subsystem 7.2 delivery package expect the following environment variables, found in the $CERESENV script, to be defined:

PGSDIR	-	Directory for Toolkit libraries

CERESHOME	-	Top Directory for CERES Software

CERESLIB	-	Directory for CERESlib

PGSINC	-	Pointer to the PGS Include file directory

PGSLIB	-	Directory which contains the 64-bit Toolkit library file

PGSMSG	-	Directory which contains Toolkit and CERES

Status Message Files

HDFDIR	-	Pointer to the HDF home directory

The included makefiles for Synoptic SARB redefine the following environment variables for x86 compilation:

F90COMP	-	Fortran 90 compilation flags (use the following options: -c -O2 -fno-second-underscore -fconvert=big-endian)

Change directory to the directory where you plan to install the SARB Subsystems.  (The following instructions assume that the directory will be $CERESHOME.)

Uncompress and untar the Synoptic SARB Subsystem files:

tar xf SynSARB_data_R5-1185.tar

tar xf SynSARB_anc_R5-1185.tar

tar xf SynSARB_src_R5-1185.tar

## Compilation

Instructions for generating the executable for PGE CER7.2.1P2 are contained in Section 2.2.1.  All libraries and executables will contain the platform type in the names.  In this document, the variable $CPUTYPE will be x86_64.   At this time, testing is done only on the x86 platform.

### Compiling PGE 7.2.1P2

PGE CER7.2.1P2:

For full subsystem deliveries, these commands will compile all the software:

cd $CERESHOME/sarb/CER7.2.1P2/rcf

./compile_CER7.2.1P2.pl all

OR

The individual libraries and exectuables can be compiled with these commands:

- The Status Message Files can be made by typing:

cd $CERESHOME/sarb/CER7.2.1P2/rcf

./compile_CER7.2.1P2.pl smf

The SARB Libraries can be made by typing:

cd $CERESHOME/sarb/CER7.2.1P2/rcf

./compile_CER7.2.1P2.pl fulib

cd $CERESHOME/sarb/CER7.2.1P2/rcf

./compile_CER7.2.1P2.pl lib

- As these are software libraries, no executable is generated.  The message “creating CER7.2.1P2_$CPUTYPE.a” appears at the end of successful compilation.  The file, CER7.2.1P2_$CPUTYPE.a, remains in the $CERESHOME/sarb/CER7.2.1P2/lib/ directory

- The Subsystem 7.2 Main-Processor executable can be made by typing:

cd $CERESHOME/sarb/CER7.2.1P2/rcf

./compile_CER7.2.1P2.pl src

The resulting executable,CER7.2.1P2_$CPUTYPE.exe, is stored in the directory $CERESHOME/sarb/CER7.2.1P2/bin.

Execute the following to compile the comparison software for the Main-Processor output:

cd $CERESHOME/sarb/CER7.2.1P2/rcf

./compile_CER7.2.1P2.pl test

The resulting executable,CER7.2.1P2Comp_$CPUTYPE.exe, remains in the directory $CERESHOME/sarb/CER7.2.1P2/test_suites.

# Test and Evaluation Procedures for Synoptic SARB

This section provides general information on how to execute the Subsystem 7.2 PGE and provides an overview of the test and evaluation procedures.  It includes a description of what is being tested and the order in which the tests should be performed.

## CER7.2.1P2 on the x86 Platform

### Stand-alone Test Procedures

#### Execution

NOTE:  All testing is done on the x86 platform.

CER7.2.1P2:  Terra (Edition4)

setenv PROD no (read input locally)

cd $CERESHOME/sarb/CER7.2.1P2/rcf

source TERRA-env.csh

cd $CERESHOME/sarb/CER7.2.1P2/rcf

CER7.2.1P2-SGE_Driver.pl -date 200110 -zone 090 -platform x86 -clean

CER7.2.1P2:  Terra-Aqua (Edition4)

setenv PROD no (read input locally)

cd $CERESHOME/sarb/CER7.2.1P2/rcf

source TERRA-AQUA-env.csh

cd $CERESHOME/sarb/CER7.2.1P2/rcf

CER7.2.1P2-SGE_Driver.pl -date 201304 -zone 090 -platform x86 -clean

CER7.2.1P2:  NPP (Edition4)

setenv PROD no (read input locally)

cd $CERESHOME/sarb/CER7.2.1P2/rcf

source NPP-env.csh

cd $CERESHOME/sarb/CER7.2.1P2/rcf

CER7.2.1P2-SGE_Driver.pl -date 201304 -zone 090 -platform x86 –clean

CER7.2.1P2:  Terra-NPP (Edition4)

setenv PROD no (read input locally)

cd $CERESHOME/sarb/CER7.2.1P2/rcf

source TERRA-NPP-env.csh

cd $CERESHOME/sarb/CER7.2.1P2/rcf

CER7.2.1P2-SGE_Driver.pl -date 201304 -zone 090 -platform x86 -clean

Exit Codes

0	-	Normal Exit,

200	-	Fatal Error.

#### Test Summary

CER7.2.1P2:  Terra

Total Run Time:	13 hours

CER7.2.1P2:  Terra-Aqua

Total Run Time:	13 hours

CER7.2.1P2:  NPP

Total Run Time:	13 hours

CER7.2.1P2:  Terra-NPP

Total Run Time:	12 hours

### Evaluation Procedures

This section provides information on how to execute the comparison software for the Synoptic SARB Subsystem PGE CER7.2.1P2.

NOTE:  The comparison software must be executed on bj21.

CER7.2.1P2:  Terra

To compare the created output data:

unlimit

cd $CERESHOME/sarb/CER7.2.1P2/rcf

source TERRA-env.csh

cd $CERESHOME/sarb/CER7.2.1P2/test_suites

compare_CER7.2.1P2_files.pl

CER7.2.1P2:  Terra-Aqua

To compare the created output data:

unlimit

cd $CERESHOME/sarb/CER7.2.1P2/rcf

source TERRA-AQUA-env.csh

cd $CERESHOME/sarb/CER7.2.1P2/test_suites

compare_CER7.2.1P2_files.pl

CER7.2.1P2:  NPP

To compare the created output data:

unlimit

cd $CERESHOME/sarb/CER7.2.1P2/rcf

source NPP-env.csh

cd $CERESHOME/sarb/CER7.2.1P2/test_suites

compare_CER7.2.1P2_files.pl

CER7.2.1P2:  Terra-NPP

To compare the created output data:

unlimit

cd $CERESHOME/sarb/CER7.2.1P2/rcf

source TERRA-NPP-env.csh

cd $CERESHOME/sarb/CER7.2.1P2/test_suites

compare_CER7.2.1P2_files.pl

#### Log and Status File Results

There are five Log files associated with this PGE.  The first three listed below are required by the Toolkit. The Toolkit Log files contain all error and/or status messages produced by the PGE during processing.

- Report Log File:  $CERESHOME/sarb/runlogs/CER7.2.1P2/CER7.2.1P2_LogReport_$SS7_2_$PS7_2_$CC7_2.YYYYMMZ{$zone}   
The Report Log File contains Instrument-related informational messages.  These messages may be strictly informative (Error Type = Status or Warning) or may indicate a fatal condition that results in premature PGE termination (Error Type = Fatal).

- Status Log File:  $CERESHOME/sarb/runlogs/CER7.2.1P2/CER7.2.1P2_LogStatus_$SS7_2_$PS7_2_$CC7_2.YYYYMMZ{$zone}   
The Status Log File contains all messages created by the Toolkit and Instrument-related messages that can lead to abnormal ending of the Preprocessor.  If an abnormal exit is encountered by the PGE, this file should be examined for ’_E_’, (error) or ’_F_’ (fatal) message types.

- User Log File:  $CERESHOME/sarb/runlogs/CER7.2.1P2/CER7.2.1P2_LogUser_$SS7_2_$PS7_2_$CC7_2.YYYYMMZ{$zone}   
The User Log File is not used at this time, but exists to satisfy the Toolkit requirements.  Typically the _U_ and _N_ (User information and Notice) will be written to User Log File and Status Log File.

- PCF Log File:  $CERESHOME/sarb/CER7.2.1P2/rcf/pcf/CER7.2.1P2_PCF_$SS7_2_$PS7_2_$CC7_2.YYYYMMZ{$zone}.log

This log file is created when the PCF is generated and contains a listing of all the environment variables set when the PCF was created along with a listing of all the files used to create this PCF.  There is also a listing of any missing optional and mandatory files. The list of existing output data files will only be created if the PGE is run more than once without clean-up.

#### Metadata Evaluation

TBD

#### Evaluation of Comparison Software Output

All comparisons done in Section 3.1.1.1 by the test script should look like the following:

SUCCESSFUL

If an error in a file comparison is found the following message will be displayed:

ERROR: Check comparison file

The comparison file will be here:

{$CERESHOME}/sarb/CER7.2.1P2/test_suites

CER_SYNI_$SS7_2_$PS7_2_$CC7_2.{$year}{$month}Z{$zone}.compare

NOTE:  The SYNI files in the directory matching the $SS7_2, $PS7_2 and $CC7_2 will be compared.

### Solutions to Possible Problems

All SYNI data should be deleted before rerunning any of the above tests.   This can be done by using the following commands:

cd $CERESHOME/sarb/CER7.2.1P2/rcf

source TERRA-env.csh

cd $CERESHOME/sarb/CER7.2.1P2/test_suites

test_cleanup_CER7.2.1P2.pl 200110Z090

cd $CERESHOME/sarb/CER7.2.1P2/rcf

source TERRA-AQUA-env.csh

cd $CERESHOME/sarb/CER7.2.1P2/test_suites

test_cleanup_CER7.2.1P2.pl 201304Z090

cd $CERESHOME/sarb/CER7.2.1P2/rcf

source TERRA-NPP-env.csh

cd $CERESHOME/sarb/CER7.2.1P2/test_suites

test_cleanup_CER7.2.1P2.pl 201304Z090

cd $CERESHOME/sarb/CER7.2.1P2/rcf

source NPP-env.csh

cd $CERESHOME/sarb/CER7.2.1P2/test_suites

test_cleanup_CER7.2.1P2.pl 201304Z090

Acronyms and Abbreviations

ASDC	Atmospheric Science Data Center

CERES	Clouds and the Earth’s Radiant Energy System

CERESlib	CERES library

CRS	Clouds and Radiation Swath

CRSB	Clouds and Radiation Swath Binary

DAAC	Distributed Active Archive Center

DRIVTAB	Derivative Table

EOS	Earth Observing System

EOS-AM	EOS Morning Crossing Mission

EOS-PM	EOS Afternoon Crossing Mission

ERBE	Earth Radiation Budget Experiment

ERBS	Earth Radiation Budget Satellite

FOV	Field-of-View

HDF	Hierarchical Data Format

LaTIS	Langley TRMM Information System

MCF	Metadata Control Files

NASA	National Aeronautics and Space Administration

NOAA	National Oceanic and Atmospheric Administration

PCF	Process Control File

PGE	Product Generation Executive

QC	Quality Control

SARB	Surface and Atmospheric Radiation Budget

SCF	Science Computing Facility

SMF	Status Message Facility

SYNI	Synoptic Intermediate Product

TRMM	Tropical Rainfall Measuring Mission

TSIB	Time Space Interpolate Binary Product

File Description Tables

Production Scripts and Executables

The following scripts must be moved to the production environment.

Table B.1-1.  Production Scripts

| File Name | Format | Description |
| --- | --- | --- |
| CER7.2.1P2_pcfgen.pl | ASCII | Perl script which creates the PCF for the Edition4 Main-Processor |
| run_CER7.2.1P2.pl | ASCII | Perl script which executes the Edition4 Main-Processor |
| CER7_2_1P2_Env.pm | ASCII | Perl module for passing env variables |
| CER7_2_1P2_FileUtils.pm | ASCII | Perl module containing needed subroutines |
| CER7.2.1P2-Launch.pl | ASCII | Perl script to send jobs to SGE |
| CER7.2.1P2-SGE_Driver.pl | ASCII | Perl script to process commands and run SGE |
| compile_CER7.2.1P2.pl | ASCII | Perl script to compile libraries and executables |

Table B.1-2.  Executables

| File Name | Format | Description |
| --- | --- | --- |
| CER7.2.1P2_x86_64.exe1 | Binary | Edition4 Main-Processor executable |
| 1. These files will be generated on execution of Subsystem software and are not included in the tar file. |

Processing Control Files (PCF), Metadata Control Files (MCF) and Status Message Files (SMF)

The Process Control Files are not included in the Software Delivery Package.  They will be created by the PCF generator scripts.

Table B.2-1.  Metadata Control Files

| File Name | Format | Description |
| --- | --- | --- |
| mcf_sarbsynqc | ODL | MCF for Binary QC Report for Main-Processor |
| mcf_sarbsyn | ODL | MCF for Binary CRS file for Main-Processor |

Table B.2-2.  Process Control Files

| File Name | Format | Description |
| --- | --- | --- |
| CER7.2.1P2_PCF_Terra-FM1-MODIS_SSIT_000000.199807Z0901 | ASCII | Process Control File for Edition4 Main-Processor |
| 1. These files will be generated on execution of Subsystem software and are not included in the tar file. |

| Table B.2-3. Status Message Files (SMF) |
| --- |
| File Name | Format | Directory | Description |
| ANCINIT_25725.t | ASCII | smf/sarb | Toolkit Message File |
| PGS_257251 | ASCII | PGS_message/sarb | Toolkit Message File |
| FLSALUT_25724.t | ASCII | smf/sarb | Toolkit Message File |
| PGS_257241 | ASCII | PGS_message/sarb | Toolkit Message File |
| GFDLAER_25716.t | ASCII | smf/sarb | Toolkit Message File |
| PGS_257161 | ASCII | PGS_message/sarb | Toolkit Message File |
| HCMOCNALB_225723.t | ASCII | smf/sarb | Toolkit Message File |
| PGS_2257231 | ASCII | PGS_message/sarb | Toolkit Message File |
| IGBPUTIL_25721.t | ASCII | smf/sarb | Toolkit Message File |
| PGS_257211 | ASCII | PGS_message/sarb | Toolkit Message File |
| INITSARB_25701.t | ASCII | smf/sarb | Toolkit Message File |
| PGS_257011 | ASCII | PGS_message/sarb | Toolkit Message File |
| MSFCALBIO_25722.t | ASCII | smf/sarb | Toolkit Message File |
| PGS_257221 | ASCII | PGS_message/sarb | Toolkit Message File |
| PGS_INGEST_25702.t | ASCII | smf/sarb | Toolkit Message File |
| PGS_257021 | ASCII | PGS_message/sarb | Toolkit Message File |
| PGS_SIGMALOAD_25703.t | ASCII | smf/sarb | Toolkit Message File |
| PGS_257031 | ASCII | PGS_message/sarb | Toolkit Message File |
| PGS_TUNEDRV_25704.t | ASCII | smf/sarb | Toolkit Message File |
| PGS_257041 | ASCII | PGS_message/sarb | Toolkit Message File |
| PGS_FLXRANGE_25705.t | ASCII | smf/sarb | Toolkit Message File |
| PGS_257051 | ASCII | PGS_message/sarb | Toolkit Message File |
| PGS_FLMODEL_25706.t | ASCII | smf/sarb | Toolkit Message File |
| PGS_257061 | ASCII | PGS_message/sarb | Toolkit Message File |
| SARBMETA_25726.t | ASCII | smf/sarb | Toolkit Message File |
| PGS_257261 | ASCII | PGS_message/sarb | Toolkit Message File |
| PGS_MODISAERRD_25751.t | ASCII | smf/sarb | Toolkit Message File |
| PGS_25751 | ASCII | PGS_message/sarb | Toolkit Message File |
| SARBIOUTIL_25750.t | ASCII | smf/sarb | Toolkit Message File |
| PGS_25750 | ASCII | PGS_message/sarb | Toolkit Message File |
| PGS_SFCALBCALC_25707.t | ASCII | smf/sarb | Toolkit Message File |
| PGS_257071 | ASCII | PGS_message/sarb | Toolkit Message File |
| PGS_SFCALBINGEST_25708.t | ASCII | smf/sarb | Toolkit Message File |
| PGS_257081 | ASCII | PGS_message/sarb | Toolkit Message File |
| PGS_DERIVLOAD_25709.t | ASCII | smf/sarb | Toolkit Message File |
| PGS_257091 | ASCII | PGS_message/sarb | Toolkit Message File |
| PGS_WRAPSARB_25710.t | ASCII | smf/sarb | Toolkit Message File |
| PGS_257101 | ASCII | PGS_message/sarb | Toolkit Message File |
| INITSYN_26003.t | ASCII | smf/sarb | Toolkit Message File |
| PGS_26003 | ASCII | PGS_message/sarb | Toolkit Message File |
| REGDRV_26005.t | ASCII | smf/sarb | Toolkit Message File |
| PGS_26005 | ASCII | PGS_message/sarb | Toolkit Message File |
| TSIRET_26004.t | ASCII | smf/sarb | Toolkit Message File |
| PGS_26004 | ASCII | PGS_message/sarb | Toolkit Message File |
| WRAPSYN_26006.t | ASCII | smf/sarb | Toolkit Message File |
| PGS_26006 | ASCII | PGS_message/sarb | Toolkit Message File |
| 1. These files will be generated on execution of Subsystem software and are not included in the tar file. |

Ancillary Input Data

The Synoptic SARB Subsystem accesses several ancillary input data files.  Files for PGE CER7.2.1P2 are located in $CERESHOME/sarb/ancillary/CER7.2.1P2.

| Table B.3-1. Ancillary Input Data |
| --- |
| File Name | Format | Description | Static/Dynamic |
| SS5_DrivTab_19990315 | Binary | Derivative tables | Static |
| IGBP_Ver3.0 | Binary | IGBP map | Static |
| SigTab_Synoptic_20141204 | ASCII | Sigma tables | Static |
| ControlFile_20141204 | ASCII | Drives selection of data sources based on specified record conditions | Static |
| SS5_ZJin_OcnAlb_20011218 | Binary | Coefficients for Zhonghai Jin surface albedo over ocean retrieval | Static |
| flsa0404_lut.2s.coef | Binary | Surface Albedo look up table for Fu-Liou model | Static |
| flsa3_lut.4s.coef_19991215 | Binary | Surface Albedo look up table for Fu-Liou model | Static |
| flsa4_lut.2s.coef_19991215 | Binary | Surface Albedo look up table for Fu-Liou model | Static |
| flsa200508c.fubin.tab | Binary | Surface Albedo look up table for Fu-Liou model | Static |
| SAH.v5.yyyymm (in sahmaps) | Binary | Surface albedo history look up tables | Static |
| MATCH_TERRA_AOTS_CLIM_ MODIS.mm (in MATCH path) | Binary | Match climatology data for Terra processing | Static |
| chlor_clim.mm (in ancillary/CER7.2.1P2/chlor_clim) | Binary | Seasonal climatology of chlorophyll used as an input to the Z. Jin Ocean spectral surface albedo | Static |
| indxs_nesds.dat (in ancillary/CER7.2.1P2/iceage) | Binary | Monthly chlorophyll based on seawifs data | Static |
| seawifs_chlor.yyyymm (in ancillary/CER7.2.1P2/seawifs) | Binary | Monthly chlorophyll based on seawifs data | Static |
| zjin.ice.bin.1 (in ancillary/CER7.2.1P2/zjin) | Binary | Ice look up tables of Zhonhai Jin's spectral surface albedo | Static |
| zjin.snow.bin.1 (in ancillary/CER7.2.1P2/zjin) | Binary | Snow look up tables of Zhonhai Jin's spectral surface albedo | Static |
| zjin_ocean_feb04.bin (in ancillary/CER7.2.1P2/zjin) | Binary | Ocean look up tables of Zhonhai Jin's spectral surface albedo | Static |

Output Temporary Data Files (Production Results)

Table B.4-1.  Output Temporary Data Files

| File Name | Format | Description |
| --- | --- | --- |
| CER_SARBCRH_Terra-Aqua-MODIS_SSIT_999999.200407Z0901 | ASCII | Temporary data file created during execution of PGE 7.2.1P2 |
| 1. These files will be generated on execution of Subsystem software and are not included in the tar file. |