Clouds and the Earth's Radiant Energy System

(CERES)

Data Management System

CERES Grid TOA and Surface Fluxes for

Instantaneous Surface Product
(Subsystem 9.0)

Release 5 Test Plan

Version 16

Primary Authors

Kay Costulis2, Rajalekshmy Raju1, and Joe Stassi1

1Science Systems and Applications, Inc. (SSAI)

One Enterprise Parkway, Suite 200

Hampton, VA  23666

2NASA Langley Research Center

Mail Stop 423

Hampton, VA  23681-2199

NASA Langley Research Center

Climate Science Branch

Science Directorate

21 Langley Boulevard

Hampton, VA  23681-2199

SW Delivered to CM:  March 2017

Document Date:  March 2017

Document Revision Record

The Document Revision Record contains information pertaining to approved document changes.  The table lists the date the Software Configuration Change Request (SCCR) was approved, the Release and Version Number, the SCCR number, a short description of the revision, and the revised sections.  The document authors are listed on the cover.  The Head of the CERES Data Management Team approves or disapproves the requested changes based on recommendations of the Configuration Control Board.

| Document Revision Record |
| --- |
| SCCR Approval Date | Release/ Version Number | SCCR Number | Description of Revision | Section(s) Affected |
| 06/25/01 | R3V3 | 274 | The CC9 configuration code was updated from “000000” to “000001” in the expected output filenames. | Secs. 3.3, 4.5.1.2, 4.5.1.3, 4.6.1.1, 4.6.1.2, 4.7.1.1, & 4.7.1.2 |
|  |  |  | Updated format to comply with standards. | All |
| 09/25/01 | R3V4 | 298 | The CC9 configuration code was updated from “000001” to “000000” in the expected output filenames. | Secs. 3.3, 4.2.1.2, 4.2.1.3, 4.3.1.1, 4.3.1.2, 4.4.1.1, 4.4.1.2, 4.5.1.2, 4.5.1.3, 4.6.1.1, 4.6.1.2, 4.7.1.1, & 4.7.1.2 |
|  |  |  | Updated format to comply with standards. | All |
| 11/13/01 | R3V5 | 309 | The CC9.1 configuration code was updated from “111111” to ”009010” in the expected output filenames. | Secs. 3.3 & 4.1.1.3 |
|  |  |  | Updated format to comply with standards. | All |
| 03/15/02 | R3V6 | 326 | Test output section was updated to remove range file name. | Sec. 3.3 Sec. 4.8 |
|  |  |  | Updated format to comply with standards. | All |
| 07/08/02 | R3V7 | 374 | The CC9 and CC6 configuration codes were updated from “000000” to “000001” in the expected output filenames. | Secs. 3.3, 4.2.1.2, 4.2.1.3, 4.3.1.1, 4.3.1.2, 4.4.1.1, 4.4.1.2, 4.5.1.2, 4.5.1.3, 4.6.1.1, 4.6.1.2, 4.7.1.1, & 4.7.1.2 |
|  |  |  | Updated format to comply with standards. | All |
| 10/04/02 | R3V8 | 388 | A second automated script is added. The runtest1 script tests Subsystem 6 PGEs with TRMM input. The runtest script tests Subsystem 9 PGEs with Terra data. | Sec. 3.2 |
| 10/04/02 (Cont’d) | R3V8 | 388 | Update the list of expected output from automated tests. New outputs added for CER9.1-4 December 2000 tests (runtest script). Outputs for CER9.2-4 February 1998 were removed. | Sec. 3.3 |
|  |  |  | Now two sets of test procedures for PGE CER9.1P1: one with 199802 date for testing TRMM data and one with 200012 date for testing Terra. | Secs. 4.1 & 4.2 |
|  |  |  | Changed from env-variable-test-set.csh script to env-variable-test1-set.csh for the Subsystem 6 PGEs. | Secs. 4.3.1, 4.4.1, & 4.5.1 |
|  |  |  | Changed TRMM-PFM-VIRS_ ValidationR3 code to Terra-FM2-MODIS_TestSuite1 in the output file names for PGEs CER9.2-4P1. | Secs. 4.6.1.2, 4.6.1.3, 4.6.1.4, 4.7.1.1, 4.7.1.2, 4.7.1.3, 4.8.1.1, 4.8.1.2, & 4.8.1.3 |
|  |  |  | Updated format to comply with standards. | All |
| 12/02/02 | R3V9 | 403 | Added new CCcode CC6_3 for PGE CER6.3P1. Added new CCcode CC9_4 for PGE CER9.4P1. | Secs. 4.5 & 4.8 |
|  |  |  | Updated format to comply with standards. | All |
| 01/23/03 | R3V10 | 409 | Updated the list of expected output from automated tests for Subsystem 6.0 TRMM and Terra data processing. | Secs. 2.0, 3.0, 4.3, 4.4, & 4.5 |
|  |  |  | Updated format to comply with standards. | All |
| 02/10/03 | R3V11 | 423 | Updated the list of expected output from automated tests for PGE6.3P1 for Terra data processing. | Secs. 3.3 & 4.5 |
|  |  |  | Updated format to comply with standards. | All |
| 04/24/03 | R3V12 | 435 | Updated tar file names and makefile. | Secs. 2.1 & 2.2 |
|  |  |  | Updated the list of expected output from automated tests for PGEs CER9.2P1, CER9.3P1, and CER9.4P1 for Aqua data processing. | Secs. 3.0, 4.6, 4.7,& 4.8 |
|  |  |  | Updated format to comply with standards. | All |
| 10/29/03 | R3V13 | 476 | Updated the list of expected output from automated tests for PGEs CER6.1P1, CER6.2P1, CER6.3P1, CER9.2P1, CER9.3P1, and CER9.4P1 for Terra data processing. | Secs. 3.0, 4.3, 4.4, 4.5, 4.6, 4.7, & 4.8 |
|  |  |  | Updated format to comply with standards. | All |
| 06/04/04 | R4V1 | 535 | Updated the list of expected output from automated tests for PGEs CER6.1P1, CER6.2P1, CER6.3P1, CER9.2P1, CER9.3P1, and CER9.4P1 for Terra & Aqua data processing. | Secs. 3.0, 4.3, 4.4, 4.5, 4.6, 4.7, & 4.8 |
|  |  |  | Updated format to comply with standards. | All |
| 08/09/04 | R4V2 | 548 | Removed PGEs 6.2, 6.3, 9.3, 9.4 expected output. | Sec. 3.3, |
|  |  |  | Added qa files. | Sec. 4.3.1.3 |
|  |  |  | Added evaluate script name that was missing in the previous version. | Sec. 4.6.2.1 |
|  |  |  | Updated format to comply with standards. | All |
| 11/04/04 | R4V3 | 565 | Added separate Production Strategy, Configuration Code environment variables for each Subsystem 9 PGEs. | Sec. 2.1 |
|  |  |  | Updated output file names. | Secs. 3.3 & 4.7 |
|  |  |  | Updated format to comply with standards. | All |
| 11/29/04 | R4V4 | 571 | Separate environment variable scripts were created for each TISA Gridding PGE. | Secs. 2.1, 4.1.1, 4.2.1, 4.3.1, 4.4.1, 4.5.1, 4.6.1, 4.7.1, & 4.8.1 |
|  |  |  | Updated format to comply with standards. | All |
| 02/07/05 | R4V5 | 575 | Updated to use SGI 64-bit compiler instead of NAG 32-bit. | Secs. 2.2.1 & 3.2 |
|  |  |  | Updated the list of expected output from automated tests for PGEs CER6.1P1, CER6.2P1, and CER6.3P1 for Terra FM1, FM2 data processing. | Secs. 3.0, 4.3, 4.4, & 4.5 |
|  |  |  | Updated format to comply with standards. | All |
| 09/15/05 | R4V6 | 594 | Added two flags (manualrun, testrun) to environment variable scripts. | Sec. 2.1 |
|  |  |  | Updated format to comply with standards. | All |
| 04/02/08 | R5V1 | 672 | Added test procedures for the new PGE CER9.0P1. | Sec. 4.2 |
| 10/21/08 | R5V2 | 684 | Updated tar file names. | Sec. 2.1 |
|  |  |  | Updated the list of expected output in manual tests for PGE CER9.1P1. | Secs. 3.3 & 4.3 |
|  |  |  | Updated directory paths to comply with the new directory structure. | Sec. 4.3, Pgs. B6 - B-9 |
| 10/21/08 | R5V3 | 685 | Updated directory paths to comply with the new directory structure. | Secs. 2.1, 2.2, & 4.4 – 4.9 |
|  |  |  | Added “setenv PROD no” and “unlimit” statements. (02/04/09) | Secs. 4.4.1, 4.5.1, 4.6.1, 4.7.1, 4.8.1, & 4.9.1 |
| 11/25/09 | R5V4 | 746 | Updated pcf, run scripts directory path location from bin directory to rcf directory for PGE CER9.0P1, and updated environment script names to be consistent with the other TISAgrid PGEs. | Secs. 2.2.4 & 4.2 |
| 11/25/09 | R5V5 | 739 | New PGEs (CER9.2P2, CER9.3P2, CER9.4P2) to support Edition3. | Secs. 1.2.9 – 1.2.11 & Sec. 2.3 New Sections |
|  |  |  | Updated directory structure according to the SEC recommendations. | Secs 4.9, 4.10, 4.11 & App. C |
|  |  |  | Updated File Description Tables. | App. D |
| 06/02/10 | R5V6 | 789 | New PGEs (CER9.2P2, CER9.3P2, CER9.4P2) to support Edition3 process on magneto (P4). | Secs. 1.2.9 – 1.2.11 & 2.3 New Sections: 4.10, 4.11, & 4.12 |
|  |  |  | Modified directory structure. | App. B |
|  |  |  | Updated File Description Tables. | App. C |
| 03/22/10 | R5V7 | 763 | New PGEs (CER9.0P2 and 9.0P3) to support ISCCP-D2like-Mrg processing on AMI (P6). | Secs. 1.25, 1.26, 2.1, 2.2.5, 2.2.6, 4.3, & 4.4 |
|  |  |  | Added QA file information and directory path in front of the commands. | Secs. 4.3 & 4.4 |
| 07/25/12 | R5V8 | 914 | Modified executable names, source set_cputype to generate executables in AMI-P6 environment. | Secs. 2.3.1, 2.3.2, & 2.3.3 |
|  |  |  | Modified scripts names and directory paths. Removed file names that no longer generate in AMI-P6 environment. | Secs. 4.5.1, 4.5.2, & 4.5.3 |
|  |  |  | Modified scripts names and directory paths. Removed file names that no longer generate in AMI-P6 environment. | Secs. 4.12.1, 4.12.2, & 4.12.3 |
|  |  |  | Added tables with run time for SGE form AMI-P6 submission. | Table 4-10 |
|  |  |  | Modified scripts names and directory paths. Removed file names that no longer generate in AMI-P6 environment. | Secs. 4.13.1, 4.13.2, & 4.13.3 |
|  |  |  | Added tables with run time for SGE form AMI-P6 submission. | Table 4-11 |
|  |  |  | Modified scripts names and directory paths. Removed file names that no longer generate in AMI-P6 environment. | Secs. 4.14.1, 4.14.2, & 4.14.3 |
|  |  |  | Added tables with run time for SGE form AMI-P6 submission. | Table 4-12 |
|  |  |  | Removed automated test section. | Sec. 3.0 |
|  |  |  | Removed PGEs CER6.1P1, CER6.2P1, CER6.3P1, CER9.1P1 (trmm only), CER9.2P1, CER9.3P1, & CER9.4P1. | Secs. 1.2.1-1.2.3, 1.2.8-1.2.10, 2.2.1-2.2.3, 2.2.8-2.2.10, 4.1-4.1.3, 4.6-4.6.2, 4.7-4.7.3, 4.8-4.8.3, 4.9-4.9.3, 4.10-4.10.3, 4.11-4.11.3 |
| 07/25/12 (Cont’d) | R5V8 | 914 | Updated C code in the filenames. | Secs. 3.4.1.1 & 3.4.1.2 |
|  |  |  | Added a table to include the test runs. | Table 3-4 |
|  |  |  | Updated tables to remove references to PGEs CER6.1P1, CER6.2P1, CER6.3P1, CER9.1P1 (trmm only), CER9.2P1, CER9.3P1, & CER9.4P1. | All Appendix C tables |
|  |  |  | Removed the PCF Generator instructions. | Secs. 3.4.1.1, 3.5.1.1, 3.6.1.1, & 3.7.1.1 |
|  |  |  | Removed the command line execution instructions. | Secs. 3.4.1.2, 3.5.1.2, 3.6.1.2, & 3.7.1.2 |
| 12/25/12 | R5V9 | 915 | Modified executable filenames. | Sec. 2.2.1 |
|  |  |  | Added executable command to evaluate hdf outputs. | Sec. 2.2.2 |
|  |  |  | Modified directory paths. | Sec. 3.1.1 |
|  |  |  | Removed checking inputs. | Sec. 3.1.1.1 |
|  |  |  | Removed the PCF Generator instructions. | Sec. 3.1.1.2 |
|  |  |  | Removed the command line execution instructions. | Sec. 3.1.1.3 |
| 03/21/13 | R5V10 | 961 | Added x86 executable names. | Secs. 2.2.3, 2.2.4, & |
|  |  |  | Updated PGE executaion instructions to include x86. | 3.2.1 |
|  |  |  | Updated runtime summary. | Table 3-2 |
|  |  |  | Updated evaluation procedures. | Sec. 3.2.2.1 |
|  |  |  | Updated PGE execution instructions to include x86. | Sec. 3.3.1.1 |
|  |  |  | Updated runtime summary. | Table 3-3 |
|  |  |  | Updated executable names created on P6 and x86. | Secs. 2.2.3, 3.2.1.1, & 3.3.1.1 |
|  |  |  | Updated output location directory and INSTANCE. | Secs. 3.2.1.1 & 3.3.1.1 |
| 12/12/12 | R5V11 | 940 | Added PGE CER9.0P4 for creating daily subset SSF. | Secs. 1.2.4, 2.2.5, & 3.4 |
|  |  |  | Added PGE CER9.0P5 for creating FluxByCloudTyp data. | Secs. 1.2.5, 2.2.6, & 3.5 |
|  |  |  | Added environment variables and new tar files for PGEs CER9.0P4 and CER9.0P5. | Sec. 2.1 |
| 06/14/14 | R5V12 | 1018 | Initial delivery of PGE CER9.1P2 to process Edition4 PMOA version. | Secs. 1.2.7, 2.2.8, & 3.7 |
|  |  |  | Added the note "This PGE is currently not active." | Secs. 3.4 & 3.5 |
| 04/16/14 | R5V13 | 1010 | Initial delivery of PGE CER9.2P3 to process Edition4 version. | Subsystem Overview, Secs. 1.2.11, 2.4.1, & 3.11 |
|  |  |  | Initial delivery of PGE CER9.3P3 to process Edition4 version. | Subsystem Overview, Secs. 1.2.12, 2.4.2, & 3.12 |
|  |  |  | Initial delivery of PGE CER9.4P3 to process Edition4 version. | Subsystem Overview, Secs. 1.2.13, 2.4.3, & 3.13 |
|  |  |  | Modified compilation command. (09/09/2014) | Secs. 2.2.8, 2.3.1, 2.3.2, 2.3.3, 2.4.1, 2.4.2, & 2.4.3 |
| 02/18/16 | R5V14 | 1113 | Modified test data for NPP. | Sec. 3.11 |
| 01/20/16 | R5V15 | 1108 | Added new PGE CER9.0P6 to create intermediate GEO zonal files using 5-channel GEO pixel data to provide inputs to PGE 9.0P8. | Sec 3.6 |
|  |  |  | Added new PGE CER9.0P7 to create intermediate MODIS zonal files and MOA file to provide inputs to PGE 9.0P8. | Sec 3.7 |
|  |  |  | Added new PGE CER9.0P8 that creates CldTypHist data product that contains GEO-MODIS derived cloud properties as a function of 9 cloud types, similar to ISCCP D2 product, where the cloud properties are stratified by pressure and optical depth. | Sec 3.8 |
| 01/20/16 (Cont'd) | R5V15 | 1108 | Modified "Subsystem Overview." | Secs. 1.2.7, 1.2.8, & 1.2.9, |
|  |  |  | Modified and added environment variables. | Sec. 2.1 |
|  |  |  | Added executables. | Secs. 2.2.7, 2.2.8, & 2.2.9 |
| 03/01/17 | R5V16 | 1237 | Renamed all instances of CER9_0P8-SGE_Driver.pl to CER9.0P8-SGE_Driver.pl to reflect the filename change to be consistent with other run scripts. | Sec. 3.8.1.1 |
|  |  |  | Adjusted Test Run Times. | Tables 3-6, 3-7, & 3-8 |
|  |  |  | Removed PGEs and any references to the following PGEs CER9.0P1, CER9.0P2, CER9.0P3, CER9.0P4, CER9.0P5, CER9.1P1, CER9.2P2, CER9.3P2, and CER9.4P2. (03/07/2019) | All |
|  |  |  | Removed Appendices B and C as they are no longer relevant. (03/13/2019) | Apps. B & C |

Document Revision Record	ii

1.0	Introduction	1

1.1	Document Overview	1

1.2	Subsystem Overview	2

1.2.1	CldTypHistB-GEO Edition4 Processor (PGE 9.0P6)	2

1.2.2	CldTypHistB-MODIS Edition4 Processor (PGE 9.0P7)	2

1.2.3	CldTypHistB-GEO-MODIS Edition4 Processor (PGE 9.0P8)	2

1.2.4	Post-MOA Processor (PGE 9.1P2)	2

1.2.5	CER9.2P3 Processor (Edition4 - PGE 9.2P3)	3

1.2.6	CER9.3P3 Processor (Edition4 - PGE 9.3P3)	3

1.2.7	CER9.4P3 Processor (Edition4 - PGE 9.4P3)	3

2.0	Software and Data File Installation Procedures	4

2.1	Installation	4

2.2	Compilation	5

2.2.1	To create Main processor executable for PGE9.0P6:	5

2.2.2	To create Main processor executable for PGE9.0P7:	6

2.2.3	To create Main processor executable for PGE9.0P8:	6

2.2.4	To create post moa processor executable for PGE9.1P2:	6

2.3	Compilation for Edition 3	6

2.4	Compilation for Edition 4	6

2.4.1	To create main processor executable for PGE9.2P3:	6

2.4.2	To create post processor executable for PGE9.3P3:	7

2.4.3	To create hdf processor executable for PGE9.4P3:	7

3.0	Manual Test and Evaluation Procedures	9

3.1	CER9.0P6 CldTypHist - GEO – Edition4	9

3.1.1	Stand-alone Test Procedures	9

3.1.1.1	Execution	9

3.1.1.2	Exit Codes	10

3.1.1.3	Main Processor CER9.0P6 Test Summary	10

3.1.2	Evaluation Procedures	11

3.1.3	Solutions to Possible Problems	11

3.2	CER9.0P7:  CldTypHist - MODIS - Edition4	12

3.2.1	Stand Alone Test Procedures	12

3.2.1.1	Execution	12

3.2.1.2	Exit Codes	14

3.2.1.3	Test Summary	14

3.2.2	Evaluation Procedures	14

3.2.2.1	Output Evaluation	14

3.2.3	Solutions to Possible Problems	15

3.3	CER9.0P8:  CldTypHist GEO-MODIS Processor	16

3.3.1	Stand Alone Test Procedures	16

3.3.1.1	Execution	16

3.3.1.2	Exit Codes	18

3.3.1.3	Test Summary	18

3.3.2	Evaluation Procedures	18

3.3.2.1	Output Evaluation	18

3.4	CER9.1P2:  Post-MOA Processor – Edition4	20

3.4.1	Stand Alone Test Procedures	20

3.4.1.1	Execution	20

3.4.1.2	Exit Codes	21

3.4.1.3	Test Summary	21

3.4.2	Evaluation Procedures	21

3.4.2.1	Output Evaluation	21

3.4.3	Solutions to Possible Problems	22

3.5	CER9.2P3:  SSF1deg-HR Processor (Edition 4)	23

3.5.1	Stand Alone Test Procedures	23

3.5.1.1	Execution	23

3.5.1.2	Exit Codes	26

3.5.1.3	Test Summary	26

3.5.2	Evaluation Procedures	26

3.5.2.1	Output Evaluation	26

3.5.3	Solutions to Possible Problems	27

3.6	CER9.3P3:  SSF1degB Postprocessor (Edition 4)	28

3.6.1	Stand Alone Test Procedures	28

3.6.1.1	Execution	28

3.6.1.2	Exit Codes	30

3.6.1.3	Test Summary	30

3.6.2	Evaluation Procedures	30

3.6.2.1	Output Evaluation	30

3.6.3	Solutions to Possible Problems	31

3.7	CER9.4P3:  SSF1deg-Hour HDF Processor (Edition 4)	32

3.7.1	Stand Alone Test Procedures	32

3.7.1.1	Execution	32

3.7.1.2	Exit Codes	33

3.7.1.3	Test Summary	33

3.7.2	Evaluation Procedures	34

3.7.2.1	Output Evaluation	34

3.7.3	Solutions to Possible Problems	34

References	35

Appendix A - Acronyms and Abbreviations	A-1

Table 3-1.  Run Times for PGE CER9.0P6	10

Table 3-2.  Run Times for PGE CER9.0P7	14

Table 3-3.  Run Times for PGE CER9.0P8	18

Table 3-4.  Run Times for PGE CER9.1P2	21

Table 3-5.  Run Times for PGE CER9.2P3	26

Table 3-6.  Run Times for PGE CER9.3P3	30

Table 3-7.  Run Times for CER9.4P3	33

# Introduction

CERES is a key component of EOS and NPP.  The first CERES instrument (PFM) flew on TRMM, four instruments are currently operating on the EOS Terra (FM1 and FM2) and Aqua (FM3 and FM4) platforms, and NPP (FM5) platform.  CERES measures radiances in three broadband channels:  a shortwave channel (0.3 - 5 m), a total channel (0.3 - 200 m), and an infrared window channel (8 - 12 m).  The last data processed from the PFM instrument aboard TRMM was March 2000; no additional data are expected.  Until June 2005, one instrument on each EOS platform operated in a fixed azimuth scanning mode and the other operated in a rotating azimuth scanning mode; now all are typically operating in the fixed azimuth scanning mode.  The NPP platform carries the FM5 instrument, which operates in the fixed azimuth scanning mode though it has the capability to operate in a rotating azimuth scanning mode.

CERES climate data records involve an unprecedented level of data fusion:  CERES measurements are combined with imager data (e.g., MODIS on Terra and Aqua, VIIRS on NPP), 4-D weather assimilation data, microwave sea-ice observations, and measurements from five geostationary satellites to produce climate-quality radiative fluxes at the top-of-atmosphere, within the atmosphere and at the surface, together with the associated cloud and aerosol properties.

The CERES project management and implementation responsibility is at NASA Langley.  The CERES Science Team is responsible for the instrument design and the derivation and validation of the scientific algorithms used to produce the data products distributed to the atmospheric sciences community.  The CERES DMT is responsible for the development and maintenance of the software that implements the science team’s algorithms in the production environment to produce CERES data products.  The Langley ASDC is responsible for the production environment, data ingest, and the processing, archival, and distribution of the CERES data products.

## Document Overview

This document, the CERES Grid TOA and Surface Fluxes for Instantaneous Surface Product (Subsystem 9.0) Release 5, Version 8 Test Plan, is part of the CERES Subsystem 9.0 Release 5 delivery package to the Langley Atmospheric Science Data Center (ASDC).  It provides a description of the CERES Subsystem 9.0 Release 5 software and it explains the procedures for installing, executing, and testing the software.  Procedures for validating the test results are also provided in this document.  Appendix A contains a list of Acronyms.

This document is organized as follows:

Section 1.0 - Introduction

Section 2.0 - Software and Data File Installation Procedures

Section 3.0 - Test and Evaluation Procedures

Appendix A - Acronyms and Abbreviations

## Subsystem Overview

CERES Grid Single Satellite Fluxes and Clouds and Compute Spatial Averages and CERES Grid TOA and Surface Fluxes for Instantaneous Surface Product Subsystem 9 provide the transformation from instantaneous, instrument-referenced data to spatially-averaged Earth-referenced data.  This Subsystem performs two major functions:  gridding and spatial averaging.  The gridding function assigns CERES footprints to the appropriate regional hour box.  The spatial averaging function computes spatial averages of the various radiative flux parameters and cloud properties over each regional hour box.  After passing through this Subsystem, the CERES data lose their traceability to specific CERES measurements.  The input product of Subsystem 9 is Single Satellite TOA; Surface Flux and Cloud Pixels (SSF); and Meteorological, Ozone, and Aerosol (MOA).  The output products are Single Satellite TOA, Surface Flux and Cloud Pixels (SFC); and Post Meteorological, Ozone, and Aerosol (PMOA).  Details of the SSF, MOA, and SFC data products can be found in the CERES Data Management System Data Products Catalog (Reference 1).  PMOA is an intermediate product produced and used only by the Time Interpolation and Spatial Averaging (TISA) Subsystems.  Subsystem 9 consists of four Product Generation Executives (PGE) which are described in the following sections.

### CldTypHistB-GEO Edition4 Processor (PGE 9.0P6)

This PGE CER9.0P6 reads pixel level cloud data from the GEO Satellites’ image files.  The pixels are assigned to a regional hour box based on GMT time associated with it.  The pixels in each regional hour box are averaged and written to zonal files.

### CldTypHistB-MODIS Edition4 Processor (PGE 9.0P7)

The PGE CER9.0P7 Processor grids and spatially averages the footprint data from the CERES Single Satellite Cloud Pixels (SSF) data product.  The footprints are assigned to a regional hour box based on GMT time associated with the footprint.  The footprints in each regional hour box are averaged together and written to 180 zonal files.  In addition, this processor grids and spatially averages MOA data product and written to one binary file.

### CldTypHistB-GEO-MODIS Edition4 Processor (PGE 9.0P8)

The PGE CER9.0P8 creates CldTypHist HDF data product contains GEO-MODIS derived cloud properties as a function of 9 cloud types, similar to ISCCP D2 product, where the cloud properties are stratified by pressure and optical depth.  In addition, it produces CldTypHist-GEO and CldTypHist_MODIS HDF QC files.

### Post-MOA Processor (PGE 9.1P2)

The Post-MOA Processor processes the hourly MOA products for a given month to produce a monthly PMOA data product.  The monthly PMOA data product is organized in four files which contain regional-hourly records sorted by region and then by hour for the CERES 1.0-degree nested regions.  The Post-MOA Processor requires at least one day (24 hours) of MOA data in order to process; however, if available, it can process the whole month of MOA data, or it can process multiple days of MOA data.  The PMOA data product is a subset of the MOA data product.

### CER9.2P3 Processor (Edition4 - PGE 9.2P3)

The CER9.2P3 Processor grids and spatially averages the footprint data from the CERES SSF data product.  The footprints are assigned to a regional hour box based on the GMT time associated with the footprint.  The footprints in each regional hour box are averaged together and written to an hourly SSF1deg-HR intermediate product.

### CER9.3P3 Processor (Edition4 - PGE 9.3P3)

The CER9.3P3 Processor sorts and merges the hourly SSF1deg-HR intermediate products for a given month to produce a monthly SSF1deg-HourB, SSF1deg-HourD data products.  The monthly SSF1deg-HourB data product is organized in 180 zonal files that contain regional hour boxes sorted by region and then by hour.  The monthly SSF1deg-HourD data product is organized in 31 daily files that contain regional hour boxes sorted by region and then by hour.  The Processor only produces the monthly SSF1deg-HourB, SSF1deg-HourD files which contain regional hour box data.

### CER9.4P3 Processor (Edition4 - PGE 9.4P3)

The CER9.4P3 Processor converts the daily SSF1deg-HourD files for a given month into a daily SSF1deg-Hour HDF data product.  The regional hour box data of a daily file is written to HDF VData where the records of the VData are sorted by region and then hour.

# Software and Data File Installation Procedures

This section describes how to install the Subsystem 9.0 TISA Gridding software in preparation for making the necessary test runs at the Langley ASDC.  The installation procedures include instructions for uncompressing and untarring the delivered tar files, properly defining environmental variables, and recompiling the TISA Gridding software.

## Installation

Software/Data File Install Procedure:

In the installation instructions, use the following definitions for the TAG variable, which is included in the file name of the delivery files.

TAG = R{R#}-{SCCR#}

where 	R# = CERES Software Release TISA Gridding Number

SCCR# = SCCR Number for TISA Gridding Delivery

Ex:	TAG= R2-050

For CERES Software Release 3 and TISA Gridding SCCR #274

The scripts, makefiles, and Process Control files in the Subsystem 9 delivery package expect the following environment variables to be set:

CERESENV	-	Pathname and script name for ceres-env.csh

PGSDIR	-	Directory for Toolkit libraries

PGSMSG	-	Directory to store the PGS message files

PGSINC	-	Directory to store the PGS include files

F90	-	Pointer to the SGI 64 bit compiler

CERESHOME	-	Top Directory for CERES Software

CERESLIB	-	Directory for CERESlib ($CERESHOME/lib)

HDFDIR	-	Pointer to the HDF home directory

SS4_5	-	Sampling Strategy for SSF {FM1 for Terra; FM3 for Aqua}

SS4_5_2	-	Sampling Strategy for SSF {FM2 for Terra; FM4 for Aqua}

SS9	-	Sampling Strategy for SFC

SS9_0	-	Sampling Strategy for ISCCP-D2like

SS9_4	-	Sampling Strategy for SSFS-Day

SS9_5	-	Sampling Strategy for FluxByCloudTyp

SS9_0G		Sampling Strategy for CldTypHist-GEO

SS9_0T		Sampling Strategy for CldTypHist-MODIS – Terra

SS9_0A		Sampling Strategy for CldTypHist-MODIS – Aqua

SS9_0M		Sampling Strategy for CldTypHist-MODIS – MOA

SS12	-	Sampling Strategy for MOA

PS4_5	-	Production Strategy for SSF

PS9	-	Production Strategy for SFC

PS9_0	-	Production Strategy for ISCCP-D2like, CldTypHist (Edition4)

PS9_4	-	Production Strategy for SSFS-Day

PS9_5	-	Production Strategy for FluxByCloudTyp

PS9_3	-	Production Strategy for SFCB, PGE CER9.3P3

PS12	-	Production Strategy for MOA

CC4_5	-	Configuration Code for SSF

CC9_1	-	Configuration Code for PMOA

CC9	-	Configuration Code for SFC, PGE CER9.2P3

CC9_0	-	Configuration Code for ISCCP-D2like, CldTypHist (Edition4)

CC9_4	-	Configuration Code for SSFS-Day

CC9_5	-	Configuration Code for FluxByCloudTyp

CC9_3	-	Configuration Code for SFCB, PGE CER9.3P3

CC9_4	-	Configuration Code for SFC HDF, PGE CER9.4P3

CC12	-	Configuration Code for MOA

SW9_1	-	Software Configuration Code for PMOA

SW9	-	Software Configuration Code for SFC

SW9_0	-	Software Configuration Code for ISCCP-D2like, CldTypHist

DATA9_1	-	Data Configuration Code for PMOA

DATA9	-	Data Configuration Code for SFC

DATA9_0	-	Data Configuration Code for ISCCP-D2like, CldTypHist

Change directory to the directory where you plan to install the TISA Gridding Subsystems.  (The following instructions assume that the directory will be $CERESHOME.)

Uncompress and untar the tar files by typing the following commands:

For most PGEs:

cp (or mv) TISAgrid9_*_{TAG}.tar.Z $CERESHOME

cd $CERESHOME

uncompress TISAgrid9_*_{TAG}.tar.Z

## Compilation

- Create the message files and message include file.

cd $CERESHOME/tisa_grid/smf

$CERESLIB/bin/smfcompile_all.csh

Complete the following steps to compile the TISA Gridding source code for each PGE.

### To create Main processor executable for PGE9.0P6:

set RCFDIR = $CERESHOME/tisa_grid/CER9.0P6/rcf

$RCFDIR/compile_9.0P6.csh

The following executable will be created on x86 in the $CERESHOME/tisa_grid/CER9.0P6/bin directory:

CER9.0P6_post_x86_64.exe

CER9.0P6_x86_64.exe

### To create Main processor executable for PGE9.0P7:

set RCFDIR = $CERESHOME/tisa_grid/CER9.0P7/rcf

$RCFDIR/compile_9.0P7.csh

The following executable will be created on x86 in the $CERESHOME/tisa_grid/CER9.0P7/bin directory:

CER9.0P7_MOA_x86_64.exe

CER9.0P7_x86_64.exe

### To create Main processor executable for PGE9.0P8:

set RCFDIR = $CERESHOME/tisa_grid/CER9.0P8/rcf

$RCFDIR/compile_9.0P8.csh

The following executable will be created on x86 in the $CERESHOME/tisa_grid/CER9.0P8/bin directory:

CER9.0P8merge_x86_64.exe

### To create post moa processor executable for PGE9.1P2:

source $CERESENV

source $CERESHOME/lib/common/set_cputype.csh

cd $CERESHOME/tisa_grid/CER9.1P2/rcf

./compile_9.1P2.csh

The following executable will be created in the $CERESHOME/tisa_grid/CER9.1P2/bin directory:

CER9.1P2_${CPU_TYPE}.exe

## Compilation for Edition 3

## Compilation for Edition 4

### To create main processor executable for PGE9.2P3:

source $CERESENV

source $CERESHOME/lib/common/set_cputype.csh

cd $CERESHOME/tisa_grid/CER9.2P3/rcf

compile_9.2P3.csh

The following executable will be created in the $CERESHOME/tisa_grid/CER9.2P3/bin directory:

CER9.2P3_${CPU_TYPE}.exe

cd $CERESHOME/tisa_grid/CER9.2P3/test_suites

make clean

make

The following executable will be created in the $CERESHOME/tisa_grid/CER9.2P3/test_suites directory:

cmp_9.2P3_output_${CPU_TYPE}.exe

### To create post processor executable for PGE9.3P3:

source $CERESENV

source $CERESHOME/lib/common/set_cputype.csh

cd $CERESHOME/tisa_grid/CER9.3P3/rcf

compile_9.3P3.csh

The following executable will be created in the $CERESHOME/tisa_grid/CER9.3P3/bin directory:

CER9.3P3_${CPU_TYPE}.exe

cd $CERESHOME/tisa_grid/CER9.3P3/test_suites

make clean

make

The following executable will be created in the $CERESHOME/tisa_grid/CER9.3P3/test_suites directory:

cmp_9.3P3_output_${CPU_TYPE}.exe

### To create hdf processor executable for PGE9.4P3:

source $CERESENV

source $CERESHOME/lib/common/set_cputype.csh

cd $CERESHOME/tisa_grid/CER9.4P3/rcf

compile_9.4P3.csh

The following executable will be created in the $CERESHOME/tisa_grid/CER9.4P3/bin directory:

CER9.4P3_${CPU_TYPE}.exe

NOTES:

The smfcompile_all.csh script and the makefile script will send a message to the screen at completion to indicate whether or not all operations performed were successful.  If problems are encountered, contact one of the Tisa Gridding analysts before proceeding further.

ASDC personnel may have an alternate procedure for compiling the message files.  Any alternate procedure should copy all message include files to the $PGSINC directory and all message files to the $PGSMSG directory.

# Manual Test and Evaluation Procedures

This section provides general information on how to execute Subsystem 9.0 and provides an overview of the test and evaluation procedures.  It includes a description of what is being tested and the order in which the tests should be performed.

## CER9.0P6 CldTypHist - GEO – Edition4

### Stand-alone Test Procedures

The CER9.0P6 test procedures cannot be run unless the appropriate environment scripts are run and environment variables are set.

Test-specific environment variables such as Sampling Strategy, Production Strategy, Configuration Code, and Software and Data SCCR Numbers, can be set by sourcing the 9.0P6 environment variable script.

$CERESHOME should be set to the home directory.

source $CERESENV

set GRID_HOME = $CERESHOME/tisa_grid

set TESTDIR  = $GRID_HOME/CER9.0P6/test_suites

set BINDIR = $GRID_HOME/CER9.0P6/bin

set RCFDIR = $GRID_HOME/CER9.0P6/rcf

set PCFDIR = $GRID_HOME/CER9.0P6/rcf/pcf

set EXPDIR = $GRID_HOME/data_exp/CER9.0P6

set LOGDIR = $GRID_HOME/runlogs

#### Execution

Test 1 - Run PGE CER9.0P6 on x86-flex:  Test month 12/2008.

set data_year = 2008

set data_month = 12

set OUTDIR = $GRID_HOME/data/CldTypHistB/GEO_TestSuite/$data_year/$data_month

cd $TESTDIR

source env-variable.csh

cd $RCFDIR

setenv DATADATE ${data_year}${data_month}

CER9.0P6-SGE_Driver.pl -date $DATADATE -clean

After job completion, the following files will have been created:

# In the $OUTDIR:

CER_CldTypHistB_GEO_TestSuite_000000.${DATADATE}Znnn

Where nnn = 31 – 150

In the $LOGDIR:

CER9.0P6_LogReport_GEO_TestSuite_000000.${DATADATE}01-31

CER9.0P6_LogStatus_GEO_TestSuite_000000.${DATADATE}01-31

CER9.0P6_LogUser_GEO_TestSuite_000000.${DATADATE}01-31

Test 2 - Run PGE CER9.0P6 on x86-flex:  Test month 10/2001.

set data_year = 2001

set data_month = 10

set OUTDIR = $GRID_HOME/data/CldTypHistB/GEO_TestSuite/$data_year/$data_month

cd $TESTDIR

source env-variable.csh

cd $RCFDIR

setenv DATADATE ${data_year}${data_month}

CER9.0P6-SGE_Driver.pl -date $DATADATE -clean

After job completion, the following files will have been created:

# In the $OUTDIR:

CER_CldTypHistB_GEO_TestSuite_000000.${DATADATE}Znnn

Where nnn = 31 – 150

In the $LOGDIR:

CER9.0P6_LogReport_GEO_TestSuite_000000.${DATADATE}01-31

CER9.0P6_LogStatus_GEO_TestSuite_000000.${DATADATE}01-31

CER9.0P6_LogUser_GEO_TestSuite_000000.${DATADATE}01-31

#### Exit Codes

All TISA_GRID software terminates using the CERES-defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.

#### Main Processor CER9.0P6 Test Summary

Here is the time function output from running the test:

Table 3-1.  Run Times for PGE CER9.0P6

|  | AMI-P6 | AMI-x86 |
| --- | --- | --- |
|  | N/A | ~3 hours |

### Evaluation Procedures

The generated files need to be compared with the expected files already in $EXPDIR.

cd $TESTDIR

cp $EXPDIR/variables-Exp .

setVariables.csh Test

source env-variable.csh

For 12/2008

$TESTDIR/eval_runtest.pl 2008 12 1

$TESTDIR/eval_runtest.pl 2008 12 2

$TESTDIR/eval_runtest.pl 2008 12 3

For 10/2001

$TESTDIR/eval_runtest.pl 2001 10 1

$TESTDIR/eval_runtest.pl 2001 10 2

$TESTDIR/eval_runtest.pl 2001 10 3

Each test evaluation should give a message indicating SUCCESS.

### Solutions to Possible Problems

NOTE:  LogReport may show ‘read_image_file’ differences.  These differences are due to multiple satellites’ are being processed simultaneously.

In the event of problems, contact one of the TISA_GRID analysts.

## CER9.0P7:  CldTypHist - MODIS - Edition4

### Stand Alone Test Procedures

These test procedures should be run on x86 platform.

source $CERESENV

set GRID_HOME = $CERESHOME/tisa_grid

set BINDIR = $GRID_HOME/CER9.0P7/bin

set EXPDIR = $GRID_HOME/data_exp/CER9.0P7

set TESTDIR = $GRID_HOME//CER9.0P7/test_suites

set RCFDIR = $GRID_HOME//CER9.0P7/rcf

set PCFDIR = $GRID_HOME/CER9.0P7/rcf/pcf

set DataArchive = $GRID_HOME/data

unlimit

#### Execution

SGE Testing Instructions:

Test 1 - Run PGE CER9.0P7 on x86-flex:  Test month 12/2008. For Terra & Aqua.

cd $TESTDIR

source env-variable.csh

cd $RCFDIR

set data_year = 2008

set data_month = 12

setenv DATADATE ${data_year}${data_month}

setenv INSTANCE ${SS9_0}_${PS9_0}_${CC9_0}.${DATADATE}

setenv INSTANCE_T ${SS9_0T}_${PS9_0}_${CC9_0}.${DATADATE}

set OUTDIR_T = $DataArchive/CldTypHistB/${SS9_0T}_${PS9_0}

setenv INSTANCE_A ${SS9_0A}_${PS9_0}_${CC9_0}.${DATADATE}

set OUTDIR_A = $DataArchive/CldTypHistB/${SS9_0A}_${PS9_0}

setenv INSTANCE_M ${SS9_0M}_${PS9_0}_${CC9_0}.${DATADATE}

set OUTDIR_M = $DataArchive/CldTypHistB/${SS9_0M}_${PS9_0}

cd $RCFDIR

$RCFDIR/CER9.0P7-SGE_Driver.pl -date $DATADATE -clean -force -satellites Terra Aqua

After job completion of the pre processor, PGE CER9.0P7, the following files will have been created:

In the $OUTDIR_T/$data_year/$data_month directory:

CER_CldTypHistB_${INSTANCE_T}Znnn

In the $OUTDIR_A/$data_year/$data_month directory:

CER_CldTypHistB_${INSTANCE_A}Znnn

where nnn = 1 .. 180

In the $OUTDIR_M/$data_year/$data_month directory:

CER_CldTypHistB_${INSTANCE_M}

In the $CERESHOME/tisa_grid/runlogs directory:

CER9.0P7_LogReport_${INSTANCE}

CER9.0P7_LogStatus_${INSTANCE}

CER9.0P7_LogUser_${INSTANCE}

Test 2 - Run PGE CER9.0P7 on x86-flex:  Test month 10/2001 For Terra Only.

set data_year = 2001

set data_month = 10

setenv DATADATE ${data_year}${data_month}

setenv INSTANCE ${SS9_0}_${PS9_0}_${CC9_0}.${DATADATE}

setenv INSTANCE_T ${SS9_0T}_${PS9_0}_${CC9_0}.${DATADATE}

setenv INSTANCE_A ${SS9_0A}_${PS9_0}_${CC9_0}.${DATADATE}

set OUTDIR_A = $DataArchive/CldTypHistB/${SS9_0A}_${PS9_0}

setenv INSTANCE_M ${SS9_0M}_${PS9_0}_${CC9_0}.${DATADATE}

set OUTDIR_M = $DataArchive/CldTypHistB/${SS9_0M}_${PS9_0}

$RCFDIR/CER9.0P7-SGE_Driver.pl -date $DATADATE -clean -force -satellites Terra

After job completion of PGE CER9.0P7, the following files will have been created:

In the $OUTDIR_T/$data_year/$data_month directory:

CER_CldTypHistB_${INSTANCE_T}Znnn

In the $OUTDIR_A/$data_year/$data_month directory:

CER_CldTypHistB_${INSTANCE_A}Znnn

where nnn = 012 .. 180

In the $OUTDIR_M/$data_year/$data_month directory:

CER_CldTypHistB_${INSTANCE_M}

In the $CERESHOME/tisa_grid/runlogs directory:

CER9.0P7_LogReport_${INSTANCE}

CER9.0P7_LogStatus_${INSTANCE}

CER9.0P7_LogUser_${INSTANCE}

#### Exit Codes

All TISA Gridding software terminates using the CERES-defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.

- -	Normal Exit

202	-	Failure Exit

#### Test Summary

Table 3-2.  Run Times for PGE CER9.0P7

|  | x86 |
| --- | --- |
| Test Case | ~4 hours |

### Evaluation Procedures

#### Output Evaluation

Execute the following commands to compare PGE CER9.0P7 generated output with expected output.  The eval_runtest.pl script will check the following outputs: (1) CldTypHistB Output files , (2) PCF; (3) Logfiles.

NOTE:  Comparisons cannot be run on the head node (ab01).  Log onto an x86 (aa09) blade to run the following commands.

cd $TESTDIR

source env-variable.csh

$TESTDIR/setVariables.csh Test

\cp $EXPDIR/variables-Exp $TESTDIR/variables-Exp

The following file will have been created:

variables-Test

NOTE:  It is important that the PGE execution and the creation of the above file be done on the same day.  If the day differs then the logfiles, and test evaluations will not be successful.

For 12/2008

$TESTDIR/eval_runtest.pl 2008 12 1

$TESTDIR/eval_runtest.pl 2008 12 2

$TESTDIR/eval_runtest.pl 2008 12 3

For 10/2001

$TESTDIR/eval_runtest.pl 2001 10 1

$TESTDIR/eval_runtest.pl 2001 10 2

$TESTDIR/eval_runtest.pl 2001 10 3

There should be no reported differences.

### Solutions to Possible Problems

In the event of problems, contact one of the TISA Gridding analysts.

## CER9.0P8:  CldTypHist GEO-MODIS Processor

### Stand Alone Test Procedures

These test procedures should be run on x86 platform.

source $CERESENV

set GRID_HOME = $CERESHOME/tisa_grid

set BINDIR = $CERESHOME/tisa_grid/CER9.0P8/bin

set EXPDIR = $CERESHOME/tisa_grid/data_exp/CER9.0P8

set TESTDIR = $CERESHOME/tisa_grid/CER9.0P8/test_suites

set RCFDIR = $CERESHOME/tisa_grid/CER9.0P8/rcf

set PCFDIR = $CERESHOME/tisa_grid/CER9.0P8/rcf/pcf

set DataArchive = $CERESHOME/tisa_grid/data

unlimit

#### Execution

SGE Testing Instructions:

Test 1 – Run PGE CER9.0P8 on x86-flex:  Test month 10/2001.  For Terra only.

cd $TESTDIR

source env-variable.csh

cd $RCFDIR

set data_year = 2008

set data_month = 12

setenv DATADATE ${data_year}${data_month}

setenv GEO_INSTANCE ${SS9_0G}_${PS9_0}_${CC9_0}.${DATADATE}

setenv MODIS_INSTANCE ${SS9_0M}_${PS9_0}_${CC9_0}.${DATADATE}

setenv GEO_MODIS_INSTANCE ${SS9_0}_${PS9_0}_${CC9_0}.${DATADATE}

set GEO_OUTDIRQC = $DataArchive/CldTypHistQC/${SS9_0G}_${PS9_0}

set MODIS_OUTDIRQC = $DataArchive/CldTypHistQC/${SS9_0QC}_${PS9_0}

set GEO_MODIS_OUTDIR = $DataArchive/CldTypHist/${SS9_0}-${SS9_0}_${PS9_0}

cd $RCFDIR

CER9.0P8-SGE_Driver.pl -date $DATADATE -clean

After job completion of the main processor, PGE CER9.0P8, the following files will have been created:

In the $GEO_OUTDIRQC/$data_year/$data_month directory:

CER_CldTypHistQC_${GEO_INSTANCE}

CER_CldTypHistQC_${GEO_INSTANCE}.met

In the $MODIS_OUTDIRQC/$data_year/$data_month directory:

CER_CldTypHistQC_${MODIS_INSTANCE}

CER_CldTypHistQC_${MODIS_INSTANCE}.met

In the $GEO_MODIS_OUTDIR/$data_year/$data_month directory:

CER_CldTypHist_${GEO_MODIS_INSTANCE}

CER_CldTypHist_${GEO_MODIS_INSTANCE}.met

In the $CERESHOME/tisa_grid/runlogs directory:

CER9.0P7_LogReport_${GEO_MODIS_INSTANCE}

CER9.0P7_LogStatus_${GEO_MODIS INSTANCE}

CER9.0P7_LogUser_${GEO_MODIS INSTANCE}

Test 2 – Run PGE CER9.0P8 on x86-flex:  Test month 12/2008.  For Terra & Aqua.

cd $TESTDIR

source env-variable.csh

cd $RCFDIR

set data_year = 2001

set data_month = 10

setenv DATADATE ${data_year}${data_month}

setenv DATADATE ${data_year}${data_month}

setenv GEO_INSTANCE ${SS9_0G}_${PS9_0}_${CC9_0}.${DATADATE}

setenv MODIS_INSTANCE ${SS9_0M}_${PS9_0}_${CC9_0}.${DATADATE}

setenv GEO_MODIS_INSTANCE ${SS9_0}_${PS9_0}_${CC9_0}.${DATADATE}

set GEO_OUTDIRQC = $DataArchive/CldTypHistQC/${SS9_0G}_${PS9_0}

set MODIS_OUTDIRQC = $DataArchive/CldTypHistQC/${SS9_0QC}_${PS9_0}

set GEO_MODIS_OUTDIR = $DataArchive/CldTypHist/${SS9_0}-${SS9_0}_${PS9_0}

cd $RCFDIR

CER9.0P8-SGE_Driver.pl -date $DATADATE -clean

After job completion of the main processor, PGE CER9.0P8, the following files will have been created:

In the $GEO_OUTDIRQC/$data_year/$data_month directory:

CER_CldTypHistQC_${GEO_INSTANCE}

CER_CldTypHistQC_${GEO_INSTANCE}.met

In the $MODIS_OUTDIRQC/$data_year/$data_month directory:

CER_CldTypHistQC_${MODIS_INSTANCE}

CER_CldTypHistQC_${MODIS_INSTANCE}.met

In the $GEO_MODIS_OUTDIR/$data_year/$data_month directory:

CER_CldTypHist_${GEO_MODIS_INSTANCE}

CER_CldTypHist_${GEO_MODIS_INSTANCE}.met

In the $CERESHOME/tisa_grid/runlogs directory:

CER9.0P8_LogReport_${GEO_MODIS_INSTANCE}

CER9.0P8_LogStatus_${GEO_MODIS INSTANCE}

CER9.0P8_LogUser_${GEO_MODIS INSTANCE}

#### Exit Codes

All TISA Gridding software terminates using the CERES-defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.

- -	Normal Exit

202	-	Failure Exit

#### Test Summary

Table 3-3.  Run Times for PGE CER9.0P8

|  | x86 |
| --- | --- |
| Test Case | ~1 hour |

### Evaluation Procedures

#### Output Evaluation

Execute the following commands to compare PGE CER9.0P7 generated output with expected output.  The eval_runtest.pl script will check the following outputs: (1) CldTypHist Output files, (2) PCF, (3) Logfiles, (4) .met files.

cd $TESTDIR

source env-variable.csh

$TESTDIR/setVariables.csh Test

\cp $EXPDIR/variables-Exp $TESTDIR/variables-Exp

The following file will have been created:

variables-Test

NOTE:  It is important that the PGE execution and the creation of the above file be done on the same day.  If the day differs then the logfiles, and test evaluations will not be successful.

For 12/2008

cd $TESTDIR

$TESTDIR/eval_runtest.pl 2008 12 1

$TESTDIR/eval_runtest.pl 2008 12 2

$TESTDIR/eval_runtest.pl 2008 12 3

$TESTDIR/eval_runtest.pl 2008 12 4

For 10/2001

$TESTDIR/eval_runtest.pl 2001 10 1

$TESTDIR/eval_runtest.pl 2001 10 2

$TESTDIR/eval_runtest.pl 2001 10 3

$TESTDIR/eval_runtest.pl 2001 10 4

## CER9.1P2:  Post-MOA Processor – Edition4

### Stand Alone Test Procedures

Before testing PGE CER9.1P2, source the appropriate environment scripts and then set some additional general environment variables.

source $CERESENV (x86 version)

set RCFDIR = $CERESHOME/tisa_grid/CER9.1P2/rcf

set PCFDIR = $CERESHOME/tisa_grid/CER9.1P2/rcf/pcf

set TESTDIR = $CERESHOME/tisa_grid/CER9.1P2/test_suites

set BINDIR = $CERESHOME/tisa_grid/CER9.1P2/bin

set EXPDIR = $CERESHOME/tisa_grid/data_exp/CER9.1P2

set DataArchive = $CERESHOME/tisa_grid/data

unlimit

#### Execution

cd $RCFDIR

set data_year = 2013

set data_month = 04

set DATADATE = $data_year$data_month

source $TESTDIR/env-variable.csh

$RCFDIR/CER9.1P2-SGE_Driver.pl -date $DATADATE -clean -platform x86

After job completion of the Post-MOA processor, PGE CER9.1P2, the following files will have been created:

In the $CERESHOME/tisa_grid/data/PMOA/CERES_GMAO-G541-Ed4/2013/04 directory:

CER_PMOA_CERES_GMAO-G541-Ed4_400400.201304F1

CER_PMOA_CERES_GMAO-G541-Ed4_400400.201304F1.met

CER_PMOA_CERES_GMAO-G541-Ed4_400400.201304F2

CER_PMOA_CERES_GMAO-G541-Ed4_400400.201304F2.met

CER_PMOA_CERES_GMAO-G541-Ed4_400400.201304F3

CER_PMOA_CERES_GMAO-G541-Ed4_400400.201304F3.met

CER_PMOA_CERES_GMAO-G541-Ed4_400400.201304F4

CER_PMOA_CERES_GMAO-G541-Ed4_400400.201304F4.met

cd $TESTDIR

$TESTDIR/setVariables.csh Test

The following file will have been created:

variables-Test

\cp $EXPDIR/variables-Exp $TESTDIR/variables-Exp

NOTE:  It is important that the PGE execution and the creation of the above file be done on the same day.  If the day differs then the logfiles, .met files, and test evaluations will not be successful.

In the $CERESHOME/tisa_grid/runlogs directory:

CER9.1P2_LogUser_CERES_GMAO-G541-Ed4_400400.201304

CER9.1P2_LogStatus_CERES_GMAO-G541-Ed4_400400.201304

CER9.1P2_LogReport_CERES_GMAO-G541-Ed4_400400.201304

#### Exit Codes

All TISA Gridding software terminates using the CERES-defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.

#### Test Summary

The UNIX time utility yielded the following results when the test was run on x86:

836.83user 179.20system 27:11.53elapsed 62%CPU (0avgtext+0avgdata 1543968maxresident)k

Table 3-4.  Run Times for PGE CER9.1P2

|  | x86 on AMI |
| --- | --- |
| Test Case | ~30 minutes |

### Evaluation Procedures

#### Output Evaluation

Execute the following commands to compare PGE CER9.1P2 generated output with expected output.  The eval_runtest.csh script will check the following outputs:  (3) Logfiles, (4) .met files, (1) PMOA Output files, (2) PCF file.

cd $TESTDIR

./eval_runtest.pl 1

./eval_runtest.pl 2

./eval_runtest.pl 3

./eval_runtest.pl 4

There should be no reported differences except sge_log file name differences  in PCF and HOST differences in met files.

### Solutions to Possible Problems

In the event of problems, contact one of the TISA Gridding analysts.

## CER9.2P3:  SSF1deg-HR Processor (Edition 4)

### Stand Alone Test Procedures

Before testing PGE CER9.2P3, source the appropriate environment scripts and then set some additional general environment variables.

source $CERESENV (P6/X86 version)

set BINDIR = $CERESHOME/tisa_grid/CER9.2P3/bin

set RCFDIR = $CERESHOME/tisa_grid/CER9.2P3/rcf

set TESTDIR = $CERESHOME/tisa_grid/CER9.2P3/test_suites

set EXPDIR = $CERESHOME/tisa_grid/data_exp/CER9.2P3

set PCFDIR = $CERESHOME/tisa_grid/CER9.2P3/rcf/pcf

set DataArchive = $CERESHOME/tisa_grid/data

unlimit

#### Execution

Terra

cd $TESTDIR

source env-variable_Terra.csh

Aqua

cd $TESTDIR

source env-variable_Aqua.csh

cd $RCFDIR

setenv data_year 2004

setenv data_month 07

setenv INSTANCE ${SS9}_${PS9}_${CC9}

set OUTDIR = $DataArchive/SSF1deg-HR/${SS9}_${PS9}

On x86:

cd $RCFDIR

CER9.2P3-SGE_Driver.pl -start 20040701 -end 20040731 -hour 12 -clean -platform x86

CER9.2P3-SGE_Driver.pl -date 20040706 -start_hour 0 -end_hour 0 -clean -platform x86

On P6:

cd $RCFDIR

CER9.2P3-SGE_Driver.pl -start 20040701 -end 20040731 -hour 12 -clean -platform p6

CER9.2P3-SGE_Driver.pl -date 20040706 -start_hour 0 -end_hour 0 -clean -platform p6

NPP

cd $TESTDIR

source env-variable_NPP.csh

cd $RCFDIR

setenv data_year 2012

setenv data_month 06

setenv INSTANCE ${SS9}_${PS9}_${CC9}

set OUTDIR = $DataArchive/SSF1deg-HR/${SS9}_${PS9}

On x86:

cd $RCFDIR

CER9.2P3-SGE_Driver.pl -date 20120619 -start_hour 02 -end_hour 02 -clean -platform x86

CER9.2P3-SGE_Driver.pl -date 20120619 -start_hour 03 -end_hour 03 -clean -platform x86

On P6:

cd $RCFDIR

CER9.2P3-SGE_Driver.pl -date 20120619 -start_hour 02 -end_hour 02 -clean -platform p6

CER9.2P3-SGE_Driver.pl -date 20120619 -start_hour 03 -end_hour 03 -clean -platform p6

After job completion of the pre processor, PGE CER9.2P3, the following files will have been created:

Terra and Aqua:

In the $OUTDIR/$data_year/$data_month directory:

CER_SSF1deg-HR_${INSTANCE}.${YYYY}${MM}${DD}${HH}

CER_SSF1deg-HR_${INSTANCE}.${YYYY}${MM}}$DD}${HH}.met

Where YYYY = 2004; MM = 07; DD = 01 – 31; HH = 12

CER_SSF1deg-HR_${INSTANCE}.${YYYY}${MM}${DD}${HH}

CER_SSF1deg-HR_${INSTANCE}.${YYYY}${MM}}$DD}${HH}.met

Where YYYY = 2004; MM = 07; DD = 06; HH = 00

NPP:

In the $OUTDIR/$data_year/$data_month directory:

CER_SSF1deg-HR_${INSTANCE}.${YYYY}${MM}${DD}${HH}

CER_SSF1deg-HR_${INSTANCE}.${YYYY}${MM}}$DD}${HH}.met

Where YYYY = 2012; MM = 06; DD = 19; HH = 02

CER_SSF1deg-HR_${INSTANCE}.${YYYY}${MM}${DD}${HH}

CER_SSF1deg-HR_${INSTANCE}.${YYYY}${MM}}$DD}${HH}.met

Where YYYY = 2012; MM = 06; DD = 19; HH = 03

In the $CERESHOME/tisa_grid/runlogs directory:

Terra and Aqua:

CER9.2P3_LogReport_${INSTANCE}.${YYYY}${MM}${DD}${HH}

CER9.2P3_LogStatus_${INSTANCE}.${YYYY}${MM}}$DD}${HH}

CER9.2P3_LogUser_${INSTANCE}.${YYYY}${MM}}$DD}${HH}

Where YYYY = 2004; MM = 07; DD = 01 – 31; HH = 12

CER9.2P3_LogReport_${INSTANCE}.${YYYY}${MM}${DD}${HH}

CER9.2P3_LogStatus_${INSTANCE}.${YYYY}${MM}}$DD}${HH}

CER9.2P3_LogUser_${INSTANCE}.${YYYY}${MM}}$DD}${HH}

Where YYYY = 2004; MM = 07; DD = 06; HH = 00

NPP:

CER9.2P3_LogReport_${INSTANCE}.${YYYY}${MM}${DD}${HH}

CER9.2P3_LogStatus_${INSTANCE}.${YYYY}${MM}}$DD}${HH}

CER9.2P3_LogUser_${INSTANCE}.${YYYY}${MM}}$DD}${HH}

Where YYYY = 2012; MM = 06; DD = 19; HH = 02

CER9.2P3_LogReport_${INSTANCE}.${YYYY}${MM}${DD}${HH}

CER9.2P3_LogStatus_${INSTANCE}.${YYYY}${MM}}$DD}${HH}

CER9.2P3_LogUser_${INSTANCE}.${YYYY}${MM}}$DD}${HH}

Where YYYY = 2012; MM = 06; DD = 19; HH = 03

#### Exit Codes

All TISA Gridding software terminates using the CERES-defined EXIT CODES for the Langley Terra Information System (LaTIS).  Successful completion is indicated by an exit code of 0.

#### Test Summary

The UNIX time utility yielded the following results for ONE of the CER9.2P3 jobs, when the test was run on P6:

Table 3-5.  Run Times for PGE CER9.2P3

|  | P6 on AMI | x86 on AMI |
| --- | --- | --- |
| Terra Test Case | 0:39.29 | 0:39.29 |
| Aqua Test Case | 1:04.82 |  |

### Evaluation Procedures

#### Output Evaluation

Execute the following commands to compare PGE CER9.2P3 generated output with expected output.  The eval_runtest.csh script will check the following outputs:  (1) SSF1deg-HR files,
(2) PCF file, (3) QA files, (4) Logfiles, (5) .met files

NOTE:  QA files are optional.  They may not get generated for some runs.

SSF1deg-HR comparisons will create a *.dmp file for each corresponding SSF1deg-HR file.  The *dmp file will have the header information and the differences if there are found any.

cd $TESTDIR

setVariables.csh Test

\cp $EXPDIR/variables-Exp $TESTDIR/variables-Exp

NOTE:  It is important that the PGE execution and the creation of the above file be done on the same day.  If the day differs then the logfiles, .met files, and test evaluations will not be successful.

cd $TESTDIR

Terra

source env-variable_Terra.csh

Aqua

source env-variable_Aqua.csh

NPP

source env-variable_NPP.csh

$TESTDIR/eval_runtest.pl 1

$TESTDIR/eval_runtest.pl 2

$TESTDIR/eval_runtest.pl 3

$TESTDIR/eval_runtest.pl 4

$TESTDIR/eval_runtest.pl 5

There should be no reported differences.

### Solutions to Possible Problems

In the event of problems, contact one of the TISA Gridding analysts.

## CER9.3P3:  SSF1degB Postprocessor (Edition 4)

### Stand Alone Test Procedures

Before testing PGE CER9.3P3, source the appropriate environment scripts and then set some additional general environment variables.

source $CERESENV (P6/x86 version)

set BINDIR = $CERESHOME/tisa_grid/CER9.3P3/bin

set RCFDIR = $CERESHOME/tisa_grid/CER9.3P3/rcf

set TESTDIR = $CERESHOME/tisa_grid/CER9.3P3/test_suites

set EXPDIR = $CERESHOME/tisa_grid/data_exp/CER9.3P3

set PCFDIR = $CERESHOME/tisa_grid/CER9.3P3/rcf/pcf

set DataArchive = $CERESHOME/tisa_grid/data

unlimit

NOTE:  PGE CER9.3P3 uses the output produced from testing PGE CER9.2P3.

#### Execution

Terra:

cd $TESTDIR

source env-variable_Terra.csh

Aqua:

cd $TESTDIR

source env-variable_Aqua.csh

set OUTDIR_B = $DataArchive/SSF1degB/${SS9}_${PS9_3}

set OUTDIR_D = $DataArchive/SSF1degD/${SS9}_${PS9_3}

setenv data_year 2004

setenv data_month 07

setenv DATADATE ${data_year}${data_month}

setenv INSTANCE ${SS9}_${PS9_3}_${CC9_3}

On P6:

cd $RCFDIR

CER9.3P3-SGE_Driver.pl -date $DATADATE -clean -platform p6

NOTE:  There are less than required input hourly files available for testing.

To test PGE with existing input files use force command as follows.

CER9.3P3-SGE_Driver.pl -date $DATADATE -clean -platform p6 -force

On x86:

cd $RCFDIR

CER9.3P3-SGE_Driver.pl -date $DATADATE -clean -platform x86

NOTE:  There are less than required input hourly files available for testing.

To test PGE with existing input files use force command as follows.

CER9.3P3-SGE_Driver.pl -date $DATADATE -clean -platform x86 -force

NPP:

cd $TESTDIR

source env-variable_NPP.csh

set OUTDIR_B = $DataArchive/SSF1degB/${SS9}_${PS9_3}

set OUTDIR_D = $DataArchive/SSF1degD/${SS9}_${PS9_3}

setenv data_year 2013

setenv data_month 04

setenv DATADATE ${data_year}${data_month}

setenv INSTANCE ${SS9}_${PS9_3}_${CC9_3}

On P6:

cd $RCFDIR

CER9.3P3-SGE_Driver.pl -date $DATADATE -clean -platform p6

NOTE:  There are less than required input hourly files available for testing.

To test PGE with existing input files use force command as follows.

CER9.3P3-SGE_Driver.pl -date $DATADATE -clean -platform p6 -force

On x86:

cd $RCFDIR

CER9.3P3-SGE_Driver.pl -date $DATADATE -clean -platform x86

NOTE:  There are less than required input hourly files available for testing.

To test PGE with existing input files use force command as follows.

CER9.3P3-SGE_Driver.pl -date $DATADATE -clean -platform x86 -force

After job completion of the post processor, PGE CER9.3P3, the following files will have been created:

Terra/Aqua/NPP:

In the $OUTDIR_B/$data_year/$data_month directory:

CER_SSF1degB_${INSTANCE}.${DATADATE}Znnn

CER_SSF1degB_${INSTANCE}.${DATADATE}Znnn.met

where nnn = 001 .. 180.

In the $OUTDIR_D/$data_year/$data_month directory:

CER_SSF1degD_${INSTANCE}.${DATADATE}dd

CER_SSF1degD_${INSTANCE}.${DATADATE}dd.met

Where dd = 1- 31

In the $CERESHOME/tisa_grid/runlogs directory:

CER9.3P3_LogReport_${INSTANCE}.${DATADATE}

CER9.3P3_LogStatus_${INSTANCE}.${DATADATE}

CER9.3P3_LogUser_${INSTANCE}.${DATADATE}

#### Exit Codes

All TISA Gridding software terminates using the CERES-defined EXIT CODES for the Langley Terra Information System (LaTIS).  Successful completion is indicated by an exit code of 0.

#### Test Summary

The UNIX time utility yielded the following results for ONE of the CER9.3P3 jobs, when the test was run on P6/ x86:

Table 3-6.  Run Times for PGE CER9.3P3

|  | AMI-P6 | AMI-x86 |
| --- | --- | --- |
| Test Case | 0:07.48 | 0:07.48 |

### Evaluation Procedures

#### Output Evaluation

Execute the following commands to compare PGE CER9.3P3 generated output with expected output.  The eval_runtest.csh script will check the following outputs:  (1) SSF1degB Binary Output files, (2) PCF file, (3) Logfiles, and (4) .met files.

cd $TESTDIR

setVariables.csh Test

\cp $EXPDIR/variables-Exp $TESTDIR/variables-Exp

NOTE:  It is important that the PGE execution and the creation of the above file be done on the same day.  If the day differs then the logfiles, .met files, and test evaluations will not be successful.

Terra:

cd $TESTDIR

source env-variable_Terra.csh

Aqua:

cd $TESTDIR

source env-variable_Aqua.csh

NPP:

cd $TESTDIR

source env-variable_NPP.csh

$TESTDIR/eval_runtest.pl 1

$TESTDIR/eval_runtest.pl 2

$TESTDIR/eval_runtest.pl 3

$TESTDIR/eval_runtest.pl 4

There should be no reported differences.

### Solutions to Possible Problems

In the event of problems, contact one of the TISA Gridding analysts.

## CER9.4P3:  SSF1deg-Hour HDF Processor (Edition 4)

### Stand Alone Test Procedures

Before testing PGE CER9.4P3, source the appropriate environment scripts and copy the test data to the appropriate directory.

source $CERESENV (P6/x86 version)

set BINDIR = $CERESHOME/tisa_grid/CER9.4P3/bin

set RCFDIR = $CERESHOME/tisa_grid/CER9.4P3/rcf

set TESTDIR = $CERESHOME/tisa_grid/CER9.4P3/test_suites

set EXPDIR = $CERESHOME/tisa_grid/data_exp/CER9.4P3

set PCFDIR = $CERESHOME/tisa_grid/CER9.4P3/rcf/pcf

set DataArchive = $CERESHOME/tisa_grid/data

unlimit

NOTE:  PGE CER9.4P3 uses the output produced from testing PGE CER9.3P3.

#### Execution

Terra:

source $TESTDIR/env-variable_Terra.csh

Aqua:

source $TESTDIR/env-variable_Aqua.csh

cd $RCFDIR

set OUTDIR = $DataArchive/SSF1deg-Hour/${SS9}_${PS9}

setenv data_year 2004

setenv data_month 07

setenv DATADATE ${data_year}${data_month}

setenv INSTANCE ${SS9}_${PS9}_${CC9_4}

On P6:

CER9.4P3-SGE_Driver.pl -date $DATADATE -clean -platform p6

On x86:

CER9.4P3-SGE_Driver.pl -date $DATADATE -clean -platform x86

NPP:

source $TESTDIR/env-variable_NPP.csh

cd $RCFDIR

set OUTDIR = $DataArchive/SSF1deg-Hour/${SS9}_${PS9}

setenv data_year 2013

setenv data_month 04

setenv DATADATE ${data_year}${data_month}

setenv INSTANCE ${SS9}_${PS9}_${CC9_4}

On P6:

CER9.4P3-SGE_Driver.pl -date $DATADATE -clean -platform p6

On x86:

CER9.4P3-SGE_Driver.pl -date $DATADATE -clean -platform x86

After job completion of the post processor, PGE CER9.4P3, the following files will have been created:

In the $OUTDIR/$data_year/$data_month directory:

CER_SSF1deg-Hour_${INSTANCE}.${DATADATE}nn

CER_SSF1deg-Hour_${INSTANCE}.${DATADATE}nn.met

where nn = 01 .. 31

In the $CERESHOME/tisa_grid/runlogs directory:

CER9.4P3_LogReport_${INSTANCE}.${DATADATE}

CER9.4P3_LogStatus_${INSTANCE}.${DATADATE}

CER9.4P3_LogUser_${INSTANCE}.${DATADATE}

#### Exit Codes

All TISA Gridding software terminates using the CERES-defined EXIT CODES for the Langley Terra Information System (LaTIS).  Successful completion is indicated by an exit code of 0.

#### Test Summary

The UNIX time utility yielded the following results for ONE of the CER9.4P3 jobs, when the test was run on P6/x86:

Table 3-7.  Run Times for CER9.4P3

|  | p6 | x86 |
| --- | --- | --- |
| Test Case | 71 minutes | 18 minutes |

### Evaluation Procedures

#### Output Evaluation

Execute the following commands to compare PGE CER9.4P2 generated output with expected output.  The eval_runtest.csh script will check the following outputs:  (1) SFC HDF Output files, (3) Logfiles, and (4) .met files.

cd $TESTDIR

setVariables.csh Test

\cp $EXPDIR/variables-Exp $TESTDIR/variables-Exp

NOTE:  It is important that the PGE execution and the creation of the above file be done on the same day.  If the day differs then the logfiles, .met files, and test evaluations will not be successful.

Terra:

source $TESTDIR/env-variable_Terra.csh

Aqua:

source $TESTDIR/env-variable_Aqua.csh

NPP:

source $TESTDIR/env-variable_NPP.csh

$TESTDIR/eval_runtest.pl 1

$TESTDIR/eval_runtest.pl 3

$TESTDIR/eval_runtest.pl 4

### Solutions to Possible Problems

In the event of problems, contact one of the TISA Gridding analysts

References

1.	Clouds and the Earth’s Radiant Energy System (CERES) Data Management System, Data Products Catalog, Release 2, March 1998

Acronyms and Abbreviations

ASDC	Atmospheric Science Data Center

CERES	Clouds and the Earth’s Radiant Energy System

CRS	Cloud Radiated Swath

DAAC	Distributed Active Archive Center

EOS	Earth Observing System

EOS-AM	EOS Morning Crossing Mission

EOS-PM	EOS Afternoon Crossing Mission

ERBE	Earth Radiation Budget Experiment

ERBS	Earth Radiation Budget Satellite

FSW	Gridded Single Satellite Fluxes and Clouds and Compute Spatial Averages

GMT	Greenwich meridian time

HDF	Hierarchical Data Format

MCF	Metadata Control Files

MOA	Meteorological, Ozone, and Aerosol

NASA	National Aeronautics and Space Administration

NOAA	National Oceanic and Atmospheric Administration

PCF	Process Control File

PGE	Product Generation Executives

PMOA	Post Meteorological, Ozone, and Aerosol

SFC	Gridded Single Satellite TOA and Surface Fluxes

SSF1deg-Hour	Gridded Single Satellite TOA and Surface Fluxes

SMF	Status Message File

SSF	Single Satellite CERES Footprint TOA and Surface Fluxes, Clouds

TISA	Time Interpolation and Spatial Averaging

TOA	Top-of-the-Atmosphere

TRMM	Tropical Rainfall Measuring Mission