Clouds and the Earth's Radiant Energy System

(CERES)

Data Management System

CERES Cloud Retrieval and Convolution

Subsystems 4.1 through 4.4

Release 5 Test Plan

Version 11

Primary Authors

Timothy D. Murray, Walter F. Miller, Ricky R. Brown, Sunny Sun-Mack, Rita Smith

Science Systems and Applications, Inc. (SSAI)

One Enterprise Parkway, Suite 200

Hampton, VA  23666

NASA Langley Research Center

Climate Science Branch

Science Directorate

21 Langley Boulevard

Hampton, VA  23681-2199

SW Delivered to CM:  May 2017

Document Date:  May 2017

Document Revision Record

The Document Revision Record contains information pertaining to approved document changes.  The table lists the date the Software Configuration Change Request (SCCR) was approved, the Release and Version Number, the SCCR number, a short description of the revision, and the revised sections.  The document authors are listed on the cover.  The Head of the CERES Data Management Team approves or disapproves the requested changes based on recommendations of the Configuration Control Board.

| Document Revision Record |
| --- |
| SCCR Approval Date | Release/ Version Number | SCCR Number | Description of Revision | Section(s) Affected |
| 05/24/01 | R3V4 | 262 | Added new subdirectory under the data Subdirectory chart in Appendix B. | App. B |
|  |  |  | Updated Table C.6-1. | App. C |
|  |  |  | Added instructions for copying the Instrument and MOA input files for the Cloud test cases to the instrument and sarb directories. | All |
|  |  |  | Updated the test summaries to accurately reflect run time for each test case. | All |
|  |  |  | For each test case, added reference to the text file which lists the expected output for each PGE. | All |
|  |  |  | Updated format to comply with standards | All |
| 07/06/01 | R3V5 | 273 | Added PGE CER4.1-4.1P2. | Sec. 5.0 |
|  |  |  | Updated format to comply with standards. | All |
| 08/07/01 | R3V6 | 284 | Added instructions for copying the Instrument and MOA input files to the instrument and sarb directories for PGE CER4.1-4.1P2. | Sec. 5.0 |
|  |  |  | Updated format to comply with standards. | All |
| 10/02/01 | R3V7 | 300 | Added an instruction for preparing VIRS files for processing. | Sec. 5.0 |
|  |  |  | Removed PGE CER4.1-4.4P1. | Sec. 8.0 |
|  |  |  | Updated format to comply with standards. | All |
| 03/21/02 | R3V8 | 318 | Changed test date for processing PGE CER4.1-4.1P2. | Sec. 5.0 |
|  |  |  | Updated Appendix B to include new directory for SSFA. | App. B |
|  |  |  | Updated file listings in Appendix C. | App. C |
|  |  |  | Updated format to comply with standards. | All |
| 06/03/02 | R3V9 | 351 | Added PGE CER4.1-4.2P2. | Sec. 7.0 |
|  |  |  | Updated Appendix B to include new directory structure for PGE CER4.1-4.2P2 and for SnowIce Maps. | App. B |
|  |  |  | Updated Appendix C File Description. | App. C |
|  |  |  | Updated format to comply with standards. | All |
| 01/29/03 | R3V10 | 421 | Added PGE CER4.1-4.1P3. | Sec. 6.0 |
|  |  |  | Updated Appendix B to include new directory structure for PGE CER4.1-4.1P3. | App. B |
|  |  |  | Updated Appendix C File Description. | App. C |
|  |  |  | Updated format to comply with standards. | All |
| 05/21/03 | R3V11 | 439 | Updated compile sections to handle PGEs independently. | Sec. 2.2 |
|  |  |  | Changed test date for processing PGE CER4.1-4.1P2. | Sec. 5.0 |
|  |  |  | Updated format to comply with standards. | All |
| 09/05/03 | R3V12 | 467 | Updated Testing Date. | All |
|  |  |  | Updated format to comply with standards. | All |
| 12/22/03 | R3V13 | 490 | Updated Testing Date. | Secs. 6.0, 7.0, & 9.0 |
|  |  |  | Updated format to comply with standards. | All |
| 06/04/04 | R4V1 | 536 | Update Testing Date. | Secs. 6.0, 7.0, & 9.0 |
|  |  |  | Update Executable names for Aqua. | App. C |
|  |  |  | Updated format to comply with standards. | All |
| 05/30/07 | R4V2 | 654 | Updated Testing Date. | Sec. 10.0 |
|  |  |  | Added Testing Procedures for Collection 005 PGEs (CER4.1-4.1P4, CER4.1-4.1P5, CER4.1-4.2P3, & CER4.1-4.3P2). | Secs. 7.0, 8.0, 11.0, & 13.0 |
|  |  |  | Run times were updated for PGEs CER 4.1-4.1P4, 4.1-4.1P5, & 4.1-4.2P3. | Secs. 7.1.3, 8.1.3, & 11.1.3 |
|  |  |  | Added Collection 005 information. | Apps. B & C |
| 01/23/08 | R4V3 | 658 | Testing and Compilation Procedures added for four new PGEs (CER4.1-4.1P6, CER4.1-4.2P4, CER4.1-4.2P5, & CER4.1-4.3P23). | Secs. 2.0, 9.0, 13.0, 14.0, 17.0, Apps. B, & C |
| 01/22/09 | R5V1 | 693 | Added new PGE CER4.1-4.0P2 for processing both 8th MESH and 16th MESH Snow and Ice map. | All |
|  |  |  | Updated delivered PGEs to be compatible with the new directory structure and processing on magneto. | All |
|  |  |  | Validation scripts converted to PERL. | All |
| 07/28/09 | R5V2 | 719 | Updated PGEs CER4.1-4.1P6, CER4.1-4.2P4, CER4.1-4.2P5, and CER4.1-4.3P3 to reflect new directory structure. | Secs. 2.2, 10.0, 14.0, 15.0, & 18.0 |
| 04/15/10 | R5V3 | 779 | Updated PGEs CER4.1-4.1P4 & CER4.1-4.1P5 to extend the range for surface pressure search. | Secs. 8.0 & 9.0 |
| 10/13/10 | R5V4 | 809 | Added input/output directory environment variables. | Sec. 2.0 |
|  |  |  | Added CPUTYPE environment variable and used it in executable file names. | Sec. 2.0 & App. C |
|  |  |  | Updated CRH file names to reflect SnowFree/SnowCovered channels. | Sec. 2.0 & App. C |
|  |  |  | Added new cleanup method and PCF checking procedure to PGEs CER4.1-4.1P6, CER4.1-4.2P4, CER4.1-4.2P5, and CER4.1-4.3P3. | Secs. 10.0, 15.0, 16.0, & 19.0 |
|  |  |  | Added SGE execution and validation instructions for PGEs CER4.1-4.1P6, CER4.1-4.2P4, CER4.1-4.2P5, and CER4.1-4.3P3. | Secs. 10.0, 15.0, 16.0, & 19.0 |
|  |  |  | Added new section for instructions on using CER4.1-4.1P6/CER4.1-4.2P5 2-day and month processing. | Sec. 11.0 |
|  |  |  | Added SGE to Acronyms and Abbreviations List. | App. A |
|  |  |  | Removed PCF ASCII Input file for CER4.1-4.1P6, CER4.1-4.2P4, CER4.1-4.2P5, CER4.1-4.3P3. | Table C.1-1 |
|  |  |  | Added Terra calibration file to Ancillary Input. | Table C.6-1 |
|  |  |  | Replaced hard-coded values with available environment variable’s names. | Secs. 10.1.1, 11.1.1, 15.1.1, 16.1.1, 19.1.1 |
| 10/13/10 (Cont’d) | R5V4 | 809 | Included information on SGE summary files. | Secs. 10.1.1, 15.1.1, 16.1.1, 19.1.1 |
|  |  |  | Modifications made in text. | Sec. 11.2.3 |
| 07/25/12 | R5V5 | 918 | Added Ancillary table for CER4.1-4.0P2. | Table C.6-2 |
|  |  |  | Modified 4.1-4.0P2 compilation procedure for AMI. | Sec. 2.2.2 |
|  |  |  | Updated 4.1-4.0P2 test cases for AMI. | Sec. 4.0 |
|  |  |  | Updated compilation steps for 4.1-4.0P2. | Sec. 2.2.2 |
|  |  |  | Updated testing and validation for 4.1-4.0P2. | Secs. 4.1.1, 4.2.3, & 4.3 |
|  |  |  | Changed test date for 4.1-4.0P2 Class_Mesh8 case. (12/13/2012) | Sec. 4.1.1 |
|  |  |  | Modified some formatting in the document for easier testing. (12/14/2012) | All |
| 01/02/13 | R5V6 | 943 | Updated 4.1-4.0P2 and added 4.1-4.0P3 Subsytem Overviews. | Secs. 1.1.2 & 1.1.3 |
|  |  |  | Added 4.1-4.0P3 Compilation instructions. | Sec. 2.2.3 |
|  |  |  | Added 4.1-4.0P3 Test and Evaluation section. | Sec. 5.0 |
| 02/06/13 | R5V7 | 947 | Removed manual commands testing. | Secs. 11.1.1, 11.2.3, 11.3, 16.1.1, 16.2.3, 16.3, 17.1.1, 17.2.3, 17.3, 20.1.1, 20.2.3, & 20.3 |
| 07/25/12 | R5V8 | 919 | Updated PGEs CER4.1-4.1P4, CER4.1-4.1P5, CER4.1-4.2P2, CER4.1-4.2P3, and CER4.1-4.3P2 compilation procedures. | Secs. 2.2.5, 2.2.8, 2.2.9, & 2.2.13 |
|  |  |  | Updated PGE CER4.1-4.1P4 execution, evaluation, and cleanup procedures. | Sec. 9.0 |
|  |  |  | Added PGE CER4.1-4.1P4/CER4.1-4.2P2 two-day execution section. | Sec. 10.0 |
|  |  |  | Updated PGE CER4.1-4.1P5 execution, evaluation, and cleanup procedures. | Sec. 11.0 |
| 07/25/12 (Cont’d) | R5V8 | 919 | Added PGE CER4.1-4.1P5/CER4.1-4.2P2 two-day execution section. | Sec. 12.0 |
|  |  |  | Updated PGE CER4.1-4.2P2 execution, evaluation, and cleanup procedures. | Sec. 16.0 |
|  |  |  | Updated PGE CER4.1-4.2P3 execution, evaluation, and cleanup procedures. | Sec. 17.0 |
|  |  |  | Updated PGE CER4.1-4.3P2 execution, evaluation, and cleanup procedures. | Sec. 21.0 |
|  |  |  | Updated PGEs CER4.1-4.1P4/CER4.1-4.1P5 script names. (01/09/2014) | Secs. 9.1.1 & 11.1.1 |
|  |  |  | Updated testing commands. (01/09/2014) | Secs. 9.2.3, 9.3, 10.2.3, 10.3, 11.2.3, 11.3, 12.2.3, 12.3, 16.2.3, 16.3, 17.2.3, 17.3, 21.2.3, & 21.3 |
| 03/21/13 | R5V9 | 960 | Added testing plan for new PGEs CER4.1-4.1P7, CER4.1-4.2P6, CER4.1-4.2P7, and CER4.1-4.3P4. | Secs. 2.2, 15.0, 16.0, 22.0, 23.0, & 27.0 |
|  |  |  | Added overviews for new PGEs. | Sec. 1.1 |
| 01/05/15 | R5V10 | 1047 | Added directions to run for whole month only. | Sec. 16.1.1 |
| 01/04/17 | R5V11 | 1205 | Removed 2-Day testing. | Sec. 14.0 |
|  |  |  | Made test dates environment variables rather than hard coded. | Secs. 13.0, 19.0, 20.0, & 25.0 |
|  |  |  | Updated compilation instructions. | Secs. 2.2.6, 2.2.11, 2.2.12, & 2.2.17 |

Document Revision Record	ii

1.0	Introduction	1

1.1	Document Overview	1

1.1	Subsystem Overview	2

1.1.1	CER4.1-4.0P1 - Snow and Ice Processor	2

1.1.2	CER4.1-4.0P2 - Snow and Ice Processor	3

1.1.3	CER4.1-4.0P3 - Snow and Ice Processor	3

1.1.4	CER4.1-4.1P1 - TRMM Main Processor	3

1.1.5	CER4.1-4.1P2 - Terra Main Processor	5

1.1.6	CER4.1-4.1P3 - Aqua Main Processor	7

1.1.7	CER4.1-4.1P4 - Terra Main Processor	9

1.1.8	CER4.1-4.1P5 - Aqua Main Processor	11

1.1.9	CER4.1-4.1P6 - Main Processor	13

1.1.10	CER4.1-4.1P7 - Main Processor	15

1.1.11	CER4.1-4.2P1 - Daily QC Processor	17

1.1.12	CER4.1-4.2P2 - Daily CRH Processor	17

1.1.13	CER4.1-4.2P3 - Daily QC Processor	18

1.1.14	CER4.1-4.2P4 - Daily QC Processor	18

1.1.15	CER4.1-4.2P5 - Daily CRH Processor	18

1.1.16	CER4.1-4.2P6 - Daily QC Processor	18

1.1.17	CER4.1-4.2P7 - Daily CRH Processor	19

1.1.18	CER4.1-4.3P1 - Monthly QC Processor	19

1.1.19	CER4.1-4.3P2 - Monthly QC Processor	19

1.1.20	CER4.1-4.3P3 - Monthly QC Processor	19

1.1.21	CER4.1-4.3P4 - Monthly QC Processor	20

2.0	Software and Data File Installation Procedures	21

2.1	Installation	21

2.2	Compilation	22

2.2.1	Compiling PGE CER4.1-4.0P1	22

2.2.2	Compiling PGE CER4.1-4.0P2	23

2.2.3	Compiling PGE CER4.1-4.0P3	23

2.2.4	Compiling PGE CER4.1-4.1P1, CER4.1-4.1P2, CER4.1-4.1P3	24

2.2.5	Compiling PGE CER4.1-4.1P4, CER4.1-4.1P5	24

2.2.6	Compiling PGE CER4.1-4.1P6	26

2.2.7	Compiling PGE CER4.1-4.1P7	27

2.2.8	Compiling PGE CER4.1-4.2P1	28

2.2.9	Compiling PGE CER4.1-4.2P2	28

2.2.10	Compiling PGE CER4.1-4.2P3	29

2.2.11	Compiling PGE CER4.1-4.2P4	29

2.2.12	Compiling PGE CER4.1-4.2P5	30

2.2.13	Compiling PGE CER4.1-4.2P6	30

2.2.14	Compiling PGE CER4.1-4.2P7	31

2.2.15	Compiling PGE CER4.1-4.3P1	31

2.2.16	Compiling PGE CER4.1-4.3P2	32

2.2.17	Compiling PGE CER4.1-4.3P3	32

2.2.18	Compiling PGE CER4.1-4.3P4	33

3.0	Test and Evaluation Procedures - CER4.1-4.0P1 Snow and Ice Processor	34

3.1	Stand Alone Test Procedures	34

3.1.1	Execution	34

3.1.1.1	NSIDC Snow and Ice Data	34

3.1.2	Exit Codes	34

3.1.3	Snow and Ice Processor Test Summary	34

3.2	Evaluation Procedures	34

3.2.1	Log and Status File Results	35

3.2.2	Metadata Evaluation	35

3.2.3	Execution of Comparison Software	35

3.2.4	Evaluation of Comparison Software Output	35

3.3	Solutions to Possible Problems	35

4.0	Test and Evaluation Procedures - CER4.1-4.0P2 Snow and Ice Processor	37

4.1	Stand Alone Test Procedures	37

4.1.1	Execution	37

4.1.2	Exit Codes	39

4.1.3	Snow and Ice Processor Test Summary	39

4.2	Evaluation Procedures	39

4.2.1	Log and Status File Results	39

4.2.2	Metadata Evaluation	39

4.2.3	Execution of Comparison Software	40

4.2.4	Evaluation of Comparison Software Output	40

4.3	Solutions to Possible Problems	40

5.0	Test and Evaluation Procedures - CER4.1-4.0P3 Snow and Ice Processor	42

5.1	Stand Alone Test Procedures	42

5.1.1	Execution	42

5.1.2	Exit Codes	43

5.1.3	Snow and Ice Processor Test Summary	43

5.2	Evaluation Procedures	43

5.2.1	Log and Status File Results	43

5.2.2	Metadata Evaluation	43

5.2.3	Execution of Comparison Software	43

5.2.4	Evaluation of Comparison Software Output	43

5.3	Solutions to Possible Problems	43

6.0	Test and Evaluation Procedures - CER4.1-4.1P1 TRMM Main Processor	45

6.1	Stand Alone Test Procedures	45

6.1.1	VIRS Imager File Preparation (for Section 6.1.2.1)	45

6.1.2	Execution	45

6.1.2.1	TRMM-VIRS Processing	45

6.1.3	Exit Codes	46

6.1.4	Main Processor Test Summary	46

6.2	Evaluation Procedures	46

6.2.1	Log and Status File Results	46

6.2.2	Metadata Evaluation	46

6.2.3	Execution of Comparison Software	46

6.2.4	Evaluation of Comparison Software Output	46

6.3	Solutions to Possible Problems	46

7.0	Test and Evaluation Procedures - CER4.1-4.1P2 Terra Main Processor	48

7.1	Stand Alone Test Procedures	48

7.1.1	MODIS Imager File Preparation (for Section 7.1.2.1)	48

7.1.2	Execution	48

7.1.2.1	Terra-MODIS Processing	48

7.1.3	Exit Codes	48

7.1.4	Main Processor Test Summary	49

7.2	Evaluation Procedures	49

7.2.1	Log and Status File Results	49

7.2.2	Metadata Evaluation	49

7.2.3	Execution of Comparison Software	49

7.2.4	Evaluation of Comparison Software Output	49

7.3	Solutions to Possible Problems	49

8.0	Test and Evaluation Procedures - CER4.1-4.1P3 Aqua Main Processor	51

8.1	Stand Alone Test Procedures	51

8.1.1	MODIS Imager File Preparation (for Section 8.1.2.1)	51

8.1.2	Execution	51

8.1.2.1	Aqua-MODIS Processing	51

8.1.3	Exit Codes	51

8.1.4	Main Processor Test Summary	51

8.2	Evaluation Procedures	51

8.2.1	Log and Status File Results	52

8.2.2	Metadata Evaluation	52

8.2.3	Execution of Comparison Software	52

8.2.4	Evaluation of Comparison Software Output	52

8.3	Solutions to Possible Problems	52

9.0	Test and Evaluation Procedures - CER4.1-4.1P4 Terra Collection 005 Main Processor	54

9.1	Stand Alone Test Procedures	54

9.1.1	Execution	54

9.1.2	Exit Codes	54

9.1.3	Main Processor Test Summary	54

9.2	Evaluation Procedures	55

9.2.1	Log and Status File Results	55

9.2.2	Metadata Evaluation	55

9.2.3	Execution of Comparison Software	55

9.2.4	Evaluation of Comparison Software Output	55

9.3	Solutions to Possible Problems	55

10.0	Test and Evaluation Procedures - CER4.1-4.1P4/CER4.1-4.2P2 2-Day Processor	57

10.1.1	Execution	57

10.1.2	Exit Codes	58

10.1.3	Test Summary	58

10.2	Evaluation Procedures	58

10.2.1	Log and Status File Results	58

10.2.2	Metadata Evaluation	58

10.2.3	Execution of Comparison Software	59

10.2.4	Evaluation of Comparison Software Output	60

10.3	Solutions to Possible Problems	60

11.0	Test and Evaluation Procedures - CER4.1-4.1P5 Aqua Collection 005 Main Processor	62

11.1	Stand Alone Test Procedures	62

11.1.1	Execution	62

11.1.2	Exit Codes	62

11.1.3	Main Processor Test Summary	63

11.2	Evaluation Procedures	63

11.2.1	Log and Status File Results	63

11.2.2	Metadata Evaluation	63

11.2.3	Execution of Comparison Software	63

11.2.4	Evaluation of Comparison Software Output	63

11.3	Solutions to Possible Problems	63

12.0	Test and Evaluation Procedures - CER4.1-4.1P5/CER4.1-4.2P2 2-Day Processor	65

12.1.1	Execution	65

12.1.2	Exit Codes	66

12.1.3	Test Summary	66

12.2	Evaluation Procedures	66

12.2.1	Log and Status File Results	66

12.2.2	Metadata Evaluation	67

12.2.3	Execution of Comparison Software	67

12.2.4	Evaluation of Comparison Software Output	68

12.3	Solutions to Possible Problems	68

13.0	Test and Evaluation Procedures - CER4.1-4.1P6 Aqua and Terra Main Processor	70

13.1	Stand Alone Test Procedures	70

13.1.1	Execution	70

13.1.2	71

13.1.3	Exit Codes	71

13.1.4	Main Processor Test Summary	72

13.2	Evaluation Procedures	72

13.2.1	Log and Status File Results	72

13.2.2	Metadata Evaluation	72

13.2.3	Execution of Comparison Software	72

13.2.4	Evaluation of Comparison Software Output	72

13.3	Solutions to Possible Problems	73

14.0	Test and Evaluation Procedures - CER4.1-4.1P7 NPP Main Processor	74

14.1	Stand Alone Test Procedures	74

14.1.1	Execution	74

14.1.2	Exit Codes	74

14.1.3	Main Processor Test Summary	74

14.2	Evaluation Procedures	74

14.2.1	Log and Status File Results	74

14.2.2	Metadata Evaluation	75

14.2.3	Execution of Comparison Software	75

14.2.4	Evaluation of Comparison Software Output	75

14.3	Solutions to Possible Problems	75

15.0	Test and Evaluation Procedures - CER4.1-4.1P7/CER4.1-4.2P7 2-Day Processor	76

15.1.1	Execution	76

15.1.2	Exit Codes	77

15.1.3	Test Summary	77

15.2	Evaluation Procedures	77

15.2.1	Log and Status File Results	77

15.2.2	Metadata Evaluation	78

15.2.3	Execution of Comparison Software	78

15.2.4	Evaluation of Comparison Software Output	79

15.3	Solutions to Possible Problems	79

16.0	Test and Evaluation Procedures - CER4.1-4.2P1 Daily QC Processor	81

16.1	Stand Alone Test Procedure	81

16.1.1	Execution	81

16.1.1.1	All Data Sources	81

16.1.2	Exit Codes	81

16.1.3	Daily QC Processor Test Summary	81

16.2	Evaluation Procedures	82

16.2.1	Log and Status File Results	82

16.2.2	Metadata Evaluation	82

16.2.3	Execution of Comparison Software	82

16.2.4	Evaluation of Comparison Software Output	82

16.3	Solutions to Possible Problems	82

17.0	Test and Evaluation Procedures - CER4.1-4.2P2 Daily CRH Processor	84

17.1	Stand Alone Test Procedure	84

17.1.1	Execution	84

17.1.2	Exit Codes	84

17.1.3	Daily CRH Processor Test Summary	85

17.2	Evaluation Procedures	85

17.2.1	Log and Status File Results	85

17.2.2	Metadata Evaluation	85

17.2.3	Execution of Comparison Software	85

17.2.4	Evaluation of Comparison Software Output	85

17.3	Solutions to Possible Problems	86

18.0	Test and Evaluation Procedures - CER4.1-4.2P3 Collection 005 Daily QC Processor	87

18.1	Stand Alone Test Procedure	87

18.1.1	Execution	87

18.1.2	Exit Codes	87

18.1.3	Daily QC Processor Test Summary	88

18.2	Evaluation Procedures	88

18.2.1	Log and Status File Results	88

18.2.2	Metadata Evaluation	88

18.2.3	Execution of Comparison Software	88

18.2.4	Evaluation of Comparison Software Output	88

18.3	Solutions to Possible Problems	89

19.0	Test and Evaluation Procedures - CER4.1-4.2P4 Daily QC Processor	90

19.1	Stand Alone Test Procedures	90

19.1.1	Execution	90

19.1.2	Exit Codes	91

19.1.3	Daily QC Processor Test Summary	91

19.2	Evaluation Procedures	91

19.2.1	Log and Status File Results	91

19.2.2	Metadata Evaluation	91

19.2.3	Execution of Comparison Software	91

19.2.4	Evaluation of Comparison Software Output	92

19.3	Solutions to Possible Problems	92

20.0	Test and Evaluation Procedures - CER4.1-4.2P5 Daily QC Processor	93

20.1	Stand Alone Test Procedures	93

20.1.1	Execution	93

20.1.2	Exit Codes	94

20.1.3	Daily QC Processor Test Summary	94

20.2	Evaluation Procedures	94

20.2.1	Log and Status File Results	94

20.2.2	Metadata Evaluation	94

20.2.3	Execution of Comparison Software	94

20.2.4	Evaluation of Comparison Software Output	95

20.3	Solutions to Possible Problems	95

21.0	Test and Evaluation Procedures - CER4.1-4.2P6 Daily QC Processor	96

21.1	Stand Alone Test Procedures	96

21.1.1	Execution	96

21.1.2	Exit Codes	96

21.1.3	Daily QC Processor Test Summary	96

21.2	Evaluation Procedures	96

21.2.1	Log and Status File Results	96

21.2.2	Metadata Evaluation	97

21.2.3	Execution of Comparison Software	97

21.2.4	Evaluation of Comparison Software Output	97

21.3	Solutions to Possible Problems	97

22.0	Test and Evaluation Procedures - CER4.1-4.2P7 Daily QC Processor	98

22.1	Stand Alone Test Procedures	98

22.1.1	Execution	98

22.1.2	Exit Codes	98

22.1.3	Daily QC Processor Test Summary	98

22.2	Evaluation Procedures	98

22.2.1	Log and Status File Results	98

22.2.2	Metadata Evaluation	99

22.2.3	Execution of Comparison Software	99

22.2.4	Evaluation of Comparison Software Output	99

22.3	Solutions to Possible Problems	99

23.0	Test and Evaluation Procedures - CER4.1-4.3P1 Monthly QC Processor	100

23.1	Stand Alone Test Procedures	100

23.1.1	Execution	100

23.1.1.1	All Data Sources	100

23.1.2	Exit Codes	100

23.1.3	Monthly QC Processor Test Summary	100

23.2	Evaluation Procedures	100

23.2.1	Log and Status File Results	101

23.2.2	Metadata Evaluation	101

23.2.3	Execution of Comparison Software	101

23.2.4	Evaluation of Comparison Software Output	101

23.3	Solutions to Possible Problems	101

24.0	Test and Evaluation Procedures - CER4.1-4.3P2 Collection 005 Monthly QC
Processor	103

24.1	Stand Alone Test Procedures	103

24.1.1	Execution	103

24.1.2	Exit Codes	103

24.1.3	Monthly QC Processor Test Summary	104

24.2	Evaluation Procedures	104

24.2.1	Log and Status File Results	104

24.2.2	Metadata Evaluation	104

24.2.3	Execution of Comparison Software	104

24.2.4	Evaluation of Comparison Software Output	104

24.3	Solutions to Possible Problems	105

25.0	Test and Evaluation Procedures - CER4.1-4.3P3 Monthly QC Processor	106

25.1	Stand Alone Test Procedures	106

25.1.1	Execution	106

25.1.2	Exit Codes	107

25.1.3	Daily QC Processor Test Summary	107

25.2	Evaluation Procedures	107

25.2.1	Log and Status File Results	107

25.2.2	Metadata Evaluation	107

25.2.3	Execution of Comparison Software	107

25.2.4	Evaluation of Comparison Software Output	108

25.3	Solutions to Possible Problems	108

26.0	Test and Evaluation Procedures - CER4.1-4.3P4 Monthly QC Processor	109

26.1	Stand Alone Test Procedures	109

26.1.1	Execution	109

26.1.2	Exit Codes	109

26.1.3	Daily QC Processor Test Summary	109

26.2	Evaluation Procedures	109

26.2.1	Log and Status File Results	109

26.2.2	Metadata Evaluation	110

26.2.3	Execution of Comparison Software	110

26.2.4	Evaluation of Comparison Software Output	110

26.3	Solutions to Possible Problems	110

Appendix A - Acronyms and Abbreviations	A-1

Appendix B - Directory Structure Diagrams	B-1

Appendix C - File Description Tables	C-1

C.1	Production Scripts	C-1

C.2	Executables	C-5

C.3	Status Message Files (SMF)	C-6

C.4	Processing Control Files (PCF) and Metadata Control Files (MCF)	C-7

C.5	HDF Read Software	C-10

C.6	Ancillary Input Data	C-10

C.7	Output Temporary Data Files (Production Results)	C-14

Appendix D - Evaluation of Comparison Software Output	D-1

Table C.1-1.  Production Scripts	C-2

Table C.2-1.  Executables1	C-2

Table C.3-1.  Status Message Files	C-2

Table C.4-1.  Metadata Control Files	C-2

Table C.4-2.  Process Control Files1	C-2

Table C.6-1.  Ancillary Input Data	C-2

Table C.6-2.  Ancillary Input Data for CER4.1-4.0P2	C-2

Table C.7-1.  Output Temporary Data Files1	C-2

# Introduction

CERES is a key component of EOS and NPP.  The first CERES instrument (PFM) flew on TRMM, four instruments are currently operating on the EOS Terra (FM1 and FM2) and Aqua (FM3 and FM4) platforms, and NPP (FM5) platform.  CERES measures radiances in three broadband channels:  a shortwave channel (0.3 - 5 m), a total channel (0.3 - 200 m), and an infrared window channel (8 - 12 m).  The last data processed from the PFM instrument aboard TRMM was March 2000; no additional data are expected.  Until June 2005, one instrument on each EOS platform operated in a fixed azimuth scanning mode and the other operated in a rotating azimuth scanning mode; now all are typically operating in the fixed azimuth scanning mode.  The NPP platform carries the FM5 instrument, which operates in the fixed azimuth scanning mode though it has the capability to operate in a rotating azimuth scanning mode.

CERES climate data records involve an unprecedented level of data fusion:  CERES measurements are combined with imager data (e.g., MODIS on Terra and Aqua, VIIRS on NPP), 4-D weather assimilation data, microwave sea-ice observations, and measurements from five geostationary satellites to produce climate-quality radiative fluxes at the top-of-atmosphere, within the atmosphere and at the surface, together with the associated cloud and aerosol properties.

The CERES project management and implementation responsibility is at NASA Langley.  The CERES Science Team is responsible for the instrument design and the derivation and validation of the scientific algorithms used to produce the data products distributed to the atmospheric sciences community.  The CERES DMT is responsible for the development and maintenance of the software that implements the science team’s algorithms in the production environment to produce CERES data products.  The Langley ASDC is responsible for the production environment, data ingest, and the processing, archival, and distribution of the CERES data products.

## Document Overview

This document, CERES Cloud Retrieval and Convolution Subsystems 4.1 through 4.4 Release 5 Test Plan, is part of the CERES Subsystems 4.1 through 4.4 Release 5 delivery package provided to the Atmospheric Science Data Center (ASDC).  It provides a description of the CERES Cloud Retrieval (4.1-4.3) and Convolution of Imager Cloud Properties with CERES Footprint Point Spread Function Subsystem (4.4) Release 5 software; supporting data files; and explains the procedures for installing, executing, and testing the software.  A section is also included on validating the software results.  A description of acronyms and abbreviations is provided in Appendix A, a directory structure diagram is contained in Appendix B, a description of the software and data files is contained in Appendix C, and an evaluation of the comparison software output is contained in Appendix D.

This document is organized as follows:

Section 1.0 -	Introduction

Section 2.0 -	Software and Data File Installation Procedures

Section 3.0 -	Test and Evaluation Procedures - CER4.1-4.0P1 - Snow and Ice Processor

Section 4.0 -	Test and Evaluation Procedures - CER4.1-4.0P2 - Snow and Ice Processor

Section 5.0 -	Test and Evaluation Procedures - CER4.1-4.0P3 Snow and Ice Processor

Section 6.0 -	Test and Evaluation Procedures - CER4.1-4.1P1 - TRMM Main Processor

Section 7.0 -	Test and Evaluation Procedures - CER4.1-4.1P2 - Terra Main Processor

Section 8.0 -	Test and Evaluation Procedures - CER4.1-4.1P3 - Aqua Main Processor

Section 9.0 -	Test and Evaluation Procedures - CER4.1-4.1P4 - Terra Collection 005 Main Processor

Section 10.0 - Test and Evaluation Procedures - CER4.1-4.1P4/CER4.1-4.2P2 2-Day Processor

Section 11.0 -	Test and Evaluation Procedures - CER4.1-4.1P5 - Aqua Collection 005 Main Processor

Section 12.0 -	Test and Evaluation Procedures - CER4.1-4.1P5/CER4.1-4.2P2 2-Day Processor

Section 13.0 -	Test and Evaluation Procedures - CER4.1-4.1P6 Aqua and Terra Main Processor

Section 14.0 -	Test and Evaluation Procedures - CER4.1-4.1P6/CER4.1-4.2P5 2-Day QC Processor

Section 15.0 -	Test and Evaluation Procedures - CER4.1-4.1P7 NPP Main Processor

Section 16.0 -	Test and Evaluation Procedures - CER4.1-4.1P7/CER4.1-4.2P7 2-Day Processor

Section 17.0 - Test and Evaluation Procedures - CER4.1-4.2P1 Daily QC Processor

Section 18.0 -	Test and Evaluation Procedures - CER4.1-4.2P2 Daily CRH Processor

Section 19.0 -	Test and Evaluation Procedures - CER4.1-4.2P3 Collection 005 Daily QC Processor

Section 20.0-	Test and Evaluation Procedures - CER4.1-4.2P4 Daily QC Processor

Section 21.0 -	Test and Evaluation Procedures - CER4.1-4.2P5 Daily QC Processor

Section 22.0 - Test and Evaluation Procedures - CER4.1-4.2P6 Daily QC Processor

Section 23.0 - Test and Evaluation Procedures - CER4.1-4.2P7 Daily QC Processor

Section 24.0 - Test and Evaluation Procedures - CER4.1-4.3P1 Monthly QC Processor

Section 25.0 -	Test and Evaluation Procedures - CER4.1-4.3P2 Collection 005 Monthly QC Processor

Section 26.0 -	Test and Evaluation Procedures - CER4.1-4.3P3 Monthly QC Processor

Section 27.0 -	Test and Evaluation Procedures - CER4.1-4.3P4 Monthly QC Processor

Appendix A -	Acronyms and Abbreviations

Appendix B -	Directory Structure Diagram

Appendix C -	File Description Tables

Appendix D -	Evaluation of Comparison Software Output

## Subsystem Overview

### CER4.1-4.0P1 - Snow and Ice Processor

The Snow and Ice Preprocessor reads available NSIDC and NESDIS Snow and Ice data sets for a given day and reprojects the data onto a 10-minute grid for use in Clouds Processing.

The primary input data set for the Snow and Ice Processor is the National Snow and Ice Data Center’s Snow and Ice Map and National Environmental Satellite, Data & Information Services’ Snow and Ice Maps.  The primary output consists of individual 10-minute snow and ice maps.

### CER4.1-4.0P2 - Snow and Ice Processor

The Snow and Ice Preprocessor reads available NSIDC and NESDIS Snow and Ice data sets for a given day and reprojects the data onto a 10-minute grid for use in Clouds Processing.

The primary input data set for the Snow and Ice Processor is the National Snow and Ice Data Center’s Snow and either National Environmental Satellite, Data & Information Services’ Snow and Ice Maps or Comprehensive Large Array-Data Stewardship System’s Snow and Ice Maps. The primary output consists of individual 10-minute snow and ice maps.

### CER4.1-4.0P3 - Snow and Ice Processor

The Snow and Ice Preprocessor reads available NSIDC and AFWA Snow and Ice data sets for a given day and reprojects the data onto a 10-minute grid for use in Clouds Processing.

The primary input data set for the Snow and Ice Processor is the National Snow and Ice Data Center’s Snow and Ice Map and Air Force Weather Agency’s 16th Mesh Snow and Ice Maps.  The primary output consists of individual 10-minute snow and ice maps.

### CER4.1-4.1P1 - TRMM Main Processor

CER4.1-4.1P1 consists of two executables.  The initial one is Cloud Retrieval Subsystem that produces a set of imager pixel clouds properties.  It is followed by Convolution Subsystem that averages cloud microphysical and optical properties from imager pixels that are within the field of view of the CERES footprints.

The objective of the Cloud Retrieval Subsystem is to use high spectral and spatial resolution cloud imager data to determine cloud microphysical and optical properties.  The major Cloud Retrieval science requirements include

Prepare a “chunk” of pixels (multiple scan lines of imager data):  Attach the imager radiometric data and various ancillary data to each imager pixel within the chunk.  Classify each pixel as clear, cloudy, or uncertain.  The pixel classification process uses various tests on the imager radiometric data and ancillary data to determine a cloud mask.

Determine cloud macrophysical properties (cloud layer and cloud top pressure) for cloudy pixels.

Determine cloud microphysical and optical properties (cloud base, effective radiating center, temperature, pressure, particle phase, particle size, optical depth at 0.65 micron, water/ice path, emittance at 10.8 micron, etc.) for cloudy pixels.

The primary input data sets for the Release 3 Cloud Retrieval Subsystem are:

- Cloud Imager Data (CID):  The CID product contains time code, pixel location, viewing geometry, and radiance data.  The Release 3 test data are Visible Infrared Scanner, VIRS, and Moderate Resolution Imager Spectroradiometer, MODIS, imager data from the TRMM and Terra spacecraft, respectively.

SURFace MAP (SURFMAP):  The SURFMAP data product is a set of maps for elevation, water content, scene ID, ecosystem, snow depth, ice coverage, and a terrain map on a 10-minute equal-angle grid.

Meteorological, Ozone, and Aerosol (MOA):  The MOA data product contains meteorological data on the 1.0 x 1.0-degree European Center for Medium-range Weather Prediction (primary) or the 2.0 x 2.5-degree Data Assimilation Office (DAO) grid.  (Surface temperature, surface pressure, atmospheric temperature, humidity, ozone and wind velocity profiles, precipitable water, column ozone and aerosols.)

Clear Radiance History (CRH):  The Release 3 CRH data product contains albedo, brightness temperature, and the cosine of the solar zenith angle on a 10-minute equal-angle grid.

The primary output products of the Cloud Retrieval Subsystem are:

- Cookiedough:  The pixel-based cloud properties, input to Subsystem 4.4

CloudVis and Subset CloudVis:  Visualization products

A binary Quality Control (QC) report

CRH_Update:  Contains CRH values for all clear pixels in the hour

The objective of the Convolution Subsystem is to average the higher spectral and spatial resolution cloud imager data derived cloud microphysical and optical properties within the larger CERES footprint weighted by the CERES instruments point spread function.  This provides a set of cloud properties optimally designed for studies of the role of clouds in the Earth's radiation budget, and enables the cloud physical properties to be tied to the cloud broadband radiative properties in a consistent manner.  This initial estimate of cloud properties is modified in Subsystem 5 to obtain consistency in cloud properties and Top-of-the-Atmosphere (TOA) broadband radiative fluxes.

The major objectives of this Subsystem include:

- Locate imager pixels within a CERES footprint by calculating the value of the Point Spread Function (PSF) for each pixel with respect to the centroid of the CERES field of view (FOV).  If the PSF value exceeds a specified threshold value, the pixel is included in the footprint.

Accumulate statistics of cloud properties for all imager pixels within the CERES footprint and write the footprint records to the intermediate Single Scanner Footprint TOA and Surface Fluxes Clouds (SSF) output file.

Write diagnostic and statistical information from each run to the Quality Control (QC) report files.

The primary input data sets for the Convolution Subsystem are:

- The CERES Instrument Earth Scans (IES) data product contains time of observation, geolocation data, and filtered radiances for each footprint in spatial order.  The CERES footprint effective diameter is 10 km for Tropical Rainfall Measuring Mission (TRMM) spacecraft and 20 km for EOS AM and PM spacecraft.  IES file from both TRMM and Terra are used as the test data sets for Release 3.

The cloud imager data from Advanced Very High Resolution Radiometer (AVHRR), Visible Infrared Scanner (VIRS), or Moderate-Resolution Imaging Spectroradiometer (MODIS) are processed by Subsystems 4.1 - 4.3 and passed to convolution via the Imager Pixel Data file, commonly designated “Cookiedough.”  This file represents a two-dimensional array (N scanlines by M pixels per scanline) with a data structure associated with each pixel containing pixel location, viewing geometry, observation time, multispectral radiance data, scene type, and cloud properties as determined in Subsystems 4.1 through 4.3.

The output science product is the intermediate SSF product (SSFI).  The intermediate SSF is subsequently processed and completed by Subsystem 4.5-4.6, and the resulting final SSF is an hourly CERES archival product that contains footprint geometry, radiance information, and the statistics for full footprint, clear footprint, cloudy footprint and overlap footprint areas.  The secondary output products are the quality control reports.  The quality control reports contain processing information, informative messages, and statistics.  In Release 3, Subsystem 4.4 creates both a formatted (ASCII) report file (FQC) and a binary report file (FQCI) which is intended to be postprocessed by one or more of a variety of flexible programs for browsing, display, or data extraction.

### CER4.1-4.1P2 - Terra Main Processor

CER4.1-4.1P2 consists of two executables.  The initial one is Cloud Retrieval Subsystem that produces a set of imager pixel clouds properties.  It is followed by Convolution Subsystem that averages cloud microphysical and optical properties from imager pixels that are within the field of view of the CERES footprints.

The objective of the Cloud Retrieval Subsystem is to use high spectral and spatial resolution cloud imager data to determine cloud microphysical and optical properties.  The major Cloud Retrieval science requirements include

- Prepare a “chunk” of pixels (multiple scan lines of imager data):  Attach the imager radiometric data and various ancillary data to each imager pixel within the chunk.  Classify each pixel as clear, cloudy, or uncertain.  The pixel classification process uses various tests on the imager radiometric data and ancillary data to determine a cloud mask.

Determine cloud macrophysical properties (cloud layer and cloud top pressure) for cloudy pixels.

Determine cloud microphysical and optical properties (cloud base, effective radiating center, temperature, pressure, particle phase, particle size, optical depth at 0.65 micron, water/ice path, emittance at 10.8 micron, etc.) for cloudy pixels.

The primary input data sets for the Release 3 Cloud Retrieval Subsystem are:

- Cloud Imager Data (CID):  The CID product contains time code, pixel location, viewing geometry, and radiance data.  The Release 3 test data are Visible Infrared Scanner, VIRS, and Moderate Resolution Imager Spectroradiometer, MODIS, imager data from the TRMM and Terra spacecraft, respectively.

SURFace MAP (SURFMAP):  The SURFMAP data product is a set of maps for elevation, water content, scene ID, ecosystem, snow depth, ice coverage, and a terrain map on a 10-minute equal-angle grid.

Meteorological, Ozone, and Aerosol (MOA):  The MOA data product contains meteorological data on the 1.0 x 1.0-degree European Center for Medium-range Weather Prediction (primary) or the 2.0 x 2.5-degree Data Assimilation Office (DAO) grid.  (Surface temperature, surface pressure, atmospheric temperature, humidity, ozone and wind velocity profiles, precipitable water, column ozone and aerosols.)

Clear Radiance History (CRH):  The Release 3 CRH data product contains albedo, brightness temperature, and the cosine of the solar zenith angle on a 10-minute equal-angle grid.

MODIS Aerosol Properties (MOD04):  The MOD04 data product contains aerosol properties over both land and ocean determined from MODIS specific algorithms.

The primary output products of the Cloud Retrieval Subsystem are:

- Cookiedough:  The pixel-based cloud properties, input to Subsystem 4.4

CloudVis and Subset CloudVis:  Visualization products

A binary Quality Control (QC) report

CRH_Update:  Contains CRH values for all clear pixels in the hour

The objective of the Convolution Subsystem is to average the higher spectral and spatial resolution cloud imager data derived cloud microphysical and optical properties within the larger CERES footprint weighted by the CERES instruments point spread function.  This provides a set of cloud properties optimally designed for studies of the role of clouds in the Earth's radiation budget, and enables the cloud physical properties to be tied to the cloud broadband radiative properties in a consistent manner.  This initial estimate of cloud properties is modified in Subsystem 5 to obtain consistency in cloud properties and Top-of-the-Atmosphere (TOA) broadband radiative fluxes.

The major objectives of this Subsystem include:

- Locate imager pixels within a CERES footprint by calculating the value of the Point Spread Function (PSF) for each pixel with respect to the centroid of the CERES field of view (FOV).  If the PSF value exceeds a specified threshold value, the pixel is included in the footprint.

Accumulate statistics of cloud properties for all imager pixels within the CERES footprint and write the footprint records to the intermediate Single Scanner Footprint TOA and Surface Fluxes Clouds (SSF) output file.

Write diagnostic and statistical information from each run to the Quality Control (QC) report files.

The primary input data sets for the Convolution Subsystem are:

- The CERES Instrument Earth Scans (IES) data product contains time of observation, geolocation data, and filtered radiances for each footprint in spatial order.  The CERES footprint effective diameter is 10 km for Tropical Rainfall Measuring Mission (TRMM) spacecraft and 20 km for EOS AM and PM spacecraft.  IES file from both TRMM and Terra are used as the test data sets for Release 3.

The cloud imager data from Advanced Very High Resolution Radiometer (AVHRR), Visible Infrared Scanner (VIRS), or Moderate-Resolution Imaging Spectroradiometer (MODIS) are processed by Subsystems 4.1 - 4.3 and passed to convolution via the Imager Pixel Data file, commonly designated “Cookiedough.”  This file represents a two-dimensional array (N scanlines by M pixels per scanline) with a data structure associated with each pixel containing pixel location, viewing geometry, observation time, multispectral radiance data, scene type, and cloud properties as determined in Subsystems 4.1 through 4.3.

The output science product is the intermediate SSF product (SSFI).  The intermediate SSF is subsequently processed and completed by Subsystem 4.5-4.6, and the resulting final SSF is an hourly CERES archival product that contains footprint geometry, radiance information, and the statistics for full footprint, clear footprint, cloudy footprint and overlap footprint areas.  The secondary output products are the quality control reports.  The quality control reports contain processing information, informative messages, and statistics.  In Release 3, Subsystem 4.4 creates both a formatted (ASCII) report file (FQC) and a binary report file (FQCI) which is intended to be postprocessed by one or more of a variety of flexible programs for browsing, display, or data extraction.

### CER4.1-4.1P3 - Aqua Main Processor

CER4.1-4.1P3 consists of two executables.  The initial one is Cloud Retrieval Subsystem that produces a set of imager pixel clouds properties.  It is followed by Convolution Subsystem that averages cloud microphysical and optical properties from imager pixels that are within the field of view of the CERES footprints.

The objective of the Cloud Retrieval Subsystem is to use high spectral and spatial resolution cloud imager data to determine cloud microphysical and optical properties.  The major Cloud Retrieval science requirements include

- Prepare a “chunk” of pixels (multiple scan lines of imager data):  Attach the imager radiometric data and various ancillary data to each imager pixel within the chunk.  Classify each pixel as clear, cloudy, or uncertain.  The pixel classification process uses various tests on the imager radiometric data and ancillary data to determine a cloud mask.

Determine cloud macrophysical properties (cloud layer and cloud top pressure) for cloudy pixels.

Determine cloud microphysical and optical properties (cloud base, effective radiating center, temperature, pressure, particle phase, particle size, optical depth at 0.65 micron, water/ice path, emittance at 10.8 micron, etc.) for cloudy pixels.

The primary input data sets for the Release 3 Cloud Retrieval Subsystem are:

- Cloud Imager Data (CID):  The CID product contains time code, pixel location, viewing geometry, and radiance data.  The Release 3 test data are Visible Infrared Scanner, VIRS, and Moderate Resolution Imager Spectroradiometer, MODIS, imager data from the TRMM and Terra spacecraft, respectively.

SURFace MAP (SURFMAP):  The SURFMAP data product is a set of maps for elevation, water content, scene ID, ecosystem, snow depth, ice coverage, and a terrain map on a 10-minute equal-angle grid.

Meteorological, Ozone, and Aerosol (MOA):  The MOA data product contains meteorological data on the 1.0 x 1.0-degree European Center for Medium-range Weather Prediction (primary) or the 2.0 x 2.5-degree Data Assimilation Office (DAO) grid.  (Surface temperature, surface pressure, atmospheric temperature, humidity, ozone and wind velocity profiles, precipitable water, column ozone and aerosols.)

Clear Radiance History (CRH):  The Release 3 CRH data product contains albedo, brightness temperature, and the cosine of the solar zenith angle on a 10-minute equal-angle grid.

The primary output products of the Cloud Retrieval Subsystem are:

- Cookiedough:  The pixel-based cloud properties, input to Subsystem 4.4

CloudVis and Subset CloudVis:  Visualization products

A binary Quality Control (QC) report

CRH_Update:  Contains CRH values for all clear pixels in the hour

The objective of the Convolution Subsystem is to average the higher spectral and spatial resolution cloud imager data derived cloud microphysical and optical properties within the larger CERES footprint weighted by the CERES instruments point spread function.  This provides a set of cloud properties optimally designed for studies of the role of clouds in the Earth's radiation budget, and enables the cloud physical properties to be tied to the cloud broadband radiative properties in a consistent manner.  This initial estimate of cloud properties is modified in Subsystem 5 to obtain consistency in cloud properties and Top-of-the-Atmosphere (TOA) broadband radiative fluxes.

The major objectives of this Subsystem include:

- Locate imager pixels within a CERES footprint by calculating the value of the Point Spread Function (PSF) for each pixel with respect to the centroid of the CERES field of view (FOV).  If the PSF value exceeds a specified threshold value, the pixel is included in the footprint.

Accumulate statistics of cloud properties for all imager pixels within the CERES footprint and write the footprint records to the intermediate Single Scanner Footprint TOA and Surface Fluxes Clouds (SSF) output file.

Write diagnostic and statistical information from each run to the Quality Control (QC) report files.

The primary input data sets for the Convolution Subsystem are:

- The CERES Instrument Earth Scans (IES) data product contains time of observation, geolocation data, and filtered radiances for each footprint in spatial order.  The CERES footprint effective diameter is 10 km for Tropical Rainfall Measuring Mission (TRMM) spacecraft and 20 km for EOS AM and PM spacecraft.  IES file from both TRMM and Terra are used as the test data sets for Release 3.

The cloud imager data from Advanced Very High Resolution Radiometer (AVHRR), Visible Infrared Scanner (VIRS), or Moderate-Resolution Imaging Spectroradiometer (MODIS) are processed by Subsystems 4.1 - 4.3 and passed to convolution via the Imager Pixel Data file, commonly designated “Cookiedough.”  This file represents a two-dimensional array (N scanlines by M pixels per scanline) with a data structure associated with each pixel containing pixel location, viewing geometry, observation time, multispectral radiance data, scene type, and cloud properties as determined in Subsystems 4.1 through 4.3.

The output science product is the intermediate SSF product (SSFI).  The intermediate SSF is subsequently processed and completed by Subsystem 4.5-4.6, and the resulting final SSF is an hourly CERES archival product that contains footprint geometry, radiance information, and the statistics for full footprint, clear footprint, cloudy footprint and overlap footprint areas.  The secondary output products are the quality control reports.  The quality control reports contains processing information, informative messages, and statistics.  In Release 3, Subsystem 4.4 creates both a formatted (ASCII) report file (FQC) and a binary report file (FQCI) which is intended to be postprocessed by one or more of a variety of flexible programs for browsing, display, or data extraction.

### CER4.1-4.1P4 - Terra Main Processor

CER4.1-4.1P4 consists of two executables.  The initial one is Cloud Retrieval Subsystem that produces a set of imager pixel clouds properties.  It is followed by Convolution Subsystem that averages cloud microphysical and optical properties from imager pixels that are within the field of view of the CERES footprints.

The objective of the Cloud Retrieval Subsystem is to use high spectral and spatial resolution cloud imager data to determine cloud microphysical and optical properties.  The major Cloud Retrieval science requirements include

- Prepare a “chunk” of pixels (multiple scan lines of imager data):  Attach the imager radiometric data and various ancillary data to each imager pixel within the chunk.  Classify each pixel as clear, cloudy, or uncertain.  The pixel classification process uses various tests on the imager radiometric data and ancillary data to determine a cloud mask.

Determine cloud macrophysical properties (cloud layer and cloud top pressure) for cloudy pixels.

Determine cloud microphysical and optical properties (cloud base, effective radiating center, temperature, pressure, particle phase, particle size, optical depth at 0.65 micron, water/ice path, emittance at 10.8 micron, etc.) for cloudy pixels.

The primary input data sets for the Release 3 Cloud Retrieval Subsystem are:

- Cloud Imager Data (CID):  The CID product contains time code, pixel location, viewing geometry, and radiance data.  The Release 3 test data are Visible Infrared Scanner, VIRS, and Moderate Resolution Imager Spectroradiometer, MODIS, imager data from the TRMM and Terra spacecraft, respectively.

SURFace MAP (SURFMAP):  The SURFMAP data product is a set of maps for elevation, water content, scene ID, ecosystem, snow depth, ice coverage, and a terrain map on a 10-minute equal-angle grid.

Meteorological, Ozone, and Aerosol (MOA):  The MOA data product contains meteorological data on the 1.0 x 1.0-degree European Center for Medium-range Weather Prediction (primary) or the 2.0 x 2.5-degree Data Assimilation Office (DAO) grid.  (Surface temperature, surface pressure, atmospheric temperature, humidity, ozone and wind velocity profiles, precipitable water, column ozone and aerosols.)

Clear Radiance History (CRH):  The Release 3 CRH data product contains albedo, brightness temperature, and the cosine of the solar zenith angle on a 10-minute equal-angle grid.

MODIS Aerosol Properties (MOD04):  The MOD04 data product contains aerosol properties over both land and ocean determined from MODIS specific algorithms.

The primary output products of the Cloud Retrieval Subsystem are:

- Cookiedough:  The pixel-based cloud properties, input to Subsystem 4.4

CloudVis and Subset CloudVis:  Visualization products

A binary Quality Control (QC) report

CRH_Update:  Contains CRH values for all clear pixels in the hour

The objective of the Convolution Subsystem is to average the higher spectral and spatial resolution cloud imager data derived cloud microphysical and optical properties within the larger CERES footprint weighted by the CERES instruments point spread function.  This provides a set of cloud properties optimally designed for studies of the role of clouds in the Earth's radiation budget, and enables the cloud physical properties to be tied to the cloud broadband radiative properties in a consistent manner.  This initial estimate of cloud properties is modified in Subsystem 5 to obtain consistency in cloud properties and Top-of-the-Atmosphere (TOA) broadband radiative fluxes.

The major objectives of this Subsystem include:

- Locate imager pixels within a CERES footprint by calculating the value of the Point Spread Function (PSF) for each pixel with respect to the centroid of the CERES field of view (FOV).  If the PSF value exceeds a specified threshold value, the pixel is included in the footprint.

Accumulate statistics of cloud properties for all imager pixels within the CERES footprint and write the footprint records to the intermediate Single Scanner Footprint TOA and Surface Fluxes Clouds (SSF) output file.

Write diagnostic and statistical information from each run to the Quality Control (QC) report files.

The primary input data sets for the Convolution Subsystem are:

- The CERES Instrument Earth Scans (IES) data product contains time of observation, geolocation data, and filtered radiances for each footprint in spatial order.  The CERES footprint effective diameter is 10 km for Tropical Rainfall Measuring Mission (TRMM) spacecraft and 20 km for EOS AM and PM spacecraft.  IES file from both TRMM and Terra are used as the test data sets for Release 3.

The cloud imager data from Advanced Very High Resolution Radiometer (AVHRR), Visible Infrared Scanner (VIRS), or Moderate-Resolution Imaging Spectroradiometer (MODIS) are processed by Subsystems 4.1 - 4.3 and passed to convolution via the Imager Pixel Data file, commonly designated “Cookiedough.”  This file represents a two-dimensional array (N scanlines by M pixels per scanline) with a data structure associated with each pixel containing pixel location, viewing geometry, observation time, multispectral radiance data, scene type, and cloud properties as determined in Subsystems 4.1 through 4.3.

The output science product is the intermediate SSF product (SSFI).  The intermediate SSF is subsequently processed and completed by Subsystem 4.5-4.6, and the resulting final SSF is an hourly CERES archival product that contains footprint geometry, radiance information, and the statistics for full footprint, clear footprint, cloudy footprint and overlap footprint areas.  The secondary output products are the quality control reports.  The quality control reports contain processing information, informative messages, and statistics.  In Release 3, Subsystem 4.4 creates both a formatted (ASCII) report file (FQC) and a binary report file (FQCI) which is intended to be postprocessed by one or more of a variety of flexible programs for browsing, display, or data extraction.

### CER4.1-4.1P5 - Aqua Main Processor

CER4.1-4.1P5 consists of two executables.  The initial one is Cloud Retrieval Subsystem that produces a set of imager pixel clouds properties.  It is followed by Convolution Subsystem that averages cloud microphysical and optical properties from imager pixels that are within the field of view of the CERES footprints.

The objective of the Cloud Retrieval Subsystem is to use high spectral and spatial resolution cloud imager data to determine cloud microphysical and optical properties.  The major Cloud Retrieval science requirements include

- Prepare a “chunk” of pixels (multiple scan lines of imager data):  Attach the imager radiometric data and various ancillary data to each imager pixel within the chunk.  Classify each pixel as clear, cloudy, or uncertain.  The pixel classification process uses various tests on the imager radiometric data and ancillary data to determine a cloud mask.

Determine cloud macrophysical properties (cloud layer and cloud top pressure) for cloudy pixels.

Determine cloud microphysical and optical properties (cloud base, effective radiating center, temperature, pressure, particle phase, particle size, optical depth at 0.65 micron, water/ice path, emittance at 10.8 micron, etc.) for cloudy pixels.

The primary input data sets for the Release 3 Cloud Retrieval Subsystem are:

- Cloud Imager Data (CID):  The CID product contains time code, pixel location, viewing geometry, and radiance data.  The Release 3 test data are Visible Infrared Scanner, VIRS, and Moderate Resolution Imager Spectroradiometer, MODIS, imager data from the TRMM and Terra spacecraft, respectively.

SURFace MAP (SURFMAP):  The SURFMAP data product is a set of maps for elevation, water content, scene ID, ecosystem, snow depth, ice coverage, and a terrain map on a 10-minute equal-angle grid.

Meteorological, Ozone, and Aerosol (MOA):  The MOA data product contains meteorological data on the 1.0 x 1.0-degree European Center for Medium-range Weather Prediction (primary) or the 2.0 x 2.5-degree Data Assimilation Office (DAO) grid.  (Surface temperature, surface pressure, atmospheric temperature, humidity, ozone and wind velocity profiles, precipitable water, column ozone and aerosols.)

Clear Radiance History (CRH):  The Release 3 CRH data product contains albedo, brightness temperature, and the cosine of the solar zenith angle on a 10-minute equal-angle grid.

The primary output products of the Cloud Retrieval Subsystem are:

- Cookiedough:  The pixel-based cloud properties, input to Subsystem 4.4

CloudVis and Subset CloudVis:  Visualization products

A binary Quality Control (QC) report

CRH_Update:  Contains CRH values for all clear pixels in the hour

The objective of the Convolution Subsystem is to average the higher spectral and spatial resolution cloud imager data derived cloud microphysical and optical properties within the larger CERES footprint weighted by the CERES instruments point spread function.  This provides a set of cloud properties optimally designed for studies of the role of clouds in the Earth's radiation budget, and enables the cloud physical properties to be tied to the cloud broadband radiative properties in a consistent manner.  This initial estimate of cloud properties is modified in Subsystem 5 to obtain consistency in cloud properties and Top-of-the-Atmosphere (TOA) broadband radiative fluxes.

The major objectives of this Subsystem include:

- Locate imager pixels within a CERES footprint by calculating the value of the Point Spread Function (PSF) for each pixel with respect to the centroid of the CERES field of view (FOV).  If the PSF value exceeds a specified threshold value, the pixel is included in the footprint.

Accumulate statistics of cloud properties for all imager pixels within the CERES footprint and write the footprint records to the intermediate Single Scanner Footprint TOA and Surface Fluxes Clouds (SSF) output file.

Write diagnostic and statistical information from each run to the Quality Control (QC) report files.

The primary input data sets for the Convolution Subsystem are:

- The CERES Instrument Earth Scans (IES) data product contains time of observation, geolocation data, and filtered radiances for each footprint in spatial order.  The CERES footprint effective diameter is 10 km for Tropical Rainfall Measuring Mission (TRMM) spacecraft and 20 km for EOS AM and PM spacecraft.  IES file from both TRMM and Terra are used as the test data sets for Release 3.

The cloud imager data from Advanced Very High Resolution Radiometer (AVHRR), Visible Infrared Scanner (VIRS), or Moderate-Resolution Imaging Spectroradiometer (MODIS) are processed by Subsystems 4.1 - 4.3 and passed to convolution via the Imager Pixel Data file, commonly designated “Cookiedough.”  This file represents a two-dimensional array (N scanlines by M pixels per scanline) with a data structure associated with each pixel containing pixel location, viewing geometry, observation time, multispectral radiance data, scene type, and cloud properties as determined in Subsystems 4.1 through 4.3.

The output science product is the intermediate SSF product (SSFI).  The intermediate SSF is subsequently processed and completed by Subsystem 4.5-4.6, and the resulting final SSF is an hourly CERES archival product that contains footprint geometry, radiance information, and the statistics for full footprint, clear footprint, cloudy footprint and overlap footprint areas.  The secondary output products are the quality control reports.  The quality control reports contains processing information, informative messages, and statistics.  In Release 3, Subsystem 4.4 creates both a formatted (ASCII) report file (FQC) and a binary report file (FQCI) which is intended to be postprocessed by one or more of a variety of flexible programs for browsing, display, or data extraction.

### CER4.1-4.1P6 - Main Processor

CER4.1-4.1P6 consists of two executables.  The initial one is Cloud Retrieval Subsystem that produces a set of imager pixel clouds properties.  It is followed by Convolution Subsystem that averages cloud microphysical and optical properties from imager pixels that are within the field of view of the CERES footprints.

The objective of the Cloud Retrieval Subsystem is to use high spectral and spatial resolution cloud imager data to determine cloud microphysical and optical properties.  The major Cloud Retrieval science requirements include

- Prepare a “chunk” of pixels (multiple scan lines of imager data):  Attach the imager radiometric data and various ancillary data to each imager pixel within the chunk.  Classify each pixel as clear, cloudy, or uncertain.  The pixel classification process uses various tests on the imager radiometric data and ancillary data to determine a cloud mask.

Determine cloud macrophysical properties (cloud layer and cloud top pressure) for cloudy pixels.

Determine cloud microphysical and optical properties (cloud base, effective radiating center, temperature, pressure, particle phase, particle size, optical depth at 0.65 micron, water/ice path, emittance at 10.8 micron, etc.) for cloudy pixels.

The primary input data sets for the Release 3 Cloud Retrieval Subsystem are:

- Cloud Imager Data (CID):  The CID product contains time code, pixel location, viewing geometry, and radiance data.  The Release 3 test data are Visible Infrared Scanner, VIRS, and Moderate Resolution Imager Spectroradiometer, MODIS, imager data from the TRMM and Terra spacecraft, respectively.

SURFace MAP (SURFMAP):  The SURFMAP data product is a set of maps for elevation, water content, scene ID, ecosystem, snow depth, ice coverage, and a terrain map on a 10-minute equal-angle grid.

Meteorological, Ozone, and Aerosol (MOA):  The MOA data product contains meteorological data on the 1.0 x 1.0-degree European Center for Medium-range Weather Prediction (primary) or the 2.0 x 2.5-degree Data Assimilation Office (DAO) grid.  (Surface temperature, surface pressure, atmospheric temperature, humidity, ozone and wind velocity profiles, precipitable water, column ozone and aerosols.)

Clear Radiance History (CRH):  The Release 3 CRH data product contains albedo, brightness temperature, and the cosine of the solar zenith angle on a 10-minute equal-angle grid.

The primary output products of the Cloud Retrieval Subsystem are:

- Cookiedough:  The pixel-based cloud properties, input to Subsystem 4.4

CloudVis and Subset CloudVis:  Visualization products

A binary Quality Control (QC) report

CRH_Update:  Contains CRH values for all clear pixels in the hour

The objective of the Convolution Subsystem is to average the higher spectral and spatial resolution cloud imager data derived cloud microphysical and optical properties within the larger CERES footprint weighted by the CERES instruments point spread function.  This provides a set of cloud properties optimally designed for studies of the role of clouds in the Earth's radiation budget, and enables the cloud physical properties to be tied to the cloud broadband radiative properties in a consistent manner.  This initial estimate of cloud properties is modified in Subsystem 5 to obtain consistency in cloud properties and Top-of-the-Atmosphere (TOA) broadband radiative fluxes.

The major objectives of this Subsystem include:

- Locate imager pixels within a CERES footprint by calculating the value of the Point Spread Function (PSF) for each pixel with respect to the centroid of the CERES field of view (FOV).  If the PSF value exceeds a specified threshold value, the pixel is included in the footprint.

Accumulate statistics of cloud properties for all imager pixels within the CERES footprint and write the footprint records to the intermediate Single Scanner Footprint TOA and Surface Fluxes Clouds (SSF) output file.

Write diagnostic and statistical information from each run to the Quality Control (QC) report files.

The primary input data sets for the Convolution Subsystem are:

- The CERES Instrument Earth Scans (IES) data product contains time of observation, geolocation data, and filtered radiances for each footprint in spatial order.  The CERES footprint effective diameter is 10 km for Tropical Rainfall Measuring Mission (TRMM) spacecraft and 20 km for EOS AM and PM spacecraft.  IES file from both TRMM and Terra are used as the test data sets for Release 3.

The cloud imager data from Advanced Very High Resolution Radiometer (AVHRR), Visible Infrared Scanner (VIRS), or Moderate-Resolution Imaging Spectroradiometer (MODIS) are processed by Subsystems 4.1 - 4.3 and passed to convolution via the Imager Pixel Data file, commonly designated “Cookiedough.”  This file represents a two-dimensional array (N scanlines by M pixels per scanline) with a data structure associated with each pixel containing pixel location, viewing geometry, observation time, multispectral radiance data, scene type, and cloud properties as determined in Subsystems 4.1 through 4.3.

The output science product is the intermediate SSF product (SSFI).  The intermediate SSF is subsequently processed and completed by Subsystem 4.5-4.6, and the resulting final SSF is an hourly CERES archival product that contains footprint geometry, radiance information, and the statistics for full footprint, clear footprint, cloudy footprint and overlap footprint areas.  The secondary output products are the quality control reports.  The quality control reports contain processing information, informative messages, and statistics.  In Release 3, Subsystem 4.4 creates both a formatted (ASCII) report file (FQC) and a binary report file (FQCI) which is intended to be postprocessed by one or more of a variety of flexible programs for browsing, display, or data extraction.

### CER4.1-4.1P7 - Main Processor

CER4.1-4.1P7 consists of two executables.  The initial one is Cloud Retrieval Subsystem that produces a set of imager pixel clouds properties.  It is followed by Convolution Subsystem that averages cloud microphysical and optical properties from imager pixels that are within the field of view of the CERES footprints.

The objective of the Cloud Retrieval Subsystem is to use high spectral and spatial resolution cloud imager data to determine cloud microphysical and optical properties.  The major Cloud Retrieval science requirements include

- Prepare a “chunk” of pixels (multiple scan lines of imager data):  Attach the imager radiometric data and various ancillary data to each imager pixel within the chunk.  Classify each pixel as clear, cloudy, or uncertain.  The pixel classification process uses various tests on the imager radiometric data and ancillary data to determine a cloud mask.

Determine cloud macrophysical properties (cloud layer and cloud top pressure) for cloudy pixels.

Determine cloud microphysical and optical properties (cloud base, effective radiating center, temperature, pressure, particle phase, particle size, optical depth at 0.65 micron, water/ice path, emittance at 10.8 micron, etc.) for cloudy pixels.

The primary input data sets for the Release 3 Cloud Retrieval Subsystem are:

- Cloud Imager Data (CID):  The CID product contains time code, pixel location, viewing geometry, and radiance data.  The Release 3 test data are Visible Infrared Scanner, VIRS, and Moderate Resolution Imager Spectroradiometer, MODIS, imager data from the TRMM and Terra spacecraft, respectively, Visible Infrared Imaging Radiometer Suite, VIIRS.

SURFace MAP (SURFMAP):  The SURFMAP data product is a set of maps for elevation, water content, scene ID, ecosystem, snow depth, ice coverage, and a terrain map on a 10-minute equal-angle grid.

Meteorological, Ozone, and Aerosol (MOA):  The MOA data product contains meteorological data on the 1.0 x 1.0-degree European Center for Medium-range Weather Prediction (primary) or the 2.0 x 2.5-degree Data Assimilation Office (DAO) grid.  (Surface temperature, surface pressure, atmospheric temperature, humidity, ozone and wind velocity profiles, precipitable water, column ozone and aerosols.)

Clear Radiance History (CRH):  The Release 3 CRH data product contains albedo, brightness temperature, and the cosine of the solar zenith angle on a 10-minute equal-angle grid.

The primary output products of the Cloud Retrieval Subsystem are:

- Cookiedough:  The pixel-based cloud properties, input to Subsystem 4.4

CloudVis and Subset CloudVis:  Visualization products

A binary Quality Control (QC) report

CRH_Update:  Contains CRH values for all clear pixels in the hour

The objective of the Convolution Subsystem is to average the higher spectral and spatial resolution cloud imager data derived cloud microphysical and optical properties within the larger CERES footprint weighted by the CERES instruments point spread function.  This provides a set of cloud properties optimally designed for studies of the role of clouds in the Earth's radiation budget, and enables the cloud physical properties to be tied to the cloud broadband radiative properties in a consistent manner.  This initial estimate of cloud properties is modified in Subsystem 5 to obtain consistency in cloud properties and Top-of-the-Atmosphere (TOA) broadband radiative fluxes.

The major objectives of this Subsystem include:

- Locate imager pixels within a CERES footprint by calculating the value of the Point Spread Function (PSF) for each pixel with respect to the centroid of the CERES field of view (FOV).  If the PSF value exceeds a specified threshold value, the pixel is included in the footprint.

Accumulate statistics of cloud properties for all imager pixels within the CERES footprint and write the footprint records to the intermediate Single Scanner Footprint TOA and Surface Fluxes Clouds (SSF) output file.

Write diagnostic and statistical information from each run to the Quality Control (QC) report files.

The primary input data sets for the Convolution Subsystem are:

- The CERES Instrument Earth Scans (IES) data product contains time of observation, geolocation data, and filtered radiances for each footprint in spatial order.  The CERES footprint effective diameter is 10 km for Tropical Rainfall Measuring Mission (TRMM) spacecraft and 20 km for EOS AM and PM spacecraft.  IES file from both TRMM and Terra are used as the test data sets for Release 3.

The cloud imager data from Advanced Very High Resolution Radiometer (AVHRR), Visible Infrared Scanner (VIRS), Moderate-Resolution Imaging Spectroradiometer (MODIS), or Visible Infrared Imaging Radiometer Suite (VIIRS) are processed by Subsystems 4.1 - 4.3 and passed to convolution via the Imager Pixel Data file, commonly designated “Cookiedough.”  This file represents a two-dimensional array (N scanlines by M pixels per scanline) with a data structure associated with each pixel containing pixel location, viewing geometry, observation time, multispectral radiance data, scene type, and cloud properties as determined in Subsystems 4.1 through 4.3.

The output science product is the intermediate SSF product (SSFI).  The intermediate SSF is subsequently processed and completed by Subsystem 4.5-4.6, and the resulting final SSF is an hourly CERES archival product that contains footprint geometry, radiance information, and the statistics for full footprint, clear footprint, cloudy footprint and overlap footprint areas.  The secondary output products are the quality control reports.  The quality control reports contain processing information, informative messages, and statistics.  In Release 3, Subsystem 4.4 creates both a formatted (ASCII) report file (FQC) and a binary report file (FQCI) which is intended to be postprocessed by one or more of a variety of flexible programs for browsing, display, or data extraction.

### CER4.1-4.2P1 - Daily QC Processor

The Daily QC processor reads all available gridded and binned QC files for a given day and generates the respective daily averaged QC files.

The primary input data sets for the PGE are:

EQCHG:	Contains gridded quality control information in a binary format for an hour.

EQCHB:	Contains binned quality control information in a binary format for an hour.

The output science products are a new clear-sky reflectance map for the next day, a daily gridded quality control report, and a daily binned quality control report.

### CER4.1-4.2P2 - Daily CRH Processor

The Daily CRH processor reads all available CRH_Update files for a given day and generates an updated CRH file for the next day’s processing.

The primary input data sets for the PGE are:

ECRHU:	Contains CRH values for all clear pixels in an hour.

The output science products are a new clear-sky reflectance map for the next day.

### CER4.1-4.2P3 - Daily QC Processor

The Daily QC processor reads all available gridded and binned QC files for a given day and generates the respective daily averaged QC files.

The primary input data sets for the PGE are:

EQCHG:	Contains gridded quality control information in a binary format for an hour.

EQCHB:	Contains binned quality control information in a binary format for an hour.

The output science products are a new clear-sky reflectance map for the next day, a daily gridded quality control report, and a daily binned quality control report.

### CER4.1-4.2P4 - Daily QC Processor

The Daily QC processor reads all available gridded and binned QC files for a given day and generates the respective daily averaged QC files.

The primary input data sets for the PGE are:

EQCHG:	Contains gridded quality control information in a binary format for an hour.

EQCHB:	Contains binned quality control information in a binary format for an hour.

The output science products are a new clear-sky reflectance map for the next day, a daily gridded quality control report, and a daily binned quality control report.

### CER4.1-4.2P5 - Daily CRH Processor

The Daily CRH processor reads all available CRH_Update files for a given day and generates an updated CRH file for the next day’s processing.

The primary input data sets for the PGE are:

ECRHU:	Contains CRH values for all clear pixels in an hour.

The output science products are a new clear-sky reflectance map for the next day.

### CER4.1-4.2P6 - Daily QC Processor

The Daily QC processor reads all available gridded and binned QC files for a given day and generates the respective daily averaged QC files.

The primary input data sets for the PGE are:

EQCHG:	Contains gridded quality control information in a binary format for an hour.

EQCHB:	Contains binned quality control information in a binary format for an hour.

The output science products are a new clear-sky reflectance map for the next day, a daily gridded quality control report, and a daily binned quality control report.

### CER4.1-4.2P7 - Daily CRH Processor

The Daily CRH processor reads all available CRH_Update files for a given day and generates an updated CRH file for the next day’s processing.

The primary input data sets for the PGE are:

ECRHU:	Contains CRH values for all clear pixels in an hour.

The output science products are a new clear-sky reflectance map for the next day.

### CER4.1-4.3P1 - Monthly QC Processor

The Monthly QC Processor reads all available binned and gridded QC for a given day and generates the respective monthly averaged QC files.

The primary input data sets for the Monthly QC Processor are:

EQCDG:	The daily gridded QC file produced by CER4.1-4.2P1.

EQCDB:	The daily binned QC file produced by CER4.1-4.2P1.

Note:  A file listing of expected output for each PGE can be found in the following directory:

$CERESHOME/clouds/data/out_comp/

### CER4.1-4.3P2 - Monthly QC Processor

The Monthly QC Processor reads all available binned and gridded QC for a given day and generates the respective monthly averaged QC files.

The primary input data sets for the Monthly QC Processor are:

EQCDG:	The daily gridded QC file produced by CER4.1-4.2P3.

EQCDB:	The daily binned QC file produced by CER4.1-4.2P3.

Note: A file listing of expected output for each PGE can be found in the following directory:

$CERESHOME/clouds/data/out_comp/

### CER4.1-4.3P3 - Monthly QC Processor

The Monthly QC Processor reads all available binned and gridded QC for a given day and generates the respective monthly averaged QC files.

The primary input data sets for the Monthly QC Processor are:

EQCDG:	The daily gridded QC file produced by CER4.1-4.2P4.

EQCDB:	The daily binned QC file produced by CER4.1-4.2P4.

Note: A file listing of expected output for each PGE can be found in the following directory:

$CERESHOME/clouds/data_exp

### CER4.1-4.3P4 - Monthly QC Processor

The Monthly QC Processor reads all available binned and gridded QC for a given day and generates the respective monthly averaged QC files.

The primary input data sets for the Monthly QC Processor are:

EQCDG:	The daily gridded QC file produced by CER4.1-4.2P6.

EQCDB:	The daily binned QC file produced by CER4.1-4.2P6.

Note: A file listing of expected output for each PGE can be found in the following directory:

$CERESHOME/clouds/data_exp

# Software and Data File Installation Procedures

This section describes how to install the Subsystems 4.1 through 4.4 Cloud Retrieval and Convolution software in preparation for making the necessary test runs at the Langley Atmospheric Science Data Center (ASDC).  The installation procedures include instructions for uncompressing and untarring the delivered tar files, properly defining environmental variables, and compiling the Cloud Retrieval and Convolution programs.

## Installation

Software/Data File Install Procedure:

- All Software Installation and Test Procedures must be run from a t-shell (tcsh).  Running otherwise could potentially produce bizarre results.

The scripts, makefiles, and Process Control Files in the Subsystems 4.1 through 4.4 delivery package expect the CERES environment variable, $CERESENV, to point to a file which sets the following environment variables:

CPUTYPE	-	Host machine type (ppc64 or x86 64)

PGSDIR	-	Directory for Toolkit libraries

F90	-	Pointer to the SGI F90 64 bit compiler

InputArchive	-	Top Directory of Archived input files

InputArchiveSS	-	Top Directory of input/output files from current subsystem

InputArchiveInt	-	Top Directory of input files from another subsystem

CERESHOME	-	Top Directory for CERES Software

MOA_Dir	-	Top Directory of input MOA files

PGSMSG	-	Directory which contains Toolkit and CERES Status Message Files

PGSLIB 	-	Directory which contains SGI 64-bit Toolkit library file

F90COMP 	-	SGI F90 compiler options

FCOMP	-	SGI F90 compiler options for f77

CFLAGS	-	SGI C compiler options

PGSINC	-	Pointer to the PGS include file directory

HDFDIR	-	Pointer to the HDF home directory

HDFINC	-	Pointer to the HDF include files

HDFEOSDIR	-	Pointer to the HDFEOS Directory

HDFEOSLIB	-	Pointer to the HDFEOS Library

Failing definition of $CERESENV, subsystem analysts source /CERES/lib/sgi_lib/ceres-env.csh on thunder/lightning or /ENG/CERES/lib/ceres-env.csh on warlock in their login scripts.

Change directory to the directory where you plan to install the Cloud Retrieval and Convolution Subsystems.  (The following instructions assume that the directory will be $CERESHOME.)

cd $CERESHOME

Uncompress and untar all delivered tar files.

The uncompressed files take up almost 4 Gbytes of disk space.  Please allow for sufficient space to accommodate them.  Certain input files are output from other Subsystems (SS1 and SS12).  These include the IES, MOA, and attitude and ephemeris files.  For convenience, these files were placed in the appropriate instrument and sarb directories and included in the tar files from those directories.  You must have write permission to the instrument and sarb partitions when untarring the files.

## Compilation

To create the required Product Generation System (PGS) include and message files for Subsystems 4.1 - 4.4 it will be necessary to execute the smfcompile utility on the files CERES_25450.t, CERES_25460.t, and FOOTPRINT_25500.t:

cd $CERESHOME/clouds/smf

$CERESLIB/bin/smfcompile_all.csh

Below are the instructions to compile the source code for each PGE as well as any necessary libraries.

### Compiling PGE CER4.1-4.0P1

A single make script to compile all libraries and executables covered by this Test Plan is provided in the directory $CERESHOME/clouds/src.  To run the make script, execute the following sequence of commands:

cd $CERESHOME/clouds/src

source $CERESHOME/clouds/bin/CER4.1-4.env 2

$CERESHOME/clouds/src/makeall CER4.1-4.0P1

Execution of the make script is indicated by a scrolling list of those libraries and executables currently being compiled.  Warning messages are allowed.  Successful compilation is indicated by:

************************

* Compilation Successful *

************************

Anything else indicates failure.

### Compiling PGE CER4.1-4.0P2

A single make script to compile all libraries and executables covered by this Test Plan is provided in the directory $CERESHOME/clouds/src.  To run the make script, execute the following sequence of commands:

cd $CERESHOME/clouds/CER4.1-4.0P2/src

source $CERESHOME/clouds/CER4.1-4.0P2/rcf/CER4.1-4.0P2.env 2

$CERESHOME/clouds/CER4.1-4.0P2/lib/makeall clean

$CERESHOME/clouds/CER4.1-4.0P2/lib/makeall

$CERESHOME/clouds/CER4.1-4.0P2/src/makeall clean

$CERESHOME/clouds/CER4.1-4.0P2/src/makeall

Execution of the make script is indicated by a scrolling list of those libraries and executables currently being compiled.  Warning messages are allowed.  Successful compilation is indicated by:

************************

* Compilation Successful *

************************

Anything else indicates failure.

The following executables should be created in the $CERESHOME/clouds/CER4.1-4.0P2/bin directory:

CER4.1-4.0P2.SnowIce_$CPUTYPE.exe

### Compiling PGE CER4.1-4.0P3

A single make script to compile all libraries and executables covered by this Test Plan is provided in the directory $CERESHOME/clouds/src.  To run the make script, execute the following sequence of commands:

cd $CERESHOME/clouds/CER4.1-4.0P3/src

source $CERESHOME/clouds/CER4.1-4.0P3/rcf/CER4.1-4.0P3.env

$CERESHOME/clouds/CER4.1-4.0P3/lib/makeall

$CERESHOME/clouds/CER4.1-4.0P3/src/makeall

Execution of the make script is indicated by a scrolling list of those libraries and executables currently being compiled.  Warning messages are allowed.  Successful compilation is indicated by:

************************

* Compilation Successful *

************************

Anything else indicates failure.

The following executables should be created in the $CERESHOME/clouds/CER4.1-4.0P3/bin directory:

CER4.1-4.0P3.SnowIce_$CPUTYPE.exe

### Compiling PGE CER4.1-4.1P1, CER4.1-4.1P2, CER4.1-4.1P3

A single make script to compile all libraries and executables covered by this Test Plan is provided in the directory $CERESHOME/clouds/src.  To run the make script, execute the following sequence of commands for the appropriate PGE:

For TRMM processing, CER4.1-4.1P1, execute the following commands:

cd $CERESHOME/clouds/src

source $CERESHOME/clouds/bin/CER4.1-4.env 2

$CERESHOME/clouds/src/makeall libraries

$CERESHOME/clouds/src/makeall CER4.1-4.1P1

For Terra processing, CER4.1-4.1P2, execute the following commands:

cd $CERESHOME/clouds/src

source $CERESHOME/clouds/bin/CER4.1-4.env 3

$CERESHOME/clouds/src/makeall libraries

$CERESHOME/clouds/src/makeall CER4.1-4.1P2

For Aqua processing, CER4.1-4.1P3, execute the following commands:

cd $CERESHOME/clouds/src

source $CERESHOME/clouds/bin/CER4.1-4.env 6

$CERESHOME/clouds/src/makeall libraries

$CERESHOME/clouds/src/makeall CER4.1-4.1P3

Execution of the make script is indicated by a scrolling list of those libraries and executables currently being compiled.  Warning messages are allowed.  Successful compilation is indicated by:

************************

* Compilation Successful *

************************

Anything else indicates failure.

### Compiling PGE CER4.1-4.1P4, CER4.1-4.1P5

A single make script to compile all libraries and executables covered by this Test Plan is provided in the directory $CERESHOME/clouds/src.  To run the make script, execute the following sequence of commands for the appropriate PGE:

For Terra Collection 005 processing, CER4.1-4.1P4, execute the following commands:

cd $CERESHOME/clouds/CER4.1-4.1P4/rcf

source CER4.1-4.env

$CERESHOME/clouds/CER4.1-4.1P4/lib/makeall

$CERESHOME/clouds/CER4.1-4.1P4/src/makeall

The following static library files should be created in the $CERESHOME/clouds/CER4.1-4.1P4/lib/lib directory:

libCloudsCommon_$CPUTYPE.a

libCloudsHDF_$CPUTYPE.a

libModisAerosolL2_$CPUTYPE.a

libModisGeoL1B_$CPUTYPE.a

libModisRadExtendL1B_$CPUTYPE.a

libModisRadSSL1B_$CPUTYPE.a

libModisRetrL2_$CPUTYPE.a

libavhrr_$CPUTYPE.a

libvint_$CPUTYPE.a

libvirs_$CPUTYPE.a

libwelch_$CPUTYPE.a

The following executables should be created in the $CERESHOME/clouds/CER4.1-4.1P4/bin directory:

CER4.1-4.1P4.footprint_$CPUTYPE.exe

CER4.1-4.1P4.retrieval_$CPUTYPE.exe

The following executables should be created in the $CERESHOME/clouds/CER4.1-4.1P4/test_suites/bin/footprint directory:

SSFA_Compare_$CPUTYPE.exe

SSF_Compare_$CPUTYPE.exe

For Aqua Collection 005 processing, CER4.1-4.1P5, execute the following commands:

cd $CERESHOME/clouds/CER4.1-4.1P5/rcf

source CER4.1-4.env

$CERESHOME/clouds/CER4.1-4.1P5/lib/makeall

$CERESHOME/clouds/CER4.1-4.1P5/src/makeall

The following static library files should be created in the $CERESHOME/clouds/CER4.1-4.1P5/lib/lib directory:

libCloudsCommon_$CPUTYPE.a

libCloudsHDF_$CPUTYPE.a

libModisAerosolL2_$CPUTYPE.a

libModisGeoL1B_$CPUTYPE.a

libModisRadExtendL1B_$CPUTYPE.a

libModisRadSSL1B_$CPUTYPE.a

libModisRetrL2_$CPUTYPE.a

libavhrr_$CPUTYPE.a

libvint_$CPUTYPE.a

libvirs_$CPUTYPE.a

libwelch_$CPUTYPE.a

The following executables should be created in the $CERESHOME/clouds/CER4.1-4.1P5/bin directory:

CER4.1-4.1P5.footprint_$CPUTYPE.exe

CER4.1-4.1P5.retrieval_$CPUTYPE.exe

The following executables should be created in the $CERESHOME/clouds/CER4.1-4.1P5/test_suites/bin/footprint directory:

SSFA_Compare_$CPUTYPE.exe

SSF_Compare_$CPUTYPE.exe

Execution of the make script is indicated by a scrolling list of those libraries and executables currently being compiled.  Warning messages are allowed.  Successful compilation is indicated by:

************************

* Compilation Successful *

************************

Anything else indicates failure.

### Compiling PGE CER4.1-4.1P6

A single make script to compile all libraries and executables covered by this Test Plan is provided in the directory $CERESHOME/clouds/src.  To run the make script, execute the following sequence of commands for the appropriate PGE on an x86 machine:

cd $CERESHOME/clouds/CER4.1-4.1P6/rcf

source CER4.1-4.env 6

$CERESHOME/clouds/CER4.1-4.1P6/lib/makeall

$CERESHOME/clouds/CER4.1-4.1P6/src/makeall

Execution of the make script is indicated by a scrolling list of those libraries and executables currently being compiled.  Warning messages are allowed.

If successful, the following libraries should be created in the $CERESHOME/clouds/CER4.1-4.1P6/lib/lib directory:

libavhrr_x86_64.a

libCloudsCommon_x86_64.a

libCloudsHDF_x86_64.a

libCloudsNetCDF_x86_64.a

libco2_x86_64.a

libmcrs_x86_64.a

libModisGeoL1B_x86_64.a

libModisRadExtendL1B_x86_64.a

libModisRadSSL1B_x86_64.a

libModisAerosolL2_x86_64.a

libvint_x86_64.a

libvirs_x86_64.a

libwelch_x86_64.a

And the following executables should be created in the $CERESHOME/clouds/CER4.1-4.1P6/bin directory:

CER4.1-4.1P6.footprint_x86_64.exe

CER4.1-4.1P6.retrieval_x86_64.exe

### Compiling PGE CER4.1-4.1P7

A single make script to compile all libraries and executables covered by this Test Plan is provided in the directory $CERESHOME/clouds/src.  To run the make script, execute the following sequence of commands for the appropriate PGE:

cd $CERESHOME/clouds/CER4.1-4.1P7/rcf

source CER4.1-4.env

$CERESHOME/clouds/CER4.1-4.1P7/lib/makeall

$CERESHOME/clouds/CER4.1-4.1P7/src/makeall

Execution of the make script is indicated by a scrolling list of those libraries and executables currently being compiled.  Warning messages are allowed.  Successful compilation is indicated by:

************************

* Compilation Successful *

************************

Anything else indicates failure.

The following executables should be created in the $CERESHOME/clouds/CER4.1-4.1P7/bin directory:

CER4.1-4.1P7.footprint_$CPUTYPE.exe

CER4.1-4.1P7.retrieval_$CPUTYPE.exe

### Compiling PGE CER4.1-4.2P1

A single make script to compile all libraries and executables covered by this Test Plan is provided in the directory $CERESHOME/clouds/src.  To run the make script, execute the following sequence of commands:

cd $CERESHOME/clouds/src

source $CERESHOME/clouds/bin/CER4.1-4.env 6

$CERESHOME/clouds/src/makeall CER4.1-4.2P1

Execution of the make script is indicated by a scrolling list of those libraries and executables currently being compiled.  Warning messages are allowed.  Successful compilation is indicated by:

************************

* Compilation Successful *

************************

Anything else indicates failure.

### Compiling PGE CER4.1-4.2P2

A single make script to compile all libraries and executables covered by this Test Plan is provided in the directory $CERESHOME/clouds/src.  To run the make script, execute the following sequence of commands:

cd $CERESHOME/clouds/CER4.1-4.2P2/rcf

source CER4.1-4.env 6

$CERESHOME/clouds/CER4.1-4.1P5/lib/makeall

$CERESHOME/clouds/CER4.1-4.2P2/src/makeall

Execution of the make script is indicated by a scrolling list of those libraries and executables currently being compiled.  Warning messages are allowed.  Successful compilation is indicated by:

************************

* Compilation Successful *

************************

Anything else indicates failure.

The following executables should be created in the $CERESHOME/clouds/CER4.1-4.2P2/bin directory:

CER4.1-4.2P2.UpdateCRH0063_$CPUTYPE.exe

CER4.1-4.2P2.UpdateCRH0160_$CPUTYPE.exe

CER4.1-4.2P2.UpdateCRH0213_$CPUTYPE.exe

### Compiling PGE CER4.1-4.2P3

A single make script to compile all libraries and executables covered by this Test Plan is provided in the directory $CERESHOME/clouds/src.  To run the make script, execute the following sequence of commands:

cd $CERESHOME/clouds/CER4.1-4.2P3/rcf

source CER4.1-4.env 6

$CERESHOME/clouds/CER4.1-4.1P5/lib/makeall

$CERESHOME/clouds/CER4.1-4.2P3/src/makeall

Execution of the make script is indicated by a scrolling list of those libraries and executables currently being compiled.  Warning messages are allowed.  Successful compilation is indicated by:

************************

* Compilation Successful *

************************

Anything else indicates failure.

The following executables should be created in the $CERESHOME/clouds/CER4.1-4.2P3/bin directory:

CER4.1-4.2P3.DailyBinned_$CPUTYPE.exe

CER4.1-4.2P3.ReadQC_$CPUTYPE.exe

CER4.1-4.2P3.UpdateQC_$CPUTYPE.exe

### Compiling PGE CER4.1-4.2P4

A single make script to compile all libraries and executables covered by this Test Plan is provided in the directory $CERESHOME/clouds/src.  To run the make script, execute the following sequence of commands on an x86 machine:

cd $CERESHOME/clouds/CER4.1-4.2P4/rcf

source CER4.1-4.env 6

$CERESHOME/clouds/CER4.1-4.1P6/lib/makeall (if libraries not already made)

$CERESHOME/clouds/CER4.1-4.2P4/src/makeall

Execution of the make script is indicated by a scrolling list of those libraries and executables currently being compiled.  Warning messages are allowed.

If successful, the following executables should be created in the $CERESHOME/clouds/CER4.1-4.2P4/bin directory:

CER4.1-4.2P4.DailyBinned_x86_64.exe

CER4.1-4.2P4.UpdateQC_x86_64.exe

### Compiling PGE CER4.1-4.2P5

A single make script to compile all libraries and executables covered by this Test Plan is provided in the directory $CERESHOME/clouds/src.  To run the make script, execute the following sequence of commands on an x86 machine:

cd $CERESHOME/clouds/CER4.1-4.2P5/rcf

source CER4.1-4.env 6

$CERESHOME/clouds/CER4.1-4.1P6/lib/makeall (if libraries not already made)

$CERESHOME/clouds/CER4.1-4.2P5/src/makeall

Execution of the make script is indicated by a scrolling list of those libraries and executables currently being compiled.  Warning messages are allowed

If successful, the following executables should be created in the $CERESHOME/clouds/CER4.1-4.2P5/bin directory:

CER4.1-4.2P5.UpdateCRH0063SF_x86_64.exe

CER4.1-4.2P5.UpdateCRH0063SFSC_x86_64.exe

CER4.1-4.2P5.UpdateCRH0160SF_x86_64.exe

CER4.1-4.2P5.UpdateCRH0213SF_x86_64.exe

CER4.1-4.2P5.UpdateCRH0124SC_x86_64.exe

CER4.1-4.2P5.UpdateCRH0124SF_x86_64.exe

### Compiling PGE CER4.1-4.2P6

A single make script to compile all libraries and executables covered by this Test Plan is provided in the directory $CERESHOME/clouds/src.  To run the make script, execute the following sequence of commands:

cd $CERESHOME/clouds/CER4.1-4.2P6/rcf

source CER4.1-4.env

$CERESHOME/clouds/CER4.1-4.1P7/lib/makeall

$CERESHOME/clouds/CER4.1-4.2P6/src/makeall

Execution of the make script is indicated by a scrolling list of those libraries and executables currently being compiled.  Warning messages are allowed.  Successful compilation is indicated by:

************************

* Compilation Successful *

************************

Anything else indicates failure.

The following executables should be created in the $CERESHOME/clouds/CER4.1-4.2P6/bin directory:

CER4.1-4.2P6.DailyBinned_$CPUTYPE.exe

CER4.1-4.2P6.ReadQC_$CPUTYPE.exe

CER4.1-4.2P6.UpdateQC_$CPUTYPE.exe

### Compiling PGE CER4.1-4.2P7

A single make script to compile all libraries and executables covered by this Test Plan is provided in the directory $CERESHOME/clouds/src.  To run the make script, execute the following sequence of commands:

cd $CERESHOME/clouds/CER4.1-4.2P7/rcf

source CER4.1-4.env

$CERESHOME/clouds/CER4.1-4.1P7/lib/makeall

$CERESHOME/clouds/CER4.1-4.2P7/src/makeall

Execution of the make script is indicated by a scrolling list of those libraries and executables currently being compiled.  Warning messages are allowed.  Successful compilation is indicated by:

************************

* Compilation Successful *

************************

Anything else indicates failure.

The following executables should be created in the $CERESHOME/clouds/CER4.1-4.2P7/bin directory:

CER4.1-4.2P7.UpdateCRH0063SF_$CPUTYPE.exe

CER4.1-4.2P7.UpdateCRH0063SFSC_$CPUTYPE.exe

CER4.1-4.2P7.UpdateCRH0160SF_$CPUTYPE.exe

CER4.1-4.2P7.UpdateCRH0160SC_$CPUTYPE.exe

CER4.1-4.2P7.UpdateCRH0213SF_$CPUTYPE.exe

CER4.1-4.2P7.UpdateCRH0124SC_$CPUTYPE.exe

CER4.1-4.2P7.UpdateCRH0124SF_$CPUTYPE.exe

### Compiling PGE CER4.1-4.3P1

A single make script to compile all libraries and executables covered by this Test Plan is provided in the directory $CERESHOME/clouds/src.  To run the make script, execute the following sequence of commands:

cd $CERESHOME/clouds/src

source $CERESHOME/clouds/bin/CER4.1-4.env 6

$CERESHOME/clouds/src/makeall CER4.1-4.3P1

Execution of the make script is indicated by a scrolling list of those libraries and executables currently being compiled.  Warning messages are allowed.  Successful compilation is indicated by:

************************

* Compilation Successful *

************************

Anything else indicates failure.

### Compiling PGE CER4.1-4.3P2

A single make script to compile all libraries and executables covered by this Test Plan is provided in the directory $CERESHOME/clouds/src.  To run the make script, execute the following sequence of commands:

cd $CERESHOME/clouds/CER4.1-4.3P2/rcf

source CER4.1-4.env 6

$CERESHOME/clouds/CER4.1-4.1P5/lib/makeall

$CERESHOME/clouds/CER4.1-4.3P2/src/makeall

Execution of the make script is indicated by a scrolling list of those libraries and executables currently being compiled.  Warning messages are allowed.  Successful compilation is indicated by:

************************

* Compilation Successful *

************************

Anything else indicates failure.

The following executables should be created in the $CERESHOME/clouds/CER4.1-4.3P2/bin directory:

CER4.1-4.3P2.ProduceMonthlyQC_$CPUTYPE.exe

### Compiling PGE CER4.1-4.3P3

A single make script to compile all libraries and executables covered by this Test Plan is provided in the directory $CERESHOME/clouds/src.  To run the make script, execute the following sequence of commands on an x86 machine:

cd $CERESHOME/clouds/CER4.1-4.3P3/rcf

source CER4.1-4.env 6

$CERESHOME/clouds/CER4.1-4.1P6/lib/makeall (if libraries not already made)

$CERESHOME/clouds/CER4.1-4.3P3/src/makeall

Execution of the make script is indicated by a scrolling list of those libraries and executables currently being compiled.  Warning messages are allowed.

If successful, the following executable should be created in the $CERESHOME/clouds/CER4.1-4.3P3/bin directory:

CER4.1-4.3P3.ProduceMonthlyQC_x86_64.exe

### Compiling PGE CER4.1-4.3P4

A single make script to compile all libraries and executables covered by this Test Plan is provided in the directory $CERESHOME/clouds/src.  To run the make script, execute the following sequence of commands:

cd $CERESHOME/clouds/CER4.1-4.3P4/rcf

source CER4.1-4.env

$CERESHOME/clouds/CER4.1-4.1P7/lib/makeall

$CERESHOME/clouds/CER4.1-4.3P4/src/makeall

Execution of the make script is indicated by a scrolling list of those libraries and executables currently being compiled.  Warning messages are allowed.  Successful compilation is indicated by:

************************

* Compilation Successful *

************************

Anything else indicates failure.

The following executables should be created in the $CERESHOME/clouds/CER4.1-4.3P4/bin directory:

CER4.1-4.3P4.ProduceMonthlyQC_$CPUTYPE.exe

# Test and Evaluation Procedures - CER4.1-4.0P1 Snow and Ice Processor

This section provides information on how to execute PGE CER4.1-4.0P1.  It also provides an overview of the test and evaluation procedures.  It includes a description of what is being tested and the order in which the tests should be performed.

## Stand Alone Test Procedures

### Execution

#### NSIDC Snow and Ice Data

The following command will copy the necessary input files for running this PGE.  This command only needs to be executed if the input files have not been copied to the appropriate directories already.  Copy the input files to appropriate locations using the following script:

$CERESHOME/clouds/test_suites/scripts/Copy_input.csh

The PGE can be executed with the following sequence of commands listed below.  This sequence of commands covers PCF generation as well as execution of the PGE.

source $CERESHOME/clouds/bin/CER4.1-4.env 3

$CERESHOME/clouds/bin/CER4.1-4.0P1.PCFGen 2001 06 14

$CERESHOME/clouds/bin/Run.CER4.1-4.0P1 $CERESHOME/clouds/rcf/CER4.1-4.0P1_PCF_CERES_NSIDCNESDIS_000000.20010614

Note:  A file listing of expected output for each PGE can be found in the following file:

$CERESHOME/clouds/data/out_exp/out_description.txt

### Exit Codes

All CER4.1-4.0P1 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.

### Snow and Ice Processor Test Summary

| PGE Number | PGE Name | Run Time (mm:ss) | Disk Storage (MB) | Memory (MB) |
| --- | --- | --- | --- | --- |
| CER4.1-4.0P1 | Snow and Ice Processor | 00:03 | 05 | 65 |

## Evaluation Procedures

The Test Evaluation procedures must be run on the same day that the Test is run.  If unable to run the Evaluation procedures at that time, contact the analyst for a work around.

The following will remove the Instrument and MOA input data files that were used for testing.  This step is done when all testing is complete.  If you are testing another PGE, then it is not necessary to do this step.

$CERESHOME/clouds/test_suites/scripts/Remove_input.csh

### Log and Status File Results

The Log and Status files are created by the Toolkit and are located in the directory $CERESHOME/clouds/data/runlogs after the PGE has been executed.  The comparisons of the Log and status files with their expected outputs are handled in Section 3.2.3.

### Metadata Evaluation

Metadata files for this PGE are created at runtime and are located with their corresponding output files.  The comparisons of the metadata files with their expected results are handled in Section 3.2.3.

### Execution of Comparison Software

The evaluation software for this Subsystem will compare the ASDC generated output with the expected output included with this delivery package.  To run the comparison software, execute the following command:

source $CERESHOME/clouds/bin/CER4.1-4.env 3

$CERESHOME/clouds/test_suites/bin/CER4.1-4.Validate CER4.1-4.0P1

### Evaluation of Comparison Software Output

See Appendix D for a description of the output from the Comparison Software.

## Solutions to Possible Problems

- Output files are opened with Status = NEW.  If any of these files exist when the generating PGE is executed, the PGE will fail.  These files must be removed before any attempt is made to re-run any of the PGEs after the initial run is made.  The Toolkit Log files also need to be deleted before each run to be consistent with the expected output.  The specific problems can generally be found in the LogReport and/or LogStatus files.  NOTE:  For testing purposes only, if the test case must be re-run, you must first cleanup the PCF file generated from a previous run as shown below.

$CERESHOME/clouds/bin/Run.CER4.1-4.Cleanup $CERESHOME/clouds/rcf/CER4.1-4.0P1_PCF_CERES_NSIDCNESDIS_000000.20010614

Please contact Subsystem Lead for assistance if the cleanup and test case re-run are unsuccessful.

Many problems encountered during compilation, linking, and execution are due to incorrect environment configuration.  Generally, these problems make themselves readily apparent via compiler errors or termination of the program during the initialization stage during the first few seconds of execution.

# Test and Evaluation Procedures - CER4.1-4.0P2 Snow and Ice Processor

This section provides information on how to execute PGE CER4.1-4.0P2.  It also provides an overview of the test and evaluation procedures.  It includes a description of what is being tested and the order in which the tests should be performed.

## Stand Alone Test Procedures

### Execution

For 8th MESH NESDIS testing:

Command Line Instructions:

unlimit

cd $CERESHOME/clouds/CER4.1-4.0P2/rcf

source CER4.1-4.0P2.env 1 1

Run.CER4.1-4.Cleanup.pl 20080617

CER4.1-4.PCFGen.pl 2008 06 17

CER4.1-4.0P2.PCFcheck.pl pcf/CER4.1-4.0P2_PCF_$SS4_0\_$PS4_0\_$CC4_0P1.20080617

If errors in PCF, correct problems and start over.

If no errors in PCF:

Run.CER4.1-4.0P2.pl pcf/CER4.1-4.0P2_PCF_$SS4_0\_$PS4_0\_$CC4_0P1.20080617

SGE Test Instructions:

cd $CERESHOME/clouds/CER4.1-4.0P2/rcf/

source CER4.1-4.0P2.env 1 1

Run.CER4.1-4.Cleanup.pl 20080617

CER4.1-4.0P2-SGE_Driver.pl -date 20080617

The submitted job can be monitored with the qstat command.

Job submission status and job progress file can be found in the file:

$CERESHOME/clouds/CER4.1-4.0P2/rcf/pcf/summary/CER4.1-4.0P2_$SS4_0\_$PS4_0\_$CC4_0P1.20080617.summary

For 8th MESH CLASS testing:

Command Line Instructions :

unlimit

cd $CERESHOME/clouds/CER4.1-4.0P2/rcf

source CER4.1-4.0P2.env 1 2

Run.CER4.1-4.Cleanup.pl 20121211

CER4.1-4.PCFGen.pl 2012 12 11

CER4.1-4.0P2.PCFcheck.pl pcf/CER4.1-4.0P2_PCF_$SS4_0\_$PS4_0\_$CC4_0P1.20121211

If errors in PCF, correct problems and start over.

If no errors in PCF:

Run.CER4.1-4.0P2.pl pcf/CER4.1-4.0P2_PCF_$SS4_0\_$PS4_0\_$CC4_0P1.20121211

SGE Test Instructions:

cd $CERESHOME/clouds/CER4.1-4.0P2/rcf/

source CER4.1-4.0P2.env 1 2

Run.CER4.1-4.Cleanup.pl 20121211

CER4.1-4.0P2-SGE_Driver.pl -date 20121211

The submitted job can be monitored with the qstat command.

Job submission status and job progress file can be found in the file:

$CERESHOME/clouds/CER4.1-4.0P2/rcf/pcf/summary/CER4.1-4.0P2_$SS4_0\_$PS4_0\_$CC4_0P1.20111231.summary

For 16th NESDIS MESH:

Command Line Instructions :

unlimit

cd $CERESHOME/clouds/CER4.1-4.0P2/rcf

source CER4.1-4.0P2.env 2

Run.CER4.1-4.Cleanup.pl 20090905

CER4.1-4.PCFGen.pl 2009 09 05

CER4.1-4.0P2.PCFcheck.pl pcf/CER4.1-4.0P2_PCF_$SS4_0\_$PS4_0\_$CC4_0P1.20090905

If errors in PCF, correct problems and start over.

If no errors in PCF:

Run.CER4.1-4.0P2.pl pcf/CER4.1-4.0P2_PCF_$SS4_0\_$PS4_0\_$CC4_0P1.20090905

SGE Test Instructions:

cd $CERESHOME/clouds/CER4.1-4.0P2/rcf/

source CER4.1-4.0P2.env 2

Run.CER4.1-4.Cleanup.pl 20090905

CER4.1-4.0P2-SGE_Driver.pl -date 20090905

The submitted job can be monitored with the qstat command.

Job submission status and job progress file can be found in the file:

$CERESHOME/clouds/CER4.1-4.0P2/rcf/pcf/summary/CER4.1-4.0P2_$SS4_0\_$PS4_0\_$CC4_0P1.20090905.summary

Note:  A file listing of expected output for each PGE can be found in the following file:

$CERESHOME/clouds/data_exp/out_description1.txt

### Exit Codes

All CER4.1-4.0P2 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.

### Snow and Ice Processor Test Summary

| PGE Number | PGE Name | Run Time (mm:ss) | Disk Storage (MB) | Memory (MB) |
| --- | --- | --- | --- | --- |
| CER4.1-4.0P2 | Snow and Ice Processor | 00:03 | 05 | 65 |

## Evaluation Procedures

### Log and Status File Results

The Log and Status files are created by the Toolkit and are located in the directory $CERESHOME/clouds/runlogs after the PGE has been executed.  The comparisons of the Log and status files with their expected outputs are handled in Section 4.2.3.

### Metadata Evaluation

Metadata files for this PGE are created at runtime and are located with their corresponding output files.  The comparisons of the metadata files with their expected results are handled in Section 4.2.3.

### Execution of Comparison Software

The evaluation software for this Subsystem will compare the ASDC generated output with the expected output included with this delivery package.  To run the comparison software, execute the following command:

For 8th MESH NESDIS cases:

source $CERESHOME/clouds/CER4.1-4.0P2/rcf/CER4.1-4.0P2.env 1 1

$CERESHOME/clouds/test_suites/bin/CER4.1-4.Validate.pl CER4.1-4.0P2

For 8th MESH CLASS cases:

source $CERESHOME/clouds/CER4.1-4.0P2/rcf/CER4.1-4.0P2.env 1 2

$CERESHOME/clouds/test_suites/bin/CER4.1-4.Validate.pl CER4.1-4.0P2

For 16th MESH cases:

source $CERESHOME/clouds/CER4.1-4.0P2/rcf/CER4.1-4.0P2.env 2

$CERESHOME/clouds/test_suites/bin/CER4.1-4.Validate.pl CER4.1-4.0P2

### Evaluation of Comparison Software Output

See Appendix D for a description of the output from the Comparison Software.

## Solutions to Possible Problems

- Output files are opened with Status = NEW.  If any of these files exist when the generating PGE is executed, the PGE will fail.  These files must be removed before any attempt is made to re-run any of the PGEs after the initial run is made.  The Toolkit Log files also need to be deleted before each run to be consistent with the expected output.  The specific problems can generally be found in the LogReport and/or LogStatus files.  NOTE:  For testing purposes only, if the test case must be re-run, you must first cleanup the PCF file generated from a previous run as shown below.

For 8th MESH NESDIS cases:

source $CERESHOME/clouds/ CER4.1-4.0P2/rcf /CER4.1-4.0P2.env 1 1

$CERESHOME/clouds/CER4.1-4.0P2/rcf/Run.CER4.1-4.Cleanup.pl 20080617

For 8th MESH CLASS cases:

source $CERESHOME/clouds/ CER4.1-4.0P2/rcf /CER4.1-4.0P2.env 1 2

$CERESHOME/clouds/CER4.1-4.0P2/rcf/Run.CER4.1-4.Cleanup.pl 20111231

For 16th MESH cases:

source $CERESHOME/clouds/ CER4.1-4.0P2/rcf /CER4.1-4.0P2.env 2

$CERESHOME/clouds/CER4.1-4.0P2/rcf/Run.CER4.1-4.Cleanup.pl 20090905

Please contact Subsystem Lead for assistance if the cleanup and test case re-run are unsuccessful.

Many problems encountered during compilation, linking, and execution are due to incorrect environment configuration.  Generally, these problems make themselves readily apparent via compiler errors or termination of the program during the initialization stage during the first few seconds of execution.

# Test and Evaluation Procedures - CER4.1-4.0P3 Snow and Ice Processor

This section provides information on how to execute PGE CER4.1-4.0P3.  It also provides an overview of the test and evaluation procedures.  It includes a description of what is being tested and the order in which the tests should be performed.

## Stand Alone Test Procedures

### Execution

Command Line Instructions :

unlimit

cd $CERESHOME/clouds/CER4.1-4.0P3/rcf

source CER4.1-4.0P3.env

Run.CER4.1-4.Cleanup.pl 20121205

CER4.1-4.PCFGen.pl 2012 12 05

CER4.1-4.0P3.PCFcheck.pl pcf/CER4.1-4.0P3_PCF_$SS4_0\_$PS4_0\_$CC4_0P1.20121205

If errors in PCF, correct problems and start over.

If no errors in PCF:

Run.CER4.1-4.0P3.pl pcf/CER4.1-4.0P3_PCF_$SS4_0\_$PS4_0\_$CC4_0P1.20121205

SGE Test Instructions:

cd $CERESHOME/clouds/CER4.1-4.0P3/rcf/

source CER4.1-4.0P3.env

Run.CER4.1-4.Cleanup.pl 20121205

CER4.1-4.0P3-SGE_Driver.pl -date 20121205

The submitted job can be monitored with the qstat command.

Job submission status and job progress file can be found in the file:

$CERESHOME/clouds/CER4.1-4.0P3/rcf/pcf/summary/CER4.1-4.0P3_$SS4_0\_$PS4_0\_$CC4_0P1.20121205.summary

Note:  A file listing of expected output for each PGE can be found in the following file:

$CERESHOME/clouds/data_exp/out_description1.txt

### Exit Codes

All CER4.1-4.0P1 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.

### Snow and Ice Processor Test Summary

| PGE Number | PGE Name | Run Time (mm:ss) | Disk Storage (MB) | Memory (MB) |
| --- | --- | --- | --- | --- |
| CER4.1-4.0P1 | Snow and Ice Processor | 00:03 | 05 | 65 |

## Evaluation Procedures

### Log and Status File Results

The Log and Status files are created by the Toolkit and are located in the directory $CERESHOME/clouds/runlogs after the PGE has been executed.  The comparisons of the Log and status files with their expected outputs are handled in Section 5.2.3.

### Metadata Evaluation

Metadata files for this PGE are created at runtime and are located with their corresponding output files.  The comparisons of the metadata files with their expected results are handled in Section 5.2.3.

### Execution of Comparison Software

The evaluation software for this Subsystem will compare the ASDC generated output with the expected output included with this delivery package.  To run the comparison software, execute the following command:

source $CERESHOME/clouds/CER4.1-4.0P3/rcf/CER4.1-4.0P3.env

$CERESHOME/clouds/test_suites/bin/CER4.1-4.Validate.pl CER4.1-4.0P3

### Evaluation of Comparison Software Output

See Appendix D for a description of the output from the Comparison Software.

## Solutions to Possible Problems

- Output files are opened with Status = NEW.  If any of these files exist when the generating PGE is executed, the PGE will fail.  These files must be removed before any attempt is made to re-run any of the PGEs after the initial run is made.  The Toolkit Log files also need to be deleted before each run to be consistent with the expected output.  The specific problems can generally be found in the LogReport and/or LogStatus files.  NOTE:  For testing purposes only, if the test case must be re-run, you must first cleanup the PCF file generated from a previous run as shown below.

source $CERESHOME/clouds/ CER4.1-4.0P3/rcf /CER4.1-4.0P3.env

$CERESHOME/clouds/CER4.1-4.0P3/rcf/Run.CER4.1-4.Cleanup.pl 20121205

Please contact Subsystem Lead for assistance if the cleanup and test case re-run are unsuccessful.

Many problems encountered during compilation, linking, and execution are due to incorrect environment configuration.  Generally, these problems make themselves readily apparent via compiler errors or termination of the program during the initialization stage during the first few seconds of execution.

# Test and Evaluation Procedures - CER4.1-4.1P1 TRMM Main Processor

This section provides information on how to execute PGE CER4.1-4.1P1.  It also provides an overview of the test and evaluation procedures.  It includes a description of what is being tested and the order in which the tests should be performed.

## Stand Alone Test Procedures

### VIRS Imager File Preparation (for Section 6.1.2.1)

The VIRS files, as received from TSDIS, are inappropriately named.  Subsystems 4.1-4.3 need the VIRS files to be named according the following convention: CER_ECID_TRMM-VIRS.YYYYMMDD_HH.XX where YYYY is a four digit year, MM is the two digit month, DD is the two digit day, HH is the two digit hour, XX is a two digit sequence.  All values correspond to the time of the hour being processed.  Included in this delivery are code and scripts to accomplish the renaming needed.  During the Execution phase of the Test Plan, appropriate instructions will be provided to correctly rename the correct VIRS files for that particular test case.

### Execution

#### TRMM-VIRS Processing

The following command will copy the necessary input files for running this PGE.  This command only needs to be executed if the input files have not been copied to the appropriate directories already.  Copy the input files to appropriate locations using the following script:

$CERESHOME/clouds/test_suites/scripts/Copy_input.csh

Rename the full version of the VIRS file with the following commands:

source $CERESHOME/clouds/bin/CER4.1-4.env 2

$CERESHOME/clouds/bin/Run.CER4.1-4.0P1.RenameVIRS $CERESHOME/clouds/data/input/VIRS/1B01.980105.612.5.HDF

The PGE can be executed with the following sequence of commands listed below.  This sequence of commands covers PCF generation as well as execution of the PGE.

source $CERESHOME/clouds/bin/CER4.1-4.env

$CERESHOME/clouds/bin/CER4.1-4.1P1.PCFGen 1998 01 05 16

$CERESHOME/clouds/bin/Run.CER4.1-4.1P1 $CERESHOME/clouds/rcf/CER4.1-4.1P1_PCF_TRMM-PFM-VIRS_SSIT_000000.1998010516

Note:  A file listing of expected output for each PGE can be found in the following file:

$CERESHOME/clouds/data/out_exp/out_description.txt

### Exit Codes

All CER4.1-4.1P1 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.

### Main Processor Test Summary

| PGE Number | PGE Name | Test Case | Run Time (mm:ss) | Disk Storage (MB) | Memory (MB) |
| --- | --- | --- | --- | --- | --- |
| CER4.1-4.1P1 | Cloud Property Retrieval and Convolution | TRMM | 26:20 | 400 | 280 |

## Evaluation Procedures

The Test Evaluation procedures must be run on the same day that the Test is run.  If unable to run the Evaluation procedures at that time, contact the analyst for a work around.

The following will remove the Instrument and MOA input data files that were used for testing.  This step is done when all testing is complete.  If you are testing another PGE, then it is not necessary to do this step.

$CERESHOME/clouds/test_suites/scripts/Remove_input.csh

### Log and Status File Results

The Log and Status files are created by the Toolkit and are located in the directory $CERESHOME/clouds/data/runlogs after the PGE has been executed.  The comparisons of the Log and status files with their expected outputs are handled in Section 6.2.3.

### Metadata Evaluation

Metadata files for this PGE are created at runtime and are located with their corresponding output files.  The comparisons of the metadata files with their expected results are handled in Section 6.2.3.

### Execution of Comparison Software

The evaluation software for this Subsystem will compare the ASDC generated output with the expected output included with this delivery package.  The software must be run for each of the four test cases.  To run the comparison software, execute the following commands:

source $CERESHOME/clouds/bin/CER4.1-4.env 2

$CERESHOME/clouds/test_suites/bin/CER4.1-4.Validate CER4.1-4.1P1

### Evaluation of Comparison Software Output

See Appendix D for a description of the output from the Comparison Software.

## Solutions to Possible Problems

- Output files are opened with Status = NEW.  If any of these files exist when the generating PGE is executed, the PGE will fail.  These files must be removed before any attempt is made to re-run any of the PGEs after the initial run is made.  The Toolkit Log files also need to be deleted before each run to be consistent with the expected output.  The specific problems can generally be found in the LogReport and/or LogStatus files.  NOTE:  For testing purposes only, if the test cases must be re-run, you must first cleanup the PCF files generated from previous runs as shown below.

For TRMM-VIRS:

$CERESHOME/clouds/bin/Run.CER4.1-4.Cleanup $CERESHOME/clouds/rcf/CER4.1-4.1P1_PCF_TRMM-PFM-VIRS_SSIT_000000.1998010516

Please contact Subsystem Lead for assistance if the cleanup and test cases re-run are unsuccessful.

Many problems encountered during compilation, linking, and execution are due to incorrect environment configuration.  Generally, these problems make themselves readily apparent via compiler errors or termination of the program during the initialization stage during the first few seconds of execution.

Most errors encountered during PCF generation will provide a diagnostic as to the problem.  If problems persist, check for the presence of all the mandatory input files and stage if necessary or contact the analyst.

# Test and Evaluation Procedures - CER4.1-4.1P2 Terra Main Processor

This section provides information on how to execute PGE CER4.1-4.1P2.  It also provides an overview of the test and evaluation procedures.  It includes a description of what is being tested and the order in which the tests should be performed.

## Stand Alone Test Procedures

### MODIS Imager File Preparation (for Section 7.1.2.1)

### Execution

#### Terra-MODIS Processing

The PGE can be executed with the following sequence of commands listed below.  This sequence of commands covers PCF generation as well as execution of the PGE.

The following command will copy the necessary input files for running this PGE.  This command only needs to be executed if the input files have not been copied to the appropriate directories already.  Copy the input files to appropriate locations using the following script:

$CERESHOME/clouds/test_suites/scripts/Copy_input.csh

source $CERESHOME/clouds/bin/CER4.1-4.env 3

$CERESHOME/clouds/bin/CER4.1-4.1P2.PCFGen 2000 06 15 23

$CERESHOME/clouds/bin/Run.CER4.1-4.1P2 $CERESHOME/clouds/rcf/CER4.1-4.1P2_PCF_Terra-FM1+FM2-MODIS_SSIT_000000.2000061523

Note:  A file listing of expected output for each PGE can be found in the following file:

$CERESHOME/clouds/data/out_exp/out_description.txt

There are 16 possible granules for each of three different MODIS file types, radiance, geolocation, and aerosol.  The file names includes the creation time which there is no way of knowing for every file.  An ls is done in the PCFGen script using the portion of the name we know.  When a file is not found, the operating system returns “ls:No match”.  This is not necessarily an error if MODIS files are missing.  Problems will be identified during execution if a matched MODIS data set is not available.

### Exit Codes

All CER4.1-4.1P2 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.

### Main Processor Test Summary

| PGE Number | PGE Name | Test Case | Run Time (mm:ss) | Disk Storage (MB) | Memory (MB) |
| --- | --- | --- | --- | --- | --- |
| CER4.1-4.1P2 | Cloud Property Retrieval and Convolution | Terra | 17:27 | 100 | 454 |

## Evaluation Procedures

The Test Evaluation procedures must be run on the same day that the Test is run.  If unable to run the Evaluation procedures at that time, contact the analyst for a work around.

The following will remove the Instrument and MOA input data files that were used for testing.  This step is done when all testing is complete.  If you are testing another PGE, then it is not necessary to do this step.

$CERESHOME/clouds/test_suites/scripts/Remove_input.csh

### Log and Status File Results

The Log and Status files are created by the Toolkit and are located in the directory $CERESHOME/clouds/data/runlogs after the PGE has been executed.  The comparisons of the Log and status files with their expected outputs are handled in Section 7.2.3.

### Metadata Evaluation

Metadata files for this PGE are created at runtime and are located with their corresponding output files.  The comparisons of the metadata files with their expected results are handled in Section 7.2.3.

### Execution of Comparison Software

The evaluation software for this Subsystem will compare the ASDC generated output with the expected output included with this delivery package.  The software must be run for each of the four test cases.  To run the comparison software, execute the following commands:

source $CERESHOME/clouds/bin/CER4.1-4.env 3

$CERESHOME/clouds/test_suites/bin/CER4.1-4.Validate CER4.1-4.1P2

### Evaluation of Comparison Software Output

See Appendix D for a description of the output from the Comparison Software.

## Solutions to Possible Problems

- Output files are opened with Status = NEW.  If any of these files exist when the generating PGE is executed, the PGE will fail.  These files must be removed before any attempt is made to re-run any of the PGEs after the initial run is made.  The Toolkit Log files also need to be deleted before each run to be consistent with the expected output.  The specific problems can generally be found in the LogReport and/or LogStatus files.  NOTE:  For testing purposes only, if the test cases must be re-run, you must first cleanup the PCF files generated from previous runs as shown below.

For Terra-MODIS:

$CERESHOME/clouds/bin/Run.CER4.1-4.Cleanup $CERESHOME/clouds/rcf/CER4.1-4.1P2_PCF_Terra-FM1+FM2-MODIS_SSIT_000000.2000061523

Please contact Subsystem Lead for assistance if the cleanup and test cases re-run are unsuccessful.

Many problems encountered during compilation, linking, and execution are due to incorrect environment configuration.  Generally, these problems make themselves readily apparent via compiler errors or termination of the program during the initialization stage during the first few seconds of execution.

Most errors encountered during PCF generation will provide a diagnostic as to the problem.  If problems persist, check for the presence of all the mandatory input files and stage if necessary or contact the analyst.

# Test and Evaluation Procedures - CER4.1-4.1P3 Aqua Main Processor

This section provides information on how to execute PGE CER4.1-4.1P3.  It also provides an overview of the test and evaluation procedures.  It includes a description of what is being tested and the order in which the tests should be performed.

## Stand Alone Test Procedures

### MODIS Imager File Preparation (for Section 8.1.2.1)

### Execution

#### Aqua-MODIS Processing

The PGE can be executed with the following sequence of commands listed below.  This sequence of commands covers PCF generation as well as execution of the PGE.

The following command will copy the necessary input files for running this PGE.  This command only needs to be executed if the input files have not been copied to the appropriate directories already.  Copy the input files to appropriate locations using the following script:

$CERESHOME/clouds/test_suites/scripts/Copy_input.csh

source $CERESHOME/clouds/bin/CER4.1-4.env 6

$CERESHOME/clouds/bin/CER4.1-4.1P3.PCFGen 2003 07 01 17

$CERESHOME/clouds/bin/Run.CER4.1-4.1P3$CERESHOME/clouds/rcf/CER4.1-4.1P3_PCF_Aqua-FM3+FM4-MODIS_SSIT_000000.2003070117

Note:  A file listing of expected output for each PGE can be found in the following file:

$CERESHOME/clouds/data/out_exp/out_description.txt

### Exit Codes

All CER4.1-4.1P3 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.

### Main Processor Test Summary

| PGE Number | PGE Name | Test Case | Run Time (mm:ss) | Disk Storage (MB) | Memory (MB) |
| --- | --- | --- | --- | --- | --- |
| CER4.1-4.1P3 | Cloud Property Retrieval and Convolution | Aqua | 39:52 | 100 | 454 |

## Evaluation Procedures

The Test Evaluation procedures must be run on the same day that the Test is run.  If unable to run the Evaluation procedures at that time, contact the analyst for a work around.

The following will remove the Instrument and MOA input data files that were used for testing.  This step is done when all testing is complete.  If you are testing another PGE, then it is not necessary to do this step.

$CERESHOME/clouds/test_suites/scripts/Remove_input.csh

### Log and Status File Results

The Log and Status files are created by the Toolkit and are located in the directory $CERESHOME/clouds/data/runlogs after the PGE has been executed.  The comparisons of the Log and status files with their expected outputs are handled in Section 8.2.3.

### Metadata Evaluation

Metadata files for this PGE are created at runtime and are located with their corresponding output files.  The comparisons of the metadata files with their expected results are handled in Section 8.2.3.

### Execution of Comparison Software

The evaluation software for this Subsystem will compare the ASDC generated output with the expected output included with this delivery package.  The software must be run for each of the four test cases.  To run the comparison software, execute the following commands:

source $CERESHOME/clouds/bin/CER4.1-4.env 6

$CERESHOME/clouds/test_suites/bin/CER4.1-4.Validate CER4.1-4.1P3

### Evaluation of Comparison Software Output

See Appendix D for a description of the output from the Comparison Software.

## Solutions to Possible Problems

- Output files are opened with Status = NEW.  If any of these files exist when the generating PGE is executed, the PGE will fail.  These files must be removed before any attempt is made to re-run any of the PGEs after the initial run is made.  The Toolkit Log files also need to be deleted before each run to be consistent with the expected output.  The specific problems can generally be found in the LogReport and/or LogStatus files.  NOTE:  For testing purposes only, if the test cases must be re-run, you must first cleanup the PCF files generated from previous runs as shown below.

For Aqua-MODIS:

$CERESHOME/clouds/bin/Run.CER4.1-4.Cleanup $CERESHOME/clouds/rcf/CER4.1-4.1P3_PCF_Aqua-FM3+FM4-MODIS_SSIT_000000.2003070117

Please contact Subsystem Lead for assistance if the cleanup and test cases re-run are unsuccessful.

Many problems encountered during compilation, linking, and execution are due to incorrect environment configuration.  Generally, these problems make themselves readily apparent via compiler errors or termination of the program during the initialization stage during the first few seconds of execution.

Most errors encountered during PCF generation will provide a diagnostic as to the problem.  If problems persist, check for the presence of all the mandatory input files and stage if necessary or contact the analyst.

# Test and Evaluation Procedures - CER4.1-4.1P4 Terra Collection 005 Main Processor

This section provides information on how to execute PGE CER4.1-4.1P4.  It also provides an overview of the test and evaluation procedures.  It includes a description of what is being tested and the order in which the tests should be performed.

## Stand Alone Test Procedures

### Execution

cd $CERESHOME/clouds/CER4.1-4.1P4/rcf/

source CER4.1-4.env

CER4.1-4.1P4.CopyECS.pl $CERESHOME/clouds/ancillary/CER4.1-4.1P4/static/CER_ECS/StartUp $SS4_2 StartUp 015000 XXXX07 $InputArchiveSS $SS4_2 $PS4_2 $CC4_2 20100728

Run.CER4.1-4.Cleanup.pl 2010072803

CER4.1-4.1P4-SGE_Driver.pl -date 20100728 -hour 03

Job submission status and job progress file can be found in the file:

$CERESHOME/clouds/CER4.1-4.1P4/rcf/pcf/summary/CER4.1-4.1P4_$SS4_4\_$PS4_1\_$CC4_1.2010072803.summary

There are 16 possible granules for each of three different MODIS file types, radiance, geolocation, and aerosol.  The file names includes the creation time which there is no way of knowing for every file.  An ls is done in the PCFGen script using the portion of the name we know.  When a file is not found, the operating system returns “ls:No match”.  This is not necessarily an error if MODIS files are missing.  Problems will be identified if a matched MODIS data set is not available

Note:  A file listing of expected output for each PGE can be found in the following file:

$CERESHOME/clouds/data_exp/CER4.1-4.1P4/out_description1P4.txt

### Exit Codes

All CER4.1-4.1P4 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.

### Main Processor Test Summary

| PGE Number | PGE Name | Test Case | Run Time (mm:ss) | Disk Storage (MB) | Memory (MB) |
| --- | --- | --- | --- | --- | --- |
| CER4.1-4.1P4 | Cloud Property Retrieval and Convolution | Terra | 1:00:00 | 100 | 454 |

## Evaluation Procedures

### Log and Status File Results

The Log and Status files are created by the Toolkit and are located in the directory $CERESHOME/clouds/runlogs after the PGE has been executed.  The comparisons of the Log and status files with their expected outputs are handled in Section 9.2.3.

### Metadata Evaluation

Metadata files for this PGE are created at runtime and are located with their corresponding output files.  The comparisons of the metadata files with their expected results are handled in Section 9.2.3.

### Execution of Comparison Software

The evaluation software for this Subsystem will compare the ASDC generated output with the expected output included with this delivery package.  To run the comparison software, execute the following commands:

NOTE:  Comparisons cannot be run on the head node (ab01).  Log onto a P6 (ba102) blade to run the following commands.

cd $CERESHOME/clouds/CER4.1-4.1P4/rcf

source CER4.1-4.env

$CERESHOME/clouds/test_suites/bin/CER4.1-4.Validate.pl CER4.1-4.1P4

### Evaluation of Comparison Software Output

See Appendix D for a description of the output from the Comparison Software.

## Solutions to Possible Problems

- Output files are opened with Status = NEW.  If any of these files exist when the generating PGE is executed, the PGE will fail.  These files must be removed before any attempt is made to re-run any of the PGEs after the initial run is made.  The Toolkit Log files also need to be deleted before each run to be consistent with the expected output.  The specific problems can generally be found in the LogReport and/or LogStatus files.  NOTE:  For testing purposes only, if the test cases must be re-run, you must first cleanup the PCF files generated from previous runs as shown below.

cd $CERESHOME/clouds/CER4.1-4.1P4/rcf

source CER4.1-4.env

$CERESHOME/clouds/CER4.1-4.1P4/rcf/Run.CER4.1-4.Cleanup.pl 2010072803

Please contact Subsystem Lead for assistance if the cleanup and test cases re-run are unsuccessful.

Many problems encountered during compilation, linking, and execution are due to incorrect environment configuration.  Generally, these problems make themselves readily apparent via compiler errors or termination of the program during the initialization stage during the first few seconds of execution.

Most errors encountered during PCF generation will provide a diagnostic as to the problem.  If problems persist, check for the presence of all the mandatory input files and stage if necessary or contact the analyst.

# Test and Evaluation Procedures - CER4.1-4.1P4/CER4.1-4.2P2 2-Day Processor

This section provides information on how to execute PGEs CER4.1-4.1P4 and CER4.1-4.2P2 in 2-day groupings.  This helps to ensure that 2 days of Clear Sky Updates are executed by CER4.1-4.2P2 at the proper time - after 2 full days of CER4.1-4.1P4 have completed and before the next 2 days of CER4.1-4.1P4 begin.  It also provides an overview of the test and evaluation procedures.

### Execution

Terra-MODIS 2-Day Testing:

cd $CERESHOME/clouds/CER4.1-4.1P4/rcf/

source CER4.1-4.env

Run.CER4.1-4.Cleanup.pl 2010072300 2010072423

source $CERESHOME/clouds/CER4.1-4.2P2/rcf/CER4.1-4.env 3

$CERESHOME/clouds/CER4.1-4.2P2/rcf/Run.CER4.1-4.Cleanup.pl 20100724

source CER4.1-4.env

CER4.1-4.1P4.CopyECS.pl $CERESHOME/clouds/ancillary/CER4.1-4.1P4/static/CER_ECS/StartUp $SS4_2 StartUp 015000 XXXX07 $InputArchiveSS $SS4_2 $PS4_2 $CC4_2 20100723

CER4.1-4.1P4.CopyECS.pl $CERESHOME/clouds/ancillary/CER4.1-4.1P4/static/CER_ECS/StartUp $SS4_2 StartUp 015000 XXXX07 $InputArchiveSS $SS4_2 $PS4_2 $CC4_2 20100724

Submit_1P4_2P2.pl -start 20100723 -end 20100724

Once all jobs submitted, sge status and job progress files can be found in the file:

$CERESHOME/clouds/CER4.1-4.1P4/rcf/pcf/summary/CER4.1-4.1P4_$SS4_4\_$PS4_1\_$CC4_1.2010072300-2010072423.summary

Terra-MODIS One Month Testing:

cd $CERESHOME/clouds/CER4.1-4.1P4/rcf/

source CER4.1-4.env

Run.CER4.1-4.Cleanup.pl 2010080100 2010083123

source $CERESHOME/clouds/CER4.1-4.2P2/rcf/CER4.1-4.env 3

$CERESHOME/clouds/CER4.1-4.2P2/rcf/Run.CER4.1-4.Cleanup.pl 20100802 20100831

source CER4.1-4.env

CER4.1-4.1P4.CopyECS.pl $CERESHOME/clouds/ancillary/CER4.1-4.1P4/static/CER_ECS/StartUp $SS4_2 StartUp 015000 XXXX08 $InputArchiveSS $SS4_2 $PS4_2 $CC4_2 20100801

CER4.1-4.1P4.CopyECS.pl $CERESHOME/clouds/ancillary/CER4.1-4.1P4/static/CER_ECS/StartUp $SS4_2 StartUp 015000 XXXX08 $InputArchiveSS $SS4_2 $PS4_2 $CC4_2 20100802

Submit_1P4_2P2.pl -run_month 201008

For each pair of days, once all jobs submitted, sge status and job progress files can be found in the file:

$CERESHOME/clouds/CER4.1-4.1P4/rcf/pcf/summary/CER4.1-4.1P4_$SS4_4\_$PS4_1\_$CC4_1.201008D100-201008D223.summary

Restart Instructions:  In the event that the script halts, it can be restarted without harming the validation process.  The pair of days where the failure occurred must be cleaned up for CER4.1-4.1P4 (D1 and D2) and CER4.1-4.2P2 (D2).  Determine the problem and make corrections.  Execution can then be resumed with dates ranging from the first cleaned up date to the end of the original date range.  For Month run, replace -run_month line argument with arguments -start YYYYMMD1 -end YYYYMMDL, where DL is the last day of month MM.  See Section 10.3 for cleanup procedures.

Note:  A file listing of expected output for each Clouds 1P4 and 2P2 test job in the 2 day and one month SGE executions can be found in the following file:

$CERESHOME/clouds/data_exp/out_description1P42P2.txt

### Exit Codes

See Sections 9.1.2 and 18.1.2 for CER4.1-4.1P4 and CER4.1-4.2P2 exit codes, respectively.

### Test Summary

| PGE Number | PGE Name | Test Case | Run Time (mm:ss) | Disk Storage (MB) | Memory (MB) |
| --- | --- | --- | --- | --- | --- |
| CER4.1-4.1P4 and CER4.1-4.2P2 | Cloud Property Retrieval and Convolution and Daily CRH Processor | Terra | 2:30:00 (2-day) 48:00:00 (monthly) | 2000 (2-day) 30000 (monthly) | 1.3 |

## Evaluation Procedures

### Log and Status File Results

The Log and Status files are created by the Toolkit and are located in the directory $CERESHOME/clouds/runlogs after the PGE has been executed.  These files will be created for each hour of CER4.1-4.1P4 run and for each day of CER4.1-4.2P2 run.  The comparisons of the Log and status files with their expected outputs are handled in Section 10.2.3.

### Metadata Evaluation

Metadata files for this section are created at runtime and are located with their corresponding output files.  These files will be created for each hour of CER4.1-4.1P4 run and for each day of CER4.1-4.2P2 run.  The comparisons of the metadata files with their expected results are handled in Section 10.2.3.

### Execution of Comparison Software

The evaluation software for this section will compare the ASDC generated output with the expected output included with this delivery package.  To run the comparison software, execute the following commands:

Terra-MODIS 2-Day Test:

NOTE:  Comparisons cannot be run on the head node (ab01).  Log onto a P6 (ba102) blade to run the following commands.

cd $CERESHOME/clouds/CER4.1-4.1P4/rcf

source CER4.1-4.env

cd $CERESHOME/clouds/test_suites

bin/CER4.1-4.Validate.pl CER4.1-4.1P4 3 >scr/TerraVal2Day_$PS4_1\vsEXP.out&

tail -f scr/TerraVal2Day_$PS4_1\vsEXP.out

(Optional command.

Enter <ctrl>-c when “VALIDATION COMPLETE” is printed to screen.

Must complete before continuing.)

cd $CERESHOME/clouds/CER4.1-4.2P2/rcf

source CER4.1-4.env 3

cd $CERESHOME/clouds/test_suites

bin/CER4.1-4.Validate.pl CER4.1-4.2P2 3 >> scr/TerraVal2Day_$PS4_1\vsEXP.out&

tail -f scr/TerraVal2Day_$PS4_1\vsEXP.out

(Optional command.

Enter <ctrl>-c when “VALIDATION COMPLETE” is printed to screen.)

The file $CERESHOME/clouds/test_suites/scr/TerraVal2Day_$PS4_1\vsEXP.out contains the 2-Day Terra validation output.  Search this file for the word “fail” to locate any comparison failures.  Search this file for “does not exist” to locate missing validation files.

Terra-MODIS One Month Test:

NOTE:  Comparisons cannot be run on the head node (ab01).  Log onto a P6 (ba102) blade to run the following commands.

cd $CERESHOME/clouds/CER4.1-4.1P4/rcf

source CER4.1-4.env

cd $CERESHOME/clouds/test_suites

bin/CER4.1-4.Validate.pl CER4.1-4.1P4 4 > scr/TerraVal1mo_$PS4_1\vsEXP.out&

tail -f scr/TerraVal1mo_$PS4_1\vsEXP.out

(Optional command.

Enter <ctrl>-c when “VALIDATION COMPLETE” is printed to screen.

Must complete before continuing.)

cd $CERESHOME/clouds/CER4.1-4.2P2/rcf

source CER4.1-4.env 3

cd $CERESHOME/clouds/test_suites

bin/CER4.1-4.Validate.pl CER4.1-4.2P2 4 >> scr/TerraVal1mo_$PS4_1\vsEXP.out&

tail -f scr/TerraVal1mo_$PS4_1\vsEXP.out

(Optional command.

Enter <ctrl>-c when “VALIDATION COMPLETE” is printed to screen.)

The file $CERESHOME/clouds/test_suites/scr/TerraVal1mo_$PS4_1\vsEXP.out contains the validation output.  Search this file for the word “fail” to locate any comparison failures.  Search this file for “does not exist” to locate missing validation files.

NOTE :  One Month Validation can be executed BEFORE the whole month has finished running, to check how the days run so far compare.  Just ignore all validation output that occurs for jobs not yet complete.

### Evaluation of Comparison Software Output

See Appendix D for a description of the output from the Comparison Software.

## Solutions to Possible Problems

- Output files are opened with Status = NEW.  If any of these files exist when the generating PGE is executed, the PGE will fail.  These files must be removed before any attempt is made to re-run any of the PGEs after the initial run is made.  The Toolkit Log files also need to be deleted before each run to be consistent with the expected output.  The specific problems can generally be found in the LogReport and/or LogStatus files.  NOTE:  For testing purposes only, if the test cases must be re-run, you must first cleanup the PCF files generated from previous runs as shown below.

Terra-MODIS 2-Day Testing:

cd $CERESHOME/clouds/CER4.1-4.1P4/rcf

source CER4.1-4.env

Run.CER4.1-4.Cleanup.pl 20100723 20100724

$CERESHOME/clouds/CER4.1-4.2P2/rcf

source CER4.1-4.env 3

Run.CER4.1-4.Cleanup.pl 20100726

Terra-MODIS One Month Testing:

cd $CERESHOME/clouds/CER4.1-4.1P4/rcf

source CER4.1-4.env

Run.CER4.1-4.Cleanup.pl 20100801 20100831

$CERESHOME/clouds/CER4.1-4.2P2/rcf

source CER4.1-4.env 3

Run.CER4.1-4.Cleanup.pl 20100802 20100831

For restarting a monthly run from a point of failure during days D1 and D2, replace 20100801 with 201008D1 in the 1P4 cleanup and replace 20100802 with 201008D2 in the 2P2 cleanup.  Then restart with the commands:

cd $CERESHOME/clouds/CER4.1-4.1P4/rcf/

source CER4.1-4.env

Submit_1P4_2P2.pl -start_date 201008D1 -end_date 20100831

Please contact Subsystem Lead for assistance if the cleanup and test cases re-run are unsuccessful.

Many problems encountered during compilation, linking, and execution are due to incorrect environment configuration.  Generally, these problems make themselves readily apparent via compiler errors or termination of the program during the initialization stage during the first few seconds of execution.

# Test and Evaluation Procedures - CER4.1-4.1P5 Aqua Collection 005 Main Processor

This section provides information on how to execute PGE CER4.1-4.1P5.  It also provides an overview of the test and evaluation procedures.  It includes a description of what is being tested and the order in which the tests should be performed.

## Stand Alone Test Procedures

### Execution

Aqua-MODIS Processing

cd $CERESHOME/clouds/CER4.1-4.1P5/rcf/

source CER4.1-4.env

CER4.1-4.1P5.CopyECS.pl $CERESHOME/clouds/ancillary/CER4.1-4.1P5/static/CER_ECS/StartUp $SS4_2 StartUp 015000 XXXX07 $InputArchiveSS $SS4_2 $PS4_2 $CC4_2 20100727

CER4.1-4.1P5.CopyECS.pl $CERESHOME/clouds/ancillary/CER4.1-4.1P5/static/CER_ECS/StartUp $SS4_2 StartUp 015000 XXXX07 $InputArchiveSS $SS4_2 $PS4_2 $CC4_2 20100728

Run.CER4.1-4.Cleanup.pl 2010072703

Run.CER4.1-4.Cleanup.pl 2010072803

CER4.1-4.1P5-SGE_Driver.pl -start 20100727 -end 20100728  -hour 03

Job submission status and job progress file can be found in the file:

$CERESHOME/clouds/CER4.1-4.1P5/rcf/pcf/summary/CER4.1-4.1P5_$SS4_4\_$PS4_1\_$CC4_1. 2010072703-2010072803.summary

There are 16 possible granules for each of three different MODIS file types, radiance, geolocation, and aerosol.  The file names includes the creation time which there is no way of knowing for every file.  An ls is done in the PCFGen script using the portion of the name we know.  When a file is not found, the operating system returns “ls:No match”.  This is not necessarily an error if MODIS files are missing.  Problems will be identified if a matched MODIS data set is not available

Note:  A file listing of expected output for each PGE can be found in the following file:

$CERESHOME/clouds/data_exp/CER4.1-4.1P5/out_description1P5.txt

### Exit Codes

All CER4.1-4.1P5 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.

### Main Processor Test Summary

| PGE Number | PGE Name | Test Case | Run Time (hh”mm:ss) | Disk Storage (MB) | Memory (MB) |
| --- | --- | --- | --- | --- | --- |
| CER4.1-4.1P5 | Cloud Property Retrieval and Convolution | Aqua | 10:15 | 100 | 454 |

## Evaluation Procedures

### Log and Status File Results

The Log and Status files are created by the Toolkit and are located in the directory $CERESHOME/clouds/runlogs after the PGE has been executed.  The comparisons of the Log and status files with their expected outputs are handled in Section 11.2.3.

### Metadata Evaluation

Metadata files for this PGE are created at runtime and are located with their corresponding output files.  The comparisons of the metadata files with their expected results are handled in Section 11.2.3.

### Execution of Comparison Software

The evaluation software for this Subsystem will compare the ASDC generated output with the expected output included with this delivery package.  To run the comparison software, execute the following commands:

NOTE:  Comparisons cannot be run on the head node (ab01).  Log onto a P6 (ba102) blade to run the following commands.

cd $CERESHOME/clouds/CER4.1-4.1P5/rcf

source CER4.1-4.env

$CERESHOME/clouds/test_suites/bin/CER4.1-4.Validate.pl CER4.1-4.1P5

### Evaluation of Comparison Software Output

See Appendix D for a description of the output from the Comparison Software.

## Solutions to Possible Problems

- Output files are opened with Status = NEW.  If any of these files exist when the generating PGE is executed, the PGE will fail.  These files must be removed before any attempt is made to re-run any of the PGEs after the initial run is made.  The Toolkit Log files also need to be deleted before each run to be consistent with the expected output.  The specific problems can generally be found in the LogReport and/or LogStatus files.  NOTE:  For testing purposes only, if the test cases must be re-run, you must first cleanup the PCF files generated from previous runs as shown below.

cd $CERESHOME/clouds/CER4.1-4.1P5/rcf

source CER4.1-4.env

Run.CER4.1-4.Cleanup.pl 2010072803

Please contact Subsystem Lead for assistance if the cleanup and test cases re-run are unsuccessful.

Many problems encountered during compilation, linking, and execution are due to incorrect environment configuration.  Generally, these problems make themselves readily apparent via compiler errors or termination of the program during the initialization stage during the first few seconds of execution.

Most errors encountered during PCF generation will provide a diagnostic as to the problem.  If problems persist, check for the presence of all the mandatory input files and stage if necessary or contact the analyst.

# Test and Evaluation Procedures - CER4.1-4.1P5/CER4.1-4.2P2 2-Day Processor

This section provides information on how to execute PGEs CER4.1-4.1P5 and CER4.1-4.2P2 in 2-day groupings.  This helps to ensure that 2 days of Clear Sky Updates are executed by CER4.1-4.2P2 at the proper time - after 2 full days of CER4.1-4.1P5 have completed and before the next 2 days of CER4.1-4.1P5 begin.  It also provides an overview of the test and evaluation procedures.

### Execution

Aqua-MODIS 2-Day Testing:

cd $CERESHOME/clouds/CER4.1-4.1P5/rcf/

source CER4.1-4.env

Run.CER4.1-4.Cleanup.pl 2010072300 2010072423

source $CERESHOME/clouds/CER4.1-4.2P2/rcf/CER4.1-4.env 6

$CERESHOME/clouds/CER4.1-4.2P2/rcf/Run.CER4.1-4.Cleanup.pl 20100724

source CER4.1-4.env

CER4.1-4.1P5.CopyECS.pl $CERESHOME/clouds/ancillary/CER4.1-4.1P5/static/CER_ECS/StartUp $SS4_2 StartUp 015000 XXXX07 $InputArchiveSS $SS4_2 $PS4_2 $CC4_2 20100723

CER4.1-4.1P5.CopyECS.pl $CERESHOME/clouds/ancillary/CER4.1-4.1P5/static/CER_ECS/StartUp $SS4_2 StartUp 015000 XXXX07 $InputArchiveSS $SS4_2 $PS4_2 $CC4_2 20100724

Submit_1P5_2P2.pl -start 20100723 -end 20100724

Once all jobs submitted, sge status and job progress files can be found in the file:

$CERESHOME/clouds/CER4.1-4.1P5/rcf/pcf/summary/CER4.1-4.1P5_$SS4_4\_$PS4_1\_$CC4_1.2010072300-2010072423.summary

Aqua-MODIS One Month Testing:

cd $CERESHOME/clouds/CER4.1-4.1P5/rcf/

source CER4.1-4.env

Run.CER4.1-4.Cleanup.pl 2010080100 2010083123

source $CERESHOME/clouds/CER4.1-4.2P2/rcf/CER4.1-4.env 6

$CERESHOME/clouds/CER4.1-4.2P2/rcf/Run.CER4.1-4.Cleanup.pl 20100802 20100831

source CER4.1-4.env

CER4.1-4.1P5.CopyECS.pl $CERESHOME/clouds/ancillary/CER4.1-4.1P5/static/CER_ECS/StartUp $SS4_2 StartUp 015000 XXXX08 $InputArchiveSS $SS4_2 $PS4_2 $CC4_2 20100801

CER4.1-4.1P5.CopyECS.pl $CERESHOME/clouds/ancillary/CER4.1-4.1P5/static/CER_ECS/StartUp $SS4_2 StartUp 015000 XXXX08 $InputArchiveSS $SS4_2 $PS4_2 $CC4_2 20100802

Submit_1P5_2P2.pl -run_month 201008

For each pair of days, once all jobs submitted, sge status and job progress files can be found in the file:

$CERESHOME/clouds/CER4.1-4.1P5/rcf/pcf/summary/CER4.1-4.1P5_$SS4_4\_$PS4_1\_$CC4_1.201008D100-201008D223.summary

Restart Instructions:  In the event that the script halts, it can be restarted without harming the validation process.  The pair of days where the failure occurred must be cleaned up for CER4.1-4.1P5 (D1 and D2) and CER4.1-4.2P2 (D2).  Determine the problem and make corrections.  Execution can then be resumed with dates ranging from the first cleaned up date to the end of the original date range.  For Month run, replace -run_month line argument with arguments -start YYYYMMD1 -end YYYYMMDL, where DL is the last day of month MM.See Section 12.3 for cleanup procedures.

Note:  A file listing of expected output for each Clouds 1P5 and 2P2 test job in the 2 day and one month SGE executions can be found in the following file:

$CERESHOME/clouds/data_exp/out_description1P52P2.txt

### Exit Codes

See Sections 11.1.2 and 18.1.2 for CER4.1-4.1P5 and CER4.1-4.2P2 exit codes, respectively.

### Test Summary

| PGE Number | PGE Name | Test Case | Run Time (hh:mm:ss) | Disk Storage (MB) | Memory (GB) |
| --- | --- | --- | --- | --- | --- |
| CER4.1-4.1P5 and CER4.1-4.2P2 | Cloud Property Retrieval and Convolution and Daily CRH Processor | Aqua | 2:30:00 (2-day) 48:00:00 (monthly) | 2000 (2-day) 30000 (monthly) | 1.3 |

## Evaluation Procedures

### Log and Status File Results

The Log and Status files are created by the Toolkit and are located in the directory $CERESHOME/clouds/runlogs after the PGE has been executed.  These files will be created for each hour of CER4.1-4.1P5 run and for each day of CER4.1-4.2P2 run.  The comparisons of the Log and status files with their expected outputs are handled in Section 12.2.3.

### Metadata Evaluation

Metadata files for this section are created at runtime and are located with their corresponding output files.  These files will be created for each hour of CER4.1-4.1P5 run and for each day of CER4.1-4.2P2 run.  The comparisons of the metadata files with their expected results are handled in Section 12.2.3.

### Execution of Comparison Software

The evaluation software for this section will compare the ASDC generated output with the expected output included with this delivery package.  To run the comparison software, execute the following commands:

Aqua-MODIS 2-Day Test:

NOTE:  Comparisons cannot be run on the head node (ab01).  Log onto a P6 (ba102) blade to run the following commands.

cd $CERESHOME/clouds/CER4.1-4.1P5/rcf

source CER4.1-4.env

cd $CERESHOME/clouds/test_suites

rm -f scr/AquaVal2Day_$PS4_1\vsEXP.out

bin/CER4.1-4.Validate.pl CER4.1-4.1P5 3 >scr/AquaVal2Day_$PS4_1\vsEXP.out&

tail -f scr/AquaVal2Day_$PS4_1\vsEXP.out

(Optional command.

Enter <ctrl>-c when “VALIDATION COMPLETE” is printed to screen.

Must complete before continuing.)

cd $CERESHOME/clouds/CER4.1-4.2P2/rcf

source CER4.1-4.env 6

cd $CERESHOME/clouds/test_suites

bin/CER4.1-4.Validate.pl CER4.1-4.2P2 3 >> scr/AquaVal2Day_$PS4_1\vsEXP.out&

tail -f scr/AquaVal2Day_$PS4_1\vsEXP.out

(Optional command.

Enter <ctrl>-c when “VALIDATION COMPLETE” is printed to screen.)

The file $CERESHOME/clouds/test_suites/scr/AquaVal2Day_$PS4_1\vsEXP.out contains the 2-Day Terra validation output.  Search this file for the word “fail” to locate any comparison failures.  Search this file for “does not exist” to locate missing validation files.

Aqua-MODIS One Month Test:

NOTE:  Comparisons cannot be run on the head node (ab01).  Log onto a P6 (ba102) blade to run the following commands.

cd $CERESHOME/clouds/CER4.1-4.1P5/rcf

source CER4.1-4.env

cd $CERESHOME/clouds/test_suites

bin/CER4.1-4.Validate.pl CER4.1-4.1P5 4 > scr/AquaVal1mo_$PS4_1\vsEXP.out&

tail -f scr/AquaVal1mo_$PS4_1\vsEXP.out

(Optional command.

Enter <ctrl>-c when “VALIDATION COMPLETE” is printed to screen.

Must complete before continuing.)

cd $CERESHOME/clouds/CER4.1-4.2P2/rcf

source CER4.1-4.env 6

cd $CERESHOME/clouds/test_suites

bin/CER4.1-4.Validate.pl CER4.1-4.2P2 4 >> scr/AquaVal1mo_$PS4_1\vsEXP.out&

tail -f scr/AquaVal1mo_$PS4_1\vsEXP.out

(Optional command.

Enter <ctrl>-c when “VALIDATION COMPLETE” is printed to screen.)

The file $CERESHOME/clouds/test_suites/scr/AquaVal1mo_$PS4_1\vsEXP.out contains the validation output.  Search this file for the word “fail” to locate any comparison failures.  Search this file for “does not exist” to locate missing validation files.

NOTE:  One Month Validation can be executed BEFORE the whole month has finished running, to check how the days run so far compare.  Just ignore all validation output that occurs for jobs not yet complete.

### Evaluation of Comparison Software Output

See Appendix D for a description of the output from the Comparison Software.

## Solutions to Possible Problems

- Output files are opened with Status = NEW.  If any of these files exist when the generating PGE is executed, the PGE will fail.  These files must be removed before any attempt is made to re-run any of the PGEs after the initial run is made.  The Toolkit Log files also need to be deleted before each run to be consistent with the expected output.  The specific problems can generally be found in the LogReport and/or LogStatus files.  NOTE:  For testing purposes only, if the test cases must be re-run, you must first cleanup the PCF files generated from previous runs as shown below.

Terra-MODIS 2-Day Testing:

cd $CERESHOME/clouds/CER4.1-4.1P5/rcf

source CER4.1-4.env

Run.CER4.1-4.Cleanup.pl 20100723 20100724

cd $CERESHOME/clouds/CER4.1-4.2P2/rcf

source CER4.1-4.env 6

Run.CER4.1-4.Cleanup.pl 20100724

Terra-MODIS One Month Testing:

cd $CERESHOME/clouds/CER4.1-4.1P5/rcf

source CER4.1-4.env

Run.CER4.1-4.Cleanup.pl 20100801 20100831

cd $CERESHOME/clouds/CER4.1-4.2P2/rcf

source CER4.1-4.env 6

Run.CER4.1-4.Cleanup.pl 20100802 20100831

For restarting a monthly run from a point of failure during days D1 and D2, replace 20100801 with 201008D1 in the 1P5 cleanup and replace 20100802 with 201008D2 in the 2P2 cleanup.  Then restart with the commands:

cd $CERESHOME/clouds/CER4.1-4.1P5/rcf/

source CER4.1-4.env

Submit_1P5_2P2.pl -start_date 201008D1 -end_date 20100831

Please contact Subsystem Lead for assistance if the cleanup and test cases re-run are unsuccessful.

Many problems encountered during compilation, linking, and execution are due to incorrect environment configuration.  Generally, these problems make themselves readily apparent via compiler errors or termination of the program during the initialization stage during the first few seconds of execution.

# Test and Evaluation Procedures - CER4.1-4.1P6 Aqua and Terra Main Processor

This section provides information on how to execute PGE CER4.1-4.1P6.  It also provides an overview of the test and evaluation procedures.  It includes a description of what is being tested and the order in which the tests should be performed.

***This testing is intended for code compilation and execution on an x86 machine.***

## Stand Alone Test Procedures

NOTE:  This version of Edition4 testing defines the test case dates in the environment script via environment variables YYYY, MM, D1, D2, for year, month, day1, day2.

### Execution

Terra-MODIS Testing:

cd $CERESHOME/clouds/CER4.1-4.1P6/rcf/

source CER4.1-4.env 3

set DAY1=$YYYY$MM$D1

set DAY2=$YYYY$MM$D2

echo;echo Testing $PGENAME $SAT $DAY1 $DAY2;echo

CER4.1-4.1P6.CopyECS.pl $CERESHOME/clouds/ancillary/CER4.1-4.1P6/static/CER_ECS/StartUp/$SAT $SS4_2 StartUp 015000 XXXX$MM $CERESHOME/clouds/data $SS4_1 $PS4_1 $CC4_1 $DAY1

CER4.1-4.1P6.CopyECS.pl $CERESHOME/clouds/ancillary/CER4.1-4.1P6/static/CER_ECS/StartUp/$SAT $SS4_2 StartUp 015000 XXXX$MM $CERESHOME/clouds/data $SS4_1 $PS4_1 $CC4_1 $DAY2

Run.CER4.1-4.Cleanup.pl $DAY1\00 $DAY2\23

setenv PGENAME CER4.1-4.2P5

Run.CER4.1-4.Cleanup.pl $DAY2

setenv PGENAME CER4.1-4.1P6

Submit_1P6_2P5.pl -start_date $DAY1 -end_date $DAY2

The submitted jobs can be monitored with the qstat command and by following the content of the SGE log files

$CERESHOME/clouds/sge_logs/$PGENAME/$PGENAME\_$SS4_4\_$PS4_1\_$CC4_1.$DAY1??.o*

$CERESHOME/clouds/sge_logs/$PGENAME/$PGENAME\_$SS4_4\_$PS4_1\_$CC4_1.$DAY2??.o*

Job submission status and job progress file can be found in the file:

$CERESHOME/clouds/$PGENAME/rcf/pcf/summary/$PGENAME\_$SS4_4\_$PS4_1\_$CC4_1.$DAY1\00-$DAY2\23.summary

Once all jobs are completed, a listing of outputs can be generated:

$CERESHOME/clouds/$PGENAME/rcf/GetExpOutput.pl purpose=outdesc

Aqua-MODIS Testing:

cd $CERESHOME/clouds/CER4.1-4.1P6/rcf/

source CER4.1-4.env 6

set DAY1=$YYYY$MM$D1

echo;echo Testing $PGENAME $SAT $DAY1;echo

CER4.1-4.1P6.CopyECS.pl $CERESHOME/clouds/ancillary/CER4.1-4.1P6/static/CER_ECS/StartUp/$SAT $SS4_2 StartUp 015000 XXXX$MM $CERESHOME/clouds/data $SS4_1 $PS4_1 $CC4_1 $YYYY$MM$D1

Run.CER4.1-4.Cleanup.pl $DAY1+

CER4.1-4.1P6-SGE_Driver.pl -date $DAY1

The submitted jobs can be monitored with the qstat command and by following the content of the SGE log files

$CERESHOME/clouds/sge_logs/$PGENAME/$PGENAME\_$SS4_4\_$PS4_1\_$CC4_1.$DAY1??.o*

Job submission status and job progress file can be found in the file:

$CERESHOME/clouds/$PGENAME/rcf/pcf/summary/$PGENAME\_$SS4_4\_$PS4_1\_$CC4_1.$DAY1\00-$DAY1\23.summary

Once all jobs are completed, a listing of outputs can be generated:

$CERESHOME/clouds/$PGENAME/rcf/GetExpOutput.pl purpose=outdesc

Note:  A file listing of expected test output can be found in the following file:

$CERESHOME/clouds/data_exp/out_description_$PGENAME.txt

### Exit Codes

All CER4.1-4.1P6 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.

### Main Processor Test Summary

| PGE Number | PGE Name | Test Case | Run Time (hh:mm:ss) | Disk Storage (MB) | Memory (GB) |
| --- | --- | --- | --- | --- | --- |
| CER4.1-4.1P6 | Cloud Property Retrieval and Convolution | Terra/Aqua | 1:00:00 | 840 | 1.3 |

## Evaluation Procedures

### Log and Status File Results

The Log and Status files are created by the Toolkit and are located in the directory $CERESHOME/clouds/runlogs after the PGE has been executed.  The comparisons of the Log and status files with their expected outputs are handled in Section 13.2.3.

### Metadata Evaluation

Metadata files for this PGE are created at runtime and are located with their corresponding output files.  The comparisons of the metadata files with their expected results are handled in Section 13.2.3.

### Execution of Comparison Software

The evaluation software for this Subsystem will compare the ASDC generated output with the expected output included with this delivery package. To run the comparison software, execute the following commands:

Terra-MODIS Test Case:

cd $CERESHOME/clouds/test_suites

source $CERESHOME/clouds/CER4.1-4.1P6/rcf/CER4.1-4.env 3

bin/CER4.1-4.Validate.pl > scr/$PGENAME\_$SAT\_val.out &

tail -f scr/$PGENAME\_$SAT\_val.out

Aqua-MODIS Test Case:

cd $CERESHOME/clouds/test_suites

source $CERESHOME/clouds/CER4.1-4.1P6/rcf/CER4.1-4.env 6

bin/CER4.1-4.Validate.pl > scr/$PGENAME\_$SAT\_val.out &

tail -f scr/$PGENAME\_$SAT\_val.out

### Evaluation of Comparison Software Output

See Appendix D for a description of the output from the Comparison Software.

## Solutions to Possible Problems

- Output files are opened with Status = NEW.  If any of these files exist when the generating PGE is executed, the PGE will fail.  These files must be removed before any attempt is made to re-run any of the PGEs after the initial run is made.  The Toolkit Log files also need to be deleted before each run to be consistent with the expected output.  The specific problems can generally be found in the LogReport and/or LogStatus files.  NOTE:  For testing purposes only, if the test cases must be re-run, you must first cleanup the PCF files generated from previous runs as shown below.

For Terra-MODIS Case:

cd $CERESHOME/clouds/CER4.1-4.1P6/rcf/

source CER4.1-4.env 3

Run.CER4.1-4.Cleanup.pl $YYYY$MM$D1 $YYYY$MM$D2

For Aqua-MODIS Case:

cd $CERESHOME/clouds/CER4.1-4.1P6/rcf/

source CER4.1-4.env 6

Run.CER4.1-4.Cleanup.pl $YYYY$MM$D1+

Please contact Subsystem Lead for assistance if the cleanup and test cases re-run are unsuccessful.

Many problems encountered during compilation, linking, and execution are due to incorrect environment configuration.  Generally, these problems make themselves readily apparent via compiler errors or termination of the program during the initialization stage during the first few seconds of execution.

Most errors encountered during PCF generation will provide a diagnostic as to the problem.  If problems persist, check for the presence of all the mandatory input files and stage if necessary or contact the analyst.

# Test and Evaluation Procedures - CER4.1-4.1P7 NPP Main Processor

This section provides information on how to execute PGE CER4.1-4.1P7.  It also provides an overview of the test and evaluation procedures.  It includes a description of what is being tested and the order in which the tests should be performed.

## Stand Alone Test Procedures

### Execution

cd $CERESHOME/clouds/CER4.1-4.1P7/rcf/

source CER4.1-4.env

CER4.1-4.1P7.CopyECS.pl $CERESHOME/clouds/ancillary/CER4.1-4.1P7/static/CER_ECS/StartUp/$SAT $SS4_2 StartUp 015000 XXXX03 $InputArchiveSS $SS4_2 $PS4_2 $CC4_2 20120304

Run.CER4.1-4.Cleanup.pl 2012030410

CER4.1-4.1P7-SGE_Driver.pl -date 20120304 -hour 10

Job submission status and job progress file can be found in the file:

$CERESHOME/clouds/CER4.1-4.1P7/rcf/pcf/summary/CER4.1-4.1P7_$SS4_4\_$PS4_1\_$CC4_1.2012030410.summary

Note:  A file listing of expected output for each PGE can be found in the following file:

$CERESHOME/clouds/data_exp/out_description1P7.txt

### Exit Codes

All CER4.1-4.1P7 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.

### Main Processor Test Summary

| PGE Number | PGE Name | Test Case | Run Time (mm:ss) | Disk Storage (MB) | Memory (MB) |
| --- | --- | --- | --- | --- | --- |
| CER4.1-4.1P7 | Cloud Property Retrieval and Convolution | NPP | 2:20:00 | 100 | 454 |

## Evaluation Procedures

### Log and Status File Results

The Log and Status files are created by the Toolkit and are located in the directory $CERESHOME/clouds/runlogs after the PGE has been executed.  The comparisons of the Log and status files with their expected outputs are handled in Section 14.2.3.

### Metadata Evaluation

Metadata files for this PGE are created at runtime and are located with their corresponding output files.  The comparisons of the metadata files with their expected results are handled in Section 14.2.3.

### Execution of Comparison Software

The evaluation software for this Subsystem will compare the ASDC generated output with the expected output included with this delivery package.  To run the comparison software, execute the following commands:

NOTE:  Comparisons cannot be run on the head node (ab01).  Log onto a P6 (ba102) blade to run the following commands.

cd $CERESHOME/clouds/CER4.1-4.1P7/rcf

source CER4.1-4.env

$CERESHOME/clouds/test_suites/bin/CER4.1-4.Validate.pl CER4.1-4.1P7

### Evaluation of Comparison Software Output

See Appendix D for a description of the output from the Comparison Software.

## Solutions to Possible Problems

- Output files are opened with Status = NEW.  If any of these files exist when the generating PGE is executed, the PGE will fail.  These files must be removed before any attempt is made to re-run any of the PGEs after the initial run is made.  The Toolkit Log files also need to be deleted before each run to be consistent with the expected output.  The specific problems can generally be found in the LogReport and/or LogStatus files.  NOTE:  For testing purposes only, if the test cases must be re-run, you must first cleanup the PCF files generated from previous runs as shown below.

cd $CERESHOME/clouds/CER4.1-4.1P7/rcf

source CER4.1-4.env

Run.CER4.1-4.Cleanup.pl 2012030410

Please contact Subsystem Lead for assistance if the cleanup and test cases re-run are unsuccessful.

Many problems encountered during compilation, linking, and execution are due to incorrect environment configuration.  Generally, these problems make themselves readily apparent via compiler errors or termination of the program during the initialization stage during the first few seconds of execution.

Most errors encountered during PCF generation will provide a diagnostic as to the problem.  If problems persist, check for the presence of all the mandatory input files and stage if necessary or contact the analyst.

# Test and Evaluation Procedures - CER4.1-4.1P7/CER4.1-4.2P7 2-Day Processor

This section provides information on how to execute PGEs CER4.1-4.1P7 and CER4.1-4.2P7 in 2-day groupings.  This helps to ensure that 2 days of Clear Sky Updates are executed by CER4.1-4.2P7 at the proper time - after 2 full days of CER4.1-4.1P7 have completed and before the next 2 days of CER4.1-4.1P7 begin.  It also provides an overview of the test and evaluation procedures.

### Execution

NPP-VIIRS 2-Day Testing:

(This method is not to be used in production unless special permission is given along with specific instructions on how to run the days that are not a whole month.)

cd $CERESHOME/clouds/CER4.1-4.1P7/rcf/

source CER4.1-4.env

Run.CER4.1-4.Cleanup.pl 20120127 20120128

source $CERESHOME/clouds/CER4.1-4.2P7/rcf/CER4.1-4.env

$CERESHOME/clouds/CER4.1-4.2P7/rcf/Run.CER4.1-4.Cleanup.pl 20120128

source CER4.1-4.env

CER4.1-4.1P7.CopyECS.pl $CERESHOME/clouds/ancillary/CER4.1-4.1P7/static/CER_ECS/StartUp/$SAT $SS4_2 StartUp 015000 XXXX01 $InputArchiveSS $SS4_2 $PS4_2 $CC4_2 20120127

CER4.1-4.1P7.CopyECS.pl $CERESHOME/clouds/ancillary/CER4.1-4.1P7/static/CER_ECS/StartUp/$SAT $SS4_2 StartUp 015000 XXXX01 $InputArchiveSS $SS4_2 $PS4_2 $CC4_2 20120128

Submit_1P7_2P7.pl -start_date 20120127 -end_date 20120128

(Enter your name “testing” and date when asked about permission to run a job that is not a whole month.)

Once all jobs submitted, sge status and job progress files can be found in the file:

$CERESHOME/clouds/CER4.1-4.1P7/rcf/pcf/summary/CER4.1-4.1P7_$SS4_4\_$PS4_1\_$CC4_1.2012012700-2012012823.summary

NPP-VIIRS One Month Testing:

cd $CERESHOME/clouds/CER4.1-4.1P7/rcf/

source CER4.1-4.env

Run.CER4.1-4.Cleanup.pl 20120201 20120229

source $CERESHOME/clouds/CER4.1-4.2P7/rcf/CER4.1-4.env

$CERESHOME/clouds/CER4.1-4.2P7/rcf/Run.CER4.1-4.Cleanup.pl 20120202 20120229

source CER4.1-4.env

CER4.1-4.1P7.CopyECS.pl $CERESHOME/clouds/ancillary/CER4.1-4.1P7/static/CER_ECS/StartUp/$SAT $SS4_2 StartUp 015000 XXXX02 $InputArchiveSS $SS4_2 $PS4_2 $CC4_2 20120201

CER4.1-4.1P7.CopyECS.pl $CERESHOME/clouds/ancillary/CER4.1-4.1P7/static/CER_ECS/StartUp/$SAT $SS4_2 StartUp 015000 XXXX02 $InputArchiveSS $SS4_2 $PS4_2 $CC4_2 20120202

Submit_1P7_2P7.pl -run_month 201202

For each pair of days, once all jobs submitted, sge status and job progress files can be found in the file:

$CERESHOME/clouds/CER4.1-4.1P7/rcf/pcf/summary/CER4.1-4.1P7_$SS4_4\_$PS4_1\_$CC4_1.201202D100-201202D223.summary

Restart Instructions:  In the event that the script halts, it can be restarted without harming the validation process.  The pair of days where the failure occurred must be cleaned up for CER4.1-4.1P7 (D1 and D2) and CER4.1-4.2P7 (D2).  Determine the problem and make corrections.  Execution can then be resumed with dates ranging from the first cleaned up date to the end of the original date range.  For Month run, replace -run_month line argument with arguments -start YYYYMMD1 -end YYYYMMDL, where DL is the last day of month MM.  See Section 15.3 for cleanup procedures.

Note:  A file listing of expected output for each Clouds 1P7 and 2P7 test job in the 2 day and one month SGE executions can be found in the following file:

$CERESHOME/clouds/data_exp/out_description1P72P7.txt

### Exit Codes

See Sections 14.1.2 and 22.1.2 for CER4.1-4.1P7 and CER4.1-4.2P7 exit codes, respectively.

### Test Summary

| PGE Number | PGE Name | Test Case | Run Time (mm:ss) | Disk Storage (MB) | Memory (MB) |
| --- | --- | --- | --- | --- | --- |
| CER4.1-4.1P7 and CER4.1-4.2P7 | Cloud Property Retrieval and Convolution and Daily CRH Processor | NPP | 3:00:00 (2-day) 48:00:00 (monthly) | 2000 (2-day) 30000 (monthly) | 1.3 |

## Evaluation Procedures

### Log and Status File Results

The Log and Status files are created by the Toolkit and are located in the directory $CERESHOME/clouds/runlogs after the PGE has been executed.  These files will be created for each hour of CER4.1-4.1P7 run and for each day of CER4.1-4.2P7 run.  The comparisons of the Log and status files with their expected outputs are handled in Section 15.2.3.

### Metadata Evaluation

Metadata files for this section are created at runtime and are located with their corresponding output files.  These files will be created for each hour of CER4.1-4.1P7 run and for each day of CER4.1-4.2P7 run.  The comparisons of the metadata files with their expected results are handled in Section 15.2.3.

### Execution of Comparison Software

The evaluation software for this section will compare the ASDC generated output with the expected output included with this delivery package.  To run the comparison software, execute the following commands:

NPP-VIIRS 2-Day Test:

NOTE:  Comparisons cannot be run on the head node (ab01).  Log onto a P6 (ba102) blade to run the following commands.

cd $CERESHOME/clouds/CER4.1-4.1P7/rcf

source CER4.1-4.env

cd $CERESHOME/clouds/test_suites

bin/CER4.1-4.Validate.pl CER4.1-4.1P7 3 >scr/NPPVal2Day_$PS4_1\vsEXP.out&

tail -f scr/NPPVal2Day_$PS4_1\vsEXP.out

(Optional command.

Enter <ctrl>-c when “VALIDATION COMPLETE” is printed to screen.

Must complete before continuing.)

cd $CERESHOME/clouds/CER4.1-4.2P7/rcf

source CER4.1-4.env

cd $CERESHOME/clouds/test_suites

bin/CER4.1-4.Validate.pl CER4.1-4.2P7 3 >> scr/NPPVal2Day_$PS4_1\vsEXP.out&

tail -f scr/NPPVal2Day_$PS4_1\vsEXP.out

(Optional command.

Enter <ctrl>-c when “VALIDATION COMPLETE” is printed to screen.)

The file $CERESHOME/clouds/test_suites/scr/NPPVal2Day_$PS4_1\vsEXP.out contains the 2-Day Terra validation output.  Search this file for the word “fail” to locate any comparison failures.  Search this file for “does not exist” to locate missing validation files.

NPP-VIIRS One Month Test:

NOTE:  Comparisons cannot be run on the head node (ab01).  Log onto a P6 (ba102) blade to run the following commands.

cd $CERESHOME/clouds/CER4.1-4.1P7/rcf

source CER4.1-4.env

cd $CERESHOME/clouds/test_suites

bin/CER4.1-4.Validate.pl CER4.1-4.1P7 4 > scr/NPPVal1mo_$PS4_1\vsEXP.out&

tail -f scr/NPPVal1mo_$PS4_1\vsEXP.out

(Optional command.

Enter <ctrl>-c when “VALIDATION COMPLETE” is printed to screen.

Must complete before continuing.)

cd $CERESHOME/clouds/CER4.1-4.2P7/rcf

source CER4.1-4.env

cd $CERESHOME/clouds/test_suites

bin/CER4.1-4.Validate.pl CER4.1-4.2P7 4 >> scr/NPPVal1mo_$PS4_1\vsEXP.out&

tail -f scr/NPPVal1mo_$PS4_1\vsEXP.out

(Optional command.

Enter <ctrl>-c when “VALIDATION COMPLETE” is printed to screen.)

The file $CERESHOME/clouds/test_suites/scr/NPPVal1mo_$PS4_1\vsEXP.out contains the validation output.  Search this file for the word “fail” to locate any comparison failures.  Search this file for “does not exist” to locate missing validation files.

NOTE :  One Month Validation can be executed BEFORE the whole month has finished running, to check how the days run so far compare.  Just ignore all validation output that occurs for jobs not yet complete.

### Evaluation of Comparison Software Output

See Appendix D for a description of the output from the Comparison Software.

## Solutions to Possible Problems

- Output files are opened with Status = NEW.  If any of these files exist when the generating PGE is executed, the PGE will fail.  These files must be removed before any attempt is made to re-run any of the PGEs after the initial run is made.  The Toolkit Log files also need to be deleted before each run to be consistent with the expected output.  The specific problems can generally be found in the LogReport and/or LogStatus files.  NOTE:  For testing purposes only, if the test cases must be re-run, you must first cleanup the PCF files generated from previous runs as shown below.

NPP-VIIRS 2-Day Testing:

cd $CERESHOME/clouds/CER4.1-4.1P7/rcf

source CER4.1-4.env

Run.CER4.1-4.Cleanup.pl 20120127 20120128

cd $CERESHOME/clouds/CER4.1-4.2P7/rcf

source CER4.1-4.env

Run.CER4.1-4.Cleanup.pl 20120128

NPP-VIIRS One Month Testing:

cd $CERESHOME/clouds/CER4.1-4.1P7/rcf

source CER4.1-4.env

Run.CER4.1-4.Cleanup.pl 20120201 20120229

cd $CERESHOME/clouds/CER4.1-4.2P7/rcf

source CER4.1-4.env

Run.CER4.1-4.Cleanup.pl 20120202 20120229

For restarting a monthly run from a point of failure during days D1 and D2, replace 20120201 with 201202D1 in the 1P7 cleanup and replace 20120202 with 201202D2 in the 2P7 cleanup.  Then restart with the commands:

cd $CERESHOME/clouds/CER4.1-4.1P7/rcf/

source CER4.1-4.env

Submit_1P7_2P7.pl -start_date 201202D1 -end_date 20120229

Please contact Subsystem Lead for assistance if the cleanup and test cases re-run are unsuccessful.

Many problems encountered during compilation, linking, and execution are due to incorrect environment configuration.  Generally, these problems make themselves readily apparent via compiler errors or termination of the program during the initialization stage during the first few seconds of execution.

# Test and Evaluation Procedures - CER4.1-4.2P1 Daily QC Processor

This section provides information on how to execute PGE CER4.1-4.2P1.  It also provides an overview of the test and evaluation procedures.  It includes a description of what is being tested and the order in which the tests should be performed.

## Stand Alone Test Procedure

### Execution

#### All Data Sources

The following command will copy the necessary input files for running this PGE.  This command only needs to be executed if the input files have not been copied to the appropriate directories already.  Copy the input files to appropriate locations using the following script:

$CERESHOME/clouds/test_suites/scripts/Copy_input.csh

The PGE can be executed with the following sequence of commands listed below.  This sequence of commands covers PCF generation as well as execution of the PGE.

source $CERESHOME/clouds/bin/CER4.1-4.env 6

$CERESHOME/clouds/bin/CER4.1-4.2P1.PCFGen 2003 07 01

$CERESHOME/clouds/bin/Run.CER4.1-4.2P1 $CERESHOME/clouds/rcf/CER4.1-4.2P1_PCF_Aqua-MODIS_SSIT_000000.20030701

Note:  A file listing of expected output for each PGE can be found in the following file:

$CERESHOME/clouds/data/out_exp/out_description.txt

There are 16 possible granules for each of three different MODIS file types, radiance, geolocation, and aerosol.  The file names includes the creation time which there is no way of knowing for every file.  An ls is done in the PCFGen script using the portion of the name we know.  When a file is not found, the operating system returns “ls:No match”.  This is not necessarily an error if MODIS files are missing.  Problems will be identified during execution if a matched MODIS data set is not available.

### Exit Codes

All CER4.1-4.2P1 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.

### Daily QC Processor Test Summary

| PGE Number | PGE Name | Run Time (mm:ss) | Disk Storage (MB) | Memory (MB) |
| --- | --- | --- | --- | --- |
| CER4.1-4.2P1 | Daily QC Processor | 00:41 | 200 | 348 |

## Evaluation Procedures

The Test Evaluation procedures must be run on the same day that the Test is run.  If unable to run the Evaluation procedures at that time, contact the analyst for a work around.

The following will remove the Instrument and MOA input data files that were used for testing.  This step is done when all testing is complete.  If you are testing another PGE, then it is not necessary to do this step.

$CERESHOME/clouds/test_suites/scripts/Remove_input.csh

### Log and Status File Results

The Log and Status files are created by the Toolkit and are located in the directory $CERESHOME/clouds/data/runlogs after the PGE has been executed.  The comparisons of the Log and status files with their expected outputs are handled in Section 16.2.3.

### Metadata Evaluation

Metadata files for this PGE are created at runtime and are located with their corresponding output files.  The comparisons of the metadata files with their expected results are handled in Section 16.2.3.

### Execution of Comparison Software

The evaluation software for this Subsystem will compare the ASDC generated output with the expected output included with this delivery package.  To run the comparison software, execute the following command:

source $CERESHOME/clouds/bin/CER4.1-4.env 6

$CERESHOME/clouds/test_suites/bin/CER4.1-4.Validate CER4.1-4.2P1

### Evaluation of Comparison Software Output

See Appendix D for a description of the output from the Comparison Software.

## Solutions to Possible Problems

- Output files are opened with Status = NEW.   If any of these files exist when the generating PGE is executed, the PGE will fail.  These files must be removed before any attempt is made to re-run any of the PGEs after the initial run is made.  The Toolkit Log files also need to be deleted before each run to be consistent with the expected output.  The specific problems can generally be found in the LogReport and/or LogStatus files.  NOTE:  For testing purposes only, if the test case must be re-run, you must first cleanup the PCF file generated from a previous run as shown below.

$CERESHOME/clouds/bin/Run.CER4.1-4.Cleanup $CERESHOME/clouds/rcf/CER4.1-4.2P1_PCF_Aqua-MODIS_SSIT_000000.20030701

Please contact Subsystem Lead for assistance if the cleanup and test case re-run are unsuccessful.

Many problems encountered during compilation, linking, and execution are due to incorrect environment configuration.  Generally, these problems make themselves readily apparent via compiler errors or termination of the program during the initialization stage during the first few seconds of execution.

# Test and Evaluation Procedures - CER4.1-4.2P2 Daily CRH Processor

This section provides information on how to execute PGE CER4.1-4.2P2.  It also provides an overview of the test and evaluation procedures.  It includes a description of what is being tested and the order in which the tests should be performed.

## Stand Alone Test Procedure

### Execution

For Terra:

cd $CERESHOME/clouds/CER4.1-4.2P2/rcf/

source CER4.1-4.env 3

Run.CER4.1-4.Cleanup.pl 20100728

CER4.1-4.2P2-SGE_Driver.pl -date 20100728 -sday

The submitted job can be monitored with the qstat command.

Job submission status and job progress file can be found in the file:

$CERESHOME/clouds/CER4.1-4.2P2/rcf/pcf/summary/CER4.1-4.2P2_$SS4_1\_$PS4_1\_$CC4_1.20100728.summary

For Aqua:

cd $CERESHOME/clouds/CER4.1-4.2P2/rcf/

source CER4.1-4.env 6

Run.CER4.1-4.Cleanup.pl 20100728

CER4.1-4.2P2-SGE_Driver.pl -date 20100728

The submitted job can be monitored with the qstat command.

Job submission status and job progress file can be found in the file:

$CERESHOME/clouds/CER4.1-4.2P2/rcf/pcf/summary/CER4.1-4.2P2_$SS4_1\_$PS4_1\_$CC4_1.20100728.summary

Note:  A file listing of expected output for each clouds PGE test can be found in the following file:

$CERESHOME/clouds/data_exp/out_description2P2.txt

### Exit Codes

All CER4.1-4.2P2 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.

### Daily CRH Processor Test Summary

| PGE Number | PGE Name | Run Time (mm:ss) | Disk Storage (MB) | Memory (MB) |
| --- | --- | --- | --- | --- |
| CER4.1-4.2P2 | Daily CRH Processor | 00:41 | 200 | 348 |

## Evaluation Procedures

### Log and Status File Results

The Log and Status files are created by the Toolkit and are located in the directory $CERESHOME/clouds/runlogs after the PGE has been executed.  The comparisons of the Log and status files with their expected outputs are handled in Section 17.2.3.

### Metadata Evaluation

Metadata files for this PGE are created at runtime and are located with their corresponding output files.  The comparisons of the metadata files with their expected results are handled in Section 17.2.3.

### Execution of Comparison Software

The evaluation software for this Subsystem will compare the ASDC generated output with the expected output included with this delivery package.  To run the comparison software, execute the following command:

For Terra:

NOTE:  Comparisons cannot be run on the head node (ab01).  Log onto a P6 (ba102) blade to run the following commands.

cd $CERESHOME/clouds/CER4.1-4.2P2/rcf

source CER4.1-4.env 3

$CERESHOME/clouds/test_suites/bin/CER4.1-4.Validate.pl CER4.1-4.2P2

For Aqua:

NOTE:  Comparisons cannot be run on the head node (ab01).  Log onto a P6 (ba102) blade to run the following commands.

cd $CERESHOME/clouds/CER4.1-4.2P2/rcf

source CER4.1-4.env 6

$CERESHOME/clouds/test_suites/bin/CER4.1-4.Validate.pl CER4.1-4.2P2

### Evaluation of Comparison Software Output

See Appendix D for a description of the output from the Comparison Software.

## Solutions to Possible Problems

- Output files are opened with Status = NEW.  If any of these files exist when the generating PGE is executed, the PGE will fail.  These files must be removed before any attempt is made to re-run any of the PGEs after the initial run is made.  The Toolkit Log files also need to be deleted before each run to be consistent with the expected output.  The specific problems can generally be found in the LogReport and/or LogStatus files.  NOTE:  For testing purposes only, if the test case must be re-run, you must first cleanup the PCF file generated from a previous run as shown below.

For Terra:

cd $CERESHOME/clouds/CER4.1-4.2P2/rcf

source CER4.1-4.env 3

Run.CER4.1-4.Cleanup.pl 20100728

For Aqua:

cd $CERESHOME/clouds/CER4.1-4.2P2/rcf

source CER4.1-4.env 6

Run.CER4.1-4.Cleanup.pl 20100728

Please contact Subsystem Lead for assistance if the cleanup and test case re-run are unsuccessful.

Many problems encountered during compilation, linking, and execution are due to incorrect environment configuration.  Generally, these problems make themselves readily apparent via compiler errors or termination of the program during the initialization stage during the first few seconds of execution.

# Test and Evaluation Procedures - CER4.1-4.2P3 Collection 005 Daily QC Processor

This section provides information on how to execute PGE CER4.1-4.2P3.  It also provides an overview of the test and evaluation procedures.  It includes a description of what is being tested and the order in which the tests should be performed.

## Stand Alone Test Procedure

### Execution

For Terra:

cd $CERESHOME/clouds/CER4.1-4.2P3/rcf/

source CER4.1-4.env 3

Run.CER4.1-4.Cleanup.pl 20100728

CER4.1-4.2P3-SGE_Driver.pl -date 20100728

For Aqua:

cd $CERESHOME/clouds/CER4.1-4.2P3/rcf/

source CER4.1-4.env 6

Run.CER4.1-4.Cleanup.pl 20100728

CER4.1-4.2P3-SGE_Driver.pl -date 20100728

The submitted job can be monitored with the qstat command.

Job submission status and job progress file can be found in the file:

$CERESHOME/clouds/CER4.1-4.2P3/rcf/pcf/summary/CER4.1-4.2P3_$SS4_1\_$PS4_1\_$CC4_1.20100728.summary

Note:  A file listing of expected output for each clouds PGE test can be found in the following file:

$CERESHOME/clouds/data_exp/out_description2P3.txt

### Exit Codes

All CER4.1-4.2P3 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.

### Daily QC Processor Test Summary

| PGE Number | PGE Name | Run Time (mm:ss) | Disk Storage (MB) | Memory (MB) |
| --- | --- | --- | --- | --- |
| CER4.1-4.2P3 | Collection 005 Daily QC Processor | 00:05 | 200 | 348 |

## Evaluation Procedures

### Log and Status File Results

The Log and Status files are created by the Toolkit and are located in the directory $CERESHOME/clouds/runlogs after the PGE has been executed.  The comparisons of the Log and status files with their expected outputs are handled in Section 18.2.3.

### Metadata Evaluation

Metadata files for this PGE are created at runtime and are located with their corresponding output files.  The comparisons of the metadata files with their expected results are handled in Section 18.2.3.

### Execution of Comparison Software

The evaluation software for this Subsystem will compare the ASDC generated output with the expected output included with this delivery package.  To run the comparison software, execute the following command:

For Terra:

NOTE:  Comparisons cannot be run on the head node (ab01).  Log onto a P6 (ba102) blade to run the following commands.

cd $CERESHOME/clouds/CER4.1-4.2P3/rcf

source CER4.1-4.env 3

$CERESHOME/clouds/test_suites/bin/CER4.1-4.Validate.pl CER4.1-4.2P3

For Aqua:

NOTE:  Comparisons cannot be run on the head node (ab01).  Log onto a P6 (ba102) blade to run the following commands.

cd $CERESHOME/clouds/CER4.1-4.2P3/rcf

source CER4.1-4.env 6

$CERESHOME/clouds/test_suites/bin/CER4.1-4.Validate.pl CER4.1-4.2P3

### Evaluation of Comparison Software Output

See Appendix D for a description of the output from the Comparison Software.

## Solutions to Possible Problems

- Output files are opened with Status = NEW.   If any of these files exist when the generating PGE is executed, the PGE will fail.  These files must be removed before any attempt is made to re-run any of the PGEs after the initial run is made.  The Toolkit Log files also need to be deleted before each run to be consistent with the expected output.  The specific problems can generally be found in the LogReport and/or LogStatus files.  NOTE:  For testing purposes only, if the test case must be re-run, you must first cleanup the PCF file generated from a previous run as shown below.

For Terra:

cd $CERESHOME/clouds/CER4.1-4.2P3/rcf

source CER4.1-4.env 3

Run.CER4.1-4.Cleanup.pl 20100728

For Aqua:

cd $CERESHOME/clouds/CER4.1-4.2P3/rcf

source CER4.1-4.env 6

Run.CER4.1-4.Cleanup.pl 20100728

Please contact Subsystem Lead for assistance if the cleanup and test case re-run are unsuccessful.

Many problems encountered during compilation, linking, and execution are due to incorrect environment configuration.  Generally, these problems make themselves readily apparent via compiler errors or termination of the program during the initialization stage during the first few seconds of execution.

# Test and Evaluation Procedures - CER4.1-4.2P4 Daily QC Processor

This section provides information on how to execute PGE CER4.1-4.2P4.  It also provides an overview of the test and evaluation procedures.  It includes a description of what is being tested and the order in which the tests should be performed.

***This testing is intended for code compilation and execution on an x86 machine.***

## Stand Alone Test Procedures

### Execution

Terra-MODIS Testing:

cd $CERESHOME/clouds/CER4.1-4.2P4/rcf/

source CER4.1-4.env 3

set DAY1=$YYYY$MM$D1

set DAY2=$YYYY$MM$D2

echo;echo Testing $PGENAME $SAT $DAY1 $DAY2;echo

Run.CER4.1-4.Cleanup.pl $DAY1 $DAY2

CER4.1-4.2P4-SGE_Driver.pl -start $DAY1 -end $DAY2

The submitted jobs can be monitored with the qstat command and by following the content of the SGE log files $CERESHOME/clouds/sge_logs/$PGENAME/$PGENAME\_$SS4_1\_$PS4_1\_$CC4_1.$DAY1.o*

$CERESHOME/clouds/sge_logs/$PGENAME/$PGENAME\_$SS4_1\_$PS4_1\_$CC4_1.$DAY2.o*

Job submission status and job progress file can be found in  the file:

$CERESHOME/clouds/$PGENAME/rcf/pcf/summary/$PGENAME\_$SS4_1\_$PS4_1\_$CC4_1.$DAY1-$DAY2.summary

Once all jobs are completed, a listing of outputs can be generated:

$CERESHOME/clouds/$PGENAME/rcf/GetExpOutput.pl purpose=outdesc

Aqua-MODIS Testing:

cd $CERESHOME/clouds/CER4.1-4.2P4/rcf/

source CER4.1-4.env 6

set DAY1=$YYYY$MM$D1

echo; echo Testing $PGENAME $SAT $DAY1 ;echo

Run.CER4.1-4.Cleanup.pl $DAY1

CER4.1-4.2P4-SGE_Driver.pl -date $DAY1

The submitted job can be monitored with the qstat command and by following the content of the SGE log file $CERESHOME/clouds/sge_logs/$PGENAME/$PGENAME\_$SS4_1\_$PS4_1\_$CC4_1.$DAY1.o*

Job submission status and job progress file can be found in the file:

$CERESHOME/clouds/$PGENAME/rcf/pcf/summary/$PGENAME\_$SS4_1\_$PS4_1\_$CC4_1.$DAY1.summary

Once all jobs are completed, a listing of outputs can be generated:

$CERESHOME/clouds/$PGENAME/rcf/GetExpOutput.pl purpose=outdesc

Note:  A file listing of expected test output can be found in the following file:

$CERESHOME/clouds/data_exp/out_description_$PGENAME.txt

### Exit Codes

All CER4.1-4.2P4 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.

### Daily QC Processor Test Summary

| PGE Number | PGE Name | Test Case | Run Time (mm:ss) | Disk Storage (MB) | Memory (MB) |
| --- | --- | --- | --- | --- | --- |
| CER4.1-4.2P4 | Collection 005 Daily QC Processor | Terra/Aqua | 00:30 | 200 | 973 |

## Evaluation Procedures

### Log and Status File Results

The Log and Status files are created by the Toolkit and are located in the directory $CERESHOME/clouds/runlogs after the PGE has been executed.  The comparisons of the Log and status files with their expected outputs are handled in Section 19.2.3.

### Metadata Evaluation

Metadata files for this PGE are created at runtime and are located with their corresponding output files.  The comparisons of the metadata files with their expected results are handled in Section 19.2.3.

### Execution of Comparison Software

The evaluation software for this Subsystem will compare the ASDC generated output with the expected output included with this delivery package.  To run the comparison software, execute the following commands:

Terra-MODIS Test Case:

source $CERESHOME/clouds/CER4.1-4.2P4/rcf/CER4.1-4.env 3

$CERESHOME/clouds/test_suites/bin/CER4.1-4.Validate.pl

Aqua-MODIS Test Case:

source $CERESHOME/clouds/CER4.1-4.2P4/rcf/CER4.1-4.env 6

$CERESHOME/clouds/test_suites/bin/CER4.1-4.Validate.pl

### Evaluation of Comparison Software Output

See Appendix D for a description of the output from the Comparison Software.

## Solutions to Possible Problems

- Output files are opened with Status = NEW.  If any of these files exist when the generating PGE is executed, the PGE will fail.  These files must be removed before any attempt is made to re-run any of the PGEs after the initial run is made.  The Toolkit Log files also need to be deleted before each run to be consistent with the expected output.  The specific problems can generally be found in the LogReport and/or LogStatus files.  NOTE:  For testing purposes only, if the test cases must be re-run, you must first cleanup the PCF files generated from previous runs as shown below.

For Terra-MODIS Case:

cd $CERESHOME/clouds/CER4.1-4.2P4/rcf/

source CER4.1-4.env 3

Run.CER4.1-4.Cleanup.pl $YYYY$MM$D1 $YYYY$MM$D2

For Aqua-MODIS Case:

cd $CERESHOME/clouds/CER4.1-4.2P4/rcf/

source CER4.1-4.env 6

Run.CER4.1-4.Cleanup.pl $YYYY$MM$D1

Please contact Subsystem Lead for assistance if the cleanup and test cases re-run are unsuccessful.

Many problems encountered during compilation, linking, and execution are due to incorrect environment configuration.  Generally, these problems make themselves readily apparent via compiler errors or termination of the program during the initialization stage during the first few seconds of execution.

Most errors encountered during PCF generation will provide a diagnostic as to the problem.  If problems persist, check for the presence of all the mandatory input files and stage if necessary or contact the analyst.

# Test and Evaluation Procedures - CER4.1-4.2P5 Daily QC Processor

This section provides information on how to execute PGE CER4.1-4.2P5.  It also provides an overview of the test and evaluation procedures.  It includes a description of what is being tested and the order in which the tests should be performed.

***This testing is intended for code compilation and execution on an x86 machine.***

## Stand Alone Test Procedures

### Execution

Terra-MODIS Testing:

cd $CERESHOME/clouds/CER4.1-4.2P5/rcf/

source CER4.1-4.env 3

set DAY1=$YYYY$MM$D1

set DAY2=$YYYY$MM$D2

echo;echo Testing $PGENAME $SAT $DAY1 $DAY2;echo

Run.CER4.1-4.Cleanup.pl $DAY2

CER4.1-4.2P5-SGE_Driver.pl -date $DAY2

The submitted job can be monitored with the qstat command and by following the content of the SGE log file $CERESHOME/clouds/sge_logs/$PGENAME/$PGENAME\_$SS4_1\_$PS4_1\_$CC4_1.$DAY2.o*

Job submission status and job progress file can be found in the file:

$CERESHOME/clouds/$PGENAME/rcf/pcf/summary/$PGENAME\_$SS4_1\_$PS4_1\_$CC4_1.$DAY2.summary

Once all jobs are completed, a listing of outputs can be generated:

$CERESHOME/clouds/$PGENAME/rcf/GetExpOutput.pl purpose=outdesc

Aqua-MODIS Testing:

cd $CERESHOME/clouds/CER4.1-4.2P5/rcf/

source CER4.1-4.env 6

set DAY1=$YYYY$MM$D1

echo;echo Testing $PGENAME $SAT $DAY1;echo

Run.CER4.1-4.Cleanup.pl $DAY1

CER4.1-4.2P5-SGE_Driver.pl -date $DAY1 -sday

The submitted job can be monitored with the qstat command and by following the content of the SGE log file $CERESHOME/clouds/sge_logs/$PGENAME/$PGENAME\_$SS4_1\_$PS4_1\_$CC4_1.$DAY1.o*

Job submission status and job progress file can be found in the file:

$CERESHOME/clouds/$PGENAME/rcf/pcf/summary/$PGENAME\_$SS4_1\_$PS4_1\_$CC4_1.$DAY1.summary

Once all jobs are completed, a listing of outputs can be generated:

$CERESHOME/clouds/$PGENAME/rcf/GetExpOutput.pl purpose=outdesc

Note:  A file listing of expected test output can be found in the following file:

$CERESHOME/clouds/data_exp/out_description_$PGENAME.txt

### Exit Codes

All CER4.1-4.2P5 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.

### Daily QC Processor Test Summary

| PGE Number | PGE Name | Test Case | Run Time (mm:ss) | Disk Storage (MB) | Memory (MB) |
| --- | --- | --- | --- | --- | --- |
| CER4.1-4.2P5 | Daily CRH Processor | Terra/Aqua | 00:30 | 200 | 348 |

## Evaluation Procedures

### Log and Status File Results

The Log and Status files are created by the Toolkit and are located in the directory $CERESHOME/clouds/runlogs after the PGE has been executed.  The comparisons of the Log and status files with their expected outputs are handled in Section 20.2.3.

### Metadata Evaluation

Metadata files for this PGE are created at runtime and are located with their corresponding output files.  The comparisons of the metadata files with their expected results are handled in Section 20.2.3.

### Execution of Comparison Software

The evaluation software for this Subsystem will compare the ASDC generated output with the expected output included with this delivery package.  To run the comparison software, execute the following commands:

Terra-MODIS Test Case:

source $CERESHOME/clouds/CER4.1-4.2P5/rcf/CER4.1-4.env 3

$CERESHOME/clouds/test_suites/bin/CER4.1-4.Validate.pl

Aqua-MODIS Test Case:

source $CERESHOME/clouds/CER4.1-4.2P5/rcf/CER4.1-4.env 6

$CERESHOME/clouds/test_suites/bin/CER4.1-4.Validate.pl

### Evaluation of Comparison Software Output

See Appendix D for a description of the output from the Comparison Software.

## Solutions to Possible Problems

- Output files are opened with Status = NEW.  If any of these files exist when the generating PGE is executed, the PGE will fail.  These files must be removed before any attempt is made to re-run any of the PGEs after the initial run is made.  The Toolkit Log files also need to be deleted before each run to be consistent with the expected output.  The specific problems can generally be found in the LogReport and/or LogStatus files.  NOTE:  For testing purposes only, if the test cases must be re-run, you must first cleanup the PCF files generated from previous runs as shown below.

For Terra-MODIS Case:

cd $CERESHOME/clouds/CER4.1-4.2P5/rcf/

source CER4.1-4.env 3

Run.CER4.1-4.Cleanup.pl $YYYY$MM$D2

For Aqua-MODIS Case:

cd $CERESHOME/clouds/CER4.1-4.2P5/rcf/

source CER4.1-4.env 6

Run.CER4.1-4.Cleanup.pl $YYYY$MM$D1

Please contact Subsystem Lead for assistance if the cleanup and test cases re-run are unsuccessful.

Many problems encountered during compilation, linking, and execution are due to incorrect environment configuration.  Generally, these problems make themselves readily apparent via compiler errors or termination of the program during the initialization stage during the first few seconds of execution.

Most errors encountered during PCF generation will provide a diagnostic as to the problem.  If problems persist, check for the presence of all the mandatory input files and stage if necessary or contact the analyst.

# Test and Evaluation Procedures - CER4.1-4.2P6 Daily QC Processor

This section provides information on how to execute PGE CER4.1-4.2P6.  It also provides an overview of the test and evaluation procedures.  It includes a description of what is being tested and the order in which the tests should be performed.

## Stand Alone Test Procedures

### Execution

NPP-VIIRS Testing:

cd $CERESHOME/clouds/CER4.1-4.2P6/rcf/

source CER4.1-4.env

Run.CER4.1-4.Cleanup.pl 20120304

CER4.1-4.2P6-SGE_Driver.pl -date 20120304

The submitted job can be monitored with the qstat command.

Job submission status and job progress file can be found in  the file:

$CERESHOME/clouds/CER4.1-4.2P6/rcf/pcf/summary/CER4.1-4.2P6_$SS4_1\_$PS4_1\_$CC4_1.20120304.summary

Note:  A file listing of expected output for each Clouds PGE testing can be found in the following file:

$CERESHOME/clouds/data_exp/out_description2P6.txt

### Exit Codes

All CER4.1-4.2P6 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.

### Daily QC Processor Test Summary

| PGE Number | PGE Name | Test Case | Run Time (mm:ss) | Disk Storage (MB) | Memory (MB) |
| --- | --- | --- | --- | --- | --- |
| CER4.1-4.2P6 | Daily QC Processor | NPP | 00:30 | 200 | 973 |

## Evaluation Procedures

### Log and Status File Results

The Log and Status files are created by the Toolkit and are located in the directory $CERESHOME/clouds/runlogs after the PGE has been executed.  The comparisons of the Log and status files with their expected outputs are handled in Section 19.2.3.

### Metadata Evaluation

Metadata files for this PGE are created at runtime and are located with their corresponding output files.  The comparisons of the metadata files with their expected results are handled in Section 19.2.3.

### Execution of Comparison Software

The evaluation software for this Subsystem will compare the ASDC generated output with the expected output included with this delivery package.  To run the comparison software, execute the following commands:

NPP-VIIRS Test Case:

cd $CERESHOME/clouds/CER4.1-4.2P6/rcf

source CER4.1-4.env

$CERESHOME/clouds/test_suites/bin/CER4.1-4.Validate.pl CER4.1-4.2P6 2

### Evaluation of Comparison Software Output

See Appendix D for a description of the output from the Comparison Software.

## Solutions to Possible Problems

- Output files are opened with Status = NEW.  If any of these files exist when the generating PGE is executed, the PGE will fail.  These files must be removed before any attempt is made to re-run any of the PGEs after the initial run is made.  The Toolkit Log files also need to be deleted before each run to be consistent with the expected output.  The specific problems can generally be found in the LogReport and/or LogStatus files.  NOTE:  For testing purposes only, if the test cases must be re-run, you must first cleanup the PCF files generated from previous runs as shown below.

For NPP-VIIRS Case:

cd $CERESHOME/clouds/CER4.1-4.2P6/rcf

source CER4.1-4.env

Run.CER4.1-4.Cleanup.pl 20120304

Please contact Subsystem Lead for assistance if the cleanup and test cases re-run are unsuccessful.

Many problems encountered during compilation, linking, and execution are due to incorrect environment configuration.  Generally, these problems make themselves readily apparent via compiler errors or termination of the program during the initialization stage during the first few seconds of execution.

Most errors encountered during PCF generation will provide a diagnostic as to the problem.  If problems persist, check for the presence of all the mandatory input files and stage if necessary or contact the analyst.

# Test and Evaluation Procedures - CER4.1-4.2P7 Daily QC Processor

This section provides information on how to execute PGE CER4.1-4.2P7.  It also provides an overview of the test and evaluation procedures.  It includes a description of what is being tested and the order in which the tests should be performed.

## Stand Alone Test Procedures

### Execution

NPP-VIIRS Testing:

cd $CERESHOME/clouds/CER4.1-4.2P7/rcf/

source CER4.1-4.env

Run.CER4.1-4.Cleanup.pl 20120304

CER4.1-4.2P7-SGE_Driver.pl -date 20120304 -sday

The submitted job can be monitored with the qstat command.

Job submission status and job progress file can be found in the file:

$CERESHOME/clouds/CER4.1-4.2P7/rcf/pcf/summary/CER4.1-4.2P7_$SS4_1\_$PS4_1\_$CC4_1.20120304.summary

Note:  A file listing of expected output for each Clouds PGE testing can be found in the following file:

$CERESHOME/clouds/data_exp/out_description2P7.txt

### Exit Codes

All CER4.1-4.2P7 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.

### Daily QC Processor Test Summary

| PGE Number | PGE Name | Test Case | Run Time (mm:ss) | Disk Storage (MB) | Memory (MB) |
| --- | --- | --- | --- | --- | --- |
| CER4.1-4.2P7 | Daily CRH Processor | NPP | 00:30 | 200 | 348 |

## Evaluation Procedures

### Log and Status File Results

The Log and Status files are created by the Toolkit and are located in the directory $CERESHOME/clouds/runlogs after the PGE has been executed.  The comparisons of the Log and status files with their expected outputs are handled in Section 20.2.3.

### Metadata Evaluation

Metadata files for this PGE are created at runtime and are located with their corresponding output files.  The comparisons of the metadata files with their expected results are handled in Section 20.2.3.

### Execution of Comparison Software

The evaluation software for this Subsystem will compare the ASDC generated output with the expected output included with this delivery package.  To run the comparison software, execute the following commands:

NPP-VIIRS Test Case:

cd $CERESHOME/clouds/CER4.1-4.2P7/rcf

source CER4.1-4.env

$CERESHOME/clouds/test_suites/bin/CER4.1-4.Validate.pl CER4.1-4.2P7 2

### Evaluation of Comparison Software Output

See Appendix D for a description of the output from the Comparison Software.

## Solutions to Possible Problems

- Output files are opened with Status = NEW.  If any of these files exist when the generating PGE is executed, the PGE will fail.  These files must be removed before any attempt is made to re-run any of the PGEs after the initial run is made.  The Toolkit Log files also need to be deleted before each run to be consistent with the expected output.  The specific problems can generally be found in the LogReport and/or LogStatus files.  NOTE:  For testing purposes only, if the test cases must be re-run, you must first cleanup the PCF files generated from previous runs as shown below.

For NPP-VIIRS Case:

cd $CERESHOME/clouds/CER4.1-4.2P7/rcf

source CER4.1-4.env

Run.CER4.1-4.Cleanup.pl 20120304

Please contact Subsystem Lead for assistance if the cleanup and test cases re-run are unsuccessful.

Many problems encountered during compilation, linking, and execution are due to incorrect environment configuration.  Generally, these problems make themselves readily apparent via compiler errors or termination of the program during the initialization stage during the first few seconds of execution.

Most errors encountered during PCF generation will provide a diagnostic as to the problem.  If problems persist, check for the presence of all the mandatory input files and stage if necessary or contact the analyst.

# Test and Evaluation Procedures - CER4.1-4.3P1 Monthly QC Processor

This section provides information on how to execute PGE CER4.1-4.3P1.  It also provides an overview of the test and evaluation procedures.  It includes a description of what is being tested and the order in which the tests should be performed.

## Stand Alone Test Procedures

### Execution

#### All Data Sources

The following command will copy the necessary input files for running this PGE.  This command only needs to be executed if the input files have not been copied to the appropriate directories already.  Copy the input files to appropriate locations using the following script:

$CERESHOME/clouds/test_suites/scripts/Copy_input.csh

The PGE can be executed with the following sequence of commands listed below.  This sequence of commands covers PCF generation as well as execution of the PGE.

source $CERESHOME/clouds/bin/CER4.1-4.env 6

$CERESHOME/clouds/bin/CER4.1-4.3P1.PCFGen 2003 07

$CERESHOME/clouds/bin/Run.CER4.1-4.3P1 $CERESHOME/clouds/rcf/CER4.1-4.3P1_PCF_Aqua-MODIS_SSIT_000000.200307

Note:  A file listing of expected output for each PGE can be found in the following file:

$CERESHOME/clouds/data/out_exp/out_description.txt

### Exit Codes

All CER4.1-4.3P1 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.

### Monthly QC Processor Test Summary

| PGE Number | PGE Name | Run Time (mm:ss) | Disk Storage (MB) | Memory (MB) |
| --- | --- | --- | --- | --- |
| CER4.1-4.3P1 | Monthly QC Processor | 00:02 | 350 | 348 |

## Evaluation Procedures

The Test Evaluation procedures must be run on the same day that the Test is run.  If unable to run the Evaluation procedures at that time, contact the analyst for a work around.

The following will remove the Instrument and MOA input data files that were used for testing.  This step is done when all testing is complete.  If you are testing another PGE, then it is not necessary to do this step.

$CERESHOME/clouds/test_suites/scripts/Remove_input.csh

### Log and Status File Results

The Log and Status files are created by the Toolkit and are located in the directory $CERESHOME/clouds/data/runlogs after the PGE has been executed.  The comparisons of the Log and status files with their expected outputs are handled in Section 23.2.3.

### Metadata Evaluation

Metadata files for this PGE are created at runtime and are located with their corresponding output files.  The comparisons of the metadata files with their expected results are handled in Section 23.2.3.

### Execution of Comparison Software

The evaluation software for this Subsystem will compare the ASDC generated output with the expected output included with this delivery package.  To run the comparison software, execute the following command:

source $CERESHOME/clouds/bin/CER4.1-4.env 6

$CERESHOME/clouds/test_suites/bin/CER4.1-4.Validate CER4.1-4.3P1

### Evaluation of Comparison Software Output

See Appendix D for a description of the output from the Comparison Software.

## Solutions to Possible Problems

- Output files are opened with Status = NEW.  If any of these files exist when the generating PGE is executed, the PGE will fail.  These files must be removed before any attempt is made to re-run any of the PGEs after the initial run is made.  The Toolkit Log files also need to be deleted before each run to be consistent with the expected output.  The specific problems can generally be found in the LogReport and/or LogStatus files.  NOTE:  For testing purposes only, if the test case must be re-run, you must first cleanup the PCF file generated from a previous run as shown below.

$CERESHOME/clouds/bin/Run.CER4.1-4.Cleanup $CERESHOME/clouds/rcf/CER4.1-4.3P1_PCF_Aqua-MODIS_SSIT_000000.200307

Please contact Subsystem Lead for assistance if the cleanup and test case re-run are unsuccessful.

Many problems encountered during compilation, linking, and execution are due to incorrect environment configuration.  Generally, these problems make themselves readily apparent via compiler errors or termination of the program during the initialization stage during the first few seconds of execution.

# Test and Evaluation Procedures - CER4.1-4.3P2 Collection 005 Monthly QC Processor

This section provides information on how to execute PGE CER4.1-4.3P2.  It also provides an overview of the test and evaluation procedures.  It includes a description of what is being tested and the order in which the tests should be performed.

## Stand Alone Test Procedures

### Execution

For Terra:

cd $CERESHOME/clouds/CER4.1-4.3P2/rcf/

source CER4.1-4.env 3

Run.CER4.1-4.Cleanup.pl  201007

CER4.1-4.3P2-SGE_Driver.pl -date 201007

The submitted job can be monitored with the qstat command.

Job submission status and job progress file can be found in the file:

$CERESHOME/clouds/CER4.1-4.3P2/rcf/pcf/summary/CER4.1-4.3P2_$SS4_1\_$PS4_1\_$CC4_1.201007.summary

For Aqua:

cd $CERESHOME/clouds/CER4.1-4.3P2/rcf/

source CER4.1-4.env 6

Run.CER4.1-4.Cleanup.pl 201007

CER4.1-4.3P2-SGE_Driver.pl -date 201007

The submitted job can be monitored with the qstat command.

Job submission status and job progress file can be found in the file:

$CERESHOME/clouds/CER4.1-4.3P2/rcf/pcf/summary/CER4.1-4.3P2_$SS4_1\_$PS4_1\_$CC4_1.201007.summary

Note:  A file listing of expected output for each Clouds PGE testing can be found in the following file:

$CERESHOME/clouds/data_exp/out_description3P2.txt

### Exit Codes

All CER4.1-4.3P2 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.

### Monthly QC Processor Test Summary

| PGE Number | PGE Name | Run Time (mm:ss) | Disk Storage (MB) | Memory (MB) |
| --- | --- | --- | --- | --- |
| CER4.1-4.3P2 | Collection 005 Monthly QC Processor | 00:02 | 350 | 348 |

## Evaluation Procedures

### Log and Status File Results

The Log and Status files are created by the Toolkit and are located in the directory $CERESHOME/clouds/runlogs after the PGE has been executed.  The comparisons of the Log and status files with their expected outputs are handled in Section 24.2.3.

### Metadata Evaluation

Metadata files for this PGE are created at runtime and are located with their corresponding output files.  The comparisons of the metadata files with their expected results are handled in Section 24.2.3.

### Execution of Comparison Software

The evaluation software for this Subsystem will compare the ASDC generated output with the expected output included with this delivery package.  To run the comparison software, execute the following command:

For Terra:

NOTE:  Comparisons cannot be run on the head node (ab01).  Log onto a P6 (ba102) blade to run the following commands.

cd $CERESHOME/clouds/CER4.1-4.3P2/rcf

source CER4.1-4.env 3

$CERESHOME/clouds/test_suites/bin/CER4.1-4.Validate.pl CER4.1-4.3P2

For Aqua:

NOTE:  Comparisons cannot be run on the head node (ab01).  Log onto a P6 (ba102) blade to run the following commands.

cd $CERESHOME/clouds/CER4.1-4.3P2/rcf

source CER4.1-4.env 6

$CERESHOME/clouds/test_suites/bin/CER4.1-4.Validate.pl CER4.1-4.3P2

### Evaluation of Comparison Software Output

See Appendix D for a description of the output from the Comparison Software.

## Solutions to Possible Problems

- Output files are opened with Status = NEW.  If any of these files exist when the generating PGE is executed, the PGE will fail.  These files must be removed before any attempt is made to re-run any of the PGEs after the initial run is made.  The Toolkit Log files also need to be deleted before each run to be consistent with the expected output.  The specific problems can generally be found in the LogReport and/or LogStatus files.  NOTE:  For testing purposes only, if the test case must be re-run, you must first cleanup the PCF file generated from a previous run as shown below.

For Terra:

cd $CERESHOME/clouds/CER4.1-4.3P2/rcf

source CER4.1-4.env 3

Run.CER4.1-4.Cleanup.pl 201007

For Aqua:

cd $CERESHOME/clouds/CER4.1-4.3P2/rcf

source CER4.1-4.env 6

Run.CER4.1-4.Cleanup.pl 201007

Please contact Subsystem Lead for assistance if the cleanup and test case re-run are unsuccessful.

Many problems encountered during compilation, linking, and execution are due to incorrect environment configuration.  Generally, these problems make themselves readily apparent via compiler errors or termination of the program during the initialization stage during the first few seconds of execution.

# Test and Evaluation Procedures - CER4.1-4.3P3 Monthly QC Processor

This section provides information on how to execute PGE CER4.1-4.3P3.  It also provides an overview of the test and evaluation procedures.  It includes a description of what is being tested and the order in which the tests should be performed.

***This testing is intended for code compilation and execution on an x86 machine.***

## Stand Alone Test Procedures

### Execution

Terra-MODIS Testing:

cd $CERESHOME/clouds/CER4.1-4.3P3/rcf/

source CER4.1-4.env 3

echo;echo Testing $PGENAME $SAT $YYYY$MM;echo

Run.CER4.1-4.Cleanup.pl  $YYYY$MM

CER4.1-4.3P3-SGE_Driver.pl -date $YYYY$MM

The submitted job can be monitored with the qstat command and by following the content of the SGE log file $CERESHOME/clouds/sge_logs/$PGENAME/$PGENAME\_$SS4_1\_$PS4_1\_$CC4_1.$YYYY$MM.o*

Job submission status and job progress file can be found in the file:

$CERESHOME/clouds/$PGENAME/rcf/pcf/summary/$PGENAME\_$SS4_1\_$PS4_1\_$CC4_1.$YYYY$MM.summary

Once all jobs are completed, a listing of outputs can be generated:

$CERESHOME/clouds/$PGENAME/rcf/GetExpOutput.pl purpose=outdesc

Aqua-MODIS Testing:

cd $CERESHOME/clouds/CER4.1-4.3P3/rcf/

source CER4.1-4.env 6

echo;echo Testing $PGENAME $SAT $YYYY$MM;echo

Run.CER4.1-4.Cleanup.pl $YYYY$MM

CER4.1-4.3P3-SGE_Driver.pl -date $YYYY$MM

The submitted job can be monitored with the qstat command and by following the content of the SGE log file $CERESHOME/clouds/sge_logs/$PGENAME/$PGENAME\_$SS4_1\_$PS4_1\_$CC4_1.$YYYY$MM.o*

Job submission status and job progress file can be found in the file:

$CERESHOME/clouds/$PGENAME/rcf/pcf/summary/$PGENAME\_$SS4_1\_$PS4_1\_$CC4_1.$YYYY$MM.summary

Once all jobs are completed, a listing of outputs can be generated:

$CERESHOME/clouds/$PGENAME/rcf/GetExpOutput.pl purpose=outdesc

Note:  A file listing of expected test output can be found in the following file:

$CERESHOME/clouds/data_exp/out_description_$PGENAME.txt

### Exit Codes

All CER4.1-4.3P3 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.

### Daily QC Processor Test Summary

| PGE Number | PGE Name | Test Case | Run Time (mm:ss) | Disk Storage (MB) | Memory (MB) |
| --- | --- | --- | --- | --- | --- |
| CER4.1-4.3P3 | Collection 005 Monthly QC Processor | Terra/Aqua | 00:20 | 350 | 374 |

## Evaluation Procedures

### Log and Status File Results

The Log and Status files are created by the Toolkit and are located in the directory $CERESHOME/clouds/runlogs after the PGE has been executed.  The comparisons of the Log and status files with their expected outputs are handled in Section 25.2.3.

### Metadata Evaluation

Metadata files for this PGE are created at runtime and are located with their corresponding output files.  The comparisons of the metadata files with their expected results are handled in Section 25.2.3.

### Execution of Comparison Software

The evaluation software for this Subsystem will compare the ASDC generated output with the expected output included with this delivery package. To run the comparison software, execute the following commands:

Terra-MODIS Test Case:

source $CERESHOME/clouds/CER4.1-4.3P3/rcf/CER4.1-4.env 3

$CERESHOME/clouds/test_suites/bin/CER4.1-4.Validate.pl

Aqua-MODIS Test Case:

source $CERESHOME/clouds/CER4.1-4.3P3/rcf/CER4.1-4.env 6

$CERESHOME/clouds/test_suites/bin/CER4.1-4.Validate.pl

### Evaluation of Comparison Software Output

See Appendix D for a description of the output from the Comparison Software.

## Solutions to Possible Problems

- Output files are opened with Status = NEW.  If any of these files exist when the generating PGE is executed, the PGE will fail.  These files must be removed before any attempt is made to re-run any of the PGEs after the initial run is made.  The Toolkit Log files also need to be deleted before each run to be consistent with the expected output.  The specific problems can generally be found in the LogReport and/or LogStatus files.  NOTE:  For testing purposes only, if the test cases must be re-run, you must first cleanup the PCF files generated from previous runs as shown below.

For Terra-MODIS Case:

cd $CERESHOME/clouds/CER4.1-4.3P3/rcf

source CER4.1-4.env 3

Run.CER4.1-4.Cleanup.pl $YYYY$MM

For Aqua-MODIS Case:

cd $CERESHOME/clouds/CER4.1-4.3P3/rcf

source CER4.1-4.env 6

Run.CER4.1-4.Cleanup.pl $YYYY$MM

Please contact Subsystem Lead for assistance if the cleanup and test cases re-run are unsuccessful.

Many problems encountered during compilation, linking, and execution are due to incorrect environment configuration.  Generally, these problems make themselves readily apparent via compiler errors or termination of the program during the initialization stage during the first few seconds of execution.

Most errors encountered during PCF generation will provide a diagnostic as to the problem.  If problems persist, check for the presence of all the mandatory input files and stage if necessary or contact the analyst.

# Test and Evaluation Procedures - CER4.1-4.3P4 Monthly QC Processor

This section provides information on how to execute PGE CER4.1-4.3P4.  It also provides an overview of the test and evaluation procedures.  It includes a description of what is being tested and the order in which the tests should be performed.

## Stand Alone Test Procedures

### Execution

NPP Testing:

cd $CERESHOME/clouds/CER4.1-4.3P4/rcf/

source CER4.1-4.env

Run.CER4.1-4.Cleanup.pl  201203

CER4.1-4.3P4-SGE_Driver.pl -date 201203

The submitted job can be monitored with the qstat command.

Job submission status and job progress file can be found in the file:

$CERESHOME/clouds/CER4.1-4.3P4/rcf/pcf/summary/CER4.1-4.3P4_$SS4_1\_$PS4_1\_$CC4_1.201203.summary

Note:  A file listing of expected output for each Clouds PGE testing can be found in the following file:

$CERESHOME/clouds/data_exp/out_description3P4.txt

### Exit Codes

All CER4.1-4.3P4 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.

### Daily QC Processor Test Summary

| PGE Number | PGE Name | Test Case | Run Time (mm:ss) | Disk Storage (MB) | Memory (MB) |
| --- | --- | --- | --- | --- | --- |
| CER4.1-4.3P4 | Monthly QC Processor | NPP | 00:20 | 350 | 374 |

## Evaluation Procedures

### Log and Status File Results

The Log and Status files are created by the Toolkit and are located in the directory $CERESHOME/clouds/runlogs after the PGE has been executed.  The comparisons of the Log and status files with their expected outputs are handled in Section 26.2.3.

### Metadata Evaluation

Metadata files for this PGE are created at runtime and are located with their corresponding output files.  The comparisons of the metadata files with their expected results are handled in Section 26.2.3.

### Execution of Comparison Software

The evaluation software for this Subsystem will compare the ASDC generated output with the expected output included with this delivery package. To run the comparison software, execute the following commands:

NPP Test Case:

cd $CERESHOME/clouds/CER4.1-4.3P4/rcf

source CER4.1-4.env

$CERESHOME/clouds/test_suites/bin/CER4.1-4.Validate.pl CER4.1-4.3P4 2

### Evaluation of Comparison Software Output

See Appendix D for a description of the output from the Comparison Software.

## Solutions to Possible Problems

- Output files are opened with Status = NEW.  If any of these files exist when the generating PGE is executed, the PGE will fail.  These files must be removed before any attempt is made to re-run any of the PGEs after the initial run is made.  The Toolkit Log files also need to be deleted before each run to be consistent with the expected output.  The specific problems can generally be found in the LogReport and/or LogStatus files.  NOTE:  For testing purposes only, if the test cases must be re-run, you must first cleanup the PCF files generated from previous runs as shown below.

cd $CERESHOME/clouds/CER4.1-4.3P4/rcf

source CER4.1-4.env

$CERESHOME/clouds/CER4.1-4.3P4/rcf/Run.CER4.1-4.Cleanup.pl 201203

Please contact Subsystem Lead for assistance if the cleanup and test cases re-run are unsuccessful.

Many problems encountered during compilation, linking, and execution are due to incorrect environment configuration.  Generally, these problems make themselves readily apparent via compiler errors or termination of the program during the initialization stage during the first few seconds of execution.

Most errors encountered during PCF generation will provide a diagnostic as to the problem.  If problems persist, check for the presence of all the mandatory input files and stage if necessary or contact the analyst.

Acronyms and Abbreviations

ASCII	American Standard Code Information Interchange

ASDC	Atmospheric Science Data Center

ATBD	Algorithm Theoretical Basis Document

AVHRR	Advanced Very High Resolution Radiometer

CERES	Clouds and the Earth’s Radiant Energy System

CERESlib	CERES library

CID	Cloud Imager Data

CRH	Clear Radiance History

DAAC	Distributed Active Archive Center

DAO	Data Assimilation Office

EOS	Earth Observing System

EOS-AM	EOS Morning Crossing Mission

EOS-PM	EOS Afternoon Crossing Mission

ERBE	Earth Radiation Budget Experiment

ERBS	Earth Radiation Budget Satellite

FOV	Field-of-View

F90	Fortran 90

IES	Instrument Earth Scans

ISCCP	International Satellite Land Surface Climatology Project

IVT	Instrument Validation Tape

LaTIS	Langley TRMM Information System

MCF	Metadata Control File

MOA	Meteorological, Ozone, and Aerosol

MODIS	Moderate-Resolution Imaging Spectroradiometer

NASA	National Aeronautics and Space Administration

NOAA	National Oceanic and Atmospheric Administration

PCF	Process Control File

PGE	Product Generation Executives

PGS	Product Generation System

PSF	Point Spread Function

QC	Quality Control

SCF	Science Computing Facility

SGE	Sun Grid Engine

SMF	Status Message File

SSAI	Science Systems and Applications, Inc.

SSF	Single Scanner Footprint TOA and Surface Fluxes, Clouds

SURFMAP	SURFace MAP

TOA	Top-of-the-atmosphere

TRMM	Tropical Rainfall Measuring Mission

VIRS	Visible and Infrared System

Directory Structure Diagrams

CERES clouds ancillary CER4.1-4.1P6 static BDM CALIB Terra CER_EANC CER_ECS StartUp Aqua GEO-ISCCP Terra TRMM CER_EDI CER_ELR CER_EM CER_FANC CO2 CO2Multi footprint MCRS Meta Tables Vint CER4.1-4.1P6 bin lib lib src avhrr cloudsCommon cloudsHDF co2 mcrs modisGeoL1B modisRadExtendL1B modisRadSSL1B modisRAerosolL2 vint virs welch rcf AncBin pcf src footprint retrieval test_suites bin footprint scripts src footprint SSFA_Compare SSF_Compare CER4.1-4.2P4 bin rcf AncBin pcf src ProduceDB ReadQC UpdateQC test_suites bin scripts CER4.1-4.2P5 bin rcf AncBin pcf src UpdateCRH0063SF UpdateCRH0063SFSC UpdateCRH0124SC UpdateCRH0124SF UpdateCRH0160SF UpdateCRH0213SF test_suites bin scripts CER4.1-4.3P3 bin rcf AncBin pcf src ProduceMonthlyQC test_suites bin scripts data Cookie CRH_Update ECS-OA0063SFm ECS-OA0063SFSCm ECS-OA0124SCm ECS-OA0124SFm ECS-OA0160SFm ECS-OA0213SFm ECV ECVS EQCDB EQCDG EQCDS EQCHB EQCHG EQCMB EQCMG FQC scr SSF_Int data_exp CER4.1-4.1P6 data support CER4.1-4.2P4 data support CER4.1-4.2P5 data support CER4.1-4.3P3 data support runlogs CER4.1-1P6_2P5 sge_logs test_suites bin footprint scr

File Description Tables

Production Scripts

| Table C.1-1. Production Scripts |
| --- |
| File Name | Format | Description |
| CER4.1-4.PCFGen | ASCII | Generic C-Shell script for PCF generation |
| CER4.1-4.PCFGen.pl | ASCII | Generic PERL script for PCF generation |
| CER4.1-4.Tokens | ASCII | Generic C-Shell script for PCF generation |
| CER4.1-4.Tokens.pl | ASCII | Generic PERL script for PCF generation |
| CER4.1-4.env | ASCII | Generic C-Shell script for PCF generation |
| Run.CER4.1-4.Cleanup | ASCII | Generic C-Shell cleanup script |
| Run.CER4.1-4.Cleanup.pl | ASCII | Generic PERL cleanup script |
| Run.CER4.1-4.MailSummary | ASCII | Generic C-Shell mail script |
| Run.CER4.1-4.MailSummary.pl | ASCII | Generic PERL mail script |
| CER4.1-4.0P1.PCFGen | ASCII | C-Shell script to generate PCFile for PGE |
| CER4.1-4.1P1.PCFGen | ASCII | C-Shell script to generate PCFile for PGE |
| CER4.1-4.1P2.PCFGen | ASCII | C-Shell script to generate PCFile for PGE |
| CER4.1-4.1P3.PCFGen | ASCII | C-Shell script to generate PCFile for PGE |
| CER4.1-4.1P4.PCFGen | ASCII | C-Shell script to generate PCFile for PGE |
| CER4.1-4.1P5.PCFGen | ASCII | C-Shell script to generate PCFile for PGE |
| CER4.1-4.1P6.PCFGen.pl | ASCII | PERL script to generate PCFile for PGE |
| CER4.1-4.2P1.PCFGen | ASCII | C-Shell script to generate PCFile for PGE |
| CER4.1-4.2P2.PCFGen | ASCII | C-Shell script to generate PCFile for PGE |
| CER4.1-4.2P3.PCFGen | ASCII | C-Shell script to generate PCFile for PGE |
| CER4.1-4.2P4.PCFGen.pl | ASCII | PERL script to generate PCFile for PGE |
| CER4.1-4.2P5.PCFGen.pl | ASCII | PERL script to generate PCFile for PGE |
| CER4.1-4.3P1.PCFGen | ASCII | C-Shell script to generate PCFile for PGE |
| CER4.1-4.3P2.PCFGen | ASCII | C-Shell script to generate PCFile for PGE |
| CER4.1-4.3P3.PCFGen.pl | ASCII | PERL script to generate PCFile for PGE |
| CER4.1-4.0P1.PCFGen.IFile | ASCII | C-Shell script to generate the ASCII input file |
| CER4.1-4.1P1.PCFGen.IFile | ASCII | C-Shell script to generate the ASCII input file |
| CER4.1-4.1P2.PCFGen.IFile | ASCII | C-Shell script to generate the ASCII input file |
| CER4.1-4.1P3.PCFGen.IFile | ASCII | C-Shell script to generate the ASCII input file |
| CER4.1-4.1P4.PCFGen.IFile | ASCII | C-Shell script to generate the ASCII input file |
| CER4.1-4.1P5.PCFGen.IFile | ASCII | C-Shell script to generate the ASCII input file |
| CER4.1-4.2P1.PCFGen.IFile | ASCII | C-Shell script to generate the ASCII input file |
| CER4.1-4.2P2.PCFGen.IFile | ASCII | C-Shell script to generate the ASCII input file |
| CER4.1-4.2P3.PCFGen.IFile | ASCII | C-Shell script to generate the ASCII input file |
| CER4.1-4.3P1.PCFGen.IFile | ASCII | C-Shell script to generate the ASCII input file |
| CER4.1-4.3P2.PCFGen.IFile | ASCII | C-Shell script to generate the ASCII input file |
| CER4.1-4.0P1.PCFGen.OFile | ASCII | C-Shell script to generate PCFile for PGE |
| CER4.1-4.1P1.PCFGen.OFile | ASCII | C-Shell script to generate PCFile for PGE |
| CER4.1-4.1P2.PCFGen.OFile | ASCII | C-Shell script to generate PCFile for PGE |
| CER4.1-4.1P3.PCFGen.OFile | ASCII | C-Shell script to generate PCFile for PGE |
| CER4.1-4.1P4.PCFGen.OFile | ASCII | C-Shell script to generate PCFile for PGE |
| CER4.1-4.1P5.PCFGen.OFile | ASCII | C-Shell script to generate PCFile for PGE |
| CER4.1-4.1P6.PCFGen.OFile.pl | ASCII | PERL script to generate PCFile for PGE |
| CER4.1-4.2P1.PCFGen.OFile | ASCII | C-Shell script to generate PCFile for PGE |
| CER4.1-4.2P2.PCFGen.OFile | ASCII | C-Shell script to generate PCFile for PGE |
| CER4.1-4.2P3.PCFGen.OFile | ASCII | C-Shell script to generate PCFile for PGE |
| CER4.1-4.2P4.PCFGen.OFile.pl | ASCII | PERL script to generate PCFile for PGE |
| CER4.1-4.2P5.PCFGen.OFile.pl | ASCII | PERL script to generate PCFile for PGE |
| CER4.1-4.3P1.PCFGen.OFile | ASCII | C-Shell script to generate PCFile for PGE |
| CER4.1-4.3P2.PCFGen.OFile | ASCII | C-Shell script to generate PCFile for PGE |
| CER4.1-4.3P3.PCFGen.OFile.pl | ASCII | PERL script to generate PCFile for PGE |
| Run.CER4.1-4.0P1 | ASCII | C-Shell script to run PGE |
| Run.CER4.1-4.0P1. RenameMonth | ASCII | C-Shell script for running part of PGE CER4.1-4.0P1 |
| Run.CER4.1-4.0P1.RenameVIRS | ASCII | C-Shell script for running part of PGE CER4.1-4.0P1 |
| Run.CER4.1-4.0P1.SnowIce | ASCII | C-Shell script for running part of PGE CER4.1-4.0P1 |
| Run.CER4.1-4.0P1.SubsetMonth | ASCII | C-Shell script for running part of PGE CER4.1-4.0P1 |
| Run.CER4.1-4.1P1 | ASCII | C-Shell script to run PGE |
| Run.CER4.1-4.1P1.retrieval | ASCII | C-Shell script for running part of PGE CER4.1-4.1P1 |
| Run.CER4.1-4.1P1.footprint | ASCII | C-Shell script for running part of PGE CER4.1-4.1P1 |
| Run.CER4.1-4.1P2 | ASCII | C-Shell script to run PGE |
| Run.CER4.1-4.1P2.retrieval | ASCII | C-Shell script for running part of PGE CER4.1-4.1P2 |
| Run.CER4.1-4.1P2.footprint | ASCII | C-Shell script for running part of PGE CER4.1-4.1P2 |
| Run.CER4.1-4.1P3 | ASCII | C-Shell script to run PGE |
| Run.CER4.1-4.1P3.retrieval | ASCII | C-Shell script for running part of PGE CER4.1-4.1P3 |
| Run.CER4.1-4.1P3.footprint | ASCII | C-Shell script for running part of PGE CER4.1-4.1P3 |
| Run.CER4.1-4.1P4 | ASCII | C-Shell script to run PGE |
| Run.CER4.1-4.1P4.retrieval | ASCII | C-Shell script for running part of PGE CER4.1-4.1P4 |
| Run.CER4.1-4.1P4.footprint | ASCII | C-Shell script for running part of PGE CER4.1-4.1P4 |
| Run.CER4.1-4.1P5 | ASCII | C-Shell script to run PGE |
| Run.CER4.1-4.1P5.retrieval | ASCII | C-Shell script for running part of PGE CER4.1-4.1P5 |
| Run.CER4.1-4.1P5.footprint | ASCII | C-Shell script for running part of PGE CER4.1-4.1P5 |
| Run.CER4.1-4.1P6.pl | ASCII | PERL script to run PGE |
| Run.CER4.1-4.1P6.retrieval.pl | ASCII | PERL script for running part of PGE CER4.1-4.1P6 |
| Run.CER4.1-4.1P6.footprint.pl | ASCII | PERL script for running part of PGE CER4.1-4.1P6 |
| Run.CER4.1-4.2P1 | ASCII | C-Shell script to run PGE |
| Run.CER4.1-4.2P1.DailyBinned | ASCII | C-Shell script for running part of PGE CER4.1-4.2P1 |
| Run.CER4.1-4.2P1.SCOOL | ASCII | C-Shell script for running part of PGE CER4.1-4.2P1 |
| Run.CER4.1-4.2P1.UpdateCRH | ASCII | C-Shell script for running part of PGE CER4.1-4.2P1 |
| Run.CER4.1-4.2P1.UpdateQC | ASCII | C-Shell script for running part of PGE CER4.1-4.2P1 |
| Run.CER4.1-4.2P2 | ASCII | C-Shell script to run PGE |
| Run.CER4.1-4.2P2.DailyBinned | ASCII | C-Shell script for running part of PGE CER4.1-4.2P2 |
| Run.CER4.1-4.2P2.SCOOL | ASCII | C-Shell script for running part of PGE CER4.1-4.2P2 |
| Run.CER4.1-4.2P2.UpdateCRH | ASCII | C-Shell script for running part of PGE CER4.1-4.2P2 |
| Run.CER4.1-4.2P2.UpdateQC | ASCII | C-Shell script for running part of PGE CER4.1-4.2P2 |
| Run.CER4.1-4.2P3 | ASCII | C-Shell script to run PGE |
| Run.CER4.1-4.2P3.DailyBinned | ASCII | C-Shell script for running part of PGE CER4.1-4.2P3 |
| Run.CER4.1-4.2P3.SCOOL | ASCII | C-Shell script for running part of PGE CER4.1-4.2P3 |
| Run.CER4.1-4.2P3.UpdateCRH | ASCII | C-Shell script for running part of PGE CER4.1-4.2P3 |
| Run.CER4.1-4.2P3.UpdateQC | ASCII | C-Shell script for running part of PGE CER4.1-4.2P3 |
| Run.CER4.1-4.2P4.pl | ASCII | PERL script to run PGE |
| Run.CER4.1-4.2P4. DailyBinned.pl | ASCII | PERL script for running part of PGE CER4.1-4.2P4 |
| Run.CER4.1-4.2P4.SCOOL.pl | ASCII | PERL script for running part of PGE CER4.1-4.2P4 |
| Run.CER4.1-4.2P4.UpdateQC.pl | ASCII | PERL script for running part of PGE CER4.1-4.2P4 |
| Run.CER4.1-4.2P5.pl | ASCII | PERL script to run PGE |
| Run.CER4.1-4.2P5. UpdateCRH0063SF.pl | ASCII | PERL script for running part of PGE CER4.1-4.2P5 |
| Run.CER4.1-4.2P5. UpdateCRH0063SFSC.pl | ASCII | PERL script for running part of PGE CER4.1-4.2P5 |
| Run.CER4.1-4.2P5. UpdateCRH0160SF.pl | ASCII | PERL script for running part of PGE CER4.1-4.2P5 |
| Run.CER4.1-4.2P5. UpdateCRH0213SF.pl | ASCII | PERL script for running part of PGE CER4.1-4.2P5 |
| Run.CER4.1-4.2P5. UpdateCRH0124SF.pl | ASCII | PERL script for running part of PGE CER4.1-4.2P5 |
| Run.CER4.1-4.2P5. UpdateCRH0124SC.pl | ASCII | PERL script for running part of PGE CER4.1-4.2P5 |
| Run.CER4.1-4.3P1 | ASCII | C-Shell script to run PGE |
| Run.CER4.1-4.3P2 | ASCII | C-Shell script to run PGE |
| Run.CER4.1-4.3P3.pl | ASCII | PERL script to run PGE |

Executables

| Table C.2-1. Executables1 |
| --- |
| File Name | Format | Description |
| Exe.CER4.1-4.0P1.SnowIce | Binary | Snow and Ice Processor executable |
| Exe.CER4.1-4.0P1.RenameVIRS | Binary | Renaming VIRS file executable |
| Exe.CER4.1-4.1P1.retrieval | Binary | Cloud Retrieval executable |
| Exe.CER4.1-4.1P1.footprint | Binary | Convolution executable |
| Exe.CER4.1-4.1P2.retrieval | Binary | Cloud Retrieval executable |
| Exe.CER4.1-4.1P2.footprint | Binary | Convolution executable |
| Exe.CER4.1-4.1P3.retrieval | Binary | Cloud Retrieval executable |
| Exe.CER4.1-4.1P3.footprint | Binary | Convolution executable |
| Exe.CER4.1-4.1P4.retrieval | Binary | Cloud Retrieval executable |
| Exe.CER4.1-4.1P4.footprint | Binary | Convolution executable |
| Exe.CER4.1-4.1P5.retrieval | Binary | Cloud Retrieval executable |
| Exe.CER4.1-4.1P5.footprint | Binary | Convolution executable |
| CER4.1-4.1P6.retrieval_$CPUTYPE.exe | Binary | Cloud Retrieval executable |
| CER4.1-4.1P6.footprint_$CPUTYPE.exe | Binary | Convolution executable |
| Exe.CER4.1-4.2P1.DailyBinnedAqua | Binary | Daily Binned QC Report executable |
| Exe.CER4.1-4.2P1.ReadQCAqua | Binary | QC Read executable |
| Exe.CER4.1-4.2P1.UpdateCRH | Binary | Cloud Retrieval executable |
| Exe.CER4.1-4.2P1.UpdateQCAqua | Binary | Daily QC File Generator executable |
| Exe.CER4.1-4.2P2.DailyBinned | Binary | Daily Binned QC Report executable |
| Exe.CER4.1-4.2P2.ReadQC | Binary | QC Read executable |
| Exe.CER4.1-4.2P2.UpdateCRH | Binary | Cloud Retrieval executable |
| Exe.CER4.1-4.2P2.UpdateQC | Binary | Daily QC File Generator executable |
| Exe.CER4.1-4.2P3.DailyBinnedAqua | Binary | Daily Binned QC Report executable |
| Exe.CER4.1-4.2P3.ReadQCAqua | Binary | QC Read executable |
| Exe.CER4.1-4.2P3.UpdateCRH | Binary | Cloud Retrieval executable |
| Exe.CER4.1-4.2P3.UpdateQCAqua | Binary | Daily QC File Generator executable |
| CER4.1-4.2P4.DailyBinned_ $CPUTYPE.exe | Binary | Daily Binned QC Report executable |
| CER4.1-4.2P4.ReadQC_$CPUTYPE.exe | Binary | QC Read executable |
| CER4.1-4.2P4.UpdateQC_ $CPUTYPE.exe | Binary | Daily QC File Generator executable |
| CER4.1-4.2P5.UpdateCRH0063SF_ $CPUTYPE.exe | Binary | Cloud Retrieval executable |
| CER4.1-4.2P5.UpdateCRH0063SFSC_ $CPUTYPE.exe | Binary | Cloud Retrieval executable |
| CER4.1-4.2P5.UpdateCRH0160SF_ $CPUTYPE.exe | Binary | Cloud Retrieval executable |
| CER4.1-4.2P5.UpdateCRH0213SF_ $CPUTYPE.exe | Binary | Cloud Retrieval executable |
| CER4.1-4.2P5.UpdateCRH0124SF_ $CPUTYPE.exe | Binary | Cloud Retrieval executable |
| CER4.1-4.2P5.UpdateCRH0124SC_ $CPUTYPE.exe | Binary | Cloud Retrieval executable |
| Exe.CER4.1-4.3P1.ProduceMonthlyQC | Binary | Monthly QC File Generator executable |
| Exe.CER4.1-4.3P2.ProduceMonthlyQC | Binary | Monthly QC File Generator executable |
| CER4.1-4.3P3.ProduceMonthlyQC_ $CPUTYPE.exe | Binary | Monthly QC File Generator executable |
| 1. These files will be generated on execution of Subsystem software and are not included in the tar file. |

Status Message Files (SMF)

Table C.3-1.  Status Message Files

| File Name | Format | Description |
| --- | --- | --- |
| CERES_25450 | ASCII | Status Message File for Subsystem 4.1 - 4.3 |
| CERES_25460 | ASCII | Status Message File for Subsystem 4.1 - 4.3 |
| FOOTPRINT_25500 | ASCII | Status Message File for Subsystem 4.4 |

Processing Control Files (PCF) and Metadata Control Files (MCF)

The Process Control Files are not included in the Software Delivery Package.  They will be created by the PCF generator scripts.

| Table C.4-1. Metadata Control Files |
| --- |
| File Name | Format | Description |
| CECRHUAC.MCF | ODL | MCF for Update CRH files |
| CECRH_AC.MCF | ODL | MCF for CRH files |
| CECVS_AC.MCF | ODL | MCF For Subset CloudVis files |
| CECV__AC.MCF | ODL | MCF For CloudVis files |
| CEICE_AC.MCF | ODL | MCF For Ice Map |
| CEIPD_AC.MCF | ODL | MCF For Cookiedough files |
| CEQCB_AC.MCF | ODL | MCF for Cloud Retrieval Binary QC files |
| CEQCS_AC.MCF | ODL | MCF for Cloud Retrieval S’COOL files |
| CEQCDVAC.MCF | ODL | MCF for Cloud Retrieval Daily binned QC files |
| CEQCD_AC.MCF | ODL | MCF for Cloud Retrieval Daily QC files |
| CEQCMBAC.MCF | ODL | MCF for Cloud Retrieval Monthly binned QC files |
| CEQCMGAC.MCF | ODL | MCF for Cloud Retrieval Monthly gridded QC files |
| CEQCV_AC.MCF | ODL | MCF for Cloud Retrieval binned QC files |
| CESNOWAC.MCF | ODL | MCF For Snow Map |
| CFQCI_AB.MCF | ODL | MCF for Convolution ASCII QC Report |
| CFQC__AB.MCF | ODL | MCF for Convolution Binary QC Report |
| CFSSFIAB.MCF | ODL | MCF File for Intermediate SSF |
| CFSSFAAB.MCF | ODL | MCF for the Intermediate SSFA |

| Table C.4-2. Process Control Files1 |
| --- |
| File Name | Format | Description |
| CER4.1-4.0P1_PCF_CERES_NSIDC_000000. 19980105 | ASCII | Process Control File template for Snow and Ice Processor |
| CER4.1-4.0P1_PCFin_CERES_NSIDC_000000. 19980105 | ASCII | ASCII file created by the ASCII file generator to be used by the Snow and Ice Processor’s PCF generator |
| CER4.1-4.1P1_PCF_TRMM-PFM-VIRS_SSIT_000000.1998010516 | ASCII | Process Control File template for Main Processor |
| CER4.1-4.1P1_PCFin_TRMM-PFM-VIRS_SSIT_000000.1998010516 | ASCII | ASCII file created by the ASCII file generator to be used by the Main Processor’s PCF generator |
| CER4.1-4.1P1_PCF_TRMM-PFM-VIRS_SubsetSSIT_000000.1998010516 | ASCII | Process Control File template for Main Processor (Subset Mode) |
| CER4.1-4.1P1_PCFin_TRMM-PFM-VIRS_SubsetSSIT_000000.1998010516 | ASCII | ASCII file created by the ASCII file generator to be used by the Main Processor’s PCF generator (Subset Mode) |
| CER4.1-4.1P1_PCF_Terra-FM1+FM2_MODIS_SSIT_000000. 2000062316 | ASCII | Process Control File template for Main Processor |
| CER4.1-4.1P1_PCFin_Terra-FM1+FM2_MODIS_SSIT_000000. 2000062316 | ASCII | ASCII file created by the ASCII file generator to be used by the Main Processor’s PCF generator |
| CER4.1-4.1P1_PCF_Terra-FM1+FM2_MODIS_SubsetSSIT_000000. 2000062316 | ASCII | Process Control File template for Main Processor |
| CER4.1-4.1P1_PCFin_Terra-FM1+FM2_MODIS_SubsetSSIT_000000. 2000062316 | ASCII | ASCII file created by the ASCII file generator to be used by the Main Processor’s PCF generator |
| CER4.1-4.1P2_PCF_Terra-FM1+FM2_MODIS_SSIT_000000. 2000062316 | ASCII | Process Control File template for Main Processor |
| CER4.1-4.1P2_PCFin_Terra-FM1+FM2_MODIS_SSIT_000000. 2000062316 | ASCII | ASCII file created by the ASCII file generator to be used by the Main Processor’s PCF generator |
| CER4.1-4.1P3_PCF_Aqua-FM3+FM4_MODIS_SSIT_000000. 2000062316 | ASCII | Process Control File template for Main Processor |
| CER4.1-4.1P3_PCFin_Aqua-FM3+FM4_MODIS_SSIT_000000. 2000062316 | ASCII | ASCII file created by the ASCII file generator to be used by the Main Processor’s PCF generator |
| CER4.1-4.1P4_PCF_Terra-FM1+FM2_MODIS_V005_000000. 2005060717 | ASCII | Process Control File template for Main Processor |
| CER4.1-4.1P4_PCFin_Terra-FM1+FM2_MODIS_V005_000000. 2005060717 | ASCII | ASCII file created by the ASCII file generator to be used by the Main Processor’s PCF generator |
| CER4.1-4.1P5_PCF_Aqua-FM3+FM4_MODIS_V005_000000. 2005060717 | ASCII | Process Control File template for Main Processor |
| CER4.1-4.1P5_PCFin_Aqua-FM3+FM4_MODIS_V005_000000. 2005060717 | ASCII | ASCII file created by the ASCII file generator to be used by the Main Processor’s PCF generator |
| CER4.1-4.1P6_PCF_Aqua-FM3+FM4-MODIS_SSIT_000000.2007070703 | ASCII | Process Control File template for Main Processor |
| CER4.1-4.1P6_PCF_Terra-FM1+FM2-MODIS_SSIT_000000.2007070703 | ASCII | Process Control File template for Main Processor |
| CER4.1-4.2P1_PCF_TRMM-PFM-VIRS_SSIT_000000.19980105 | ASCII | Process Control File template for Clear Sky Update Processor |
| CER4.1-4.2P1_PCFin_TRMM-PFM-VIRS_SSIT_000000.19980105 | ASCII | ASCII file created by the ASCII file generator to be used by the Clear Sky Update Processor’s PCF generator |
| CER4.1-4.2P2_PCF_TRMM-PFM-VIRS_SSIT_000000.19980105 | ASCII | Process Control File template for Clear Sky Update Processor |
| CER4.1-4.2P2_PCFin_TRMM-PFM-VIRS_SSIT_000000.19980105 | ASCII | ASCII file created by the ASCII file generator to be used by the Clear Sky Update Processor’s PCF generator |
| CER4.1-4.2P3_PCF_Aqua-MODIS_V005_000000.20050607 | ASCII | Process Control File template for Clear Sky Update Processor |
| CER4.1-4.2P3_PCFin_Aqua-MODIS_V005_000000.20050607 | ASCII | ASCII file created by the ASCII file generator to be used by the Clear Sky Update Processor’s PCF generator |
| CER4.1-4.2P3_PCF_Terra-MODIS_V005_000000.20050607 | ASCII | Process Control File template for Clear Sky Update Processor |
| CER4.1-4.2P3_PCFin_Terra-MODIS_V005_000000.20050607 | ASCII | ASCII file created by the ASCII file generator to be used by the Clear Sky Update Processor’s PCF generator |
| CER4.1-4.2P4_PCF_Aqua- MODIS_SSIT_000000.20070707 | ASCII | Process Control File template for Daily QC Processor |
| CER4.1-4.2P4_PCF_Terra- MODIS_SSIT_000000.20070707 | ASCII | Process Control File template for Daily QC Processor |
| CER4.1-4.2P5_PCF_Aqua- MODIS_SSIT_000000.20070707 | ASCII | Process Control File template for ClearSky Update Processor |
| CER4.1-4.2P5_PCF_Terra- MODIS_SSIT_000000.20060715 | ASCII | Process Control File template for ClearSky Update Processor |
| CER4.1-4.3P3_PCF_Aqua- MODIS_SSIT_000000.200707 | ASCII | Process Control File template for Monthly QC Processor |
| CER4.1-4.3P3_PCF_Terra- MODIS_SSIT_000000.200707 | ASCII | Process Control File template for Monthly QC Processor |
| CER4.1-4.#P3_PCFin_Terra-MODIS_SSIT_000000.200607 | ASCII | ASCII file created by the ASCII file generator to be used by the Monthly QC Processor’s PCF generator |
| 1. These files will be generated on execution of Subsystem software and are not included in the tar file. |

HDF Read Software

There is no HDF read software associated with the delivered PGEs.

Ancillary Input Data

| Table C.6-1. Ancillary Input Data |
| --- |
| File Name | Format | Description |
| BDM/CER_EAI_BDM0063_015000.epoch | Binary | Bi-directional Model, 0.63 |
| BDM/CER_EAI_BDM0160_015000.epoch | Binary | Bi-directional Model, 1.6 |
| BDM/CER_EAI_DM0063_<SAT>-<IMAG>_015000.epoch | Binary | Directional Model, 0.63 micron |
| BDM/CER_EAI_DM0160_<SAT>-<IMAG>_015000.epoch | Binary | Directional Model, 1.6 micron |
| BDM/CER_EAI_DM1663_<SAT>-<IMAG>_015000.epoch | Binary | Ratio Directional Model, 1.6/0.63 |
| BDM/CER_EAI_TOAREFALBSIMM0063_015000. epoch | Binary | Snow and Ice Reflectance Model for 0.6m summer |
| BDM/CER_EAI_TOAREFALBSIMM0160S_015000. epoch | Binary | Snow and Ice Reflectance Model for 1.6m for summer |
| BDM/CER_EAI_TOAREFALBSIMM0160W_015000. epoch | Binary | Snow and Ice Reflectance Model for 1.6m for winter |
| BDM/CER_EAI_TOAREFALBSIMM0375S_015000. epoch | Binary | Snow and Ice Reflectance Model for 3.75m for summer |
| BDM/CER_EAI_TOAREFALBSIMM0375W_015000. epoch | Binary | Snow and Ice Reflectance Model for 3.75m for winter |
| footprint/CER_FPARAM_CERES_<CC>.epoch1 | ASCII | Science inputs for footprint control |
| footprint/CER_FPSF_<SAT><INST><IMAG>.<CC>. epoch1 | ASCII | CERES point spread function for satellite/instrument/ and imager |
| footprint/CER_FDBin_<SAT>-<INST>-<IMAG>_000000.epoch | ASCII | File listing footprints to print |
| footprint/CER_FAOT063_CERES_<CC>.epoch1 | Binary | Stowe third generation 0.63 Look-up Table |
| footprint/CER_FAOT160_CERES_<CC>.epoch1 | Binary | Stowe third generation 1.60 Look-up Table |
| Tables/CER_EICF_<SAT>-<IMAG>_014000.epoch | ASCII | Imager Coefficients |
| Tables/CER_EICF_<SAT>-<IMAG>_014000.epoch | ASCII | Calibration File |
| Tables/CER_EIEASE_CERES_00003.epoch | Binary | File for polar sterographic to cartesian coordinates |
| Tables/CER_EPARAM_<IMAG>.epoch | ASCII | Science inputs for retrieval control |
| Tables/CER_EPCParamMap_015000.epoch | ASCII | Logical IDs for PCF generation |
| Tables/CER_ESCF_Stowe-0063_015000.epoch | Binary | Stowe 0.63 LUT |
| Tables/CER_ESCF_Stowe-0160_015000.epoch | Binary | Stowe 1.6 LUT |
| Tables/CER_ESCF_CERESThres_015000.epoch | ASCII | CERES Cloud Mask Thresholds |
| Tables/CER_ESCF_ChiThrTable_015000.epoch | ASCII | CERES Chi Thresholds |
| Tables/CER_ESCF_SubsetRegions_015000.epoch | ASCII | Subset CloudVis Regions |
| SCOOL/CER_ESCF_SCOOLRegions_011000. YYYYMM2 | ASCII | SCOOL Participant Locations for year YYYY and month MM |
| Vint/CER_EDM_<IMAG>.epoch | Binary | VINT Algorithm Input File |
| Vint/ERBEBDMreformatted.dat | ASCII | VINT Algorithm Input File |
| Vint/LNPWderiv.ch4.allvz.dy.dat | Binary | VINT Algorithm Input File |
| Vint/SkinTderiv.ch4.allvz.dy.dat | Binary | VINT Algorithm Input File |
| Vint/bdnnref.dat | Binary | VINT Algorithm Input File |
| Vint/channel2.coefs | Binary | VINT Algorithm Input File |
| Vint/channel3.coefs | Binary | VINT Algorithm Input File |
| Vint/channel4.coefs | Binary | VINT Algorithm Input File |
| Vint/channel5.coefs | Binary | VINT Algorithm Input File |
| Vint/dxalbmean.dat | ASCII | VINT Algorithm Input File |
| Vint/modelsnew.3.7.dat | Binary | VINT Algorithm Input File |
| Vint/modelsnew.dat | Binary | VINT Algorithm Input File |
| Vint/ratios1_6.dat | Binary | VINT Algorithm Input File |
| Vint/raybref.dat | Binary | VINT Algorithm Input File |
| Vint/table-invcld | ASCII | VINT Algorithm Input File |
| Vint/virs.corrk.coefs.1.interval | Binary | VINT Algorithm Input File |
| Vint/virs.corrk.coefs.5.intervals | ASCII | VINT Algorithm Input File |
| Vint/CER_ECOEFS_<IMAG>_CORRK.epoch | ASCII | VINT Algorithm Input File |
| Vint/all_dif_coefs | ASCII | VINT Algorithm Input File |
| Vint/CER_EMODEL_<IMAG>_0375.epoch | ASCII | VINT Algorithm Input File |
| Vint/nmodels.1.6.dat | ASCII | VINT Algorithm Input File |
| Vint/virsdir | ASCII | VINT Algorithm Input File |
| CO2/modisbnd.am1 | Binary | CO2 Slicing Algorithm input file |
| CO2/modisdry.am1 | Binary | CO2 Slicing Algorithm input file |
| CO2/modisozo.am1 | Binary | CO2 Slicing Algorithm input file |
| CO2/modiswco.am1 | Binary | CO2 Slicing Algorithm input file |
| CO2/modiswtl.am1 | Binary | CO2 Slicing Algorithm input file |
| CO2/modiswts.am1 | Binary | CO2 Slicing Algorithm input file |
| CER_ECS/CER_ECS-SOA0063m_<SAT>-<IMAG>_StartUp_015000.XXXXMM3 | Binary | Start-up CRH map for Albedo 0.63 mean |
| CER_ECS/CER_ECS-SOA0063s_015000.XXXXMM3 | Binary | Start-up CRH map for Albedo 0.63 std |
| CER_ECS/CER_ECS-SOA0160m_015000.XXXXMM3 | Binary | Start-up CRH map for Albedo 1.60 mean |
| CER_ECS/CER_ECS-SOA0160s_015000.XXXXMM3 | Binary | Start-up CRH map for Albedo 1.60 std |
| CER_ECS/CER_ECS-SOA1663m_015000.XXXXMM3 | Binary | Start-up CRH map for Albedo 1.6:0.63 ratio mean |
| CER_ECS/CER_ECS-SOA1663s_015000.XXXXMM3 | Binary | Start-up CRH map for Albedo 1.6:0.63 ratio Std |
| CER_ECS/StartUp/$SAT/CER_ECS-SOA????*m_ $SAT-$IMAG_StartUp_015000.XXXXMM | Binary | Start-up CRH map for Albedo ???? mean, * = (SC,SF, or SFSC) |
| CER_ECS/CER_ECS-SBT1080m_015000.XXXXMM3 | Binary | Start-up CRH map for Brightness Temperature 10.8 mean |
| CER_ECS/CER_ECS-SBT1080s_015000.XXXXMM3 | Binary | Start-up CRH map for Brightness Temperature 10.8 std |
| CER_EDI/CER_EDiCorrm_<MOA_SRC>_015000. XXXXMM3 | Binary | Diurnal correction model for MOA product. Dependent on MOA source. |
| CER_EDI/CER_EDiCorrs_<MOA_SRC>_015000. XXXXMM3 | Binary | Diurnal correction model for MOA product. Dependent on MOA source. |
| CER_EANC/CER_EH2O_CERES_00003.epoch | Binary | Percent Water Coverage |
| CER_EANC/CER_EIGBP_CERES_011000.epoch | Binary | IGPB Ecosystem Map |
| CER_EANC/CER_ELEV_CERES_00003.epoch | Binary | Surface Elevation Map |
| CER_EANC/CER_ETERR_CERES_00003.epoch | Binary | Terrain Characteristic Map |
| CER_EANC/CER_EMOAF_CERES_011000.epoch | Binary | MOA Water Flag |
| CER_EANC/CER_EMOAS_CERES_000004.epoch | Binary | MOA Scene Type |
| CER_EANC/CER_EMOAW_<MOA_SRC>_015000. epoch | Binary | MOA Water Percentage |
| CER_FANC/CER_FREFL_CERES_000005.epoch | ASCII | Reflect Algorithm Input File |
| CER_EANC/CER_WELCHMASK_<IMAG>_015000. epoch | Binary | Welch Algorithm Input File |
| CER_EANC/CER_WELCHTERR_015000.epoch | Binary | Welch Algorithm Input File |
| CER_EANC/CER_WELCHMASK_Old19Chan_ MODIS_015000.epoch | Binary | Welch Algorithm Input File |
| CER_EM/CER_EM0375_CERES_010000.XXXXMM3 | Binary | Emissivity Map Channel 3.75 |
| CER_EM/CER_EM1080_CERES_010000.XXXXMM3 | Binary | Emissivity Map Channel 10.80 |
| CER_EM/CER_EM1190_CERES_010000.XXXXMM3 | Binary | Emissivity Map Channel 11.90 |
| CALIB/Terra/CER_CALIB-0375_Terra-MODIS_015000.YYYYMM | ASCII | Terra calibration |
| 1. CC represents Configuration Code. 2. YYYYMM represents a specific year and month combination between 199801 and 199906. 3. XXXXMM represents a specific month without dependency on the year. |
| Table C.6-2. Ancillary Input Data for CER4.1-4.0P2 |
| File Name | Format | Description |
| Tables/CER_EIEASE_CERES_00003.epoch | Binary | File for polar sterographic to cartesian coordinates |
| Tables/CER_ENESDISIndex_CERES_00003.epoch | Binary |  |
| Tables/CER_EIGBP_CERES_011000.epoch | Binary |  |
| Tables/CER_ENESDISMesh16thIndex_CERES_00004.epoch | Binary |  |
| Meta/CESNOWAC.MCF | ASCII |  |
| Meta/CEICE_AC.MCF | ASCII |  |

Output Temporary Data Files (Production Results)

| Table C.7-1. Output Temporary Data Files1 |
| --- |
| File Name | Format | Description |
| CER_IPD_TRMM-VIRS_SSIT_000000.1998010516 | Binary | Imager data file containing pixel-level cloud property data |
| CER_IPD_TRMM-VIRS_SSIT_000000.1998010516.met | ODL | Metadata load file for imager data file |
| CER4.1-4.1P1_MCFScr_TRMM-PFM-VIRS_SSIT_000000.1998010516 | ASCII | Toolkit generated file used in reading metadata |
| CER_IPD_TRMM-VIRS_SubsetSSIT_000000.1998010516 | Binary | Imager data file containing pixel-level cloud property data |
| CER_IPD_TRMM-VIRS_SubsetSSIT_000000.1998010516.met | ODL | Metadata load file for imager data file |
| CER4.1-4.1P1_MCFScr_TRMM-PFM-VIRS_SubsetSSIT_000000.1998010516 | ASCII | Toolkit generated file used in reading metadata |
| CER_IPD_Terra-MODIS_SSIT_000000.2000062316 | Binary | Imager data file containing pixel-level cloud property data |
| CER_IPD_Terra-MODIS_SSIT_000000.2000062316.met | ODL | Metadata load file for imager data file |
| CER4.1-4.1P1_MCFScr_Terra-FM1+FM2-MODIS_SSIT_000000.2000062316 | ASCII | Toolkit generated file used in reading metadata |
| CER4.1-4.1P2_MCFScr_Terra-FM1+FM2-MODIS_SSIT_000000.2000062316 | ASCII | Toolkit generated file used in reading metadata |
| CER4.1-4.1P3_MCFScr_Aqua-FM3+FM4-MODIS_SSIT_000000.2000062316 | ASCII | Toolkit generated file used in reading metadata |
| CER_IPD_Terra-MODIS_SubsetSSIT_000000.2000062316 | Binary | Imager data file containing pixel-level cloud property data |
| CER_IPD_Terra-MODIS_SubsetSSIT_000000.2000062316.met | ODL | Metadata load file for imager data file |
| CER4.1-4.1P1_MCFScr_Terra-FM1+FM2-MODIS_SubsetSSIT_000000.2000062316 | ASCII | Toolkit generated file used in reading metadata |
| MCFWrite.temp | ASCII | Toolkit generated file used in writing metadata |
| pcxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx2 | Binary or ASCII | Toolkit generated work file |
| 1. These files will be generated on execution of Subsystem software and are not included in the tar file. 2. A 30-digit random number is generated by Toolkit to append after pc in naming its temporary files. |

Evaluation of Comparison Software Output

There are four phases run during the execution of the Comparison Software.  The progress of the program is shown on the screen during execution and should resemble:

Validating Data Products for <PGE>

.

Validating Metadata Files for <PGE>

.

Validating Support Files for <PGE>

.

Validating Log Files for <PGE>

.

Where <PGE> is the PGE being validated and the “.” indicates a series of files evaluated during that phase.  Data Products and Metadata files are those products produced by the subsystem. Support files are the PCF and its internal file. Log files are the Toolkit generated files.  For each successful comparison, a message is issued:

Level <N> Comparison Successful for <FILE>

where “Level <N>” indicates the first level of test which yielded a successful result and “<FILE>” is the file compared. The levels you may see are:

Level 1:  A flat binary compare between the generated and expected outputs was successful.

Level 2:  An ASCII file, such as a log file, cannot successfully pass a binary compare. A successful Level 2 comparison means that certain strings, such as date, time, and OS specific fields, have been removed from both the generated and expected outputs and the results successfully compared.

Level 3:  This level of comparison is provided for those support files, like the PCF, that may contain temporary file names generated by the Toolkit.  This level of comparison removes the temporary file names from the generated and expected outputs.

Level 4:  This level of comparison is used only to execute the software developed to compare Interim SSFs.

Level 5:  This level of comparison is used to execute software developed to compare supposedly identical HDF files.