Clouds and the Earth's Radiant Energy System

(CERES)

Data Management System

CERES ERBE-like Inversion to Instantaneous TOA Fluxes

and Averaging to Monthly TOA Fluxes

Subsystems 2.0 and 3.0

Release 8 Test Plan

Version 6

Primary Authors

Dale Walikainen
Jeremie Lande

Science Systems Applications Inc. (SSAI)

One Enterprise Parkway, Suite 200

Hampton, VA  23666

NASA Langley Research Center

Climate Science Branch

Science Directorate

21 Langley Boulevard

Hampton, VA  23681-2199

SW Delivered to CM: October 2018

Document Date:  October 2018

Document Revision Record

The Document Revision Record contains information pertaining to approved document changes.  The table lists the date the Software Configuration Change Request (SCCR) was approved, the Release and Version Number, the SCCR number, a short description of the revision, and the revised sections.  The document authors are listed on the cover.  The Head of the CERES Data Management Team approves or disapproves the requested changes based on recommendations of the Configuration Control Board.

| Document Revision Record |
| --- |
| SCCR Approval Date | Release/ Version Number | SCCR Number | Description of Revision | Section(s) Affected |
| 06/21/01 | R3V5 | 271 | Updated data date used for testing. | Sec. 3.0 |
|  |  |  | Updated command line options for CER2.2P1, CER2.3P1, and CER2.3P2 PCF generators. | Secs. 3.2.1.1, 3.3.1.1, & 3.4.1.1 |
|  |  |  | Updated directory structure diagram. | App. B |
|  |  |  | Added ERBE processing executable and ancillary input data files needed for ERBE processing. | App. C |
|  |  |  | Updated format to comply with standards. | All |
| 04/26/02 | R3V6 | 341 | Added new PGE CER2.4P1. | Sec. 5.0 |
|  |  |  | Added the reference and description to new PGE CER2.4P1. | Introduction |
|  |  |  | Updated Parent PGEs Table 2-1. | Sec. 2.1.3 |
|  |  |  | Modified CER2.2P1, CER2.3P1, and CER2.3P2 runtime parameter “spcor” to include new “M” option. | Secs. 2.2.1, 2.2.5, 3.2.1, & 4.2.1 |
|  |  |  | Added new environment variable “CC2_4”. | Secs. 2.2.2, 3.2.2, & 4.2.2 |
|  |  |  | Added new processor dependent data set from CER2.4P1 to inversion PGEs. | Secs. 2.3.4, 3.3.4, & 4.3.4 |
|  |  |  | Error message Table B-4 created for new PGE 2.4P1. | App. B |
|  |  |  | Added sample input file listing for CER2.4P1. | App. C |
|  |  |  | Updated format to comply with standards. | All |
| 04/17/03 | R4V1 | 432 | Changed test date from 200105 to 200210. | All |
|  |  |  | Added another test for PGE CER3.2P1 to generate a combined product with Terra and Aqua instruments. | Sec. 3.8 |
|  |  |  | Added ES-8 nadir files needed for input for executing CER3.2P1 FM1FM2. | Sec. 3.7.1 |
|  |  |  | Added CER3.2P1 direct comparison and three channel inter-comparison output files generated during execution. | Sec. 3.7.1.2 |
| 04/17/03 | R4V1 | 432 | Added the CER3.2P1 direct comparison web file evaluation. | Sec. 3.7.2.3.10 |
| (Cont’d) |  |  | Added the CER3.2P1 three channel inter-comparison web file evaluation. | Sec. 3.7.2.3.11 |
|  |  |  | Added CER2.4P1 spectral response trend output files generated during execution. | Sec. 3.2.1.2 |
|  |  |  | Added CER2.4P1 spectral response trend file evaluation. | Sec. 3.2.2.7 |
|  |  |  | Updated format to comply with standards. | All |
| 12/08/03 | R4V2 | 484 | Changed test date from 200105 to 200210. | All |
|  |  |  | Added another test for PGE CER3.2P1 to generate a combined product with Terra and Aqua instruments. | Sec. 3.8 |
|  |  |  | Added ES-8 nadir files needed for input for executing CER3.2P1 FM1+FM2. | Sec. 3.7.1 |
|  |  |  | Added CER3.2P1 direct comparison and three channel inter-comparison output files generated during execution. | Sec. 3.7.1.2 |
|  |  |  | Added the CER3.2P1 direct comparison web file evaluation. | Sec. 3.7.2.3.10 |
|  |  |  | Added the CER3.2P1 three channel inter-comparison web file evaluation. | Sec. 3.7.2.3.11 |
|  |  |  | Added CER2.4P1 spectral response trend output files generated during execution. | Sec. 3.2.1.2 |
|  |  |  | Added CER2.4P1 spectral response trend file evaluation. | Sec. 3.2.2.7 |
|  |  |  | Updated format to comply with standards. | All |
| 9/30/09 | R5V1 | 726 | Updated pathnames for new directory structure. | All |
|  |  |  | Added new tests for P4 executions. | All |
| 09/30/09 | R5V2 | 727 | Updated CER2.4P1’s compilation instructions. | Sec. 2.0 |
|  |  |  | Updated CER2.4P1 to handle Edition3 coefficients. | Sec. 3.2 |
|  |  |  | Updated Directory Structure Diagram. | App. B |
| 10/28/09 | R5V3 | 735 | Corrected & updated compilation instructions. | Sec. 2.0 |
|  |  |  | Updated CER3.1P1 & CER3.2P1 test & evaluation instructions. | Secs. 3.6 & 3.7 |
|  |  |  | Updated Directory Structure Diagram. | App. B |
| 10/28/09 | R5V4 | 734 | Corrected and updated compilation instructions | Sec. 2.0 |
|  |  |  | Updated CER2.2P1, CER2.3P1, and CER2.3P2 test and evaluation instructions. | Secs. 3.3, 3,4, & 3.5 |
|  |  |  | Updated Directory Structure. | App. B |
|  |  |  | Added FM1, FM3, FM4, and FM5 tests cases to CER2.2P1, CER2.3P1, and CER2.3P2 testing and evaluation. (07/12/2010) | Secs. 3.3, 3.4, & 3.5 |
|  |  |  | Modified command lines with “unlimit” and added quotes around _TestPlan_221001. (08/05/2010) | Secs. 3.1.1.2, 3.2.1.2, 3.3.1.2, 3.3.2.1, 3.4.1.2, 3.5.1.2, & 3.8.1.2 |
| 09/09/10 | R5V5 | 806 | Added test cases for CER2.4P1 and removed 3 sections in 3.2.2: Execution of SCCN Comparison Software, Execution of SCCD Comparison Software, and Spectral Response Trend File Evaluation. | Secs. 2.2.4 & 3.2.2.x |
| 11/25/09 | R6V1 | 740 | Upgraded all PGEs for AMI production environment: conversion of PCF generators and run scripts from c-shell to perl, updated all scripts to use DPO-like directory structure, created SGE test cases and renaming of executables to PGE_EXEC_ppc64.exe format. | All |
| 09/21/11 | R7V1 | 867 | Added notes to run tests on p6 and x86 platforms. | All |
|  |  |  | Added pcf log files as expected output. | Secs. 3.2.1.2 & 3.1.1.1 |
|  |  |  | Comparison software replaces diff command for evaluating the two major output files; “SCCD” and “SCCN.” | Secs. 3.2.2.3 & 3.2.2.4 |
|  |  |  | Added instructions to compile CER2.4P1 comparison code. | Sec. 2.2.4 |
|  |  |  | Replaced all instances of ppc64 with $CPUTYPE and added it to erbelike_lib.a. | Secs. 2.2, 3.3, 3.4, & 3.5 |
|  |  |  | Updated Test Cases to reflect 867 updates. | Secs. 3.3, 3.4, & 3.5 |
|  |  |  | Modified the “Introduction” paragraph. (11/29/2012) | Sec. 1.0 |
|  |  |  | Formatting issues were fixed. (11/29/2012) | All |
| 06/22/16 | R8V1 | 1144 | Added new PGE CER2.2P2. | Secs. 1.2.8, 2.2.7, & 3.8 |
|  |  |  | Updated Directory Structure. | App. B |
| 06/22/16 (Cont'd) | R8V1 | 1144 | Updated tables to reflect the addition of PGE CER2.2P2. | Tables C.1-1 & C.2-1 |
| 6/07/17 | R8V2 | 1262 | Removed p6 from CER2.1P1 testing. | Sec. 3.1.2.3 |
|  |  |  | Changed incorrect date. | Sec. 3.1.1.2 |
| 1/31/2018 | R8V3 | 1326 | Updated CER2.2P2 to unfilter LW channel radiances, removed JCT4 test cases, and added Baseline1-QC PRES8 for testing. | Sec. 3.8 |
|  |  |  | Updated compilation for new code. | Sec. 2.2.7 |
|  |  |  | Added … src/inv subdirectory to CER2.2P2 directory. | App. B |
| 5/9/2018 | R8V4 | 1356 | Added FM6 test cases for CER2.3P1, CER2.3P2, and CER3.1P1. | Secs. 3.4.1.1 #11, 3.5.1.1 #11, & 3.6.1.1 #8 |
|  |  |  | Additional modifications were also made. | Secs. 3.4.1, 3.4.1.2, 3.4.2.2, 3.4.2.3, 3.5.1, 3.5.1.2, 3.5.2.2, 3.5.2.3, 3.6.1.2, 3.6.2.2, 3.6.2.3.1, 3.6.2.3.2, & 3.6.2.3.3 |
| 5/9/2018 | R8V5 | 1330 | Updated CER2.4P1 test section for x86. | Sec. 3.2 |
|  |  |  | Removed Comparison code for CER2.4P1 and added “source” to compile_2.4P1.csh. | Sec. 2.2.4 |
| 9/25/18 | R8V6 | 1387 | Updated Test/Evaluation sections. | Secs. 3.3.1, 3.4.1, 3.5.1, & 3.8.1 |
|  |  |  | Replaced $PS2 with $PS2_0. | Entire Document |

Document Revision Record	ii

1.0	Introduction	1

1.1	Document Overview	1

1.2	Subsystem Overview	2

1.2.1	CERES ERBE-like Monthly Geo-Scene and Snow Map, and Longwave
and Albedo Thresholds	3

1.2.2	CERES ERBE-like Spectral Correction Coefficients and Spectral Responses	3

1.2.3	CERES ERBE-like Daily Inversion for a Single Instrument	3

1.2.3.1	CERES ERBE-like Daily Inversion Main-Processor for a Single Instrument	3

1.2.3.2	CERES ERBE-like ES-8 HDF-EOS Generator	3

1.2.3.3	CERES ERBE-like Inversion ES-8 GIF File Generator	3

1.2.4	CERES ERBE-like Monthly Inversion for the First Day of the Next Month	3

1.2.5	CERES ERBE-like Monthly Inversion for the Last Day of the Previous Month	3

1.2.6	CERES ERBE-like Monthly TOA Flux Averaging for a Single Instrument	3

1.2.7	CERES ERBE-like Monthly TOA Flux Averaging for Multiple Instruments	4

1.2.8	CERES ERBE-like Daily Inversion for FM6	4

1.2.8.1	CERES ERBE-like Daily Inversion Main-Processor for FM6	4

1.2.8.2	CERES ERBE-like ES-8 HDF-EOS Generator	4

2.0	Software and Data File Installation Procedures	5

2.1	Installation	5

2.2	Compilation	5

2.2.1	Compiling PRES8 Processor library	6

2.2.2	Compiling PGE 2.1P1	6

2.2.3	Compiling CER2.2P1	7

2.2.4	Compiling CER2.3P1 and CER2.3P2	8

2.2.5	Compiling PGE 2.4P1	8

2.2.6	Compiling PGE 3.1P1	8

2.2.7	Compiling PGE 3.2P1	9

2.2.8	Compiling PGE CER2.2P2	10

3.0	Test and Evaluation Procedures	11

3.1	CER2.1P1 CERES ERBE-like Monthly Geo-Scene and Snow Map, and Longwave
and Albedo Thresholds	11

3.1.1	Test Procedures	11

3.1.1.1	PCF Generator	11

3.1.1.2	Execution	12

3.1.1.3	Exit Codes	13

3.1.1.4	CER2.1P1 Test Summary	13

3.1.2	Evaluation Procedures	13

3.1.2.1	Log and Status File Results	13

3.1.2.2	Metadata Evaluation	13

3.1.2.3	Execution of Comparison Software	14

3.1.2.4	Evaluation of Comparison Software Output	14

3.1.3	Solutions to Possible Problems	14

3.2	CER2.4P1 CERES ERBE-like Spectral Response Functions and Correction
Coefficients	15

3.2.1	Test Procedures	15

3.2.1.1	Execution	15

3.2.1.2	Expected Output	16

3.2.1.3	Exit Codes	17

3.2.1.4	CER2.4P1 Test Summary	17

3.2.2	Evaluation Procedures	17

3.2.2.1	Log and Status File Results	17

3.2.2.2	Metadata Evaluation	18

3.2.2.3	Evaluation of SCCD	19

3.2.2.4	Evaluation of SCCN	20

3.2.3	Solutions to Possible Problems	20

3.3	CER2.2P1 CERES ERBE-like Daily Inversion for a Single Instrument	22

3.3.1	Stand-alone Test Procedures	22

3.3.1.1	Execution	23

3.3.1.2	Expected Output Files	26

3.3.1.3	Exit Codes	27

3.3.1.4	CER2.2P1 Test Summary	27

3.3.2	Evaluation Procedures	27

3.3.2.1	Log and Status File Results	27

3.3.2.2	Metadata Evaluation	28

3.3.2.3	Execution of EID-6 Comparison Software	28

3.3.2.4	Evaluation of EID-6 Comparison Software Output	28

3.3.2.5	Quality Control Data Evaluation	28

3.3.2.6	Execution of the HDF ES-8 Data Comparison Tool	29

3.3.2.7	Evaluation of ES-8 Nadir Comparison Software Output	29

3.3.3	Solutions to Possible Problems	29

3.4	CER2.3P1 CERES ERBE-like Monthly Inversion for the First Day of the
Next Month	30

3.4.1	Stand-alone Test Procedures	30

3.4.1.1	Execution	30

3.4.1.2	Expected Output Files	32

3.4.1.3	Exit Codes	33

3.4.1.4	CER2.3P1 Test Summary	33

3.4.2	Evaluation Procedures	33

3.4.2.1	Log and Status File Results	33

3.4.2.2	Metadata Evaluation	34

3.4.2.3	Comparison of CQCIX and EID6X	34

3.4.3	Solutions to Possible Problems	35

3.5	CER2.3P2 CERES ERBE-like Monthly Inversion for the Last Day of the
Previous Month	36

3.5.1	Stand-alone Test Procedures	36

3.5.1.1	Execution	36

3.5.1.2	Expected Output Files	38

3.5.1.3	Exit Codes	39

3.5.1.4	CER2.3P2 Test Summary	39

3.5.2	Evaluation Procedures	39

3.5.2.1	Log and Status File Results	39

3.5.2.2	Metadata Evaluation	39

3.5.2.3	Comparison of CQCIX and EIDX	40

3.5.2.4	Evaluation of EID-6 Comparison Software Output	40

3.5.3	Solutions to Possible Problems	41

3.6	CER3.1P1 CERES ERBE-like Monthly TOA Flux Averaging for a
Single Instrument	42

3.6.1	Stand-alone Test Procedures	42

3.6.1.1	Execution	42

3.6.1.2	Expected Output Files	45

3.6.1.3	Exit Codes	48

3.6.1.4	CER3.1P1 Test Summary	48

3.6.2	Evaluation Procedures	49

3.6.2.1	Log and Status File Results	49

3.6.2.2	Metadata Evaluation	49

3.6.2.3	Output Data Evaluation	49

3.6.2.3.1	Execution of HDF ES-4 Comparison Utility	49

3.6.2.3.2	Evaluation of HDF ES-4 Comparison Software	50

3.6.2.3.3	Evaluation of ES-4 GIF Files	50

3.6.3	Solutions to Possible Problems	50

3.7	CER3.2P1 CERES ERBE-like Monthly TOA Flux Averaging for Multiple
Instruments (current default: FM1+FM3)	52

3.7.1	Stand-alone Test Procedures	52

3.7.1.1	Execution	52

3.7.1.2	Expected Output Files	52

3.7.1.3	Exit Codes	54

3.7.1.4	CER3.2P1 Test Summary	54

3.7.2	Evaluation Procedures	55

3.7.2.1	Log and Status File Results	55

3.7.2.2	Metadata Evaluation	55

3.7.2.3	Output Data Evaluation	55

3.7.2.3.1	Execution of HDF ES-4 Comparison Utility	55

3.7.2.3.2	Evaluation of HDF ES-4 Comparison Software	56

3.7.2.3.3	Evaluation of ES-4 GIF Files	56

3.7.2.3.4	Evaluation of ES-4 Statistical Trend Files	56

3.7.3	Solutions to Possible Problems	57

3.8	CER2.2P2 CERES ERBE-like Daily Inversion for FM6	58

3.8.1	Stand-alone Test Procedure	58

3.8.1.1	Execution	58

3.8.1.2	Expected Output Files	59

3.8.1.3	Exit Codes	59

3.8.1.4	CER2.2P2 Test Summary	59

3.8.2	Evaluation Procedures	59

3.8.2.1	Log and Status File Results	59

3.8.2.2	ES-8 Comparison	59

3.8.2.3	Evaluation of ES-8 Comparison Software Output	60

3.8.3	Solutions to Possible Problems	60

Appendix A - Acronyms and Abbreviations	A-1

Appendix B - Directory Structure Diagram  (under $ERBELIKEHOME/erbelike)	B-1

Appendix C - File Description Tables	C-1

C.1	Production Scripts	C-1

C.2	Executables	C-3

C.3	Status Message Files	C-5

C.4	Processing Control Files (PCF) and Metadata Control Files (MCF)	C-5

C.5	HDF Read Software	C-8

C.6	Ancillary Input Data	C-9

C.7	Output Temporary Data Files (Production Results)	C-10

Table C.1-1.  Production Scripts ($ERBELIKEHOME/erbelike/CER*.*P*/rcf)	C-1

Table C.2-1.  Executables ($ERBELIKEHOME/erbelike/bin or CER*.*P*/bin)	C-3

Table C.3-1.  Status Message Files ($ERBELIKEHOME/erbelike/smf)	C-5

Table C.4-1.  Metadata Control Files ($ERBELIKEHOME/erbelike/mcf)	C-6

Table C.4-2.  Process Control Files ($ERBELIKEHOME/erbelike/CER*.*P*/rcf/pcf)	C-7

Table C.5-1.  ERBE-like Read Software Files ($ERBELIKEHOME/erbelike/src)	C-8

Table C.6-1.  Ancillary Input Data ($ERBELIKEHOME/erbelike/ancillary)	C-9

Table C.7-1.  Output Temporary Data Files ($ERBELIKEHOME/erbelike/
	CER*.*P*/data/scr)	C-10

# Introduction

CERES is a key component of EOS and NPP.  The first CERES instrument (PFM) flew on TRMM, four instruments are currently operating on the EOS Terra (FM1 and FM2) and Aqua (FM3 and FM4) platforms, and NPP (FM5) platform.  CERES measures radiances in three broadband channels:  a shortwave channel (0.3 - 5 m), a total channel (0.3 - 200 m), and an infrared window channel (8 - 12 m).  The last data processed from the PFM instrument aboard TRMM was March 2000; no additional data are expected.  Until June 2005, one instrument on each EOS platform operated in a fixed azimuth scanning mode and the other operated in a rotating azimuth scanning mode; now all are typically operating in the fixed azimuth scanning mode.  The NPP platform carries the FM5 instrument, which operates in the fixed azimuth scanning mode though it has the capability to operate in a rotating azimuth scanning mode.

CERES climate data records involve an unprecedented level of data fusion:  CERES measurements are combined with imager data (e.g., MODIS on Terra and Aqua, VIIRS on NPP), 4-D weather assimilation data, microwave sea-ice observations, and measurements from five geostationary satellites to produce climate-quality radiative fluxes at the top-of-atmosphere, within the atmosphere and at the surface, together with the associated cloud and aerosol properties.

The CERES project management and implementation responsibility is at NASA Langley.  The CERES Science Team is responsible for the instrument design and the derivation and validation of the scientific algorithms used to produce the data products distributed to the atmospheric sciences community.  The CERES DMT is responsible for the development and maintenance of the software that implements the science team’s algorithms in the production environment to produce CERES data products.  The Langley ASDC is responsible for the production environment, data ingest, and the processing, archival, and distribution of the CERES data products.

## Document Overview

This document, CERES ERBE-like Inversion to Instantaneous Top-of-the-Atmosphere (TOA) Fluxes and ERBE-like Averaging to Monthly TOA Fluxes Subsystems 2.0 and 3.0 Release 3 Test Plan, is part of the CERES Subsystems 2.0 and 3.0 Release 3 delivery package provided to the Langley Atmospheric Science Data Center (ASDC).  It provides a description of the CERES ERBE-like Inversion to Instantaneous TOA Fluxes and ERBE-like Averaging to Monthly TOA Fluxes Release 3 software and explains the procedures for installing, executing, and testing the software.  A section is also included on validating the software results.  A description of acronyms and abbreviations is provided in Appendix A, a directory structure diagram is contained in Appendix B, and a description of the software and data files is contained in Appendix C.

This document is organized as follows:

Section 1.0 - Introduction

Section 2.0 - Software and Data File Installation Procedures

Section 3.0 - Test and Evaluation Procedures

Appendix A - Acronyms and Abbreviations

Appendix B - Directory Structure Diagram

Appendix C - File Description Tables

## Subsystem Overview

The ERBE-like Subsystems (2.0 and 3.0) mainly come from the ERBE Subsystems V and VI.  Details concerning the conversion process from the ERBE to the CERES ERBE-like code may be found in the CERES Software Requirement Documents for Subsystems 2.0 and 3.0.

The ERBE-like Inversion Subsystem (2.0) estimates the radiant flux at the top-of-the-atmosphere (TOA) based on satellite altitude data from the Instrument Subsystem (1.0).  This inversion process is dependent on several factors, including Earth surface features; cloudiness; and the relative geometry of the spacecraft, the Sun, and the measurement field-of-view.  Each radiometric measurement is spectrally corrected to give an unfiltered measurement.  The observed scene is determined by a scene identification algorithm based on these unfiltered measurements; using angular distribution models and statistics provided by the CERES Science Team.  Estimates of the radiant flux at the TOA are computed based on scene information, geometrical considerations, and the unfiltered measurements.  The output of the Inversion Subsystem includes the ES-8 science archival product and the EID-6 which contains averaged regional data and serves as input for Subsystem 3.0.  In addition, daily quality control reports and browse images of selected parameters from the ES-8 product are generated and made available for viewing over the Web following Subsystem 2.0 job completion

Up to this phase of the processing, data are processed in time-ordered sequence regardless of the location of the measurements.  To obtain monthly averages of the radiometric measurements for geographic regions, the data must be made accessible by region.  To accomplish this data transition, a Daily Data Base which contains data for an entire month is created to store the time-sequenced inverted data.  The data base is comprised of 36 latitudinal data files and a housekeeping file.  The housekeeping file provides the necessary information for accessing data from the data base.  As each daily EID-6 file from Inversion is processed, individual records are written to one of the 36 latitudinal data files based on region number.  After all EID-6 files are processed, a final sort is performed to each of the 36 latitudinal files.

The ERBE-like Monthly Time/Space Averaging Subsystem (3.0) produces monthly averages of shortwave and longwave radiant flux at the TOA on a regional basis.  These calculations are made at the spatial resolution of a 2.5-degree region on the Earth’s surface.  These data are processed for each instrument to produce monthly daily averages, monthly hourly averages (each hour averaged for all data during the month), and two grand monthly averages (averages of the daily and monthly hourly averages) for each geographic region.  The averages are stored in the ES-9 and then used to produce regional, zonal, and global output products, ES-4/ES-4G.  Browse images of selected parameters from the ES-4/ES-4G product are generated from the on-line script and are available for viewing over the Web following Subsystem 3.0 job completion.

### CERES ERBE-like Monthly Geo-Scene and Snow Map, and Longwave and Albedo Thresholds

Product Generation Executive (PGE) CER2.1P1 generates a binary input file containing geo-scene types (including snow cover) and albedo and longwave threshold values used by the other ERBE-like Subsystem 2.0 PGEs.  This PGE also generates geo-scene maps as color postscript files and as gif files for display over the Web.

### CERES ERBE-like Spectral Correction Coefficients and Spectral Responses

PGE CER2.4P1 is the ERBE-like processor to generate the Spectral Response Functions and Correction Coefficients data created from an off-line process.  This PGE executes scripts which create the Spectral Response Function and Correction Coefficient day and night files needed for input to the ERBE-like daily inversion process.

### CERES ERBE-like Daily Inversion for a Single Instrument

PGE CER2.2P1 is the ERBE-like Daily-Processor for combined Fixed Azimuth Plane Scan (FAPS) and Rotating Azimuth Plane Scan (RAPS) data.  This PGE executes scripts which create the binary ES-8, the HDF ES-8, the ERBE-like Inversion QC Report, and ES-8 GIF files.

#### CERES ERBE-like Daily Inversion Main-Processor for a Single Instrument

Script, inv, executes the main ERBE-like Inversion daily software for combined Fixed Azimuth Plane Scan (FAPS) and Rotating Azimuth Plane Scan (RAPS) data, and outputs the binary ES-8, the EID-6, and the ERBE-like Inversion QC Report.

#### CERES ERBE-like ES-8 HDF-EOS Generator

Script, gen_es8hdf, converts the binary ES-8 output to HDF-EOS format.

#### CERES ERBE-like Inversion ES-8 GIF File Generator

Web post-processor, plot_es8, uses the binary ES-8 from the ERBE-like Inversion Daily-Processor to generate ES-8 GIF files.

### CERES ERBE-like Monthly Inversion for the First Day of the Next Month

PGE CER2.3P1 is the ERBE-like Monthly Overlap-Processor for combined Fixed Azimuth Plane Scan (FAPS) and Rotating Azimuth Plane Scan (RAPS) data from the first day of the next month.  This PGE executes scripts which create an overlap EID-6 file, if there is overlap data from the next month.

### CERES ERBE-like Monthly Inversion for the Last Day of the Previous Month

PGE CER2.3P2 is the ERBE-like Monthly Overlap-Processor for combined Fixed Azimuth Plane Scan (FAPS) and Rotating Azimuth Plane Scan (RAPS) data from the last day of the previous month.  This PGE executes scripts which create an overlap EID-6 file if there is overlap data from the previous month.

### CERES ERBE-like Monthly TOA Flux Averaging for a Single Instrument

PGE CER3.1P1 is the ERBE-like Monthly Averaging Main-Processor for combined Fixed Azimuth Plane Scan (FAPS) and Rotating Azimuth Plane Scan (RAPS) data. It invokes ERBE-like daily data base, monthly time/space averaging, and monthly regional, zonal, and global averaging programs for monthly data processing.  It converts binary ES-4G output files from the ERBE-like Monthly Averaging Main-Processor to HDF-EOS format.  It converts binary ES-9 output files from the ERBE-like Monthly Averaging Main-Processor to HDF format.  It uses the binary ES-4G files from the ERBE-like Monthly Averaging Main-Processor to generate an ES-4 GIF file.

### CERES ERBE-like Monthly TOA Flux Averaging for Multiple Instruments

PGE CER3.2P1 is the ERBE-like Monthly Averaging Main-Processor to combine files previously generated from two or more instruments by PGE CER3.1P1.

### CERES ERBE-like Daily Inversion for FM6

PGE CER2.2P2 is the ERBE-like Daily-Processor for combined Fixed Azimuth Plane Scan (FAPS) and Rotating Azimuth Plane Scan (RAPS) data.  This PGE executes scripts which create the binary ES-8, the HDF ES-8 and ERBE-like Inversion QC Report.

#### CERES ERBE-like Daily Inversion Main-Processor for FM6

Script, inv, executes the main ERBE-like Inversion daily software for combined Fixed Azimuth Plane Scan (FAPS) and Rotating Azimuth Plane Scan (RAPS) data, and outputs the binary ES-8, the EID-6, and the ERBE-like Inversion QC Report.

#### CERES ERBE-like ES-8 HDF-EOS Generator

Script, gen_es8hdf, converts the binary ES-8 output to HDF-EOS format.

# Software and Data File Installation Procedures

This section describes how to install the ERBE-like software in preparation for making the necessary test runs at the Langley ASDC.  The installation procedures include instructions for uncompressing and untarring the delivered tar files, properly defining environmental variables and recompiling the ERBE-like programs.

## Installation

Software/Data File Install Procedure:

The scripts, makefiles and Process Control File (PCF) in the Subsystems 2.0 and 3.0 delivery package expect the following environment variables, created by sourcing the platform-appropriate $CERESENV script (i.e., either /SCF/CERES/lib/p6-xlf/ceres-env.csh or /SCF/CERES/lib/x86-gnu/ceres-env.csh), to be defined:

PGSDIR	-	Directory for Toolkit libraries

PGSLIB 	-	Directory containing IBM P6 Toolkit library file

PGSMSG	-	Directory containing Toolkit and CERES Status Message Files (SMFs)

PGSINC	-	Pointer to the PGS/include file directory

HDFDIR	-	Pointer to the HDF home directory (xlf, linux64)

CERESHOME	-	Top Directory for CERES Software

CERESLIB	-	Directory for CERESlib

F90, CC	-	Pointer to the IBM P6 F90, C compilers (xlf90, gcc)

F90COMP 	-	IBM P6 F90 compiler options

Change directory to the directory where you plan to install the ERBE-like Subsystems.  By default, this would be the top directory for CERES software (i.e., cd $CERESHOME).  In any case, the installation location needs to be designated as the ERBE-like home directory (i.e., setenv ERBELIKEHOME $cwd).  Place the ERBE-like tar files (containing the source codes, ancillary data, and other data) there.

Uncompress and untar the tar files (i.e., uncompress or gunzip *.tar.Z, tar xf filenames.tar).  This will result in the creation of the erbelike directory alongside the tar files.

## Compilation

There are 22 source codes for generating the Product Generation System, or PGS, include and message files for the ERBE-like PGEs.  These codes are to be delivered in one directory (erbelike/smf).  A similar situation applies for the general-purpose ERBE-like library (erbelike/lib/erbelike_lib), except that is not needed by all PGEs (i.e., CER2.1P1 works without it).  In addition, each PGE uses its own unique set of source codes and libraries organized as such.  The instructions for compiling these portions of the subsystem follow:

- The PGS files can be made by typing:

cd $ERBELIKEHOME/erbelike/smf

$CERESLIB/bin/smfcompile_all.csh

This script will first create the required include and message files locally before moving them to their respective directories.  At the end of the script, if all went well, the following message will appear:

-------------------------------------------------------

SUCCESS SUCCESS SUCCESS SUCCESS SUCCESS SUCCESS SUCCESS

-------------------------------------------------------

This can be verified by looking for the include PGS files that would result (and would not be present otherwise), such as:

ls -l $PGSINC/*25222.f

ls -l $PGSINC/*25208.f

The ERBE-like Library can be made by typing:

cd $ERBELIKEHOME/erbelike/rcf

source ENVerbelike-env.csh

cd $ERBELIKEHOME/erbelike/lib/erbelike_lib

make clean

make

This compilation can be verified by looking for the newly created library that would result (and would not be present otherwise):

ls -l erbelike_lib_$CPUTYPE.a

### Compiling PRES8 Processor library

- The PRES8 Processor library creates 1 executable when compiled and this executable is used by PGEs CER2.2P1, CER2.2P2, CER2.3P1, and CER2.3P2.  It is compiled by running a compilation script in the library directory.  To run this script, go to its directory and source it by typing:

setenv ERBELIKEHOME $CERESHOME

cd $ERBELIKEHOME/erbelike/lib/pres8_generator

./PRES8_compile.pl

This script will create an executable that can be verified via the following:

cd $ERBELIKEHOME/erbelike/lib/pres8_generator

ls -l PRES8Processor_x86_64.exe

### Compiling PGE 2.1P1

- The monthly ‘actual’ snow map generator (PGE CER2.1P1) has 1 executable that is recompiled via the PGE’s compiling script.  To run this script, go to its directory and source it by typing:

cd $ERBELIKEHOME/erbelike/CER2.1P1/rcf

compile_2.1P1

This script will create an executable that can be verified via the following:

cd $ERBELIKEHOME/erbelike/CER2.1P1/bin

ls -l CER2.1P1_gen_snow_$CPUTYPE.exe

The comparison software for PGE CER2.1P1 consists of 1 executable that is recompiled via its makefile.  To run this script, go to its directory and make it by typing:

cd $ERBELIKEHOME/erbelike/test_suites

make clean -f Makefile.iigs

make -f Makefile.iigs

This script will create an executable that can be verified via the following:

ls -l cmp_iigs_$CPUTYPE.exe

### Compiling CER2.2P1

- The ERBE-like inversion subsystem is compiled from a script:

cd $ERBELIKEHOME/erbelike/CER2.2P1/rcf/

source compile_2.2P1.csh

Two executables will be created:

$ERBELIKEHOME/erbelike/CER2.2P1/bin/CER2.2P1_gen_es8hdf_$CPUTYPE.exe

$ERBELIKEHOME/erbelike/bin/CER2.2P1_inv_$CPUTYPE.exe

This creates all necessary executables for daily inversion (CER2.2P1) and the first of 3 for monthly overlaps (CER2.3Px).  Also, the two ES8 validation graphics executables appear:

$ERBELIKEHOME/erbelike/CER2.2P1/Web/src/
CER2.2P1_GenEs8Ppm_$CPUTYPE.exe, CER2.2P1_GenEs8SenID_$CPUTYPE.exe

- Comparison Codes

PGE CER2.2P1 has 4 executables (cmp_eid6, cmp_es8, cmp_es8n and es8_rec_print) to compare test results with expected output.  They are to be compiled from their source codes via their respective makefiles:

cd $ERBELIKEHOME/erbelike/test_suites

make clean -f Makefile.eid6

make -f Makefile.eid6

make clean -f Makefile.es8

make -f Makefile.es8

make clean -f Makefile.es8n

make -f Makefile.es8n

make clean -f Makefile.reades8hdf

make -f Makefile.reades8hdf

### Compiling CER2.3P1 and CER2.3P2

The executables and comparison codes for these PGEs are created by compiling PGE CER2.2P1 and PGE CER3.1P1.  Please see the ERBE-like Subsystem Lead for further instructions for a specific delivery.

### Compiling PGE 2.4P1

- The Subsystem 2.0 monthly SCC generator (PGE CER2.4P1) has 11 executables that are recompiled via the PGE’s compiling script.  To run this script, go to its directory and source it by typing:

cd $ERBELIKEHOME/erbelike/CER2.4P1

source compile_2.4P1.csh

The script will first recompile the CER2.4P1 library, then all of the PGE’s source codes, with the resulting executables, being stored in the directory
$ERBELIKEHOME/erbelike/CER2.4P1/bin

where one will find the following:

CER2.4P1_calbkn_$CPUTYPE.exe, CER2.4P1_interp_resp_$CPUTYPE.exe

CER2.4P1_regr_lw_$CPUTYPE.exe, CER2.4P1_spcoef_lnd_$CPUTYPE.exe

CER2.4P1_spcoef_night_$CPUTYPE.exe, CER2.4P1_stitch_$CPUTYPE.exe

CER2.4P1_checker_$CPUTYPE.exe, CER2.4P1_meta_$CPUTYPE.exe

CER2.4P1_regr_$CPUTYPE.exe, CER2.4P1_spcoef_night_lnd_$CPUTYPE.exe

CER2.4P1_spcoef_$CPUTYPE.exe

If any of these files are missing or not up-to-date (i.e., check via ls -l *.exe), then the compilation was unsuccessful.

### Compiling PGE 3.1P1

- The ERBE-like single instrument monthly averaging generator (PGE CER3.1P1) has 3 executables (2 for daily database and one for monthly time-space averaging) that can be recompiled via their own makefiles.  However, the subsystem 3 ERBE-like libraries must be compiled beforehand.  Both steps are handled via a script written specifically for this purpose.  To run this script, go to its respective directory and source it by typing:

$ERBELIKEHOME/erbelike/CER3.1P1/rcf/compile_src.pl

After a few minutes, the PGE’s 3 executables will then be created and placed in the directory $ERBELIKEHOME/erbelike/CER3.1P1/bin

where one will find the following:

CER3.1P1_ddbsrt_$CPUTYPE.exe, CER3.1P1_ddbuer_$CPUTYPE.exe, CER3.1P1_mtsa1_$CPUTYPE.exe

One should also verify the successful compilation of the code used to translate the output data into graphics (CER3.1P1_s4_gen_ppm_$CPUTYPE.exe, located under CER3.1P1/Web/s4g/src/genppm, and CER3.1P1_s4g_get_$CPUTYPE.exe, located under CER3.1P1/Web/s4g/src/gets4g).  If any of these files are missing or not up-to-date (i.e., check via ls -l *.exe), then the compilation was unsuccessful.

Comparison Codes

PGE CER3.1P1 has 2 executables for verifying its 2 main output data sets, ES-4 and ES-9 for a single instrument.  In addition, it uses 1 executable for hdf output.  As the final step of running compile_src.pl, the following executables should have been created in the test_suites directory:

CER3.1P1_cmp_es4_$CPUTYPE.exe, CER3.1P1_cmp_es9_$CPUTYPE.exe, CER3_hcmp_$CPUTYPE.exe

### Compiling PGE 3.2P1

- The ERBE-like multiple instrument monthly averaging generator (PGE CER3.2P1) has 2 executables (both for monthly time-space averaging) that can be recompiled via their own makefiles.  However, the subsystem 3 libraries must be compiled beforehand, a step fulfilled by compiling PGE CER3.1P1.  Then one can proceed to 3.2 via a script written specifically for it.  To run this script, go its respective directory and source it by typing:

$ERBELIKEHOME/erbelike/CER3.2P1/rcf/compile_src.pl

The PGE’s 2 executables will then be created and placed in the directory $ERBELIKEHOME/erbelike/CER3.2P1/bin

where one will find the following:

CER3.2P1_mtsa0_$CPUTYPE.exe, CER3.2P1_mtsa3_$CPUTYPE.exe

One should also verify the successful compilation of the code used to translate the output data into graphics:

CER3.2P1/Web/s4g/src/genppm/CER3.2P1_s4_gen_ppm_$CPUTYPE.exe CER3.2P1/Web/s4g/src/gets4g/CER3.2P1_s4g_get_$CPUTYPE.exe

If any of these files are missing or not up-to-date (i.e. check via ls -l *.exe), then the compilation was unsuccessful.

Comparison Codes

PGE CER3.2P1 has 3 executables to compare test results with expected output.  One is the same code as used by 3.1P1 for comparing hdf data.  The remaining two are specific to 3.2P1 and used for verifying its main output data sets:  ES-4 and ES-9 for multiple instruments. As the final step of running compile_src.pl, the following executables should have been created in the test_suites directory:

CER3.2P1_cmp_mes4_$CPUTYPE.exe

CER3.2P1_cmp_mes9_$CPUTYPE.exe

### Compiling PGE CER2.2P2

- The ERBE-like inversion subsystem for FM6 is compiled from a script:

cd $ERBELIKEHOME/erbelike/CER2.2P2/rcf/

source compile_2.2P2.csh

Two executables will be created:

$ERBELIKEHOME/erbelike/CER2.2P2/bin/CER2.2P2_gen_es8hdf_$CPUTYPE.exe

$ERBELIKEHOME/erbelike/bin/CER2.2P2_inv_$CPUTYPE.exe

where $CPUTYPE is x86_64 for the x86 platform.

This creates all necessary executables for daily FM6 inversion (CER2.2P2).

# Test and Evaluation Procedures

This section provides general information on how to execute Subsystems 2.0 and 3.0 and provides an overview of the test and evaluation procedures.  It includes a description of the PGEs being tested and the order in which the tests should be performed.  It assumes that the ceres environment definitions have been redefined by re-sourcing $CERESENV beforehand (and thereby redefining $CERESHOME as the top directory for CERES software), as was the case before compiling the PGE’s source codes.  Also, the amount of memory necessary to run a PGE may exceed the amount currently available.  This deficiency should be resolved before the run with the unlimit command.

## CER2.1P1 CERES ERBE-like Monthly Geo-Scene and Snow Map, and Longwave and Albedo Thresholds

### Test Procedures

#### PCF Generator

The production script, CER2.1P1, references a Process Control File (PCF) which contains the file names and paths for the test procedures.  The PCF for the test case is created by executing a combined PCF log and PCF generator, gen_pcf.CER2.1P1.

For production runs, the PCF log and PCF generator, gen_pcf.CER2.1P1, must be executed to create the PCF log and PCF for a particular production run.  The PCF log and PCF generator requires one command-line argument, yyyymm (where yyyy is the 4-digit year, and mm is the 2-digit month).

- Clean up the test directories:

Command Line Test:

setenv ERBELIKEHOME $CERESHOME

cd $ERBELIKEHOME/erbelike/CER2.1P1/rcf

source $ERBELIKEHOME/erbelike/data/input/CER2.1P1/ENVerbelike-env.TestPlan_211002.csh

clr_dir.PGE2.1 200912

SGE Test:

setenv ERBELIKEHOME $CERESHOME

cd $ERBELIKEHOME/erbelike/CER2.1P1/rcf

source $ERBELIKEHOME/erbelike/data/input/CER2.1P1/ENVerbelike-env.TestPlan_211002.csh

clr_dir.PGE2.1 200912

- Generate the PCF log and the PCF for the test case:

Command Line Test:

CER2.1P1_gen_pcf.pl 200912

SGE Test:

PCF generator built into CER2.1P1-SGE_Driver.pl called below.

The following file will be generated in $ERBELIKEHOME/erbelike/CER2.1P1/rcf/pcf/:

CER2.1P1_PCF_CERES_TestPlan_211002.200912

CER2.1P1_PCF_CERES_TestPlan_211002.200912.log

#### Execution

Execute the production script by typing the script name, CER2.1P1, followed by a string which designates the instance of the PCF.  The string should be formatted, ’Sampling Strategy’_’Production Strategy’_’Configuration Code’.’Data Date’.  The date parameter is formatted, yyyymm, where yyyy is the 4-digit year and mm is the 2-digit month of the data.

For this test, use Sampling Strategy:  CERES, Production

Strategy:  TestPlan, Configuration Code:  211001 and Data Date:  200912

Command Line Test:

unlimit

CER2.1P1_run.pl CERES_TestPlan_211002.200912

SGE Test:

CER2.1P1-SGE_Driver.pl -d 200912

The following files and associated .met files will be generated $ERBELIKEHOME/erbelike/data/CERES/SNOW/CERES_NSIDC/2009/12:

CER_SNOW_CERES_TestPlan_211002.200912

$ERBELIKEHOME/erbelike/data/CERES/CQCR/2009/12/:

CER_CQCR_CERES_TestPlan_211002.200912

$ERBELIKEHOME/erbelike/web/CER2.1P1/CERESfmt/:

CERESfmt_200912.map

$ERBELIKEHOME/erbelike/web/CER2.1P1/CERESweb/:

CERESweb_200912.map

#### Exit Codes

All CER2.1P1 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.  This test should complete with “Exit Status = 0”.

#### CER2.1P1 Test Summary

Total Run Time:	0:10 minutes

Memory:	64 Megabytes

Required Disk Space:	0.416 Megabytes

### Evaluation Procedures

When running the production script, CER2.1P1, the system message, “Cannot access <filename>: No such file or directory” may be written to the screen.  This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

#### Log and Status File Results

The Error and Status Log Files are located in directory $ERBELIKEHOME/erbelike/runlogs/CER2.1P1 after CER2.1P1 has been executed.  These files are:

CER2.1P1_LogReport_CERES_TestPlan_211002.200912

CER2.1P1_LogStatus_CERES_TestPlan_211002.200912

CER2.1P1_LogUser_CERES_TestPlan_211002.200912

#### Metadata Evaluation

The metadata files, which end in extension ‘.met’, are located in the same directory as their corresponding output files after CER2.1P1 has been executed.  Compare the metadata for the test case with the metadata provided in this delivery, using the diff command:

diff $ERBELIKEHOME/erbelike/data_exp/CER2.1P1/CER_SNOW_CERES_TestPlan_211002.200912.met $ERBELIKEHOME/erbelike/data/CERES/SNOW/CERES_NSIDC/2009/12/CER_SNOW_CERES_TestPlan_211002.200912.met

diff $ERBELIKEHOME/erbelike/data_exp/CER2.1P1/CER_CQCR_CERES_TestPlan_211002.200912.met $ERBELIKEHOME/erbelike/data/CERES/CQCR/2009/12/CER_CQCR_CERES_TestPlan_211002.200912.met

The only differences between the files should be the production times and the directory paths where the tests were run.

#### Execution of Comparison Software

The CER2.1P1 evaluation software will compare the snow file created from this test and the snow file included in the $ERBELIKEHOME/erbelike/data_exp/CER2.1P1 directory.

To run the compare program after the SNOW output file has been created at $ERBELIKEHOME/erbelike/data/CERES/SNOW/CERES_NSIDC/2009/12:

cd $ERBELIKEHOME/erbelike/test_suites

setenv GFORTRAN_CONVERT_UNIT "swap"

cmp_iigs_x86_64.exe 200912

unsetenv GFORTRAN_CONVERT_UNIT

#### Evaluation of Comparison Software Output

The Snow compare program, cmp_iigs.exe, produces the output file cmp_iigs.out.  When the files compared are identical, the output file will contain the statement “NO DIFFERENCES FOUND.”  If there are any differences, the statement “FILES ARE DIFFERENT” and the conflicting data will be written to the output file.

### Solutions to Possible Problems

- All output files are opened with Status = NEW in the CER2.2P1 software.  These files must be removed before rerunning these test procedures.  A script, which removes PGE created files, clr_dir.CER2.1P1, is located in directory $ERBELIKEHOME/erbelike/bin.  Use the data date (4-digit year, 2-digit month) as a command-line argument:

clr_dir.PGE2.1 200912

If more than 10 days of snow data are not available for the data month, the program will terminate and the target PGEs should not run.

Refer to the Message and Log files created in $ERBELIKEHOME/erbelike/data/runlogs for explanations of possible problems.

## CER2.4P1 CERES ERBE-like Spectral Response Functions and Correction Coefficients

### Test Procedures

#### Execution

The production script, CER2.4P1_run.pl, references a Process Control File (PCF) which contains the file names and paths for the test procedures.  The PCFs for the test cases is created by executing a combined PCF log and PCF generator, CER2.4P1_gen_pcf.pl.

For production runs, the PCF log and PCF generator, gen_pcf.CER2.4P1.pl, must be executed to create the PCF log and PCF for a particular production run.  The PCF log and PCF generator requires three command-line arguments:  (1) yyyymm (where yyyy is the 4-digit year and mm is the 2-digit month); (2) channel_code (a number indicating the instrument channel combination of the input files:  1=SW, 2=TOT, 3=WN, 12=SW/TOT, 13=SW/WN, 23=TOT/WN, or 123=SW/TOT/WN); and (3) data product edition code (G for Baseline1-QC, Edition1-CV, and Edition2; Ed3 for Edition3).

- FM1 Edition4:

setenv ERBELIKEHOME $CERESHOME

cd $ERBELIKEHOME/erbelike/data/input/CER2.4P1

source ENV-FM1_SCCR-1330.csh

cd $ERBELIKEHOME/erbelike/CER2.4P1/rcf

CER2.4P1_clr_dir.csh 200302

CER2.4P1-SGE_Driver.pl -d 200302 -- 12 Ed4

FM2 Edition4:

setenv ERBELIKEHOME $CERESHOME

cd $ERBELIKEHOME/erbelike/data/input/CER2.4P1

source ENV-FM2_SCCR-1330.csh

cd $ERBELIKEHOME/erbelike/CER2.4P1/rcf

CER2.4P1_clr_dir.csh 200302

CER2.4P1-SGE_Driver.pl -d 200302 -- 123 Ed4

FM3 Edition4:

setenv ERBELIKEHOME $CERESHOME

cd $ERBELIKEHOME/erbelike/data/input/CER2.4P1

source ENV-FM3_SCCR-1330.csh

cd $ERBELIKEHOME/erbelike/CER2.4P1/rcf

CER2.4P1_clr_dir.csh 200302

CER2.4P1-SGE_Driver.pl -d 200302 -- 123 Ed4

FM4 Edition4:

setenv ERBELIKEHOME $CERESHOME

cd $ERBELIKEHOME/erbelike/data/input/CER2.4P1

source ENV-FM4_SCCR-1330.csh

cd $ERBELIKEHOME/erbelike/CER2.4P1/rcf

CER2.4P1_clr_dir.csh 200302

CER2.4P1-SGE_Driver.pl -d 200302 -- 123 Ed4

#### Expected Output

The following files will be generated in $ERBELIKEHOME/erbelike/CER2.4P1/rcf/pcf/:

FM1_Edition4:

CER2.4P1_PCF_Terra-FM1_SCCR_1330.20030215

CER2.4P1_PCF_Terra-FM1_SCCR_1330.20030215.log

FM2_Edition4:

CER2.4P1_PCF_Terra-FM2_SCCR_1330.20030215

CER2.4P1_PCF_Terra-FM2_SCCR_1330.20030215.log

FM3_Edition4:

CER2.4P1_PCF_Aqua-FM3_SCCR_1330.20030215

CER2.4P1_PCF_Aqua-FM3_SCCR_1330.20030215.log

FM4_Edition4:

CER2.4P1_PCF_Aqua-FM4_SCCR_1330.20030215

CER2.4P1_PCF_Aqua-FM4_SCCR_1330.20030215.log

The following files and associated .met files will be generated in $ERBELIKEHOME/erbelike/data/CERES/

FM1_Edition4:

SCCD/Terra-FM1_SCCR/2003/02/CER_SCCD_Terra-FM1_SCCR_1330.20030215.met

SCCD/Terra-FM1_SCCR/2003/02/CER_SCCD_Terra-FM1_SCCR_1330.20030215

SCCN/Terra-FM1_SCCR/2003/02/CER_SCCN_Terra-FM1_SCCR_1330.20030215.met

SCCN/Terra-FM1_SCCR/2003/02/CER_SCCN_Terra-FM1_SCCR_1330.20030215

FM2_Edition4:

SCCD/Terra-FM2_SCCR/2003/02/CER_SCCD_Terra-FM2_SCCR_1330.20030215.met

SCCD/Terra-FM2_SCCR/2003/02/CER_SCCD_Terra-FM2_SCCR_1330.20030215

SCCN/Terra-FM2_SCCR/2003/02/CER_SCCN_Terra-FM2_SCCR_1330.20030215.met

SCCN/Terra-FM2_SCCR/2003/02/CER_SCCN_Terra-FM2_SCCR_1330.20030215

FM3_Edition4:

SCCD/Aqua-FM3_SCCR/2003/02/CER_SCCD_Aqua-FM3_SCCR_1330.20030215.met

SCCD/Aqua-FM3_SCCR/2003/02/CER_SCCD_Aqua-FM3_SCCR_1330.20030215

SCCN/Aqua-FM3_SCCR/2003/02/CER_SCCN_Aqua-FM3_SCCR_1330.20030215.met

SCCN/Aqua-FM3_SCCR/2003/02/CER_SCCN_Aqua-FM3_SCCR_1330.20030215

FM4_Edition4:

SCCD/Aqua-FM4_SCCR/2003/02/CER_SCCD_Aqua-FM4_SCCR_1330.20030215.met

SCCD/Aqua-FM4_SCCR/2003/02/CER_SCCD_Aqua-FM4_SCCR_1330.20030215

SCCN/Aqua-FM4_SCCR/2003/02/CER_SCCN_Aqua-FM4_SCCR_1330.20030215.met

SCCN/Aqua-FM4_SCCR/2003/02/CER_SCCN_Aqua-FM4_SCCR_1330.20030215

#### Exit Codes

All CER2.4P1 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.  This test should complete with “Exit Status = 0”.

#### CER2.4P1 Test Summary

Median Run Time:	16 minutes

Memory:	7.5 Megabytes

Required Disk Space:	4480 Megabytes

### Evaluation Procedures

When running the production script, CER2.4P1, the system message, “Cannot access <filename>: No such file or directory” may be written to the screen.  This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

#### Log and Status File Results

The Error and Status Log Files are located in directory $ERBELIKEHOME/erbelike/runlogs/CER2.4P1 after CER2.4P1-SGE_Driver.pl has been executed.  These files are:

FM1_Edition4:

CER2.4P1_LogReport_Terra-FM1_SCCR_1330.20030215

CER2.4P1_LogStatus_Terra-FM1_SCCR_1330.20030215

CER2.4P1_LogUser_Terra-FM1_SCCR_1330.20030215

FM2_Edition4:

CER2.4P1_LogReport_Terra-FM2_SCCR_1330.20030215

CER2.4P1_LogStatus_Terra-FM2_SCCR_1330.20030215

CER2.4P1_LogUser_Terra-FM2_SCCR_1330.20030215

FM3_Edition4:

CER2.4P1_LogReport_Aqua-FM3_SCCR_1330.20030215

CER2.4P1_LogStatus_Aqua-FM3_SCCR_1330.20030215

CER2.4P1_LogUser_Aqua-FM3_SCCR_1330.20030215

FM4_Edition4:

CER2.4P1_LogReport_Aqua-FM4_SCCR_1330.20030215

CER2.4P1_LogStatus_Aqua-FM4_SCCR_1330.20030215

CER2.4P1_LogUser_Aqua-FM4_SCCR_1330.20030215

#### Metadata Evaluation

The metadata files, which end in extension ‘.met’, are located in the same directory as their corresponding output files after CER2.4P1 has been executed.  Compare the metadata for the test case with the metadata provided in this delivery, using the diff command:

FM1_Edition4:

sdiff -s $ERBELIKEHOME/erbelike/data/CERES/SCCD/Terra-FM1_SCCR/2003/02/CER_SCCD_Terra-FM1_SCCR_1330.20030215.met $ERBELIKEHOME/erbelike/data_exp/CER2.4P1/CER_SCCD_Terra-FM1_SCCR_1330.20030215.met

sdiff -s $ERBELIKEHOME/erbelike/data/CERES/SCCN/Terra-FM1_SCCR/2003/02/CER_SCCN_Terra-FM1_SCCR_1330.20030215.met $ERBELIKEHOME/erbelike/data_exp/CER2.4P1/CER_SCCN_Terra-FM1_SCCR_1330.20030215.met

FM2_Edition4:

sdiff -s $ERBELIKEHOME/erbelike/data/CERES/SCCD/Terra-FM2_SCCR/2003/02/CER_SCCD_Terra-FM2_SCCR_1330.20030215.met $ERBELIKEHOME/erbelike/data_exp/CER2.4P1/CER_SCCD_Terra-FM2_SCCR_1330.20030215.met

sdiff -s $ERBELIKEHOME/erbelike/data/CERES/SCCN/Terra-FM2_SCCR/2003/02/CER_SCCN_Terra-FM2_SCCR_1330.20030215.met $ERBELIKEHOME/erbelike/data_exp/CER2.4P1/CER_SCCN_Terra-FM2_SCCR_1330.20030215.met

FM3_Edition4:

sdiff -s $ERBELIKEHOME/erbelike/data/CERES/SCCD/Aqua-FM3_SCCR/2003/02/CER_SCCD_Aqua-FM3_SCCR_1330.20030215.met $ERBELIKEHOME/erbelike/data_exp/CER2.4P1/CER_SCCD_Aqua-FM3_SCCR_1330.20030215.met

sdiff -s $ERBELIKEHOME/erbelike/data/CERES/SCCN/Aqua-FM3_SCCR/2003/02/CER_SCCN_Aqua-FM3_SCCR_1330.20030215.met $ERBELIKEHOME/erbelike/data_exp/CER2.4P1/CER_SCCN_Aqua-FM3_SCCR_1330.20030215.met

FM4_Edition4:

sdiff -s $ERBELIKEHOME/erbelike/data/CERES/SCCN/Aqua-FM4_SCCR/2003/02/CER_SCCN_Aqua-FM4_SCCR_1330.20030215.met $ERBELIKEHOME/erbelike/data_exp/CER2.4P1/CER_SCCN_Aqua-FM4_SCCR_1330.20030215.met

sdiff -s $ERBELIKEHOME/erbelike/data/CERES/SCCN/Aqua-FM4_SCCR/2003/02/CER_SCCN_Aqua-FM4_SCCR_1330.20030215.met $ERBELIKEHOME/erbelike/data_exp/CER2.4P1/CER_SCCN_Aqua-FM4_SCCR_1330.20030215.met

The only differences between the files should be the production times and the directory paths where the tests were run.

#### Evaluation of SCCD

Compare the SCCD file for the test case with the SCCD file provided in this delivery.

There should be no differences.

FM1_Edition4:

sdiff -s $ERBELIKEHOME/erbelike/data/CERES/SCCD/Terra-FM1_SCCR/2003/02/CER_SCCD_Terra-FM1_SCCR_1330.20030215 $ERBELIKEHOME/erbelike/data_exp/CER2.4P1/CER_SCCD_Terra-FM1_SCCR_1330.20030215

FM2_Edition4:

sdiff -s $ERBELIKEHOME/erbelike/data/CERES/SCCD/Terra-FM2_SCCR/2003/02/CER_SCCD_Terra-FM2_SCCR_1330.20030215 $ERBELIKEHOME/erbelike/data_exp/CER2.4P1/CER_SCCD_Terra-FM2_SCCR_1330.20030215

FM3_Edition4:

sdiff -s $ERBELIKEHOME/erbelike/data/CERES/SCCD/Aqua-FM3_SCCR/2003/02/CER_SCCD_Aqua-FM3_SCCR_1330.20030215 $ERBELIKEHOME/erbelike/data_exp/CER2.4P1/CER_SCCD_Aqua-FM3_SCCR_1330.20030215

FM4_Edition4:

sdiff -s $ERBELIKEHOME/erbelike/data/CERES/SCCD/Aqua-FM4_SCCR/2003/02/CER_SCCD_Aqua-FM4_SCCR_1330.20030215 $ERBELIKEHOME/erbelike/data_exp/CER2.4P1/CER_SCCD_Aqua-FM4_SCCR_1330.20030215

#### Evaluation of SCCN

Compare the SCCN file for the test case with the SCCN file provided in this delivery.

There should be no differences.

FM1_Edition4:

sdiff -s $ERBELIKEHOME/erbelike/data/CERES/SCCN/Terra-FM1_SCCR/2003/02/CER_SCCN_Terra-FM1_SCCR_1330.20030215 $ERBELIKEHOME/erbelike/data_exp/CER2.4P1/CER_SCCN_Terra-FM1_SCCR_1330.20030215

FM2_Edition4:

sdiff -s $ERBELIKEHOME/erbelike/data/CERES/SCCN/Terra-FM2_SCCR/2003/02/CER_SCCN_Terra-FM2_SCCR_1330.20030215 $ERBELIKEHOME/erbelike/data_exp/CER2.4P1/CER_SCCN_Terra-FM2_SCCR_1330.20030215

FM3_Edition4:

sdiff -s $ERBELIKEHOME/erbelike/data/CERES/SCCN/Aqua-FM3_SCCR/2003/02/CER_SCCN_Aqua-FM3_SCCR_1330.20030215 $ERBELIKEHOME/erbelike/data_exp/CER2.4P1/CER_SCCN_Aqua-FM3_SCCR_1330.20030215

FM4_Edition4:

sdiff -s $ERBELIKEHOME/erbelike/data/CERES/SCCN/Aqua-FM4_SCCR/2003/02/CER_SCCN_Aqua-FM4_SCCR_1330.20030215 $ERBELIKEHOME/erbelike/data_exp/CER2.4P1/CER_SCCN_Aqua-FM4_SCCR_1330.20030215

### Solutions to Possible Problems

- All output files are opened with Status = NEW in the CER2.4P1 software.  These files must be removed before rerunning these test procedures.  A script written for this purpose, clr_dir.PGE2.4, is located in directory $ERBELIKEHOME/erbelike/CER2.4P1/rcf.  Use the data date (4-digit year and 2-digit month) as the command-line argument:

FM1_Edition4:  $ERBELIKEHOME/erbelike/CER2.4P1/rcf/CER2.4P1_clr_dir.csh 200203

FM2_Edition4:  $ERBELIKEHOME/erbelike/CER2.4P1/rcf/CER2.4P1_clr_dir.csh 200203

FM3_Edition4:  $ERBELIKEHOME/erbelike/CER2.4P1/rcf/CER2.4P1_clr_dir.csh 200203

FM4_Edition4:  $ERBELIKEHOME/erbelike/CER2.4P1/rcf/CER2.4P1_clr_dir.csh 200203

Refer to the Message and Log files created in $ERBELIKEHOME/erbelike/runlogs/CER2.4P1 for explanations of possible problems.

## CER2.2P1 CERES ERBE-like Daily Inversion for a Single Instrument

### Stand-alone Test Procedures

Before starting the processing of CER2.2P1, make sure the instrument-specific test BDS input files are accessible from the testing directory:

cd $ERBELIKEHOME/erbelike/CER2.2P1/rcf

FM1:

ls /ASDC_archive/CERES/BDS/Terra-FM1_Edition1-CV/2018/01/CER_BDS_Terra-FM1_Edition1-CV_300309.20180109

ls /ASDC_archive/CERES/BDS/Terra-FM1_Baseline1-QC/2018/03/CER_BDS_Terra-FM1_Baseline1-QC_300309.20180320

ls /ASDC_archive/CERES/BDS/Terra-FM1_Edition4/2018/03/CER_BDS_Terra-FM1_Edition4_400407.20180316

FM2:

ls /ASDC_archive/CERES/BDS/Terra-FM2_Edition1-CV/2018/01/CER_BDS_Terra-FM2_Edition1-CV_300309.20180119

ls /ASDC_archive/CERES/BDS/Terra-FM2_Baseline1-QC/2018/03/CER_BDS_Terra-FM2_Baseline1-QC_300309.20180310

ls /ASDC_archive/CERES/BDS/Terra-FM2_Edition4/2018/03/CER_BDS_Terra-FM2_Edition4_400407.20180320

FM3:

ls /ASDC_archive/CERES/BDS/Aqua-FM3_Edition1-CV/2018/03/CER_BDS_Aqua-FM3_Edition1-CV_300309.20180321

ls /ASDC_archive/CERES/BDS/Aqua-FM3_Baseline1-QC/2018/03/CER_BDS_Aqua-FM3_Baseline1-QC_300309.20180306

ls /ASDC_archive/CERES/BDS/Aqua-FM3_Edition4/2018/03/CER_BDS_Aqua-FM3_Edition4_400407.20180328

FM4:

ls /ASDC_archive/CERES/BDS/Aqua-FM4_Ed1-CV-NoSW/2018/03/CER_BDS_Aqua-FM4_Ed1-CV-NoSW_300309.20180322

ls /ASDC_archive/CERES/BDS/Aqua-FM4_Baseline1-QC/2018/03/CER_BDS_Aqua-FM4_Baseline1-QC_300309.20180313

ls /ASDC_archive/CERES/BDS/Aqua-FM4_Ed4-NoSW/2018/03/CER_BDS_Aqua-FM4_Ed4-NoSW_400407.20180323

FM5:

ls /ASDC_archive/CERES/BDS/NPP-FM5_Edition1-CV/2018/03/CER_BDS_NPP-FM5_Edition1-CV_300309.20180324

ls /ASDC_archive/CERES/BDS/NPP-FM5_Baseline1-QC/2018/03/CER_BDS_NPP-FM5_Baseline1-QC_300309.20180325

ls /ASDC_archive/CERES/BDS/NPP-FM5_Edition1/2018/03/CER_BDS_NPP-FM5_Edition1_100107.20180302

There should be 15 files for Terra,Aqua and NPP (5 instruments x 3 Editions).

#### Execution

The production script, CER2.2P1.pl, references a PCF file containing the file names and paths for the test procedures.  The PCF for each test case is created by executing a combined log file and PCF generator, gen_pcf.CER2.2.pl.

The PCF log and PCF generator requires five command-line arguments, yyyymmdd (where yyyy is the 4-digit year, mm is the 2-digit month, and dd is the 2-digit day), “C” for composite snow or “A” for actual snow input file, “F” for Original ADM structure, “M” to use one of the Instrument Team’s monthly modified Slope Intercept Spectral Correction inputs (“N” if not applicable, i.e., prior to Edition2 input data), “T” for Thermal SW Offsets or “K” for Edition3 processing.

- Terra-FM1:  Baseline1-QC

source $ERBELIKEHOME/erbelike/data/input/CER2.2P1/ENV-FM1_1QC_221_1387.csh

setenv yyyy 2018

setenv mm 03

setenv yyyymmdd ${yyyy}${mm}20

cd $ERBELIKEHOME/erbelike/CER2.2P1/rcf

CER2.2P1-SGE_Driver.pl -date $yyyymmdd -snow C -adm F -spcor N -swoff T -clean

Terra-FM1:  Edition1-CV

source $ERBELIKEHOME/erbelike/data/input/CER2.2P1/ENV-FM1_1CV_221_1387.csh

setenv yyyy 2018

setenv mm 01

setenv yyyymmdd ${yyyy}${mm}09

cd $ERBELIKEHOME/erbelike/CER2.2P1/rcf

CER2.2P1-SGE_Driver.pl -date $yyyymmdd -snow A -adm F -spcor N -swoff T -clean

Terra-FM1:  Edition4

source $ERBELIKEHOME/erbelike/data/input/CER2.2P1/ENV-FM1_Ed4_221_1387.csh

setenv yyyy 2018

setenv mm 03

setenv yyyymmdd ${yyyy}${mm}16

cd $ERBELIKEHOME/erbelike/CER2.2P1/rcf

CER2.2P1-SGE_Driver.pl -date $yyyymmdd -snow A -adm F -spcor M -swoff T -clean

Terra-FM2:  Baseline1-QC

source $ERBELIKEHOME/erbelike/data/input/CER2.2P1/ENV-FM2_1QC_221_1387.csh

setenv yyyy 2018

setenv mm 03

setenv yyyymmdd ${yyyy}${mm}10

cd $ERBELIKEHOME/erbelike/CER2.2P1/rcf

CER2.2P1-SGE_Driver.pl -date $yyyymmdd -snow C -adm F -spcor N -swoff T -clean

Terra-FM2:  Edition1-CV

source $ERBELIKEHOME/erbelike/data/input/CER2.2P1/ENV-FM2_1CV_221_1387.csh

setenv yyyy 2018

setenv mm 01

setenv yyyymmdd ${yyyy}${mm}19

cd $ERBELIKEHOME/erbelike/CER2.2P1/rcf

CER2.2P1-SGE_Driver.pl -date $yyyymmdd -snow A -adm F -spcor N -swoff T -clean

Terra-FM2:  Edition4

source $ERBELIKEHOME/erbelike/data/input/CER2.2P1/ENV-FM2_Ed4_221_1387.csh

setenv yyyy 2018

setenv mm 03

setenv yyyymmdd ${yyyy}${mm}20

cd $ERBELIKEHOME/erbelike/CER2.2P1/rcf

CER2.2P1-SGE_Driver.pl -date $yyyymmdd -snow A -adm F -spcor M -swoff T -clean

Aqua-FM3:  Baseline1-QC

source $ERBELIKEHOME/erbelike/data/input/CER2.2P1/ENV-FM3_1QC_221_1387.csh

setenv yyyy 2018

setenv mm 03

setenv yyyymmdd ${yyyy}${mm}06

cd $ERBELIKEHOME/erbelike/CER2.2P1/rcf

CER2.2P1-SGE_Driver.pl -date $yyyymmdd -snow C -adm F -spcor N -swoff T -clean

Aqua-FM3:  Edition1-CV

source $ERBELIKEHOME/erbelike/data/input/CER2.2P1/ENV-FM3_1CV_221_1387.csh

setenv yyyy 2018

setenv mm 03

setenv yyyymmdd ${yyyy}${mm}21

cd $ERBELIKEHOME/erbelike/CER2.2P1/rcf

CER2.2P1-SGE_Driver.pl -date $yyyymmdd -snow A -adm F -spcor N -swoff T -clean

Aqua-FM3:  Edition4

source $ERBELIKEHOME/erbelike/data/input/CER2.2P1/ENV-FM3_Ed4_221_1387.csh

setenv yyyy 2018

setenv mm 03

setenv yyyymmdd ${yyyy}${mm}28

cd $ERBELIKEHOME/erbelike/CER2.2P1/rcf

CER2.2P1-SGE_Driver.pl -date $yyyymmdd -snow A -adm F -spcor M -swoff T -clean

Aqua-FM4:  Baseline1-QC

source $ERBELIKEHOME/erbelike/data/input/CER2.2P1/ENV-FM4_1QC_221_1387.csh

setenv yyyy 2018

setenv mm 03

setenv yyyymmdd ${yyyy}${mm}13

cd $ERBELIKEHOME/erbelike/CER2.2P1/rcf

CER2.2P1-SGE_Driver.pl -date $yyyymmdd -snow C -adm F -spcor N -swoff T -clean

Aqua-FM4:  Edition1-CV

source $ERBELIKEHOME/erbelike/data/input/CER2.2P1/ENV-FM4_1CV_221_1387.csh

setenv yyyy 2018

setenv mm 03

setenv yyyymmdd ${yyyy}${mm}22

cd $ERBELIKEHOME/erbelike/CER2.2P1/rcf

CER2.2P1-SGE_Driver.pl -date $yyyymmdd -snow A -adm F -spcor N -swoff T -clean

Aqua-FM4:  Edition4

source $ERBELIKEHOME/erbelike/data/input/CER2.2P1/ENV-FM4_Ed4_221_1387.csh

setenv yyyy 2018

setenv mm 03

setenv yyyymmdd ${yyyy}${mm}23

cd $ERBELIKEHOME/erbelike/CER2.2P1/rcf

CER2.2P1-SGE_Driver.pl -date $yyyymmdd -snow A -adm F -spcor M -swoff T -clean

NPP-FM5:  Baseline1-QC

source $ERBELIKEHOME/erbelike/data/input/CER2.2P1/ENV-FM5_1QC_221_1387.csh

setenv yyyy 2018

setenv mm 03

setenv yyyymmdd ${yyyy}${mm}25

cd $ERBELIKEHOME/erbelike/CER2.2P1/rcf

CER2.2P1-SGE_Driver.pl -date $yyyymmdd -snow C -adm F -spcor N -swoff T -clean

NPP-FM5:  Edition1-CV

source $ERBELIKEHOME/erbelike/data/input/CER2.2P1/ENV-FM5_1CV_221_1387.csh

setenv yyyy 2018

setenv mm 03

setenv yyyymmdd ${yyyy}${mm}24

cd $ERBELIKEHOME/erbelike/CER2.2P1/rcf

CER2.2P1-SGE_Driver.pl -date $yyyymmdd -snow A -adm F -spcor N -swoff T -clean

NPP-FM5:  Edition1

source $ERBELIKEHOME/erbelike/data/input/CER2.2P1/ENV-FM5_Ed1_221_1387.csh

setenv yyyy 2018

setenv mm 03

setenv yyyymmdd ${yyyy}${mm}02

cd $ERBELIKEHOME/erbelike/CER2.2P1/rcf

CER2.2P1-SGE_Driver.pl -date $yyyymmdd -snow A -adm F -spcor N -swoff T -clean

#### Expected Output Files

Each instrument ($INST) test will have a sampling Strategy ($SS2), a Production Strategy ($PS2_0), a Configuration Code ($CC2=1387) and a Data Date ($yyyymmdd).  After the Product Generation Executive (PGE) CER2.2P1 is executed, it should have created the following files in the following directories:

The following files will be generated in

$ERBELIKEHOME/erbelike/CER2.2P1/rcf/pcf/:

CER2.2P1_PCF_${SS2}_${PS2_0}_$CC2.$yyyymmdd.log

CER2.2P1_PCF_${SS2}_${PS2_0}_$CC2.$yyyymmdd

The following files (product=PROD) and associated .met files will be generated in $ERBELIKEHOME/erbelike/data/CERES/PROD/${SS2}_${PS2_0}/$yyyy/$mm/:

PROD=CQCI: CER_CQCI_${SS2}_${PS2_0}_$CC2.$yyyymmdd

PROD=EID6: CER_EID6_${SS2}_${PS2_0}_$CC2.$yyyymmdd

PROD=ES8: CER_ES8_${SS2}_${PS2_0}_$CC2.$yyyymmdd

PROD=ES8B: CER_ES8B_${SS2}_${PS2_0}_$CC2.$yyyymmdd

PROD=ES8N: CER_ES8N_${SS2}_${PS2_0}_$CC2.$yyyymmdd

PROD=CMSG: CER_CMSG_${SS2}_${PS2_0}_$CC2.$yyyymmdd

PROD=ES8G: CER_ES8B_${SS2}_${PS2_0}_$CC2.$yyyymmdd_*

Where * are the 17 plot id numbers corresponding to the following plot files (@ in = `echo $INST | cut -c 3` + 1) generated in

$ERBELIKEHOME/erbelike/web/CER2.2P1/gif/ES8_$yyyy$mm\_$in/ES8_$yyyymmdd\_$in/:

ES8_$yyyymmdd\_$in\_11.gif
ES8_$yyyymmdd\_$in\_12.gif
ES8_$yyyymmdd\_$in\_21.gif
ES8_$yyyymmdd\_$in\_22.gif
ES8_$yyyymmdd\_$in\_31.gif
ES8_$yyyymmdd\_$in\_32.gif
ES8_$yyyymmdd\_$in\_41.gif
ES8_$yyyymmdd\_$in\_42.gif
ES8_$yyyymmdd\_$in\_51.gif
ES8_$yyyymmdd\_$in\_52.gif
ES8_$yyyymmdd\_$in\_61.gif
ES8_$yyyymmdd\_$in\_62.gif
ES8_$yyyymmdd\_$in\_71.gif
ES8_$yyyymmdd\_$in\_72.gif
ES8_$yyyymmdd\_$in\_81.gif
ES8_$yyyymmdd\_$in\_82.gif
ES8_$yyyymmdd\_$in\_9.gif

#### Exit Codes

All CER2.2P1 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.  This test should complete with “Exit Status = 0”.

#### CER2.2P1 Test Summary

Total Run Time:	4-5 minutes (on P6)

Memory:	546 Megabytes

Required Disk Space:	800 Megabytes

### Evaluation Procedures

#### Log and Status File Results

The Error and Status Log Files are located in directory $ERBELIKEHOME/erbelike/runlogs/CER2.2P1/ after CER2.2P1 has been executed.  These files are:

CER2.2P1_LogReport_${SS2}_${PS2_0}_$CC2.$yyyymmdd

CER2.2P1_LogStatus_${SS2}_${PS2_0}_$CC2.$yyyymmdd

CER2.2P1_LogUser_${SS2}_${PS2_0}_$CC2.$yyyymmdd

#### Metadata Evaluation

The metadata files, which end in extension ‘.met’, are located in the same directory as their corresponding output files after CER2.2P1 has been executed.  Compare the metadata for the test case with the metadata provided in this delivery, using the gdiff command (available via ssh -X):

cd $ERBELIKEHOME/erbelike/data_exp/CER2.2P1/

gdiff CER_ES8B_${SS2}_${PS2_0}_$CC2.$yyyymmdd.met $ERBELIKEHOME/erbelike/data/CERES/ES8B/${SS2}_${PS2_0}/$yyyy/$mm/CER_ES8B_${SS2}_${PS2_0}_$CC2.$yyyymmdd.met

gdiff CER_ES8_${SS2}_${PS2_0}_$CC2.$yyyymmdd.met $ERBELIKEHOME/erbelike/data/CERES/ES8/${SS2}_${PS2_0}/$yyyy/$mm/CER_ES8_${SS2}_${PS2_0}_$CC2.$yyyymmdd.met

gdiff CER_EID6_${SS2}_${PS2_0}_$CC2.$yyyymmdd.met $ERBELIKEHOME/erbelike/data/CERES/EID6/${SS2}_${PS2_0}/$yyyy/$mm/CER_EID6_${SS2}_${PS2_0}_$CC2.$yyyymmdd.met

The only differences between the files should be the production times, directory paths, and usually the host node (and often the operating system) where the tests were run.

#### Execution of EID-6 Comparison Software

The EID-6 evaluation software will compare the EID-6 file created from this test and the EID-6 file included in the directory $ERBELIKEHOME/erbelike/data_exp/CER2.2P1.

To run the compare program after the EID-6 output file has been created at $ERBELIKEHOME/erbelike/data/CERES/EID6/$SS2_$PS2_0/$yyyy/$mm:

cd $ERBELIKEHOME/erbelike/test_suites

CER2.2P1_cmp_eid6_$CPUTYPE.exe $yyyymmdd EID6

#### Evaluation of EID-6 Comparison Software Output

The EID-6 compare program, cmp_eid6, produces the output file cmp_eid6_$yyyymmdd.out.  If it cannot find differences larger than a threshold value (currently set to 0.00025), the compared files are automatically considered scientifically equivalent, and the output file will contain the statement “NO SUCH DIFFERENCES FOUND.”  If there are any such differences, an appropriate message and the conflicting data (for up to 9 records) will be written to the output file.  If more than 9 records differ, the code will terminate.  If not, a record mismatch evaluation will be written at the bottom.

#### Quality Control Data Evaluation

The production run QC report file, with product name ‘CQCI’, contains data quality info as well as statistical averages of various parameters of interest.  After CER2.2P1 has been executed, compare the test case version with the one provided in this delivery, using the gdiff command:

cd $ERBELIKEHOME/erbelike/data_exp/CER2.2P1

gdiff CER_CQCI_${SS2}_${PS2_0}_$CC2.$yyyymmdd $ERBELIKEHOME/erbelike/data/CERES/CQCI/${SS2}_${PS2_0}/$yyyy/$mm/CER_CQCI_${SS2}_${PS2_0}_$CC2.$yyyymmdd

The only differences between the files should be the production dates and times corresponding to when the tests were run, and in the case of different platform types, computer/wall times as well as scene sigma values and associated Std Dev LW Flux data (though these should be small).

#### Execution of the HDF ES-8 Data Comparison Tool

The ES-8 HDF evaluation utility will compare the ES-8 HDF file created from this test and the ES-8 HDF file included in the $ERBELIKEHOME/erbelike/data_exp/CER2.2P1 directory.

To run this comparison program after the ES-8 HDF output file has been created at $ERBELIKEHOME/erbelike/data/CERES/ES8/$SS2_$PS2_0/$yyyy/$mm:

cd $ERBELIKEHOME/erbelike/data_exp/CER2.2P1

hdiff -d -t 0.00025 CER_ES8_${SS2}_${PS2_0}_$CC2.$yyyymmdd $ERBELIKEHOME/erbelike/data/CERES/ES8/${SS2}_${PS2_0}/$yyyy/$mm/CER_ES8_${SS2}_${PS2_0}_$CC2.$yyyymmdd

#### Evaluation of ES-8 Nadir Comparison Software Output

The ES-8 data comparison tool, hdiff, returns a list of differences by position, parameter name, and values in both files.  If all data differences between the compared files are within the trigger value provided, there will be no output.  As long as the differences are small in both number and magnitude, the files can be considered scientifically equivalent.

### Solutions to Possible Problems

- All output files are opened with Status = NEW in the CER2.2P1 software.  These files must be removed before rerunning these test procedures.  A script, which removes PGE files created via the command line, clr_dir.CER2.2.csh, is located in directory $ERBELIKEHOME/erbelike/CER2.2P1/rcf.

Use the data date (4-digit year, 2-digit month, 2-digit day) as a command-line argument:

clr_dir.CER2.2.csh $yyyymmdd

Refer to the Message and Log files created in $ERBELIKEHOME/erbelike/runlogs/CER2.2P1 (and $ERBELIKEHOME/erbelike/sge_logs/CER2.2P1 in the case of SGE jobs) for explanations of possible problems.7

## CER2.3P1 CERES ERBE-like Monthly Inversion for the First Day of the Next Month

### Stand-alone Test Procedures

Before starting the processing of CER2.3P1, make sure the instrument-specific test BDS input files are accessible from the testing directory:

setenv ERBELIKEHOME $CERESHOME

cd $ERBELIKEHOME/erbelike/CER2.3P1/rcf

FM1:

ls /ASDC_archive/CERES/BDS/Terra-FM1_Edition1-CV/2018/05/CER_BDS_Terra-FM1_Edition1-CV_300309.20180501

ls /ASDC_archive/CERES/BDS/Terra-FM1_Edition4/2018/02/CER_BDS_Terra-FM1_Edition4_400407.20180201

FM2:

ls /ASDC_archive/CERES/BDS/Terra-FM2_Edition1-CV/2018/05/CER_BDS_Terra-FM2_Edition1-CV_300309.20180501

FM3:

ls /ASDC_archive/CERES/BDS/Aqua-FM3_Edition1-CV/2018/05/CER_BDS_Aqua-FM3_Edition1-CV_300309.20180501

ls /ASDC_archive/CERES/BDS/Aqua-FM3_Edition4/2018/03/CER_BDS_Aqua-FM3_Edition4_400407.20180301

FM5:

ls /ASDC_archive/CERES/BDS/NPP-FM5_Edition1-CV/2018/05/CER_BDS_NPP-FM5_Edition1-CV_300309.20180501

ls /ASDC_archive/CERES/BDS/NPP-FM5_Edition1/2018/04/CER_BDS_NPP-FM5_Edition1_100107.20180401

FM6:

ls /ASDC_archive/CERES/BDS/J01-FM6_Edition1-CV/2018/07/CER_BDS_J01-FM6_Edition1-CV_300312.20180701

There should be 8 files for FM1, FM2, FM3, FM5, and FM6.

#### Execution

The production script, CER2.3P1.pl, references a PCF file containing the file names and paths for the test procedures.  The PCF file for the test case is created by executing a combined log/PCF files generator, gen_pcf.CER2.3P1.pl.

The log/PCF files generator requires five command-line arguments, yyyymm (where yyyy is the 4-digit year, and mm is the 2-digit month), “A” for Actual snow input file, “F” for Original ADM structure, “M” for the Instrument Team’s monthly modified Slope Intercept Spectral Correction input (or “N” if not applicable, i.e. prior to Edition2), “T” for Thermal SW Offsets or “K” (for Edition3 processing).  Only in the case of the run script is the day (dd =‘01’) used.

- Terra-FM1:  Edition1-CV

source $ERBELIKEHOME/erbelike/data/input/CER2.3P1/ENV-FM1_1CV_231_1387.csh

setenv yyyy 2018

setenv mm 05

setenv yyyymmdd ${yyyy}${mm}01

cd $ERBELIKEHOME/erbelike/CER2.3P1/rcf

CER2.3P1-SGE_Driver.pl -date $yyyy$mm -snow A -adm F -spcor N -swoff T -clean

Terra-FM1:  Edition4

source $ERBELIKEHOME/erbelike/data/input/CER2.3P1/ENV-FM1_Ed4_231_1387.csh

setenv yyyy 2018

setenv mm 02

setenv yyyymmdd ${yyyy}${mm}01

cd $ERBELIKEHOME/erbelike/CER2.3P1/rcf

CER2.3P1-SGE_Driver.pl -date $yyyy$mm -snow A -adm F -spcor M -swoff T -clean

Terra-FM2:  Edition1-CV

source $ERBELIKEHOME/erbelike/data/input/CER2.3P1/ENV-FM2_1CV_231_1387.csh

setenv yyyy 2018

setenv mm 05

setenv yyyymmdd ${yyyy}${mm}01

cd $ERBELIKEHOME/erbelike/CER2.3P1/rcf

CER2.3P1-SGE_Driver.pl -date $yyyy$mm -snow A -adm F -spcor N -swoff T -clean

Terra-FM2:  Edition4

source $ERBELIKEHOME/erbelike/data/input/CER2.3P1/ENV-FM2_Ed4_231_1387.csh

setenv yyyy 2008

setenv mm 08

setenv yyyymmdd ${yyyy}${mm}01

cd $ERBELIKEHOME/erbelike/CER2.3P1/rcf

CER2.3P1-SGE_Driver.pl -date $yyyy$mm -snow A -adm F -spcor M -swoff T -clean

Aqua-FM3:  Edition1-CV

source $ERBELIKEHOME/erbelike/data/input/CER2.3P1/ENV-FM3_1CV_231_1387.csh

setenv yyyy 2018

setenv mm 05

setenv yyyymmdd ${yyyy}${mm}01

cd $ERBELIKEHOME/erbelike/CER2.3P1/rcf

CER2.3P1-SGE_Driver.pl -date $yyyy$mm -snow A -adm F -spcor N -swoff T -clean

Aqua-FM3:  Edition4

source $ERBELIKEHOME/erbelike/data/input/CER2.3P1/ENV-FM3_Ed4_231_1387.csh

setenv yyyy 2018

setenv mm 03

setenv yyyymmdd ${yyyy}${mm}01

cd $ERBELIKEHOME/erbelike/CER2.3P1/rcf

CER2.3P1-SGE_Driver.pl -date $yyyy$mm -snow A -adm F -spcor M -swoff T -clean

NPP-FM5:  Edition1-CV

source $ERBELIKEHOME/erbelike/data/input/CER2.3P1/ENV-FM5_1CV_231_1387.csh

setenv yyyy 2018

setenv mm 05

setenv yyyymmdd ${yyyy}${mm}01

cd $ERBELIKEHOME/erbelike/CER2.3P1/rcf

CER2.3P1-SGE_Driver.pl -date $yyyy$mm -snow A -adm F -spcor N -swoff T -clean

NPP-FM5:  Edition1

source $ERBELIKEHOME/erbelike/data/input/CER2.3P1/ENV-FM5_Ed1_231_1387.csh

setenv yyyy 2018

setenv mm 04

setenv yyyymmdd ${yyyy}${mm}01

cd $ERBELIKEHOME/erbelike/CER2.3P1/rcf

CER2.3P1-SGE_Driver.pl -date $yyyy$mm -snow A -adm F -spcor N -swoff T -clean

J01-FM6:  Edition1-CV

source $ERBELIKEHOME/erbelike/data/input/CER2.3P1/ENV-FM6_1CV_231_1387.csh

setenv yyyy 2018

setenv mm 07

setenv yyyymmdd ${yyyy}${mm}01

cd $ERBELIKEHOME/erbelike/CER2.3P1/rcf

CER2.3P1-SGE_Driver.pl -date $yyyy$mm -snow A -adm F -spcor N -swoff T -clean

#### Expected Output Files

Each instrument test will have a sampling Strategy ($SS2), a Production Strategy (‘TestPlan’), a Configuration Code ($CC2) and a Data Date ($yyyymmdd).  After the Product Generation Executive (PGE) CER2.3P1 is executed, it should have created the following files in the following directories:

Two files will be generated in the pcf subdirectory:

$ERBELIKEHOME/erbelike/CER2.3P1/rcf/pcf/CER2.3P1_PCF_${SS2}_${PS2_0}_$CC2.$yyyymmdd.log

$ERBELIKEHOME/erbelike/CER2.3P1/rcf/pcf/CER2.3P1_PCF_${SS2}_${PS2_0}_$CC2.$yyyymmdd

Five files and associated .met files will be generated:

$ERBELIKEHOME/erbelike/data/CERES/CQCIX/${SS2}_${PS2_0}/$yyyy/$mm/CER_CQCIX_${SS2}_${PS2_0}_$CC2.$yyyymmdd

$ERBELIKEHOME/erbelike/data/CERES/EID6X/${SS2}_${PS2_0}/$yyyy/$mm/CER_EID6X_${SS2}_${PS2_0}_$CC2.$yyyymmdd

$ERBELIKEHOME/erbelike/data/CERES/CQCD/${SS2}_${PS2_0}/$yyyy/$mm/CER_CQCD_${SS2}_${PS2_0}_$CC2.$yyyymmdd

$ERBELIKEHOME/erbelike/data/CERES/CXDR/${SS2}_${PS2_0}/$yyyy/$mm/CER_CXDR_${SS2}_${PS2_0}_$CC2.$yyyymmdd

$ERBELIKEHOME/erbelike/data/CERES/CMSGX/${SS2}_${PS2_0}/$yyyy/$mm/CER_CMSGX_${SS2}_${PS2_0}_$CC2.$yyyymmdd

#### Exit Codes

All CER2.3P1 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.  This test should complete with “Exit Status = 0”.

#### CER2.3P1 Test Summary

Total Run Time:	~1/2 minute (on P6)

Memory:	5.04 Megabytes

Required Disk Space:	13 Megabytes

### Evaluation Procedures

#### Log and Status File Results

The Error and Status Log Files are to be located in directory $ERBELIKEHOME/erbelike/runlogs/CER2.3P1 after CER2.3P1 has been executed.  These files are:

CER2.3P1_LogReport_${SS2}_${PS2_0}_$CC2.$yyyymmdd

CER2.3P1_LogStatus_${SS2}_${PS2_0}_$CC2.$yyyymmdd

CER2.3P1_LogUser_${SS2}_${PS2_0}_$CC2.$yyyymmdd

#### Metadata Evaluation

The metadata files, which end in extension ‘.met’, are located in the same directory as their corresponding output files after CER2.3P1 has been executed.  Compare the metadata for the test case with the metadata provided in this delivery, using the sdiff command;

cd $ERBELIKEHOME/erbelike/data_exp/CER2.3P1

sdiff -s CER_CXDR_${SS2}_${PS2_0}_$CC2.$yyyymmdd.met $ERBELIKEHOME/erbelike/data/CERES/CXDR/${SS2}_${PS2_0}/$yyyy/$mm/CER_CXDR_${SS2}_${PS2_0}_$CC2.$yyyymmdd.met

sdiff -s CER_EID6X_${SS2}_${PS2_0}_$CC2.$yyyymmdd.met $ERBELIKEHOME/erbelike/data/CERES/EID6X/${SS2}_${PS2_0}/$yyyy/$mm/CER_EID6X_${SS2}_${PS2_0}_$CC2.$yyyymmdd.met

The only differences between the files should be the production times and the directory paths where the tests were run, as well as the host node.

#### Comparison of CQCIX and EID6X

cd $ERBELIKEHOME/erbelike/data_exp/CER2.3P1

sdiff -s -w 240 CER_CQCIX_${SS2}_${PS2_0}_$CC2.$yyyymmdd $ERBELIKEHOME/erbelike/data/CERES/CQCIX/${SS2}_${PS2_0}/$yyyy/$mm/CER_CQCIX_${SS2}_${PS2_0}_$CC2.$yyyymmdd

The only differences between the files should be the production times.

The EID-6 evaluation software will compare the EID6X file created from this test and the EID6X file included in the $ERBELIKEHOME/erbelike/data_exp/CER2.3P1 directory.

To run the compare program after the EID6X output file has been created at $ERBELIKEHOME/erbelike/data/CERES/EID6X/$SS2_$PS2_0/$yyyy/$mm/:

If needed, recompile the comparison code:

cd $ERBELIKEHOME/erbelike/test_suites

make clean -f Makefile.eid6

make -f Makefile.eid6

Run comparison:

cd $ERBELIKEHOME/erbelike/test_suites

CER2.2P1_cmp_eid6_$CPUTYPE.exe $yyyymmdd EID6X1

Evaluation of EID-6 Comparison Software Output

The EID-6 compare program, cmp_eid6, produces the output file cmp_eid6x_$yyyymmdd.out. If it cannot find differences larger than a threshold value (currently set to 0.00025), the compared files are automatically considered scientifically equivalent, and the output file will contain the statement “NO SUCH DIFFERENCES FOUND.”  If there are any such differences, an appropriate message and the conflicting data (for up to 9 records) will be written to the output file.  If more than 9 records differ, the code will terminate.  If not, a record mismatch evaluation will be written at the bottom.

### Solutions to Possible Problems

- All output files are opened with Status = NEW in the CER2.3P1 software.  These files must be removed before re-running these test procedures.  A script, which removes PGE files created via the command line, clr_dir.PGE2.3P1.csh, is located in directory $ERBELIKEHOME/erbelike/CER2.3P1/rcf.  Use the data date (4-digit year, 2-digit month, 2-digit day) as a command-line argument:

clr_dir.PGE2.3P1.csh $yyyymmdd

When running this script, the system message, “Cannot access <filename>:  No such file or directory” may be written to the screen.  This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

Refer to the Message and Log files created in $ERBELIKEHOME/erbelike/runlogs/CER2.3P1 (and $ERBELIKEHOME/erbelike/sge_logs/CER2.3P1 in the case of SGE jobs) for explanations of possible problems.

## CER2.3P2 CERES ERBE-like Monthly Inversion for the Last Day of the Previous Month

### Stand-alone Test Procedures

Before starting the processing of CER2.3P2, make sure the instrument-specific test BDS input files are accessible from the testing directory:

setenv ERBELIKEHOME $CERESHOME

cd $ERBELIKEHOME/erbelike/CER2.3P2/rcf

FM1:

ls /ASDC_archive/CERES/BDS/Terra-FM1_Edition1-CV/2018/01/CER_BDS_Terra-FM1_Edition1-CV_300309.20180131

ls /ASDC_archive/CERES/BDS/Terra-FM1_Edition4/2018/03/CER_BDS_Terra-FM1_Edition4_400407.20180331

FM2:

ls /ASDC_archive/CERES/BDS/Terra-FM1_Edition1-CV/2018/01/CER_BDS_Terra-FM1_Edition1-CV_300309.20180131

ls /ASDC_archive/CERES/BDS/Terra-FM1_Edition4/2008/12/CER_BDS_Terra-FM1_Edition4_400403.20081231

FM3:

ls /ASDC_archive/CERES/BDS/Aqua-FM3_Edition1-CV/2018/01/CER_BDS_Aqua-FM3_Edition1-CV_300309.20180131

ls /ASDC_archive/CERES/BDS/Aqua-FM3_Edition4/2018/03/CER_BDS_Aqua-FM3_Edition4_400407.20180331

FM5:

ls /ASDC_archive/CERES/BDS/NPP-FM5_Edition1-CV/2018/03/CER_BDS_NPP-FM5_Edition1-CV_300309.20180331

ls /ASDC_archive/CERES/BDS/NPP-FM5_Edition1/2018/03/CER_BDS_NPP-FM5_Edition1_100107.20180331

FM6:

ls /ASDC_archive/CERES/BDS/J01-FM6_Edition1-CV/2018/07/CER_BDS_J01-FM6_Edition1-CV_300312.20180731

There should be 6 files for Terra and Aqua (3 instruments x 2 editions), 2 files (1 instrument x 2 Editions) for FM5 and one Edition1-CV file for FM6.

#### Execution

The production script, CER2.3P2.pl, references a PCF file containing the file names and paths for the test procedures.  The PCF file for each test case is created by executing a combined PCF/log files generator, gen_pcf.CER2.3P2.pl.

The PCF/log files generator requires five command-line arguments, yyyymm (where yyyy is the 4-digit year, and mm is the 2-digit month), “A” for Actual snow input file, “F” for Original ADM structure, “M” for the Instrument Team’s monthly modified Slope Intercept Spectral Correction input (or “N” if not applicable, i.e. prior to Edition2), “T” for Thermal SW Offsets or “K” (Edition3 processing).  Only the run script requires the day (dd) to be specified.

- Terra-FM1:  Edition1-CV

source $ERBELIKEHOME/erbelike/data/input/CER2.3P2/ENV-FM1_1CV_232_1387.csh

setenv yyyy 2018

setenv mm 04

setenv yyyymmdd ${yyyy}${mm}30

cd $ERBELIKEHOME/erbelike/CER2.3P2/rcf

CER2.3P2-SGE_Driver.pl -date $yyyy$mm -snow A -adm F -spcor N -swoff T -clean

Terra-FM1:  Edition4

source $ERBELIKEHOME/erbelike/data/input/CER2.3P2/ENV-FM1_Ed4_232_1387.csh

setenv yyyy 2018

setenv mm 03

setenv yyyymmdd ${yyyy}${mm}31

cd $ERBELIKEHOME/erbelike/CER2.3P2/rcf

CER2.3P2-SGE_Driver.pl -date $yyyy$mm -snow A -adm F -spcor M -swoff T -clean

Terra-FM2:  Edition1-CV

source $ERBELIKEHOME/erbelike/data/input/CER2.3P2/ENV-FM2_1CV_232_1387.csh

setenv yyyy 2018

setenv mm 03

setenv yyyymmdd ${yyyy}${mm}31

cd $ERBELIKEHOME/erbelike/CER2.3P2/rcf

CER2.3P2-SGE_Driver.pl -date $yyyy$mm -snow A -adm F -spcor N -swoff T -clean

Terra-FM2:  Edition4

source $ERBELIKEHOME/erbelike/data/input/CER2.3P2/ENV-FM2_Ed4_232_1387.csh

setenv yyyy 2008

setenv mm 08

setenv yyyymmdd ${yyyy}${mm}31

cd $ERBELIKEHOME/erbelike/CER2.3P2/rcf

CER2.3P2-SGE_Driver.pl -date $yyyy$mm -snow A -adm F -spcor M -swoff T -clean

Aqua-FM3:  Edition1-CV

source $ERBELIKEHOME/erbelike/data/input/CER2.3P2/ENV-FM3_1CV_232_1387.csh

setenv yyyy 2018

setenv mm 03

setenv yyyymmdd ${yyyy}${mm}31

cd $ERBELIKEHOME/erbelike/CER2.3P2/rcf

CER2.3P2-SGE_Driver.pl -date $yyyy$mm -snow A -adm F -spcor N -swoff T -clean

Aqua-FM3:  Edition4

source $ERBELIKEHOME/erbelike/data/input/CER2.3P2/ENV-FM3_Ed4_232_1387.csh

setenv yyyy 2018

setenv mm 03

setenv yyyymmdd ${yyyy}${mm}31

cd $ERBELIKEHOME/erbelike/CER2.3P2/rcf

CER2.3P2-SGE_Driver.pl -date $yyyy$mm -snow A -adm F -spcor M -swoff T -clean

NPP-FM5:  Edition1-CV

source $ERBELIKEHOME/erbelike/data/input/CER2.3P2/ENV-FM5_1CV_232_1387.csh

setenv yyyy 2018

setenv mm 03

setenv yyyymmdd ${yyyy}${mm}31

cd $ERBELIKEHOME/erbelike/CER2.3P2/rcf

CER2.3P2-SGE_Driver.pl -date $yyyy$mm -snow A -adm F -spcor N -swoff T -clean

NPP-FM5:  Edition1

source $ERBELIKEHOME/erbelike/data/input/CER2.3P2/ENV-FM5_Ed1_232_1387.csh

setenv yyyy 2018

setenv mm 03

setenv yyyymmdd ${yyyy}${mm}31

cd $ERBELIKEHOME/erbelike/CER2.3P2/rcf

CER2.3P2-SGE_Driver.pl -date $yyyy$mm -snow A -adm F -spcor N -swoff T -clean

Edition1-CV:  FM6

source $ERBELIKEHOME/erbelike/data/input/CER2.3P2/ENV-FM6_1CV_232_1387.csh

setenv yyyy 2018

setenv mm 07

setenv yyyymmdd ${yyyy}${mm}31

cd $ERBELIKEHOME/erbelike/CER2.3P2/rcf

CER2.3P2-SGE_Driver.pl -date $yyyy$mm -snow A -adm F -spcor N -swoff T -clean

#### Expected Output Files

Each instrument test will have a sampling Strategy ($SS2), a Production Strategy (‘TestPlan’), a Configuration Code ($CC2) and a Data Date ($yyyymmdd).  After the Product Generation Executive (PGE) CER2.3P2 is executed, it should have created the following files in the following directories:

Two files will be generated in the pcf subdirectory:

$ERBELIKEHOME/erbelike/CER2.3P2/rcf/pcf/CER2.3P2_PCF_${SS2}_${PS2_0}_$CC2.$yyyymmdd.log

$ERBELIKEHOME/erbelike/CER2.3P2/rcf/pcf/CER2.3P2_PCF_${SS2}_${PS2_0}_$CC2.$yyyymmdd

Five files and associated .met files will be generated:

$ERBELIKEHOME/erbelike/data/CERES/CQCIX/${SS2}_${PS2_0}/$yyyy/$mm/CER_CQCIX_${SS2}_${PS2_0}_$CC2.$yyyymmdd

$ERBELIKEHOME/erbelike/data/CERES/EID6X/${SS2}_${PS2_0}/$yyyy/$mm/CER_EID6X_${SS2}_${PS2_0}_$CC2.$yyyymmdd

$ERBELIKEHOME/erbelike/data/CERES/CQCD/${SS2}_${PS2_0}/$yyyy/$mm/CER_CQCD_${SS2}_${PS2_0}_$CC2.$yyyymmdd

$ERBELIKEHOME/erbelike/data/CERES/CXDR/${SS2}_${PS2_0}/$yyyy/$mm/CER_CXDR_${SS2}_${PS2_0}_$CC2.$yyyymmdd

$ERBELIKEHOME/erbelike/data/CERES/CMSGX/${SS2}_${PS2_0}/$yyyy/$mm/CER_CMSGX_${SS2}_${PS2_0}_$CC2.$yyyymmdd

#### Exit Codes

All CER2.3P2 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.  This test should complete with “Exit Status = 0”.

#### CER2.3P2 Test Summary

Total Run Time:	~ 1/2 minute (on P6)

Memory:	5.3 Megabytes

Required Disk Space:	13 Megabytes

### Evaluation Procedures

#### Log and Status File Results

The Error and Status Log Files are located in directory $ERBELIKEHOME/erbelike/runlogs/CER2.3P2 after CER2.3P2 has been executed.

These files are:

CER2.3P2_LogReport_${SS2}_${PS2_0}_$CC2.$yyyymmdd

CER2.3P2_LogStatus_${SS2}_${PS2_0}_$CC2.$yyyymmdd

CER2.3P2_LogUser_${SS2}_${PS2_0}_$CC2.$yyyymmdd

#### Metadata Evaluation

The metadata files, which end in extension ‘.met’, are located in the same directory as their corresponding output files after CER2.3P2 has been executed.  Compare the metadata for the test case with the metadata provided in this delivery, using the sdiff command:

cd $ERBELIKEHOME/erbelike/data_exp/CER2.3P2

sdiff -s CER_CXDR_${SS2}_${PS2_0}_$CC2.$yyyymmdd.met $ERBELIKEHOME/erbelike/data/CERES/CXDR/${SS2}_${PS2_0}/$yyyy/$mm/CER_CXDR_${SS2}_${PS2_0}_$CC2.$yyyymmdd.met

sdiff -s CER_EID6X_${SS2}_${PS2_0}_$CC2.$yyyymmdd.met $ERBELIKEHOME/erbelike/data/CERES/EID6X/${SS2}_${PS2_0}/$yyyy/$mm/CER_EID6X_${SS2}_${PS2_0}_$CC2.$yyyymmdd.met

The only differences between the files should be the production times, directory paths, and the host name.

#### Comparison of CQCIX and EIDX

cd $ERBELIKEHOME/erbelike/data_exp/CER2.3P2

sdiff -s -w 240 CER_CQCIX_${SS2}_${PS2_0}_$CC2.$yyyymmdd $ERBELIKEHOME/erbelike/data/CERES/CQCIX/${SS2}_${PS2_0}/$yyyy/$mm/CER_CQCIX_${SS2}_${PS2_0}_$CC2.$yyyymmdd

The only differences between the files should be the production times.

Execution of EID-6 Comparison Software

The EID-6 evaluation software will compare the EID6X file created from this test and the EID6X file included in the $ERBELIKEHOME/erbelike/data_exp/CER2.3P2 directory.

To run the compare program after the EID6X output file has been created at $ERBELIKEHOME/erbelike/data/CERES/EID6X/$SS2_$PS2_0/$yyyy/$mm/:

If needed, recompile the comparison code:

cd $ERBELIKEHOME/erbelike/test_suites

make clean -f Makefile.eid6

make -f Makefile.eid6

Run comparison:

cd $ERBELIKEHOME/erbelike/test_suites

CER2.2P1_cmp_eid6_$CPUTYPE.exe $yyyymmdd EID6X2

#### Evaluation of EID-6 Comparison Software Output

The EID-6 compare program, cmp_eid6, produces the output file cmp_eid6x_$yyyymmdd.out. If it cannot find differences larger than a threshold value (currently set to 0.00025), the compared files are automatically considered scientifically equivalent, and the output file will contain the statement “NO SUCH DIFFERENCES FOUND.”  If there are any such differences, an appropriate message and the conflicting data (for up to 9 records) will be written to the output file.  If more than 9 records differ, the code will terminate.  If not, a record mismatch evaluation will be written at the bottom.

### Solutions to Possible Problems

- All output files are opened with Status = NEW in the CER2.3P2 software.  These files must be removed before rerunning these test procedures.  A script, which removes PGE files created via the command line, clr_dir.PGE2.3P2.csh, is located in directory $ERBELIKEHOME/erbelike/CER2.3P2/rcf.  Use the data date (4-digit year, 2-digit month, 2-digit day) as a command-line argument:

clr_dir.PGE2.3P2.csh $yyyymmdd

When running this script, the system message, “Cannot access <filename>:  No such file or directory” may be written to the screen.  This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

Refer to the Message and Log files created in $ERBELIKEHOME/erbelike/runlogs/CER2.3P2 (and $ERBELIKEHOME/erbelike/sge_logs/CER2.2P1 in the case of SGE jobs) for explanations of possible problems.

## CER3.1P1 CERES ERBE-like Monthly TOA Flux Averaging for a Single Instrument

### Stand-alone Test Procedures

Before starting the processing of CER3.1P1, make sure the EID6 input files for this test plan are accessible from the testing directory:

setenv ERBELIKEHOME $CERESHOME

cd $ERBELIKEHOME/erbelike/CER3.1P1/rcf

FM1-4:

ls /ASDC_archive/CERES/EID6/*Ed*V*/2009/06/*200906?? | wc -l

ls /ASDC_archive/CERES/EID6/*trk*/2011/02/*201102?? | wc -l

There should be 120 files covering 30 days x 4 instruments x 1 Edition, and 56 files covering 28 days on 2 Ed3 (cross-track) platforms.  Also, make sure the overlap files of the corresponding previous and following months are also available:

FM1-4:

ls /ASDC_archive/CERES/CXDR/*Ed*V*/2009/05/*20090531 | wc -l

ls /ASDC_archive/CERES/CXDR/*Ed*V*/2009/07/*20090701 | wc -l

ls /ASDC_archive/CERES/CXDR/*trk*/2011/01/*20110131

ls /ASDC_archive/CERES/CXDR/*trk*/2011/03/*20110301

There should be 4 files covering one day x 4 instrument x 1 Edition cases, and a single file for each platform-edition-day combinations.  For the FM5 test case, since no Edition3  data is expected, only AtLaunch input data will be tested:

FM5:

ls /ASDC_archive/CERES/EID6/*5*h/2012/02/*201202?? | wc -l

ls /ASDC_archive/CERES/CXDR/*5*h/2012/01/*20120131

ls /ASDC_archive/CERES/CXDR/*5*h/2012/03/*20120301

Currently, there are only 28 FM5 EID6 files available and no FM5 CXDR files for this test month.  Verify that this is still the case.

#### Execution

The production script, CER3.1P1.pl, references a Process Control File (PCF) containing the file names and paths for the test procedures.  The PCF for the test case is created by executing a combined PCF log and PCF generator, gen_pcf.CER3.1.pl.

The PCF generator requires only one command-line argument, the data date yyyymm (where yyyy is the 4-digit year, and mm is the 2-digit month).

- Terra-FM1:  Edition1-CV

Command Line Test:

setenv ERBELIKEHOME $CERESHOME

cd $ERBELIKEHOME/erbelike/CER3.1P1/rcf

source $ERBELIKEHOME/erbelike/data/input/CER3.1P1/TestPlan_ENV_FM1Ed1.csh

clr_dir.PGE3.1P1.csh 200906

gen_pcf.CER3.1P1.pl 200906

CER3.1P1.pl $SS3_$PS2_0_$CC3.$yyyymm

SGE Test:

setenv ERBELIKEHOME $CERESHOME

cd $ERBELIKEHOME/erbelike/CER3.1P1/rcf

source $ERBELIKEHOME/erbelike/data/input/CER3.1P1/TestPlan_ENV_FM1Ed1.csh

clr_dir.PGE3.1P1.csh 200906

CER3.1P1-SGE_Driver.pl -d 200906

- Terra-FM2:  Edition1-CV

Command Line Test:

setenv ERBELIKEHOME $CERESHOME

cd $ERBELIKEHOME/erbelike/CER3.1P1/rcf

source $ERBELIKEHOME/erbelike/data/input/CER3.1P1/TestPlan_ENV_FM2Ed1.csh

clr_dir.PGE3.1P1.csh 200906

gen_pcf.CER3.1P1.pl 200906

CER3.1P1.pl $SS3_$PS2_0_$CC3.$yyyymm

SGE Test:

setenv ERBELIKEHOME $CERESHOME

cd $ERBELIKEHOME/erbelike/CER3.1P1/rcf

source $ERBELIKEHOME/erbelike/data/input/CER3.1P1/TestPlan_ENV_FM2Ed1.csh

clr_dir.PGE3.1P1.csh 200906

CER3.1P1-SGE_Driver.pl -d 200906

- Aqua-FM3:  Edition1-CV

Command Line Test:

setenv ERBELIKEHOME $CERESHOME

cd $ERBELIKEHOME/erbelike/CER3.1P1/rcf

source $ERBELIKEHOME/erbelike/data/input/CER3.1P1/TestPlan_ENV_FM3Ed1.csh

clr_dir.PGE3.1P1.csh 200906

gen_pcf.CER3.1P1.pl 200906

CER3.1P1.pl $SS3_$PS2_0_$CC3.$yyyymm

SGE Test:

setenv ERBELIKEHOME $CERESHOME

cd $ERBELIKEHOME/erbelike/CER3.1P1/rcf

source $ERBELIKEHOME/erbelike/data/input/CER3.1P1/TestPlan_ENV_FM3Ed1.csh

clr_dir.PGE3.1P1.csh 200906

CER3.1P1-SGE_Driver.pl -d 200906

- Aqua-FM4:  Edition1-CV

Command Line Test:

setenv ERBELIKEHOME $CERESHOME

cd $ERBELIKEHOME/erbelike/CER3.1P1/rcf

source $ERBELIKEHOME/erbelike/data/input/CER3.1P1/TestPlan_ENV_FM4Ed1.csh

clr_dir.PGE3.1P1.csh 200906

gen_pcf.CER3.1P1.pl 200906

CER3.1P1.pl $SS3_$PS2_0_$CC3.$yyyymm

SGE Test:

setenv ERBELIKEHOME $CERESHOME

cd $ERBELIKEHOME/erbelike/CER3.1P1/rcf

source $ERBELIKEHOME/erbelike/data/input/CER3.1P1/TestPlan_ENV_FM4Ed1.csh

clr_dir.PGE3.1P1.csh 200906

CER3.1P1-SGE_Driver.pl -d 200906

- NPP-FM5: Edition1-CV

Command Line Test:

setenv ERBELIKEHOME $CERESHOME

cd $ERBELIKEHOME/erbelike/CER3.1P1/rcf

source $ERBELIKEHOME/erbelike/data/input/CER3.1P1/TestPlan_ENV_FM5Ed1.csh

clr_dir.PGE3.1P1.csh 201202

gen_pcf.CER3.1P1.pl 201202

CER3.1P1.pl $SS3_$PS2_0_$CC3.$yyyymm

SGE Test:

setenv ERBELIKEHOME $CERESHOME

cd $ERBELIKEHOME/erbelike/CER3.1P1/rcf

source $ERBELIKEHOME/erbelike/data/input/CER3.1P1/TestPlan_ENV_FM5Ed1.csh

clr_dir.PGE3.1P1.csh 201202

CER3.1P1-SGE_Driver.pl -d 201202

- Edition3:  Terra

Command Line Test:

setenv ERBELIKEHOME $CERESHOME

cd $ERBELIKEHOME/erbelike/CER3.1P1/rcf

source $ERBELIKEHOME/erbelike/data/input/CER3.1P1/TestPlan_ENV_TerraEd3.csh

clr_dir.PGE3.1P1.csh 201102

gen_pcf.CER3.1P1.pl 201102

CER3.1P1.pl $SS3_$PS2_0_$CC3.$yyyymm

SGE Test:

setenv ERBELIKEHOME $CERESHOME

cd $ERBELIKEHOME/erbelike/CER3.1P1/rcf

source $ERBELIKEHOME/erbelike/data/input/CER3.1P1/TestPlan_ENV_TerraEd3.csh

clr_dir.PGE3.1P1.csh 201102

CER3.1P1-SGE_Driver.pl -d 201102

- Edition3:  Aqua

Command Line Test:

setenv ERBELIKEHOME $CERESHOME

cd $ERBELIKEHOME/erbelike/CER3.1P1/rcf

source $ERBELIKEHOME/erbelike/data/input/CER3.1P1/TestPlan_ENV_AquaEd3.csh

clr_dir.PGE3.1P1.csh 201102

gen_pcf.CER3.1P1.pl 201102

CER3.1P1.pl $SS3_$PS2_0_$CC3.$yyyymm

SGE Test:

setenv ERBELIKEHOME $CERESHOME

cd $ERBELIKEHOME/erbelike/CER3.1P1/rcf

source $ERBELIKEHOME/erbelike/data/input/CER3.1P1/TestPlan_ENV_AquaEd3.csh

clr_dir.PGE3.1P1.csh 201102

CER3.1P1-SGE_Driver.pl -d 201102

- Edition1-CV: FM6

SGE Test:

setenv mm 04

setenv yyyy 2018

setenv yyyymm 201804

setenv ERBELIKEHOME $CERESHOME

cd $ERBELIKEHOME/erbelike/CER3.1P1/rcf

source $ERBELIKEHOME/erbelike/data/input/CER3.1P1/ENV-1356-cer311.csh

clr_dir.PGE3.1P1.csh $yyyymm

CER3.1P1-SGE_Driver.pl -d $yyyymm

#### Expected Output Files

Each instrument test will have a sampling Strategy ($SS3), a Production Strategy (‘TestPlan’), a Configuration Code ($CC3) and a Data Date ($yyyymm).  After the Product Generation Executive (PGE) CER3.1P1 is executed, it should have created the following files in the following directories:

$ERBELIKEHOME/erbelike/CER3.1P1/rcf/pcf/CER3.1P1_PCF_$SS3_$PS2_0_$CC3.$yyyymm.log

$ERBELIKEHOME/erbelike/CER3.1P1/rcf/pcf/CER3.1P1_PCF_$SS3_$PS2_0_$CC3.$yyyymm

$ERBELIKEHOME/erbelike/data/CERES/DQCA/$SS3_$PS2_0/$yyyy/$mm/CER_DQCA_$SS3_$PS2_0_$CC3.$yyyymm

$ERBELIKEHOME/erbelike/data/CERES/DQCA/$SS3_$PS2_0/$yyyy/$mm/CER_DQCA_$SS3_$PS2_0_$CC3.$yyyymm.met

$ERBELIKEHOME/erbelike/data/CERES/DQCA/$SS3_$PS2_0/$yyyy/$mm/CER_DQCA_$SS3_$PS2_0_$CC3.$yyyymm

$ERBELIKEHOME/erbelike/data/CERES/DQCB/$SS3_$PS2_0/$yyyy/$mm/CER_DQCB_$SS3_$PS2_0_$CC3.$yyyymm.met

$ERBELIKEHOME/erbelike/data/CERES/DQCC/$SS3_$PS2_0/$yyyy/$mm/CER_DQCC_$SS3_$PS2_0_$CC3.$yyyymm

$ERBELIKEHOME/erbelike/data/CERES/DQCC/$SS3_$PS2_0/$yyyy/$mm/CER_DQCC_$SS3_$PS2_0_$CC3.$yyyymm.met

$ERBELIKEHOME/erbelike/data/CERES/DQCD/$SS3_$PS2_0/$yyyy/$mm/CER_DQCD_$SS3_$PS2_0_$CC3.$yyyymm

$ERBELIKEHOME/erbelike/data/CERES/DQCD/$SS3_$PS2_0/$yyyy/$mm/CER_DQCD_$SS3_$PS2_0_$CC3.$yyyymm.met

$ERBELIKEHOME/erbelike/data/CERES/DQCG/$SS3_$PS2_0/$yyyy/$mm/CER_DQCG_$SS3_$PS2_0_$CC3.$yyyymm

$ERBELIKEHOME/erbelike/data/CERES/DQCG/$SS3_$PS2_0/$yyyy/$mm/CER_DQCG_$SS3_$PS2_0_$CC3.$yyyymm.met

$ERBELIKEHOME/erbelike/data/CERES/DQCS/$SS3_$PS2_0/$yyyy/$mm/CER_DQCS_$SS3_$PS2_0_$CC3.$yyyymm

$ERBELIKEHOME/erbelike/data/CERES/DQCS/$SS3_$PS2_0/$yyyy/$mm/CER_DQCS_$SS3_$PS2_0_$CC3.$yyyymm.met

$ERBELIKEHOME/erbelike/data/CERES/DQCX/$SS3_$PS2_0/$yyyy/$mm/CER_DQCX_$SS3_$PS2_0_$CC3.$yyyymm

$ERBELIKEHOME/erbelike/data/CERES/DQCX/$SS3_$PS2_0/$yyyy/$mm/CER_DQCX_$SS3_$PS2_0_$CC3.$yyyymm.met

$ERBELIKEHOME/erbelike/data/CERES/DES9/$SS3_$PS2_0/$yyyy/$mm/CER_DES9_$SS3_$PS2_0_$CC3.$yyyymm

$ERBELIKEHOME/erbelike/data/CERES/DES9/$SS3_$PS2_0/$yyyy/$mm/CER_DES9_$SS3_$PS2_0_$CC3.$yyyymm.met

$ERBELIKEHOME/erbelike/data/CERES/ES9/$SS3_$PS2_0/$yyyy/$mm/CER_ES9_$SS3_$PS2_0_$CC3.$yyyymm

$ERBELIKEHOME/erbelike/data/CERES/ES9/$SS3_$PS2_0/$yyyy/$mm/CER_ES9_$SS3_$PS2_0_$CC3.$yyyymm.met

$ERBELIKEHOME/erbelike/data/CERES/DES4/$SS3_$PS2_0/$yyyy/$mm/CER_DES4_$SS3_$PS2_0_$CC3.$yyyymm

$ERBELIKEHOME/erbelike/data/CERES/DES4/$SS3_$PS2_0/$yyyy/$mm/CER_DES4_$SS3_$PS2_0_$CC3.$yyyymm.met

$ERBELIKEHOME/erbelike/data/CERES/ES4/$SS3_$PS2_0/$yyyy/$mm/CER_ES4_$SS3_$PS2_0_$CC3.$yyyymm

$ERBELIKEHOME/erbelike/data/CERES/ES4/$SS3_$PS2_0/$yyyy/$mm/CER_ES4_$SS3_$PS2_0_$CC3.$yyyymm.met

$ERBELIKEHOME/erbelike/data/CERES/ES4G1/$SS3_$PS2_0/$yyyy/$mm/CER_ES4G1_$SS3_$PS2_0_$CC3.$yyyymm

$ERBELIKEHOME/erbelike/data/CERES/ES4G1/$SS3_$PS2_0/$yyyy/$mm/CER_ES4G1_$SS3_$PS2_0_$CC3.$yyyymm.met

$ERBELIKEHOME/erbelike/data/CERES/ES4G2/$SS3_$PS2_0/$yyyy/$mm/CER_ES4G2_$SS3_$PS2_0_$CC3.$yyyymm

$ERBELIKEHOME/erbelike/data/CERES/ES4G2/$SS3_$PS2_0/$yyyy/$mm/CER_ES4G2_$SS3_$PS2_0_$CC3.$yyyymm.met

$ERBELIKEHOME/erbelike/data/CERES/ES4G3/$SS3_$PS2_0/$yyyy/$mm/CER_ES4G3_$SS3_$PS2_0_$CC3.$yyyymm

$ERBELIKEHOME/erbelike/data/CERES/ES4G3/$SS3_$PS2_0/$yyyy/$mm/CER_ES4G3_$SS3_$PS2_0_$CC3.$yyyymm.met

$ERBELIKEHOME/erbelike/data/CERES/ES4G4/$SS3_$PS2_0/$yyyy/$mm/CER_ES4G4_$SS3_$PS2_0_$CC3.$yyyymm

$ERBELIKEHOME/erbelike/data/CERES/ES4G4/$SS3_$PS2_0/$yyyy/$mm/CER_ES4G4_$SS3_$PS2_0_$CC3.$yyyymm.met

$ERBELIKEHOME/erbelike/data/CERES/DMSG/$SS3_$PS2_0/$yyyy/$mm/CER_DMSG_$SS3_$PS2_0_$CC3.$yyyymm

$ERBELIKEHOME/erbelike/data/CERES/DMSG/$SS3_$PS2_0/$yyyy/$mm/CER_DMSG_$SS3_$PS2_0_$CC3.$yyyymm.met

$ERBELIKEHOME/erbelike/web/CER3.1P1/qc/CER_DQCBW_$SS3_$PS2_0_$CC3.$yyyymm

$ERBELIKEHOME/erbelike/web/CER3.1P1/qc/CER_DQCGW_$SS3_$PS2_0_$CC3.$yyyymm

$ERBELIKEHOME/erbelike/data/CERES/ES4G/$SS3_$PS2_0/$yyyy/$mm/CER_ES4G_$SS3_$PS2_0_$CC3.$yyyymm\_1

$ERBELIKEHOME/erbelike/data/CERES/ES4G/$SS3_$PS2_0/$yyyy/$mm/CER_ES4G_$SS3_$PS2_0_$CC3.$yyyymm\_2

$ERBELIKEHOME/erbelike/data/CERES/ES4G/$SS3_$PS2_0/$yyyy/$mm/CER_ES4G_$SS3_$PS2_0_$CC3.$yyyymm\_3

$ERBELIKEHOME/erbelike/data/CERES/ES4G/$SS3_$PS2_0/$yyyy/$mm/CER_ES4G_$SS3_$PS2_0_$CC3.$yyyymm\_4

$ERBELIKEHOME/erbelike/data/CERES/ES4G/$SS3_$PS2_0/$yyyy/$mm/CER_ES4G_$SS3_$PS2_0_$CC3.$yyyymm\_5

$ERBELIKEHOME/erbelike/data/CERES/ES4G/$SS3_$PS2_0/$yyyy/$mm/CER_ES4G_$SS3_$PS2_0_$CC3.$yyyymm\_6

$ERBELIKEHOME/erbelike/data/CERES/ES4G/$SS3_$PS2_0/$yyyy/$mm/CER_ES4G_$SS3_$PS2_0_$CC3.$yyyymm\_7

$ERBELIKEHOME/erbelike/data/CERES/ES4G/$SS3_$PS2_0/$yyyy/$mm/CER_ES4G_$SS3_$PS2_0_$CC3.$yyyymm\_8

$ERBELIKEHOME/erbelike/data/CERES/ES4G/$SS3_$PS2_0/$yyyy/$mm/CER_ES4G_$SS3_$PS2_0_$CC3.$yyyymm\_9

$ERBELIKEHOME/erbelike/web/CER3.1P1/s4g/gif/S4G_${yyyymm}_7/MH_NET_CF_R2520.gif

$ERBELIKEHOME/erbelike/web/CER3.1P1/s4g/gif/S4G_${yyyymm}_7/MH_SW_CF_R2520.gif

$ERBELIKEHOME/erbelike/web/CER3.1P1/s4g/gif/S4G_${yyyymm}_7/MH_LW_CF_R2520.gif

$ERBELIKEHOME/erbelike/web/CER3.1P1/s4g/gif/S4G_${yyyymm}_7/MH_SW_R2520.gif

$ERBELIKEHOME/erbelike/web/CER3.1P1/s4g/gif/S4G_${yyyymm}_7/MH_CS_SW_R2520.gif

$ERBELIKEHOME/erbelike/web/CER3.1P1/s4g/gif/S4G_${yyyymm}_7/MH_CS_ALB_R2520.gif

$ERBELIKEHOME/erbelike/web/CER3.1P1/s4g/gif/S4G_${yyyymm}_7/MH_LW_R2520.gif

$ERBELIKEHOME/erbelike/web/CER3.1P1/s4g/gif/S4G_${yyyymm}_7/MH_CS_LW_R2520.gif

$ERBELIKEHOME/erbelike/web/CER3.1P1/s4g/gif/S4G_${yyyymm}_7/MH_ALB_R2520.gif

#### Exit Codes

All CER3.1P1 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.  This test should complete with “Exit Status = 0”.

#### CER3.1P1 Test Summary

Total Run Time:	3 minutes (on P6)

Memory:	288 Megabytes

Required Disk Space:	192 Megabytes (output data)

### Evaluation Procedures

#### Log and Status File Results

The Error and Status Log Files are located in directory $ERBELIKEHOME/erbelike/runlogs/CER3.1P1 after CER3.1P1 has been executed.  These files are:

CER3.1P1_LogReport_$SS3_$PS2_0_$CC3.$yyyymm

CER3.1P1_LogStatus_$SS3_$PS2_0_$CC3.$yyyymm

CER3.1P1_LogUser_$SS3_$PS2_0_$CC3.$yyyymm

#### Metadata Evaluation

The metadata files, which end in extension ‘.met’, are located in the same directory as their corresponding output files after CER3.1P1 has been executed.  Compare the metadata for the test case with the metadata provided in this delivery, using the sdiff command:

sdiff -s $ERBELIKEHOME/erbelike/data/CERES/DES9/$SS3_$PS2_0/$yyyy/$mm/CER_DES9_$SS3_$PS2_0_$CC3.$yyyymm.met $ERBELIKEHOME/erbelike/data_exp/CER3.1P1/CER_DES9_$SS3_$PS2_0_$CC3.$yyyymm.met

sdiff -s $ERBELIKEHOME/erbelike/data/CERES/DES4/$SS3_$PS2_0/$yyyy/$mm/CER_DES4_$SS3_$PS2_0_$CC3.$yyyymm.met $ERBELIKEHOME/erbelike/data_exp/CER3.1P1/CER_DES4_$SS3_$PS2_0_$CC3.$yyyymm.met

The only differences between the files should be the production times and the directory paths where the tests were run.

#### Output Data Evaluation

##### Execution of HDF ES-4 Comparison Utility

The hdiff utility compares 2 files containing HDF data.  The two files to be compared are entered as command-line arguments.

Compare the ES4 for the test case:

hdiff -d -t 0.1 $ERBELIKEHOME/erbelike/data/CERES/ES4/$SS3_$PS2_0/$yyyy/$mm/*_$CC3.$yyyymm $ERBELIKEHOME/erbelike/data_exp/CER3.1P1/*$SS3\_*$CC3.$yyyymm

hdiff -d -t 0.01 $ERBELIKEHOME/erbelike/data/CERES/ES4/$SS3_$PS2_0/$yyyy/$mm/*_$CC3.$yyyymm $ERBELIKEHOME/erbelike/data_exp/CER3.1P1/*$SS3\_*$CC3.$yyyymm | wc -l

Note:  Total Run Time should not exceed 15 secs

##### Evaluation of HDF ES-4 Comparison Software

The ES-4 data comparison tool, hdiff, returns a list of differences by position, parameter name, and values in both files.  If all data differences between the compared files are within the trigger value provided, there will be no output.  As long as the differences are small in both number and magnitude, the files can be considered scientifically equivalent.

For the first test (trigger set at 0.1), only a handful of differences should be found and none should be much greater than 0.1 (i.e. 2 Shortwave flux of 0.100006 and 1 of 0.100002).

For the second test (trigger set at 0.01), one can expect the number of difference to grow to a dozen spread out over different flux parameters.  This could lead to a listing of up to 50 lines.

For FM6 there should be no differences.

##### Evaluation of ES-4 GIF Files

The resulting 9 “gif” images (see Section 3.6.1.2) must be evaluated by an external viewer application that can display an image on a workstation screen running an X server (i.e. display).  The CERES Test Coordinator may contact a member of the ERBE-like Subsystem Team to assist in the evaluation of these gif images.

cd $ERBELIKEHOME/erbelike/web/CER3.1P1/s4g/gif/S4G_${yyyymm}_$ksc

display MH_*_R2520.gif

cd $ERBELIKEHOME/erbelike/data_exp/CER3.1P1/Web/$PS2/S4G_${yyyymm}_7

display MH_*_R2520.gif

Click on each X server window with the right mouse button

Double click matching filenames in both windows and visually compare the two plots.

### Solutions to Possible Problems

- All output files are opened with Status = NEW in the CER3.1P1 software.  These files must be removed before rerunning these test procedures.  A script, which removes PGE files created via the command line, clr_dir.PGE3.1P1, is located in directory $ERBELIKEHOME/erbelike/CER3.1P1/rcf.  Use the data date (4-digit year, 2-digit month) as a command-line argument:

clr_dir.PGE3.1P1.csh $yyyymm

When running this script, the system message, “Cannot access <filename>:  No such file or directory” may be written to the screen.  This message occurs when the script tries to remove an old output directory that does not exist yet for this data instance or was removed during a successful previous run.  Therefore, this does not signify a problem.

Refer to the Message and Log files created in $ERBELIKEHOME/erbelike/runlogs/CER3.1P1 (and $ERBELIKEHOME/erbelike/sge_logs/CER3.1P1 in the case of SGE jobs) for explanations of possible problems.

## CER3.2P1 CERES ERBE-like Monthly TOA Flux Averaging for Multiple Instruments (current default: FM1+FM3)

### Stand-alone Test Procedures

Before starting the processing of CER3.2P1, make sure the DES-9 input files for this test plan (generated by CER3.1P1 in the previous section of the Test Plan) are in the following directory:

cd $ERBELIKEHOME/erbelike/data/CERES/DES9/

ls *_TestPlan/2011/02/CER_DES9_*_TestPlan_221003.201102 (Edition3)

There should be 2 files there for Edition3, where * = Terra, Aqua.

#### Execution

The production script, CER3.2P1, references a Process Control File (PCF) containing the file names and paths for the test procedures.  The PCF for each test case is created by executing a combined PCF log and PCF generator, gen_pcf.CER3.2.pl.  Go to their locations:

cd $ERBELIKEHOME/erbelike/CER3.2P1/rcf

The PCF generator requires one  command-line argument, yyyymm (where yyyy is the 4-digit year, and mm is the 2-digit month), with “1”, indicating FAPS+RAPS data, being optional since default.

- Edition3:  Terra+Aqua

Command Line Test:

setenv ERBELIKEHOME $CERESHOME

cd $ERBELIKEHOME/erbelike/CER3.2P1/rcf

source $ERBELIKEHOME/erbelike/data/input/CER3.2P1/*TerraAquaEd3.csh

clr_dir.PGE3.2P1.csh $yyyymm

gen_pcf.CER3.2P1.pl $yyyymm

CER3.2P1.pl $SS3_2_$PS2_0_$CC3_2.$yyyymm

SGE Test:

setenv ERBELIKEHOME $CERESHOME

cd $ERBELIKEHOME/erbelike/CER3.2P1/rcf

source $ERBELIKEHOME/erbelike/data/input/CER3.2P1/*TerraAquaEd3.csh

clr_dir.PGE3.2P1.csh $yyyymm

CER3.2P1-SGE_Driver.pl -d $yyyymm

#### Expected Output Files

Each instrument test will have a sampling Strategy: $SS3_2, a Production Strategy:  ‘TestPlan’, a Configuration Code: $CC3_2 and a Data Date: $yyyymm.  After Product Generation Executive (PGE) CER3.2P1 is executed, it should have created the following files in the following directories:

$ERBELIKEHOME/erbelike/CER3.2P1/rcf/pcf/:

CER3.2P1_PCF_$SS3_2_$PS2_0_$CC3_2.$yyyymm.log

CER3.2P1_PCF_$SS3_2_$PS2_0_$CC3_2.$yyyymm

$ERBELIKEHOME/erbelike/data/CERES/DQCA/$SS3_2_$PS2_0/$yyyy/$mm:

CER_DQCA_$SS3_2_$PS2_0_$CC3_2.$yyyymm

CER_DQCA_$SS3_2_$PS2_0_$CC3_2.$yyyymm.met

$ERBELIKEHOME/erbelike/data/CERES/DQCB/$SS3_2_$PS2_0/$yyyy/$mm:

CER_DQCB_$SS3_2_$PS2_0_$CC3_2.$yyyymm

CER_DQCB_$SS3_2_$PS2_0_$CC3_2.$yyyymm.met

$ERBELIKEHOME/erbelike/data/CERES/DQCC/$SS3_2_$PS2_0/$yyyy/$mm:

CER_DQCC_$SS3_2_$PS2_0_$CC3_2.$yyyymm

CER_DQCC_$SS3_2_$PS2_0_$CC3_2.$yyyymm.met

$ERBELIKEHOME/erbelike/data/CERES/DQCG/$SS3_2_$PS2_0/$yyyy/$mm:

CER_DQCG_$SS3_2_$PS2_0_$CC3_2.$yyyymm

CER_DQCG_$SS3_2_$PS2_0_$CC3_2.$yyyymm.met

$ERBELIKEHOME/erbelike/data/CERES/DES9/$SS3_2_$PS2_0/$yyyy/$mm:

CER_DES9_$SS3_2_$PS2_0_$CC3_2.$yyyymm

CER_DES9_$SS3_2_$PS2_0_$CC3_2.$yyyymm.met

$ERBELIKEHOME/erbelike/data/CERES/ES9/$SS3_2_$PS2_0/$yyyy/$mm:

CER_ES9_$SS3_2_$PS2_0_$CC3_2.$yyyymm

CER_ES9_$SS3_2_$PS2_0_$CC3_2.$yyyymm.met

$ERBELIKEHOME/erbelike/data/CERES/DES4/$SS3_2_$PS2_0/$yyyy/$mm:

CER_DES4_$SS3_2_$PS2_0_$CC3_2.$yyyymm

CER_DES4_$SS3_2_$PS2_0_$CC3_2.$yyyymm.met

$ERBELIKEHOME/erbelike/data/CERES/ES4/$SS3_2_$PS2_0/$yyyy/$mm:

CER_ES4_$SS3_2_$PS2_0_$CC3_2.$yyyymm

CER_ES4_$SS3_2_$PS2_0_$CC3_2.$yyyymm.met

$ERBELIKEHOME/erbelike/data/CERES/ES4G1/$SS3_2_$PS2_0/$yyyy/$mm:

CER_ES4G1_$SS3_2_$PS2_0_$CC3_2.$yyyymm

CER_ES4G1_$SS3_2_$PS2_0_$CC3_2.$yyyymm.met

$ERBELIKEHOME/erbelike/data/CERES/ES4G2/$SS3_2_$PS2_0/$yyyy/$mm:

CER_ES4G2_$SS3_2_$PS2_0_$CC3_2.$yyyymm

CER_ES4G2_$SS3_2_$PS2_0_$CC3_2.$yyyymm.met

$ERBELIKEHOME/erbelike/data/CERES/ES4G3/$SS3_2_$PS2_0/$yyyy/$mm:

CER_ES4G3_$SS3_2_$PS2_0_$CC3_2.$yyyymm

CER_ES4G3_$SS3_2_$PS2_0_$CC3_2.$yyyymm.met

$ERBELIKEHOME/erbelike/data/CERES/ES4G4/$SS3_2_$PS2_0/$yyyy/$mm:

CER_ES4G4_$SS3_2_$PS2_0_$CC3_2.$yyyymm

CER_ES4G4_$SS3_2_$PS2_0_$CC3_2.$yyyymm.met

$ERBELIKEHOME/erbelike/data/CERES/DMSG/$SS3_2_$PS2_0/$yyyy/$mm:

CER_DMSG_$SS3_2_$PS2_0_$CC3_2.$yyyymm

CER_DMSG_$SS3_2_$PS2_0_$CC3_2.$yyyymm.met

$ERBELIKEHOME/erbelike/web/CER3.2P1/qc/:

CER_DQCBW_$SS3_2_$PS2_0_$CC3_2.$yyyymm

CER_DQCGW_$SS3_2_$PS2_0_$CC3_2.$yyyymm

$ERBELIKEHOME/erbelike/data/CERES/ES4G/$SS3_2_$PS2_0/$yyyy/$mm:

CER_ES4G_$SS3_2_$PS2_0_$CC3_2.$yyyymm_i  (where i=1-9)

$ERBELIKEHOME/erbelike/web/CER3.2P1/s4g/gif/S4G_${yyyymm}_$ksc/:

MH_ALB_R2520.gif

MH_CS_ALB_R2520.gif

MH_CS_LW_R2520.gif

MH_CS_SW_R2520.gif

MH_LW_CF_R2520.gif

MH_LW_R2520.gif

MH_NET_CF_R2520.gif

MH_SW_CF_R2520.gif

MH_SW_R2520.gif

The following files will be generated in

$ERBELIKEHOME/erbelike/web/CER3.2P1/es4_stats/data/:

DQCG_Stats_$SS3_2_$PS2_0.web

Monthly_LW_Stats_$SS3_2_$PS2_0.web

Monthly_SW_Stats_$SS3_2_$PS2_0.web

Monthly_Stats_log_$SS3_2_$PS2_0.$yyyymm

#### Exit Codes

All CER3.2P1 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.  This test should complete with “Exit Status = 0”.

#### CER3.2P1 Test Summary

Total Run Time:	3:11 minutes (on P6)

Memory:	452 Megabytes

Required Disk Space:	340 Megabytes

### Evaluation Procedures

When running the clear directory script, clr_dir.PGE3.2P1.csh, the system message, “rm: cannot remove ‘<dirname>’:  No such file or directory” may be written to the screen.  This message occurs when the script tries to remove an old output directory that does not exist.  This does not signify a problem, as these directories are yet to be created (1st run case) or run-time only (unsuccessful run leftovers).

#### Log and Status File Results

The Error and Status Log Files are located in directory $ERBELIKEHOME/erbelike/runlogs/CER3.2P1 after CER3.2P1 has been executed.  These files are:

CER3.2P1_LogReport_$SS3_2_$PS2_0_$CC3_2.$yyyymm

CER3.2P1_LogStatus_$SS3_2_$PS2_0_$CC3_2.$yyyymm

CER3.2P1_LogUser_$SS3_2_$PS2_0_$CC3_2.$yyyymm

#### Metadata Evaluation

The metadata files, which end in extension ‘.met’, are located in the same directory as their corresponding output files after CER3.2P1 has been executed.  Compare the metadata for the test case with the metadata provided in this delivery, using the gdiff command (available via ssh -X):

gdiff $ERBELIKEHOME/erbelike/data/CERES/DES9/$SS3_2_$PS2_0/$yyyy/$mm/CER_DES9_$SS3_2_$PS2_0_$CC3_2.$yyyymm.met $ERBELIKEHOME/erbelike/data_exp/CER3.2P1/CER_DES9_$SS3_2_$PS2_0_$CC3_2.$yyyymm.met

gdiff $ERBELIKEHOME/erbelike/data/CERES/DES4/$SS3_2_$PS2_0/$yyyy/$mm/CER_DES4_$SS3_2_$PS2_0_$CC3_2.$yyyymm.met $ERBELIKEHOME/erbelike/data_exp/CER3.2P1/CER_DES4_$SS3_2_$PS2_0_$CC3_2.$yyyymm.met

The only differences between the files should be the production times and the directory paths where the tests were run.

#### Output Data Evaluation

##### Execution of HDF ES-4 Comparison Utility

The hdiff utility can be used to evaluate the ES-4 HDF data.  The two files to be compared are entered as command-line arguments.

Compare the ES4 for the test case:

cd $ERBELIKEHOME/erbelike/test_suites

hdiff -d -t 0.1 $ERBELIKEHOME/erbelike/data/CERES/ES4/$SS3_2_$PS2_0/$yyyy/$mm/*_$CC3_2.$yyyymm $ERBELIKEHOME/erbelike/data_exp/CER3.2P1/*_ES4_*$CC3_2.$yyyymm

hdiff -d -t 0.01 $ERBELIKEHOME/erbelike/data/CERES/ES4/$SS3_2_$PS2_0/$yyyy/$mm/*_$CC3_2.$yyyymm $ERBELIKEHOME/erbelike/data_exp/CER3.2P1/*_ES4_*$CC3_2.$yyyymm | wc -l

Note:  Total Run Time should not > 15 secs

##### Evaluation of HDF ES-4 Comparison Software

The ES-4 data comparison tool, hdiff, returns a list of differences by position, parameter name, and values in both files.  If all data differences between the compared files are within the trigger value provided, there will be no output.  As long as the differences are small in both number and magnitude, the files can be considered scientifically equivalent.

For the first test (trigger set at 0.1), only a handful of differences should be found and none should be much greater than 0.1 (i.e. 2 Shortwave flux of 0.100006 and 1 of 0.100002).

For the second test (trigger set at 0.01), one can expect the number of difference to grow to a dozen spread out over different flux parameters.  This could lead to a listing of up to 50 lines.

##### Evaluation of ES-4 GIF Files

The resulting 9 “gif” images (see Section 3.7.1.2) must be evaluated by an external viewer (i.e., xv or display).  The CERES Test Coordinator may contact a member of the ERBE-like Subsystem Team to assist in the evaluation of these gif images.

cd $ERBELIKEHOME/erbelike/web/CER3.2P1/s4g/gif/S4G_$yyyymm\_$ksc

display MH_*_R2520.gif

cd $ERBELIKEHOME/erbelike/data_exp/CER3.2P1/Web/S4G_$yyyymm\_$ksc

display MH_*_R2520.gif

Click on each xwindow with the right mouse button

Double click matching file names in both windows and visually compare the two plots.

##### Evaluation of ES-4 Statistical Trend Files

The resulting 3 “.web” files (see Section 3.7.1.2) contain statistical averages of the ES-4 data set that can be compared with their expected equivalents:

cd $ERBELIKEHOME/erbelike/web/CER3.2P1/es4_stats/data

gdiff DQCG_Stats_$SS3_2_$PS2_0.web $ERBELIKEHOME/erbelike/data_exp/CER3.2P1/Web/es4_stats/DQCG_Stats_$SS3_2_$PS2_0.web

gdiff Monthly_LW_Stats_$SS3_2_$PS2_0.web $ERBELIKEHOME/erbelike/data_exp/CER3.2P1/Web/es4_stats/Monthly_LW_Stats_$SS3_2_$PS2_0.web

diff Monthly_SW_Stats_$SS3_2_$PS2_0.web $ERBELIKEHOME/erbelike/data_exp/CER3.2P1/Web/es4_stats/Monthly_SW_Stats_$SS3_2_$PS2_0.web

### Solutions to Possible Problems

- All output files are opened with Status = NEW in the CER3.2P1 software.  These files must be removed before rerunning these test procedures.  A script, which removes PGE files created via the command line, clr_dir.PGE3.2P1.csh, is located in directory $ERBELIKEHOME/erbelike/CER3.2P1/rcf.  Use the data date (4-digit year, 2-digit month) as a command-line argument:

clr_dir.PGE3.2P1.csh $yyyymm

Refer to the Message and Log files created in $ERBELIKEHOME/erbelike/runlogs/CER3.2P1 (for command line runs) or $ERBELIKEHOME/erbelike/sge_logs/CER3.2P1 (for sge runs) for explanations of possible problems.

## CER2.2P2 CERES ERBE-like Daily Inversion for FM6

### Stand-alone Test Procedure

Before starting the processing of CER2.2P2, make sure the instrument-specific test pre-ES8 input file is accessible from the archive:

ls /ASDC_archive/CERES/BDS/J01-FM6_Edition1-CV/2018/03/CER_BDS_J01-FM6_Edition1-CV_300312.20180323

ls /ASDC_archive/CERES/BDS/J01-FM6_Baseline1-QC/2018/03/CER_BDS_J01-FM6_Baseline1-QC_300312.20180330

#### Execution

The production script, CER2.2P2.pl, references a PCF file containing the file names and paths for the test procedures.  The PCF for each test case is created by executing a combined log file and PCF generator, gen_pcf.CER2.2.pl.

The PCF log and PCF generator requires five command-line arguments, yyyymmdd (where yyyy is the 4-digit year, mm is the 2-digit month, and dd is the 2-digit day), “C” for composite snow or “A” for actual snow input file, “F” for Original ADM structure, “M” to use one of the Instrument Team’s monthly modified Slope Intercept Spectral Correction inputs (“N” if not applicable, i.e., prior to Edition2 input data), “T” for Thermal SW Offsets or “K” for Edition3 processing.

- J01-FM6: Baseline1-QC

source $ERBELIKEHOME/erbelike/data/input/CER2.2P2/ENV-FM6_1QC_222_1387.csh

setenv yyyy 2018

setenv mm 03

setenv yyyymmdd ${yyyy}${mm}30

cd $ERBELIKEHOME/erbelike/CER2.2P2/rcf

CER2.2P2-SGE_Driver.pl -date $yyyymmdd -snow C -adm F -spcor N -swoff T -clean

- J01-FM6: Edition1-CV

source $ERBELIKEHOME/erbelike/data/input/CER2.2P2/ENV-FM6_1CV_222_1387.csh

setenv yyyy 2018

setenv mm 03

setenv yyyymmdd ${yyyy}${mm}22

cd $ERBELIKEHOME/erbelike/CER2.2P2/rcf

CER2.2P2-SGE_Driver.pl -date $yyyymmdd -snow A -adm F -spcor N -swoff T -clean

#### Expected Output Files

Each test will have a sampling Strategy ($SS2), a Production Strategy (‘TestPlan’), a Configuration Code ($CC2) and a Data Date (20180222).  After the Product Generation Executive (PGE) CER2.2P2 is executed, it should have created the following files in the following directories:

The following files will be generated in

$ERBELIKEHOME/erbelike/CER2.2P2/rcf/pcf/:

CER2.2P2_PCF_${SS2}_${PS2_0}_$CC2.$yyyymmdd.log

CER2.2P2_PCF_${SS2}_${PS2_0}_$CC2.$yyyymmdd

The following files (product=PROD) and associated .met files will be generated in $ERBELIKEHOME/erbelike/data/CERES/PROD/${SS2}_${PS2_0}/$yyyy/$mm/:

PROD=CQCI: CER_CQCI_${SS2}_${PS2_0}_$CC2.$yyyymmdd

PROD=EID6: CER_EID6_${SS2}_${PS2_0}_$CC2.$yyyymmdd

PROD=ES8: CER_ES8_${SS2}_${PS2_0}_$CC2.$yyyymmdd

PROD=ES8B: CER_ES8B_${SS2}_${PS2_0}_$CC2.$yyyymmdd

PROD=ES8N: CER_ES8N_${SS2}_${PS2_0}_$CC2.$yyyymmdd

PROD=CMSG: CER_CMSG_${SS2}_${PS2_0}_$CC2.$yyyymmdd

#### Exit Codes

All CER2.2P2 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.  This test should complete with “Exit Status = 0”.

#### CER2.2P2 Test Summary

Total Run Time:	1 minute

Memory:	546 Megabytes

Required Disk Space:	800 Megabytes

### Evaluation Procedures

#### Log and Status File Results

The Error and Status Log Files are located in directory $ERBELIKEHOME/erbelike/runlogs/CER2.2P2/ after CER2.2P2 has been executed.  These files are:

CER2.2P2_LogReport_${SS2}_${PS2_0}_$CC2.$yyyymmdd

CER2.2P2_LogStatus_${SS2}_${PS2_0}_$CC2.$yyyymmdd

CER2.2P2_LogUser_${SS2}_${PS2_0}_$CC2.$yyyymmdd

#### ES-8 Comparison

The ES-8 HDF output file has been created at $ERBELIKEHOME/erbelike/data/CERES/ES8/${SS2}_${PS2_0}/$yyyy/$mm:

We will use hdiff to compare.

hdiff for test 2 – Edition1-CV

source $ERBELIKEHOME/erbelike/data/input/CER2.2P2/ENV-FM6_1CV_222_1387.csh

cd $ERBELIKEHOME/erbelike/data/CERES/ES8/J01-FM6_Edition1-CV/2018/03

hdiff -d -t 0.0001 CER_ES8_J01-FM6_Edition1-CV_1387.20180322  $ERBELIKEHOME/erbelike/data_exp/CER2.2P2/CER_ES8_J01-FM6_Edition1-CV_1387.20180322

This may take ~ 20 seconds and if successfull go from command to new prompt.

hdiff for test1 – Baseline1-QC

source $ERBELIKEHOME/erbelike/data/input/CER2.2P2/ENV-FM6_1QC_222_1387.csh

cd $ERBELIKEHOME/erbelike/data/CERES/ES8/J01-FM6_Baseline1-QC/2018/03

hdiff -d -t 0.0001 CER_ES8_J01-FM6_Baseline1-QC_1387.20180330   $ERBELIKEHOME/erbelike/data_exp/CER2.2P2/CER_ES8_J01-FM6_Baseline1-QC_1387.20180330

This may take ~ 20 seconds and if successfull go from command to new prompt.

#### Evaluation of ES-8 Comparison Software Output

The ES-8 data comparison tool, hdiff, returns a list of differences by position, parameter name, and values in both files.  If no data differences exist between the files there will be no output.

### Solutions to Possible Problems

- Refer to the Message and Log files created in $ERBELIKEHOME/erbelike/runlogs/CER2.2P2 (and $ERBELIKEHOME/erbelike/sge_logs/CER2.2P2 in the case of SGE jobs) for explanations of possible problems.

Acronyms and Abbreviations

ASCII	American Standard Code Information Interchange

ASDC	Atmospheric Science Data Center

CERES	Clouds and the Earth’s Radiant Energy System

CERESlib	CERES library

DAAC	Distributed Active Archive Center

EOS	Earth Observing System

EOS-AM	EOS Morning Crossing (Ascending) Mission

EOS-PM	EOS Afternoon Crossing (Descending) Mission

ERBE	Earth Radiation Budget Experiment

ERBS	Earth Radiation Budget Satellite

FAPS	Fixed Azimuth Plane Scan

FAPS+RAPS	Indicates FAPS and RAPS data processed together

FAPS, RAPS	Indicates FAPS and RAPS data processed separately

FM	Flight Model

F90	Fortran 90

HDF 	Hierarchical Data Format

LaTIS	Langley TRMM Information System

LW	Longwave

MB	Mega Byte

met	metadata file (or .met)

N/A	Not Applicable

NASA	National Aeronautics and Space Administration

NOAA	National Oceanic and Atmospheric Administration

PCF	Process Control File

PFM	Prototype Flight Model (on TRMM)

PGE	Product Generation Executives

QC	Quality Control

RAPS	Rotating Azimuth Plane Scan

SSAI	Science Systems Applications Inc.

SSF	Single Satellite CERES Footprint TOA and Surface Fluxes, Clouds

SW	Shortwave

Terra	EOS Morning Crossing (Ascending) Mission; also known as EOS-AM

TOA	Top of the Atmosphere, Top of Atmosphere

TRMM	Tropical Rainfall Measuring Mission

Directory Structure Diagram 
(under $ERBELIKEHOME/erbelike)

bin/

CER2.1P1

bin/

data/

scr/

rcf/

pcf/
			summary/

src/

CER2.2P1

bin/

data/

scr/

rcf/

pcf/
			summary/

src/

gen_es8hdf/
	Web/
		anc/

color/
				ppm/

font/
		csh/
		src/

CER2.3P1

data/

scr/

rcf/

pcf/
			summary/

CER2.3P2

data/

scr/

rcf/

pcf/
			summary/

CER2.4P1

bin/

lib/

data/

scr/

input/

rcf/

pcf/

summary/

src/

Web/

scc_trend/
			data/

CER3.1P1

bin/

data/

scr/

rcf/

mcf/

pcf/

summary/

src/

ddbsrt/

ddbuer/

mtsa1/

Web/

s4g/

anc/

font/

Outlines/

Screencol/

csh/

src/

genppm/

gets4g/

CER3.2P1

bin/

data/

scr/

rcf/

pcf/

summary/

src/

mtsa0/

mtsa3/

Web/

es4_stats/

bin/

src/

s4g/

anc/

font/

Outlines/

Screencol/

csh/

src/

genppm/

gets4g/

ancillary/

CER2.1P1/

ERBEgeoscene/

NSIDCgrid/

SNOWcomposite/

SNOWnorthern/

ERBEalbedos/

LWThresholds/

CER2.4P1/

modtran

CER2.2P1/

Xtrk_db/

QCchecker/

Inversion/

ERBEscnID/

ADMparameters

Tolerances/

data/

CERES/

CMSG/

CMSGX/

CQCD/

CQCI/

CQCIX/

CQCR

CXDR/

DES4/

DES9/

DMSG/

DQCA/

DQCB/

DQCBW/

DQCC/

DQCD/

DQCG/

DQCGW/

DQCS/

DQCX/

EID6/

EID6X/

ES4/

ES4G1/

ES4G2/

ES4G3/

ES4G4/

ES8/

ES8B/

ES8N/

ES9/

PRES8/

SCCD/

SCCN/

SNOW/

input/

CER2.1P1/

CER2.4P1

CER3.1P1/

CER3.2P1/

web/

CER2.1P1/

CERESweb/

CERESfmt/

CER2.2P1/

gif/

CER3.1P1/

qc/

s4g/

dat/

gif/

CER3.2P1/

es4_stats/

data/

qc/

s4g/

dat/

gif/

data_exp/

CER2.1P1/

CER2.2P1/

CER2.2P2/

CER2.3P1/

CER2.3P2/

CER2.4P1/

CER3.1P1/

Web/

CER3.2P1/

Web/

es4_stats/

lib/

erbelike_lib/

ddbint/

ddbuer/

ddbupd/

es4/

gen_es4hdf/

gen_es9hdf/

inv/

CER2.2P2/

pre_es4/

sol_dec/

tsalib/

mcf/

rcf/

runlogs/

CER2.1P1/

CER2.2P1/

CER2.2P2

CER2.3P1/

CER2.3P2/

CER2.4P1/

CER3.1P1/

CER3.2P1/

sge_logs/

CER2.1P1/

CER2.2P1/

CER2.2P2

CER2.3P1/

CER2.3P2/

CER2.4P1/

CER3.1P1/

CER3.2P1/

smf/

test_suites/

CER2.2P2

bin/

data/

scr/

rcf/

pcf/
			summary/

src/

gen_es8hdf/

inv

Web/
		anc/

color/
				ppm/

font/
		csh/
		src/

File Description Tables

Production Scripts

The following scripts must be moved to the production environment.

| Table C.1-1. Production Scripts ($ERBELIKEHOME/erbelike/CER*.*P*/rcf) |
| --- |
| File Name | Format | Description |
| CER2.1P1_run.pl | ASCII | Perl script to run ERBE-like Subsystem 2.1P1 |
| CER2.2P1.pl | ASCII | Perl script invokes ERBE-like inversion program to process a day’s combined FAPS and RAPS data from a single instrument. |
| CER2.2P2.pl | ASCII | Perl script invokes ERBE-like inversion program to process a day’s combined FAPS and RAPS data from FM6. |
| CER2.3P1.pl | ASCII | Perl script invokes ERBE-like inversion program, daily data base initialization, and daily data update programs to process the daily combined FAPS and RAPS data from a single instrument for the 1st day of a month. This script generates an overlap data file for the previous month’s monthly processing. |
| CER2.3P2.pl | ASCII | Perl script invokes ERBE-like inversion program, daily data base initialization, and daily data update programs to process the daily combined FAPS and RAPS data from a single instrument for the last day of a month. This script generates an overlap data file for the next month’s monthly processing. |
| CER2.4P1_run.pl | ASCII | Perl script invokes ERBE-like spectral response function and spectral correction coefficient program. |
| CER3.1P1.pl | ASCII | Perl script invokes ERBE-like Daily Data Base (ddbint, ddbupd, ddbuer, and ddbsrt), Monthly Time/Space Averaging (mtsa1), and Monthly Regional, Zonal, and Global Averages (es4) for single instrument monthly data processing. |
| CER3.2P1.pl | ASCII | Perl script invokes ERBE-like Daily Data Base (ddbint, ddbupd, ddbuer, and ddbsrt), Monthly Time/Space Averaging (mtsa3), and Monthly Regional, Zonal, and Global Averages (es4) for multiple instrument monthly data processing. |
| ../../rcf/ ENVerbelike-env.csh | ASCII | C-shell script sets environment variables for ERBE-like PCF generators and PGEs (except for CER3.2P1). |
| ../../rcf/ ENVerbelike-env2.csh | ASCII | Special case of ENVerbelike-env.csh: 2 instruments processing (option for CER3.2P1 only). |
| ../../rcf/ ENVerbelike-env4.csh | ASCII | Special case of ENVerbelike-env.csh: 4 instruments processing (option for CER3.2P1 only). |
| Fail2.1p1_template | ASCII | ASCII file used as template for mail feature in 2.1P1 |
| QCchecker.csh | ASCII | C-shell script invokes ERBE-like Quality Control file checker processing. |
| ../../bin/Succ2.1p1_template | ASCII | ASCII file used as template for mail feature in SS2.1P1 |
| Succ2.1p1_template2 | ASCII | ASCII file used as template for mail feature in SS2.1P1 |
| clr_dir.PGE2.1 | ASCII | C-shell script to clear output data files and directories before executing CER2.1P1 |
| clr_dir.CER2.2.csh | ASCII | C-shell script to clear output data files and directories before executing CER2.2P1 |
| clr_dir.PGE2.3P1.csh, clr_dir.PGE2.3P2.csh | ASCII | C-shell scripts to clear output data files and directories before executing CER2.3P1 or CER2.3P2 |
| CER2.4P1_clr_dir.csh | ASCII | C-shell script to clear output data files and directories before executing CER2.4P1 |
| clr_dir.PGE3.1P1.csh | ASCII | C-shell script to clear output data files and directories before executing CER3.1P1 |
| clr_dir.PGE3.2P1.csh | ASCII | C-shell script to clear output data files and directories before executing CER3.2P1 |
| CER2.1P1_gen_pcf.pl | ASCII | Perl script creating a PCF log and PCF for PGE2.1P1 |
| gen_pcf.CER2.2.pl | ASCII | Perl script creating a PCF log and PCF for PGE2.2P1 |
| gen_pcf.CER2.3P1.pl | ASCII | Perl script creating a PCF log and PCF for CER2.3P1 |
| gen_pcf.CER2.3P2.pl | ASCII | Perl script creating a PCF log and PCF for CER2.3P2 |
| CER2.4P1_gen_pcf.pl | ASCII | Perl script creating a PCF log and PCF for CER2.4P1 |
| gen_pcf.CER3.1P1.pl | ASCII | Perl script creating a PCF log and PCF for PGE3.1P1 |
| gen_pcf.CER3.2P1.pl | ASCII | Perl script creating a PCF log and PCF for CER3.2P1 |
| ../Web/s4g/ plot_es4.csh | ASCII | C-shell script invokes es4Allgif to generate monthly ES4 plots for Web pages (CER3.1P1/3.2P1) |
| plot_es8.csh | ASCII | C-shell script invokes es8Gif to generate daily ES8 plots for Web page |
| plot_qc.csh | ASCII | C-shell script invokes combine_qc.pl to generate Inversion monthly QC report file for Web page |
| plot_scc | ASCII | Short version of CER2.4P1 script to test the scc_trend plots |
| regen_pict.CER2.1p1 | ASCII | C-shell script to regenerate the PostScript and gif files using existing SNOW files |
| CER2.4P1_archival.csh | ASCII | C-shell script to put archival data (channel CERESlib SCCs) into temporary (scratch) file for later processing |
| CER2.4P1_calc_dates.csh | ASCII | C-shell script to calculate the interpolation interval based on the input file dates and the interval between the first input date and the run date |
| CER2.4P1_calc_files.csh | ASCII | C-shell script to determine the spectral response functions and correction coefficient input file names |
| CER2.4P1_daymasterfile.csh | ASCII | C-shell script to combine regression files to generate the spectral correction coefficient day file |
| CER2.4P1_gen.csh | ASCII | C-shell script to produce all intermediate coefficient and regression files |
| CER2.4P1_nightmasterfile.csh | ASCII | C-shell script to combine regression files to generate the spectral correction coefficient night file |
| ../bin/ MonthlyIIGS_Plot.idl | ASCII | Text file used by IDL to run the monthly IIGS plots for the Web pages of CER2.1P1 |

Executables

| Table C.2-1. Executables ($ERBELIKEHOME/erbelike/bin or CER*.*P*/bin) |
| --- |
| File Name | Format | Description |
| CER3.1P1_s4_gen_ppm_$CPUTYPE.exe | Binary | CER3.?/P1/Web/s4g/src/genppm code for converting ppm ES4 plots to gif format |
| CER3.1P1_ddbint_$CPUTYPE.exe | Binary | ERBE-like Daily Data Base Initialization program. |
| CER3.1P1_ddbsrt_$CPUTYPE.exe | Binary | ERBE-like Daily Data Base Monthly Data Sort program. |
| CER3.1P1_ddbuer_$CPUTYPE.exe | Binary | ERBE-like Daily Data Base Overlap Data Update program. |
| CER3.1P1_ddbupd_$CPUTYPE.exe | Binary | ERBE-like Daily Data Base Update program. |
| CER3.1P1_es4_$CPUTYPE.exe | Binary | ERBE-like Monthly Regional, Zonal, and Global Averages program. |
| CER3.1P1_gen_es4hdf_ $CPUTYPE.exe | Binary | ERBE-like conversion of ES4G1-4 to ES4 HDF-EOS program. |
| CER2.2P1_gen_es8hdf_ $CPUTYPE.exe | Binary | ERBE-like conversion of ES8 to ES8 HDF-EOS program. |
| CER3.1P1_gen_es9hdf_ $CPUTYPE.exe | Binary | ERBE-like conversion of ES9 to ES9 HDF program. |
| CER2.1P1_gen_snow_ $CPUTYPE.exe | Binary | ERBE-like program generating a monthly snow map file. |
| CER2.2P1_GenEs8SenID_$CPUTYPE.exe | Binary | CER2.2P1/Web/src code for generating the ES8 scene ID plots |
| CER2.2P1_inv_ $CPUTYPE.exe | Binary | ERBE-like inversion program |
| CER2.2P2_inv_ $CPUTYPE.exe | Binary | ERBE-like inversion program for FM6 |
| CER3.2P1_mtsa0_$CPUTYPE.exe | Binary | ERBE-like Single-Instrument Monthly Time/Space Averaging program. |
| CER3.1P1_mtsa1_$CPUTYPE.exe | Binary | ERBE-like Multi-Instrument Monthly Time/Space Averaging program. |
| CER3.2P1_mtsa3_$CPUTYPE.exe | Binary | ERBE-like Multi-Instrument Monthly Time/Space Averaging program. |
| CER2.2P1_GenEs8Ppm_$CPUTYPE.exe | Binary | CER2.2P1/Web/src code for converting ppm ES8 plots to gif format |
| CER3.1P1_pre_es4_$CPUTYPE.exe | Binary | ERBE-like program generating monthly regional, zonal, and global averages housekeeping. |
| pre_es8.exe | Binary | ERBE-like program generating a CERES PRES8 (inversion input) from an ERBE S8 (inversion output) data file. |
| read_qc.exe | Binary | ERBE-like Quality Control file checker program. |
| scc_calbkn.exe | Binary | Reads in filtered and unfiltered results from spcoef for clear and ovc land/ocean cases only, and determines filtered and unfiltered values for broken cases. Also, reads in filtered and unfiltered values for deep convective clouds |
| scc_checker.exe | Binary | Performs quality control check on SCCs day/night files generated by CER2.4P1 |
| scc_interp_resp.exe | Binary | Derives the response function using linear fit of two given response functions. |
| scc_meta.exe | Binary | Generates meta data files (.met) for new SCCs day/night files generated by CER2.4P1 |
| scc_regr.exe | Binary | Reads simulated filtered and unfiltered radiances based on modtran calculations and fits a line to ncas pairs. |
| scc_regr_lw.exe | Binary | Reads simulated filtered and unfiltered radiances based on modtran calculations and fits a line to ncas pairs. |
| scc_spcoef.exe | Binary | Uses spectral radiances from modtran runs and spectral responses. |
| scc_spcoef_lnd.exe | Binary | Uses SW radiances from modtran runs and spectral response to determine unfiltering coefficients |
| scc_spcoef_night.exe | Binary | Generates nighttime total and window radiances. |
| scc_spcoef_night_lnd.exe | Binary | Generates nighttime total and window radiances. |
| scc_stitch.exe | Binary | Reads in ocean clr and old cloud modtran tape 7 results and stitches an output file together that has one clear followed by four cloud cases. |
| CER3.1P1_sol_dec_$CPUTYPE.exe | Binary | ERBE-like program generating monthly solar declination file. |
| Note: These files will be generated on execution of Subsystem software and are not included in the tar file. |

Status Message Files

| Table C.3-1. Status Message Files ($ERBELIKEHOME/erbelike/smf) |
| --- |
| File Name | Format | Description |
| albedo_mod_25201.t | ASCII | Message file for module makealbmaps_all.f90 |
| combine_mod_25202.t | ASCII | Message file for module makecombine_file.f90 |
| ddb_25203.t | ASCII | Message file for Daily Data Base modules |
| erbe_mod_25204.t | ASCII | Message file for module ERBE_Mod.f90 |
| erbeqc_25205.t | ASCII | Message file for module qc_reader.f90 |
| es4_25206.t | ASCII | Message file for es4 modules |
| esxhdf_25207.t | ASCII | Message file for es4, es8 and es9 hdf modules |
| inv_25208.t | ASCII | Message file for program inv.f90 |
| invsurf_25221.t | ASCII | Message file for module es8_at_surf.f90 |
| mtsa_25209.t | ASCII | Message file for Monthly Time/Space Averaging modules |
| nadir_25219.t | ASCII | Message file for module nadir_util.f90 |
| postproc_mod_25210.t | ASCII | Message file for module PostProc.f90 |
| pres4_25211.t | ASCII | Message file for module pre_es4.f90 |
| pres8_25220.t | ASCII | Message file for program gen_pres8.f90 |
| s4stats_25223.t | ASCII | Message file for es4_stats programs |
| scc_25222.t | ASCII | Message file for scc programs |
| scnlib_25212.t | ASCII | Message file for scnlib modules |
| snow_main_25214.t | ASCII | Message file for module Snow_Main.f90 |
| snow_mod_25215.t | ASCII | Message file for module Snow_Mod.f90 |
| soldec_25216.t | ASCII | Message file for sol_dec.f90 |
| thres_mod_25217.t | ASCII | Message file for module makeallthresholds.f90 |
| tsalib_25218.t | ASCII | Message file for tsalib modules |

Processing Control Files (PCF) and Metadata Control Files (MCF)

The Process Control Files are not included in the Software Delivery Package.  They will be created by the PCF generator scripts.

| Table C.4-1. Metadata Control Files ($ERBELIKEHOME/erbelike/mcf) |
| --- |
| File Name | Format | Description |
| CCES8_AB.mcf | ODL | Metadata control file template |
| CCES8HAB.mcf | ODL | Metadata control file template |
| CCESN_AB.mcf | ODL | Metadata control file template |
| CCID6_AB.mcf | ODL | Metadata control file template |
| CCIDX_AB.mcf | ODL | Metadata control file template |
| CCMSG_AB.mcf | ODL | Metadata control file template |
| CCMSX_AB.mcf | ODL | Metadata control file template |
| CCQCD_AB.mcf | ODL | Metadata control file template |
| CCQCI_AB.mcf | ODL | Metadata control file template |
| CCQCR_AA.mcf | ODL | Metadata control file template |
| CCQCX_AB.mcf | ODL | Metadata control file template |
| CCSNOWAA.mcf | ODL | Metadata control file template |
| CCXDR_AB.mcf | ODL | Metadata control file template |
| CD4G1_AB.mcf | ODL | Metadata control file template |
| CD4G2_AB.mcf | ODL | Metadata control file template |
| CD4G3_AB.mcf | ODL | Metadata control file template |
| CD4G4_AB.mcf | ODL | Metadata control file template |
| CDES4_AB.mcf | ODL | Metadata control file template |
| CDES9_AB.mcf | ODL | Metadata control file template |
| CDMSG_AB.mcf | ODL | Metadata control file template |
| CDQCA_AB.mcf | ODL | Metadata control file template |
| CDQCB_AB.mcf | ODL | Metadata control file template |
| CDQCC_AB.mcf | ODL | Metadata control file template |
| CDQCD_AB.mcf | ODL | Metadata control file template |
| CDQCG_AB.mcf | ODL | Metadata control file template |
| CDQCS_AB.mcf | ODL | Metadata control file template |
| CDQCX_AB.mcf | ODL | Metadata control file template |
| CDS4_HAB.mcf | ODL | Metadata control file template |
| CDS9_HAB.mcf | ODL | Metadata control file template |
| CDXDR_AB.mcf | ODL | Metadata control file template |
| CSCCD_AB.mcf | ODL | Metadata control file template |
| CSCCN_AB.mcf | ODL | Metadata control file template |

| Table C.4-2. Process Control Files ($ERBELIKEHOME/erbelike/CER*.*P*/rcf/pcf) |
| --- |
| File Name | Format | Description |
| CER2.1P1_PCF_CERES_NSIDC_022019.200404.log1 | ASCII | PCF log for CER2.1P1 |
| CER2.1P1_PCF_CERES_NSIDC_022019.2004041 | ASCII | Process control file for CER2.1P1 |
| CER2.2P1_PCF_$SS2_TestPlan_$CC2.$yyyymmdd.log1 | ASCII | PCF log for CER2.2P1 |
| CER2.2P1_PCF_$SS2_TestPlan_$CC2.$yyyymmdd 1 | ASCII | Process control file for CER2.2P1 |
| CER2.3P1_PCF_$SS2_TestPlan_$CC2.$yyyymmdd.log1 | ASCII | PCF log for CER2.3P1 |
| CER2.3P1_PCF_$SS2_TestPlan_$CC2.$yyyymmdd 1 | ASCII | Process control file for CER2.3P1 |
| CER2.3P2_PCF_$SS2_TestPlan_$CC2.$yyyymmdd.log1 | ASCII | PCF log for CER2.3P2 |
| CER2.3P2_PCF_$SS2_TestPlan_$CC2.$yyyymmdd 1 | ASCII | Process control file for CER2.3P2 |
| CER2.4P1_PCF_$SS2_TestPlan_$CC2_4.$yyyymmdd.log1 | ASCII | PCF log for CER2.4P1 |
| CER2.4P1_PCF_$SS2_TestPlan_$CC2_4.$yyyymmdd 1 | ASCII | Process control file for CER2.4P1 |
| CER3.1P1_PCF_$SS3_TestPlan_$CC3.$yyyymmdd.log1 | ASCII | PCF log for CER3.1P1 |
| CER3.1P1_PCF_$SS3_TestPlan_$CC3.$yyyymmdd 1 | ASCII | Process control file for CER3.1P1 |
| CER3.2P1_PCF_$SS3_2_TestPlan_$CC3_2.$yyyymmdd.log1 | ASCII | PCF log for CER3.2P1 |
| CER3.2P1_PCF_$SS3_2_TestPlan_$CC3_2.$yyyymmdd 1 | ASCII | Process control file for CER3.2P1 |
| 1These files will be generated on execution of the subsystem software and are not included in the tar file. |

HDF Read Software

| Table C.5-1. ERBE-like Read Software Files ($ERBELIKEHOME/erbelike/src) |
| --- |
| File Name | Format | Description |
| es8hdf/readHDF/README_read | ASCII | Contains a description of the files for the ES-8 HDF-EOS read program. |
| es8hdf/readHDF/HDFread.h | ASCII | Header file for the ES-8 HDF-EOS read program. |
| es8hdf/readHDF/readHDFfuncs.c | ASCII | Calls HDF functions for the ES-8 HDF-EOS read program. |
| es8hdf/readHDF/test_rdES8.c | ASCII | Reads an SDS and Vdata from an ES-8 HDF-EOS file. |
| es8hdf/readHDF/compile_rdES8 | ASCII | Compiler for the ES-8 HDF-EOS read program. |
| es9hdf/readHDF/README_read | ASCII | Contains a description of the files for the ES-9 HDF read program. |
| es9hdf/readHDF/HDFread.h | ASCII | Header file for the ES-9 HDF read program. |
| es9hdf/readHDF/readHDFfuncs.c | ASCII | Calls HDF functions for the ES-9 HDF read program. |
| es9hdf/readHDF/test_rdES9.c | ASCII | Reads an SDS and Vdata from an ES-9 HDF file. |
| es9hdf/readHDF/compile_rdES9 | ASCII | Compiler for the ES-9 HDF read program. |
| es4hdf/readHDF/README_read | ASCII | Contains a description of the files for the ES-4 HDF-EOS read program. |
| es4hdf/readHDF/HDFread.h | ASCII | Header file for the ES-4 HDF-EOS read program. |
| es4hdf/readHDF/readHDFfuncs.c | ASCII | Calls HDF functions for the ES-4 HDF-EOS read program. |
| es4hdf/readHDF/test_rdES4.c | ASCII | Reads an SDS and Vdata from an ES-4 HDF-EOS file. |
| es4hdf/readHDF/compile_rdES4 | ASCII | Compiler for the ES-4 HDF-EOS read program. |

Ancillary Input Data

| Table C.6-1. Ancillary Input Data ($ERBELIKEHOME/erbelike/ancillary) |
| --- |
| File Name | Format | Description |
| /CER2.2P1/Inversion/ERBEscnID/ BIILWss.yyyymmdd | Binary | Four ERBE binary seasonally varying scene identification algorithm parameter files for the Inversion program using old ADMs. |
| /CER2.2P1/Inversion/ERBEscnID/ BIISW02.yyyymmdd | Binary | ERBE binary temporally invariant scene identification algorithm parameter file for the inversion program using old ADMs. |
| /CER3.1P1/ ISDM2.yyyymmdd | Binary | ERBE binary direction model file for MTSA programs. |
| /CER2.2P1/Inversion/ADMparameters/ NIISCOLD.yyyymmdd | Binary | Binary parameter file for the Inversion program using old ADMs. |
| /CER2.2P1/Inversion/ADMparameters/ NIPSC.yyyymmdd | ASCII | One namelist file for Inversion Subsystem for CERES data processing using new ADMs and new LW thresholds. |
| /CER2.2P1/QCchecker/ QCcheck.list.20030418 QCcheck.list.20031006 | ASCII | List of parameters and instructions for QC evaluation software. |
| /CER2.1P1/SNOWcomposite/ SNOW_COMPOSITE_MM.yyyymmdd | Binary | Twelve binary monthly varying scene identification algorithm parameter files for the Inversion program. |
| /CER2.1P1/ERBEgeoscene/ baseline.map.19971101 | ASCII | ERBE GeoScene Types of static Ocean, Land, Desert and Coast. |
| /CER2.2P1/Inversion/ ceres_SI_inst_day.yyyymmdd | ASCII | Daytime Slope Intercept Spectral Correction Coefficients. |
| /CER2.2P1/Inversion/ ceres_SI_inst_night.yyyymmdd | ASCII | Nighttime Slope Intercept Spectral Correction Coefficients. |
| /CER2.1P1/ERBEalbedos/ combaut.19980130 | Binary | ERBE binary seasonally varying albedo thresholds. |
| /CER2.1P1/ERBEalbedos/ combspr.19980130 | Binary | ERBE binary seasonally varying albedo thresholds. |
| /CER2.1P1/ERBEalbedos/ combsum.19980130 | Binary | ERBE binary seasonally varying albedo thresholds. |
| /CER2.1P1/ERBEalbedos/ combwin.19980130 | Binary | ERBE binary seasonally varying albedo thresholds. |
| /CER2.1P1/NSIDCgrid/ indx_EASE_dat.19971101 | Binary | EASE indexes for grid transformation from Polar Sterographic grid data to Equal Angle grid. |
| /CER2.2P1/Inversion/Tolerances/ map_inst_fullscan.yyyymmdd | ASCII | LW Tolerances file. |
| /CER2.1P1/SNOWnorthern/ psnow.map.19971231 | Binary | ERBE GeoScene Type of Permanent Snow regions. |
| /CER2.4P1/modtran/dc_szXX.spectra.tp7 | ASCII | Spectral radiances for deep convective clouds. |
| /CER2.4P1/modtran/dc_vz.spectra.tp7 | ASCII | Spectral WN radiances for deep convective clouds. |
| /CER2.4P1/modtran/lnd_szXXL.tp7 | ASCII | Spectral radiances for land scenes |
| /CER2.4P1/modtran/lnd_vz.tp7 | ASCII | Spectral WN radiances for land scenes. |
| /CER2.4P1/modtran/ocecld_szXXL.tp7 | ASCII | Spectral radiances for ocean cloud scenes. |
| /CER2.4P1/modtran/ocecld_vz.tp7 | ASCII | Spectral WN radiances for ocean cloud scenes. |
| /CER2.4P1/modtran/oceclr_szXXL.tp7 | ASCII | Spectral radiances for ocean clear scenes. |
| /CER2.4P1/modtran/oceclr_vz.tp7 | ASCII | Spectral WN radiances for ocean clear scenes. |
| /CER2.4P1/modtran/sno_szXXL.tp7 | ASCII | Spectral radiances for snow scenes. |
| /CER2.4P1/modtran/sno_vz.tp7 | ASCII | Spectral WN radiances for snow scenes. |
| Note: All references in this table to dd = creation day, DD = data day, mm = creation month, MM = data month, ss = season, inst = instrument ID, yyyy = creation year, YYYY = data year and XX = ( 00, 41, 60, 75, and 85). |

Output Temporary Data Files (Production Results)

Table C.7-1.  Output Temporary Data Files ($ERBELIKEHOME/erbelike/CER*.*P*/data/scr)

| File Name | Format | Description |
| --- | --- | --- |
| CER2.1P1_CERES_NSIDC_022019.$date/ TempSNOW.ps | PostScript | IDL Postscript file used to create GIF image in CER2.1P1. |
| CER2.1P1_CERES_NSIDC_022019.$date/ TempENV.dat | ASCII | Created by CER2.1P1 to pass environment variables used in FORTRAN to IDL program. |
| CER?.?P?_$SS_TestPlan_$CC.$date/ ShmMem | ASCII | Used in production of metadata for all PGEs. |
| Note: These files will be generated on execution of Subsystem software and are not included in the tar file. All references in this table to date = data date in the form YYYYMM (4-digit year, 2-digit month) or YYYYMMDD (4-digit year, 2-digit month, 2-digit day). |