Clouds and the Earth's Radiant Energy System

(CERES)

Data Management System

CERES Inversion to Instantaneous TOA Fluxes

and Empirical Estimates of Surface Radiation Budget,

Subsystems 4.5 and 4.6 Test Plan

Release 5

Version 18

Primary Authors

Sandra K. Nolan, Carla B. Franklin, Aaron T. Hoppe, Victor Sothcott

Science Systems Applications, Inc. (SSAI)

One Enterprise Parkway, Suite 200

Hampton, VA  23666

NASA Langley Research Center

Climate Science Branch

Science Directorate

21 Langley Boulevard

Hampton, VA  23681-2199

SW Delivered to CM:  February 2017

Document Date:  February 2017

Document Revision Record

The Document Revision Record contains information pertaining to approved document changes.  The table lists the date the Software Configuration Change Request (SCCR) was approved, the Release and Version Number, the SCCR number, a short description of the revision, and the revised sections.  The document authors are listed on the cover.  The Head of the CERES Data Management Team approves or disapproves the requested changes based on recommendations of the Configuration Control Board.

| Document Revision Record |
| --- |
| SCCR Approval Date | Release/ Version Number | SCCR Number | Description of Revision | Section(s) Affected |
| 10/19/01 | R3V5 | 302 | Changed input MOA file names to use $CC12. | Secs. 3.1.1.1 & 3.1.2 |
|  |  |  | Updated format to comply with standards. | All |
| 03/21/02 | R3V6 | 322 | Added new PGEs CER4.5-6.1P2 and CER4.5-6.2P2. | New sections: 3.2 & 3.4 |
|  |  |  | Updated format to comply with standards. | All |
| 04/26/02 | R3V7 | 346 | SSFB-nadir and SSF-nadir products produced by PGE CER4.5-6.2P2. | Secs. 3.4.2.2 & 3.4.2.3 |
|  |  |  | Updated format to comply with standards. | All |
| 06/21/02 | R4V1 | 367 | Added new PGE CER4.5-6.1P3 for processing Aqua data. | Secs. 1.2, 2.2.1, & 3.3 |
|  |  |  | Updated CER4.5-6.1P2 to use dynamic SCC produced by PGE CER2.4P1. | Secs. 3.2.1.1 & 3.2.2 |
|  |  |  | Updated format to comply with standards. | All |
| 08/20/02 | R4V2 | 381 | Updated CER4.5-6.2P2 to produce binary SSF/SSFA validation product. | Secs. 1.2.2, 3.5, 3.5.2.1, 3.5.2.2, & 3.5.2.3 |
|  |  |  | Updated format to comply with standards. | All |
| 01/27/03 | R4V3 | 416 | Modified command line for CER4.5-6.1P3 PCF generator. | Sec. 3.3.1.1 |
|  |  |  | Updated format to comply with standards. | All |
| 04/24/03 | R4V4 | 434 | Modified Instance definition line to use environment variables for CER4.5-6.1P1. | Secs. 2.1, 3.1.1.1, 3.1.1.4, 3.1.2, & C.2 |
|  |  |  | Updated format to comply with standards. | All |
| 08/27/03 | R4V5 | 461 | Added new PGE CER4.5-6.3P2. | Apps. B & C |
|  |  |  | Added new PGE CER4.5-6.4P1. | Secs. 2.2.4, 2.2.5, 3.7, & 3.8 |
|  |  |  | Updated format to comply with standards. | All |
| 10/29/03 | R4V6 | 477 | Updated CER4.5-6.2P2 to produce new parameter ADMGEO. | Sec. 3.5.1.1 |
|  |  |  | Updated format to comply with standards. | All |
| 12/08/03 | R4V7 | 488 | Updated PGE CER4.5-6.3P2 to use Terra Edition2 ADMs. | Sec. 3.7.1.1 |
|  |  |  | Added new PGE CER4.5-6.3P3. | Secs. 2.2.5, 3.8, & App. C |
|  |  |  | Updated format to comply with standards. | All |
| 12/01/04 | R4V8 | 570 | Updated PGE CER4.5-6.3P3 to include Spectral Correction and new test data. There are now separate test cases for FM3 and FM4. | Secs. 1.2.5, 2.2.7, & 3.8 |
|  |  |  | Added new PGE CER4.5-6.6P2. | Sec. 3.10, Apps. B & C |
|  |  |  | Updated format to comply with standards. | All |
| 12/08/04 | R4V9 | 572 | Added new PGE CER4.5-6.6P3. | Secs. 1.2.6, 3.11, Apps. B & C |
|  |  |  | Updated format to comply with standards. | All |
| 03/07/05 | R4V10 | 578 | Modified PGE CER4.5-6.6P2. Changed output instance variable name for FM1 test case to INSTANCE_FM1. | Secs. 3.10.1-4 |
|  |  |  | Added FM2 test case for CER4.5-6.6P2. | Secs. 3.10.5-8 |
|  |  |  | Updated format to comply with standards. | All |
| 04/04/05 | R4V11 | 581 | Modified test case for CER4.5-6.6P2. Changed output instance variable name for FM1 test case to INSTANCE3_FM1. | Secs. 3.7.1-4 |
|  |  |  | Added FM2 test case for CER4.5-6.3P2. | Secs. 3.7.5-8 |
|  |  |  | Updated format to comply with standards. | All |
| 05/11/05 | R4V12 | 587 | Modified test case for CER4.5-6.2P2. Added tests for SCOOL output. | Secs. 3.5.2 & 3.5.5 |
|  |  |  | Added FM3 and FM4 test cases for CER4.5-6.2P2. | Secs. 3.5.7-12 |
|  |  |  | Updated format to comply with standards. | All |
| 10/10/05 | R4V13 | 596 | Modified test case for CER4.5-6.1P3. Added separate FM3 and FM4 test cases for CER4.5-6.1P3. | Sec. 3.3 |
|  |  |  | Modified input data for FM3 and FM4 test cases for CER4.5-6.3P3. | Sec. 3.8 |
|  |  |  | Updated Description Tables for CER4.5.6-6P2 & CER4.5-6.6P3. | App. C |
|  |  |  | Updated format to comply with standards. | All |
| 10/04/06 | R4V14 | 638 | Changed SAIC and address to SSAI and new address. | Cover page |
|  |  |  | Changed SAIC to SSAI. | Preface |
| 10/04/06 Continued | R4V14 | 638 | Removed Item #2 that references emailing the results because this no longer happens. | Secs. 3.1.2.3, 3.2.2.3, 3.3.2.3, 3.3.5.3, 3.6.2.3, 3.7.3.2, 3.7.7.2, 3.8.3.2, & 3.8.7.2 |
|  |  |  | Removed SAIC and added SSAI to acronym list. | App. A |
| 06/29/07 | R4V15 | 659 | Changed SCOOL input filename and the ’copy to’ location in PGE CER4.5-6.2P2. | Secs. 3.5.1.1, 3.5.4.1, 3.5.7.1, & 3.5.10.1 |
| 02/21/08 | R5V1 | 666 | Added PGEs CER4.5-6.1P4, CER4.5-6.1P5, CER4.5-6.2P3, and CER4.5-6.4P2. | Secs. 1.2.1, 1.2.2, 2.2.2, 2.2.3, 2.2.5, 2.2.10, 3.4, 3.5, 3.8, 3.13, Apps. B, & C |
| 12/08/08 | R5V2 | 690 | Changed directory structure for PGEs CER4.5-6.1P2, CER4.5-6.1P3, CER4.5-6.2P2, CER4.5-6.3P2, CER4.5-6.3P3, CER4.5-6.4P1, CER4.5-6.6P2, and CER4.5-6.6P3. | Secs. 2.1, 2.2.1, 2.2.4, 2.2.7, 2.2.8, 2.2.9, 2.2.11, 2.2.12, 3.2.1.1, 3.2.1.4, 3.2.2.1, 3.2.2.4, 3.2.3, 3.3.1.1, 3.3.1.2, 3.3.1.4, 3.3.2.1, 3.3.2.2, 3.3.2.4, 3.3.3, 3.3.4.1, 3.3.4.2, 3.3.4.4, 3.3.5.1, 3.3.5.2, 3.3.5.4, 3.3.6, 3.7.1.1, 3.7.1.2, 3.7.1.4, 3.7.2.1, 3.7.2.4, 3.7.3, 3.7.4.1, 3.7.4.2, 3.7.4.4, 3.7.5.1, 3.7.5.4, 3.7.6, 3.7.7.1, 3.7.7.2, 3.7.7.4, 3.7.8.1, 3.7.8.4, 3.7.9, 3.7.10.1, 3.7.10.2, 3.7.10.4, 3.7.11.1, |
| 12/08/08 (Continued) | R5V2 | 690 | Changed directory structure for PGEs CER4.5-6.1P2, CER4.5-6.1P3, CER4.5-6.2P2, CER4.5-6.3P2, CER4.5-6.3P3, CER4.5-6.4P1, CER4.5-6.6P2, and CER4.5-6.6P3. | Secs. 3.7.11.4, 3.7.12, 3.10.1.1, 3.10.1.2, 3.10.1.4, 3.10.3, 3.10.3.1, 3.10.3.3, 3.10.4, 3.10.5.1, 3.10.5.2, 3.10.5.4, 3.10.7, 3.10.7.1, 3.10.7.3, 3.10.8, 3.11.1.1, 3.11.1.2, 3.11.1.4, 3.11.3, 3.11.3.1, 3.11.3.3, 3.11.4, 3.11.5.1, 3.11.5.2, 3.11.5.4, 3.11.7, 3.11.7.1, 3.11.7.3, 3.11.8, 3.12.1.1, 3.12.1.2, 3.12.1.4, 3.12.2.1, 3.12.3, 3.14.1.1, 3.14.1.2, 3.14.1.4, 3.14.3, 3.14.5.1, 3.14.5.2, 3.14.5.4, 3.14.7, 3.14.7.1, 3.14.7.3, 3.14.8, 3.15.1.1, 3.15.1.2, 3.15.1.4, 3.15.3, 3.15.3.1, 3.15.3.3, 3.15.4, 3.15.5.1, 3.15.5.2, 3.15.5.4, 3.15.7, 3.15.7.1, 3.15.7.3, 3.15.8, App B |
| 12/08/08 (Continued) | R5V2 | 690 | Changed directory name from “PCF” to “pcf.” (04/02/09) | All |
| 03/04/09 | R5V3 | 704 | Updated test data and dates for PGEs CER4.5-6.1P4, CER4.5-6.1P5, CER4.5-6.2P3 and CER4.5-6.4P2. Updated evaluation procedures for PGEs CER4.5-6.1P4, CER4.5-6.1P5 and CER4.5-6.2P3. Removed PCFin files and corrected the PCF directory for PGEs CER4.5-6.1P4, CER4.5-6.1P5, CER4.5-6.2P3 and CER4.5-6.4P2. | Secs. 3.4.1.1, 3.4.2, 3.4.2.4, 3.4.4.1, 3.4.5, 3.4.5.4, 3.5.1.1, 3.5.2, 3.5.2.4, 3.5.4.1, 3.5.5, 3.5.5.4, 3.8.1.1, 3.8.2, 3.8.2.4, 3.8.4.1, 3.8.5, 3.8.5.4, 3.8.7.1, 3..8, 3.8.8.4, 3.8.10.1, 3.8.11, 3.8.11.2, 3.8.11.4, 3.13.1.1, 3.13.2, 3.13.4.1, 3.13.5, 3.13.7.1, 3.13.8, 3.13.10.1, & 3.13.11 |
| 09/04/09 | R5V4 | 722 | Added PGEs CER4.5-6.5P2 and CER4.5-6.5P3. | Secs. 1.2.5, 2.2.11, 2.2.12, 3.13, 3.14, Fig. B-2, Tables C.1-14, C.1-15, C.1-16, C.1-17, C.2-14, C-2-15, C.2-16, C.2-17, C.4-6, C.4-7, C.4-22, C.4-23, C.4-24, C.4-25, & C.6-2 |
|  |  |  | Corrections to directory paths (changed “PGE” to “CER.” (05/14/10) | Secs. 2.2.1, 2.2.4, 2.2.7, 2.2.8, 2.2.9, 2.2.13, & 2.2.14 |
| 05/28/2010 | R5V5 | 786 | Added PGEs CER4.5-6.5P4 and CER4.5-6.5P5. | Secs. 3-16, 3-17, 1.2.6, 2.2.13, 2.2.14, Fig. B-2, Tables C.1-16, C.1-17, C.2-16, C.2-17, C.4-6, C.4-7, C.4-24, C.4-25, & C.5-2 |
|  |  |  | Changed references of Edition3 to Edition4. | Secs. 1.2.1, 1.2.2, 3.8, 3.13, Tables C.2-4, & C.2-5 |
| 06/22/2010 | R5V6 | 791 | Added PGE CER4.5-6.2P4. | Secs. 1.2.2, 2.2.6, & 3.9, Fig. B-3, Tables C.1-9, C.2-9, C.4-4, & C.4-17 |
| 11/04/2010 | R5V7 | 814 | Updated PGEs CER4.5-6.1P4, CER4.5-6.1P5, CER4.5-6.2P3, and CER4.5-6.4P2 to include testing for SGE. | Secs. 3.4, 3.5, 3.8, 3.14, Tables C.1-4, C.1-5, C.1-8, C.1-14, & C.5-2 |
| 7/25/2012 | R5V8 | 912 | Updated PGEs CER4.5-6.2P4, CER4.5-6.4P1, CER4.5-6.5P4, and CER4.5-6.5P5 to include testing for SGE and for operation on AMI-P6 and x86 systems. | Secs. 3.10, 3.14, 3.18, & 3.19 |
|  |  |  | Updated compilation information for PGEs CER4.5-6.2P4, CER4.5-6.4P1, CER4.5-6.5P4, and CER4.5-6.5P5. | Secs. 2.2.6, 2.2.10, 2.2.14, & 2.2.15 |
|  |  |  | Updated Production Scripts and Executables Tables for PGEs CER4.5-6.2P4, CER4.5-6.4P1, CER4.5-6.5P4, and CER4.5-6.5P5. | Tables C.1-9, C.1-13, C.1-17, C.1-18, C.2-9, C.2-13, C.2-17, & C.2-18 |
|  |  |  | Added PGE CER4.5-6.1P6 for future use. | Sec. 3.6 |
| 7/25/2012 | R5V9 | 913 | Updated PGEs CER4.5-6.1P2, CER4.5-6.1P3, and CER4.5-6.2P2 to include testing for SGE and for operation on AMI-P6 and x86 systems. | Secs. 3.2, 3.3, & 3.8 |
|  |  |  | Updated compilation information for PGEs CER4.5-6.1P2, CER4.5-6.1P3, CER4.5-6.1P4, CER4.5-6.1P5, CER4.5-6.2P2, and CER4.5-6.2P3. | Secs. 2.2.1, 2.2.2, 2.2.3, 2.2.4, & 2.2.5 |
| 7/25/2012 (Continued) | R5V9 | 913 | Updated Production Scripts and Executables Tables for PGEs CER4.5-6.1P2, CER4.5-6.1P3, and CER4.5-6.2P2. | Tables C.1-2, C.1-3, C.1-7, C.2-2, C.2-3, C.2-7, C.4-10, C.4-11, C.4-12, C.4-13, C.4-15, C.4-16, C.4-17, C.4-21, & C.4-22 |
| 11/26/2012 | R5V10 | 939 | Removed command line testing from PGEs CER4.5-6.2P4, CER4.5-6.4P1, CER4.5-6.5P4, and CER4.5-6.5P5. | Secs. 3.10.1.2, 3.10.4.2, 3.10.7.2, 3.10.10.2, 3.14.1.2, 3.14.4.2, 3.14.7.2, 3.14.10.2, 3.18.1.2, 3.18.5.2, 3.19.1.2, & 3.19.5.2 |
|  |  |  | Formatting issues were fixed. (12/05/2012) | All |
| 7/29/2013 | R5V11 | 973 | Added sibiMap input data and updated the MATCH input data. | Secs. 3.6.1.1, 3.6.2, 3.6.4.1, 3.6.5, 3.6.7.1, 3.6.8, 3.6.10.1, 3.6.11, 3.6.13.1, 3.6.14, 3.6.16.1, 3.6.17, 3.6.19.1, 3.6.20, 3.6.22.1, 3.6.23, 3.6.25.1, 3.6.26, 3.6.28.1, 3.6.29, 3.6.31.1, 3.6.32, 3.6.34.1, & 3.6.35 |
| 7/29/2013 (Cont'd) | R5V11 | 973 | Added P6 and x86 processing and changed c-shell scripts to perl scripts. | Secs. 3.6.1.2, 3.6.2, 3.6.2.1, 3.6.3, 3.6.4.2, 3.6.5, 3.6.5.1, 3.6.6, 3.6.7.2, 3.6.8, 3.6.8.1, 3.6.9, 3.6.10.2, 3.6.11, 3.6.11.1, 3.6.12, 3.6.13.2, 3.6.14, 3.6.14.1, 3.6.15, 3.6.16.2, 3.6.17, 3.6.17.1, 3.6.18, 3.6.19.2, 3.6.20, 3.6.20.1, 3.6.21, 3.6.22.2, 3.6.23, 3.6.23.1, 3.6.24, 3.6.25.2, 3.6.26, 3.6.26.1, 3.6.27, 3.6.28.2, 3.6.29, 3.6.29.1, 3.6.30, 3.6.31.2, 3.6.32, 3.6.32.1, 3.6.33, 3.6.34.2, 3.6.35, 3.6.35.1, & 3.6.36 |
|  |  |  | Updated Test Summary. | Secs. 3.6.1.4, 3.6.4.4, 3.6.7.4, 3.6.10.4, 3.6.13.4, 3.6.16.4, 3.6.19.4, 3.6.22.4, 3.6.25.4, 3.6.28.4, 3.6.31.4, & 3.6.34.4 |
|  |  |  | Updated compiling instructions for PGE CER4.5-6.1P6. | Sec. 2.2.2 |
| 2/19/2014 | R5V12 | 1001 | Added PGE CER4.5-6.0P6. | Secs. 1.2.1, 2.2.1, 3.1, Tables C.1-2, C.2-1, & C.4-1 |
| 2/19/2014 (Continued) | R5V12 | 1001 | Added fixes for PGE CER4.5-6.1P6. | Secs. 1.2.2, 2.2.3, 2.2.5, Tables C.1-8, C.2-8, C.4-3, & C.4-16 |
| 4/16/2014 | R5V13 | 1009 | Modified compilation instructions. | Sec. 2.2.5 |
|  |  |  | Removed SCOOL output files from PGEs CER4.5-6.2P2, CER4.5-6.2P3, and CER4.5-6.2P4. | Secs. 3.9, 3.9.1.1, 3.9.2.2-3, 3.9.4.1, 3.9.5, 3.9.5.2-3, 3.9.7.1, 3.9.8, 3.9.8.2-3, 3.9.10.1, 3.9.11, 3.9.11.2-3, 3.10, 3.10.1.1, 3.10.2, 3.10.2.1-3, 3.10.4.1, 3.10.5, 3.10.5.1-3, 3.10.7.1, 3.10.8, 3.10.8.1-3, 3.10.10.1, 3.10.11, 3.10.11.1-3, 3.11, 3.11.1.1, 3.11.2, 3.11.2.2-3, 3.11.4.1, 3.11.5, 3.11.5.2-3, 3.11.7.1, 3.11.8, 3.11.8.2-3, 3.11.10.1, 3.11.11, 3.11.11.2-3, & Fig. B-2 |
|  |  |  | Added Stand Alone Test Procedures for FM5. | Sec. 3.10.13 |
| 03/21/13 | R5V14 | 959 | Added and updated PGE CER4.5-6.1P7 for NPP. | Secs. 1.2.2, 2.2.4, 3.8, Fig. B-3, Tables C.1-8, C.2-8, C.4-3, C.4-17, & C.5-2 |
| 03/21/13 (Cont'd) | R5V14 | 959 | Added MATCH-daily input files for PGEs CER4.5-6.1P6 and CER4.5-6.1P7 and added the SORCE TSI input file for PGE CER4.5-6.1P6. | Secs. 3.7.1.1, 3.7.2, 3.7.4.1, 3.7.5, 3.7.7.1, 3.7.8, 3.7.10.1, 3.7.11, 3.7.13.1, 3.7.14, 3.7.16.1, 3.7.17, 3.8.1.1, 3.8.2, 3.8.4.1, 3.8.5, 3.8.7.1 & 3.8.8 |
|  |  |  | Modified a minor formatting issue. (07/03/2014) | Sec. 3.1.19.1 |
| 04/02/15 | R5V15 | 1064 | Added wording to clarify the HDF file comparison procedure for PGE CER4.5-6.1P7. | Secs. 3.8.2.4, 3.8.5.4, & 3.8.8.4 |
| 06/25/2015 | R5V16 | 1078 | Added P7 and x86-flex processors to the testing proceedures. | Secs. 3.8.1.2, 3.8.4.2, & 3.8.7.2 |
| 12/2/2015 | R5V17 | 1100 | Added commands to move existing input files into temporary directories before CER4.5-6.0P6 tests, then restore them after tests complete. | Secs. 3.1.1.1, 3.1.2, 3.1.5.1, 3.1.6, 3.1.9.1, 3.1.10, 3.1.13.1, 3.1.14, 3.1.17.1, & 3.1.18 |
| 02/01/2017 | R5V18 | 1217 | Updated PGE CER4.5-6.1P6 to be x86 only. | Secs. 2.2.3, 3.7.1.2, 3.7.4.2, 3.7.7.2, 3.7.10.2, 3.7.13.2, 3.7.16.2, 3.7.19.2, 3.7.22.2, 3.7.25.2, 3.7.28.2, 3.7.31.2, & 3.7.34.2 |
| 02/01/2017 | R5V18 | 1218 | Updated PGE CER4.5-6.2P3 to be x86 only. | Secs. 2.2.6, 3.11.1.2, 3.11.4.2, 3.11.7.2, 3.11.10.2, & 3.11.13.2 |
| 02/01/2017 | R5V18 | 1219 | Updated PGE CER4.5-6.4P2 to be x86 only. Added FM5 testing and removed command line testing. | Secs. 2.2.12, 3.17.1.2, 3.17.2, 3.17.4.2, 3.17.5, 3.17.7.2, 3.17.8, 3.17.10.2, 3.17.11, & 3.17.13-3.17.15 |
| 02/01/2017 | R5V18 | 1220 | Updated PGE CER4.5-6.0P6 to be x86 only. Added additional Terra test case. | Secs. 2.2.1, 3.1.1.2, 3.1.5-3.1.8, 3.1.9.2, 3.1.13.2, 3.1.17.2, & 3.1.21.2 |
|  |  |  | Removed PGEs and any references to the following PGEs CER4.5-6.1P1, CER4.5-6.1P2, CER4.5-6.1P3, CER4.5-6.1P4, CER4.5-6.1P5, CER4.5-6.2P1, CER4.5-6.2P2, CER4.5-6.2P4, CER4.5-6.3P1, CER4.5-6.3P2, CER4.5-6.3P3, CER4.5-6.4P1, CER4.5-6.5P2, CER4.5-6.5P3, CER4.5-6.5P4, CER4.5-6.5P5, CER4.5-6.6P2, CER4.5-6.6P3. (03/26/2019) | All |
|  |  |  | Removed Appendices B and C as they are no longer relevant. (03/26/2019) | Apps. B & C |

Preface

The Clouds and the Earth’s Radiant Energy System (CERES) Data Management System (DMS) supports the data processing needs of the CERES Science Team research to increase understanding of the Earth’s climate and radiant environment.  The CERES Data Management Team works with the CERES Science Team to develop the software necessary to support the science algorithms.  This software, being developed to operate at the Langley Atmospheric Science Data Center (ASDC), produces an extensive set of science data products.

The DMS consists of 12 subsystems; each subsystem contains one or more Product Generation Executables.  Each subsystem executes when all of its required input data sets are available and produces one or more archival science products.

This Test Plan is written by the responsible CERES subsystem team for the CERES Configuration Management Team and the Langley ASDC to support subsystem testing.  This document describes the software and supporting data files for this Subsystem and explains the procedures for installing, executing, and testing the software in the Science Software Integration and Testing environment.  A section is also included on validating the software results.

Acknowledgment is given to Tammy O. Ayers and Joanne Saunders of Science Systems Applications, Inc. for their support in preparing this document.

Document Revision Record	ii

1.0	Introduction	1

1.1	Document Overview	1

1.2	Subsystem Overview	2

1.2.1	CER4.5-6.0P6 = CERES Sea Ice Brightness Index Inversion Subsystem 4.5
Pre Processor for Terra and Aqua Edition4 Processing and NPP Processing	2

1.2.2	CERES Inversion to Instantaneous TOA Fluxes and Empirical Estimates of Surface Radiation Budget Subsystems 4.5 and 4.6 Main Processors and HDF
Post Processor	2

1.2.3	CERES Inversion to Instantaneous TOA Fluxes and Empirical Estimates of Surface Radiation Budget Subsystems 4.5 and 4.6 Subset Post Processors	3

1.2.4	CERES Inversion to Instantaneous TOA Fluxes and Empirical Estimates of Surface Radiation Budget Subsystems 4.5 and 4.6 Monthly Validation Site
Post Processor	3

1.2.5	CERES Inversion to Instantaneous TOA Fluxes and Empirical Estimates of Surface Radiation Budget Subsystems 4.5 and 4.6 Alternate Main Processor
and HDF Post Processor Using Instrument IES data	3

1.2.6	CERES Inversion to Instantaneous TOA Fluxes and Empirical Estimates of Surface Radiation Budget Subsystems 4.5 and 4.6 Alternate Main Processor
and HDF Post Processor Using Instrument IES data	3

2.0	Software and Data File Installation Procedures	4

2.1	Installation	4

2.2	Compilation	4

2.2.1	Compiling PGE CER4.5-6.0P6	4

2.2.2	Compiling PGE CER4.5-6.1P6	5

2.2.3	Compiling PGE CER4.5-6.1P7	5

2.2.4	Compiling PGE CER4.5-6.2P3	5

2.2.5	Compiling PGE CER4.5-6.4P2	6

3.0	Test and Evaluation Procedures	7

3.1	CER4_5-6.0P6 Pre Processor for Terra, Aqua and NPP Processing	7

3.1.1	Stand Alone Test Procedures for Terra, Environment variable
REPROCESS=’yes’	7

3.1.1.1	Environment setup and file preparation	7

3.1.1.2	Execution	7

3.1.1.3	Exit Codes	8

3.1.1.4	Test Summary	8

3.1.2	Evaluation Procedures	8

3.1.3	Log and Status File Results and Metadata Evaluation	9

3.1.3.1	Execution of Comparison Software for the Main Processor	9

3.1.4	Solutions to Possible Problems	9

3.1.5	Stand Alone Test Procedures for Terra, Environment variable
REPROCESS=’no’	10

3.1.5.1	Environment setup and file preparation	10

3.1.5.2	Execution	10

3.1.5.3	Exit Codes	11

3.1.5.4	Test Summary	11

3.1.6	Evaluation Procedures	11

3.1.7	Log and Status File Results and Metadata Evaluation	11

3.1.7.1	Execution of Comparison Software for the Main Processor	12

3.1.8	Solutions to Possible Problems	12

3.1.9	Stand Alone Test Procedures for Aqua, Environment variable
REPROCESS=’yes’	13

3.1.9.1	Environment setup and file preparation	13

3.1.9.2	Execution	13

3.1.9.3	Exit Codes	14

3.1.9.4	Test Summary	14

3.1.10	Evaluation Procedures	14

3.1.11	Log and Status File Results and Metadata Evaluation	14

3.1.11.1	Execution of Comparison Software for the Main Processor	15

3.1.12	Solutions to Possible Problems	15

3.1.13	Stand Alone Test Procedures for Aqua, Environment variable
REPROCESS=’no’	16

3.1.13.1	Environment setup and file preparation	16

3.1.13.2	Execution	16

3.1.13.3	Exit Codes	17

3.1.13.4	Test Summary	17

3.1.14	Evaluation Procedures	17

3.1.15	Log and Status File Results and Metadata Evaluation	17

3.1.15.1	Execution of Comparison Software for the Main Processor	18

3.1.16	Solutions to Possible Problems	18

3.1.17	Stand Alone Test Procedures for NPP, Environment variable
REPROCESS=’yes’	19

3.1.17.1	Environment setup and file preparation	19

3.1.17.2	Execution	19

3.1.17.3	Exit Codes	20

3.1.17.4	Test Summary	20

3.1.18	Evaluation Procedures	20

3.1.19	Log and Status File Results and Metadata Evaluation	20

3.1.19.1	Execution of Comparison Software for the Main Processor	21

3.1.20	Solutions to Possible Problems	21

3.1.21	Stand Alone Test Procedures for NPP, Environment variable
REPROCESS=’no’	22

3.1.21.1	Environment setup and file preparation	22

3.1.21.2	Execution	22

3.1.21.3	Exit Codes	23

3.1.21.4	Test Summary	23

3.1.22	Evaluation Procedures	23

3.1.23	Log and Status File Results and Metadata Evaluation	23

3.1.23.1	Execution of Comparison Software for the Main Processor	24

3.1.24	Solutions to Possible Problems	24

3.2	CER4_5-6.1P6 Main and Post Processors for Terra and Aqua Edition4 Processing	25

3.2.1	Stand Alone Test Procedures for FM1, Environment variables:
REPROCESS = ‘NO’, READ_IES = ‘NO’ and PROD = ‘no’	25

3.2.1.1	Environment setup and file preparation	25

3.2.1.2	Execution	26

3.2.1.3	Exit Codes	26

3.2.1.4	Test Summary	27

3.2.2	Evaluation Procedures	27

3.2.2.1	Log and Status File Results and Metadata Evaluation	27

3.2.2.2	Execution of Comparison Software for the Main Processor	28

3.2.2.3	Evaluation of Comparison Software Output	28

3.2.2.4	Evaluation of SSF HDF Product	28

3.2.3	Solutions to Possible Problems	29

3.2.4	Stand Alone, command line, Test Procedures for FM1, Environment
Variables REPROCESS = ‘YES’, READ_IES = ‘NO’ and PROD = ‘no’	30

3.2.4.1	Environment setup and file preparation	30

3.2.4.2	Execution	31

3.2.4.3	Exit Codes	31

3.2.4.4	Test Summary	32

3.2.5	Evaluation Procedures	32

3.2.5.1	Log and Status File Results and Metadata Evaluation	32

3.2.5.2	Execution of Comparison Software for the Main Processor	33

3.2.5.3	Evaluation of Comparison Software Output	33

3.2.5.4	Evaluation of SSF HDF Product	33

3.2.6	Solutions to Possible Problems	34

3.2.7	Stand Alone, command line, Test Procedures for FM1, Environment
Variables REPROCESS = ‘YES’ and READ_IES = ‘YES’	35

3.2.7.1	Environment setup and file preparation	35

3.2.7.2	Execution	36

3.2.7.3	Exit Codes	36

3.2.7.4	Test Summary	37

3.2.8	Evaluation Procedures	37

3.2.8.1	Log and Status File Results and Metadata Evaluation	37

3.2.8.2	Execution of Comparison Software for the Main Processor	38

3.2.8.3	Evaluation of Comparison Software Output	38

3.2.8.4	Evaluation of SSF HDF Product	39

3.2.9	Solutions to Possible Problems	39

3.2.10	Stand Alone Test Procedures for FM2, Environment variables:
REPROCESS = ‘NO’, READ_IES = ‘NO’ and PROD = ‘no’	40

3.2.10.1	Environment setup and file preparation	40

3.2.10.2	Execution	41

3.2.10.3	Exit Codes	41

3.2.10.4	Test Summary	41

3.2.11	Evaluation Procedures	42

3.2.11.1	Log and Status File Results and Metadata Evaluation	42

3.2.11.2	Execution of Comparison Software for the Main Processor	43

3.2.11.3	Evaluation of Comparison Software Output	43

3.2.11.4	Evaluation of SSF HDF Product	43

3.2.12	Solutions to Possible Problems	44

3.2.13	Stand Alone, command line, Test Procedures for FM2, Environment
Variables REPROCESS = ‘YES’, READ_IES = ‘NO’ and PROD = ‘no’	45

3.2.13.1	Environment setup and file preparation	45

3.2.13.2	Execution	46

3.2.13.3	Exit Codes	46

3.2.13.4	Test Summary	47

3.2.14	Evaluation Procedures	47

3.2.14.1	Log and Status File Results and Metadata Evaluation	47

3.2.14.2	Execution of Comparison Software for the Main Processor	48

3.2.14.3	Evaluation of Comparison Software Output	48

3.2.14.4	Evaluation of SSF HDF Product	48

3.2.15	Solutions to Possible Problems	49

3.2.16	Stand Alone, command line, Test Procedures for FM2, Environment
Variables REPROCESS = ‘YES’ and READ_IES = ‘YES’	50

3.2.16.1	Environment setup and file preparation	50

3.2.16.2	Execution	51

3.2.16.3	Exit Codes	51

3.2.16.4	Test Summary	52

3.2.17	Evaluation Procedures	52

3.2.17.1	Log and Status File Results and Metadata Evaluation	52

3.2.17.2	Execution of Comparison Software for the Main Processor	53

3.2.17.3	Evaluation of Comparison Software Output	53

3.2.17.4	Evaluation of SSF HDF Product	54

3.2.18	Solutions to Possible Problems	54

3.2.19	Stand Alone Test Procedures for FM3, Environment variables:
REPROCESS = ‘NO’, READ_IES = ‘NO’ and PROD = ‘no’	55

3.2.19.1	Environment setup and file preparation	55

3.2.19.2	Execution	56

3.2.19.3	Exit Codes	56

3.2.19.4	Test Summary	56

3.2.20	Evaluation Procedures	57

3.2.20.1	Log and Status File Results and Metadata Evaluation	57

3.2.20.2	Execution of Comparison Software for the Main Processor	58

3.2.20.3	Evaluation of Comparison Software Output	58

3.2.20.4	Evaluation of SSF HDF Product	58

3.2.21	Solutions to Possible Problems	59

3.2.22	Stand Alone, command line, Test Procedures for FM3, Environment
Variables REPROCESS = ‘YES’, READ_IES = ‘NO’ and PROD = ‘no’	60

3.2.22.1	Environment setup and file preparation	60

3.2.22.2	Execution	61

3.2.22.3	Exit Codes	61

3.2.22.4	Test Summary	62

3.2.23	Evaluation Procedures	62

3.2.23.1	Log and Status File Results and Metadata Evaluation	62

3.2.23.2	Execution of Comparison Software for the Main Processor	63

3.2.23.3	Evaluation of Comparison Software Output	63

3.2.23.4	Evaluation of SSF HDF Product	63

3.2.24	Solutions to Possible Problems	64

3.2.25	Stand Alone, command line, Test Procedures for FM3, Environment
Variables REPROCESS = ‘YES’ and READ_IES = ‘YES’	65

3.2.25.1	Environment setup and file preparation	65

3.2.25.2	Execution	66

3.2.25.3	Exit Codes	66

3.2.25.4	Test Summary	67

3.2.26	Evaluation Procedures	67

3.2.26.1	Log and Status File Results and Metadata Evaluation	67

3.2.26.2	Execution of Comparison Software for the Main Processor	68

3.2.26.3	Evaluation of Comparison Software Output	68

3.2.26.4	Evaluation of SSF HDF Product	68

3.2.27	Solutions to Possible Problems	69

3.2.28	Stand Alone Test Procedures for FM4, Environment variables:
REPROCESS = ‘NO’, READ_IES = ‘NO’ and PROD = ‘no’	70

3.2.28.1	Environment setup and file preparation	70

3.2.28.2	Execution	71

3.2.28.3	Exit Codes	71

3.2.28.4	Test Summary	71

3.2.29	Evaluation Procedures	72

3.2.29.1	Log and Status File Results and Metadata Evaluation	72

3.2.29.2	Execution of Comparison Software for the Main Processor	73

3.2.29.3	Evaluation of Comparison Software Output	73

3.2.29.4	Evaluation of SSF HDF Product	73

3.2.30	Solutions to Possible Problems	74

3.2.31	Stand Alone, command line, Test Procedures for FM4, Environment
Variables REPROCESS = ‘YES’, READ_IES = ‘NO’ and PROD = ‘no’	75

3.2.31.1	Environment setup and file preparation	75

3.2.31.2	Execution	76

3.2.31.3	Exit Codes	76

3.2.31.4	Test Summary	77

3.2.32	Evaluation Procedures	77

3.2.32.1	Log and Status File Results and Metadata Evaluation	78

3.2.32.2	Execution of Comparison Software for the Main Processor	78

3.2.32.3	Evaluation of Comparison Software Output	78

3.2.32.4	Evaluation of SSF HDF Product	79

3.2.33	Solutions to Possible Problems	79

3.2.34	Stand Alone, command line, Test Procedures for FM4, Environment
Variables REPROCESS = ‘YES’ and READ_IES = ‘YES’	80

3.2.34.1	Environment setup and file preparation	80

3.2.34.2	Execution	81

3.2.34.3	Exit Codes	81

3.2.34.4	Test Summary	82

3.2.35	Evaluation Procedures	82

3.2.35.1	Log and Status File Results and Metadata Evaluation	83

3.2.35.2	Execution of Comparison Software for the Main Processor	83

3.2.35.3	Evaluation of Comparison Software Output	83

3.2.35.4	Evaluation of SSF HDF Product	84

3.2.36	Solutions to Possible Problems	84

3.3	CER4_5-6.1P7 Main and Post Processors for S-NPP Processing	85

3.3.1	Stand Alone Test Procedures for FM5, Environment variables:
REPROCESS = ‘NO’, READ_IES = ‘NO’ and PROD = ‘no’	85

3.3.1.1	Environment setup and file preparation	85

3.3.1.2	Execution	86

3.3.1.3	Exit Codes	86

3.3.1.4	Test Summary	86

3.3.2	Evaluation Procedures	87

3.3.2.1	Log and Status File Results and Metadata Evaluation	87

3.3.2.2	Execution of Comparison Software for the Main Processor	88

3.3.2.3	Evaluation of Comparison Software Output	88

3.3.2.4	Evaluation of SSF HDF Product	88

3.3.3	Solutions to Possible Problems	89

3.3.4	Stand Alone, command line, Test Procedures for FM5, Environment
Variables REPROCESS = ‘YES’, READ_IES = ‘NO’ and PROD = ‘no’	90

3.3.4.1	Environment setup and file preparation	90

3.3.4.2	Execution	91

3.3.4.3	Exit Codes	91

3.3.4.4	Test Summary	91

3.3.5	Evaluation Procedures	92

3.3.5.1	Log and Status File Results and Metadata Evaluation	92

3.3.5.2	Execution of Comparison Software for the Main Processor	93

3.3.5.3	Evaluation of Comparison Software Output	93

3.3.5.4	Evaluation of SSF HDF Product	93

3.3.6	Solutions to Possible Problems	94

3.3.7	Stand Alone, command line, Test Procedures for FM5, Environment
Variables REPROCESS = ‘YES’ and READ_IES = ‘YES’	95

3.3.7.1	Environment setup and file preparation	95

3.3.7.2	Execution	96

3.3.7.3	Exit Codes	96

3.3.7.4	Test Summary	96

3.3.8	Evaluation Procedures	97

3.3.8.1	Log and Status File Results and Metadata Evaluation	97

3.3.8.2	Execution of Comparison Software for the Main Processor	98

3.3.8.3	Evaluation of Comparison Software Output	98

3.3.8.4	Evaluation of SSF HDF Product	98

3.3.9	Solutions to Possible Problems	99

3.4	CER4_5-6.2P3 Terra and Aqua Edition4 and NPP Edition1 SSF Subsetting
Post Processor Producing Daily SSF and SSFA Subset Files, and Nadir SSF,
Validation SSF, and Validation SSFA Subset Products	100

3.4.1	Stand Alone Test Procedures for FM1	100

3.4.1.1	Environment setup and file preparation	100

3.4.1.2	Execution	100

3.4.1.3	Exit Codes	101

3.4.1.4	Test Summary	101

3.4.2	Evaluation Procedures	101

3.4.2.1	Log and Status File Results and Metadata Evaluation	101

3.4.2.2	Execution of Comparison Software for the SSF Subset Post Processor	102

3.4.2.3	Evaluation of Comparison Software Output	102

3.4.2.4	Evaluation of SSF HDF Product	102

3.4.3	Solutions to Possible Problems	103

3.4.4	Stand Alone Test Procedures for FM2	104

3.4.4.1	Environment setup and file preparation	104

3.4.4.2	Execution	104

3.4.4.3	Exit Codes	105

3.4.4.4	Test Summary	105

3.4.5	Evaluation Procedures	105

3.4.5.1	Log and Status File Results and Metadata Evaluation	105

3.4.5.2	Execution of Comparison Software for the SSF Subset Post Processor	106

3.4.5.3	Evaluation of Comparison Software Output	106

3.4.5.4	Evaluation of SSF HDF Product	106

3.4.6	Solutions to Possible Problems	107

3.4.7	Stand Alone Test Procedures for FM3	108

3.4.7.1	Environment setup and file preparation	108

3.4.7.2	Execution	108

3.4.7.3	Exit Codes	109

3.4.7.4	Test Summary	109

3.4.8	Evaluation Procedures	109

3.4.8.1	Log and Status File Results and Metadata Evaluation	109

3.4.8.2	Execution of Comparison Software for the SSF Subset Post Processor	110

3.4.8.3	Evaluation of Comparison Software Output	110

3.4.8.4	Evaluation of SSF HDF Product	110

3.4.9	Solutions to Possible Problems	111

3.4.10	Stand Alone Test Procedures for FM4	112

3.4.10.1	Environment setup and file preparation	112

3.4.10.2	Execution	112

3.4.10.3	Exit Codes	113

3.4.10.4	Test Summary	113

3.4.11	Evaluation Procedures	113

3.4.11.1	Log and Status File Results and Metadata Evaluation	113

3.4.11.2	Execution of Comparison Software for the SSF Subset Post Processor	114

3.4.11.3	Evaluation of Comparison Software Output	114

3.4.11.4	Evaluation of SSF HDF Product – THERE IS NO HDF PRODUCT
WITH THIS TEST DATA.	115

3.4.12	Solutions to Possible Problems	115

3.4.13	Stand Alone Test Procedures for FM5	116

3.4.13.1	Environment setup and file preparation	116

3.4.13.2	Execution	116

3.4.13.3	Exit Codes	117

3.4.13.4	Test Summary	117

3.4.14	Evaluation Procedures	117

3.4.14.1	Log and Status File Results and Metadata Evaluation	117

3.4.14.2	Execution of Comparison Software for the SSF Subset Post Processor	118

3.4.14.3	Evaluation of Comparison Software Output	118

3.4.14.4	Evaluation of SSF HDF Product	119

3.4.15	Solutions to Possible Problems	119

3.5	CER4_5-6.4P2 Terra and Aqua Edition4 SSF Post Processor Producing
Monthly SSF and SSFA Validation subset files	120

3.5.1	Stand Alone Test Procedures for FM1	120

3.5.1.1	Environment setup and file preparation	120

3.5.1.2	Execution	120

3.5.1.3	Exit Codes	121

3.5.1.4	Test Summary	121

3.5.2	Evaluation Procedures	121

3.5.2.1	Log and Status File Results and Metadata Evaluation	121

3.5.2.2	Execution of Comparison Software for the SSF Subset Post Processor	122

3.5.2.3	Evaluation of Comparison Software Output	122

3.5.3	Solutions to Possible Problems	122

3.5.4	Stand Alone Test Procedures for FM2	124

3.5.4.1	Environment setup and file preparation	124

3.5.4.2	Execution	124

3.5.4.3	Exit Codes	125

3.5.4.4	Test Summary	125

3.5.5	Evaluation Procedures	125

3.5.5.1	Log and Status File Results and Metadata Evaluation	125

3.5.5.2	Execution of Comparison Software for the SSF Subset Post Processor	126

3.5.5.3	Evaluation of Comparison Software Output	126

3.5.6	Solutions to Possible Problems	126

3.5.7	Stand Alone Test Procedures for FM3	128

3.5.7.1	Environment setup and file preparation	128

3.5.7.2	Execution	128

3.5.7.3	Exit Codes	129

3.5.7.4	Test Summary	129

3.5.8	Evaluation Procedures	129

3.5.8.1	Log and Status File Results and Metadata Evaluation	129

3.5.8.2	Execution of Comparison Software for the SSF Subset Post Processor	130

3.5.8.3	Evaluation of Comparison Software Output	130

3.5.9	Solutions to Possible Problems	130

3.5.10	Stand Alone Test Procedures for FM4	131

3.5.10.1	Environment setup and file preparation	131

3.5.10.2	Execution	131

3.5.10.3	Exit Codes	132

3.5.10.4	Test Summary	132

3.5.11	Evaluation Procedures	132

3.5.11.1	Log and Status File Results and Metadata Evaluation	132

3.5.11.2	Execution of Comparison Software for the SSF Subset Post Processor	133

3.5.11.3	Evaluation of Comparison Software Output	133

3.5.12	Solutions to Possible Problems	133

3.5.13	Stand Alone Test Procedures for FM5	135

3.5.13.1	Environment setup and file preparation	135

3.5.13.2	Execution	135

3.5.13.3	Exit Codes	136

3.5.13.4	Test Summary	136

3.5.14	Evaluation Procedures	136

3.5.14.1	Log and Status File Results and Metadata Evaluation	136

3.5.14.2	Execution of Comparison Software for the SSF Subset Post Processor	137

3.5.14.3	Evaluation of Comparison Software Output	137

3.5.15	Solutions to Possible Problems	137

Appendix A - Acronyms and Abbreviations	A-1

# Introduction

CERES is a key component of EOS and NPP.  The first CERES instrument (PFM) flew on TRMM, four instruments are currently operating on the EOS Terra (FM1 and FM2) and Aqua (FM3 and FM4) platforms, and NPP (FM5) platform.  CERES measures radiances in three broadband channels:  a shortwave channel (0.3 - 5 m), a total channel (0.3 - 200 m), and an infrared window channel (8 - 12 m).  The last data processed from the PFM instrument aboard TRMM was March 2000; no additional data are expected.  Until June 2005, one instrument on each EOS platform operated in a fixed azimuth scanning mode and the other operated in a rotating azimuth scanning mode; now all are typically operating in the fixed azimuth scanning mode.  The NPP platform carries the FM5 instrument, which operates in the fixed azimuth scanning mode though it has the capability to operate in a rotating azimuth scanning mode.

CERES climate data records involve an unprecedented level of data fusion:  CERES measurements are combined with imager data (e.g., MODIS on Terra and Aqua, VIIRS on NPP), 4-D weather assimilation data, microwave sea-ice observations, and measurements from five geostationary satellites to produce climate-quality radiative fluxes at the top-of-atmosphere, within the atmosphere and at the surface, together with the associated cloud and aerosol properties.

The CERES project management and implementation responsibility is at NASA Langley.  The CERES Science Team is responsible for the instrument design and the derivation and validation of the scientific algorithms used to produce the data products distributed to the atmospheric sciences community.  The CERES DMT is responsible for the development and maintenance of the software that implements the science team’s algorithms in the production environment to produce CERES data products.  The Langley ASDC is responsible for the production environment, data ingest, and the processing, archival, and distribution of the CERES data products.

## Document Overview

This document, CERES Inversion to Instantaneous Top-of-Atmosphere (TOA) Fluxes and Empirical Estimates of Surface Radiation Budget Subsystems 4.5 and 4.6 Release 4 Test Plan, is part of the CERES Subsystems 4.5 and 4.6 Release 4 delivery package provided to the Langley Atmospheric Science Data Center (ASDC).  It provides a description of the CERES Inversion to Instantaneous TOA Fluxes and Empirical Estimates of Surface Radiation Budget Release 4 software and explains the procedures for installing, executing, and testing the software.  A section is also included on validating the software results.  A description of acronyms and abbreviations is provided in Appendix A.

This document is organized as follows:

Section 1.0 - Introduction

Section 2.0 - Software and Data File Installation Procedures

Section 3.0 - Test and Evaluation Procedures

Appendix A - Acronyms and Abbreviations

## Subsystem Overview

### CER4.5-6.0P6 = CERES Sea Ice Brightness Index Inversion Subsystem 4.5 Pre Processor for Terra and Aqua Edition4 Processing and NPP Processing

The Terra and Aqua Edition4 and the NPP ADMs for fresh snow and sea ice scene types rely on the MODIS spectral information for scene classification.  For clear-sky and partly cloudy sky scenes this information is computed using the clear-sky radiances.  For overcast scenes where we can't see the surface, a monthly map of the relevant value is used to determine which ADM to use.

For sea ice scenes the Sea Ice Brightness Index (SIBI) is used to determine the ADM type.  The SIBI is defined as 1.0-(ref_0469-ref_0858)/(ref_0469+ref_0858), where ref_0469 is the clear-sky reflectance in the 0.469 micron band and ref_0858 is the clear-sky reflectance in the 0.858 micron band.

The code reads in the cross-track SSF files for each month and outputs the mean SIBI in each grid box defined by the CERES nested-grid routine.  For the SIBI, the conditions require that there be some sea ice present from at least one of sfc_type (ssf-25 & ssf-26) and/or snow_ice (ssf-69).  The cloud fraction must be greater than or equal to 0% and less than 99%.  The SIBI value is calculated in the main program.  The FOV's are looped over and the respective values are summed for each grid box and the count is kept.  Once the month has finished processing the mean value (sum/count) is output for each region that has a count greater than zero.

### CERES Inversion to Instantaneous TOA Fluxes and Empirical Estimates of Surface Radiation Budget Subsystems 4.5 and 4.6 Main Processors and HDF Post Processor

The Main Processor Product Generation Executives (PGE) CER4.5-6.1P6 and CER4.5-6.1P7 CERES Inversion to Instantaneous TOA Fluxes and the Empirical Estimates of Surface Radiation Budget, Subsystems 4.5 and 4.6, convert CERES filtered radiance measurements to instantaneous radiative flux estimates at the top of the Earth’s atmosphere and produces radiative flux estimates at the Earth’s surface for each CERES footprint.  The output of the Subsystems 4.5 and 4.6 Main Processor PGE CER4.5-6.1P6, which is for Terra/Aqua Edition4 processing, consists of a binary Single Scanner Footprint TOA/Surface Fluxes and Clouds (SSF) product, a binary SSF Aerosol (SSFA) product containing MODIS aerosols, an ASCII Quality Control (QC) report, and a binary QC file. This PGE also has the option of using an alternate Instrument IES as input.  The output of the Subsystems 4.5 and 4.6 Main Processor PGE CER4.5-6.1P7, which is for S-NPP processing, consists of a binary Single Scanner Footprint TOA/Surface Fluxes and Clouds (SSF) product, a binary SSF Aerosol (SSFA) product containing MODIS aerosols, an ASCII Quality Control (QC) report, and a binary QC file.  This PGE also has the option of using an alternate Instrument IES as input.

The HDF Post Processor for CERES Inversion to Instantaneous TOA Fluxes and the Empirical Estimates of Surface Radiation Budget, Subsystems 4.5 and 4.6, reads the binary SSF (and the binary SSFA for Terra and Aqua processing) as input and generates an SSF product in Hierarchical Data Format (HDF).

### CERES Inversion to Instantaneous TOA Fluxes and Empirical Estimates of Surface Radiation Budget Subsystems 4.5 and 4.6 Subset Post Processors

The Subsetting Post Processor PGE CER4.5-6.2P3 (for Terra and Aqua Edition4 SSF subsetting) for CERES Inversion to Instantaneous TOA Fluxes and the Empirical Estimates of Surface Radiation Budget, Subsystems 4.5 and 4.6, reads up to 24 hourly binary SSF products as input and generates two SSF daily subset files, the first containing daytime data and the second containing nighttime data.  CER4.5-6.2P3 also read in the hourly Terra or Aqua binary SSFA products as input and subsets the SSFA file into two daytime and nighttime aerosol binary files.  The same footprints that were placed on the SSF subset files are selected for the SSF aerosol subset files.  PGE CER4.5-6.2P3 also produce daily binary and HDF SSF Nadir products that contain nadir viewing footprints and a daily binary SSF validation product.

### CERES Inversion to Instantaneous TOA Fluxes and Empirical Estimates of Surface Radiation Budget Subsystems 4.5 and 4.6 Monthly Validation Site Post Processor

The Monthly Validation Site Post Processor combines all of the CERES validation site footprint records that were archived in the daily validation site SSF products for a single instrument during a data month and combines them into a single monthly binary SSF file.

### CERES Inversion to Instantaneous TOA Fluxes and Empirical Estimates of Surface Radiation Budget Subsystems 4.5 and 4.6 Alternate Main Processor and HDF Post Processor Using Instrument IES data

The Alternate Main Processor converts CERES unfiltered radiance measurements to instantaneous radiative flux estimates at the top of the Earth’s atmosphere and produces radiative flux estimates at the Earth’s surface for each CERES footprint.  This processor uses an archived binary SSF and an archived binary IES as input and only the TOA and surface fluxes are replaced.  The output of Subsystems 4.5 and 4.6 Alternate Main Processor consists of an Edition4 binary Single Scanner Footprint (SSF) product and an SSF product in Hierarchical Data Format (HDF).

### CERES Inversion to Instantaneous TOA Fluxes and Empirical Estimates of Surface Radiation Budget Subsystems 4.5 and 4.6 Alternate Main Processor and HDF Post Processor Using Instrument IES data

The Alternate Main Processor converts CERES unfiltered radiance measurements to instantaneous radiative flux estimates at the top of the Earth’s atmosphere and produces radiative flux estimates at the Earth’s surface for each CERES footprint.  This processor uses an archived binary SSF and an archived binary IES as input and only the TOA and surface fluxes are replaced.  The output of Subsystems 4.5 and 4.6 Alternate Main Processor consists of an Edition3 binary Single Scanner Footprint (SSF) product and an SSF product in Hierarchical Data Format (HDF).

# Software and Data File Installation Procedures

This section describes how to install the Subsystems 4.5 and 4.6 Inversion software in preparation for making the necessary test runs at the Langley ASDC.  The installation procedures include instructions for uncompressing and untarring the delivered tar files, properly defining environmental variables, and compiling the Inversion programs.

## Installation

Software/Data File Install Procedure:

The scripts, makefiles and Process Control Files in the Subsystems 4.5 and 4.6 delivery package expect the CERES environment variable, $CERESENV, to point to a file which sets the following environment variables:

PGSDIR	-	Directory for Toolkit libraries

F90	-	Pointer to the SGI F90 64 bit compiler

CERESHOME	-	Top Directory for CERES Software

CERESLIB	-	Directory for CERESlib

PGSMSG	-	Directory which contains Toolkit and CERES Status Message Files

PGSLIB	-	Directory which contains SGI 64-bit Toolkit library file

PGSINC	-	Pointer to the PGS include file directory

HDFDIR	-	Pointer to the HDF home directory

HDFINC	-	Pointer to the directory containing the HDF header files

HDFLIB	-	Pointer to the directory containing the HDF library

Change directory to the directory where you plan to install the Inversion Subsystems.  (The following instructions assume that the directory will be $CERESHOME.)

Uncompress and untar the tar files by replacing XXX with the appropriate SCCR number and typing the following commands:

uncompress inversion_src_R5-XXX.tar.Z

tar xf inversion_src_R5-XXX.tar

uncompress inversion_anc_R5-XXX.tar.Z

tar xf inversion_anc_R5-XXX.tar

uncompress inversion_data_R5-XXX.tar.Z

tar xf inversion_data_R5-XXX.tar

## Compilation

### Compiling PGE CER4.5-6.0P6

To create the Pre Processor executables on directory $CERESHOME/inversion/CER4.5-6.0P6/bin/ and to create the comparison software executables on $CERESHOME/inversion/test_suites/bin, type the following commands:

source $CERESENV

cd $CERESHOME/inversion/CER4.5-6.0P6/rcf

For Terra, Aqua and NPP processing, execute the following command:

compile_4.5-6.0P6.pl

The following files will be created in $CERESHOME/inversion/CER4.5-6.0P6/bin:

mapSpecModels_x86_64.exe for x86 processor

### Compiling PGE CER4.5-6.1P6

To create the Main and Post Processor executables on directory $CERESHOME/inversion/CER4.5-6.1P6/bin/ and to create the comparison software executables on $CERESHOME/inversion/test_suites/bin, type the following commands:

source $CERESENV

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

For Terra and Aqua processing, execute the following command:

compile_4.5-6.1P6.pl

The following files will be created in $CERESHOME/inversion/CER4.5-6.1P6/bin:

invsurf_1p6_x86_64.exe for x86 processor

ssf2hdf_ed4_x86_64.exe for x86 processor

### Compiling PGE CER4.5-6.1P7

To create the Main and Post Processor executables on directory $CERESHOME/inversion/CER4.5-6.1P7/bin/ and to create the comparison software executables on $CERESHOME/inversion/test_suites/bin, type the following commands:

source $CERESENV

cd $CERESHOME/inversion/CER4.5-6.1P7/rcf

For Terra and Aqua processing, execute the following command:

compile_4.5-6.1P7.pl

The following files will be created in $CERESHOME/inversion/CER4.5-6.1P7/bin:

invsurf_1p7_ppc64.exe for P6 processor

invsurf_1p7_x86_64.exe for x86 processor

ssf2hdf_ed4_ppc64.exe for P6 processor

ssf2hdf_ed4_x86_64.exe for x86 processor

### Compiling PGE CER4.5-6.2P3

To create the SSF Subset Post Processor and HDF Post Processor for PGE CER4.5-6.2P3 on directory $CERESHOME/inversion/CER4.5-6.2P3/bin/ and to create the comparison software executable on $CERESHOME/inversion/test_suites/bin, type the following commands:

source $CERESENV

cd $CERESHOME/inversion/CER4.5-6.2P3/rcf

For Terra, Aqua, and NPP processing, execute the following command:

compile_4.5-6.2P3.csh

The following files will be created in $CERESHOME/inversion/CER4.5-6.2P3/bin:

ssf2hdf_ed4_x86_64.exe for x86 processor

subset_ssf_2p3_x86_64.exe for x86 processor

The following files will be created in $CERESHOME/inversion/test_suites/bin:

comp_subsets_2p3_x86_64.exe for x86 processor

comp_ssf2a_subsets_2p3_x86_64.exe for x86 processor

compare_nadir_ssf_2p3_x86_64.exe for x86 processor

compare_ssfa_2p3_x86_64.exe for x86 processor

### Compiling PGE CER4.5-6.4P2

To create the Alternate Main and Post Processor executables on directory $CERESHOME/inversion/CER4.5-6.4P2/bin/ and to create the comparison software executables on $CERESHOME/inversion/test_suites/bin, type the following commands:

source $CERESENV

cd $CERESHOME/inversion/CER4.5-6.4P2/rcf

compile_4.5-6.4P2.csh

The following files will be created in $CERESHOME/inversion/CER4.5-6.4P2/bin:

monthly_val_ssf_x86_64.exe for x86 processors

# Test and Evaluation Procedures

This section provides general information on how to execute Subsystems 4.5 and 4.6 and provides an overview of the test and evaluation procedures.  It includes a description of what is being tested and the order in which the tests should be performed.

## CER4_5-6.0P6 Pre Processor for Terra, Aqua and NPP Processing

### Stand Alone Test Procedures for Terra, Environment variable REPROCESS=’yes’

#### Environment setup and file preparation

cd $CERESHOME/inversion/CER4.5-6.0P6/rcf

setenv YEAR 2004

setenv MONTH 07

setenv INSTANCE_0P6 Terra-MODIS_Edition4_000000.200407

source $CERESHOME/inversion/CER4.5-6.0P6/rcf/inversion-terra-env.csh

Copy any existing input files to a temporary directory:

mkdir $InputArchive/SSFB/Terra-FM1-MODIS_Beta2-Ed4/2004/07/TEMP_MV_FOR_CM_TEST

mv $InputArchive/SSFB/Terra-FM1-MODIS_Beta2-Ed4/2004/07/CER* $InputArchive/SSFB/Terra-FM1-MODIS_Beta2-Ed4/2004/07/TEMP_MV_FOR_CM_TEST/

Copy the input files to appropriate locations:

cp $CERESHOME/inversion/data/input/CER4.5-6.0P6/CER_SSFB_Terra-FM1-MODIS_Beta2-Ed4_400401.200407*12 $InputArchive/SSFB/Terra-FM1-MODIS_Beta2-Ed4/2004/07/

#### Execution

Execute the production script by typing the script name, CER4.5-6.0P6-SGE_Driver.pl, followed by the date and hour options and the cleanup option.

cd $CERESHOME/inversion/CER4.5-6.0P6/rcf

$CERESHOME/inversion/CER4.5-6.0P6/rcf/CER4.5-6.0P6-SGE_Driver.pl -date 200407 -clean

The following file will be generated:

$CERESHOME/inversion/CER4.5-6.0P6/rcf/pcf/CER4.5-6.0P6_PCF_$INSTANCE_0P6

The submitted job can be monitored with the qstat command.

The most recently created sge_log file can be viewed to monitor progress of this job.  This will be the last file listed by the command:

ls -arlt $CERESHOME/inversion/sge_logs/CER4.5-6.0P6/CER4.5-6.0P6_$INSTANCE_0P6.o*

Output file generation test:

The script, list_4.5-6.0P6.pl, will list the files that were created during execution of the PGE:

$CERESHOME/inversion/CER4.5-6.0P6/rcf/list_4.5-6.0P6.pl $INSTANCE_0P6

Note:	If any file that should have been created is missing, then a message is written to the screen naming which file could not be found.

#### Exit Codes

All CER4.5-6.0P6 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.  This test should complete with an exit code of 0 for each of the two executables.

#### Test Summary

Test Summary:

Total Run Time:	1:34 minutes

Memory:	300 K

Required Disk Space:	0.1 Megabytes

### Evaluation Procedures

When running the production script, run_4.5-6.0P6.pl, the system message, ’No match’, may be written to the screen.  This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

Remove input files:

rm $InputArchive/SSFB/Terra-FM1-MODIS_Beta2-Ed4/2004/07/CER_SSFB_Terra-FM1-MODIS_Beta2-Ed4_400401.200407*12

Restore original contents of input file directory and remove temporary folder:

mv $InputArchive/SSFB/Terra-FM1-MODIS_Beta2-Ed4/2004/07/TEMP_MV_FOR_CM_TEST/* $InputArchive/SSFB/Terra-FM1-MODIS_Beta2-Ed4/2004/07/

rmdir $InputArchive/SSFB/Terra-FM1-MODIS_Beta2-Ed4/2004/07/TEMP_MV_FOR_CM_TEST/

### Log and Status File Results and Metadata Evaluation

The Error and Status Log File, CER4.5-6.0P6_LogReport_$INSTANCE_0P6, is located in directory $CERESHOME/inversion/runlogs after CER4.5-6.0P6 has been executed.  Metadata files, which end in extension '.met', are located in the same directories as their corresponding output files after CER4.5-6.0P6 has been executed.

Compare the information contained in the log file with the expected contents of the Log Report file found in directory $CERESHOME/inversion/data_exp/CER4.5-6.0P6 and compare the metadata files with the expected contents of the files with the same names found in directory $CERESHOME/inversion/data_exp/CER4.5-6.0P6, using the following diff_4.5-6.0P6.pl script:

cd $CERESHOME/inversion/CER4.5-6.0P6/rcf

$CERESHOME/inversion/CER4.5-6.0P6/rcf/diff_4.5-6.0P6.pl $INSTANCE_0P6

The only differences between the files should be the production times and differences in the directory paths where the tests were run.

#### Execution of Comparison Software for the Main Processor

The evaluation software for the Subsystem Pre Processor will perform a single test.  This test will compare the parameters of the sibiMap to the values in comparison files provided with the software delivery.

- To compare the sibiMap files, type the following command:

diff $CERESHOME/inversion/data/sibiMap/Terra-MODIS_Edition4/2004/07/CER_sibiMap_Terra-MODIS_Edition4_000000.200407 $CERESHOME/inversion/data_exp/CER4.5-6.0P6/

### Solutions to Possible Problems

- All output files are opened with Status = NEW in the CER4.5-6.0P6 software.  These files must be removed before rerunning these test procedures.  A script which removes PGE created files, cleanup_4.5-6.0P6.pl, is located in directory $CERESHOME/inversion/CER4.5-6.0P6/rcf.  To use the clean-up script:

cd $CERESHOME/inversion/CER4.5-6.0P6/rcf

$CERESHOME/inversion/CER4.5-6.0P6/rcf/cleanup_4.5-6.0P6.pl 200407

Use the latest version of CERESlib.

Ignore the warnings received during compilation.

### Stand Alone Test Procedures for Terra, Environment variable REPROCESS=’no’

#### Environment setup and file preparation

cd $CERESHOME/inversion/CER4.5-6.0P6/rcf

setenv YEAR 2016

setenv MONTH 06

setenv INSTANCE_0P6 Terra-MODIS_Edition1-CV_400400.201606

source $CERESHOME/inversion/CER4.5-6.0P6/rcf/inversion-terra-env1.csh

Copy any existing input files to a temporary directory:

mkdir $InputArchiveInt/SSF_Int/Terra-FM1-MODIS_Edition1-CV/2016/06/TEMP_MV_FOR_CM_TEST

mv $InputArchiveInt/SSF_Int/Terra-FM1-MODIS_Edition1-CV/2016/06/CER* $InputArchiveInt/SSF_Int/Terra-FM1-MODIS_Edition1-CV/2016/06/TEMP_MV_FOR_CM_TEST/

Copy the input files to appropriate locations:

cp $CERESHOME/inversion/data/input/CER4.5-6.0P6/CER_SSFI_Terra-FM1-MODIS_Edition1-CV_400400.201606*12 $InputArchiveInt/SSF_Int/Terra-FM1-MODIS_Edition1-CV/2016/06/

#### Execution

Execute the production script by typing the script name, CER4.5-6.0P6-SGE_Driver.pl, followed by the date and hour options and the cleanup option.

cd $CERESHOME/inversion/CER4.5-6.0P6/rcf

$CERESHOME/inversion/CER4.5-6.0P6/rcf/CER4.5-6.0P6-SGE_Driver.pl -date 201606 -clean

The following file will be generated:

$CERESHOME/inversion/CER4.5-6.0P6/rcf/pcf/CER4.5-6.0P6_PCF_$INSTANCE_0P6

The submitted job can be monitored with the qstat command.

The most recently created sge_log file can be viewed to monitor progress of this job.  This will be the last file listed by the command:

ls -arlt $CERESHOME/inversion/sge_logs/CER4.5-6.0P6/CER4.5-6.0P6_$INSTANCE_0P6.o*

Output file generation test:

The script, list_4.5-6.0P6.pl, will list the files that were created during execution of the PGE:

$CERESHOME/inversion/CER4.5-6.0P6/rcf/list_4.5-6.0P6.pl $INSTANCE_0P6

Note:	If any file that should have been created is missing, then a message is written to the screen naming which file could not be found.

#### Exit Codes

All CER4.5-6.0P6 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.  This test should complete with an exit code of 0 for each of the two executables.

#### Test Summary

Test Summary:

Total Run Time:	1:34 minutes

Memory:	300 K

Required Disk Space:	0.1 Megabytes

### Evaluation Procedures

When running the production script, run_4.5-6.0P6.pl, the system message, ’No match’, may be written to the screen.  This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

Remove input files:

rm $InputArchiveInt/SSF_Int/Terra-FM1-MODIS_Edition1-CV/2016/06/CER_SSFI_Terra-FM1-MODIS_Edition1-CV_400400.201606*12

Restore original contents of input file directory and remove temporary folder:

mv $InputArchiveInt/SSF_Int/Terra-FM1-MODIS_Edition1-CV/2016/06/TEMP_MV_FOR_CM_TEST/* $InputArchiveInt/SSF_Int/Terra-FM1-MODIS_Edition1-CV/2016/06/

rmdir $InputArchiveInt/SSF_Int/Terra-FM1-MODIS_Edition1-CV/2016/06/TEMP_MV_FOR_CM_TEST/

### Log and Status File Results and Metadata Evaluation

The Error and Status Log File, CER4.5-6.0P6_LogReport_$INSTANCE_0P6, is located in directory $CERESHOME/inversion/runlogs after CER4.5-6.0P6 has been executed.  Metadata files, which end in extension '.met', are located in the same directories as their corresponding output files after CER4.5-6.0P6 has been executed.

Compare the information contained in the log file with the expected contents of the Log Report file found in directory $CERESHOME/inversion/data_exp/CER4.5-6.0P6 and compare the metadata files with the expected contents of the files with the same names found in directory $CERESHOME/inversion/data_exp/CER4.5-6.0P6, using the following diff_4.5-6.0P6.pl script:

cd $CERESHOME/inversion/CER4.5-6.0P6/rcf

$CERESHOME/inversion/CER4.5-6.0P6/rcf/diff_4.5-6.0P6.pl $INSTANCE_0P6

The only differences between the files should be the production times and differences in the directory paths where the tests were run.

#### Execution of Comparison Software for the Main Processor

The evaluation software for the Subsystem Pre Processor will perform a single test.  This test will compare the parameters of the sibiMap to the values in comparison files provided with the software delivery.

- To compare the sibiMap files, type the following command:

diff $CERESHOME/inversion/data/sibiMap/Terra-MODIS_Edition1-CV/2016/06/CER_sibiMap_Terra-MODIS_Edition1-CV_400400.201606 $CERESHOME/inversion/data_exp/CER4.5-6.0P6/

### Solutions to Possible Problems

- All output files are opened with Status = NEW in the CER4.5-6.0P6 software.  These files must be removed before rerunning these test procedures.  A script which removes PGE created files, cleanup_4.5-6.0P6.pl, is located in directory $CERESHOME/inversion/CER4.5-6.0P6/rcf.  To use the clean-up script:

cd $CERESHOME/inversion/CER4.5-6.0P6/rcf

$CERESHOME/inversion/CER4.5-6.0P6/rcf/cleanup_4.5-6.0P6.pl 201606

Use the latest version of CERESlib.

Ignore the warnings received during compilation.

### Stand Alone Test Procedures for Aqua, Environment variable REPROCESS=’yes’

#### Environment setup and file preparation

cd $CERESHOME/inversion/CER4.5-6.0P6/rcf

setenv YEAR 2004

setenv MONTH 07

setenv INSTANCE_0P6 Aqua-MODIS_Edition4_000000.200407

source $CERESHOME/inversion/CER4.5-6.0P6/rcf/inversion-aqua-env1.csh

Copy any existing input files to a temporary directory:

mkdir $InputArchive/SSFB/Aqua-FM3-MODIS_Beta2-Ed4/2004/07/TEMP_MV_FOR_CM_TEST

mv $InputArchive/SSFB/Aqua-FM3-MODIS_Beta2-Ed4/2004/07/CER* $InputArchive/SSFB/Aqua-FM3-MODIS_Beta2-Ed4/2004/07/TEMP_MV_FOR_CM_TEST/

Copy the input files to appropriate locations:

cp $CERESHOME/inversion/data/input/CER4.5-6.0P6/CER_SSFB_Aqua-FM3-MODIS_Beta2-Ed4_400401.200407*12 $InputArchive/SSFB/Aqua-FM3-MODIS_Beta2-Ed4/2004/07/

#### Execution

Execute the production script by typing the script name, CER4.5-6.0P6-SGE_Driver.pl, followed by the date and hour options and the cleanup option.

cd $CERESHOME/inversion/CER4.5-6.0P6/rcf

$CERESHOME/inversion/CER4.5-6.0P6/rcf/CER4.5-6.0P6-SGE_Driver.pl -date 200407 -clean

The following file will be generated:

$CERESHOME/inversion/CER4.5-6.0P6/rcf/pcf/CER4.5-6.0P6_PCF_$INSTANCE_0P6

The submitted job can be monitored with the qstat command.

The most recently created sge_log file can be viewed to monitor progress of this job.  This will be the last file listed by the command:

ls -arlt $CERESHOME/inversion/sge_logs/CER4.5-6.0P6/CER4.5-6.0P6_$INSTANCE_0P6.o*

Output file generation test:

The script, list_4.5-6.0P6.pl, will list the files that were created during execution of the PGE:

$CERESHOME/inversion/CER4.5-6.0P6/rcf/list_4.5-6.0P6.pl $INSTANCE_0P6

Note:	If any file that should have been created is missing, then a message is written to the screen naming which file could not be found.

#### Exit Codes

All CER4.5-6.0P6 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.  This test should complete with an exit code of 0 for each of the two executables.

#### Test Summary

Test Summary:

Total Run Time:	1:34 minutes

Memory:	300 K

Required Disk Space:	0.1 Megabytes

### Evaluation Procedures

When running the production script, run_4.5-6.0P6.pl, the system message, ’No match’, may be written to the screen.  This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

Remove input files:

rm $InputArchive/SSFB/Aqua-FM3-MODIS_Beta2-Ed4/2004/07/CER_SSFB_Aqua-FM3-MODIS_Beta2-Ed4_400401.200407*12

Restore original contents of input file directory and remove temporary folder:

mv $InputArchive/SSFB/Aqua-FM3-MODIS_Beta2-Ed4/2004/07/TEMP_MV_FOR_CM_TEST/* $InputArchive/SSFB/Aqua-FM3-MODIS_Beta2-Ed4/2004/07/

rmdir $InputArchive/SSFB/Aqua-FM3-MODIS_Beta2-Ed4/2004/07/TEMP_MV_FOR_CM_TEST

### Log and Status File Results and Metadata Evaluation

The Error and Status Log File, CER4.5-6.0P6_LogReport_$INSTANCE_0P6, is located in directory $CERESHOME/inversion/runlogs after CER4.5-6.0P6 has been executed.  Metadata files, which end in extension '.met', are located in the same directories as their corresponding output files after CER4.5-6.0P6 has been executed.

Compare the information contained in the log file with the expected contents of the Log Report file found in directory $CERESHOME/inversion/data_exp/CER4.5-6.0P6 and compare the metadata files with the expected contents of the files with the same names found in directory $CERESHOME/inversion/data_exp/CER4.5-6.0P6, using the following diff_4.5-6.0P6.pl script:

cd $CERESHOME/inversion/CER4.5-6.0P6/rcf

$CERESHOME/inversion/CER4.5-6.0P6/rcf/diff_4.5-6.0P6.pl $INSTANCE_0P6

The only differences between the files should be the production times and differences in the directory paths where the tests were run.

#### Execution of Comparison Software for the Main Processor

The evaluation software for the Subsystem Pre Processor will perform a single test.  This test will compare the parameters of the sibiMap to the values in comparison files provided with the software delivery.

- To compare the sibiMap files, type the following command:

diff $CERESHOME/inversion/data/sibiMap/Aqua-MODIS_Edition4/2004/07/CER_sibiMap_Aqua-MODIS_Edition4_000000.200407 $CERESHOME/inversion/data_exp/CER4.5-6.0P6/

### Solutions to Possible Problems

- All output files are opened with Status = NEW in the CER4.5-6.0P6 software.  These files must be removed before rerunning these test procedures.  A script which removes PGE created files, cleanup_4.5-6.0P6.pl, is located in directory $CERESHOME/inversion/CER4.5-6.0P6/rcf.  To use the clean-up script:

cd $CERESHOME/inversion/CER4.5-6.0P6/rcf

$CERESHOME/inversion/CER4.5-6.0P6/rcf/cleanup_4.5-6.0P6.pl 200407

Use the latest version of CERESlib.

Ignore the warnings received during compilation.

### Stand Alone Test Procedures for Aqua, Environment variable REPROCESS=’no’

#### Environment setup and file preparation

cd $CERESHOME/inversion/CER4.5-6.0P6/rcf

setenv YEAR 2012

setenv MONTH 02

setenv INSTANCE_0P6 Aqua-MODIS_Edition4_000000.201202

source $CERESHOME/inversion/CER4.5-6.0P6/rcf/inversion-aqua-env2.csh

Copy any existing input files to a temporary directory:

mkdir $InputArchiveInt/SSF_Int/Aqua-FM3-MODIS_Ed4Test/2012/02/TEMP_MV_FOR_CM_TEST

mv $InputArchiveInt/SSF_Int/Aqua-FM3-MODIS_Ed4Test/2012/02/CER* $InputArchiveInt/SSF_Int/Aqua-FM3-MODIS_Ed4Test/2012/02/TEMP_MV_FOR_CM_TEST/

Copy the input files to appropriate locations:

cp $CERESHOME/inversion/data/input/CER4.5-6.0P6/CER_SSFI_Aqua-FM3-MODIS_Ed4Test_000000.201202*12 $InputArchiveInt/SSF_Int/Aqua-FM3-MODIS_Ed4Test/2012/02/

#### Execution

Execute the production script by typing the script name, CER4.5-6.0P6-SGE_Driver.pl, followed by the date and hour options and the cleanup option.

cd $CERESHOME/inversion/CER4.5-6.0P6/rcf

$CERESHOME/inversion/CER4.5-6.0P6/rcf/CER4.5-6.0P6-SGE_Driver.pl -date 201202 -clean

The following file will be generated:

$CERESHOME/inversion/CER4.5-6.0P6/rcf/pcf/CER4.5-6.0P6_PCF_$INSTANCE_0P6

The submitted job can be monitored with the qstat command.

The most recently created sge_log file can be viewed to monitor progress of this job.  This will be the last file listed by the command:

ls -arlt $CERESHOME/inversion/sge_logs/CER4.5-6.0P6/CER4.5-6.0P6_$INSTANCE_0P6.o*

Output file generation test:

The script, list_4.5-6.0P6.pl, will list the files that were created during execution of the PGE:

$CERESHOME/inversion/CER4.5-6.0P6/rcf/list_4.5-6.0P6.pl $INSTANCE_0P6

Note:	If any file that should have been created is missing, then a message is written to the screen naming which file could not be found.

#### Exit Codes

All CER4.5-6.0P6 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.  This test should complete with an exit code of 0 for each of the two executables.

#### Test Summary

Test Summary:

Total Run Time:	1:34 minutes

Memory:	300 K

Required Disk Space:	0.1 Megabytes

### Evaluation Procedures

When running the production script, run_4.5-6.0P6.pl, the system message, ’No match’, may be written to the screen.  This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

Remove input files:

rm $InputArchiveInt/SSF_Int/Aqua-FM3-MODIS_Ed4Test/2012/02/CER_SSFI_Aqua-FM3-MODIS_Ed4Test_000000.201202*12

Restore original contents of input file directory and remove temporary folder:

mv $InputArchiveInt/SSF_Int/Aqua-FM3-MODIS_Ed4Test/2012/02/TEMP_MV_FOR_CM_TEST/* $InputArchiveInt/SSF_Int/Aqua-FM3-MODIS_Ed4Test/2012/02/

rmdir $InputArchiveInt/SSF_Int/Aqua-FM3-MODIS_Ed4Test/2012/02/TEMP_MV_FOR_CM_TEST

### Log and Status File Results and Metadata Evaluation

The Error and Status Log File, CER4.5-6.0P6_LogReport_$INSTANCE_0P6, is located in directory $CERESHOME/inversion/runlogs after CER4.5-6.0P6 has been executed.  Metadata files, which end in extension '.met', are located in the same directories as their corresponding output files after CER4.5-6.0P6 has been executed.

Compare the information contained in the log file with the expected contents of the Log Report file found in directory $CERESHOME/inversion/data_exp/CER4.5-6.0P6 and compare the metadata files with the expected contents of the files with the same names found in directory $CERESHOME/inversion/data_exp/CER4.5-6.0P6, using the following diff_4.5-6.0P6.pl script:

cd $CERESHOME/inversion/CER4.5-6.0P6/rcf

$CERESHOME/inversion/CER4.5-6.0P6/rcf/diff_4.5-6.0P6.pl $INSTANCE_0P6

The only differences between the files should be the production times and differences in the directory paths where the tests were run.

#### Execution of Comparison Software for the Main Processor

The evaluation software for the Subsystem Pre Processor will perform a single test.  This test will compare the parameters of the sibiMap to the values in comparison files provided with the software delivery.

- To compare the sibiMap files, type the following command:

diff $CERESHOME/inversion/data/sibiMap/Aqua-MODIS_Edition4/2012/02/CER_sibiMap_Aqua-MODIS_Edition4_000000.201202 $CERESHOME/inversion/data_exp/CER4.5-6.0P6/

### Solutions to Possible Problems

- All output files are opened with Status = NEW in the CER4.5-6.0P6 software.  These files must be removed before rerunning these test procedures.  A script which removes PGE created files, cleanup_4.5-6.0P6.pl, is located in directory $CERESHOME/inversion/CER4.5-6.0P6/rcf.  To use the clean-up script:

cd $CERESHOME/inversion/CER4.5-6.0P6/rcf

$CERESHOME/inversion/CER4.5-6.0P6/rcf/cleanup_4.5-6.0P6.pl 201202

Use the latest version of CERESlib.

Ignore the warnings received during compilation.

### Stand Alone Test Procedures for NPP, Environment variable REPROCESS=’yes’

#### Environment setup and file preparation

cd $CERESHOME/inversion/CER4.5-6.0P6/rcf

setenv YEAR 2012

setenv MONTH 02

setenv INSTANCE_0P6 NPP-VIIRS_Edition4_000000.201202

source $CERESHOME/inversion/CER4.5-6.0P6/rcf/inversion-npp-env1.csh

Copy any existing input files to a temporary directory:

mkdir $InputArchive/SSFB/NPP-FM5-VIIRS_SSIT/2012/02/TEMP_MV_FOR_CM_TEST

mv $InputArchive/SSFB/NPP-FM5-VIIRS_SSIT/2012/02/CER* $InputArchive/SSFB/NPP-FM5-VIIRS_SSIT/2012/02/TEMP_MV_FOR_CM_TEST/

Copy the input files to appropriate locations:

cp $CERESHOME/inversion/data/input/CER4.5-6.0P6/CER_SSFB_NPP-FM5-VIIRS_SSIT_000000.201202*12 $InputArchive/SSFB/NPP-FM5-VIIRS_SSIT/2012/02/

#### Execution

Execute the production script by typing the script name, CER4.5-6.0P6-SGE_Driver.pl, followed by the date and hour options and the cleanup option.

cd $CERESHOME/inversion/CER4.5-6.0P6/rcf

$CERESHOME/inversion/CER4.5-6.0P6/rcf/CER4.5-6.0P6-SGE_Driver.pl -date 201202 -clean

The following file will be generated:

$CERESHOME/inversion/CER4.5-6.0P6/rcf/pcf/CER4.5-6.0P6_PCF_$INSTANCE_0P6

The submitted job can be monitored with the qstat command.

The most recently created sge_log file can be viewed to monitor progress of this job.  This will be the last file listed by the command:

ls -arlt $CERESHOME/inversion/sge_logs/CER4.5-6.0P6/CER4.5-6.0P6_$INSTANCE_0P6.o*

Output file generation test:

The script, list_4.5-6.0P6.pl, will list the files that were created during execution of the PGE:

$CERESHOME/inversion/CER4.5-6.0P6/rcf/list_4.5-6.0P6.pl $INSTANCE_0P6

Note:	If any file that should have been created is missing, then a message is written to the screen naming which file could not be found.

#### Exit Codes

All CER4.5-6.0P6 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.  This test should complete with an exit code of 0 for each of the two executables.

#### Test Summary

Test Summary:

Total Run Time:	1:34 minutes

Memory:	300 K

Required Disk Space:	0.1 Megabytes

### Evaluation Procedures

When running the production script, run_4.5-6.0P6.pl, the system message, ’No match’, may be written to the screen.  This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

Remove input files:

rm $InputArchive/SSFB/NPP-FM5-VIIRS_SSIT/2012/02/CER_SSFB_NPP-FM5-VIIRS_SSIT_000000.201202*12

Restore original contents of input file directory and remove temporary folder:

mv $InputArchive/SSFB/NPP-FM5-VIIRS_SSIT/2012/02/TEMP_MV_FOR_CM_TEST/* $InputArchive/SSFB/NPP-FM5-VIIRS_SSIT/2012/02/

rmdir $InputArchive/SSFB/NPP-FM5-VIIRS_SSIT/2012/02/TEMP_MV_FOR_CM_TEST

### Log and Status File Results and Metadata Evaluation

The Error and Status Log File, CER4.5-6.0P6_LogReport_$INSTANCE_0P6, is located in directory $CERESHOME/inversion/runlogs after CER4.5-6.0P6 has been executed.  Metadata files, which end in extension '.met', are located in the same directories as their corresponding output files after CER4.5-6.0P6 has been executed.

Compare the information contained in the log file with the expected contents of the Log Report file found in directory $CERESHOME/inversion/data_exp/CER4.5-6.0P6 and compare the metadata files with the expected contents of the files with the same names found in directory $CERESHOME/inversion/data_exp/CER4.5-6.0P6, using the following diff_4.5-6.0P6.pl script:

cd $CERESHOME/inversion/CER4.5-6.0P6/rcf

$CERESHOME/inversion/CER4.5-6.0P6/rcf/diff_4.5-6.0P6.pl $INSTANCE_0P6

The only differences between the files should be the production times and differences in the directory paths where the tests were run.

#### Execution of Comparison Software for the Main Processor

The evaluation software for the Subsystem Pre Processor will perform a single test.  This test will compare the parameters of the sibiMap to the values in comparison files provided with the software delivery.

- To compare the sibiMap files, type the following command:

diff $CERESHOME/inversion/data/sibiMap/NPP-VIIRS_Edition4/2012/02/CER_sibiMap_NPP-VIIRS_Edition4_000000.201202 $CERESHOME/inversion/data_exp/CER4.5-6.0P6/

### Solutions to Possible Problems

- All output files are opened with Status = NEW in the CER4.5-6.0P6 software.  These files must be removed before rerunning these test procedures.  A script which removes PGE created files, cleanup_4.5-6.0P6.pl, is located in directory $CERESHOME/inversion/CER4.5-6.0P6/rcf.  To use the clean-up script:

cd $CERESHOME/inversion/CER4.5-6.0P6/rcf

$CERESHOME/inversion/CER4.5-6.0P6/rcf/cleanup_4.5-6.0P6.pl 201202

Use the latest version of CERESlib.

Ignore the warnings received during compilation.

### Stand Alone Test Procedures for NPP, Environment variable REPROCESS=’no’

#### Environment setup and file preparation

cd $CERESHOME/inversion/CER4.5-6.0P6/rcf

setenv YEAR 2012

setenv MONTH 02

setenv INSTANCE_0P6 NPP-VIIRS_Edition4_999999.201202

source $CERESHOME/inversion/CER4.5-6.0P6/rcf/inversion-npp-env2.csh

Copy any existing input files to a temporary directory:

mkdir $InputArchiveInt/SSF_Int/NPP-FM5-VIIRS_SSIT/2012/02/TEMP_MV_FOR_CM_TEST

mv $InputArchiveInt/SSF_Int/NPP-FM5-VIIRS_SSIT/2012/02/CER* $InputArchiveInt/SSF_Int/NPP-FM5-VIIRS_SSIT/2012/02/TEMP_MV_FOR_CM_TEST/

Copy the input files to appropriate locations:

cp $CERESHOME/inversion/data/input/CER4.5-6.0P6/CER_SSFI_NPP-FM5-VIIRS_SSIT_000000.201202*12 $InputArchiveInt/SSF_Int/NPP-FM5-VIIRS_SSIT/2012/02/

#### Execution

Execute the production script by typing the script name, CER4.5-6.0P6-SGE_Driver.pl, followed by the date and hour options and the cleanup option.

cd $CERESHOME/inversion/CER4.5-6.0P6/rcf

$CERESHOME/inversion/CER4.5-6.0P6/rcf/CER4.5-6.0P6-SGE_Driver.pl -date 201202 -clean

The following file will be generated:

$CERESHOME/inversion/CER4.5-6.0P6/rcf/pcf/CER4.5-6.0P6_PCF_$INSTANCE_0P6

The submitted job can be monitored with the qstat command.

The most recently created sge_log file can be viewed to monitor progress of this job.  This will be the last file listed by the command:

ls -arlt $CERESHOME/inversion/sge_logs/CER4.5-6.0P6/CER4.5-6.0P6_$INSTANCE_0P6.o*

Output file generation test:

The script, list_4.5-6.0P6.pl, will list the files that were created during execution of the PGE:

$CERESHOME/inversion/CER4.5-6.0P6/rcf/list_4.5-6.0P6.pl $INSTANCE_0P6

Note:	If any file that should have been created is missing, then a message is written to the screen naming which file could not be found.

#### Exit Codes

All CER4.5-6.0P6 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.  This test should complete with an exit code of 0 for each of the two executables.

#### Test Summary

Test Summary:

Total Run Time:	1:34 minutes

Memory:	300 K

Required Disk Space:	0.1 Megabytes

### Evaluation Procedures

When running the production script, run_4.5-6.0P6.pl, the system message, ’No match’, may be written to the screen.  This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

Remove input files:

rm $InputArchiveInt/SSF_Int/NPP-FM5-VIIRS_SSIT/2012/02/CER_SSFI_NPP-FM5-VIIRS_SSIT_000000.201202*12

Restore original contents of input file directory and remove temporary folder:

mv $InputArchiveInt/SSF_Int/NPP-FM5-VIIRS_SSIT/2012/02/TEMP_MV_FOR_CM_TEST/* $InputArchiveInt/SSF_Int/NPP-FM5-VIIRS_SSIT/2012/02/

rmdir $InputArchiveInt/SSF_Int/NPP-FM5-VIIRS_SSIT/2012/02/TEMP_MV_FOR_CM_TEST

### Log and Status File Results and Metadata Evaluation

The Error and Status Log File, CER4.5-6.0P6_LogReport_$INSTANCE_0P6, is located in directory $CERESHOME/inversion/runlogs after CER4.5-6.0P6 has been executed.  Metadata files, which end in extension '.met', are located in the same directories as their corresponding output files after CER4.5-6.0P6 has been executed.

Compare the information contained in the log file with the expected contents of the Log Report file found in directory $CERESHOME/inversion/data_exp/CER4.5-6.0P6 and compare the metadata files with the expected contents of the files with the same names found in directory $CERESHOME/inversion/data_exp/CER4.5-6.0P6, using the following diff_4.5-6.0P6.pl script:

cd $CERESHOME/inversion/CER4.5-6.0P6/rcf

$CERESHOME/inversion/CER4.5-6.0P6/rcf/diff_4.5-6.0P6.pl $INSTANCE_0P6

The only differences between the files should be the production times and differences in the directory paths where the tests were run.

#### Execution of Comparison Software for the Main Processor

The evaluation software for the Subsystem Pre Processor will perform a single test.  This test will compare the parameters of the sibiMap to the values in comparison files provided with the software delivery.

- To compare the sibiMap files, type the following command:

diff $CERESHOME/inversion/data/sibiMap/NPP-VIIRS_Edition4/2012/02/CER_sibiMap_NPP-VIIRS_Edition4_999999.201202 $CERESHOME/inversion/data_exp/CER4.5-6.0P6/

### Solutions to Possible Problems

- All output files are opened with Status = NEW in the CER4.5-6.0P6 software.  These files must be removed before rerunning these test procedures.  A script which removes PGE created files, cleanup_4.5-6.0P6.pl, is located in directory $CERESHOME/inversion/CER4.5-6.0P6/rcf.  To use the clean-up script:

cd $CERESHOME/inversion/CER4.5-6.0P6/rcf

$CERESHOME/inversion/CER4.5-6.0P6/rcf/cleanup_4.5-6.0P6.pl 201202

Use the latest version of CERESlib.

Ignore the warnings received during compilation.

## CER4_5-6.1P6 Main and Post Processors for Terra and Aqua Edition4 Processing

### Stand Alone Test Procedures for FM1, Environment variables:  REPROCESS = ‘NO’, READ_IES = ‘NO’ and PROD = ‘no’

#### Environment setup and file preparation

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

setenv YEAR 2008

setenv MONTH 07

setenv DAY 15

setenv HOUR 15

setenv DATE_1P6 $YEAR$MONTH$DAY$HOUR

setenv INSTANCE_1P6 Terra-FM1-MODIS_Ed4Test_000000.$DATE_1P6

setenv SCC_1P6 Terra-FM1_Edition3_300300.20080715

source $CERESHOME/inversion/CER4.5-6.1P6/rcf/inversion-FM1-test1-env.csh

Copy the input files to appropriate locations:

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_MOA_CERES_DAO-G5-CERES_020032.2008071512 $InputArchive/MOA/CERES_DAO-G5-CERES/2008/07/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_MOA_CERES_DAO-G5-CERES_020032.2008071518 $InputArchive/MOA/CERES_DAO-G5-CERES/2008/07/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SSFI_Terra-FM1-MODIS_Ed4Test_000000.2008071515 $InputArchiveInt/SSF_Int/Terra-FM1-MODIS_Ed4Test/2008/07/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SSFAI_Terra-FM1-MODIS_Ed4Test_000000.2008071515 $InputArchiveInt/SSF_Int/Terra-FM1-MODIS_Ed4Test/2008/07/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SSFAI_Terra-FM1-MODIS_Ed4Test_000000.2008071515.met $InputArchiveInt/SSF_Int/Terra-FM1-MODIS_Ed4Test/2008/07/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_FQCI_Terra-FM1-MODIS_Ed4Test_000000.2008071515 $InputArchiveInt/FQC/Terra-FM1-MODIS_Ed4Test/2008/07/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SCCD_$SCC_1P6 $InputArchive/SCCD/Terra-FM1_Edition3/2008/07/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SCCN_$SCC_1P6 $InputArchive/SCCN/Terra-FM1_Edition3/2008/07/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_MATCH-daily_Terra-Aqua-MODIS_Edition4_400400.20080715.nc $CERESHOME/inversion/data/MATCH-daily/Terra-Aqua-MODIS_Edition4/2008/07/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/sorce_tsi_v15.txt.20140331 $CERESHOME/inversion/data/SORCE/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_sibiMap_Terra-MODIS_Edition4_400400.200807 $CERESHOME/inversion/data/sibiMap/Terra-MODIS_Edition4/2008/07/

#### Execution

Execute the production script by typing the script name, CER4.5-6.1P6-SGE_Driver.pl, followed by the date and hour options and the cleanup option.

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

$CERESHOME/inversion/CER4.5-6.1P6/rcf/CER4.5-6.1P6-SGE_Driver.pl -date 20080715 -hour 15 -clean

The following file will be generated:

$CERESHOME/inversion/CER4.5-6.1P6/rcf/pcf/CER4.5-6.1P6_PCF_$INSTANCE_1P6

The submitted job can be monitored with the qstat command.

The most recently created sge_log file can be viewed to monitor progress of this job.  This will be the last file listed by the command:

ls -arlt $CERESHOME/inversion/sge_logs/CER4.5-6.1P6/CER4.5-6.1P6_$INSTANCE_1P6.o*

Output file generation test:

The script, list_4.5-6.1P6.pl, will list the files that were created during execution of the PGE:

$CERESHOME/inversion/CER4.5-6.1P6/rcf/list_4.5-6.1P6.pl $INSTANCE_1P6

Note:	If any file that should have been created is missing, then a message is written to the screen naming which file could not be found.

#### Exit Codes

All CER4.5-6.1P6 software terminates using the CERES defined EXIT CODES.  Successful completion is indicated by an exit code of 0.  This test should complete with an exit code of 0 for each of the executables.

#### Test Summary

Test Summary:

Total Run Time:	6:24 minutes

Memory:	5.7 G

Required Disk Space:	232 Megabytes

### Evaluation Procedures

When running the production script, run_4.5-6.1P6.pl, the system message, ’No match’, may be written to the screen.  This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

Remove input data:

rm $InputArchiveInt/SSF_Int/Terra-FM1-MODIS_Ed4Test/2008/07/CER_SSFI_$INSTANCE_1P6

rm $InputArchiveInt/SSF_Int/Terra-FM1-MODIS_Ed4Test/2008/07/CER_SSFAI_$INSTANCE_1P6

rm $InputArchiveInt/SSF_Int/Terra-FM1-MODIS_Ed4Test/2008/07/CER_SSFAI_$INSTANCE_1P6.met

rm $InputArchiveInt/FQC/Terra-FM1-MODIS_Ed4Test/2008/07/CER_FQCI_$INSTANCE_1P6

rm $InputArchive/SCCD/Terra-FM1_Edition3/2008/07/CER_SCCD_$SCC_1P6

rm $InputArchive/SCCN/Terra-FM1_Edition3/2008/07/CER_SCCN_$SCC_1P6

rm $InputArchive/MOA/CERES_DAO-G5-CERES/2008/07/CER_MOA_CERES_DAO-G5-CERES_020032.2008071512

rm $InputArchive/MOA/CERES_DAO-G5-CERES/2008/07/CER_MOA_CERES_DAO-G5-CERES_020032.2008071518

rm $CERESHOME/inversion/data/MATCH-daily/Terra-Aqua-MODIS_Edition4/2008/07/CER_MATCH-daily_Terra-Aqua-MODIS_Edition4_400400.20080715.nc

rm $CERESHOME/inversion/data/SORCE/sorce_tsi_v15.txt.20140331

rm $CERESHOME/inversion/data/sibiMap/Terra-MODIS_Edition4/2008/07/CER_sibiMap_Terra-MODIS_Edition4_400400.200807

#### Log and Status File Results and Metadata Evaluation

The Error and Status Log File, CER4.5-6.1P6_LogReport_$INSTANCE_1P6, is located in directory $CERESHOME/inversion/runlogs after CER4.5-6.1P6 has been executed.  Metadata files, which end in extension '.met', are located in the same directories as their corresponding output files after CER4.5-6.1P6 has been executed

Compare the information contained in the log file with the expected contents of the Log Report file found in directory $CERESHOME/inversion/data_exp/CER4.5-6.1P6 and compare the metadata files with the expected contents of the files with the same names found in directory

$CERESHOME/inversion/data_exp/CER4.5-6.1P6, using the following diff_4.5-6.1P6.pl script:

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

$CERESHOME/inversion/CER4.5-6.1P6/rcf/diff_4.5-6.1P6.pl $INSTANCE_1P6

The only differences between the files should be the production times and differences in the directory paths where the tests were run.

#### Execution of Comparison Software for the Main Processor

The evaluation software for the Subsystem Main Processor will perform a single test.  This test will compare all of the parameters on the binary SSF and the binary SSFA (if it exists) to the values in comparison files provided with the software delivery.

- The executable for the comparison software is not provided in the tar file.  It was created when all the software’s code was compiled.

To execute the comparison software for the binary SSF and binary SSFA, type the following commands:

cd $CERESHOME/inversion/test_suites/bin

run_compare_1p6 $INSTANCE_1P6

Two files will be created:

$CERESHOME/inversion/test_suites/results/CmpReport_$DATE_1P6

$CERESHOME/inversion/test_suites/results/CmpReportSSFA_$DATE_1P6

#### Evaluation of Comparison Software Output

This section provides the procedure for evaluating the output from the CER4.5-6.1P6 comparison software.

Examine the comparison reports files by typing:

cat $CERESHOME/inversion/test_suites/results/CmpReport_$DATE_1P6

cat $CERESHOME/inversion/test_suites/results/CmpReportSSFA_$DATE_1P6

The final line of these files will report the status of the comparison between the generated data and the expected output.

#### Evaluation of SSF HDF Product

This section provides the procedure for evaluating the output from the SSF HDF product produced by the test software.  The comparison software was compiled when all software was compiled in a previous step.  Execute the program by typing the following lines:

hdiff $CERESHOME/inversion/data/SSF/Terra-FM1-MODIS_Ed4Test/2008/07/CER_SSF_$INSTANCE_1P6 $CERESHOME/inversion/data_exp/CER4.5-6.1P6/CER_SSF_$INSTANCE_1P6

The executable, hdiff, compares each Vdata and each SDS on the SSF HDF output file.

The only differences between the two HDF output files should be the dates on Vfields:  “SSF_DATE” on the “SSF_Header” Vdata and “CERPRODUCTIONDATETIME” on the “CERES_metadata” Vdata.  If CERESLIB has changed, the date may be different in the “LOCALVERSIONID” on the “CERES_metadata” Vdata.  Differences in the third to sixth decimal places for the data fields are acceptable.

### Solutions to Possible Problems

- All output files are opened with Status = NEW in the CER4.5-6.1P6 software.  These files must be removed before rerunning these test procedures.  A script which removes PGE created files, cleanup_4.5-6.1P6.pl, is located in directory $CERESHOME/inversion/CER4.5-6.1P6/rcf.  To use the clean-up script:

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

$CERESHOME/inversion/CER4.5-6.1P6/rcf/cleanup_4.5-6.1P6.pl $DATE_1P6

Use the latest version of CERESlib.

Ignore the warnings received during compilation.

### Stand Alone, command line, Test Procedures for FM1, Environment Variables REPROCESS = ‘YES’, READ_IES = ‘NO’ and PROD = ‘no’

#### Environment setup and file preparation

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

setenv YEAR 2008

setenv MONTH 07

setenv DAY 15

setenv HOUR 15

setenv DATE_1P6 $YEAR$MONTH$DAY$HOUR

setenv INSTANCE_1P6 Terra-FM1-MODIS_Ed4Test-reproc_000000.$DATE_1P6

setenv SCC_1P6 Terra-FM1_Edition3_300300.20080715

source $CERESHOME/inversion/CER4.5-6.1P6/rcf/inversion-FM1-test2-env.csh

Copy the input files to appropriate locations:

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_MOA_CERES_DAO-G5-CERES_020032.2008071512 $InputArchive/MOA/CERES_DAO-G5-CERES/2008/07/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_MOA_CERES_DAO-G5-CERES_020032.2008071518 $InputArchive/MOA/CERES_DAO-G5-CERES/2008/07/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SSFB_Terra-FM1-MODIS_Ed4Test_000000.2008071515 $InputArchive/SSFB/Terra-FM1-MODIS_Ed4Test/2008/07/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SSFA_Terra-FM1-MODIS_Ed4Test_000000.2008071515 $InputArchive/SSFA/Terra-FM1-MODIS_Ed4Test/2008/07/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SSFA_Terra-FM1-MODIS_Ed4Test_000000.2008071515.met $InputArchive/SSFA/Terra-FM1-MODIS_Ed4Test/2008/07/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_GQCI_Terra-FM1-MODIS_Ed4Test_000000.2008071515 $InputArchive/GQCI/Terra-FM1-MODIS_Ed4Test/2008/07/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SCCD_$SCC_1P6 $InputArchive/SCCD/Terra-FM1_Edition3/2008/07/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SCCN_$SCC_1P6 $InputArchive/SCCN/Terra-FM1_Edition3/2008/07/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_MATCH-daily_Terra-Aqua-MODIS_Edition4_400400.20080715.nc $CERESHOME/inversion/data/MATCH-daily/Terra-Aqua-MODIS_Edition4/2008/07/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/sorce_tsi_v15.txt.20140331 $CERESHOME/inversion/data/SORCE/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_sibiMap_Terra-MODIS_Edition4_400400.200807 $CERESHOME/inversion/data/sibiMap/Terra-MODIS_Edition4/2008/07/

#### Execution

Execute the production script by typing the script name, CER4.5-6.1P6-SGE_Driver.pl, followed by the date and hour options and the cleanup option.

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

$CERESHOME/inversion/CER4.5-6.1P6/rcf/CER4.5-6.1P6-SGE_Driver.pl -date 20080715 -hour 15 -clean

The following file will be generated:

$CERESHOME/inversion/CER4.5-6.1P6/rcf/pcf/CER4.5-6.1P6_PCF_$INSTANCE_1P6

The submitted job can be monitored with the qstat command.

The most recently created sge_log file can be viewed to monitor progress of this job.  This will be the last file listed by the command:

ls -arlt $CERESHOME/inversion/sge_logs/CER4.5-6.1P6/CER4.5-6.1P6_$INSTANCE_1P6.o*

Output file generation test:

The script, list_4.5-6.1P6.pl, will list the files that were created during execution of the PGE:

$CERESHOME/inversion/CER4.5-6.1P6/rcf/list_4.5-6.1P6.pl $INSTANCE_1P6

Note:	If any file that should have been created is missing, then a message is written to the screen naming which file could not be found.

#### Exit Codes

All CER4.5-6.1P6 software terminates using the CERES defined EXIT CODES.  Successful completion is indicated by an exit code of 0.  This test should complete with an exit code of 0 for each of the executables.

#### Test Summary

Test Summary:

Total Run Time:	6:24 minutes

Memory:	5.7 G

Required Disk Space:	232 Megabytes

### Evaluation Procedures

When running the production script, run_4.5-6.1P6.pl, the system message, ’No match’, may be written to the screen.  This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

Remove input data:

rm $InputArchive/SSFB/Terra-FM1-MODIS_Ed4Test/2008/07/CER_SSFB_Terra-FM1-MODIS_Ed4Test_000000.2008071515

rm $InputArchive/SSFA/Terra-FM1-MODIS_Ed4Test/2008/07/CER_SSFA_Terra-FM1-MODIS_Ed4Test_000000.2008071515

rm $InputArchive/SSFA/Terra-FM1-MODIS_Ed4Test/2008/07/CER_SSFA_Terra-FM1-MODIS_Ed4Test_000000.2008071515.met

rm $InputArchive/GQCI/Terra-FM1-MODIS_Ed4Test/2008/07/CER_GQCI_Terra-FM1-MODIS_Ed4Test_000000.2008071515

rm $InputArchive/SCCD/Terra-FM1_Edition3/2008/07/CER_SCCD_$SCC_1P6

rm $InputArchive/SCCN/Terra-FM1_Edition3/2008/07/CER_SCCN_$SCC_1P6

rm $InputArchive/MOA/CERES_DAO-G5-CERES/2008/07/CER_MOA_CERES_DAO-G5-CERES_020032.2008071512

rm $InputArchive/MOA/CERES_DAO-G5-CERES/2008/07/CER_MOA_CERES_DAO-G5-CERES_020032.2008071518

rm $CERESHOME/inversion/data/MATCH-daily/Terra-Aqua-MODIS_Edition4/2008/07/CER_MATCH-daily_Terra-Aqua-MODIS_Edition4_400400.20080715.nc

rm $CERESHOME/inversion/data/SORCE/sorce_tsi_v15.txt.20140331

rm $CERESHOME/inversion/data/sibiMap/Terra-MODIS_Edition4/2008/07/CER_sibiMap_Terra-MODIS_Edition4_400400.200807

#### Log and Status File Results and Metadata Evaluation

The Error and Status Log File, CER4.5-6.1P6_LogReport_$INSTANCE_1P6, is located in directory $CERESHOME/inversion/runlogs after CER4.5-6.1P6 has been executed.  Metadata files, which end in extension '.met', are located in the same directories as their corresponding output files after CER4.5-6.1P6 has been executed

Compare the information contained in the log file with the expected contents of the Log Report file found in directory $CERESHOME/inversion/data_exp/CER4.5-6.1P6 and compare the metadata files with the expected contents of the files with the same names found in directory $CERESHOME/inversion/data_exp/CER4.5-6.1P6, using the following diff_4.5-6.1P6.pl script:

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

$CERESHOME/inversion/CER4.5-6.1P6/rcf/diff_4.5-6.1P6.pl $INSTANCE_1P6

The only differences between the files should be the production times and differences in the directory paths where the tests were run.

#### Execution of Comparison Software for the Main Processor

The evaluation software for the Subsystem Main Processor will perform a single test.  This test will compare all of the parameters on the binary SSF and the binary SSFA (if it exists) to the values in comparison files provided with the software delivery.

- The executable for the comparison software is not provided in the tar file.  It was created when all the software’s code was compiled.

To execute the comparison software for the binary SSF and binary SSFA, type the following commands:

cd $CERESHOME/inversion/test_suites/bin

run_compare_1p6 $INSTANCE_1P6

Two files will be created:

$CERESHOME/inversion/test_suites/results/CmpReport_$DATE_1P6

$CERESHOME/inversion/test_suites/results/CmpReportSSFA_$DATE_1P6

#### Evaluation of Comparison Software Output

This section provides the procedure for evaluating the output from the CER4.5-6.1P6 comparison software.

Examine the comparison reports files by typing:

cat $CERESHOME/inversion/test_suites/results/CmpReport_$DATE_1P6

cat $CERESHOME/inversion/test_suites/results/CmpReportSSFA_$DATE_1P6

The final line of these files will report the status of the comparison between the generated data and the expected output.

#### Evaluation of SSF HDF Product

This section provides the procedure for evaluating the output from the SSF HDF product produced by the test software.  The comparison software was compiled when all software was compiled in a previous step.  Execute the program by typing the following lines:

hdiff $CERESHOME/inversion/data/SSF/Terra-FM1-MODIS_Ed4Test-reproc/2008/07/CER_SSF_$INSTANCE_1P6 $CERESHOME/inversion/data_exp/CER4.5-6.1P6/CER_SSF_$INSTANCE_1P6

The executable, hdiff, compares each Vdata and each SDS on the SSF HDF output file.

The only differences between the two HDF output files should be the dates on Vfields:  “SSF_DATE” on the “SSF_Header” Vdata and “CERPRODUCTIONDATETIME” on the “CERES_metadata” Vdata.  If CERESLIB has changed, the date may be different in the “LOCALVERSIONID” on the “CERES_metadata” Vdata. Differences in the third to sixth decimal places for the data fields are acceptable.

### Solutions to Possible Problems

- All output files are opened with Status = NEW in the CER4.5-6.1P6 software.  These files must be removed before rerunning these test procedures.  A script which removes PGE created files, cleanup_4.5-6.1P6.pl, is located in directory $CERESHOME/inversion/CER4.5-6.1P6/rcf.  To use the clean-up script:

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

$CERESHOME/inversion/CER4.5-6.1P6/rcf/cleanup_4.5-6.1P6.pl $DATE_1P6

Use the latest version of CERESlib.

Ignore the warnings received during compilation.

### Stand Alone, command line, Test Procedures for FM1, Environment Variables REPROCESS = ‘YES’ and READ_IES = ‘YES’

#### Environment setup and file preparation

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

setenv YEAR 2008

setenv MONTH 07

setenv DAY 15

setenv HOUR 15

setenv DATE_1P6 $YEAR$MONTH$DAY$HOUR

setenv INSTANCE_1P6 Terra-FM1-MODIS_Ed4Test-reproc-ies_000000.$DATE_1P6

setenv SCC_1P6 Terra-FM1_Edition3_300300.20080715

source $CERESHOME/inversion/CER4.5-6.1P6/rcf/inversion-FM1-test3-env.csh

Copy the input files to appropriate locations:

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_MOA_CERES_DAO-G5-CERES_020032.2008071512 $InputArchive/MOA/CERES_DAO-G5-CERES/2008/07/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_MOA_CERES_DAO-G5-CERES_020032.2008071518 $InputArchive/MOA/CERES_DAO-G5-CERES/2008/07/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SSFB_Terra-FM1-MODIS_Ed4Test_000000.2008071515 $InputArchive/SSFB/Terra-FM1-MODIS_Ed4Test/2008/07/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SSFA_Terra-FM1-MODIS_Ed4Test_000000.2008071515 $InputArchive/SSFA/Terra-FM1-MODIS_Ed4Test/2008/07/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SSFA_Terra-FM1-MODIS_Ed4Test_000000.2008071515.met $InputArchive/SSFA/Terra-FM1-MODIS_Ed4Test/2008/07/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_GQCI_Terra-FM1-MODIS_Ed4Test_000000.2008071515 $InputArchive/GQCI/Terra-FM1-MODIS_Ed4Test/2008/07/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SCCD_$SCC_1P6 $InputArchive/SCCD/Terra-FM1_Edition3/2008/07/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SCCN_$SCC_1P6 $InputArchive/SCCN/Terra-FM1_Edition3/2008/07/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_MATCH-daily_Terra-Aqua-MODIS_Edition4_400400.20080715.nc $CERESHOME/inversion/data/MATCH-daily/Terra-Aqua-MODIS_Edition4/2008/07/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/sorce_tsi_v15.txt.20140331 $CERESHOME/inversion/data/SORCE/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_IES_Terra-FM1_Edition3_032040.2008071515 $InputArchive/IES/Terra-FM1_Edition3/2008/07/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_sibiMap_Terra-MODIS_Edition4_400400.200807 $CERESHOME/inversion/data/sibiMap/Terra-MODIS_Edition4/2008/07/

#### Execution

Execute the production script by typing the script name, CER4.5-6.1P6-SGE_Driver.pl, followed by the date and hour options and the cleanup option.

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

$CERESHOME/inversion/CER4.5-6.1P6/rcf/CER4.5-6.1P6-SGE_Driver.pl -date 20080715 -hour 15 -clean

The following file will be generated:

$CERESHOME/inversion/CER4.5-6.1P6/rcf/pcf/CER4.5-6.1P6_PCF_$INSTANCE_1P6

The submitted job can be monitored with the qstat command.

The most recently created sge_log file can be viewed to monitor progress of this job.  This will be the last file listed by the command:

ls -arlt $CERESHOME/inversion/sge_logs/CER4.5-6.1P6/CER4.5-6.1P6_$INSTANCE_1P6.o*

Output file generation test:

The script, list_4.5-6.1P6.pl, will list the files that were created during execution of the PGE:

$CERESHOME/inversion/CER4.5-6.1P6/rcf/list_4.5-6.1P6.pl $INSTANCE_1P6

Note:	If any file that should have been created is missing, then a message is written to the screen naming which file could not be found.

#### Exit Codes

All CER4.5-6.1P6 software terminates using the CERES defined EXIT CODES.  Successful completion is indicated by an exit code of 0.  This test should complete with an exit code of 0 for each of the executables.

#### Test Summary

Test Summary:

Total Run Time:	6:24 minutes

Memory:	5.7 G

Required Disk Space:	232 Megabytes

### Evaluation Procedures

When running the production script, run_4.5-6.1P6.pl, the system message, ’No match’, may be written to the screen.  This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

Remove input data:

rm $InputArchive/SSFB/Terra-FM1-MODIS_Ed4Test/2008/07/CER_SSFB_Terra-FM1-MODIS_Ed4Test_000000.2008071515

rm $InputArchive/SSFA/Terra-FM1-MODIS_Ed4Test/2008/07/CER_SSFA_Terra-FM1-MODIS_Ed4Test_000000.2008071515

rm $InputArchive/SSFA/Terra-FM1-MODIS_Ed4Test/2008/07/CER_SSFA_Terra-FM1-MODIS_Ed4Test_000000.2008071515.met

rm $InputArchive/GQCI/Terra-FM1-MODIS_Ed4Test/2008/07/CER_GQCI_Terra-FM1-MODIS_Ed4Test_000000.2008071515

rm $InputArchive/SCCD/Terra-FM1_Edition3/2008/07/CER_SCCD_$SCC_1P6

rm $InputArchive/SCCN/Terra-FM1_Edition3/2008/07/CER_SCCN_$SCC_1P6

rm $InputArchive/MOA/CERES_DAO-G5-CERES/2008/07/CER_MOA_CERES_DAO-G5-CERES_020032.2008071512

rm $InputArchive/MOA/CERES_DAO-G5-CERES/2008/07/CER_MOA_CERES_DAO-G5-CERES_020032.2008071518

rm $CERESHOME/inversion/data/MATCH-daily/Terra-Aqua-MODIS_Edition4/2008/07/CER_MATCH-daily_Terra-Aqua-MODIS_Edition4_400400.20080715.nc

rm $CERESHOME/inversion/data/SORCE/sorce_tsi_v15.txt.20140331

rm $InputArchive/IES/Terra-FM1_Edition3/2008/07/CER_IES_Terra-FM1_Edition3_032040.2008071515

rm $CERESHOME/inversion/data/sibiMap/Terra-MODIS_Edition4/2008/07/CER_sibiMap_Terra-MODIS_Edition4_400400.200807

#### Log and Status File Results and Metadata Evaluation

The Error and Status Log File, CER4.5-6.1P6_LogReport_$INSTANCE_1P6, is located in directory $CERESHOME/inversion/runlogs after CER4.5-6.1P6 has been executed.  Metadata

files, which end in extension '.met', are located in the same directories as their corresponding output files after CER4.5-6.1P6 has been executed.

Compare the information contained in the log file with the expected contents of the Log Report file found in directory $CERESHOME/inversion/data_exp/CER4.5-6.1P6 and compare the metadata files with the expected contents of the files with the same names found in directory $CERESHOME/inversion/data_exp/CER4.5-6.1P6, using the following diff_4.5-6.1P6.pl script:

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

$CERESHOME/inversion/CER4.5-6.1P6/rcf/diff_4.5-6.1P6.pl $INSTANCE_1P6

The only differences between the files should be the production times and differences in the directory paths where the tests were run.

#### Execution of Comparison Software for the Main Processor

The evaluation software for the Subsystem Main Processor will perform a single test.  This test will compare all of the parameters on the binary SSF and the binary SSFA (if it exists) to the values in comparison files provided with the software delivery.

- The executable for the comparison software is not provided in the tar file.  It was created when all the software’s code was compiled.

To execute the comparison software for the binary SSF and binary SSFA, type the following commands:

cd $CERESHOME/inversion/test_suites/bin

run_compare_1p6 $INSTANCE_1P6

Two files will be created:

$CERESHOME/inversion/test_suites/results/CmpReport_$DATE_1P6

$CERESHOME/inversion/test_suites/results/CmpReportSSFA_$DATE_1P6

#### Evaluation of Comparison Software Output

This section provides the procedure for evaluating the output from the CER4.5-6.1P6 comparison software.

Examine the comparison reports files by typing:

cat $CERESHOME/inversion/test_suites/results/CmpReport_$DATE_1P6

cat $CERESHOME/inversion/test_suites/results/CmpReportSSFA_$DATE_1P6

The final line of these files will report the status of the comparison between the generated data and the expected output.

#### Evaluation of SSF HDF Product

This section provides the procedure for evaluating the output from the SSF HDF product produced by the test software.  The comparison software was compiled when all software was compiled in a previous step.  Execute the program by typing the following lines:

hdiff $CERESHOME/inversion/data/SSF/Terra-FM1-MODIS_Ed4Test-reproc-ies/2008/07/CER_SSF_$INSTANCE_1P6 $CERESHOME/inversion/data_exp/CER4.5-6.1P6/CER_SSF_$INSTANCE_1P6

The executable, hdiff, compares each Vdata and each SDS on the SSF HDF output file.

The only differences between the two HDF output files should be the dates on Vfields:  “SSF_DATE” on the “SSF_Header” Vdata and “CERPRODUCTIONDATETIME” on the “CERES_metadata” Vdata.  If CERESLIB has changed, the date may be different in the “LOCALVERSIONID” on the “CERES_metadata” Vdata. Differences in the third to sixth decimal places for the data fields are acceptable.

### Solutions to Possible Problems

- All output files are opened with Status = NEW in the CER4.5-6.1P6 software.  These files must be removed before rerunning these test procedures.  A script which removes PGE created files, cleanup_4.5-6.1P6.pl, is located in directory $CERESHOME/inversion/CER4.5-6.1P6/rcf.  To use the clean-up script:

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

$CERESHOME/inversion/CER4.5-6.1P6/rcf/cleanup_4.5-6.1P6.pl $DATE_1P6

Use the latest version of CERESlib.

Ignore the warnings received during compilation.

### Stand Alone Test Procedures for FM2, Environment variables:  REPROCESS = ‘NO’, READ_IES = ‘NO’ and PROD = ‘no’

#### Environment setup and file preparation

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

setenv YEAR 2001

setenv MONTH 04

setenv DAY 15

setenv HOUR 15

setenv DATE_1P6 $YEAR$MONTH$DAY$HOUR

setenv INSTANCE_1P6 Terra-FM2-MODIS_SSIT2_000000.$DATE_1P6

setenv SCC_1P6 Terra-FM2_Edition3_300300.20010415

source $CERESHOME/inversion/CER4.5-6.1P6/rcf/inversion-FM2-test1-env.csh

Copy the input files to appropriate locations:

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_MOA_CERES_GMAO-G541-Ed4_400400.2001041512 $InputArchive/MOA/CERES_GMAO-G541-Ed4/2001/04/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_MOA_CERES_GMAO-G541-Ed4_400400.2001041518 $InputArchive/MOA/CERES_GMAO-G541-Ed4/2001/04/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SSFI_Terra-FM2-MODIS_SSIT2_000000.2001041515 $InputArchiveInt/SSF_Int/Terra-FM2-MODIS_SSIT2/2001/04/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SSFAI_Terra-FM2-MODIS_SSIT2_000000.2001041515 $InputArchiveInt/SSF_Int/Terra-FM2-MODIS_SSIT2/2001/04/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SSFAI_Terra-FM2-MODIS_SSIT2_000000.2001041515.met $InputArchiveInt/SSF_Int/Terra-FM2-MODIS_SSIT2/2001/04/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_FQCI_Terra-FM2-MODIS_SSIT2_000000.2001041515 $InputArchiveInt/FQC/Terra-FM2-MODIS_SSIT2/2001/04/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SCCD_$SCC_1P6 $InputArchive/SCCD/Terra-FM2_Edition3/2001/04/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SCCN_$SCC_1P6 $InputArchive/SCCN/Terra-FM2_Edition3/2001/04/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_MATCH-daily_Terra-Aqua-MODIS_Edition4_400400.20010415.nc $CERESHOME/inversion/data/MATCH-daily/Terra-Aqua-MODIS_Edition4/2001/04/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/sorce_tsi_v15.txt.20140331 $CERESHOME/inversion/data/SORCE/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_sibiMap_Terra-MODIS_Edition4_400400.200104 $CERESHOME/inversion/data/sibiMap/Terra-MODIS_Edition4/2001/04/

#### Execution

Execute the production script by typing the script name, CER4.5-6.1P6-SGE_Driver.pl, followed by the date and hour options and the cleanup option.

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

$CERESHOME/inversion/CER4.5-6.1P6/rcf/CER4.5-6.1P6-SGE_Driver.pl -date 20010415 -hour 15 -clean

The following file will be generated:

$CERESHOME/inversion/CER4.5-6.1P6/rcf/pcf/CER4.5-6.1P6_PCF_$INSTANCE_1P6

The submitted job can be monitored with the qstat command.

The most recently created sge_log file can be viewed to monitor progress of this job.  This will be the last file listed by the command:

ls -arlt $CERESHOME/inversion/sge_logs/CER4.5-6.1P6/CER4.5-6.1P6_$INSTANCE_1P6.o*

Output file generation test:

The script, list_4.5-6.1P6.pl, will list the files that were created during execution of the PGE:

$CERESHOME/inversion/CER4.5-6.1P6/rcf/list_4.5-6.1P6.pl $INSTANCE_1P6

Note:	If any file that should have been created is missing, then a message is written to the screen naming which file could not be found.

#### Exit Codes

All CER4.5-6.1P6 software terminates using the CERES defined EXIT CODES.  Successful completion is indicated by an exit code of 0.  This test should complete with an exit code of 0 for each of the executables.

#### Test Summary

Test Summary:

Total Run Time:	6:19 minutes

Memory:	5.7 G

Required Disk Space:	232 Megabytes

### Evaluation Procedures

When running the production script, run_4.5-6.1P6.pl, the system message, ’No match’, may be written to the screen.  This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

Remove input data:

rm $InputArchiveInt/SSF_Int/Terra-FM2-MODIS_SSIT2/2001/04/CER_SSFI_$INSTANCE_1P6

rm $InputArchiveInt/SSF_Int/Terra-FM2-MODIS_SSIT2/2001/04/CER_SSFAI_$INSTANCE_1P6

rm $InputArchiveInt/SSF_Int/Terra-FM2-MODIS_SSIT2/2001/04/CER_SSFAI_$INSTANCE_1P6.met

rm $InputArchiveInt/FQC/Terra-FM2-MODIS_SSIT2/2001/04/CER_FQCI_$INSTANCE_1P6

rm $InputArchive/SCCD/Terra-FM2_Edition3/2001/04/CER_SCCD_$SCC_1P6

rm $InputArchive/SCCN/Terra-FM2_Edition3/2001/04/CER_SCCN_$SCC_1P6

rm $InputArchive/MOA/CERES_GMAO-G541-Ed4/2001/04/CER_MOA_CERES_GMAO-G541-Ed4_400400.2001041512

rm $InputArchive/MOA/CERES_GMAO-G541-Ed4/2001/04/CER_MOA_CERES_GMAO-G541-Ed4_400400.2001041518

rm $CERESHOME/inversion/data/MATCH-daily/Terra-Aqua-MODIS_Edition4/2001/04/CER_MATCH-daily_Terra-Aqua-MODIS_Edition4_400400.20010415.nc

rm $CERESHOME/inversion/data/SORCE/sorce_tsi_v15.txt.20140331

rm $CERESHOME/inversion/data/sibiMap/Terra-MODIS_Edition4/2001/04/CER_sibiMap_Terra-MODIS_Edition4_400400.200104

#### Log and Status File Results and Metadata Evaluation

The Error and Status Log File, CER4.5-6.1P6_LogReport_$INSTANCE_1P6, is located in directory $CERESHOME/inversion/runlogs after CER4.5-6.1P6 has been executed.  Metadata files, which end in extension '.met', are located in the same directories as their corresponding output files after CER4.5-6.1P6 has been executed

Compare the information contained in the log file with the expected contents of the Log Report file found in directory $CERESHOME/inversion/data_exp/CER4.5-6.1P6 and compare the metadata files with the expected contents of the files with the same names found in directory $CERESHOME/inversion/data_exp/CER4.5-6.1P6, using the following diff_4.5-6.1P6.pl script:

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

$CERESHOME/inversion/CER4.5-6.1P6/rcf/diff_4.5-6.1P6.pl $INSTANCE_1P6

The only differences between the files should be the production times and differences in the directory paths where the tests were run.

#### Execution of Comparison Software for the Main Processor

The evaluation software for the Subsystem Main Processor will perform a single test.  This test will compare all of the parameters on the binary SSF and the binary SSFA (if it exists) to the values in comparison files provided with the software delivery.

- The executable for the comparison software is not provided in the tar file.  It was created when all the software’s code was compiled.

To execute the comparison software for the binary SSF and binary SSFA, type the following commands:

cd $CERESHOME/inversion/test_suites/bin

run_compare_1p6 $INSTANCE_1P6

Two files will be created:

$CERESHOME/inversion/test_suites/results/CmpReport_$DATE_1P6

$CERESHOME/inversion/test_suites/results/CmpReportSSFA_$DATE_1P6

#### Evaluation of Comparison Software Output

This section provides the procedure for evaluating the output from the CER4.5-6.1P6 comparison software.

Examine the comparison reports files by typing:

cat $CERESHOME/inversion/test_suites/results/CmpReport_$DATE_1P6

cat $CERESHOME/inversion/test_suites/results/CmpReportSSFA_$DATE_1P6

The final line of these files will report the status of the comparison between the generated data and the expected output.

#### Evaluation of SSF HDF Product

This section provides the procedure for evaluating the output from the SSF HDF product produced by the test software.  The comparison software was compiled when all software was compiled in a previous step.  Execute the program by typing the following lines:

hdiff $CERESHOME/inversion/data/SSF/Terra-FM2-MODIS_SSIT2/2001/04/CER_SSF_$INSTANCE_1P6 $CERESHOME/inversion/data_exp/CER4.5-6.1P6/CER_SSF_$INSTANCE_1P6

The executable, hdiff, compares each Vdata and each SDS on the SSF HDF output file.

The only differences between the two HDF output files should be the dates on Vfields:  “SSF_DATE” on the “SSF_Header” Vdata and “CERPRODUCTIONDATETIME” on the “CERES_metadata” Vdata.  If CERESLIB has changed, the date may be different in the “LOCALVERSIONID” on the “CERES_metadata” Vdata. Differences in the third to sixth decimal places for the data fields are acceptable.

### Solutions to Possible Problems

- All output files are opened with Status = NEW in the CER4.5-6.1P6 software.  These files must be removed before rerunning these test procedures.  A script which removes PGE created files, cleanup_4.5-6.1P6.pl, is located in directory $CERESHOME/inversion/CER4.5-6.1P6/rcf.  To use the clean-up script:

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

$CERESHOME/inversion/CER4.5-6.1P6/rcf/cleanup_4.5-6.1P6.pl $DATE_1P6

Use the latest version of CERESlib.

Ignore the warnings received during compilation.

### Stand Alone, command line, Test Procedures for FM2, Environment Variables REPROCESS = ‘YES’, READ_IES = ‘NO’ and PROD = ‘no’

#### Environment setup and file preparation

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

setenv YEAR 2001

setenv MONTH 04

setenv DAY 15

setenv HOUR 15

setenv DATE_1P6 $YEAR$MONTH$DAY$HOUR

setenv INSTANCE_1P6 Terra-FM2-MODIS_Ed4Test-reproc_000000.$DATE_1P6

setenv SCC_1P6 Terra-FM2_Edition3_300300.20010415

source $CERESHOME/inversion/CER4.5-6.1P6/rcf/inversion-FM2-test2-env.csh

Copy the input files to appropriate locations:

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_MOA_CERES_GMAO-G541-Ed4_400400.2001041512 $InputArchive/MOA/CERES_GMAO-G541-Ed4/2001/04/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_MOA_CERES_GMAO-G541-Ed4_400400.2001041518 $InputArchive/MOA/CERES_GMAO-G541-Ed4/2001/04/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SSFB_Terra-FM2-MODIS_SSIT2_000000.2001041515 $InputArchive/SSFB/Terra-FM2-MODIS_SSIT2/2001/04/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SSFA_Terra-FM2-MODIS_SSIT2_000000.2001041515 $InputArchive/SSFA/Terra-FM2-MODIS_SSIT2/2001/04/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SSFA_Terra-FM2-MODIS_SSIT2_000000.2001041515.met $InputArchive/SSFA/Terra-FM2-MODIS_SSIT2/2001/04/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_GQCI_Terra-FM2-MODIS_SSIT2_000000.2001041515 $InputArchive/GQCI/Terra-FM2-MODIS_SSIT2/2001/04/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SCCD_$SCC_1P6 $InputArchive/SCCD/Terra-FM2_Edition3/2001/04/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SCCN_$SCC_1P6 $InputArchive/SCCN/Terra-FM2_Edition3/2001/04/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_MATCH-daily_Terra-Aqua-MODIS_Edition4_400400.20010415.nc $CERESHOME/inversion/data/MATCH-daily/Terra-Aqua-MODIS_Edition4/2001/04/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/sorce_tsi_v15.txt.20140331 $CERESHOME/inversion/data/SORCE/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_sibiMap_Terra-MODIS_Edition4_400400.200104 $CERESHOME/inversion/data/sibiMap/Terra-MODIS_Edition4/2001/04/

#### Execution

Execute the production script by typing the script name, CER4.5-6.1P6-SGE_Driver.pl, followed by the date and hour options and the cleanup option.

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

$CERESHOME/inversion/CER4.5-6.1P6/rcf/CER4.5-6.1P6-SGE_Driver.pl -date 20010415 -hour 15 -clean

The following file will be generated:

$CERESHOME/inversion/CER4.5-6.1P6/rcf/pcf/CER4.5-6.1P6_PCF_$INSTANCE_1P6

The submitted job can be monitored with the qstat command.

The most recently created sge_log file can be viewed to monitor progress of this job.  This will be the last file listed by the command:

ls -arlt $CERESHOME/inversion/sge_logs/CER4.5-6.1P6/CER4.5-6.1P6_$INSTANCE_1P6.o*

Output file generation test:

The script, list_4.5-6.1P6.pl, will list the files that were created during execution of the PGE:

$CERESHOME/inversion/CER4.5-6.1P6/rcf/list_4.5-6.1P6.pl $INSTANCE_1P6

Note:	If any file that should have been created is missing, then a message is written to the screen naming which file could not be found.

#### Exit Codes

All CER4.5-6.1P6 software terminates using the CERES defined EXIT CODES.  Successful completion is indicated by an exit code of 0.  This test should complete with an exit code of 0 for each of the executables.

#### Test Summary

Test Summary:

Total Run Time:	6:42 minutes

Memory:	5.7 G

Required Disk Space:	232 Megabytes

### Evaluation Procedures

When running the production script, run_4.5-6.1P6.pl, the system message, ’No match’, may be written to the screen.  This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

Remove input data:

rm $InputArchive/SSFB/Terra-FM2-MODIS_SSIT2/2001/04/CER_SSFB_Terra-FM2-MODIS_SSIT2_000000.2001041515

rm $InputArchive/SSFA/Terra-FM2-MODIS_SSIT2/2001/04/CER_SSFA_Terra-FM2-MODIS_SSIT2_000000.2001041515

rm $InputArchive/SSFA/Terra-FM2-MODIS_SSIT2/2001/04/CER_SSFA_Terra-FM2-MODIS_SSIT2_000000.2001041515.met

rm $InputArchive/GQCI/Terra-FM2-MODIS_SSIT2/2001/04/CER_GQCI_Terra-FM2-MODIS_SSIT2_000000.2001041515

rm $InputArchive/SCCD/Terra-FM2_Edition3/2001/04/CER_SCCD_$SCC_1P6

rm $InputArchive/SCCN/Terra-FM2_Edition3/2001/04/CER_SCCN_$SCC_1P6

rm $InputArchive/MOA/CERES_GMAO-G541-Ed4/2001/04/CER_MOA_CERES_GMAO-G541-Ed4_400400.2001041512

rm $InputArchive/MOA/CERES_GMAO-G541-Ed4/2001/04/CER_MOA_CERES_GMAO-G541-Ed4_400400.2001041518

rm $CERESHOME/inversion/data/MATCH-daily/Terra-Aqua-MODIS_Edition4/2001/04/CER_MATCH-daily_Terra-Aqua-MODIS_Edition4_400400.20010415.nc

rm $CERESHOME/inversion/data/SORCE/sorce_tsi_v15.txt.20140331

rm $CERESHOME/inversion/data/sibiMap/Terra-MODIS_Edition4/2001/04/CER_sibiMap_Terra-MODIS_Edition4_400400.200104

#### Log and Status File Results and Metadata Evaluation

The Error and Status Log File, CER4.5-6.1P6_LogReport_$INSTANCE_1P6, is located in directory $CERESHOME/inversion/runlogs after CER4.5-6.1P6 has been executed.  Metadata files, which end in extension '.met', are located in the same directories as their corresponding output files after CER4.5-6.1P6 has been executed

Compare the information contained in the log file with the expected contents of the Log Report file found in directory $CERESHOME/inversion/data_exp/CER4.5-6.1P6 and compare the metadata files with the expected contents of the files with the same names found in directory $CERESHOME/inversion/data_exp/CER4.5-6.1P6, using the following diff_4.5-6.1P6.pl script:

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

$CERESHOME/inversion/CER4.5-6.1P6/rcf/diff_4.5-6.1P6.pl $INSTANCE_1P6

The only differences between the files should be the production times and differences in the directory paths where the tests were run.

#### Execution of Comparison Software for the Main Processor

The evaluation software for the Subsystem Main Processor will perform a single test.  This test will compare all of the parameters on the binary SSF and the binary SSFA (if it exists) to the values in comparison files provided with the software delivery.

- The executable for the comparison software is not provided in the tar file.  It was created when all the software’s code was compiled.

To execute the comparison software for the binary SSF and binary SSFA, type the following commands:

cd $CERESHOME/inversion/test_suites/bin

run_compare_1p6 $INSTANCE_1P6

Two files will be created:

$CERESHOME/inversion/test_suites/results/CmpReport_$DATE_1P6

$CERESHOME/inversion/test_suites/results/CmpReportSSFA_$DATE_1P6

#### Evaluation of Comparison Software Output

This section provides the procedure for evaluating the output from the CER4.5-6.1P6 comparison software.

Examine the comparison reports files by typing:

cat $CERESHOME/inversion/test_suites/results/CmpReport_$DATE_1P6

cat $CERESHOME/inversion/test_suites/results/CmpReportSSFA_$DATE_1P6

The final line of these files will report the status of the comparison between the generated data and the expected output.

#### Evaluation of SSF HDF Product

This section provides the procedure for evaluating the output from the SSF HDF product produced by the test software.  The comparison software was compiled when all software was compiled in a previous step.  Execute the program by typing the following lines:

hdiff $CERESHOME/inversion/data/SSF/Terra-FM2-MODIS_Ed4Test-reproc/2001/04/CER_SSF_$INSTANCE_1P6 $CERESHOME/inversion/data_exp/CER4.5-6.1P6/CER_SSF_$INSTANCE_1P6

The executable, hdiff, compares each Vdata and each SDS on the SSF HDF output file.

The only differences between the two HDF output files should be the dates on Vfields: “SSF_DATE” on the “SSF_Header” Vdata and “CERPRODUCTIONDATETIME” on the “CERES_metadata” Vdata.  If CERESLIB has changed, the date may be different in the “LOCALVERSIONID” on the “CERES_metadata” Vdata. Differences in the third to sixth decimal places for the data fields are acceptable.

### Solutions to Possible Problems

- All output files are opened with Status = NEW in the CER4.5-6.1P6 software.  These files must be removed before rerunning these test procedures.  A script which removes PGE created files, cleanup_4.5-6.1P6.pl, is located in directory $CERESHOME/inversion/CER4.5-6.1P6/rcf.  To use the clean-up script:

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

$CERESHOME/inversion/CER4.5-6.1P6/rcf/cleanup_4.5-6.1P6.pl $DATE_1P6

Use the latest version of CERESlib.

Ignore the warnings received during compilation.

### Stand Alone, command line, Test Procedures for FM2, Environment Variables REPROCESS = ‘YES’ and READ_IES = ‘YES’

#### Environment setup and file preparation

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

setenv YEAR 2001

setenv MONTH 04

setenv DAY 15

setenv HOUR 15

setenv DATE_1P6 $YEAR$MONTH$DAY$HOUR

setenv INSTANCE_1P6 Terra-FM2-MODIS_Ed4Test-reproc-ies_000000.$DATE_1P6

setenv SCC_1P6 Terra-FM2_Edition3_300300.20010415

source $CERESHOME/inversion/CER4.5-6.1P6/rcf/inversion-FM2-test3-env.csh

Copy the input files to appropriate locations:

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_MOA_CERES_GMAO-G541-Ed4_400400.2001041512 $InputArchive/MOA/CERES_GMAO-G541-Ed4/2001/04/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_MOA_CERES_GMAO-G541-Ed4_400400.2001041518 $InputArchive/MOA/CERES_GMAO-G541-Ed4/2001/04/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SSFB_Terra-FM2-MODIS_SSIT2_000000.2001041515 $InputArchive/SSFB/Terra-FM2-MODIS_SSIT2/2001/04/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SSFA_Terra-FM2-MODIS_SSIT2_000000.2001041515 $InputArchive/SSFA/Terra-FM2-MODIS_SSIT2/2001/04/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SSFA_Terra-FM2-MODIS_SSIT2_000000.2001041515.met $InputArchive/SSFA/Terra-FM2-MODIS_SSIT2/2001/04/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_GQCI_Terra-FM2-MODIS_SSIT2_000000.2001041515 $InputArchive/GQCI/Terra-FM2-MODIS_SSIT2/2001/04/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SCCD_$SCC_1P6 $InputArchive/SCCD/Terra-FM2_Edition3/2001/04/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SCCN_$SCC_1P6 $InputArchive/SCCN/Terra-FM2_Edition3/2001/04/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_MATCH-daily_Terra-Aqua-MODIS_Edition4_400400.20010415.nc $CERESHOME/inversion/data/MATCH-daily/Terra-Aqua-MODIS_Edition4/2001/04/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/sorce_tsi_v15.txt.20140331 $CERESHOME/inversion/data/SORCE/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_IES_Terra-FM2_Edition3_032040.2001041515 $InputArchive/IES/Terra-FM2_Edition3/2001/04/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_sibiMap_Terra-MODIS_Edition4_400400.200104 $CERESHOME/inversion/data/sibiMap/Terra-MODIS_Edition4/2001/04/

#### Execution

Execute the production script by typing the script name, CER4.5-6.1P6-SGE_Driver.pl, followed by the date and hour options and the cleanup option.

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

$CERESHOME/inversion/CER4.5-6.1P6/rcf/CER4.5-6.1P6-SGE_Driver.pl -date 20010415 -hour 15 -clean

The following file will be generated:

$CERESHOME/inversion/CER4.5-6.1P6/rcf/pcf/CER4.5-6.1P6_PCF_$INSTANCE_1P6

The submitted job can be monitored with the qstat command.

The most recently created sge_log file can be viewed to monitor progress of this job.  This will be the last file listed by the command:

ls -arlt $CERESHOME/inversion/sge_logs/CER4.5-6.1P6/CER4.5-6.1P6_$INSTANCE_1P6.o*

Output file generation test:

The script, list_4.5-6.1P6.pl, will list the files that were created during execution of the PGE:

$CERESHOME/inversion/CER4.5-6.1P6/rcf/list_4.5-6.1P6.pl $INSTANCE_1P6

Note:	If any file that should have been created is missing, then a message is written to the screen naming which file could not be found.

#### Exit Codes

All CER4.5-6.1P6 software terminates using the CERES defined EXIT CODES.  Successful completion is indicated by an exit code of 0.  This test should complete with an exit code of 0 for each of the executables.

#### Test Summary

Test Summary:

Total Run Time:	6:42 minutes

Memory:	5.7 G

Required Disk Space:	232 Megabytes

### Evaluation Procedures

When running the production script, run_4.5-6.1P6.pl, the system message, ’No match’, may be written to the screen.  This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

Remove input data:

rm $InputArchive/SSFB/Terra-FM2-MODIS_SSIT2/2001/04/CER_SSFB_Terra-FM2-MODIS_SSIT2_000000.2001041515

rm $InputArchive/SSFA/Terra-FM2-MODIS_SSIT2/2001/04/CER_SSFA_Terra-FM2-MODIS_SSIT2_000000.2001041515

rm $InputArchive/SSFA/Terra-FM2-MODIS_SSIT2/2001/04/CER_SSFA_Terra-FM2-MODIS_SSIT2_000000.2001041515.met

rm $InputArchive/GQCI/Terra-FM2-MODIS_SSIT2/2001/04/CER_GQCI_Terra-FM2-MODIS_SSIT2_000000.2001041515

rm $InputArchive/SCCD/Terra-FM2_Edition3/2001/04/CER_SCCD_$SCC_1P6

rm $InputArchive/SCCN/Terra-FM2_Edition3/2001/04/CER_SCCN_$SCC_1P6

rm $InputArchive/MOA/CERES_GMAO-G541-Ed4/2001/04/CER_MOA_CERES_GMAO-G541-Ed4_400400.2001041512

rm $InputArchive/MOA/CERES_GMAO-G541-Ed4/2001/04/CER_MOA_CERES_GMAO-G541-Ed4_400400.2001041518

rm $CERESHOME/inversion/data/MATCH-daily/Terra-Aqua-MODIS_Edition4/2001/04/CER_MATCH-daily_Terra-Aqua-MODIS_Edition4_400400.20010415.nc

rm $CERESHOME/inversion/data/SORCE/sorce_tsi_v15.txt.20140331

rm $InputArchive/IES/Terra-FM2_Edition3/2001/04/CER_IES_Terra-FM2_Edition3_032040.2001041515

rm $CERESHOME/inversion/data/sibiMap/Terra-MODIS_Edition4/2001/04/CER_sibiMap_Terra-MODIS_Edition4_400400.200104

#### Log and Status File Results and Metadata Evaluation

The Error and Status Log File, CER4.5-6.1P6_LogReport_$INSTANCE_1P6, is located in directory $CERESHOME/inversion/runlogs after CER4.5-6.1P6 has been executed.  Metadata

files, which end in extension '.met', are located in the same directories as their corresponding output files after CER4.5-6.1P6 has been executed.

Compare the information contained in the log file with the expected contents of the Log Report file found in directory $CERESHOME/inversion/data_exp/CER4.5-6.1P6 and compare the metadata files with the expected contents of the files with the same names found in directory $CERESHOME/inversion/data_exp/CER4.5-6.1P6, using the following diff_4.5-6.1P6.pl script:

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

$CERESHOME/inversion/CER4.5-6.1P6/rcf/diff_4.5-6.1P6.pl $INSTANCE_1P6

The only differences between the files should be the production times and differences in the directory paths where the tests were run.

#### Execution of Comparison Software for the Main Processor

The evaluation software for the Subsystem Main Processor will perform a single test.  This test will compare all of the parameters on the binary SSF and the binary SSFA (if it exists) to the values in comparison files provided with the software delivery.

- The executable for the comparison software is not provided in the tar file.  It was created when all the software’s code was compiled.

To execute the comparison software for the binary SSF and binary SSFA, type the following commands:

cd $CERESHOME/inversion/test_suites/bin

run_compare_1p6 $INSTANCE_1P6

Two files will be created:

$CERESHOME/inversion/test_suites/results/CmpReport_$DATE_1P6

$CERESHOME/inversion/test_suites/results/CmpReportSSFA_$DATE_1P6

#### Evaluation of Comparison Software Output

This section provides the procedure for evaluating the output from the CER4.5-6.1P6 comparison software.

Examine the comparison reports files by typing:

cat $CERESHOME/inversion/test_suites/results/CmpReport_$DATE_1P6

cat $CERESHOME/inversion/test_suites/results/CmpReportSSFA_$DATE_1P6

The final line of these files will report the status of the comparison between the generated data and the expected output.

#### Evaluation of SSF HDF Product

This section provides the procedure for evaluating the output from the SSF HDF product produced by the test software.  The comparison software was compiled when all software was compiled in a previous step.  Execute the program by typing the following lines:

hdiff $CERESHOME/inversion/data/SSF/Terra-FM2-MODIS_Ed4Test-reproc-ies/2001/04/CER_SSF_$INSTANCE_1P6 $CERESHOME/inversion/data_exp/CER4.5-6.1P6/CER_SSF_$INSTANCE_1P6

The executable, hdiff, compares each Vdata and each SDS on the SSF HDF output file.

The only differences between the two HDF output files should be the dates on Vfields: “SSF_DATE” on the “SSF_Header” Vdata and “CERPRODUCTIONDATETIME” on the “CERES_metadata” Vdata.  If CERESLIB has changed, the date may be different in the “LOCALVERSIONID” on the “CERES_metadata” Vdata. Differences in the third to sixth decimal places for the data fields are acceptable.

### Solutions to Possible Problems

- All output files are opened with Status = NEW in the CER4.5-6.1P6 software.  These files must be removed before rerunning these test procedures.  A script which removes PGE created files, cleanup_4.5-6.1P6.pl, is located in directory $CERESHOME/inversion/CER4.5-6.1P6/rcf.  To use the clean-up script:

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

$CERESHOME/inversion/CER4.5-6.1P6/rcf/cleanup_4.5-6.1P6.pl $DATE_1P6

Use the latest version of CERESlib.

Ignore the warnings received during compilation.

### Stand Alone Test Procedures for FM3, Environment variables:  REPROCESS = ‘NO’, READ_IES = ‘NO’ and PROD = ‘no’

#### Environment setup and file preparation

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

setenv YEAR 2008

setenv MONTH 10

setenv DAY 15

setenv HOUR 07

setenv DATE_1P6 $YEAR$MONTH$DAY$HOUR

setenv INSTANCE_1P6 Aqua-FM3-MODIS_SSIT_000000.$DATE_1P6

setenv SCC_1P6 Aqua-FM3_Edition3_300300.20081015

source $CERESHOME/inversion/CER4.5-6.1P6/rcf/inversion-FM3-test1-env.csh

Copy the input files to appropriate locations:

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_MOA_CERES_GMAO-G5-Edition3-54_999999.2008101506 $InputArchive/MOA/CERES_GMAO-G5-Edition3-54/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_MOA_CERES_GMAO-G5-Edition3-54_999999.2008101512 $InputArchive/MOA/CERES_GMAO-G5-Edition3-54/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SSFI_Aqua-FM3-MODIS_SSIT_000000.2008101507 $InputArchiveInt/SSF_Int/Aqua-FM3-MODIS_SSIT/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SSFAI_Aqua-FM3-MODIS_SSIT_000000.2008101507 $InputArchiveInt/SSF_Int/Aqua-FM3-MODIS_SSIT/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SSFAI_Aqua-FM3-MODIS_SSIT_000000.2008101507.met $InputArchiveInt/SSF_Int/Aqua-FM3-MODIS_SSIT/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_FQCI_Aqua-FM3-MODIS_SSIT_000000.2008101507 $InputArchiveInt/FQC/Aqua-FM3-MODIS_SSIT/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SCCD_$SCC_1P6 $InputArchive/SCCD/Aqua-FM3_Edition3/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SCCN_$SCC_1P6 $InputArchive/SCCN/Aqua-FM3_Edition3/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_MATCH-daily_Terra-Aqua-MODIS_Edition4_400400.20081015.nc $CERESHOME/inversion/data/MATCH-daily/Terra-Aqua-MODIS_Edition4/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/sorce_tsi_v15.txt.20140331 $CERESHOME/inversion/data/SORCE/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_sibiMap_Aqua-MODIS_Edition4_400400.200810 $CERESHOME/inversion/data/sibiMap/Aqua-MODIS_Edition4/2008/10/

#### Execution

Execute the production script by typing the script name, CER4.5-6.1P6-SGE_Driver.pl, followed by the date and hour options and the cleanup option.

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

$CERESHOME/inversion/CER4.5-6.1P6/rcf/CER4.5-6.1P6-SGE_Driver.pl -date 20081015 -hour 07 -clean

The following file will be generated:

$CERESHOME/inversion/CER4.5-6.1P6/rcf/pcf/CER4.5-6.1P6_PCF_$INSTANCE_1P6

The submitted job can be monitored with the qstat command.

The most recently created sge_log file can be viewed to monitor progress of this job.  This will be the last file listed by the command:

ls -arlt $CERESHOME/inversion/sge_logs/CER4.5-6.1P6/CER4.5-6.1P6_$INSTANCE_1P6.o*

Output file generation test:

The script, list_4.5-6.1P6.pl, will list the files that were created during execution of the PGE:

$CERESHOME/inversion/CER4.5-6.1P6/rcf/list_4.5-6.1P6.pl $INSTANCE_1P6

Note:	If any file that should have been created is missing, then a message is written to the screen naming which file could not be found.

#### Exit Codes

All CER4.5-6.1P6 software terminates using the CERES defined EXIT CODES.  Successful completion is indicated by an exit code of 0.  This test should complete with an exit code of 0 for each of the executables.

#### Test Summary

Test Summary:

Total Run Time:	6:22 minutes

Memory:	5.7 G

Required Disk Space:	232 Megabytes

### Evaluation Procedures

When running the production script, run_4.5-6.1P6.pl, the system message, ’No match’, may be written to the screen.  This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

Remove input data:

rm $InputArchiveInt/SSF_Int/Aqua-FM3-MODIS_SSIT/2008/10/CER_SSFI_$INSTANCE_1P6

rm $InputArchiveInt/SSF_Int/Aqua-FM3-MODIS_SSIT/2008/10/CER_SSFAI_$INSTANCE_1P6

rm $InputArchiveInt/SSF_Int/Aqua-FM3-MODIS_SSIT/2008/10/CER_SSFAI_$INSTANCE_1P6.met

rm $InputArchiveInt/FQC/Aqua-FM3-MODIS_SSIT/2008/10/CER_FQCI_$INSTANCE_1P6

rm $InputArchive/SCCD/Aqua-FM3_Edition3/2008/10/CER_SCCD_$SCC_1P6

rm $InputArchive/SCCN/Aqua-FM3_Edition3/2008/10/CER_SCCN_$SCC_1P6

rm $InputArchive/MOA/CERES_GMAO-G5-Edition3-54/2008/10/CER_MOA_CERES_GMAO-G5-Edition3-54_999999.2008101506

rm $InputArchive/MOA/CERES_GMAO-G5-Edition3-54/2008/10/CER_MOA_CERES_GMAO-G5-Edition3-54_999999.2008101512

rm $CERESHOME/inversion/data/MATCH-daily/Terra-Aqua-MODIS_Edition4/2008/10/CER_MATCH-daily_Terra-Aqua-MODIS_Edition4_400400.20081015.nc

rm $CERESHOME/inversion/data/SORCE/sorce_tsi_v15.txt.20140331

rm $CERESHOME/inversion/data/sibiMap/Aqua-MODIS_Edition4/2008/10/CER_sibiMap_Aqua-MODIS_Edition4_400400.200810

#### Log and Status File Results and Metadata Evaluation

The Error and Status Log File, CER4.5-6.1P6_LogReport_$INSTANCE_1P6, is located in directory $CERESHOME/inversion/runlogs after CER4.5-6.1P6 has been executed.  Metadata files, which end in extension '.met', are located in the same directories as their corresponding output files after CER4.5-6.1P6 has been executed

Compare the information contained in the log file with the expected contents of the Log Report file found in directory $CERESHOME/inversion/data_exp/CER4.5-6.1P6 and compare the metadata files with the expected contents of the files with the same names found in directory $CERESHOME/inversion/data_exp/CER4.5-6.1P6, using the following diff_4.5-6.1P6.pl script:

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

$CERESHOME/inversion/CER4.5-6.1P6/rcf/diff_4.5-6.1P6.pl $INSTANCE_1P6

The only differences between the files should be the production times and differences in the directory paths where the tests were run.

#### Execution of Comparison Software for the Main Processor

The evaluation software for the Subsystem Main Processor will perform a single test.  This test will compare all of the parameters on the binary SSF and the binary SSFA (if it exists) to the values in comparison files provided with the software delivery.

- The executable for the comparison software is not provided in the tar file.  It was created when all the software’s code was compiled.

To execute the comparison software for the binary SSF and binary SSFA, type the following commands:

cd $CERESHOME/inversion/test_suites/bin

run_compare_1p6 $INSTANCE_1P6

Two files will be created:

$CERESHOME/inversion/test_suites/results/CmpReport_$DATE_1P6

$CERESHOME/inversion/test_suites/results/CmpReportSSFA_$DATE_1P6

#### Evaluation of Comparison Software Output

This section provides the procedure for evaluating the output from the CER4.5-6.1P6 comparison software.

Examine the comparison reports files by typing:

cat $CERESHOME/inversion/test_suites/results/CmpReport_$DATE_1P6

cat $CERESHOME/inversion/test_suites/results/CmpReportSSFA_$DATE_1P6

The final line of these files will report the status of the comparison between the generated data and the expected output.

#### Evaluation of SSF HDF Product

This section provides the procedure for evaluating the output from the SSF HDF product produced by the test software.  The comparison software was compiled when all software was compiled in a previous step.  Execute the program by typing the following lines:

hdiff $CERESHOME/inversion/data/SSF/Aqua-FM3-MODIS_SSIT/2008/10/CER_SSF_$INSTANCE_1P6 $CERESHOME/inversion/data_exp/CER4.5-6.1P6/CER_SSF_$INSTANCE_1P6

The executable, hdiff, compares each Vdata and each SDS on the SSF HDF output file.

The only differences between the two HDF output files should be the dates on Vfields: “SSF_DATE” on the “SSF_Header” Vdata and “CERPRODUCTIONDATETIME” on the “CERES_metadata” Vdata.  If CERESLIB has changed, the date may be different in the “LOCALVERSIONID” on the “CERES_metadata” Vdata. Differences in the third to sixth decimal places for the data fields are acceptable.

### Solutions to Possible Problems

- All output files are opened with Status = NEW in the CER4.5-6.1P6 software.  These files must be removed before rerunning these test procedures.  A script which removes PGE created files, cleanup_4.5-6.1P6.pl, is located in directory $CERESHOME/inversion/CER4.5-6.1P6/rcf.  To use the clean-up script:

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

$CERESHOME/inversion/CER4.5-6.1P6/rcf/cleanup_4.5-6.1P6.pl $DATE_1P6

Use the latest version of CERESlib.

Ignore the warnings received during compilation.

### Stand Alone, command line, Test Procedures for FM3, Environment Variables REPROCESS = ‘YES’, READ_IES = ‘NO’ and PROD = ‘no’

#### Environment setup and file preparation

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

setenv YEAR 2008

setenv MONTH 10

setenv DAY 15

setenv HOUR 07

setenv DATE_1P6 $YEAR$MONTH$DAY$HOUR

setenv INSTANCE_1P6 Aqua-FM3-MODIS_Ed4Test-reproc_000000.$DATE_1P6

setenv SCC_1P6 Aqua-FM3_Edition3_300300.20081015

source $CERESHOME/inversion/CER4.5-6.1P6/rcf/inversion-FM3-test2-env.csh

Copy the input files to appropriate locations:

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_MOA_CERES_GMAO-G5-Edition3-54_999999.2008101506 $InputArchive/MOA/CERES_GMAO-G5-Edition3-54/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_MOA_CERES_GMAO-G5-Edition3-54_999999.2008101512 $InputArchive/MOA/CERES_GMAO-G5-Edition3-54/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SSFB_Aqua-FM3-MODIS_SSIT_000000.2008101507 $InputArchive/SSFB/Aqua-FM3-MODIS_SSIT/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SSFA_Aqua-FM3-MODIS_SSIT_000000.2008101507 $InputArchive/SSFA/Aqua-FM3-MODIS_SSIT/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SSFA_Aqua-FM3-MODIS_SSIT_000000.2008101507.met $InputArchive/SSFA/Aqua-FM3-MODIS_SSIT/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_GQCI_Aqua-FM3-MODIS_SSIT_000000.2008101507 $InputArchive/GQCI/Aqua-FM3-MODIS_SSIT/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SCCD_$SCC_1P6 $InputArchive/SCCD/Aqua-FM3_Edition3/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SCCN_$SCC_1P6 $InputArchive/SCCN/Aqua-FM3_Edition3/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_MATCH-daily_Terra-Aqua-MODIS_Edition4_400400.20081015.nc $CERESHOME/inversion/data/MATCH-daily/Terra-Aqua-MODIS_Edition4/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/sorce_tsi_v15.txt.20140331 $CERESHOME/inversion/data/SORCE/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_sibiMap_Aqua-MODIS_Edition4_400400.200810 $CERESHOME/inversion/data/sibiMap/Aqua-MODIS_Edition4/2008/10/

#### Execution

Execute the production script by typing the script name, CER4.5-6.1P6-SGE_Driver.pl, followed by the date and hour options and the cleanup option.

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

$CERESHOME/inversion/CER4.5-6.1P6/rcf/CER4.5-6.1P6-SGE_Driver.pl -date 20081015 -hour 07 -clean

The following file will be generated:

$CERESHOME/inversion/CER4.5-6.1P6/rcf/pcf/CER4.5-6.1P6_PCF_$INSTANCE_1P6

The submitted job can be monitored with the qstat command.

The most recently created sge_log file can be viewed to monitor progress of this job.  This will be the last file listed by the command:

ls -arlt $CERESHOME/inversion/sge_logs/CER4.5-6.1P6/CER4.5-6.1P6_$INSTANCE_1P6.o*

Output file generation test:

The script, list_4.5-6.1P6.pl, will list the files that were created during execution of the PGE:

$CERESHOME/inversion/CER4.5-6.1P6/rcf/list_4.5-6.1P6.pl $INSTANCE_1P6

Note:	If any file that should have been created is missing, then a message is written to the screen naming which file could not be found.

#### Exit Codes

All CER4.5-6.1P6 software terminates using the CERES defined EXIT CODES.  Successful completion is indicated by an exit code of 0.  This test should complete with an exit code of 0 for each of the executables.

#### Test Summary

Test Summary:

Total Run Time:	6:22 minutes

Memory:	5.7 G

Required Disk Space:	232 Megabytes

### Evaluation Procedures

When running the production script, run_4.5-6.1P6.pl, the system message, ’No match’, may be written to the screen.  This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

Remove input data:

rm $InputArchive/SSFB/Aqua-FM3-MODIS_SSIT/2008/10/CER_SSFB_Aqua-FM3-MODIS_SSIT_000000.2008101507

rm $InputArchive/SSFA/Aqua-FM3-MODIS_SSIT/2008/10/CER_SSFA_Aqua-FM3-MODIS_SSIT_000000.2008101507

rm $InputArchive/SSFA/Aqua-FM3-MODIS_SSIT/2008/10/CER_SSFA_Aqua-FM3-MODIS_SSIT_000000.2008101507.met

rm $InputArchive/GQCI/Aqua-FM3-MODIS_SSIT/2008/10/CER_GQCI_Aqua-FM3-MODIS_SSIT_000000.2008101507

rm $InputArchive/SCCD/Aqua-FM3_Edition3/2008/10/CER_SCCD_$SCC_1P6

rm $InputArchive/SCCN/Aqua-FM3_Edition3/2008/10/CER_SCCN_$SCC_1P6

rm $InputArchive/MOA/CERES_GMAO-G5-Edition3-54/2008/10/CER_MOA_CERES_GMAO-G5-Edition3-54_999999.2008101506

rm $InputArchive/MOA/CERES_GMAO-G5-Edition3-54/2008/10/CER_MOA_CERES_GMAO-G5-Edition3-54_999999.2008101512

rm $CERESHOME/inversion/data/MATCH-daily/Terra-Aqua-MODIS_Edition4/2008/10/CER_MATCH-daily_Terra-Aqua-MODIS_Edition4_400400.20081015.nc

rm $CERESHOME/inversion/data/SORCE/sorce_tsi_v15.txt.20140331

rm $CERESHOME/inversion/data/sibiMap/Aqua-MODIS_Edition4/2008/10/CER_sibiMap_Aqua-MODIS_Edition4_400400.200810

#### Log and Status File Results and Metadata Evaluation

The Error and Status Log File, CER4.5-6.1P6_LogReport_$INSTANCE_1P6, is located in directory $CERESHOME/inversion/runlogs after CER4.5-6.1P6 has been executed.  Metadata files, which end in extension '.met', are located in the same directories as their corresponding output files after CER4.5-6.1P6 has been executed

Compare the information contained in the log file with the expected contents of the Log Report file found in directory $CERESHOME/inversion/data_exp/CER4.5-6.1P6 and compare the metadata files with the expected contents of the files with the same names found in directory $CERESHOME/inversion/data_exp/CER4.5-6.1P6, using the following diff_4.5-6.1P6.pl script:

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

$CERESHOME/inversion/CER4.5-6.1P6/rcf/diff_4.5-6.1P6.pl $INSTANCE_1P6

The only differences between the files should be the production times and differences in the directory paths where the tests were run.

#### Execution of Comparison Software for the Main Processor

The evaluation software for the Subsystem Main Processor will perform a single test.  This test will compare all of the parameters on the binary SSF and the binary SSFA (if it exists) to the values in comparison files provided with the software delivery.

- The executable for the comparison software is not provided in the tar file.  It was created when all the software’s code was compiled.

To execute the comparison software for the binary SSF and binary SSFA, type the following commands:

cd $CERESHOME/inversion/test_suites/bin

run_compare_1p6 $INSTANCE_1P6

Two files will be created:

$CERESHOME/inversion/test_suites/results/CmpReport_$DATE_1P6

$CERESHOME/inversion/test_suites/results/CmpReportSSFA_$DATE_1P6

#### Evaluation of Comparison Software Output

This section provides the procedure for evaluating the output from the CER4.5-6.1P6 comparison software.

Examine the comparison reports files by typing:

cat $CERESHOME/inversion/test_suites/results/CmpReport_$DATE_1P6

cat $CERESHOME/inversion/test_suites/results/CmpReportSSFA_$DATE_1P6

The final line of these files will report the status of the comparison between the generated data and the expected output.

#### Evaluation of SSF HDF Product

This section provides the procedure for evaluating the output from the SSF HDF product produced by the test software.  The comparison software was compiled when all software was compiled in a previous step.  Execute the program by typing the following lines:

hdiff $CERESHOME/inversion/data/SSF/Aqua-FM3-MODIS_Ed4Test-reproc/2008/10/CER_SSF_$INSTANCE_1P6 $CERESHOME/inversion/data_exp/CER4.5-6.1P6/CER_SSF_$INSTANCE_1P6

The executable, hdiff, compares each Vdata and each SDS on the SSF HDF output file.

The only differences between the two HDF output files should be the dates on Vfields: “SSF_DATE” on the “SSF_Header” Vdata and “CERPRODUCTIONDATETIME” on the “CERES_metadata” Vdata.  If CERESLIB has changed, the date may be different in the “LOCALVERSIONID” on the “CERES_metadata” Vdata.  Differences in the third to sixth decimal places for the data fields are acceptable.

### Solutions to Possible Problems

- All output files are opened with Status = NEW in the CER4.5-6.1P6 software.  These files must be removed before rerunning these test procedures.  A script which removes PGE created files, cleanup_4.5-6.1P6.pl, is located in directory $CERESHOME/inversion/CER4.5-6.1P6/rcf.  To use the clean-up script:

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

$CERESHOME/inversion/CER4.5-6.1P6/rcf/cleanup_4.5-6.1P6.pl $DATE_1P6

Use the latest version of CERESlib.

Ignore the warnings received during compilation.

### Stand Alone, command line, Test Procedures for FM3, Environment Variables REPROCESS = ‘YES’ and READ_IES = ‘YES’

#### Environment setup and file preparation

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

setenv YEAR 2008

setenv MONTH 10

setenv DAY 15

setenv HOUR 07

setenv DATE_1P6 $YEAR$MONTH$DAY$HOUR

setenv INSTANCE_1P6 Aqua-FM3-MODIS_Ed4Test-reproc-ies_000000.$DATE_1P6

setenv SCC_1P6 Aqua-FM3_Edition3_300300.20081015

source $CERESHOME/inversion/CER4.5-6.1P6/rcf/inversion-FM3-test3-env.csh

Copy the input files to appropriate locations:

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_MOA_CERES_GMAO-G5-Edition3-54_999999.2008101506 $InputArchive/MOA/CERES_GMAO-G5-Edition3-54/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_MOA_CERES_GMAO-G5-Edition3-54_999999.2008101512 $InputArchive/MOA/CERES_GMAO-G5-Edition3-54/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SSFB_Aqua-FM3-MODIS_SSIT_000000.2008101507 $InputArchive/SSFB/Aqua-FM3-MODIS_SSIT/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SSFA_Aqua-FM3-MODIS_SSIT_000000.2008101507 $InputArchive/SSFA/Aqua-FM3-MODIS_SSIT/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SSFA_Aqua-FM3-MODIS_SSIT_000000.2008101507.met $InputArchive/SSFA/Aqua-FM3-MODIS_SSIT/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_GQCI_Aqua-FM3-MODIS_SSIT_000000.2008101507 $InputArchive/GQCI/Aqua-FM3-MODIS_SSIT/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SCCD_$SCC_1P6 $InputArchive/SCCD/Aqua-FM3_Edition3/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SCCN_$SCC_1P6 $InputArchive/SCCN/Aqua-FM3_Edition3/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_MATCH-daily_Terra-Aqua-MODIS_Edition4_400400.20081015.nc $CERESHOME/inversion/data/MATCH-daily/Terra-Aqua-MODIS_Edition4/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/sorce_tsi_v15.txt.20140331 $CERESHOME/inversion/data/SORCE/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_IES_Aqua-FM3_Edition3_032040.2008101507 $InputArchive/IES/Aqua-FM3_Edition3/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_sibiMap_Aqua-MODIS_Edition4_400400.200810 $CERESHOME/inversion/data/sibiMap/Aqua-MODIS_Edition4/2008/10/

#### Execution

Execute the production script by typing the script name, CER4.5-6.1P6-SGE_Driver.pl, followed by the date and hour options and the cleanup option.

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

$CERESHOME/inversion/CER4.5-6.1P6/rcf/CER4.5-6.1P6-SGE_Driver.pl -date 20081015 -hour 07 -clean

The following file will be generated:

$CERESHOME/inversion/CER4.5-6.1P6/rcf/pcf/CER4.5-6.1P6_PCF_$INSTANCE_1P6

The submitted job can be monitored with the qstat command.

The most recently created sge_log file can be viewed to monitor progress of this job.  This will be the last file listed by the command:

ls -arlt $CERESHOME/inversion/sge_logs/CER4.5-6.1P6/CER4.5-6.1P6_$INSTANCE_1P6.o*

Output file generation test:

The script, list_4.5-6.1P6.pl, will list the files that were created during execution of the PGE:

$CERESHOME/inversion/CER4.5-6.1P6/rcf/list_4.5-6.1P6.pl $INSTANCE_1P6

Note:	If any file that should have been created is missing, then a message is written to the screen naming which file could not be found.

#### Exit Codes

All CER4.5-6.1P6 software terminates using the CERES defined EXIT CODES.  Successful completion is indicated by an exit code of 0.  This test should complete with an exit code of 0 for each of the executables.

#### Test Summary

Test Summary:

Total Run Time:	7:25 minutes

Memory:	5.7 G

Required Disk Space:	232 Megabytes

### Evaluation Procedures

When running the production script, run_4.5-6.1P6.pl, the system message, ’No match’, may be written to the screen.  This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

Remove input data:

rm $InputArchive/SSFB/Aqua-FM3-MODIS_SSIT/2008/10/CER_SSFB_Aqua-FM3-MODIS_SSIT_000000.2008101507

rm $InputArchive/SSFA/Aqua-FM3-MODIS_SSIT/2008/10/CER_SSFA_Aqua-FM3-MODIS_SSIT_000000.2008101507

rm $InputArchive/SSFA/Aqua-FM3-MODIS_SSIT/2008/10/CER_SSFA_Aqua-FM3-MODIS_SSIT_000000.2008101507.met

rm $InputArchive/GQCI/Aqua-FM3-MODIS_SSIT/2008/10/CER_GQCI_Aqua-FM3-MODIS_SSIT_000000.2008101507

rm $InputArchive/SCCD/Aqua-FM3_Edition3/2008/10/CER_SCCD_$SCC_1P6

rm $InputArchive/SCCN/Aqua-FM3_Edition3/2008/10/CER_SCCN_$SCC_1P6

rm $InputArchive/MOA/CERES_GMAO-G5-Edition3-54/2008/10/CER_MOA_CERES_GMAO-G5-Edition3-54_999999.2008101506

rm $InputArchive/MOA/CERES_GMAO-G5-Edition3-54/2008/10/CER_MOA_CERES_GMAO-G5-Edition3-54_999999.2008101512

rm $CERESHOME/inversion/data/MATCH-daily/Terra-Aqua-MODIS_Edition4/2008/10/CER_MATCH-daily_Terra-Aqua-MODIS_Edition4_400400.20081015.nc

rm $CERESHOME/inversion/data/SORCE/sorce_tsi_v15.txt.20140331

rm $InputArchive/IES/Aqua-FM3_Edition3/2008/10/CER_IES_Aqua-FM3_Edition3_032040.2008101507

rm $CERESHOME/inversion/data/sibiMap/Aqua-MODIS_Edition4/2008/10/CER_sibiMap_Aqua-MODIS_Edition4_400400.200810

#### Log and Status File Results and Metadata Evaluation

The Error and Status Log File, CER4.5-6.1P6_LogReport_$INSTANCE_1P6, is located in directory $CERESHOME/inversion/runlogs after CER4.5-6.1P6 has been executed.  Metadata files, which end in extension '.met', are located in the same directories as their corresponding output files after CER4.5-6.1P6 has been executed.

Compare the information contained in the log file with the expected contents of the Log Report file found in directory $CERESHOME/inversion/data_exp/CER4.5-6.1P6 and compare the metadata files with the expected contents of the files with the same names found in directory $CERESHOME/inversion/data_exp/CER4.5-6.1P6, using the following diff_4.5-6.1P6.pl script:

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

$CERESHOME/inversion/CER4.5-6.1P6/rcf/diff_4.5-6.1P6.pl $INSTANCE_1P6

The only differences between the files should be the production times and differences in the directory paths where the tests were run.

#### Execution of Comparison Software for the Main Processor

The evaluation software for the Subsystem Main Processor will perform a single test.  This test will compare all of the parameters on the binary SSF and the binary SSFA (if it exists) to the values in comparison files provided with the software delivery.

- The executable for the comparison software is not provided in the tar file.  It was created when all the software’s code was compiled.

To execute the comparison software for the binary SSF and binary SSFA, type the following commands:

cd $CERESHOME/inversion/test_suites/bin

run_compare_1p6 $INSTANCE_1P6

Two files will be created:

$CERESHOME/inversion/test_suites/results/CmpReport_$DATE_1P6

$CERESHOME/inversion/test_suites/results/CmpReportSSFA_$DATE_1P6

#### Evaluation of Comparison Software Output

This section provides the procedure for evaluating the output from the CER4.5-6.1P6 comparison software.

Examine the comparison reports files by typing:

cat $CERESHOME/inversion/test_suites/results/CmpReport_$DATE_1P6

cat $CERESHOME/inversion/test_suites/results/CmpReportSSFA_$DATE_1P6

The final line of these files will report the status of the comparison between the generated data and the expected output.

#### Evaluation of SSF HDF Product

This section provides the procedure for evaluating the output from the SSF HDF product produced by the test software.  The comparison software was compiled when all software was compiled in a previous step.  Execute the program by typing the following lines:

hdiff $CERESHOME/inversion/data/SSF/Aqua-FM3-MODIS_Ed4Test-reproc-ies/2008/10/CER_SSF_$INSTANCE_1P6 $CERESHOME/inversion/data_exp/CER4.5-6.1P6/CER_SSF_$INSTANCE_1P6

The executable, hdiff, compares each Vdata and each SDS on the SSF HDF output file.

The only differences between the two HDF output files should be the dates on Vfields: “SSF_DATE” on the “SSF_Header” Vdata and “CERPRODUCTIONDATETIME” on the “CERES_metadata” Vdata.  If CERESLIB has changed, the date may be different in the “LOCALVERSIONID” on the “CERES_metadata” Vdata. Differences in the third to sixth decimal places for the data fields are acceptable.

### Solutions to Possible Problems

- All output files are opened with Status = NEW in the CER4.5-6.1P6 software.  These files must be removed before rerunning these test procedures.  A script which removes PGE created files, cleanup_4.5-6.1P6.pl, is located in directory $CERESHOME/inversion/CER4.5-6.1P6/rcf.  To use the clean-up script:

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

$CERESHOME/inversion/CER4.5-6.1P6/rcf/cleanup_4.5-6.1P6.pl $DATE_1P6

Use the latest version of CERESlib.

Ignore the warnings received during compilation.

### Stand Alone Test Procedures for FM4, Environment variables:  REPROCESS = ‘NO’, READ_IES = ‘NO’ and PROD = ‘no’

#### Environment setup and file preparation

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

setenv YEAR 2008

setenv MONTH 10

setenv DAY 15

setenv HOUR 07

setenv DATE_1P6 $YEAR$MONTH$DAY$HOUR

setenv INSTANCE_1P6 Aqua-FM4-MODIS_SSIT-NoSW_000000.$DATE_1P6

setenv INSTANCE1_1P6 Aqua-FM4-MODIS_SSIT_000000.$DATE_1P6

setenv SCC_1P6 Aqua-FM4_Ed3-NoSW_300300.20081015

source $CERESHOME/inversion/CER4.5-6.1P6/rcf/inversion-FM4-test1-env.csh

Copy the input files to appropriate locations:

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_MOA_CERES_GMAO-G5-Edition3-54_999999.2008101506 $InputArchive/MOA/CERES_GMAO-G5-Edition3-54/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_MOA_CERES_GMAO-G5-Edition3-54_999999.2008101512 $InputArchive/MOA/CERES_GMAO-G5-Edition3-54/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SSFI_Aqua-FM4-MODIS_SSIT_000000.2008101507 $InputArchiveInt/SSF_Int/Aqua-FM4-MODIS_SSIT/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SSFAI_Aqua-FM4-MODIS_SSIT_000000.2008101507 $InputArchiveInt/SSF_Int/Aqua-FM4-MODIS_SSIT/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SSFAI_Aqua-FM4-MODIS_SSIT_000000.2008101507.met $InputArchiveInt/SSF_Int/Aqua-FM4-MODIS_SSIT/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_FQCI_Aqua-FM4-MODIS_SSIT_000000.2008101507 $InputArchiveInt/FQC/Aqua-FM4-MODIS_SSIT/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SCCD_$SCC_1P6 $InputArchive/SCCD/Aqua-FM4_Ed3-NoSW/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SCCN_$SCC_1P6 $InputArchive/SCCN/Aqua-FM4_Ed3-NoSW/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_MATCH-daily_Terra-Aqua-MODIS_Edition4_400400.20081015.nc $CERESHOME/inversion/data/MATCH-daily/Terra-Aqua-MODIS_Edition4/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/sorce_tsi_v15.txt.20140331 $CERESHOME/inversion/data/SORCE/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_sibiMap_Aqua-MODIS_Edition4_400400.200810 $CERESHOME/inversion/data/sibiMap/Aqua-MODIS_Edition4/2008/10/

#### Execution

Execute the production script by typing the script name, CER4.5-6.1P6-SGE_Driver.pl, followed by the date and hour options and the cleanup option.

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

$CERESHOME/inversion/CER4.5-6.1P6/rcf/CER4.5-6.1P6-SGE_Driver.pl -date 20081015 -hour 07 -clean

The following file will be generated:

$CERESHOME/inversion/CER4.5-6.1P6/rcf/pcf/CER4.5-6.1P6_PCF_$INSTANCE_1P6

The submitted job can be monitored with the qstat command.

The most recently created sge_log file can be viewed to monitor progress of this job.  This will be the last file listed by the command:

ls -arlt $CERESHOME/inversion/sge_logs/CER4.5-6.1P6/CER4.5-6.1P6_$INSTANCE_1P6.o*

Output file generation test:

The script, list_4.5-6.1P6.pl, will list the files that were created during execution of the PGE:

$CERESHOME/inversion/CER4.5-6.1P6/rcf/list_4.5-6.1P6.pl $INSTANCE_1P6

Note:	If any file that should have been created is missing, then a message is written to the screen naming which file could not be found.

#### Exit Codes

All CER4.5-6.1P6 software terminates using the CERES defined EXIT CODES.  Successful completion is indicated by an exit code of 0.  This test should complete with an exit code of 0 for each of the executables.

#### Test Summary

Test Summary:

Total Run Time:	8:08 minutes

Memory:	5.7 G

Required Disk Space:	232 Megabytes

### Evaluation Procedures

When running the production script, run_4.5-6.1P6.pl, the system message, ’No match’, may be written to the screen.  This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

Remove input data:

rm $InputArchiveInt/SSF_Int/Aqua-FM4-MODIS_SSIT/2008/10/CER_SSFI_$INSTANCE1_1P6

rm $InputArchiveInt/SSF_Int/Aqua-FM4-MODIS_SSIT/2008/10/CER_SSFAI_$INSTANCE1_1P6

rm $InputArchiveInt/SSF_Int/Aqua-FM4-MODIS_SSIT/2008/10/CER_SSFAI_$INSTANCE1_1P6.met

rm $InputArchiveInt/FQC/Aqua-FM4-MODIS_SSIT/2008/10/CER_FQCI_$INSTANCE1_1P6

rm $InputArchive/SCCD/Aqua-FM4_Ed3-NoSW/2008/10/CER_SCCD_$SCC_1P6

rm $InputArchive/SCCN/Aqua-FM4_Ed3-NoSW/2008/10/CER_SCCN_$SCC_1P6

rm $InputArchive/MOA/CERES_GMAO-G5-Edition3-54/2008/10/CER_MOA_CERES_GMAO-G5-Edition3-54_999999.2008101506

rm $InputArchive/MOA/CERES_GMAO-G5-Edition3-54/2008/10/CER_MOA_CERES_GMAO-G5-Edition3-54_999999.2008101512

rm $CERESHOME/inversion/data/MATCH-daily/Terra-Aqua-MODIS_Edition4/2008/10/CER_MATCH-daily_Terra-Aqua-MODIS_Edition4_400400.20081015.nc

rm $CERESHOME/inversion/data/SORCE/sorce_tsi_v15.txt.20140331

rm $CERESHOME/inversion/data/sibiMap/Aqua-MODIS_Edition4/2008/10/CER_sibiMap_Aqua-MODIS_Edition4_400400.200810

#### Log and Status File Results and Metadata Evaluation

The Error and Status Log File, CER4.5-6.1P6_LogReport_$INSTANCE_1P6, is located in directory $CERESHOME/inversion/runlogs after CER4.5-6.1P6 has been executed.  Metadata files, which end in extension '.met', are located in the same directories as their corresponding output files after CER4.5-6.1P6 has been executed

Compare the information contained in the log file with the expected contents of the Log Report file found in directory $CERESHOME/inversion/data_exp/CER4.5-6.1P6 and compare the metadata files with the expected contents of the files with the same names found in directory $CERESHOME/inversion/data_exp/CER4.5-6.1P6, using the following diff_4.5-6.1P6.pl script:

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

$CERESHOME/inversion/CER4.5-6.1P6/rcf/diff_4.5-6.1P6.pl $INSTANCE_1P6

The only differences between the files should be the production times and differences in the directory paths where the tests were run.

#### Execution of Comparison Software for the Main Processor

The evaluation software for the Subsystem Main Processor will perform a single test.  This test will compare all of the parameters on the binary SSF and the binary SSFA (if it exists) to the values in comparison files provided with the software delivery.

- The executable for the comparison software is not provided in the tar file.  It was created when all the software’s code was compiled.

To execute the comparison software for the binary SSF and binary SSFA, type the following commands:

cd $CERESHOME/inversion/test_suites/bin

run_compare_1p6 $INSTANCE_1P6

Two files will be created:

$CERESHOME/inversion/test_suites/results/CmpReport_$DATE_1P6

$CERESHOME/inversion/test_suites/results/CmpReportSSFA_$DATE_1P6

#### Evaluation of Comparison Software Output

This section provides the procedure for evaluating the output from the CER4.5-6.1P6 comparison software.

Examine the comparison reports files by typing:

cat $CERESHOME/inversion/test_suites/results/CmpReport_$DATE_1P6

cat $CERESHOME/inversion/test_suites/results/CmpReportSSFA_$DATE_1P6

The final line of these files will report the status of the comparison between the generated data and the expected output.

#### Evaluation of SSF HDF Product

This section provides the procedure for evaluating the output from the SSF HDF product produced by the test software.  The comparison software was compiled when all software was compiled in a previous step.  Execute the program by typing the following lines:

hdiff $CERESHOME/inversion/data/SSF/Aqua-FM4-MODIS_SSIT-NoSW/2008/10/CER_SSF_$INSTANCE_1P6 $CERESHOME/inversion/data_exp/CER4.5-6.1P6/CER_SSF_$INSTANCE_1P6

The executable, hdiff, compares each Vdata and each SDS on the SSF HDF output file.

The only differences between the two HDF output files should be the dates on Vfields: “SSF_DATE” on the “SSF_Header” Vdata and “CERPRODUCTIONDATETIME” on the “CERES_metadata” Vdata.  If CERESLIB has changed, the date may be different in the “LOCALVERSIONID” on the “CERES_metadata” Vdata. Differences in the third to sixth decimal places for the data fields are acceptable.

### Solutions to Possible Problems

- All output files are opened with Status = NEW in the CER4.5-6.1P6 software.  These files must be removed before rerunning these test procedures.  A script which removes PGE created files, cleanup_4.5-6.1P6.pl, is located in directory $CERESHOME/inversion/CER4.5-6.1P6/rcf.  To use the clean-up script:

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

$CERESHOME/inversion/CER4.5-6.1P6/rcf/cleanup_4.5-6.1P6.pl $DATE_1P6

Use the latest version of CERESlib.

Ignore the warnings received during compilation.

### Stand Alone, command line, Test Procedures for FM4, Environment Variables REPROCESS = ‘YES’, READ_IES = ‘NO’ and PROD = ‘no’

#### Environment setup and file preparation

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

setenv YEAR 2008

setenv MONTH 10

setenv DAY 15

setenv HOUR 07

setenv DATE_1P6 $YEAR$MONTH$DAY$HOUR

setenv INSTANCE_1P6 Aqua-FM4-MODIS_Ed4Test-NoSW-reproc_000000.$DATE_1P6

setenv SCC_1P6 Aqua-FM4_Ed3-NoSW_300300.20081015

source $CERESHOME/inversion/CER4.5-6.1P6/rcf/inversion-FM4-test2-env.csh

Copy the input files to appropriate locations:

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_MOA_CERES_GMAO-G5-Edition3-54_999999.2008101506 $InputArchive/MOA/CERES_GMAO-G5-Edition3-54/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_MOA_CERES_GMAO-G5-Edition3-54_999999.2008101512 $InputArchive/MOA/CERES_GMAO-G5-Edition3-54/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SSFB_Aqua-FM4-MODIS_SSIT-NoSW_000000.2008101507 $InputArchive/SSFB/Aqua-FM4-MODIS_SSIT-NoSW/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SSFA_Aqua-FM4-MODIS_SSIT-NoSW_000000.2008101507 $InputArchive/SSFA/Aqua-FM4-MODIS_SSIT-NoSW/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SSFA_Aqua-FM4-MODIS_SSIT-NoSW_000000.2008101507.met $InputArchive/SSFA/Aqua-FM4-MODIS_SSIT-NoSW/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_GQCI_Aqua-FM4-MODIS_SSIT-NoSW_000000.2008101507 $InputArchive/GQCI/Aqua-FM4-MODIS_SSIT-NoSW/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SCCD_$SCC_1P6 $InputArchive/SCCD/Aqua-FM4_Ed3-NoSW/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SCCN_$SCC_1P6 $InputArchive/SCCN/Aqua-FM4_Ed3-NoSW/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_MATCH-daily_Terra-Aqua-MODIS_Edition4_400400.20081015.nc $CERESHOME/inversion/data/MATCH-daily/Terra-Aqua-MODIS_Edition4/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/sorce_tsi_v15.txt.20140331 $CERESHOME/inversion/data/SORCE/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_sibiMap_Aqua-MODIS_Edition4_400400.200810 $CERESHOME/inversion/data/sibiMap/Aqua-MODIS_Edition4/2008/10/

#### Execution

Execute the production script by typing the script name, CER4.5-6.1P6-SGE_Driver.pl, followed by the date and hour options and the cleanup option.

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

$CERESHOME/inversion/CER4.5-6.1P6/rcf/CER4.5-6.1P6-SGE_Driver.pl -date 20081015 -hour 07 -clean

The following file will be generated:

$CERESHOME/inversion/CER4.5-6.1P6/rcf/pcf/CER4.5-6.1P6_PCF_$INSTANCE_1P6

The submitted job can be monitored with the qstat command.

The most recently created sge_log file can be viewed to monitor progress of this job.  This will be the last file listed by the command:

ls -arlt $CERESHOME/inversion/sge_logs/CER4.5-6.1P6/CER4.5-6.1P6_$INSTANCE_1P6.o*

Output file generation test:

The script, list_4.5-6.1P6.pl, will list the files that were created during execution of the PGE:

$CERESHOME/inversion/CER4.5-6.1P6/rcf/list_4.5-6.1P6.pl $INSTANCE_1P6

Note:	If any file that should have been created is missing, then a message is written to the screen naming which file could not be found.

#### Exit Codes

All CER4.5-6.1P6 software terminates using the CERES defined EXIT CODES.  Successful completion is indicated by an exit code of 0.  This test should complete with an exit code of 0 for each of the executables.

#### Test Summary

Test Summary:

Total Run Time:	6:27 minutes

Memory:	5.7 G

Required Disk Space:	232 Megabytes

### Evaluation Procedures

When running the production script, run_4.5-6.1P6.pl, the system message, ’No match’, may be written to the screen.  This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

Remove input data:

rm $InputArchive/SSFB/Aqua-FM4-MODIS_SSIT-NoSW/2008/10/CER_SSFB_Aqua-FM4-MODIS_SSIT-NoSW_000000.2008101507

rm $InputArchive/SSFA/Aqua-FM4-MODIS_SSIT-NoSW/2008/10/CER_SSFA_Aqua-FM4-MODIS_SSIT-NoSW_000000.2008101507

rm $InputArchive/SSFA/Aqua-FM4-MODIS_SSIT-NoSW/2008/10/CER_SSFA_Aqua-FM4-MODIS_SSIT-NoSW_000000.2008101507.met

rm $InputArchive/GQCI/Aqua-FM4-MODIS_SSIT-NoSW/2008/10/CER_GQCI_Aqua-FM4-MODIS_SSIT-NoSW_000000.2008101507

rm $InputArchive/SCCD/Aqua-FM4_Ed3-NoSW/2008/10/CER_SCCD_$SCC_1P6

rm $InputArchive/SCCN/Aqua-FM4_Ed3-NoSW/2008/10/CER_SCCN_$SCC_1P6

rm $InputArchive/MOA/CERES_GMAO-G5-Edition3-54/2008/10/CER_MOA_CERES_GMAO-G5-Edition3-54_999999.2008101506

rm $InputArchive/MOA/CERES_GMAO-G5-Edition3-54/2008/10/CER_MOA_CERES_GMAO-G5-Edition3-54_999999.2008101512

rm $CERESHOME/inversion/data/MATCH-daily/Terra-Aqua-MODIS_Edition4/2008/10/CER_MATCH-daily_Terra-Aqua-MODIS_Edition4_400400.20081015.nc

rm $CERESHOME/inversion/data/SORCE/sorce_tsi_v15.txt.20140331

rm $CERESHOME/inversion/data/sibiMap/Aqua-MODIS_Edition4/2008/10/CER_sibiMap_Aqua-MODIS_Edition4_400400.200810

#### Log and Status File Results and Metadata Evaluation

The Error and Status Log File, CER4.5-6.1P6_LogReport_$INSTANCE_1P6, is located in directory $CERESHOME/inversion/runlogs after CER4.5-6.1P6 has been executed.  Metadata files, which end in extension '.met', are located in the same directories as their corresponding output files after CER4.5-6.1P6 has been executed

Compare the information contained in the log file with the expected contents of the Log Report file found in directory $CERESHOME/inversion/data_exp/CER4.5-6.1P6 and compare the metadata files with the expected contents of the files with the same names found in directory

$CERESHOME/inversion/data_exp/CER4.5-6.1P6, using the following diff_4.5-6.1P6.pl script:

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

$CERESHOME/inversion/CER4.5-6.1P6/rcf/diff_4.5-6.1P6.pl $INSTANCE_1P6

The only differences between the files should be the production times and differences in the directory paths where the tests were run.

#### Execution of Comparison Software for the Main Processor

The evaluation software for the Subsystem Main Processor will perform a single test.  This test will compare all of the parameters on the binary SSF and the binary SSFA (if it exists) to the values in comparison files provided with the software delivery.

- The executable for the comparison software is not provided in the tar file.  It was created when all the software’s code was compiled.

To execute the comparison software for the binary SSF and binary SSFA, type the following commands:

cd $CERESHOME/inversion/test_suites/bin

run_compare_1p6 $INSTANCE_1P6

Two files will be created:

$CERESHOME/inversion/test_suites/results/CmpReport_$DATE_1P6

$CERESHOME/inversion/test_suites/results/CmpReportSSFA_$DATE_1P6

#### Evaluation of Comparison Software Output

This section provides the procedure for evaluating the output from the CER4.5-6.1P6 comparison software.

Examine the comparison reports files by typing:

cat $CERESHOME/inversion/test_suites/results/CmpReport_$DATE_1P6

cat $CERESHOME/inversion/test_suites/results/CmpReportSSFA_$DATE_1P6

The final line of these files will report the status of the comparison between the generated data and the expected output.

#### Evaluation of SSF HDF Product

This section provides the procedure for evaluating the output from the SSF HDF product produced by the test software.  The comparison software was compiled when all software was compiled in a previous step.  Execute the program by typing the following lines:

hdiff $CERESHOME/inversion/data/SSF/Aqua-FM4-MODIS_Ed4Test-NoSW-reproc/2008/10/CER_SSF_$INSTANCE_1P6 $CERESHOME/inversion/data_exp/CER4.5-6.1P6/CER_SSF_$INSTANCE_1P6

The executable, hdiff, compares each Vdata and each SDS on the SSF HDF output file.

The only differences between the two HDF output files should be the dates on Vfields: “SSF_DATE” on the “SSF_Header” Vdata and “CERPRODUCTIONDATETIME” on the “CERES_metadata” Vdata.  If CERESLIB has changed, the date may be different in the “LOCALVERSIONID” on the “CERES_metadata” Vdata. Differences in the third to sixth decimal places for the data fields are acceptable.

### Solutions to Possible Problems

- All output files are opened with Status = NEW in the CER4.5-6.1P6 software.  These files must be removed before rerunning these test procedures.  A script which removes PGE created files, cleanup_4.5-6.1P6.pl, is located in directory $CERESHOME/inversion/CER4.5-6.1P6/rcf.  To use the clean-up script:

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

$CERESHOME/inversion/CER4.5-6.1P6/rcf/cleanup_4.5-6.1P6.pl $DATE_1P6

Use the latest version of CERESlib.

Ignore the warnings received during compilation.

### Stand Alone, command line, Test Procedures for FM4, Environment Variables REPROCESS = ‘YES’ and READ_IES = ‘YES’

#### Environment setup and file preparation

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

setenv YEAR 2008

setenv MONTH 10

setenv DAY 15

setenv HOUR 07

setenv DATE_1P6 $YEAR$MONTH$DAY$HOUR

setenv INSTANCE_1P6 Aqua-FM4-MODIS_Ed4Test-NoSW-reproc-ies_000000.$DATE_1P6

setenv SCC_1P6 Aqua-FM4_Ed3-NoSW_300300.20081015

source $CERESHOME/inversion/CER4.5-6.1P6/rcf/inversion-FM4-test3-env.csh

Copy the input files to appropriate locations:

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_MOA_CERES_GMAO-G5-Edition3-54_999999.2008101506 $InputArchive/MOA/CERES_GMAO-G5-Edition3-54/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_MOA_CERES_GMAO-G5-Edition3-54_999999.2008101512 $InputArchive/MOA/CERES_GMAO-G5-Edition3-54/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SSFB_Aqua-FM4-MODIS_SSIT-NoSW_000000.2008101507 $InputArchive/SSFB/Aqua-FM4-MODIS_SSIT-NoSW/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SSFA_Aqua-FM4-MODIS_SSIT-NoSW_000000.2008101507 $InputArchive/SSFA/Aqua-FM4-MODIS_SSIT-NoSW/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SSFA_Aqua-FM4-MODIS_SSIT-NoSW_000000.2008101507.met $InputArchive/SSFA/Aqua-FM4-MODIS_SSIT-NoSW/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_GQCI_Aqua-FM4-MODIS_SSIT-NoSW_000000.2008101507 $InputArchive/GQCI/Aqua-FM4-MODIS_SSIT-NoSW/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SCCD_$SCC_1P6 $InputArchive/SCCD/Aqua-FM4_Ed3-NoSW/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_SCCN_$SCC_1P6 $InputArchive/SCCN/Aqua-FM4_Ed3-NoSW/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_MATCH-daily_Terra-Aqua-MODIS_Edition4_400400.20081015.nc $CERESHOME/inversion/data/MATCH-daily/Terra-Aqua-MODIS_Edition4/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/sorce_tsi_v15.txt.20140331 $CERESHOME/inversion/data/SORCE/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_IES_Aqua-FM4_Ed3-NoSW_032040.2008101507 $InputArchive/IES/Aqua-FM4_Ed3-NoSW/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P6/CER_sibiMap_Aqua-MODIS_Edition4_400400.200810 $CERESHOME/inversion/data/sibiMap/Aqua-MODIS_Edition4/2008/10/

#### Execution

Execute the production script by typing the script name, CER4.5-6.1P6-SGE_Driver.pl, followed by the date and hour options and the cleanup option.

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

$CERESHOME/inversion/CER4.5-6.1P6/rcf/CER4.5-6.1P6-SGE_Driver.pl -date 20081015 -hour 07 -clean

The following file will be generated:

$CERESHOME/inversion/CER4.5-6.1P6/rcf/pcf/CER4.5-6.1P6_PCF_$INSTANCE_1P6

The submitted job can be monitored with the qstat command.

The most recently created sge_log file can be viewed to monitor progress of this job.  This will be the last file listed by the command:

ls -arlt $CERESHOME/inversion/sge_logs/CER4.5-6.1P6/CER4.5-6.1P6_$INSTANCE_1P6.o*

Output file generation test:

The script, list_4.5-6.1P6.pl, will list the files that were created during execution of the PGE:

$CERESHOME/inversion/CER4.5-6.1P6/rcf/list_4.5-6.1P6.pl $INSTANCE_1P6

Note:	If any file that should have been created is missing, then a message is written to the screen naming which file could not be found.

#### Exit Codes

All CER4.5-6.1P6 software terminates using the CERES defined EXIT CODES.  Successful completion is indicated by an exit code of 0.  This test should complete with an exit code of 0 for each of the executables.

#### Test Summary

Test Summary:

Total Run Time:	6:12 minutes

Memory:	5.7 G

Required Disk Space:	232 Megabytes

### Evaluation Procedures

When running the production script, run_4.5-6.1P6.pl, the system message, ’No match’, may be written to the screen.  This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

Remove input data:

rm $InputArchive/SSFB/Aqua-FM4-MODIS_SSIT-NoSW/2008/10/CER_SSFB_Aqua-FM4-MODIS_SSIT-NoSW_000000.2008101507

rm $InputArchive/SSFA/Aqua-FM4-MODIS_SSIT-NoSW/2008/10/CER_SSFA_Aqua-FM4-MODIS_SSIT-NoSW_000000.2008101507

rm $InputArchive/SSFA/Aqua-FM4-MODIS_SSIT-NoSW/2008/10/CER_SSFA_Aqua-FM4-MODIS_SSIT-NoSW_000000.2008101507.met

rm $InputArchive/GQCI/Aqua-FM4-MODIS_SSIT-NoSW/2008/10/CER_GQCI_Aqua-FM4-MODIS_SSIT-NoSW_000000.2008101507

rm $InputArchive/SCCD/Aqua-FM4_Ed3-NoSW/2008/10/CER_SCCD_$SCC_1P6

rm $InputArchive/SCCN/Aqua-FM4_Ed3-NoSW/2008/10/CER_SCCN_$SCC_1P6

rm $InputArchive/MOA/CERES_GMAO-G5-Edition3-54/2008/10/CER_MOA_CERES_GMAO-G5-Edition3-54_999999.2008101506

rm $InputArchive/MOA/CERES_GMAO-G5-Edition3-54/2008/10/CER_MOA_CERES_GMAO-G5-Edition3-54_999999.2008101512

rm $CERESHOME/inversion/data/MATCH-daily/Terra-Aqua-MODIS_Edition4/2008/10/CER_MATCH-daily_Terra-Aqua-MODIS_Edition4_400400.20081015.nc

rm $CERESHOME/inversion/data/SORCE/sorce_tsi_v15.txt.20140331

rm $InputArchive/IES/Aqua-FM4_Ed3-NoSW/2008/10/CER_IES_Aqua-FM4_Ed3-NoSW_032040.2008101507

rm $CERESHOME/inversion/data/sibiMap/Aqua-MODIS_Edition4/2008/10/CER_sibiMap_Aqua-MODIS_Edition4_400400.200810

#### Log and Status File Results and Metadata Evaluation

The Error and Status Log File, CER4.5-6.1P6_LogReport_$INSTANCE_1P6, is located in directory $CERESHOME/inversion/runlogs after CER4.5-6.1P6 has been executed.  Metadata files, which end in extension '.met', are located in the same directories as their corresponding output files after CER4.5-6.1P6 has been executed.

Compare the information contained in the log file with the expected contents of the Log Report file found in directory $CERESHOME/inversion/data_exp/CER4.5-6.1P6 and compare the metadata files with the expected contents of the files with the same names found in directory $CERESHOME/inversion/data_exp/CER4.5-6.1P6, using the following diff_4.5-6.1P6.pl script:

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

$CERESHOME/inversion/CER4.5-6.1P6/rcf/diff_4.5-6.1P6.pl $INSTANCE_1P6

The only differences between the files should be the production times and differences in the directory paths where the tests were run.

#### Execution of Comparison Software for the Main Processor

The evaluation software for the Subsystem Main Processor will perform a single test.  This test will compare all of the parameters on the binary SSF and the binary SSFA (if it exists) to the values in comparison files provided with the software delivery.

- The executable for the comparison software is not provided in the tar file.  It was created when all the software’s code was compiled.

To execute the comparison software for the binary SSF and binary SSFA, type the following commands:

cd $CERESHOME/inversion/test_suites/bin

run_compare_1p6 $INSTANCE_1P6

Two files will be created:

$CERESHOME/inversion/test_suites/results/CmpReport_$DATE_1P6

$CERESHOME/inversion/test_suites/results/CmpReportSSFA_$DATE_1P6

#### Evaluation of Comparison Software Output

This section provides the procedure for evaluating the output from the CER4.5-6.1P6 comparison software.

Examine the comparison reports files by typing:

cat $CERESHOME/inversion/test_suites/results/CmpReport_$DATE_1P6

cat $CERESHOME/inversion/test_suites/results/CmpReportSSFA_$DATE_1P6

The final line of these files will report the status of the comparison between the generated data and the expected output.

#### Evaluation of SSF HDF Product

This section provides the procedure for evaluating the output from the SSF HDF product produced by the test software.  The comparison software was compiled when all software was compiled in a previous step.  Execute the program by typing the following lines:

hdiff $CERESHOME/inversion/data/SSF/Aqua-FM4-MODIS_Ed4Test-NoSW-reproc-ies/2008/10/CER_SSF_$INSTANCE_1P6 $CERESHOME/inversion/data_exp/CER4.5-6.1P6/CER_SSF_$INSTANCE_1P6

The executable, hdiff, compares each Vdata and each SDS on the SSF HDF output file.

The only differences between the two HDF output files should be the dates on Vfields: “SSF_DATE” on the “SSF_Header” Vdata and “CERPRODUCTIONDATETIME” on the “CERES_metadata” Vdata.  If CERESLIB has changed, the date may be different in the “LOCALVERSIONID” on the “CERES_metadata” Vdata. Differences in the third to sixth decimal places for the data fields are acceptable.

### Solutions to Possible Problems

- All output files are opened with Status = NEW in the CER4.5-6.1P6 software.  These files must be removed before rerunning these test procedures.  A script which removes PGE created files, cleanup_4.5-6.1P6.pl, is located in directory $CERESHOME/inversion/CER4.5-6.1P6/rcf.  To use the clean-up script:

cd $CERESHOME/inversion/CER4.5-6.1P6/rcf

$CERESHOME/inversion/CER4.5-6.1P6/rcf/cleanup_4.5-6.1P6.pl $DATE_1P6

Use the latest version of CERESlib.

Ignore the warnings received during compilation.

## CER4_5-6.1P7 Main and Post Processors for S-NPP Processing

### Stand Alone Test Procedures for FM5, Environment variables:  REPROCESS = ‘NO’, READ_IES = ‘NO’ and PROD = ‘no’

#### Environment setup and file preparation

cd $CERESHOME/inversion/CER4.5-6.1P7/rcf

setenv YEAR 2012

setenv MONTH 02

setenv DAY 08

setenv HOUR 15

setenv DATE_1P7 $YEAR$MONTH$DAY$HOUR

setenv INSTANCE_1P7 NPP-FM5-VIIRS_SSIT_000000.$DATE_1P7

source $CERESHOME/inversion/CER4.5-6.1P7/rcf/inversion-FM5-test1-env.csh

Copy the input files to appropriate locations. Since there are not Spectral Calibration files available for this test, there are not any copied and PS4_7=DefaultSCC is set in the environment script.:

cp $CERESHOME/inversion/data/input/CER4.5-6.1P7/CER_MOA_CERES_DAO-G5-CERES_020033.2012020812 $InputArchive/MOA/CERES_DAO-G5-CERES/2012/02/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P7/CER_MOA_CERES_DAO-G5-CERES_020033.2012020818 $InputArchive/MOA/CERES_DAO-G5-CERES/2012/02/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P7/CER_SSFI_NPP-FM5-VIIRS_SSIT_000000.2012020815 $InputArchiveInt/SSF_Int/NPP-FM5-VIIRS_SSIT/2012/02/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P7/CER_SSFAI_NPP-FM5-VIIRS_SSIT_000000.2012020815 $InputArchiveInt/SSF_Int/NPP-FM5-VIIRS_SSIT/2012/02/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P7/CER_SSFAI_NPP-FM5-VIIRS_SSIT_000000.2012020815.met $InputArchiveInt/SSF_Int/NPP-FM5-VIIRS_SSIT/2012/02/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P7/CER_FQCI_NPP-FM5-VIIRS_SSIT_000000.2012020815 $InputArchiveInt/FQC/NPP-FM5-VIIRS_SSIT/2012/02/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P7/CER_MATCH-daily_Terra-Aqua-MODIS_Edition4_400400.20120208.nc $CERESHOME/inversion/data/MATCH-daily/Terra-Aqua-MODIS_Edition4/2012/02/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P7/CER_sibiMap_NPP-VIIRS_Edition4_400400.201202 $CERESHOME/inversion/data/sibiMap/NPP-VIIRS_Edition4/2012/02/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P7/sorce_tsi_v15.txt.20140331 $CERESHOME/inversion/data/SORCE/

#### Execution

Execute the production script by typing the script name, CER4.5-6.1P7-SGE_Driver.pl, followed by the date and hour options, the cleanup option and the platform option selecting either P6, P7, x86, or x86-flex.

cd $CERESHOME/inversion/CER4.5-6.1P7/rcf

$CERESHOME/inversion/CER4.5-6.1P7/rcf/CER4.5-6.1P7-SGE_Driver.pl -date 20120208 -hour 15 -clean -platform p6/p7/x86/x86-flex

The following file will be generated:

$CERESHOME/inversion/CER4.5-6.1P7/rcf/pcf/CER4.5-6.1P7_PCF_$INSTANCE_1P7

The submitted job can be monitored with the qstat command.

The most recently created sge_log file can be viewed to monitor progress of this job.  This will be the last file listed by the command:

ls -arlt $CERESHOME/inversion/sge_logs/CER4.5-6.1P7/CER4.5-6.1P7_$INSTANCE_1P7.o*

Output file generation test:

The script, list_4.5-6.1P7.pl, will list the files that were created during execution of the PGE:

$CERESHOME/inversion/CER4.5-6.1P7/rcf/list_4.5-6.1P7.pl $INSTANCE_1P7

Note:	If any file that should have been created is missing, then a message is written to the screen naming which file could not be found.

#### Exit Codes

All CER4.5-6.1P7 software terminates using the CERES defined EXIT CODES.  Successful completion is indicated by an exit code of 0.  This test should complete with an exit code of 0 for each of the executables.

#### Test Summary

Test Summary:

Total Run Time:	6:24 minutes

Memory:	5.7 G

Required Disk Space:	232 Megabytes

### Evaluation Procedures

When running the production script, run_4.5-6.1P7.pl, the system message, ’No match’, may be written to the screen.  This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

Remove input data:

rm $InputArchiveInt/SSF_Int/NPP-FM5-VIIRS_SSIT/2012/02/CER_SSFI_$INSTANCE_1P7

rm $InputArchiveInt/SSF_Int/NPP-FM5-VIIRS_SSIT/2012/02/CER_SSFAI_$INSTANCE_1P7

rm $InputArchiveInt/SSF_Int/NPP-FM5-VIIRS_SSIT/2012/02/CER_SSFAI_$INSTANCE_1P7.met

rm $InputArchiveInt/FQC/NPP-FM5-VIIRS_SSIT/2012/02/CER_FQCI_$INSTANCE_1P7

rm $InputArchive/MOA/CERES_DAO-G5-CERES/2012/02/CER_MOA_CERES_DAO-G5-CERES_020033.2012020812

rm $InputArchive/MOA/CERES_DAO-G5-CERES/2012/02/CER_MOA_CERES_DAO-G5-CERES_020033.2012020818

rm $CERESHOME/inversion/data/MATCH-daily/Terra-Aqua-MODIS_Edition4/2012/02/CER_MATCH-daily_Terra-Aqua-MODIS_Edition4_400400.20120208.nc

rm $CERESHOME/inversion/data/sibiMap/NPP-VIIRS_Edition4/2012/02/CER_sibiMap_NPP-VIIRS_Edition4_400400.201202

rm $CERESHOME/inversion/data/SORCE/sorce_tsi_v15.txt.20140331

#### Log and Status File Results and Metadata Evaluation

The Error and Status Log File, CER4.5-6.1P7_LogReport_$INSTANCE_1P7, is located in directory $CERESHOME/inversion/runlogs after CER4.5-6.1P7 has been executed.  Metadata files, which end in extension '.met', are located in the same directories as their corresponding output files after CER4.5-6.1P7 has been executed

Compare the information contained in the log file with the expected contents of the Log Report file found in directory $CERESHOME/inversion/data_exp/CER4.5-6.1P7 and compare the metadata files with the expected contents of the files with the same names found in directory $CERESHOME/inversion/data_exp/CER4.5-6.1P7, using the following diff_4.5-6.1P7.pl script:

cd $CERESHOME/inversion/CER4.5-6.1P7/rcf

$CERESHOME/inversion/CER4.5-6.1P7/rcf/diff_4.5-6.1P7.pl $INSTANCE_1P7

The only differences between the files should be the production times and differences in the directory paths where the tests were run.

#### Execution of Comparison Software for the Main Processor

The evaluation software for the Subsystem Main Processor will perform a single test.  This test will compare all of the parameters on the binary SSF and the binary SSFA (if it exists) to the values in comparison files provided with the software delivery.

- The executable for the comparison software is not provided in the tar file.  It was created when all the software’s code was compiled.

To execute the comparison software for the binary SSF and binary SSFA, type the following commands:

cd $CERESHOME/inversion/test_suites/bin

run_compare_1p7 $INSTANCE_1P7

Two files will be created:

$CERESHOME/inversion/test_suites/results/CmpReport_$DATE_1P7

$CERESHOME/inversion/test_suites/results/CmpReportarSSFA_$DATE_1P7

#### Evaluation of Comparison Software Output

This section provides the procedure for evaluating the output from the CER4.5-6.1P7 comparison software.

Examine the comparison reports files by typing:

cat $CERESHOME/inversion/test_suites/results/CmpReport_$DATE_1P7

cat $CERESHOME/inversion/test_suites/results/CmpReportSSFA_$DATE_1P7

The final line of these files will report the status of the comparison between the generated data and the expected output.

#### Evaluation of SSF HDF Product

This section provides the procedure for evaluating the output from the SSF HDF product produced by the test software.  The comparison software was compiled when all software was compiled in a previous step.  Execute the program by typing the following lines:

hdiff $CERESHOME/inversion/data/SSF/NPP-FM5-VIIRS_SSIT/2012/02/CER_SSF_$INSTANCE_1P7 $CERESHOME/inversion/data_exp/CER4.5-6.1P7/CER_SSF_$INSTANCE_1P7

The executable, hdiff, compares each Vdata and each SDS on the SSF HDF output file.

The main purpose of the hdiff command is to verify that the HDF converter worked correctly.  If the status from the "Evaluation of Comparison Software Output" section reports that it was successful, then the HDF file is not likely to have a major issue since it is created from the successfully compared data files.  Watch the screen as any results scroll by.  Presence of any major issues should be obvious as there would be many differences large enough to catch the eye.  Differences in the third to sixth decimal places for the data fields are acceptable and expected due to rounding differences between P6 and x86 resulting in different paths through the Inversion software.

The only other differences between the two HDF output files should be the dates on Vfields:  “SSF_DATE” on the “SSF_Header” Vdata and “CERPRODUCTIONDATETIME” on the “CERES_metadata” Vdata.  If CERESLIB has changed, the date may be different in the “LOCALVERSIONID” on the “CERES_metadata” Vdata.

### Solutions to Possible Problems

- All output files are opened with Status = NEW in the CER4.5-6.1P7 software.  These files must be removed before rerunning these test procedures.  A script which removes PGE created files, cleanup_4.5-6.1P7.pl, is located in directory $CERESHOME/inversion/CER4.5-6.1P7/rcf.  To use the clean-up script:

cd $CERESHOME/inversion/CER4.5-6.1P7/rcf

$CERESHOME/inversion/CER4.5-6.1P7/rcf/cleanup_4.5-6.1P7.pl $DATE_1P7

Use the latest version of CERESlib.

Ignore the warnings received during compilation.

### Stand Alone, command line, Test Procedures for FM5, Environment Variables REPROCESS = ‘YES’, READ_IES = ‘NO’ and PROD = ‘no’

#### Environment setup and file preparation

cd $CERESHOME/inversion/CER4.5-6.1P7/rcf

setenv YEAR 2012

setenv MONTH 02

setenv DAY 08

setenv HOUR 15

setenv DATE_1P7 $YEAR$MONTH$DAY$HOUR

setenv INSTANCE_1P7 NPP-FM5-VIIRS_SSIT-reproc_000000.$DATE_1P7

source $CERESHOME/inversion/CER4.5-6.1P7/rcf/inversion-FM5-test2-env.csh

Copy the input files to appropriate locations:

cp $CERESHOME/inversion/data/input/CER4.5-6.1P7/CER_MOA_CERES_DAO-G5-CERES_020033.2012020812 $InputArchive/MOA/CERES_DAO-G5-CERES/2012/02/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P7/CER_MOA_CERES_DAO-G5-CERES_020033.2012020818 $InputArchive/MOA/CERES_DAO-G5-CERES/2012/02/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P7/CER_SSFB_NPP-FM5-VIIRS_SSIT_000000.2012020815 $InputArchive/SSFB/NPP-FM5-VIIRS_SSIT/2012/02/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P7/CER_SSFA_NPP-FM5-VIIRS_SSIT_000000.2012020815 $InputArchive/SSFA/NPP-FM5-VIIRS_SSIT/2012/02/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P7/CER_SSFA_NPP-FM5-VIIRS_SSIT_000000.2012020815.met $InputArchive/SSFA/NPP-FM5-VIIRS_SSIT/2012/02/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P7/CER_GQCI_NPP-FM5-VIIRS_SSIT_000000.2012020815 $InputArchive/GQCI/NPP-FM5-VIIRS_SSIT/2012/02/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P7/CER_MATCH-daily_Terra-Aqua-MODIS_Edition4_400400.20120208.nc $CERESHOME/inversion/data/MATCH-daily/Terra-Aqua-MODIS_Edition4/2012/02/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P7/CER_sibiMap_NPP-VIIRS_Edition4_400400.201202 $CERESHOME/inversion/data/sibiMap/NPP-VIIRS_Edition4/2012/02/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P7/sorce_tsi_v15.txt.20140331 $CERESHOME/inversion/data/SORCE/

#### Execution

Execute the production script by typing the script name, CER4.5-6.1P7-SGE_Driver.pl, followed by the date and hour options, the cleanup option and the platform option selecting either P6, P7, x86, or x86-flex.

cd $CERESHOME/inversion/CER4.5-6.1P7/rcf

$CERESHOME/inversion/CER4.5-6.1P7/rcf/CER4.5-6.1P7-SGE_Driver.pl -date 20120208 -hour 15 -clean -platform p6/p7/x86/x86-flex

The following file will be generated:

$CERESHOME/inversion/CER4.5-6.1P7/rcf/pcf/CER4.5-6.1P7_PCF_$INSTANCE_1P7

The submitted job can be monitored with the qstat command.

The most recently created sge_log file can be viewed to monitor progress of this job.  This will be the last file listed by the command:

ls -arlt $CERESHOME/inversion/sge_logs/CER4.5-6.1P7/CER4.5-6.1P7_$INSTANCE_1P7.o*

Output file generation test:

The script, list_4.5-6.1P7.pl, will list the files that were created during execution of the PGE:

$CERESHOME/inversion/CER4.5-6.1P7/rcf/list_4.5-6.1P7.pl $INSTANCE_1P7

Note:	If any file that should have been created is missing, then a message is written to the screen naming which file could not be found.

#### Exit Codes

All CER4.5-6.1P7 software terminates using the CERES defined EXIT CODES.  Successful completion is indicated by an exit code of 0.  This test should complete with an exit code of 0 for each of the executables.

#### Test Summary

Test Summary:

Total Run Time:	6:24 minutes

Memory:	5.7 G

Required Disk Space:	232 Megabytes

### Evaluation Procedures

When running the production script, run_4.5-6.1P7.pl, the system message, ’No match’, may be written to the screen.  This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

Remove input data:

rm $InputArchive/SSFB/NPP-FM5-VIIRS_SSIT/2012/02/CER_SSFB_NPP-FM5-VIIRS_SSIT_000000.2012020815

rm $InputArchive/SSFA/NPP-FM5-VIIRS_SSIT/2012/02/CER_SSFA_NPP-FM5-VIIRS_SSIT_000000.2012020815

rm $InputArchive/SSFA/NPP-FM5-VIIRS_SSIT/2012/02/CER_SSFA_NPP-FM5-VIIRS_SSIT_000000.2012020815.met

rm $InputArchive/GQCI/NPP-FM5-VIIRS_SSIT/2012/02/CER_GQCI_NPP-FM5-VIIRS_SSIT_000000.2012020815

rm $InputArchive/MOA/CERES_DAO-G5-CERES/2012/02/CER_MOA_CERES_DAO-G5-CERES_020033.2012020812

rm $InputArchive/MOA/CERES_DAO-G5-CERES/2012/02/CER_MOA_CERES_DAO-G5-CERES_020033.2012020818

rm $CERESHOME/inversion/data/MATCH-daily/Terra-Aqua-MODIS_Edition4/2012/02/CER_MATCH-daily_Terra-Aqua-MODIS_Edition4_400400.20120208.nc

rm $CERESHOME/inversion/data/sibiMap/NPP-VIIRS_Edition4/2012/02/CER_sibiMap_NPP-VIIRS_Edition4_400400.201202

rm $CERESHOME/inversion/data/SORCE/sorce_tsi_v15.txt.20140331

#### Log and Status File Results and Metadata Evaluation

The Error and Status Log File, CER4.5-6.1P7_LogReport_$INSTANCE_1P7, is located in directory $CERESHOME/inversion/runlogs after CER4.5-6.1P7 has been executed.  Metadata files, which end in extension '.met', are located in the same directories as their corresponding output files after CER4.5-6.1P7 has been executed

Compare the information contained in the log file with the expected contents of the Log Report file found in directory $CERESHOME/inversion/data_exp/CER4.5-6.1P7 and compare the metadata files with the expected contents of the files with the same names found in directory $CERESHOME/inversion/data_exp/CER4.5-6.1P7, using the following diff_4.5-6.1P7.pl script:

cd $CERESHOME/inversion/CER4.5-6.1P7/rcf

$CERESHOME/inversion/CER4.5-6.1P7/rcf/diff_4.5-6.1P7.pl $INSTANCE_1P7

The only differences between the files should be the production times and differences in the directory paths where the tests were run.

#### Execution of Comparison Software for the Main Processor

The evaluation software for the Subsystem Main Processor will perform a single test.  This test will compare all of the parameters on the binary SSF and the binary SSFA (if it exists) to the values in comparison files provided with the software delivery.

- The executable for the comparison software is not provided in the tar file.  It was created when all the software’s code was compiled.

To execute the comparison software for the binary SSF and binary SSFA, type the following commands:

cd $CERESHOME/inversion/test_suites/bin

run_compare_1p7 $INSTANCE_1P7

Two files will be created:

$CERESHOME/inversion/test_suites/results/CmpReport_$DATE_1P7

$CERESHOME/inversion/test_suites/results/CmpReportSSFA_$DATE_1P7

#### Evaluation of Comparison Software Output

This section provides the procedure for evaluating the output from the CER4.5-6.1P7 comparison software.

Examine the comparison reports files by typing:

cat $CERESHOME/inversion/test_suites/results/CmpReport_$DATE_1P7

cat $CERESHOME/inversion/test_suites/results/CmpReportSSFA_$DATE_1P7

The final line of these files will report the status of the comparison between the generated data and the expected output.

#### Evaluation of SSF HDF Product

This section provides the procedure for evaluating the output from the SSF HDF product produced by the test software.  The comparison software was compiled when all software was compiled in a previous step.  Execute the program by typing the following lines:

hdiff $CERESHOME/inversion/data/SSF/NPP-FM5-VIIRS_SSIT-reproc/2012/02/CER_SSF_$INSTANCE_1P7 $CERESHOME/inversion/data_exp/CER4.5-6.1P7/CER_SSF_$INSTANCE_1P7

The executable, hdiff, compares each Vdata and each SDS on the SSF HDF output file.

The main purpose of the hdiff command is to verify that the HDF converter worked correctly.  If the status from the "Evaluation of Comparison Software Output" section reports that it was successful, then the HDF file is not likely to have a major issue since it is created from the successfully compared data files.  Watch the screen as any results scroll by.  Presence of any major issues should be obvious as there would be many differences large enough to catch the eye.  Differences in the third to sixth decimal places for the data fields are acceptable and expected due to rounding differences between P6 and x86 resulting in different paths through the Inversion software.

The only other differences between the two HDF output files should be the dates on Vfields:  “SSF_DATE” on the “SSF_Header” Vdata and “CERPRODUCTIONDATETIME” on the “CERES_metadata” Vdata.  If CERESLIB has changed, the date may be different in the “LOCALVERSIONID” on the “CERES_metadata” Vdata.

### Solutions to Possible Problems

- All output files are opened with Status = NEW in the CER4.5-6.1P7 software.  These files must be removed before rerunning these test procedures.  A script which removes PGE created files, cleanup_4.5-6.1P7.pl, is located in directory $CERESHOME/inversion/CER4.5-6.1P7/rcf.  To use the clean-up script:

cd $CERESHOME/inversion/CER4.5-6.1P7/rcf

$CERESHOME/inversion/CER4.5-6.1P7/rcf/cleanup_4.5-6.1P7.pl $DATE_1P7

Use the latest version of CERESlib.

Ignore the warnings received during compilation.

### Stand Alone, command line, Test Procedures for FM5, Environment Variables REPROCESS = ‘YES’ and READ_IES = ‘YES’

#### Environment setup and file preparation

cd $CERESHOME/inversion/CER4.5-6.1P7/rcf

setenv YEAR 2012

setenv MONTH 02

setenv DAY 08

setenv HOUR 15

setenv DATE_1P7 $YEAR$MONTH$DAY$HOUR

setenv INSTANCE_1P7 NPP-FM5-VIIRS_SSIT-reproc-ies_000000.$DATE_1P7

source $CERESHOME/inversion/CER4.5-6.1P7/rcf/inversion-FM5-test3-env.csh

Copy the input files to appropriate locations:

cp $CERESHOME/inversion/data/input/CER4.5-6.1P7/CER_MOA_CERES_DAO-G5-CERES_020033.2012020812 $InputArchive/MOA/CERES_DAO-G5-CERES/2012/02/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P7/CER_MOA_CERES_DAO-G5-CERES_020033.2012020818 $InputArchive/MOA/CERES_DAO-G5-CERES/2012/02/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P7/CER_SSFB_NPP-FM5-VIIRS_SSIT_000000.2012020815 $InputArchive/SSFB/NPP-FM5-VIIRS_SSIT/2012/02/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P7/CER_SSFA_NPP-FM5-VIIRS_SSIT_000000.2012020815 $InputArchive/SSFA/NPP-FM5-VIIRS_SSIT/2012/02/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P7/CER_SSFA_NPP-FM5-VIIRS_SSIT_000000.2012020815.met $InputArchive/SSFA/NPP-FM5-VIIRS_SSIT/2012/02/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P7/CER_GQCI_NPP-FM5-VIIRS_SSIT_000000.2012020815 $InputArchive/GQCI/NPP-FM5-VIIRS_SSIT/2012/02/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P7/CER_MATCH-daily_Terra-Aqua-MODIS_Edition4_400400.20120208.nc $CERESHOME/inversion/data/MATCH-daily/Terra-Aqua-MODIS_Edition4/2012/02/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P7/CER_IES_NPP-FM5_AtLaunch_300301.2012020815 $InputArchive/IES/NPP-FM5_AtLaunch/2012/02/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P7/CER_sibiMap_NPP-VIIRS_Edition4_400400.201202 $CERESHOME/inversion/data/sibiMap/NPP-VIIRS_Edition4/2012/02/

cp $CERESHOME/inversion/data/input/CER4.5-6.1P7/sorce_tsi_v15.txt.20140331 $CERESHOME/inversion/data/SORCE/

#### Execution

Execute the production script by typing the script name, CER4.5-6.1P7-SGE_Driver.pl, followed by the date and hour options, the cleanup option and the platform option selecting either P6, P7, x86, or x86-flex.

cd $CERESHOME/inversion/CER4.5-6.1P7/rcf

$CERESHOME/inversion/CER4.5-6.1P7/rcf/CER4.5-6.1P7-SGE_Driver.pl -date 20120208 -hour 15 -clean -platform p6/p7/x86/x86-flex

The following file will be generated:

$CERESHOME/inversion/CER4.5-6.1P7/rcf/pcf/CER4.5-6.1P7_PCF_$INSTANCE_1P7

The submitted job can be monitored with the qstat command.

The most recently created sge_log file can be viewed to monitor progress of this job.  This will be the last file listed by the command:

ls -arlt $CERESHOME/inversion/sge_logs/CER4.5-6.1P7/CER4.5-6.1P7_$INSTANCE_1P7.o*

Output file generation test:

The script, list_4.5-6.1P7.pl, will list the files that were created during execution of the PGE:

$CERESHOME/inversion/CER4.5-6.1P7/rcf/list_4.5-6.1P7.pl $INSTANCE_1P7

Note:	If any file that should have been created is missing, then a message is written to the screen naming which file could not be found.

#### Exit Codes

All CER4.5-6.1P7 software terminates using the CERES defined EXIT CODES.  Successful completion is indicated by an exit code of 0.  This test should complete with an exit code of 0 for each of the executables.

#### Test Summary

Test Summary:

Total Run Time:	6:24 minutes

Memory:	5.7 G

Required Disk Space:	232 Megabytes

### Evaluation Procedures

When running the production script, run_4.5-6.1P7.pl, the system message, ’No match’, may be written to the screen.  This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

Remove input data:

rm $InputArchive/SSFB/NPP-FM5-VIIRS_SSIT/2012/02/CER_SSFB_NPP-FM5-VIIRS_SSIT_000000.2012020815

rm $InputArchive/SSFA/NPP-FM5-VIIRS_SSIT/2012/02/CER_SSFA_NPP-FM5-VIIRS_SSIT_000000.2012020815

rm $InputArchive/SSFA/NPP-FM5-VIIRS_SSIT/2012/02/CER_SSFA_NPP-FM5-VIIRS_SSIT_000000.2012020815.met

rm $InputArchive/GQCI/NPP-FM5-VIIRS_SSIT/2012/02/CER_GQCI_NPP-FM5-VIIRS_SSIT_000000.2012020815

rm $InputArchive/MOA/CERES_DAO-G5-CERES/2012/02/CER_MOA_CERES_DAO-G5-CERES_020033.2012020812

rm $InputArchive/MOA/CERES_DAO-G5-CERES/2012/02/CER_MOA_CERES_DAO-G5-CERES_020033.2012020818

rm $CERESHOME/inversion/data/MATCH-daily/Terra-Aqua-MODIS_Edition4/2012/02/CER_MATCH-daily_Terra-Aqua-MODIS_Edition4_400400.20120208.nc

rm $InputArchive/IES/NPP-FM5_AtLaunch/2012/02/CER_IES_NPP-FM5_AtLaunch_300301.2012020815

rm $CERESHOME/inversion/data/sibiMap/NPP-VIIRS_Edition4/2012/02/CER_sibiMap_NPP-VIIRS_Edition4_400400.201202

rm $CERESHOME/inversion/data/SORCE/sorce_tsi_v15.txt.20140331

#### Log and Status File Results and Metadata Evaluation

The Error and Status Log File, CER4.5-6.1P7_LogReport_$INSTANCE_1P7, is located in directory $CERESHOME/inversion/runlogs after CER4.5-6.1P7 has been executed.  Metadata files, which end in extension '.met', are located in the same directories as their corresponding output files after CER4.5-6.1P7 has been executed.

Compare the information contained in the log file with the expected contents of the Log Report file found in directory $CERESHOME/inversion/data_exp/CER4.5-6.1P7 and compare the metadata files with the expected contents of the files with the same names found in directory $CERESHOME/inversion/data_exp/CER4.5-6.1P7, using the following diff_4.5-6.1P7.pl script:

cd $CERESHOME/inversion/CER4.5-6.1P7/rcf

$CERESHOME/inversion/CER4.5-6.1P7/rcf/diff_4.5-6.1P7.pl $INSTANCE_1P7

The only differences between the files should be the production times and differences in the directory paths where the tests were run.

#### Execution of Comparison Software for the Main Processor

The evaluation software for the Subsystem Main Processor will perform a single test.  This test will compare all of the parameters on the binary SSF and the binary SSFA (if it exists) to the values in comparison files provided with the software delivery.

- The executable for the comparison software is not provided in the tar file.  It was created when all the software’s code was compiled.

To execute the comparison software for the binary SSF and binary SSFA, type the following commands:

cd $CERESHOME/inversion/test_suites/bin

run_compare_1p7 $INSTANCE_1P7

Two files will be created:

$CERESHOME/inversion/test_suites/results/CmpReport_$DATE_1P7

$CERESHOME/inversion/test_suites/results/CmpReportSSFA_$DATE_1P7

#### Evaluation of Comparison Software Output

This section provides the procedure for evaluating the output from the CER4.5-6.1P7 comparison software.

Examine the comparison reports files by typing:

cat $CERESHOME/inversion/test_suites/results/CmpReport_$DATE_1P7

cat $CERESHOME/inversion/test_suites/results/CmpReportSSFA_$DATE_1P7

The final line of these files will report the status of the comparison between the generated data and the expected output.

#### Evaluation of SSF HDF Product

This section provides the procedure for evaluating the output from the SSF HDF product produced by the test software.  The comparison software was compiled when all software was compiled in a previous step.  Execute the program by typing the following lines:

hdiff $CERESHOME/inversion/data/SSF/NPP-FM5-VIIRS_SSIT-reproc-ies/2012/02/CER_SSF_$INSTANCE_1P7 $CERESHOME/inversion/data_exp/CER4.5-6.1P7/CER_SSF_$INSTANCE_1P7

The executable, hdiff, compares each Vdata and each SDS on the SSF HDF output file.

The main purpose of the hdiff command is to verify that the HDF converter worked correctly.  If the status from the "Evaluation of Comparison Software Output" section reports that it was successful, then the HDF file is not likely to have a major issue since it is created from the successfully compared data files.  Watch the screen as any results scroll by.  Presence of any major issues should be obvious as there would be many differences large enough to catch the eye.  Differences in the third to sixth decimal places for the data fields are acceptable and expected due to rounding differences between P6 and x86 resulting in different paths through the Inversion software.

The only other differences between the two HDF output files should be the dates on Vfields:  “SSF_DATE” on the “SSF_Header” Vdata and “CERPRODUCTIONDATETIME” on the “CERES_metadata” Vdata.  If CERESLIB has changed, the date may be different in the “LOCALVERSIONID” on the “CERES_metadata” Vdata.

### Solutions to Possible Problems

- All output files are opened with Status = NEW in the CER4.5-6.1P7 software.  These files must be removed before rerunning these test procedures.  A script which removes PGE created files, cleanup_4.5-6.1P7.pl, is located in directory $CERESHOME/inversion/CER4.5-6.1P7/rcf.  To use the clean-up script:

cd $CERESHOME/inversion/CER4.5-6.1P7/rcf

$CERESHOME/inversion/CER4.5-6.1P7/rcf/cleanup_4.5-6.1P7.pl $DATE_1P7

Use the latest version of CERESlib.

Ignore the warnings received during compilation.

## CER4_5-6.2P3 Terra and Aqua Edition4 and NPP Edition1 SSF Subsetting Post Processor Producing Daily SSF and SSFA Subset Files, and Nadir SSF, Validation SSF, and Validation SSFA Subset Products

### Stand Alone Test Procedures for FM1

#### Environment setup and file preparation

cd $CERESHOME/inversion/CER4.5-6.2P3/rcf

setenv YEAR 2008

setenv MONTH 07

setenv DAY 15

setenv DATE_2P3 $YEAR$MONTH$DAY

setenv INSTANCE2_2P3 Terra-FM1-MODIS_Ed4Test_000000.$DATE_2P3

source $CERESHOME/inversion/CER4.5-6.2P3/rcf/inversion-terra-test-FM1-subset-env.csh

Copy the input files to appropriate locations:

cp $CERESHOME/inversion/data/input/CER4.5-6.2P3/CER_SSFA_Terra-FM1-MODIS_Ed4Test_000000.2008071515 $CERESHOME/inversion/data/SSFA/Terra-FM1-MODIS_Ed4Test/2008/07/

cp $CERESHOME/inversion/data/input/CER4.5-6.2P3/CER_SSFB_Terra-FM1-MODIS_Ed4Test_000000.2008071515 $CERESHOME/inversion/data/SSFB/Terra-FM1-MODIS_Ed4Test/2008/07/

#### Execution

Execute the production script by typing the script name, CER4.5-6.2P3-SGE_Driver.pl, followed by the date option and the cleanup option.

cd $CERESHOME/inversion/CER4.5-6.2P3/rcf

$CERESHOME/inversion/CER4.5-6.2P3/rcf/CER4.5-6.2P3-SGE_Driver.pl -date $DATE_2P3 -clean

The following file will be generated:

$CERESHOME/inversion/CER4.5-6.2P3/rcf/pcf/CER4.5-6.2P3_PCF_$INSTANCE2_2P3

The submitted job can be monitored with the qstat command.

The most recently created sge_log file can be viewed to monitor progress of this job.  This will be the last file listed by the command:

ls -arlt $CERESHOME/inversion/sge_logs/CER4.5-6.2P3/CER4.5-6.2P3_$INSTANCE2_2P3.o*

Output file generation test:

The SSF subset Processor Product Generation Executive (PGE), CER4.5-6.2P3, will be executed and will create the files printed out by the list_4.5-6.2P3csh script:

$CERESHOME/inversion/CER4.5-6.2P3/rcf/list_4.5-6.2P3.csh $INSTANCE2_2P3

Note:	If any file that should have been created is missing, then a message is written to the screen naming which file could not be found.

#### Exit Codes

All CER4.5-6.2P3 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.  This test should complete with an exit code of 0 for each of the executables.

#### Test Summary

SSF Subset Postprocessor Test Summary:

Total Run Time:	0:10 minutes

Memory:	5422 K

Required Disk Space:	60.5 Megabytes

### Evaluation Procedures

Clean up the input directories:

rm $CERESHOME/inversion/data/SSFA/Terra-FM1-MODIS_Ed4Test/2008/07/CER_SSFA_Terra-FM1-MODIS_Ed4Test_000000.2008071515

rm $CERESHOME/inversion/data/SSFB/Terra-FM1-MODIS_Ed4Test/2008/07/CER_SSFB_Terra-FM1-MODIS_Ed4Test_000000.2008071515

#### Log and Status File Results and Metadata Evaluation

The Error and Status Log File, CER4.5-6.2P3_LogReport_$INSTANCE2_2P3 is located in directory $CERESHOME/inversion/runlogs after CER4.5-6.2P3 has been executed.  Metadata files which end in extension, '.met', are located in the same directories as their corresponding output files after CER4.5-6.2P3 has been executed.

Compare the metadata files with the expected contents of the files with the same names found in directory $CERESHOME/inversion/data_exp/CER4.5-6.2P3, using the following diff_4.5-6.2P3.csh script:

cd $CERESHOME/inversion/CER4.5-6.2P3/rcf

$CERESHOME/inversion/CER4.5-6.2P3/rcf/diff_4.5-6.2P3.csh $INSTANCE2_2P3

The only differences between the *.met files should be the production times and differences in the directory paths where the tests were run.

#### Execution of Comparison Software for the SSF Subset Post Processor

The evaluation software for this SSF Subset Post Processor will perform a single test.  This test will compare the data on the two newly created SSF subset files to the comparison files provided with the software delivery.

- The executable for the comparison software is not provided in the tar file.  It was created when all the software’s code was compiled.

To execute the comparison software for the CER4.5-6.2P3, type the following commands:

cd $CERESHOME/inversion/test_suites/bin

run_subset_compare $INSTANCE2_2P3

run_subset_aerosol_compare $INSTANCE2_2P3

run_nadir_compare $INSTANCE2_2P3

run_validation_compare $INSTANCE2_2P3

run_validation_aero_compare $INSTANCE2_2P3

The following comparison output files will be created:

$CERESHOME/inversion/test_suites/results/CmpSubset_$DATE_2P3

$CERESHOME/inversion/test_suites/results/CmpSubsetSSF2A_$DATE_2P3

$CERESHOME/inversion/test_suites/results/CmpSubsetSSFNadir_$DATE_2P3

$CERESHOME/inversion/test_suites/results/CmpSubsetSSFVal_$DATE_2P3

$CERESHOME/inversion/test_suites/results/CmpSubsetSSFAVal_$DATE_2P3

#### Evaluation of Comparison Software Output

This section provides the procedure for evaluating the output from the CER4.5-6.2P3 comparison software.

Examine the comparison report files by typing:

cat $CERESHOME/inversion/test_suites/results/CmpSubset_$DATE_2P3

cat $CERESHOME/inversion/test_suites/results/CmpSubsetSSF2A_$DATE_2P3

cat $CERESHOME/inversion/test_suites/results/CmpSubsetSSFNadir_$DATE_2P3

cat $CERESHOME/inversion/test_suites/results/CmpSubsetSSFVal_$DATE_2P3

cat $CERESHOME/inversion/test_suites/results/CmpSubsetSSFAVal_$DATE_2P3

The final line of this file will report the status of the comparison between the generated data and the expected output.

#### Evaluation of SSF HDF Product

This section provides the procedure for evaluating the output from the SSF HDF product produced by the test software.  The comparison software was compiled when all software was compiled in a previous step.  Execute the program by typing the following lines:

hdiff $CERESHOME/inversion/data/SSF-nadir/Terra-FM1-MODIS_Ed4Test/2008/07/CER_SSF-nadir_$INSTANCE2_2P3 $CERESHOME/inversion/data_exp/CER4.5-6.2P3/CER_SSF-nadir_$INSTANCE2_2P3

The executable, hdiff, compares each Vdata and each SDS on the SSF HDF output file.

The only differences between the two HDF output files should be the dates on Vfields: “SSF_DATE” on the “SSF_Header” Vdata and “CERPRODUCTIONDATETIME” on the “CERES_metadata” Vdata.  If CERESLIB has changed, the date may be different in the “LOCALVERSIONID” on the “CERES_metadata” Vdata.

### Solutions to Possible Problems

- All output files are opened with Status = NEW in the CER4.5-6.2P3 software.  These files must be removed before running these test procedures.  A script, which removes PGE created files, cleanup_4.5-6.2P3.csh, is located in directory $CERESHOME/inversion/CER4.5-6.2P3/rcf.  To use the clean-up script:

$CERESHOME/inversion/CER4.5-6.2P3/rcf/cleanup_4.5-6.2P3.csh $INSTANCE2_2P3

Use the latest version of CERESlib.

Ignore the warnings received during compilation.

### Stand Alone Test Procedures for FM2

#### Environment setup and file preparation

cd $CERESHOME/inversion/CER4.5-6.2P3/rcf

setenv YEAR 2001

setenv MONTH 04

setenv DAY 15

setenv DATE_2P3 $YEAR$MONTH$DAY

setenv INSTANCE2_2P3 Terra-FM2-MODIS_SSIT2_000000.$DATE_2P3

source $CERESHOME/inversion/CER4.5-6.2P3/rcf/inversion-terra-test-FM2-subset-env.csh

Copy the input files to appropriate locations:

cp $CERESHOME/inversion/data/input/CER4.5-6.2P3/CER_SSFA_Terra-FM2-MODIS_SSIT2_000000.2001041515 $CERESHOME/inversion/data/SSFA/Terra-FM2-MODIS_SSIT2/2001/04/

cp $CERESHOME/inversion/data/input/CER4.5-6.2P3/CER_SSFB_Terra-FM2-MODIS_SSIT2_000000.2001041515 $CERESHOME/inversion/data/SSFB/Terra-FM2-MODIS_SSIT2/2001/04/

#### Execution

Execute the production script by typing the script name, CER4.5-6.2P3-SGE_Driver.pl, followed by the date option and the cleanup option.

cd $CERESHOME/inversion/CER4.5-6.2P3/rcf

$CERESHOME/inversion/CER4.5-6.2P3/rcf/CER4.5-6.2P3-SGE_Driver.pl -date $DATE_2P3 -clean

The following file will be generated:

$CERESHOME/inversion/CER4.5-6.2P3/rcf/pcf/CER4.5-6.2P3_PCF_$INSTANCE2_2P3

The submitted job can be monitored with the qstat command.

The most recently created sge_log file can be viewed to monitor progress of this job.  This will be the last file listed by the command:

ls -arlt $CERESHOME/inversion/sge_logs/CER4.5-6.2P3/CER4.5-6.2P3_$INSTANCE2_2P3.o*

Output file generation test:

The SSF subset Processor Product Generation Executive (PGE), CER4.5-6.2P3, will be executed and will create the files printed out by the list_4.5-6.2P3csh script:

$CERESHOME/inversion/CER4.5-6.2P3/rcf/list_4.5-6.2P3.csh $INSTANCE2_2P3

Note:	If any file that should have been created is missing, then a message is written to the screen naming which file could not be found.

#### Exit Codes

All CER4.5-6.2P3 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.  This test should complete with an exit code of 0 for each of the executables.

#### Test Summary

SSF Subset Postprocessor Test Summary:

Total Run Time:	0:10 minutes

Memory:	5422 K

Required Disk Space:	60.5 Megabytes

### Evaluation Procedures

Clean up the input directories:

rm $CERESHOME/inversion/data/SSFA/Terra-FM2-MODIS_SSIT2/2001/04/CER_SSFA_Terra-FM2-MODIS_SSIT2_000000.2001041515

rm $CERESHOME/inversion/data/SSFB/Terra-FM2-MODIS_SSIT2/2001/04/CER_SSFB_Terra-FM2-MODIS_SSIT2_000000.2001041515

#### Log and Status File Results and Metadata Evaluation

The Error and Status Log File, CER4.5-6.2P3_LogReport_$INSTANCE2_2P3 is located in directory $CERESHOME/inversion/runlogs after CER4.5-6.2P3 has been executed.  Metadata files which end in extension, '.met', are located in the same directories as their corresponding output files after CER4.5-6.2P3 has been executed.

Compare the metadata files with the expected contents of the files with the same names found in directory $CERESHOME/inversion/data_exp/CER4.5-6.2P3, using the following diff_4.5-6.2P3.csh script:

cd $CERESHOME/inversion/CER4.5-6.2P3/rcf

$CERESHOME/inversion/CER4.5-6.2P3/rcf/diff_4.5-6.2P3.csh $INSTANCE2_2P3

The only differences between the *.met files should be the production times and differences in the directory paths where the tests were run.

#### Execution of Comparison Software for the SSF Subset Post Processor

The evaluation software for this SSF Subset Post Processor will perform a single test.  This test will compare the data on the two newly created SSF subset files to the comparison files provided with the software delivery.

- The executable for the comparison software is not provided in the tar file.  It was created when all the software’s code was compiled.

To execute the comparison software for the CER4.5-6.2P3, type the following commands:

cd $CERESHOME/inversion/test_suites/bin

run_subset_compare $INSTANCE2_2P3

run_subset_aerosol_compare $INSTANCE2_2P3

run_nadir_compare $INSTANCE2_2P3

run_validation_compare $INSTANCE2_2P3

run_validation_aero_compare $INSTANCE2_2P3

The following comparison output files will be created:

$CERESHOME/inversion/test_suites/results/CmpSubset_$DATE_2P3

$CERESHOME/inversion/test_suites/results/CmpSubsetSSF2A_$DATE_2P3

$CERESHOME/inversion/test_suites/results/CmpSubsetSSFNadir_$DATE_2P3

$CERESHOME/inversion/test_suites/results/CmpSubsetSSFVal_$DATE_2P3

$CERESHOME/inversion/test_suites/results/CmpSubsetSSFAVal_$DATE_2P3

#### Evaluation of Comparison Software Output

This section provides the procedure for evaluating the output from the CER4.5-6.2P3 comparison software.

Examine the comparison report files by typing:

cat $CERESHOME/inversion/test_suites/results/CmpSubset_$DATE_2P3

cat $CERESHOME/inversion/test_suites/results/CmpSubsetSSF2A_$DATE_2P3

cat $CERESHOME/inversion/test_suites/results/CmpSubsetSSFNadir_$DATE_2P3

cat $CERESHOME/inversion/test_suites/results/CmpSubsetSSFVal_$DATE_2P3

cat $CERESHOME/inversion/test_suites/results/CmpSubsetSSFAVal_$DATE_2P3

The final line of this file will report the status of the comparison between the generated data and the expected output.

#### Evaluation of SSF HDF Product

This section provides the procedure for evaluating the output from the SSF HDF product produced by the test software.  The comparison software was compiled when all software was compiled in a previous step.  Execute the program by typing the following lines:

hdiff $CERESHOME/inversion/data/SSF-nadir/Terra-FM2-MODIS_SSIT2/2001/04/CER_SSF-nadir_$INSTANCE2_2P3 $CERESHOME/inversion/data_exp/CER4.5-6.2P3/CER_SSF-nadir_$INSTANCE2_2P3

The executable, hdiff, compares each Vdata and each SDS on the SSF HDF output file.

The only differences between the two HDF output files should be the dates on Vfields: “SSF_DATE” on the “SSF_Header” Vdata and “CERPRODUCTIONDATETIME” on the “CERES_metadata” Vdata.  If CERESLIB has changed, the date may be different in the “LOCALVERSIONID” on the “CERES_metadata” Vdata.

### Solutions to Possible Problems

- All output files are opened with Status = NEW in the CER4.5-6.2P3 software.  These files must be removed before running these test procedures.  A script, which removes PGE created files, cleanup_4.5-6.2P3.csh, is located in directory $CERESHOME/inversion/CER4.5-6.2P3/rcf.  To use the clean-up script:

$CERESHOME/inversion/CER4.5-6.2P3/rcf/cleanup_4.5-6.2P3.csh $INSTANCE2_2P3

Use the latest version of CERESlib.

Ignore the warnings received during compilation.

### Stand Alone Test Procedures for FM3

#### Environment setup and file preparation

cd $CERESHOME/inversion/CER4.5-6.2P3/rcf

setenv YEAR 2008

setenv MONTH 10

setenv DAY 15

setenv DATE_2P3 $YEAR$MONTH$DAY

setenv INSTANCE2_2P3 Aqua-FM3-MODIS_SSIT_000000.$DATE_2P3

source $CERESHOME/inversion/CER4.5-6.2P3/rcf/inversion-aqua-test-FM3-subset-env.csh

Copy the input files to appropriate locations:

cp $CERESHOME/inversion/data/input/CER4.5-6.2P3/CER_SSFA_Aqua-FM3-MODIS_SSIT_000000.2008101507 $CERESHOME/inversion/data/SSFA/Aqua-FM3-MODIS_SSIT/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.2P3/CER_SSFB_Aqua-FM3-MODIS_SSIT_000000.2008101507 $CERESHOME/inversion/data/SSFB/Aqua-FM3-MODIS_SSIT/2008/10/

#### Execution

Execute the production script by typing the script name, CER4.5-6.2P3-SGE_Driver.pl, followed by the date option and the cleanup option.

cd $CERESHOME/inversion/CER4.5-6.2P3/rcf

$CERESHOME/inversion/CER4.5-6.2P3/rcf/CER4.5-6.2P3-SGE_Driver.pl -date $DATE_2P3 -clean

The following file will be generated:

$CERESHOME/inversion/CER4.5-6.2P3/rcf/pcf/CER4.5-6.2P3_PCF_$INSTANCE2_2P3

The submitted job can be monitored with the qstat command.

The most recently created sge_log file can be viewed to monitor progress of this job.  This will be the last file listed by the command:

ls -arlt $CERESHOME/inversion/sge_logs/CER4.5-6.2P3/CER4.5-6.2P3_$INSTANCE2_2P3.o*

Output file generation test:

The SSF subset Processor Product Generation Executive (PGE), CER4.5-6.2P3, will be executed and will create the files printed out by the list_4.5-6.2P3csh script:

$CERESHOME/inversion/CER4.5-6.2P3/rcf/list_4.5-6.2P3.csh $INSTANCE2_2P3

Note:	If any file that should have been created is missing, then a message is written to the screen naming which file could not be found.

#### Exit Codes

All CER4.5-6.2P3 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.  This test should complete with an exit code of 0 for each of the executables.

#### Test Summary

SSF Subset Postprocessor Test Summary:

Total Run Time:	0:10 minutes

Memory:	5422 K

Required Disk Space:	60.5 Megabytes

### Evaluation Procedures

When running the production script, run_4.5-6.2P3.csh, the system message, ’No match’, may be written to the screen.  This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

Clean up the input directories:

rm $CERESHOME/inversion/data/SSFA/Aqua-FM3-MODIS_SSIT/2008/10/CER_SSFA_Aqua-FM3-MODIS_SSIT_000000.2008101507

rm $CERESHOME/inversion/data/SSFB/Aqua-FM3-MODIS_SSIT/2008/10/CER_SSFB_Aqua-FM3-MODIS_SSIT_000000.2008101507

#### Log and Status File Results and Metadata Evaluation

The Error and Status Log File, CER4.5-6.2P3_LogReport_$INSTANCE2_2P3 is located in directory $CERESHOME/inversion/runlogs after CER4.5-6.2P3 has been executed.  Metadata files which end in extension, '.met', are located in the same directories as their corresponding output files after CER4.5-6.2P3 has been executed.

Compare the metadata files with the expected contents of the files with the same names found in directory $CERESHOME/inversion/data_exp/CER4.5-6.2P3, using the following diff_4.5-6.2P3.csh script:

cd $CERESHOME/inversion/CER4.5-6.2P3/rcf

$CERESHOME/inversion/CER4.5-6.2P3/rcf/diff_4.5-6.2P3.csh $INSTANCE2_2P3

The only differences between the *.met files should be the production times and differences in the directory paths where the tests were run.

#### Execution of Comparison Software for the SSF Subset Post Processor

The evaluation software for this SSF Subset Post Processor will perform a single test.  This test will compare the data on the two newly created SSF subset files to the comparison files provided with the software delivery.

- The executable for the comparison software is not provided in the tar file.  It was created when all the software’s code was compiled.

To execute the comparison software for the CER4.5-6.2P3, type the following commands:

cd $CERESHOME/inversion/test_suites/bin

run_subset_compare $INSTANCE2_2P3

run_subset_aerosol_compare $INSTANCE2_2P3

run_nadir_compare $INSTANCE2_2P3

run_validation_compare $INSTANCE2_2P3

run_validation_aero_compare $INSTANCE2_2P3

The following comparison output files will be created:

$CERESHOME/inversion/test_suites/results/CmpSubset_$DATE_2P3

$CERESHOME/inversion/test_suites/results/CmpSubsetSSF2A_$DATE_2P3

$CERESHOME/inversion/test_suites/results/CmpSubsetSSFNadir_$DATE_2P3

$CERESHOME/inversion/test_suites/results/CmpSubsetSSFVal_$DATE_2P3

$CERESHOME/inversion/test_suites/results/CmpSubsetSSFAVal_$DATE_2P3

#### Evaluation of Comparison Software Output

This section provides the procedure for evaluating the output from the CER4.5-6.2P3 comparison software.

Examine the comparison report files by typing:

cat $CERESHOME/inversion/test_suites/results/CmpSubset_$DATE_2P3

cat $CERESHOME/inversion/test_suites/results/CmpSubsetSSF2A_$DATE_2P3

cat $CERESHOME/inversion/test_suites/results/CmpSubsetSSFNadir_$DATE_2P3

cat $CERESHOME/inversion/test_suites/results/CmpSubsetSSFVal_$DATE_2P3

cat $CERESHOME/inversion/test_suites/results/CmpSubsetSSFAVal_$DATE_2P3

The final line of this file will report the status of the comparison between the generated data and the expected output.

#### Evaluation of SSF HDF Product

This section provides the procedure for evaluating the output from the SSF HDF product produced by the test software.  The comparison software was compiled when all software was compiled in a previous step.  Execute the program by typing the following lines:

hdiff $CERESHOME/inversion/data/SSF-nadir/Aqua-FM3-MODIS_SSIT/2008/10/CER_SSF-nadir_$INSTANCE2_2P3 $CERESHOME/inversion/data_exp/CER4.5-6.2P3/CER_SSF-nadir_$INSTANCE2_2P3

The executable, hdiff, compares each Vdata and each SDS on the SSF HDF output file.

The only differences between the two HDF output files should be the dates on Vfields: “SSF_DATE” on the “SSF_Header” Vdata and “CERPRODUCTIONDATETIME” on the “CERES_metadata” Vdata.  If CERESLIB has changed, the date may be different in the “LOCALVERSIONID” on the “CERES_metadata” Vdata.

### Solutions to Possible Problems

- All output files are opened with Status = NEW in the CER4.5-6.2P3 software.  These files must be removed before running these test procedures.  A script, which removes PGE created files, cleanup_4.5-6.2P3.csh, is located in directory $CERESHOME/inversion/CER4.5-6.2P3/rcf.  To use the clean-up script:

$CERESHOME/inversion/CER4.5-6.2P3/rcf/cleanup_4.5-6.2P3.csh $INSTANCE2_2P3

Use the latest version of CERESlib.

Ignore the warnings received during compilation.

### Stand Alone Test Procedures for FM4

#### Environment setup and file preparation

cd $CERESHOME/inversion/CER4.5-6.2P3/rcf

setenv YEAR 2008

setenv MONTH 10

setenv DAY 15

setenv DATE_2P3 $YEAR$MONTH$DAY

setenv INSTANCE2_2P3 Aqua-FM4-MODIS_SSIT-NoSW_000000.$DATE_2P3

source $CERESHOME/inversion/CER4.5-6.2P3/rcf/inversion-aqua-test-FM4-subset-env.csh

Copy the input files to appropriate locations:

cp $CERESHOME/inversion/data/input/CER4.5-6.2P3/CER_SSFA_Aqua-FM4-MODIS_SSIT-NoSW_000000.2008101507 $CERESHOME/inversion/data/SSFA/Aqua-FM4-MODIS_SSIT-NoSW/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.2P3/CER_SSFB_Aqua-FM4-MODIS_SSIT-NoSW_000000.2008101507 $CERESHOME/inversion/data/SSFB/Aqua-FM4-MODIS_SSIT-NoSW/2008/10/

#### Execution

Execute the production script by typing the script name, CER4.5-6.2P3-SGE_Driver.pl, followed by the date option and the cleanup option.

cd $CERESHOME/inversion/CER4.5-6.2P3/rcf

$CERESHOME/inversion/CER4.5-6.2P3/rcf/CER4.5-6.2P3-SGE_Driver.pl -date $DATE_2P3 -clean

The following file will be generated:

$CERESHOME/inversion/CER4.5-6.2P3/rcf/pcf/CER4.5-6.2P3_PCF_$INSTANCE2_2P3

The submitted job can be monitored with the qstat command.

The most recently created sge_log file can be viewed to monitor progress of this job.  This will be the last file listed by the command:

ls -arlt $CERESHOME/inversion/sge_logs/CER4.5-6.2P3/CER4.5-6.2P3_$INSTANCE2_2P3.o*

Output file generation test:

The SSF subset Processor Product Generation Executive (PGE), CER4.5-6.2P3, will be executed and will create the files printed out by the list_4.5-6.2P3csh script:

$CERESHOME/inversion/CER4.5-6.2P3/rcf/list_4.5-6.2P3.csh $INSTANCE2_2P3

Note:	If any file that should have been created is missing, then a message is written to the screen naming which file could not be found.  THERE ARE NOT ANY SSFB-nadir OR SSF-nadir PRODUCTS WITH THIS TEST.  THESE FILES WILL SHOW AS MISSING.

#### Exit Codes

All CER4.5-6.2P3 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.  This test should complete with an exit code of 0 for each of the executables.

#### Test Summary

SSF Subset Postprocessor Test Summary:

Total Run Time:	0:10 minutes

Memory:	5422 K

Required Disk Space:	60.5 Megabytes

### Evaluation Procedures

When running the production script, run_4.5-6.2P3.csh, the system message, ’No match’, may be written to the screen.  This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

Clean up the input directories:

rm $CERESHOME/inversion/data/SSFA/Aqua-FM4-MODIS_SSIT-NoSW/2008/10/CER_SSFA_Aqua-FM4-MODIS_SSIT-NoSW_000000.2008101507

rm $CERESHOME/inversion/data/SSFB/Aqua-FM4-MODIS_SSIT-NoSW/2008/10/CER_SSFB_Aqua-FM4-MODIS_SSIT-NoSW_000000.2008101507

#### Log and Status File Results and Metadata Evaluation

The Error and Status Log File, CER4.5-6.2P3_LogReport_$INSTANCE2_2P3 is located in directory $CERESHOME/inversion/runlogs after CER4.5-6.2P3 has been executed.  Metadata files which end in extension, '.met', are located in the same directories as their corresponding output files after CER4.5-6.2P3 has been executed.

Compare the metadata files with the expected contents of the files with the same names found in directory $CERESHOME/inversion/data_exp/CER4.5-6.2P3, using the following diff_4.5-6.2P3.csh script:

cd $CERESHOME/inversion/CER4.5-6.2P3/rcf

$CERESHOME/inversion/CER4.5-6.2P3/rcf/diff_4.5-6.2P3.csh $INSTANCE2_2P3

The only differences between the *.met files should be the production times and differences in the directory paths where the tests were run.

#### Execution of Comparison Software for the SSF Subset Post Processor

The evaluation software for this SSF Subset Post Processor will perform a single test.  This test will compare the data on the two newly created SSF subset files to the comparison files provided with the software delivery.

- The executable for the comparison software is not provided in the tar file.  It was created when all the software’s code was compiled.

To execute the comparison software for the CER4.5-6.2P3, type the following commands:

cd $CERESHOME/inversion/test_suites/bin

run_subset_compare $INSTANCE2_2P3

run_subset_aerosol_compare $INSTANCE2_2P3

run_nadir_compare $INSTANCE2_2P3

run_validation_compare $INSTANCE2_2P3

run_validation_aero_compare $INSTANCE2_2P3

The following comparison output files will be created:

$CERESHOME/inversion/test_suites/results/CmpSubset_$DATE_2P3

$CERESHOME/inversion/test_suites/results/CmpSubsetSSF2A_$DATE_2P3

$CERESHOME/inversion/test_suites/results/CmpSubsetSSFNadir_$DATE_2P3

$CERESHOME/inversion/test_suites/results/CmpSubsetSSFVal_$DATE_2P3

$CERESHOME/inversion/test_suites/results/CmpSubsetSSFAVal_$DATE_2P3

#### Evaluation of Comparison Software Output

This section provides the procedure for evaluating the output from the CER4.5-6.2P3 comparison software.

Examine the comparison report files by typing:

cat $CERESHOME/inversion/test_suites/results/CmpSubset_$DATE_2P3

cat $CERESHOME/inversion/test_suites/results/CmpSubsetSSF2A_$DATE_2P3

cat $CERESHOME/inversion/test_suites/results/CmpSubsetSSFNadir_$DATE_2P3

cat $CERESHOME/inversion/test_suites/results/CmpSubsetSSFVal_$DATE_2P3

cat $CERESHOME/inversion/test_suites/results/CmpSubsetSSFAVal_$DATE_2P3

The final line of this file will report the status of the comparison between the generated data and the expected output.

#### Evaluation of SSF HDF Product – THERE IS NO HDF PRODUCT WITH THIS TEST DATA.

This section provides the procedure for evaluating the output from the SSF HDF product produced by the test software.  The comparison software was compiled when all software was compiled in a previous step.  Execute the program by typing the following lines:

hdiff $CERESHOME/inversion/data/SSF-nadir/Aqua-FM4-MODIS_SSIT-NoSW/2008/10/CER_SSF-nadir_$INSTANCE2_2P3 $CERESHOME/inversion/data_exp/CER4.5-6.2P3/CER_SSF-nadir_$INSTANCE2_2P3

The executable, hdiff, compares each Vdata and each SDS on the SSF HDF output file.

The only differences between the two HDF output files should be the dates on Vfields: “SSF_DATE” on the “SSF_Header” Vdata and “CERPRODUCTIONDATETIME” on the “CERES_metadata” Vdata.  If CERESLIB has changed, the date may be different in the “LOCALVERSIONID” on the “CERES_metadata” Vdata.

### Solutions to Possible Problems

- All output files are opened with Status = NEW in the CER4.5-6.2P3 software.  These files must be removed before running these test procedures.  A script, which removes PGE created files, cleanup_4.5-6.2P3.csh, is located in directory $CERESHOME/inversion/CER4.5-6.2P3/rcf.  To use the clean-up script:

$CERESHOME/inversion/CER4.5-6.2P3/rcf/cleanup_4.5-6.2P3.csh $INSTANCE2_2P3

Use the latest version of CERESlib.

Ignore the warnings received during compilation.

### Stand Alone Test Procedures for FM5

#### Environment setup and file preparation

cd $CERESHOME/inversion/CER4.5-6.2P3/rcf

setenv YEAR 2012

setenv MONTH 02

setenv DAY 15

setenv DATE_2P3 $YEAR$MONTH$DAY

setenv INSTANCE2_2P3 NPP-FM5-VIIRS_SSIT_000000.$DATE_2P3

source $CERESHOME/inversion/CER4.5-6.2P3/rcf/inversion-npp-test-FM5-subset-env.csh

Copy the input files to appropriate locations:

cp $CERESHOME/inversion/data/input/CER4.5-6.2P3/CER_SSFA_NPP-FM5-VIIRS_SSIT_000000.2012021507 $CERESHOME/inversion/data/SSFA/NPP-FM5-VIIRS_SSIT/2012/02/

cp $CERESHOME/inversion/data/input/CER4.5-6.2P3/CER_SSFB_NPP-FM5-VIIRS_SSIT_000000.2012021507 $CERESHOME/inversion/data/SSFB/NPP-FM5-VIIRS_SSIT/2012/02/

#### Execution

Execute the production script by typing the script name, CER4.5-6.2P3-SGE_Driver.pl, followed by the date option and the cleanup option.

cd $CERESHOME/inversion/CER4.5-6.2P3/rcf

$CERESHOME/inversion/CER4.5-6.2P3/rcf/CER4.5-6.2P3-SGE_Driver.pl -date $DATE_2P3 -clean

The following file will be generated:

$CERESHOME/inversion/CER4.5-6.2P3/rcf/pcf/CER4.5-6.2P3_PCF_$INSTANCE2_2P3

The submitted job can be monitored with the qstat command.

The most recently created sge_log file can be viewed to monitor progress of this job.  This will be the last file listed by the command:

ls -arlt $CERESHOME/inversion/sge_logs/CER4.5-6.2P3/CER4.5-6.2P3_$INSTANCE2_2P3.o*

Output file generation test:

The SSF subset Processor Product Generation Executive (PGE), CER4.5-6.2P3, will be executed and will create the files printed out by the list_4.5-6.2P3csh script:

$CERESHOME/inversion/CER4.5-6.2P3/rcf/list_4.5-6.2P3.csh $INSTANCE2_2P3

Note:	If any file that should have been created is missing, then a message is written to the screen naming which file could not be found.

#### Exit Codes

All CER4.5-6.2P3 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.  This test should complete with an exit code of 0 for each of the executables.

#### Test Summary

SSF Subset Postprocessor Test Summary:

Total Run Time:	0:10 minutes

Memory:	5422 K

Required Disk Space:	60.5 Megabytes

### Evaluation Procedures

When running the production script, run_4.5-6.2P3.csh, the system message, ’No match’, may be written to the screen.  This message occurs when the script tries to remove an old output file that does not exist.  This does not signify a problem.

Clean up the input directories:

rm $CERESHOME/inversion/data/SSFA/NPP-FM5-VIIRS_SSIT/2012/02/CER_SSFA_NPP-FM5-VIIRS_SSIT_000000.2012021507

rm $CERESHOME/inversion/data/SSFB/NPP-FM5-VIIRS_SSIT/2012/02/CER_SSFB_NPP-FM5-VIIRS_SSIT_000000.2012021507

#### Log and Status File Results and Metadata Evaluation

The Error and Status Log File, CER4.5-6.2P3_LogReport_$INSTANCE2_2P3 is located in directory $CERESHOME/inversion/runlogs after CER4.5-6.2P3 has been executed.  Metadata files which end in extension, '.met', are located in the same directories as their corresponding output files after CER4.5-6.2P3 has been executed.

Compare the metadata files with the expected contents of the files with the same names found in directory $CERESHOME/inversion/data_exp/CER4.5-6.2P3, using the following diff_4.5-6.2P3.csh script:

cd $CERESHOME/inversion/CER4.5-6.2P3/rcf

$CERESHOME/inversion/CER4.5-6.2P3/rcf/diff_4.5-6.2P3.csh $INSTANCE2_2P3

The only differences between the *.met files should be the production times and differences in the directory paths where the tests were run.

#### Execution of Comparison Software for the SSF Subset Post Processor

The evaluation software for this SSF Subset Post Processor will perform a single test.  This test will compare the data on the two newly created SSF subset files to the comparison files provided with the software delivery.

- The executable for the comparison software is not provided in the tar file.  It was created when all the software’s code was compiled.

To execute the comparison software for the CER4.5-6.2P3, type the following commands:

cd $CERESHOME/inversion/test_suites/bin

run_subset_compare $INSTANCE2_2P3

run_subset_aerosol_compare $INSTANCE2_2P3

run_nadir_compare $INSTANCE2_2P3

run_validation_compare $INSTANCE2_2P3

run_validation_aero_compare $INSTANCE2_2P3

The following comparison output files will be created:

$CERESHOME/inversion/test_suites/results/CmpSubset_$DATE_2P3

$CERESHOME/inversion/test_suites/results/CmpSubsetSSF2A_$DATE_2P3

$CERESHOME/inversion/test_suites/results/CmpSubsetSSFNadir_$DATE_2P3

$CERESHOME/inversion/test_suites/results/CmpSubsetSSFVal_$DATE_2P3

$CERESHOME/inversion/test_suites/results/CmpSubsetSSFAVal_$DATE_2P3

#### Evaluation of Comparison Software Output

This section provides the procedure for evaluating the output from the CER4.5-6.2P3 comparison software.

Examine the comparison report files by typing:

cat $CERESHOME/inversion/test_suites/results/CmpSubset_$DATE_2P3

cat $CERESHOME/inversion/test_suites/results/CmpSubsetSSF2A_$DATE_2P3

cat $CERESHOME/inversion/test_suites/results/CmpSubsetSSFNadir_$DATE_2P3

cat $CERESHOME/inversion/test_suites/results/CmpSubsetSSFVal_$DATE_2P3

cat $CERESHOME/inversion/test_suites/results/CmpSubsetSSFAVal_$DATE_2P3

The final line of this file will report the status of the comparison between the generated data and the expected output.

#### Evaluation of SSF HDF Product

This section provides the procedure for evaluating the output from the SSF HDF product produced by the test software.  The comparison software was compiled when all software was compiled in a previous step.  Execute the program by typing the following lines:

hdiff $CERESHOME/inversion/data/SSF-nadir/NPP-FM5-VIIRS_SSIT/2012/02/CER_SSF-nadir_$INSTANCE2_2P3 $CERESHOME/inversion/data_exp/CER4.5-6.2P3/CER_SSF-nadir_$INSTANCE2_2P3

The executable, hdiff, compares each Vdata and each SDS on the SSF HDF output file.

The only differences between the two HDF output files should be the dates on Vfields: “SSF_DATE” on the “SSF_Header” Vdata and “CERPRODUCTIONDATETIME” on the “CERES_metadata” Vdata.  If CERESLIB has changed, the date may be different in the “LOCALVERSIONID” on the “CERES_metadata” Vdata.

### Solutions to Possible Problems

- All output files are opened with Status = NEW in the CER4.5-6.2P3 software.  These files must be removed before running these test procedures.  A script, which removes PGE created files, cleanup_4.5-6.2P3.csh, is located in directory $CERESHOME/inversion/CER4.5-6.2P3/rcf.  To use the clean-up script:

$CERESHOME/inversion/CER4.5-6.2P3/rcf/cleanup_4.5-6.2P3.csh $INSTANCE2_2P3

Use the latest version of CERESlib.

Ignore the warnings received during compilation.

## CER4_5-6.4P2 Terra and Aqua Edition4 SSF Post Processor Producing Monthly SSF and SSFA Validation subset files

### Stand Alone Test Procedures for FM1

#### Environment setup and file preparation

cd $CERESHOME/inversion/CER4.5-6.4P2/rcf

setenv YEAR 2008

setenv MONTH 07

setenv DATE_4P2 $YEAR$MONTH

setenv INSTANCE2_4P2 Terra-FM1-MODIS_Ed4Test_000000.$DATE_4P2

source $CERESHOME/inversion/CER4.5-6.4P2/rcf/inversion-FM1-valmm-subset.csh

Copy the input files to appropriate locations:

cp $CERESHOME/inversion/data/input/CER4.5-6.4P2/CER_SSFA-val_Terra-FM1-MODIS_Ed4Test_000000.20080715 $CERESHOME/inversion/data/SSFA-val/Terra-FM1-MODIS_Ed4Test/2008/07/

cp $CERESHOME/inversion/data/input/CER4.5-6.4P2/CER_SSFB-val_Terra-FM1-MODIS_Ed4Test_000000.20080715 $CERESHOME/inversion/data/SSFB-val/Terra-FM1-MODIS_Ed4Test/2008/07/

#### Execution

Execute the production script by typing the script name, CER4.5-6.4P2-SGE_Driver.pl, followed by the date option and the cleanup option.

cd $CERESHOME/inversion/CER4.5-6.4P2/rcf

$CERESHOME/inversion/CER4.5-6.4P2/rcf/CER4.5-6.4P2-SGE_Driver.pl -date $DATE_4P2 -clean

The following file will be generated:

$CERESHOME/inversion/CER4.5-6.4P2/rcf/pcf/CER4.5-6.4P2_PCF_$INSTANCE2_4P2

The submitted job can be monitored with the qstat command.

The most recently created sge_log file can be viewed to monitor progress of this job.  This will be the last file listed by the command:

ls -arlt $CERESHOME/inversion/sge_logs/CER4.5-6.4P2/CER4.5-6.4P2_$INSTANCE2_4P2.o*

Output file generation test:

The SSF subset Processor Product Generation Executive (PGE), CER4.5-6.4P2, will be executed and will create the files printed out by the list_4.5-6.4P2csh script:

$CERESHOME/inversion/CER4.5-6.4P2/rcf/list_4.5-6.4P2.csh $INSTANCE2_4P2

Note:	If any file that should have been created is missing, then a message is written to the screen naming which file could not be found.

#### Exit Codes

All CER4.5-6.4P2 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.  This test should complete with an exit code of 0 for each of the executables.

#### Test Summary

SSF Subset Postprocessor Test Summary:

Total Run Time:	0:02 minutes

Memory:	4631 K

Required Disk Space:	2.0 Megabytes

### Evaluation Procedures

Clean up the input directories:

rm $CERESHOME/inversion/data/SSFA-val/Terra-FM1-MODIS_Ed4Test/2008/07/CER_SSFA-val_Terra-FM1-MODIS_Ed4Test_000000.20080715

rm $CERESHOME/inversion/data/SSFB-val/Terra-FM1-MODIS_Ed4Test/2008/07/CER_SSFB-val_Terra-FM1-MODIS_Ed4Test_000000.20080715

#### Log and Status File Results and Metadata Evaluation

The Error and Status Log File, CER4.5-6.4P2_LogReport_$INSTANCE2_4P2 is located in directory $CERESHOME/inversion/runlogs after CER4.5-6.4P2 has been executed.  Metadata files which end in extension, '.met', are located in the same directories as their corresponding output files after CER4.5-6.4P2 has been executed.

Metadata files:

CER_SSFB-valmm_$INSTANCE_4P2.met

CER_SSFA-valmm_$INSTANCE_4P2.met

Compare the metadata files with the expected contents of the files with the same names found in directory $CERESHOME/inversion/data_exp/CER4.5-6.4P2, using the following diff_4.5-6.4P2.csh script:

cd $CERESHOME/inversion/CER4.5-6.4P2/rcf

$CERESHOME/inversion/CER4.5-6.4P2/rcf/diff_4.5-6.4P2.csh $INSTANCE2_4P2

The only differences between the *.met files should be the production times and differences in the directory paths where the tests were run.

#### Execution of Comparison Software for the SSF Subset Post Processor

The evaluation software for this SSF Post Processor will perform a single test.  This test will compare the data on the two newly created monthly validation site SSF files to the comparison files provided with the software delivery.

- The executable for the comparison software is not provided in the tar file.  It was created when all the software’s code was compiled.

To execute the comparison software for the CER4.5-6.4P2, type the following commands:

cd $CERESHOME/inversion/test_suites/bin

run_valmm_compare $INSTANCE2_4P2

run_valmm_a_compare $INSTANCE2_4P2

The following comparison output files will be created:

$CERESHOME/inversion/test_suites/results/CmpSubsetSSFValmm_$DATE_4P2

$CERESHOME/inversion/test_suites/results/CmpSubsetSSFAValmm_$DATE_4P2

#### Evaluation of Comparison Software Output

This section provides the procedure for evaluating the output from the CER4.5-6.4P2 comparison software.

Examine the comparison report files by typing:

cat $CERESHOME/inversion/test_suites/results/CmpSubsetSSFValmm_$DATE_4P2

cat $CERESHOME/inversion/test_suites/results/CmpSubsetSSFAValmm_$DATE_4P2

The final line of this file will report the status of the comparison between the generated data and the expected output.

### Solutions to Possible Problems

- All output files are opened with Status = NEW in the CER4.5-6.4P2 software.  These files must be removed before running these test procedures.  A script, which removes PGE created files, cleanup_4.5-6.4P2.csh, is located in directory $CERESHOME/inversion/CER4.5-6.4P2/rcf.  To use the clean-up script:

$CERESHOME/inversion/CER4.5-6.4P2/rcf/cleanup_4.5-6.4P2.csh $INSTANCE2_4P2

Use the latest version of CERESlib.

Ignore the warnings received during compilation.

### Stand Alone Test Procedures for FM2

#### Environment setup and file preparation

cd $CERESHOME/inversion/CER4.5-6.4P2/rcf

setenv YEAR 2001

setenv MONTH 04

setenv DATE_4P2 $YEAR$MONTH

setenv INSTANCE2_4P2 Terra-FM2-MODIS_SSIT2_000000.$DATE_4P2

source $CERESHOME/inversion/CER4.5-6.4P2/rcf/inversion-FM2-valmm-subset.csh

Copy the input files to appropriate locations:

cp $CERESHOME/inversion/data/input/CER4.5-6.4P2/CER_SSFA-val_Terra-FM2-MODIS_SSIT2_000000.20010415 $CERESHOME/inversion/data/SSFA-val/Terra-FM2-MODIS_SSIT2/2001/04/

cp $CERESHOME/inversion/data/input/CER4.5-6.4P2/CER_SSFB-val_Terra-FM2-MODIS_SSIT2_000000.20010415 $CERESHOME/inversion/data/SSFB-val/Terra-FM2-MODIS_SSIT2/2001/04/

#### Execution

Execute the production script by typing the script name, CER4.5-6.4P2-SGE_Driver.pl, followed by the date option and the cleanup option.

cd $CERESHOME/inversion/CER4.5-6.4P2/rcf

$CERESHOME/inversion/CER4.5-6.4P2/rcf/CER4.5-6.4P2-SGE_Driver.pl -date $DATE_4P2 -clean

The following file will be generated:

$CERESHOME/inversion/CER4.5-6.4P2/rcf/pcf/CER4.5-6.4P2_PCF_$INSTANCE2_4P2

The submitted job can be monitored with the qstat command.

The most recently created sge_log file can be viewed to monitor progress of this job.  This will be the last file listed by the command:

ls -arlt $CERESHOME/inversion/sge_logs/CER4.5-6.4P2/CER4.5-6.4P2_$INSTANCE2_4P2.o*

Output file generation test:

The SSF subset Processor Product Generation Executive (PGE), CER4.5-6.4P2, will be executed and will create the files printed out by the list_4.5-6.4P2csh script:

$CERESHOME/inversion/CER4.5-6.4P2/rcf/list_4.5-6.4P2.csh $INSTANCE2_4P2

Note:	If any file that should have been created is missing, then a message is written to the screen naming which file could not be found.

#### Exit Codes

All CER4.5-6.4P2 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.  This test should complete with an exit code of 0 for each of the executables.

#### Test Summary

SSF Subset Postprocessor Test Summary:

Total Run Time:	0:02 minutes

Memory:	4631 K

Required Disk Space:	2.0 Megabytes

### Evaluation Procedures

Clean up the input directories:

rm $CERESHOME/inversion/data/SSFA-val/Terra-FM2-MODIS_SSIT2/2001/04/CER_SSFA-val_Terra-FM2-MODIS_SSIT2_000000.20010415

rm $CERESHOME/inversion/data/SSFB-val/Terra-FM2-MODIS_SSIT2/2001/04/CER_SSFB-val_Terra-FM2-MODIS_SSIT2_000000.20010415

#### Log and Status File Results and Metadata Evaluation

The Error and Status Log File, CER4.5-6.4P2_LogReport_$INSTANCE2_4P2 is located in directory $CERESHOME/inversion/runlogs after CER4.5-6.4P2 has been executed.  Metadata files which end in extension, '.met', are located in the same directories as their corresponding output files after CER4.5-6.4P2 has been executed.

Metadata files:

CER_SSFB-valmm_$INSTANCE_4P2.met

CER_SSFA-valmm_$INSTANCE_4P2.met

Compare the metadata files with the expected contents of the files with the same names found in directory $CERESHOME/inversion/data_exp/CER4.5-6.4P2, using the following diff_4.5-6.4P2.csh script:

cd $CERESHOME/inversion/CER4.5-6.4P2/rcf

$CERESHOME/inversion/CER4.5-6.4P2/rcf/diff_4.5-6.4P2.csh $INSTANCE2_4P2

The only differences between the *.met files should be the production times and differences in the directory paths where the tests were run.

#### Execution of Comparison Software for the SSF Subset Post Processor

The evaluation software for this SSF Post Processor will perform a single test.  This test will compare the data on the two newly created monthly validation site SSF files to the comparison files provided with the software delivery.

- The executable for the comparison software is not provided in the tar file.  It was created when all the software’s code was compiled.

To execute the comparison software for the CER4.5-6.4P2, type the following commands:

cd $CERESHOME/inversion/test_suites/bin

run_valmm_compare $INSTANCE2_4P2

run_valmm_a_compare $INSTANCE2_4P2

The following comparison output files will be created:

$CERESHOME/inversion/test_suites/results/CmpSubsetSSFValmm_$DATE_4P2

$CERESHOME/inversion/test_suites/results/CmpSubsetSSFAValmm_$DATE_4P2

#### Evaluation of Comparison Software Output

This section provides the procedure for evaluating the output from the CER4.5-6.4P2 comparison software.

Examine the comparison report files by typing:

cat $CERESHOME/inversion/test_suites/results/CmpSubsetSSFValmm_$DATE_4P2

cat $CERESHOME/inversion/test_suites/results/CmpSubsetSSFAValmm_$DATE_4P2

The final line of this file will report the status of the comparison between the generated data and the expected output.

### Solutions to Possible Problems

- All output files are opened with Status = NEW in the CER4.5-6.4P2 software.  These files must be removed before running these test procedures.  A script, which removes PGE created files, cleanup_4.5-6.4P2.csh, is located in directory $CERESHOME/inversion/CER4.5-6.4P2/rcf.  To use the clean-up script:

$CERESHOME/inversion/CER4.5-6.4P2/rcf/cleanup_4.5-6.4P2.csh $INSTANCE2_4P2

Use the latest version of CERESlib.

Ignore the warnings received during compilation.

### Stand Alone Test Procedures for FM3

#### Environment setup and file preparation

cd $CERESHOME/inversion/CER4.5-6.4P2/rcf

setenv YEAR 2008

setenv MONTH 10

setenv DATE_4P2 $YEAR$MONTH

setenv INSTANCE2_4P2 Aqua-FM3-MODIS_SSIT_000000.$DATE_4P2

source $CERESHOME/inversion/CER4.5-6.4P2/rcf/inversion-FM3-valmm-subset.csh

Copy the input files to appropriate locations:

cp $CERESHOME/inversion/data/input/CER4.5-6.4P2/CER_SSFA-val_Aqua-FM3-MODIS_SSIT_000000.20081015 $CERESHOME/inversion/data/SSFA-val/Aqua-FM3-MODIS_SSIT/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.4P2/CER_SSFB-val_Aqua-FM3-MODIS_SSIT_000000.20081015 $CERESHOME/inversion/data/SSFB-val/Aqua-FM3-MODIS_SSIT/2008/10/

#### Execution

Execute the production script by typing the script name, CER4.5-6.4P2-SGE_Driver.pl, followed by the date option and the cleanup option.

cd $CERESHOME/inversion/CER4.5-6.4P2/rcf

$CERESHOME/inversion/CER4.5-6.4P2/rcf/CER4.5-6.4P2-SGE_Driver.pl -date $DATE_4P2 -clean

The following file will be generated:

$CERESHOME/inversion/CER4.5-6.4P2/rcf/pcf/CER4.5-6.4P2_PCF_$INSTANCE2_4P2

The submitted job can be monitored with the qstat command.

The most recently created sge_log file can be viewed to monitor progress of this job.  This will be the last file listed by the command:

ls -arlt $CERESHOME/inversion/sge_logs/CER4.5-6.4P2/CER4.5-6.4P2_$INSTANCE2_4P2.o*

Output file generation test:

The SSF subset Processor Product Generation Executive (PGE), CER4.5-6.4P2, will be executed and will create the files printed out by the list_4.5-6.4P2csh script:

$CERESHOME/inversion/CER4.5-6.4P2/rcf/list_4.5-6.4P2.csh $INSTANCE2_4P2

Note:	If any file that should have been created is missing, then a message is written to the screen naming which file could not be found.

#### Exit Codes

All CER4.5-6.4P2 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.  This test should complete with an exit code of 0 for each of the executables.

#### Test Summary

SSF Subset Postprocessor Test Summary:

Total Run Time:	0:02 minutes

Memory:	4631 K

Required Disk Space:	2.0 Megabytes

### Evaluation Procedures

Clean up the input directories:

rm $CERESHOME/inversion/data/SSFA-val/Aqua-FM3-MODIS_SSIT/2008/10/CER_SSFA-val_Aqua-FM3-MODIS_SSIT_000000.20081015

rm $CERESHOME/inversion/data/SSFB-val/Aqua-FM3-MODIS_SSIT/2008/10/CER_SSFB-val_Aqua-FM3-MODIS_SSIT_000000.20081015

#### Log and Status File Results and Metadata Evaluation

The Error and Status Log File, CER4.5-6.4P2_LogReport_$INSTANCE2_4P2 is located in directory $CERESHOME/inversion/runlogs after CER4.5-6.4P2 has been executed.  Metadata files which end in extension, '.met', are located in the same directories as their corresponding output files after CER4.5-6.4P2 has been executed.

Metadata files:

CER_SSFB-valmm_$INSTANCE_4P2.met

CER_SSFA-valmm_$INSTANCE_4P2.met

Compare the metadata files with the expected contents of the files with the same names found in directory $CERESHOME/inversion/data_exp/CER4.5-6.4P2, using the following diff_4.5-6.4P2.csh script:

cd $CERESHOME/inversion/CER4.5-6.4P2/rcf

$CERESHOME/inversion/CER4.5-6.4P2/rcf/diff_4.5-6.4P2.csh $INSTANCE2_4P2

The only differences between the *.met files should be the production times and differences in the directory paths where the tests were run.

#### Execution of Comparison Software for the SSF Subset Post Processor

The evaluation software for this SSF Post Processor will perform a single test.  This test will compare the data on the two newly created monthly validation site SSF files to the comparison files provided with the software delivery.

- The executable for the comparison software is not provided in the tar file.  It was created when all the software’s code was compiled.

To execute the comparison software for the CER4.5-6.4P2, type the following commands:

cd $CERESHOME/inversion/test_suites/bin

run_valmm_compare $INSTANCE2_4P2

run_valmm_a_compare $INSTANCE2_4P2

The following comparison output files will be created:

$CERESHOME/inversion/test_suites/results/CmpSubsetSSFValmm_$DATE_4P2

$CERESHOME/inversion/test_suites/results/CmpSubsetSSFAValmm_$DATE_4P2

#### Evaluation of Comparison Software Output

This section provides the procedure for evaluating the output from the CER4.5-6.4P2 comparison software.

Examine the comparison report files by typing:

cat $CERESHOME/inversion/test_suites/results/CmpSubsetSSFValmm_$DATE_4P2

cat $CERESHOME/inversion/test_suites/results/CmpSubsetSSFAValmm_$DATE_4P2

The final line of this file will report the status of the comparison between the generated data and the expected output.

### Solutions to Possible Problems

- All output files are opened with Status = NEW in the CER4.5-6.4P2 software.  These files must be removed before running these test procedures.  A script, which removes PGE created files, cleanup_4.5-6.4P2.csh, is located in directory $CERESHOME/inversion/CER4.5-6.4P2/rcf.  To use the clean-up script:

$CERESHOME/inversion/CER4.5-6.4P2/rcf/cleanup_4.5-6.4P2.csh $INSTANCE2_4P2

Use the latest version of CERESlib.

Ignore the warnings received during compilation.

### Stand Alone Test Procedures for FM4

#### Environment setup and file preparation

cd $CERESHOME/inversion/CER4.5-6.4P2/rcf

setenv YEAR 2008

setenv MONTH 10

setenv DATE_4P2 $YEAR$MONTH

setenv INSTANCE2_4P2 Aqua-FM4-MODIS_SSIT-NoSW_000000.$DATE_4P2

source $CERESHOME/inversion/CER4.5-6.4P2/rcf/inversion-FM4-valmm-subset.csh

Copy the input files to appropriate locations:

cp $CERESHOME/inversion/data/input/CER4.5-6.4P2/CER_SSFA-val_Aqua-FM4-MODIS_SSIT-NoSW_000000.20081015 $CERESHOME/inversion/data/SSFA-val/Aqua-FM4-MODIS_SSIT-NoSW/2008/10/

cp $CERESHOME/inversion/data/input/CER4.5-6.4P2/CER_SSFB-val_Aqua-FM4-MODIS_SSIT-NoSW_000000.20081015 $CERESHOME/inversion/data/SSFB-val/Aqua-FM4-MODIS_SSIT-NoSW/2008/10/

#### Execution

Execute the production script by typing the script name, CER4.5-6.4P2-SGE_Driver.pl, followed by the date option and the cleanup option.

cd $CERESHOME/inversion/CER4.5-6.4P2/rcf

$CERESHOME/inversion/CER4.5-6.4P2/rcf/CER4.5-6.4P2-SGE_Driver.pl -date $DATE_4P2 -clean

The following file will be generated:

$CERESHOME/inversion/CER4.5-6.4P2/rcf/pcf/CER4.5-6.4P2_PCF_$INSTANCE2_4P2

The submitted job can be monitored with the qstat command.

The most recently created sge_log file can be viewed to monitor progress of this job.  This will be the last file listed by the command:

ls -arlt $CERESHOME/inversion/sge_logs/CER4.5-6.4P2/CER4.5-6.4P2_$INSTANCE2_4P2.o*

Output file generation test:

The SSF subset Processor Product Generation Executive (PGE), CER4.5-6.4P2, will be executed and will create the files printed out by the list_4.5-6.4P2csh script:

$CERESHOME/inversion/CER4.5-6.4P2/rcf/list_4.5-6.4P2.csh $INSTANCE2_4P2

Note:	If any file that should have been created is missing, then a message is written to the screen naming which file could not be found.

#### Exit Codes

All CER4.5-6.4P2 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.  This test should complete with an exit code of 0 for each of the executables.

#### Test Summary

SSF Subset Postprocessor Test Summary:

Total Run Time:	0:02 minutes

Memory:	4631 K

Required Disk Space:	2.0 Megabytes

### Evaluation Procedures

Clean up the input directories:

rm $CERESHOME/inversion/data/SSFA-val/Aqua-FM4-MODIS_SSIT-NoSW/2008/10/CER_SSFA-val_Aqua-FM4-MODIS_SSIT-NoSW_000000.20081015

rm $CERESHOME/inversion/data/SSFB-val/Aqua-FM4-MODIS_SSIT-NoSW/2008/10/CER_SSFB-val_Aqua-FM4-MODIS_SSIT-NoSW_000000.20081015

#### Log and Status File Results and Metadata Evaluation

The Error and Status Log File, CER4.5-6.4P2_LogReport_$INSTANCE2_4P2 is located in directory $CERESHOME/inversion/runlogs after CER4.5-6.4P2 has been executed.  Metadata files which end in extension, '.met', are located in the same directories as their corresponding output files after CER4.5-6.4P2 has been executed.

Metadata files:

CER_SSFB-valmm_$INSTANCE_4P2.met

CER_SSFA-valmm_$INSTANCE_4P2.met

Compare the metadata files with the expected contents of the files with the same names found in directory $CERESHOME/inversion/data_exp/CER4.5-6.4P2, using the following diff_4.5-6.4P2.csh script:

cd $CERESHOME/inversion/CER4.5-6.4P2/rcf

$CERESHOME/inversion/CER4.5-6.4P2/rcf/diff_4.5-6.4P2.csh $INSTANCE2_4P2

The only differences between the *.met files should be the production times and differences in the directory paths where the tests were run.

#### Execution of Comparison Software for the SSF Subset Post Processor

The evaluation software for this SSF Post Processor will perform a single test.  This test will compare the data on the two newly created monthly validation site SSF files to the comparison files provided with the software delivery.

- The executable for the comparison software is not provided in the tar file.  It was created when all the software’s code was compiled.

To execute the comparison software for the CER4.5-6.4P2, type the following commands:

cd $CERESHOME/inversion/test_suites/bin

run_valmm_compare $INSTANCE2_4P2

run_valmm_a_compare $INSTANCE2_4P2

The following comparison output files will be created:

$CERESHOME/inversion/test_suites/results/CmpSubsetSSFValmm_$DATE_4P2

$CERESHOME/inversion/test_suites/results/CmpSubsetSSFAValmm_$DATE_4P2

#### Evaluation of Comparison Software Output

This section provides the procedure for evaluating the output from the CER4.5-6.4P2 comparison software.

Examine the comparison report files by typing:

cat $CERESHOME/inversion/test_suites/results/CmpSubsetSSFValmm_$DATE_4P2

cat $CERESHOME/inversion/test_suites/results/CmpSubsetSSFAValmm_$DATE_4P2

The final line of this file will report the status of the comparison between the generated data and the expected output.

### Solutions to Possible Problems

- All output files are opened with Status = NEW in the CER4.5-6.4P2 software.  These files must be removed before running these test procedures.  A script, which removes PGE created files, cleanup_4.5-6.4P2.csh, is located in directory $CERESHOME/inversion/CER4.5-6.4P2/rcf.  To use the clean-up script:

$CERESHOME/inversion/CER4.5-6.4P2/rcf/cleanup_4.5-6.4P2.csh $INSTANCE2_4P2

Use the latest version of CERESlib.

Ignore the warnings received during compilation.

### Stand Alone Test Procedures for FM5

#### Environment setup and file preparation

cd $CERESHOME/inversion/CER4.5-6.4P2/rcf

setenv YEAR 2014

setenv MONTH 07

setenv DATE_4P2 $YEAR$MONTH

setenv INSTANCE2_4P2 NPP-FM5-VIIRS_Edition1A_100101.$DATE_4P2

source $CERESHOME/inversion/CER4.5-6.4P2/rcf/inversion-FM5-valmm-subset.csh

Copy the input files to appropriate locations:

cp $CERESHOME/inversion/data/input/CER4.5-6.4P2/CER_SSFA-val_NPP-FM5-VIIRS_Edition1A_100101.20140715 $CERESHOME/inversion/data/SSFA-val/NPP-FM5-VIIRS_Edition1A/2014/07/

cp $CERESHOME/inversion/data/input/CER4.5-6.4P2/CER_SSFB-val_NPP-FM5-VIIRS_Edition1A_100101.20140715 $CERESHOME/inversion/data/SSFB-val/NPP-FM5-VIIRS_Edition1A/2014/07/

#### Execution

Execute the production script by typing the script name, CER4.5-6.4P2-SGE_Driver.pl, followed by the date option and the cleanup option.

cd $CERESHOME/inversion/CER4.5-6.4P2/rcf

$CERESHOME/inversion/CER4.5-6.4P2/rcf/CER4.5-6.4P2-SGE_Driver.pl -date $DATE_4P2 -clean

The following file will be generated:

$CERESHOME/inversion/CER4.5-6.4P2/rcf/pcf/CER4.5-6.4P2_PCF_$INSTANCE2_4P2

The submitted job can be monitored with the qstat command.

The most recently created sge_log file can be viewed to monitor progress of this job.  This will be the last file listed by the command:

ls -arlt $CERESHOME/inversion/sge_logs/CER4.5-6.4P2/CER4.5-6.4P2_$INSTANCE2_4P2.o*

Output file generation test:

The SSF subset Processor Product Generation Executive (PGE), CER4.5-6.4P2, will be executed and will create the files printed out by the list_4.5-6.4P2csh script:

$CERESHOME/inversion/CER4.5-6.4P2/rcf/list_4.5-6.4P2.csh $INSTANCE2_4P2

Note:	If any file that should have been created is missing, then a message is written to the screen naming which file could not be found.

#### Exit Codes

All CER4.5-6.4P2 software terminates using the CERES defined EXIT CODES for the Langley TRMM Information System (LaTIS).  Successful completion is indicated by an exit code of 0.  This test should complete with an exit code of 0 for each of the executables.

#### Test Summary

SSF Subset Postprocessor Test Summary:

Total Run Time:	0:02 minutes

Memory:	4631 K

Required Disk Space:	2.0 Megabytes

### Evaluation Procedures

Clean up the input directories:

rm $CERESHOME/inversion/data/SSFA-val/NPP-FM5-VIIRS_Edition1A/2014/07/CER_SSFA-val_NPP-FM5-VIIRS_Edition1A_100101.20140715

rm $CERESHOME/inversion/data/SSFB-val/NPP-FM5-VIIRS_Edition1A/2014/07/CER_SSFB-val_NPP-FM5-VIIRS_Edition1A_100101.20140715

#### Log and Status File Results and Metadata Evaluation

The Error and Status Log File, CER4.5-6.4P2_LogReport_$INSTANCE2_4P2 is located in directory $CERESHOME/inversion/runlogs after CER4.5-6.4P2 has been executed.  Metadata files which end in extension, '.met', are located in the same directories as their corresponding output files after CER4.5-6.4P2 has been executed.

Metadata files:

CER_SSFB-valmm_$INSTANCE_4P2.met

CER_SSFA-valmm_$INSTANCE_4P2.met

Compare the metadata files with the expected contents of the files with the same names found in directory $CERESHOME/inversion/data_exp/CER4.5-6.4P2, using the following diff_4.5-6.4P2.csh script:

cd $CERESHOME/inversion/CER4.5-6.4P2/rcf

$CERESHOME/inversion/CER4.5-6.4P2/rcf/diff_4.5-6.4P2.csh $INSTANCE2_4P2

The only differences between the *.met files should be the production times and differences in the directory paths where the tests were run.

#### Execution of Comparison Software for the SSF Subset Post Processor

The evaluation software for this SSF Post Processor will perform a single test.  This test will compare the data on the two newly created monthly validation site SSF files to the comparison files provided with the software delivery.

- The executable for the comparison software is not provided in the tar file.  It was created when all the software’s code was compiled.

To execute the comparison software for the CER4.5-6.4P2, type the following commands:

cd $CERESHOME/inversion/test_suites/bin

run_valmm_compare $INSTANCE2_4P2

run_valmm_a_compare $INSTANCE2_4P2

The following comparison output files will be created:

$CERESHOME/inversion/test_suites/results/CmpSubsetSSFValmm_$DATE_4P2

$CERESHOME/inversion/test_suites/results/CmpSubsetSSFAValmm_$DATE_4P2

#### Evaluation of Comparison Software Output

This section provides the procedure for evaluating the output from the CER4.5-6.4P2 comparison software.

Examine the comparison report files by typing:

cat $CERESHOME/inversion/test_suites/results/CmpSubsetSSFValmm_$DATE_4P2

cat $CERESHOME/inversion/test_suites/results/CmpSubsetSSFAValmm_$DATE_4P2

The final line of this file will report the status of the comparison between the generated data and the expected output.

### Solutions to Possible Problems

- All output files are opened with Status = NEW in the CER4.5-6.4P2 software.  These files must be removed before running these test procedures.  A script, which removes PGE created files, cleanup_4.5-6.4P2.csh, is located in directory $CERESHOME/inversion/CER4.5-6.4P2/rcf.  To use the clean-up script:

$CERESHOME/inversion/CER4.5-6.4P2/rcf/cleanup_4.5-6.4P2.csh $INSTANCE2_4P2

Use the latest version of CERESlib.

Ignore the warnings received during compilation.

Acronyms and Abbreviations

ASCII	American Standard Code Information Interchange

ASDC	Atmospheric Science Data Center

CERES	Clouds and the Earth’s Radiant Energy System

CERESlib	CERES library

DAAC	Distributed Active Archive Center

EOS	Earth Observing System

EOS-AM	EOS Morning Crossing Mission

EOS-PM	EOS Afternoon Crossing Mission

ERBE	Earth Radiation Budget Experiment

ERBS	Earth Radiation Budget Satellite

F90	Fortran 90

HDF 	Hierarchical Data Format

LaTIS	Langley TRMM Information System

NASA	National Aeronautics and Space Administration

NOAA	National Oceanic and Atmospheric Administration

PCF	Process Control File

PGE	Product Generation Executives

QC	Quality Control

SSAI	Science Systems Applications, Inc.

SSF	Single Scanner Footprint TOA/Surface Fluxes and Clouds

SSF	Single Scanner Footprint TOA/Surface Fluxes and Clouds

SSFA	Single Scanner Footprint TOA/Surface Fluxes and Clouds Aerosols

TOA	Top-of-Atmosphere

TRMM	Tropical Rainfall Measuring Mission